.HM A 1 1 1 1 1 1
.H 1 "Appendix for as8048 Frankenstein Assembler"
.H 2 "Pseudo Operations"
.H 3 "Standard Pseudo Operation Mnemonics"
.VL 40 5 1
.LI "End"
END
.LI "File Inclusion"
INCL
INCLUDE
.LI "If"
IF
.LI "Else"
ELSE
.LI "End If"
ENDI
.LI "Equate"
EQU
.LI "Set"
SET
.LI "Org"
ORG
.LI "Reserve Memory"
RESERVE
RMB
.LI "Define Byte Data"
BYTE
DB
FCB
.LI "Define Word Data"
DW
FDB
WORD
.LI "Define String Data"
FCC
STRING
.LI "Define Character Set Translation"
CHARSET
.LI "Define Character Value"
CHARDEF
CHD
.LI "Use Character Translation"
CHARUSE
.LE
.H 3 "Machine Dependent Pseudo Operations"
.H 4 "Instruction Set Selection"
.DS I N
CPU string
.DE
The instruction set can be specified in the source file with the CPU 
pseudooperation.
The string, delimited by quotes or apostrophes, is scanned for a
substring which selects which instruction set is used.
When the program is invoked, this operation is performed on the name of
the program, then the -p optional arguement, if any, and then any CPU
statements.
The last one selects which subset of the instructions the assembler will
accept.
The instruction set can be changed at any place in the source file. 
.VL 30 5 1
.LI "Instruction Set"
Substrings
.LI "80C48"
C48 
c48 
C35 
c35 
.LI "80C49"
C49
c49 
C39 
c39 
.LI "80C50"
C50 
c50 
C40 
c40 
.LI "8048"
48 
35 
.LI "8049"
49 
39 
.LI "8050"
50 
40 
.LI "8041"
41 
.LI "8042"
42 
.LE
.H 4 "Register Set"
.DS I N
Label REGISTER expr 
.DE
.P
The REGISTER statement is a version of the SET statement that checks that the
value of its expression is a valid data register location for the current
CPU selection.
The REGISTER statement sets the symbol specified in the label field with the
numeric value of the expression.
The REGISTER statement can change the value of a symbol, but only if the
symbol is originally defined in a previous SET or REGISTER statement.
.DS I N
Example
.SP
dtabl	register	32

	mov	r1, #dtabl
	mov	a, @r1
.DE
.H 2 "Instructions"
.H 3 "Instruction List"
.TS H
;
l l l.
Opcode	Syntax	Selection Criteria
.sp
.TH
.sp
ADD	 A ',' '#' expr	
ADD	 A ',' '@' REG	
ADD	 A ',' REG	
.sp
ADDC	 A ',' '#' expr	
ADDC	 A ',' '@' REG	
ADDC	 A ',' REG	
.sp
ANL	 A ',' '#' expr	
ANL	 A ',' '@' REG	
ANL	 A ',' REG	
ANL	 BUS ',' '#' expr	INSTNOT41
ANL	 P1 ',' '#' expr	
ANL	 P2 ',' '#' expr	
.sp
ANLD	 P47 ',' A	
.sp
CALL	 expr
.sp
CLR	 A	
CLR	 C	
CLR	 F0	
CLR	 F1	
.sp
CPL	 A	
CPL	 C	
CPL	 F0	
CPL	 F1	
.sp
DA	 A	
.sp
DEC	 A	
DEC	 REG
.sp
DIS	 I	
DIS	 TCNTI	
.sp
DJNZ	 REG ',' expr
.sp
EN	 DMA	INST41
EN	 FLAGS	INST41
EN	 I	
EN	 TCNTI	
.sp
ENT0	 CLK	INSTNOT41
.sp
HALT		INSTIDL
.sp
IDL		INSTIDL
.sp
IN	 A ',' DBB	INST41
IN	 A ',' P1
IN	 A ',' P2	
.sp
INC	 '@' REG
INC	 A	
INC	 REG
.sp
INS	 A ',' BUS	INSTNOT41
.sp
JB0	 expr
.sp
JB1	 expr
.sp
JB2	 expr
.sp
JB3	 expr
.sp
JB4	 expr
.sp
JB5	 expr
.sp
JB6	 expr
.sp
JB7	 expr
.sp
JC	 expr
.sp
JF0	 expr
.sp
JF1	 expr
.sp
JMP	 expr
.sp
JMPP	 '@' A	
.sp
JNC	 expr
.sp
JNI	 expr	INSTNOT41
.sp
JNIBF	 expr	INST41
.sp
JNT0	 expr
.sp
JNT1	 expr
.sp
JNZ	 expr
.sp
JOBF	 expr	INST41
.sp
JT0	 expr
.sp
JT1	 expr
.sp
JTF	 expr
.sp
JZ	 expr
.sp
MOV	 '@' REG ',' '#' expr
MOV	 '@' REG ',' A	
MOV	 A ',' '#' expr	
MOV	 A ',' '@' REG	
MOV	 A ',' PSW	
MOV	 A ',' T	
MOV	 A ',' REG	
MOV	 PSW ',' A	
MOV	 STS ',' A	
MOV	 T ',' A	
MOV	 REG ',' '#' expr
MOV	 REG ',' A	
.sp
MOVD	 A ',' P47 	
MOVD	 P47 ',' A	
.sp
MOVP3	 A ',' '@' A	
.sp
MOVP	 A ',' '@' A	
.sp
MOVX	 '@' REG ',' A	INSTNOT41
MOVX	 A ',' '@' REG	INSTNOT41
.sp
NOP	
.sp
ORL	 A ',' '#' expr	
ORL	 A ',' '@' REG	
ORL	 A ',' REG	
ORL	 BUS ',' '#' expr	INSTNOT41
ORL	 P1 ',' '#' expr	
ORL	 P2 ',' '#' expr	
.sp
ORLD	 P47 ',' A	
.sp
OUT	 DBB ',' A	INST41
.sp
OUTL	 BUS ',' A	INSTNOT41
OUTL	 P1 ',' A	
OUTL	 P2 ',' A	
.sp
RET	
.sp
RETR	
.sp
RL	 A	
.sp
RLC	 A	
.sp
RR	 A	
.sp
RRC	 A	
.sp
SEL	 MSELC	INSTNOT41
SEL	 RSELC
.sp
STOP	 TCNT	
.sp
STRT	 CNT	
STRT	 T	
.sp
SWAP	 A	
.sp
XCH	 A ',' '@' REG	
XCH	 A ',' REG	
.sp
XCHD	 A ',' '@' REG	
.sp
XRL	 A ',' '#' expr	
XRL	 A ',' '@' REG	
XRL	 A ',' REG	
.TE
.H 3 "Operands"
.VL 25 5
.LI REG
REG can be any of r0, r1, r2, r3, r4, r5, r6, r7, unless proceeded by a
'@' where only r0, and r1 are accepted.
.LI MSELC
MSELC represents the symbols mb0 and mb1.
.LI RSELC
RSELC represents the symbols rb0 and rb1.
.LI P47
P47 represents the symbols p4, p5, p6, p7.
.LE
.P
There are uppercase versions of all the reserved symbols.
.H 3 "Selection Criteria Keywords"
.VL 25 5 
.LI INSTIDL
The instruction is only available on CMOS implementations.
.LI INSTNOT41
The instruction is not available in the 8041.
.LI INST41
The instruction is only available in the 8041.
.LE
.H 3 "Apostrophes"
The apostrophes in the syntax field are a notation used for the
parser generator and are not put in the assembler source statement.
.H 2 "Notes"
.H 3 "Reserved Symbols"
.H 4 "Machine Dependent Reserved Symbols"
A
BUS
C
CLK
CNT
DBB
DMA
F0
F1
FLAGS
I
MB0
MB1
P1
P2
P4
P5
P6
P7
PSW
R0
R1
R2
R3
R4
R5
R6
R7
RB0
RB1
STS
T
TCNT
TCNTI
a
bus
c
clk
cnt
dbb
dma
f0
f1
flags
i
mb0
mb1
p1
p2
p4
p5
p6
p7
psw
r0
r1
r2
r3
r4
r5
r6
r7
rb0
rb1
sts
t
tcnt
tcnti
.H 4 "Standard Reserved Symbols"
AND
DEFINED
EQ
GE
GT
HIGH
LE
LOW
LT
MOD
NE
NOT
OR
SHL
SHR
XOR
and
defined
eq
ge
gt
high
le
low
lt
mod
ne
not
or
shl
shr
xor
.TC 1 1 7