GAMESRVR.DLL -- Full-screen support for DIVE game applications          ÿ

Overview:ÿ
---------

The purpose of the GameSrvr is to support games in video modes other
than that used by the OS/2 desktop.  The reason for this is quite
simple:  SPEED.

Most games on the market today use the 320x200x256 VGA mode.  There are
a number of reasons for using this mode that outweigh the mediocre
resolution of 320 by 200 pels in 256 colors.

  Compatibility:  This mode exists on all VGA and SuperVGA cards.

  Ease of Use:  This mode uses a flat frame buffer and exactly one byte
     per pel.  This greatly simplifies the coding of graphics routines,
     since hardware registers and bit packing can be ignored.

  Speed:  Not only are the graphics algorithms faster due to their
     simplicity, but the buffer is only 64000 bytes.  Compare this to a
     typical desktop resolution of 1024x768x256 with a frame buffer of
     786432 bytes, more than 12 times larger and slower.  If the
     resolution or number of colors is increased, this will only get
     worse.

By using the functions provided by the GameSrvr, PM programs can be
written to use the full screen without paying the penalty of a large
frame buffer.

Installation and Use:ÿ
---------------------

To install the GameSrvr, run GSRVINST.EXE to perform the following
steps:

  Copy GAMESRVR.DLL and DIVE.DLL to d:\OS2\DLL, where d is the boot
  drive.

  Add the GAMESRVR key to the PM_ED_HOOKS application in OS2.INI with
  the key value of d:\OS2\DLL\GAMESRVR.DLL, where d is the boot drive.

  If SVGADATA.PMI exists in the d:\OS2 directory, copy SVGA.EXE to
  d:\OS2, then execute SVGA ON INIT to rebuild the SVGADATA.PMI file,
  adding the 320x200x256 mode.

Depending on the video card that you have installed, the installation may
end in the full-screen DOS session where SVGA.EXE was executed.  If so,
you should type EXIT to return to your OS/2 session.

The system will have to be rebooted to allow these changes to take
effect.  Applications written to use the GameSrvr will automatically
take advantage of its presence.

Once an application has initialized with GameSrvr, the user can switch
to full screen mode by hitting "ALT + HOME" ( Only the home key on the
key pad will work ). This mechanism is supported by GameSrvr directly.
An application can also provide a user interface that takes advantage
of GameSrvr APIs to switch to full screen mode.




Programming:ÿ
------------

The GameSrvr is loaded at execution time by performing a DosLoadModule
on GAMESRVR.  If this is successful, the address of the
InitGameFrameProc routine my be queried using DosQueryProcAddr.  When
you call this routine with the handle of the frame window of the
application, it subclasses the frame window procedure.  This allows the
GameSrvr to process all messages sent to the application, especially
focus change messages which may require restoration of the original
desktop mode.

Communication with the GameSrvr is through the following three messages:

  WM_SetVideoMode (0x04A0)

    This message uses mp1 to select either one of the preset game window
    styles or a specific video mode, as extracted from the table of
    supported video modes.

    mp1 == 0 restores the original mode of the desktop, as well as the
             original size and location of the application's window.

    mp1 == 1 restores the original mode of the desktop, but expands the
             size of the client window so that only the client window
             and the command bar are visible.

    mp1 == 2 expands the client window to fill the screen, then sets the
             video mode to the standard 320x200x256 game mode.

    mp1 > 2 expands the client window to fill the screen, then sets the
             video mode defined by the VIDEOMODEINFO structure addressed
             by mp1.

    The return value from this message is 1, if successful, otherwise 0.

  WM_NotifyVideoModeChange (0x04A1)

    This message is generated by the GameSrvr to notify the application
    immediately before and again immediately after a video mode change.

    mp1 == 0 indicates that the video mode is about to change.

    mp1 == 1 indicates that the video mode change is complete.

    In both cases, mp2 contains the address of the VIDEOMODEINFO
    structure which describes the video mode or 0 or 1, as described for
    the WM_SetVideoMode message.  The value of 2 will never be returned.
    Instead it is transformed into a pointer to a VIDEOMODEINFO
    structure.

    The return value of this message is ignored.

  WM_GetVideoModeTable (0x04A2)

    This message is used only if you wish to select a video mode other
    than the standard 320x200x256 mode.

    mp1 is the address of a PVOID to receive the address of an array of
             VIDEOMODEINFO structures describing all of the modes
             supported by the current display card.  This array is
             allocated for you.  You may delete it yourself or allow it
             to be automatically deleted at process termination.

    mp2 is the address of a ULONG to receive the number of structures in
             the array that was allocated.

    The return value from this message is 1, if successful, otherwise 0.