ÜÛÛÛÛÛÛÜ     ÜÛÛß ÜÛÛÛÛÛÛÜ
                            ÛÛÛ  ÛÛÛ   ÜÛÛß   ÛÛÛ  ÛÛÛ
                            ÛÛÛÜÜÜÜ  ÜÛÛß ÜÜÜ ßÛÛÜÜÛÛß
                             ßßßßÛÛÛ ÛÛÛÜÜÛÛÛ ÜÛÛßßÛÛÜ
                            ÛÛÛ  ÛÛÛ ßßßßßÛÛÛ ÛÛÛ  ÛÛÛ
                            ßÛÛÛÛÛÛß      ÛÛÛ ßÛÛÛÛÛÛß


           A Full Screen Simulator for 8048 Compatible Microprocessors
                                   Version 1.3

                                  William Luitje
                                   23 July 1996 


       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Background ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        I  wrote this simulator as part of my work on a consulting job  a 
        few years ago.   There is still quite a lot of work one could  do 
        to improve it, such as providing a way to manually change RAM and 
        ports,   allowing  disassembly of any part  of  ROM,   simulating 
        changes in inputs,  command files...  A LOT!  Still, I think it's 
        useful,   as  is,   for learning the 8048   instruction  set  and 
        debugging small programs.   I hope it's useful to you; if you use 
        it,   please  see  the registration section at the  end  of  this 
        document (relax, no money is involved). 

        With  the  work I mentioned above and some features  specifically 
        for  an educational environment,  this program would make a great 
        tool   for  teaching  microprocessor  programming.     Commercial 
        programs like this cost from US$200 to $300.  If I make an educa-
        tional version of S48,  I  envision a site licensing  arrangement 
        which would cost a very modest amount per student.  If you are an 
        instructor or administrator and are interested in pursuing  this, 
        contact  me at the address given at the end of this document even 
        if you use a different micro in your course. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Introduction ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        S48   simulates the instruction set and some of the hardware  for 
        the 8048,  8049,  8050, 8021, 8022  microprocessors originated by 
        Intel and now widely second-sourced.  The simulator handles these 
        hardware parameters: 

        þ 4096 bytes of ROM
        þ 128 bytes of internal RAM
        þ 256 bytes of external RAM
        þ 7 I/O ports
        þ one 8 bit timer

        The  hardware  registers  and  flags  and  RAM  are  continuously 
        displayed  on  screen  and  are updated as  each  instruction  is 
        executed.  There is a disassembly window showing the instructions 
        as they are executed.   You can trace through instructions one at 
        a time or execute them continuously until a breakpoint is reached 
        or you stop the program manually. 
        
        The  hardware requirements to run S48  are quite simple;   you'll 
        need  a  PC  with a monochrome,  Hercules,  CGA,   EGA,   or  VGA 
        compatible  video card (the program does direct screen writes  so 
        you'll  see snow using CGA).   A  color display is  not  strictly 
        necessary, but is certainly helpful in reading the screen easily.  
        Obviously,  the faster your CPU,  the faster the simulation  will 
        run.  A 4.77 MHz PC is adequate for small programs.  The software 
        requirements  are even simpler:  you'll need some version of DOS, 
        S48 and an 8048 program to simulate.  
         
       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Sample Program ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        I've included a very simple sample program for you to play  with, 
        called demo.bin.  demo.asm is the source file and implements a 16 
        bit  counter in software.   There is an interrupt service routine 
        which  captures  the low byte of that counter and  stores  it  in 
        consecutive  locations  in  external RAM when  the  interrupt  is 
        invoked.  The timer interrupt service routine increments an 8 bit 
        counter  when the timer overflows.  It's short enough that I  can 
        reproduce  its  assembly listing here: 

                                     .org   0
           0000 00                   nop    
           0001 04 09                jmp    start
           0003                      .org   3
           0003 00                   nop
           0004 00                   nop
           0005 04 1B                jmp    intsvc
           0007                      .org   7
           0007 04 21                jmp    tmrsvc
           0009             ; Initialization
           0009 27          start    clr    a
           000A A8                   mov    r0,a
           000B A9                   mov    r1,a
           000C AB                   mov    r3,a
           000D 62                   mov    t,a
           000E B8 18                mov    r0,#24
           0010 A0                   mov    @r0,a
           0011 25                   en     tcnti
           0012 55                   strt   t
           0013 05                   en     i
           0014             ; Main Loop
           0014 18          loop     inc    r0
           0015 F8                   mov    a,r0
           0016 96 14                jnz    loop
           0018 19                   inc    r1
           0019 04 14                jmp    loop
           001B             ; External Interrupt Service Routine
           001B F8          intsvc   mov    a,r0
           001C D5                   sel    rb1
           001D 90                   movx   @r0,a
           001E 18                   inc    r0
           001F C5                   sel    rb0
           0020 93                   retr
           0021             ; Timer Overflow Interrupt Service Routine
           0021 1B          tmrsvc   inc    r3
           0022 93                   retr
           0023                      .end

        You'll also need an understanding of the 8048 instruction set and 
        architecture.  You won't find much help in this document. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Tutorial ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        The 8048 program to be executed can be in either Intel hex format 
        or binary, like you would use to program an EPROM.  The simulator 
        tries  to  read  the file in hex format first and if  that  fails 
        assumes that the file is binary.   To invoke the simulator,  just 
        give the name of the program file as an argument, e.g.: 

        s48 demo.bin 

        Take  a  minute to familiarize yourself with the  layout  of  the 
        screen: 

 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 ³Cmd:                                                                        ³
 ³ 35 bytes read from demo.bin                                                ³
 ³ÚÄPC¿ ÚAÄ¿ÚPSWÂCYÂACÂF0ÂF1ÂRBÂSTK¿TIEÂTSÂTFÂTM¿                             ³
 ³À000Ù À  ÙÀÄ08ÁÄ ÁÄ ÁÄ0ÁÄ0ÁÄ0ÁÄÄ0ÙÀÄ0ÁÄ0Á00Á  Ù                             ³
 ³ ÚMB¿ ÚBus¿ÚP1ÂP2ÂP3ÂP4ÂP5ÂP6ÂP7¿ ÚT0ÂT1ÂIIÂIE¿                             ³
 ³ ÀÄ0Ù ÀÄ  ÙÀ  Á  Á  Á  Á  Á  Á  Ù ÀÄ ÁÄ ÁÄ ÁÄ Ù                             ³
 ³    ÉÍ00ÍÍ10ÍÍ20ÍÍ30ÍÍ40ÍÍ50ÍÍ60ÍÍ70ÍÍÍ»          ±000±00±±±±NOP±±±±±±±     ³
 ³ 00 º °°                               º 08        001 04 06 JMP  006       ³
 ³ 01 º °°                               º 09        003 00    NOP            ³
 ³ 02 º °°                               º 0A        004 00    NOP            ³
 ³ 03 º °°                               º 0B        006 04 1B JMP  01B       ³
 ³ 04 º °°                               º 0C        007 04 21 JMP  021       ³
 ³ 05 º °°                               º 0D        ÚÄÄÄÄBreakpointsÄÄÄÄ¿    ³
 ³ 06 º °°                               º 0E        À±±± ±±± ±±± ±±± ±±±Ù    ³
 ³ 07 º °°                               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»    ³
 ³    ÌÍ00ÍÍ10ÍÍ20ÍÍ30ÍÍ40ÍÍ50ÍÍ60ÍÍ70ÍÍ80ÍÍ90ÍÍA0ÍÍB0ÍÍC0ÍÍD0ÍÍE0ÍÍF0ÍÍÍ¹    ³
 ³ 00 º                                                                  º  08³
 ³ 01 º                                                                  º  09³
 ³ 02 º                                                                  º  0A³
 ³ 03 º                                                                  º  0B³
 ³ 04 º                                                                  º  0C³
 ³ 05 º                                                                  º  0D³
 ³ 06 º                                                                  º  0E³
 ³ 07 º                                                                  º  0F³
 ³    ÈÍÍÍ0FÍÍ1FÍÍ2FÍÍ3FÍÍ4FÍÍ5FÍÍ6FÍÍ7FÍÍ8FÍÍ9FÍÍAFÍÍBFÍÍCFÍÍDFÍÍEFÍÍFFÍ¼    ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        The  top  line is where you type your commands to the  simulator.  
        The  second  line is where any messages from S48  are  displayed.  
        The hardware registers and flags are displayed with a light  blue 
        background  at  the  top  left  of  the  screen.    There  is  an 
        instruction disassembly window at the top right with the  current 
        instruction (the one to be executed next) shown in reverse video.  
        Below   it   are  the  5  instructions  following   the   current 
        instruction.    Above  it will be displayed the 6  most  recently 
        executed instructions.  Below the disassembly window is where the 
        breakpoints are displayed. 
              
        The large L shaped box shows all of RAM.   The top part shows 128 
        bytes of internal RAM and the lower shows 256  bytes of  external 
        RAM.   There isn't enough room on the screen to have blank  space 
        between  the columns so they are distinguished by the  background 
        color.   The first column contains locations 00  through 07;  the 
        second holds 08 through 0F, and so on.  The light blue background 
        in internal RAM shows the active register bank. 

        When  the  simulator is started the processor is in  reset.   The 
        values  of registers which are initialized by RESET,  e.g.    the 
        Program Counter,  are shown;  registers which are undefined after 
        RESET, such as the Accumulator and RAM are shown as blank. 

        Let's do some simulation.  Give a Trace command by pressing the t 
        key  and  return  (or  more  simply,   just  return).    The  NOP 
        instruction has now moved above the current instruction line, the 
        PC  has  changed to 001  and the current instruction is JMP  006.  
        Give another trace command and the current instruction changes to 
        CLR   A.    Notice  that  the  instructions  after  the   current 
        instruction  have now changed to reflect the jump.   Their  color 
        has  changed,   too,  to make it easier to see that the jump  was 
        taken.    (This  is especially useful for  following  conditional 
        jumps.)     Trace  again  and  notice  how  the  Accumulator   is 
        initialized to zero. 
        
        Now  let's  watch the simulation run for a while.   Give  the  Go 
        command  by  pressing the g key and return.   As  the  simulation 
        runs, notice how the timer register changes and memory location 0 
        counts up quickly and memory location 1 counts slowly.  Press any 
        key to stop the simulation. 

        To invoke the interrupt, press the i key and return.   Notice how 
        the  current instruction changes to the first instruction of  the 
        interrupt  service routine at location 003.   Trace  through  the 
        rest  of  the  interrupt  service  routine  and  notice  how  the 
        background  of the register banks changes as the active  register 
        bank is switched. 

        To  demonstrate setting a breakpoint,  type "b 18"   and  return.  
        This  will  set a breakpoint at the instruction which  increments 
        the high byte of the 16 bit counter. Now give a go command and in 
        a few seconds the simulation will stop at location 18.  To remove 
        the  breakpoint,   use the kill command with the address  of  the 
        breakpoint you want to remove.   In this case, "k 18"  and return 
        will do the trick. 

        To Quit the simulator, press q and return. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Command Summary ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        You've  seen all of the commands except for Help,  Reset and Port 
        in the tutorial; here we'll summarize them and give a little more 
        information about them.   Only the first letter of the command is 
        parsed  and  it can be either upper or lower case.   Some of  the 
        commands can take a numeric argument which is always expressed in 
        hexadecimal and need not be given in some cases. 

        g #   Go: Start simulating at address #.  Simulation stops when a 
              breakpoint  is reached or when a key is pressed.   If #  is 
              not given,  simulation starts at the current instruction.

        t #   Trace:  Trace  #  instructions.   If # is not  given,   one 
              instruction is traced.

        <ret> Trace one instruction; equivalent to "t 1".

        b #   Breakpoint:  Set  a breakpoint at the given address.    The 
              command has no effect if a number is not given. 

        k #   Kill  breakpoint:   Remove  the  breakpoint  at  the  given 
              address.    The  command has no effect if a number  is  not 
              given or if there is no breakpoint at that address. 

        p # # Port value:  Set the port  specified by the first # to  the 
              value  specified by the second #.   Two parameters must  be 
              given. 

        r     Reset:  Simulate a  reset.   The Program Counter is set  to 
              zero and other registers are set as appropriate.  Registers 
              which are not affected by RESET are not changed. 

        i     Interrupt:  Simulate  an external interrupt.   The  Program 
              Counter  is  set to the location of the  interrupt  service 
              routine, 0003H, and further interrupts are disabled. 

        q     Quit:  Quit the simulation.  Come back again soon!

        h     or  any  unrecognized  command  will  display  a small help 
              screen listing the available commands and their syntax. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Timer Simulation ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        The boxes which display the state of the timer are located in the 
        top  row of registers at the extreme right of the register  area.  
        They are explained as follows: 

        TIE - the Timer Interrupt Enable bit.  This is set by an EN TCNTI 
        instruction and cleared by DIS TCNTI. 

        TS - the Timer Started bit. This is set by the STRT T and cleared 
        by the STOP TCNT instructions. 

        TF - contains two bits related to timer overflow.   The right one 
        is  the  Timer  Flag  which is tested  and  cleared  by  the  JTF 
        instruction.   The left one is the Timer Overflow Flipflop  which 
        is  set  when the timer overflows and the Timer Interrupt  Enable 
        bit is set.  It is cleared when the timer interrupt is invoked so 
        you  won't see this bit set unless the external interrupt  is  in 
        progress when the timer overflows. 

        TM - the  timer register itself.   It  is  updated after each in-
        struction is simulated.  The state of the prescaler is not shown. 

        The  counter is not simulated at this time since there is no  way 
        to simulate changes in external inputs. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Screen Colors ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        If you don't have a color monitor or simply don't like all of the 
        colors  but have a color capable display adapter,  you can  force 
        S48 to display in monochrome by using the DOS MODE command to set 
        the   default  display  mode  to  either  BW80   or  MONO.    S48 
        automatically detects MDA and Hercules display adapters. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Distribution ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        The S48 package consists of the following files:

          þ s48.exe
          þ s48.doc
          þ demo.asm
          þ demo.bin
          þ also_by.wvl
        
        This package and the individual files in it are copyrighted works 
        of William Luitje.  The author grants you a non-exclusive license 
        to   copy  and  distribute  these  works  as  long  as  they  are 
        distributed as a group and are not modified in any way  including 
        the deletion of any files or addition of other files (such as BBS 
        ads) in the distribution archive. 

        On a related note,  I am distributing this package for free.   If 
        you paid money for a floppy or CD-ROM with this package on it, be 
        aware that I am not seeing a penny of it.   What you paid for  is 
        the  service of distribution.   I'm sure that you understand  the 
        nature of transactions like that but I have heard from people who 
        "bought  one  of  my  programs"   and  expect  me  to  conduct  a 
        correspondence  course on basic PC techniques,  theory and repair 
        because  of  their  "purchase".   While I am always open  to  bug 
        reports  and  well  thought out questions  and  suggestions  (and 
        postcards!),   please read the documentation carefully and  check 
        with local experts before you fire up your word processor. 

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Registration ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        While this software may be freely copied and used,  I  do request 
        that  you  register  it if you use it.   Just send  me  either  a 
        postcard   or   some  e-mail  telling  which  program   you   are 
        registering.   I'd prefer a local,  picture postcard;  after all, 
        whether  it's great or whether it's a pit,  the place  where  you 
        live is probably interesting in some way, right? 
          
        This is only partially an ego massage for the author.   I   enjoy 
        writing  useful  utilities  and  have  several  other  pieces  of 
        freeware  out  floating  around  the  net  (see  ALSO_BY.WVL  for 
        details).    I'd  like  feedback about which  of  them  is  worth 
        expanding and supporting.   Postware really works!  I support the 
        programs  which  are  most  used.   I'm not  planning  on  adding 
        features to this program, but I might if I get enough postcards!  

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± Conditions of Use ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        The program has not been tested against a real live 8048  because 
        I  don't  have  access to an 8048  hardware  development  system.  
        That's why I wrote this simulator in the first place!   The Intel 
        data  books  I  used were ambiguous in places so I  made  guesses 
        about  how  some of the subtler points of the  simulation  should 
        work.    E.g.,  does INC set AC?   Until one of my correspondents 
        wrote some test software and ran it on real silicon, I could only 
        guess that it did not.   That turned out to be correct but  there 
        may be instances where I guessed wrong.  Bug reports are welcome, 
        especially  when  you  can provide documentation  about  how  the 
        simulation really should work. 

        So, keep in mind that this software is provided as is.  I make no 
        guarantees about it except that it will take up space on any disk 
        you place it on.  Further, any software you write with the aid of 
        this simulator is your responsibility.   Verify that it  operates 
        properly  with  actual  hardware before you use it  in  the  real 
        world. 

        William Luitje
        2677 Wayside Drive
        Ann Arbor, MI 48103
        USA

        My  e-mail address is somewhat unstable at the current  time  and 
        one  or both of the following addresses may disappear.   Try  the 
        first  address  and if that doesn't work,  try the  second.    If 
        neither works, try looking for "William Luitje"  (I think I'm the 
        only  one  in  the world!)   on one of  the  WWW  e-mail  address 
        databases, such as www.four11.com or www.whowhere.com.  I plan to 
        stay connected so be persistent and you'll get through to me! 

        luitje@m-net.arbornet.org
        luitje@cyberspace.org

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³±±± History ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        Version 1.0  1 Aug 94 
          Initial public release

        Version 1.1 11 Feb 95 
          Added command to set ports
          Added color change of prospective disassembly window after jump,
            branch or interrupt. 

        Version 1.2  24 Nov 95
          Added automatic detection and support for MDA/Hercules video cards
          Added <ret> as a synonym for T 1
          Rewrote user input routine to set background color, handle long 
            lines and ESC correctly
          Added ability to read Intel format hex files (Rainer Glaschick 
            supplied the code for this)
          Fixed several emulation bugs (thanks to Rainer Glaschick, 
            Leonhard Schneider, Gabriel Patulea and Mike Loving for 
            their reports)

        Version 1.3 23 Jul 96
          Added timer emulation
          Added a small on-line help screen
          Increased speed of emulation by 70%
          Fixed an emulation bug (thanks to Motti Grinberg for the 
            report)

        Copyright 1994-1996 by William Luitje