TN211-9.DOC
                             SYSOP COMMAND LIST
                           **********************

    Besides the USER command listing, there are  a  special set of commands for
SYSOP use.  To be able to use these,  one must be recognized  by  the node as a
SYSOP.    The method for doing this is  to  answer correctly  the random set of
numbers given in response to a (S)YSOP command as described previously.

    INFO  (I) - Allows the SYSOP to enter text into the soft coded INFO section
on the  node.  The INFO section has available a maximum of 160 characters.   Up
to  80  characters  per line  are allowed.    To use,  type:  "I  (space)  text
<enter>"  for  the  first line.   If one prefers NOT having text appear on  the
first  line,  then type "I (space) (Control G) <return>."  This gives a  "beep"
along  with  a  blank  first  line.  For text to be  entered  on  the  2nd  and
subsequent  lines,  type:   "I (space) + <text> <return>" until the  total  160
character limit is reached.


An example for setting INFO:

SYSOP action:  I (control G) <return>

Node response:  SVATST:NJ7P-4}

SYSOP action:  I +Sierra Vista, AZ

Node response:  SVATST:NJ7P-4}
                Sierra Vista, AZ

SYSOP action:  I +145.01 MHz

Node response:  SVATST:NJ7P-4}
                Sierra Vista, AZ 
                145.01 MHz

SYSOP action:  I +CARA elections coming up soon, be prepared to help!

Node response:  SVATST:NJ7P-4}
                Sierra Vista, AZ
                145.01 MHz
                CARA elections coming up soon, be prepared to help!

SYSOP action:   I +BISBEE node will soon QSY to 145.11 MHz.


Node response:  SVATST:NJ7P-4}
                Sierra Vista, AZ
                145.01 MHz
                CARA elections coming up soon, be prepared to help!
                BISBEE node will soon QSY to 145.11 MHz.

    This process can be repeated until the maximum of 160 characters, including
non-typing  and  punctuation,  has  been reached.  To  erase  the  entire  INFO
section,  just type:  "I <Control G>."  If the INFO section is frequently to be
changed,  an  INFO  file  could be prepared in  advance  with  the  appropriate
commands and text included.  After SYSOPing the node, the file can be uploaded.
Another  advantage  of preparing the file in advance is it doesn't  require  as
much on-the-air time.

    While  160  characters are  available,  good  network  management  practice
dictates only enough text is used to get the  message across.   Although it may
seem  "distinctive"  to fill the remainder with spaces, line feeds,  or Control
G's,  please  don't  do it.     Users  find  such  practices  annoying  plus it
unnecessarily congests the network.

    Examples of INFO text and format are:

WTEX:W5CDM-3}
Located at Notrees, Tx.  Ant 600 ft. courtesy of WD5THB & W5CDM...

RDG:WA6YNG-1> From 18 Miles West of Redding
On Shasta Bally at 6200 Ft. - 145.05 Mhz.
With a Motorola Micor 60 watt radio on battery and float supply.

YKA:VE7RKA>
Greenstone Mountain Packet System
Kamloops, B.C.
SysOps- VE7EHL - VE7EJE

Mark your calendars, Nov 22, Packet meeting at the Lotus, C U There...


    KEY  TONE  (K T) - Operates the PTT line of the TNC and turns on  the  Mark
(low) tone or the Space (high) tone for approximately 22 seconds.

    KEY  DIDDLE (K D) - Operates the PTT line of the TNC and alternates rapidly
between Mark and Space for approximately 22 seconds.

    The  purpose of the "KEY" commands are to make the NodeOp's job of  setting
deviation  and  RF  frequency  much easier.  Previously  it  was  necessary  to
reinstall  the original TNC firmware chip and perform the CALIBRA procedure  to
set FM deviation.    Now, if the NodeOp has appropriate equipment and is within
radio  range  of  the node,  he can  routinely  check  frequency  and deviation
remotely.  At the site, this same procedure can be done via the HOST mode port.
Once  entered,  there is NO way the KEY  command  can  be terminated  until the
internal timer runs its course.  If the TNC-2  watchdog timer  is  set for less
than a 22 second duration, the watchdog will unkey  the PTT.  However, the node
will  continue the  KEY  command until the remaining time has expired.   During
this period, the node will not execute any other commands.

    Due  to the  nature  of  the  SIO chip  in the TNC-2,  it's necessary it be
"toggled"  to switch  from high to the low tone, or vice versa.   This was done
in the  TAPR  modem alignment  procedure by tapping the  space bar.   Of course
this isn't feasible when remotely SYSOPing and some experimentation is required
if one wants to change tones.    One  way would be to perform a K T command and
if  the  tone  is  not  the  one desired, do a "CQ" and repeat the K T command.
Oftentimes one or more  "CQs" will toggle to the opposite tone.  This procedure
is also required in HOST SYSOP mode.

    ON - OFF - A simplified remote control capability as compared with the HIGH
LOW commands  found in TheNet version 1.0.  "ON" turns on the CON LED and "OFF"
turns  the  LED  off.   In the MFJ 1270B, the voltage sense from  the  CON  LED
appears on pin 8 of the DB-25 connector.  The voltage sense also appears on the
base  of Q16, a 2N3904, the output of which goes to pin 2 of the TTL connector.
The  main caution here is that the controlled device  not draw  more than a few
milliamps either source or sink.   In the MFJ-1270B, pin 2 (NOT-DCD) of the TTL
connector  is low  when  ON and  high when OFF.

   A solid state  SPST  relay such  as the Teledyne p/n 611-2  can switch up to
25 amps at 250 VAC.   It requires a DC control  of 3 - 28  volts.   In the MFJ-
1270B,  replace Q16  with a 2N3906.    Replace  R103  with  a 220 ohm  1/4 watt
resistor.   On the bottom of the board add a 470 ohm 1/4 watt resistor  between
the  base of Q16 and the ground tab of radio port connector J2.   These changes
will  source 4 volts at 4 milliamps  through pin 2 of the TTL connector.    The
input  of the relay is connected between pin 2 (+) and pin 3 or 6 (-) on the J5
TTL  connector.    This satisfactorily  switches the relay and provides correct
"sense" for the CON LED.  It will glow when the relay is ON and be extinguished
when  the  relay  is OFF.    Other relay types may  require a transistor buffer
between  pin 2  and the controlled device.    As with any higher voltage wiring
projects,  be sure to comply  with applicable  electrical safety  practices and
codes.


    PARMS  (P) - Allows the NodeOp to make changes, as necessary.  To use, type
"P space  parameter  number space new value <enter>" to change any of the parms
to a new value.   For example, to change parameter 14 from a "0" to a "1," type
"P 14 1" to  effect the change.   Parameters are  numbered  starting  with "1,"
from left to right.   Multiple parameter changes in one command are disallowed.

NOTE: The above is a new procedure with version 2.09/2.10.

    LOCKING NODES - Occasionally a need may arise to modify node entries in the
NODES table.  The SYSOP command for this is:

N [LOCKED NODECALLSIGN] + ALIAS QUALITY OBS PORT [LOCKED NODECALLSIGN]

For example:  N K7WAA-1 + CAHTO 0 0 0 K7WAA-1

    Assuming  the  path  to  neighbor node CAHTO is  unreliable,  good  network
management  practices would dictate CAHTO be locked out.  In the above example,
setting  the  QUALITY to 0 will prevent CAHTO from appearing as a direct  path.
Setting the Obsolescence count to 0 makes CAHTO be listed as a permanent locked
entry.   If  the Obs count was set to a value between 6 - 1, this locked  entry
would  then  be  deleted  at  a   time  as  established  between  Parameters  4
(Obsolescence counter) and 6 (Broadcast interval).

To manually unlock CAHTO, the command is reversed:

N K7WAA-1 - CAHTO 0 0 0 K7WAA-1

    Here  one  will  note,  the minus  sign is  used for this purpose.    It is
essential  the  unlock  command  be  the  same  as the lock  command,  with the
exception of the minus sign.

    Setting  the  Obsolescence to zero permanently locks the  destination  node
into the nodes  table.   Even if the locked node fails, it will still be listed
in the nodes  table.   For this reason, the locked NODES procedure is not often
used as it's counterproductive network practice to broadcast failed nodes.   It
should  be  noted  this  procedure  only  works  with  "Net"  nodes  capable of
generating valid Level 4 Transport Layer responses.  If one attempts to connect
from the node to a locked  TNC or a  KA-node,  one will initially see a connect
made.   But when TheNet fails to receive a return Level 4 acknowledgement after
two or three interrogations, the circuit is disconnected.

    The LOCKED NODES command to use if a node should NOT have an alias is:

N [LOCKED NODECALLSIGN] + * QUALITY OBS PORT [LOCKED NODECALLSIGN]

Usage example: N AK7Z-1 + * 143 0 0 AK7Z-1