GRABEGA                                               Page 1
          Command
          ------------------------------------------------------------

          Purpose:  Capture an EGA graphics screen to a disk file in a
                    format compatible with RIX SoftWorks' EGA Paint 2005
                    and with EGA2GIF by SPARKS.

          Format:   [d:path\]grabega [/480]

          Type:     External

                    GRABEGA Version 3.0 22oct87
                    Copyright 1987 by Ray L. McVay (all rights reserved)
                    
                    S P A R K S
                    1609 Tulip Drive
                    Arlington, TX 76013-4915
                    CIS 75006,2563

          Remarks:

                    GRABEGA is a TSR (terminate and stay resident)
                    utility that captures EGA 320x200, 640x200, 640x350
                    and 640x480 graphic screens to files formatted like
                    uncompressed EGA Paint screen files.  When run, it
                    prints a sign on message and loads the resident
                    portion of the program which occupies about 2700
                    bytes of memory.  It has been used concurrently with
                    EGA Paint 2005, Sidekick, CED, STACKEY, CTRLALT and
                    EGABLANK2 with no problems but is incompatible with
                    BASIC interpreters, QuickBASIC, SYMDEB and Code
                    View.  Running one of the incompatible programs with
                    GRABEGA resident will cause your computer to lock up
                    and require the "big red switch" to recover.

                    In general, you should treat GRABEGA as a special
                    purpose utility to be loaded and used only when
                    needed.  Save yourself a lot of grey hair and always
                    reboot your computer when you are finished using
                    GRABEGA or any other special purpose resident
                    software.

                    To activate GRABEGA and save a screen you rapidly
                    press and release the left shift key twice.  If all
                    is well you will see activity on the default disk
                    drive and hear a normal BEEP when GRABEGA is
                    finished.  Wait until you hear the BEEP before
                    moving a mouse cursor around the screen or your
                    screen image will be corrupted.

                    If GRABEGA cannot save the screen then it will make
                    an odd noise and ignore the keystrokes.  There are
                    two main reasons GRABEGA will not be able to save a
                    screen: 1. The screen is not in one of the
                    recognised EGA graphics modes.  2. The program that
                    is running is executing an un-interruptable DOS or
                    BIOS function.








          GRABEGA                                               Page 2
          Command
          ------------------------------------------------------------
                    The files written by GRABEGA vary in size from 32016
                    bytes to 153616 bytes depending on the type of
                    screen it is saving.  The files all have names
                    following the pattern EGASCRNx.SCy where the "x" in
                    the pattern will change with each screen to produce
                    a unique name.  The "y" is set automatically
                    according to the size of the screen being saved as
                    shown in the following table:

                         D    320 x 200, EGA mode 13 (not an EGA
                              Paint format)
                         E    640 x 200 EGA mode 14
                         R    640 x 350 EGA mode 16
                         P    640 x 480 extended EGA mode inabled
                              by using /480 option

                    For example, the first 640x350 screen saved will be
                    EGASCRNA.SCR, then EGASCRNB.SCR, etc.  These files
                    are written to the current working directory of the
                    default disk drive.

                    GRABEGA uses a little known feature of the EGA BIOS
                    called the "dynamic save buffer" to determine the
                    palette settings of the EGA at the time of the
                    screen capture.  Programs that alter the EGA palette
                    settings by writing directly to the registers on the
                    adapter card will probably produce captured screens
                    with invalid colors.  Microsoft WORD is the only
                    example of this behavior that I've found so far.

                    The files produced by GRABEGA can be converted to
                    CompuServe Graphic Interchange Format (GIF) picture
                    files by the EGA2GIF utility included in this
                    package.  All but the 320x200 screens can also be
                    read and edited using EGA Paint 2005 by RIX
                    SoftWorks.

          TSR Shell Credit:

                    Much of the stability of GRABEGA is due to the fine
                    TSR shell copyrighted 1987 by Thomas Brandenborg,
                    Lundbyesgade 11, DK-8000 Aarhus C, DENMARK.

          Shareware license:

                    You are granted a non-exclusive license to use
                    GRABEGA for your personal enjoyment.  You may not
                    sell GRABEGA or include it with other software you
                    offer for sale.  If you use GRABEGA regularly
                    because it fills a unique graphics need then a $10
                    donation to SPARKS, 1609 Tulip Dr., Arlington, TX
                    76013 would be appreciated.  If GRABEGA is used in a
                    commercial environment then it MUST be licensed for
                    $10 per active copy.  Contact SPARKS for details on
                    site licenses, custom versions and GIF applications.








          GRABEGA                                               Page 3
          Command
          ------------------------------------------------------------
                    SPARKS also offers shareware versions of EGA2GIF (a
                    GIF encoder) and EGAGIF (a GIF viewer).  These also
                    carry shareware contrbution or commercial licenses
                    of $10 per package.  Any two of these may be
                    licensed for $15 and all three may be licensed for
                    $20.

          Graphics Interchange Format and GIF are trademarks of
          CompuServe, Inc. an H&R Block Company.  EGA Paint 2005 is a
          trademark of RIX SoftWorks, Inc.  QuickBASIC, SYMDEB and Code
          View are trademarks of Microsoft.