01
      ESC  -  Emergency Shutdown.

                This  function key causes the reactor to  execute 
                an  Emergency  SCRAM.   The rods are sent to  the 
                bottom,  and  the make-up feed pump speed is  in-
                creased  to  100% and the make-up  feed  flow  is 
                directed to the primary loop.   The primary drain 
                valve  is shut and the emergency cooling pump  is 
                started.   This function key will safely shutdown 
                the  reactor  and minimize damage to the  reactor 
                core.  It should be used in any emergency.
02
      F1  -  SCRAM.

                This function key shuts down the reactor by send-
                ing  the rods to the bottom and by  shutting  the 
                primary drain valve.  This function key should be 
                used  while conducting a normal shut-down of  the 
                reactor.  Care must be taken to prevent damage to 
                the  reactor  core due to low  pressurizer  level 
                when using this function key.
03
      F2  -  Primary Drain Valve.

                This  function  key  controls the  primary  drain 
                valve which is used to maintain pressurizer level 
                within the required range on 50-85%.   This  fun-
                ction  key alternately opens and shuts the  drain 
                valve.

04
      F3  -  Turbine Trip Valve.

                This  function key controls the position  of  the 
                turbine  trip  {bypass}  valve which is  used  to 
                prevent  liquid water from entering the  turbine.   
                This  valve  should be open  {Turb  Trip  warning 
                (Yellow)  on} whenever heat exchanger temperature 
                is  below  100C.   Care should be  taken  not  to 
                exceed  the condenser pressure/temperature limits 
                when operating this valve.
05
      F4  -  Generator Field Control.
 
                This  function key controls the  generator  field 
                and  speed control system.   The generator  field 
                must  be  on for production of power.   When  the 
                generator field is on, the turbine speed is auto-
                matically regulated to 3,600 RPM to maintain  the 
                electric  current frequency at 60 Hz.   This fun-
                ction  key  provides the only direct  control  of 
                turbine speed.
06
      F5  -  Automatic Control.

                This  function  key controls  the  automatic  rod 
                height  control system which is designed to main-
                tain  the  heat exchanger  temperature  near  the 
                control set point temperature.   This system fun-
                ctions  only  above 500C reactor temperature  and 
                will  maintain the temperature within  the  range 
                specifed  by  the Bias setting below the  control 
                set point temperature.
07
      F6  -  Automatic Set-point.

                This  function  key controls  the  automatic  set 
                point   computer.    This  computer  adjusts  the 
                control set point and primary and secondary cool-
                ant  pumps to maintain the production rate  above 
                the demand.   This computer should generally only 
                be used when the demand is above 1700 KW.
08
      F7  -  Pressurizer Heaters.

                This  function key controls the pressurizer  hea-
                ters which are used to maintain a steam bubble in 
                the pressurizer.   The steam bubble creates pres-
                sure  on the primary loop which prevents  boiling 
                in the reactor core,  which could cause fuel ele-
                ment failure or meltdown.    The pressurizer hea-
                ters  must be on any time the reactor temperature 
                exceeds 100C.    Primary coolant pressure must be 
                at  least 2X reactor core temperature to  prevent 
                damage to the reactor core.

09
      F8  -  Lube Oil Pump.
 
                This  function key controls the operation the the 
                turbine and generator lubricating oil circulation 
                pump.   This  pump provides high pressure oil  to 
                the bearings of the turbine and  generator.   The 
                Lube  oil pump must be on whenever the turbine is 
                operating.
10
      F9  -  Condenser Circulating Pump

                This   function   key  controls   the   condenser 
                circulating  pump.   This pump  provides  coolant 
                flow  for the condenser.   The exhaust steam from 
                the  turbine  is condensed into  water,  and  the 
                condensate  is pumped to the steam generator  for 
                recycling.   This pump should be operating  when-
                ever the secondary temperature is above 212F.
11
      F10  -  Auxiliary Power.  

                This  function key controls the  auxiliary  power 
                source  which  is used to provide electricity  to 
                the  reactor plant whenever the generator is  not 
                functioning.   Auxiliary power is required during 
                start up and shutdown of the reactor  plant,  and 
                should be on at all times.
12
      Left Arrow  -  Plant Display.
 
           This  function  key swithes the  display  between  the 
           graphic  and  numeric displays.   The numeric  display 
           shows the current value of the specific system values.  
           This display also shows the last 5 log entrys,  if the 
           Autolog-Screen  function  is  selected.   The  graphic 
           display  shows  a schematic of the plant and  a  chart 
           displaying  the  last  30 minutes  of  the  four  most 
           important indicators.   Pumps,  valves, and levels are 
           indicated  on the schematic.   Pumps that are off  are 
           indicated  by  an  '+',  pumps that  are  running  are 
           indicated  by an 'O',  and pumps that have failed  are 
           indicated  by an 'X'.   Shut valves are indicated by a 
           solid  white circle.   Open valves are indicated by  a 
           black stripe indicating the direction of flow  through 
           the valve.  Fluid levels are indicated by white blocks 
           in the various vessels and storage tanks.  Turbine and 
           generator  speeds  are indicated by the angle  of  the 
           throttle  vanes  in the symbols.   A  horizontal  vane 
           indicates  speed  0,  and  a verticle  vane  indicates 
           normal operating speed.

13
      Up Arrow  -  Alarm Silence.

           This  function key switches the audible alarm  on  and 
           off.   The alarm sounds whenever there is a warning or 
           danger indication on the alarm panel.

99