Building a DAC:
---------------
  Well...although there are many different ways to build yourself a DAC, 
I'm only going to demonstrate 1 way...the simplest and cheapest way <g>.

Ingredients:
  1 25 pin male D type plug
  8 resistors, in ratios of approximately 1:(2:4:8:16:32:64:128), such as
  5k1ê, 10kê, 20kê, 39kê, 82kê, 160kê, 330kê, 620kê
  a 390ê resistor
  a 100nf capacitor to smooth the signal out
  some insulated wire to connect it all up
  something to build the circuit on, such as some stripboard
  a socket for the output to connect it to your amplifier
  an amplifier

Instructions:
                                                         100nf
                                                       ÚÄÛÃÄÄÄ>signal to amp
                                                       ³ ÚÄÄÄÄ>ground to amp
                                                       ³ ³
                                                   390ê±±±
              ÚÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄ´ ³
          5k1ê± 10ê± 20kê± 39kê± 82kê±160kê±320kê±640kê± ³
             ÚÁÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÁ¿D plug
             ÀÂÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÂÙ
pin number    2    3     4     5     6     7     8     9 25

Build the  circuit,  as shown above,  and connect it to  your amplifier
(maybe active walkman-style speakers,  or a stereo system), plug it into 
your parallel port and tell DOMINATION  that you have a Mono/1 DAC on  
whatever parallel port you plugged it into.  You can build two of these, 
and then tell DOMINATION that you have a Stereo/2 DAC if you want stereo 
explosions <g>.   More ways to build better DAC's are  available in the 
file 'hardware.doc'  that comes with Mark J Cox's  MODPLAY program,  
and his Stereo-on-1 and DAC's  that use a ZN426E  chip sound better,
but are harder to build.  When you have built and tested this DAC you 
should put it in a case to prevent  it from short-circuiting, and possibly
damaging your computer.