SHOW87 Version 1.10
                       Copyright (c) 1987-1988 Eric Tauck
                               All Rights Reserved
                                   03/06/1988

       SHOW87 is a memory resident program that displays the entire state
       of an installed 8087 coprocessor chip.  This program will only
       work if an 8087 is present.  SHOW87 is very useful when debugging
       code that contains 8087 instructions.

       SHOW87 has two modes of installation.  The default is the shell
       mode in which SHOW87, rather than making itself truly resident,
       executes a DOS shell.  This allows you to deinstall SHOW87 by
       typing EXIT at any DOS prompt.  The disadvantage of the shell mode
       is that a second command processor must be invoked, which uses an
       extra 3000 to 4000 bytes of memory.  The other type of
       installation is the resident mode, which is specified by the /R
       parameter. SHOW87 uses less memory in this mode, but cannot be
       removed.  SHOW87 alone uses about 5700 bytes of memory.

       Once installed, the program may be invoked at any time by pressing
       ALT-7. Invoking SHOW87 causes most of the upper half of the screen
       to display the flags, registers, and other information regarding
       the 8087.  Pressing any key exits the display and restores the
       screen.  The normal sequence of events is to install SHOW87 before
       debugging 8087 code and then removing SHOW87 when it is not needed
       any longer.

       If SHOW87 cannot properly install itself, it will display an error
       message and terminate.  The most common reasons for such an error
       are insufficient memory and COMMAND.COM not found.  COMMAND.COM is
       only needed when SHOW87 is run in the shell mode.  SHOW87 finds
       the COMMAND.COM file by looking for the COMSPEC parameter in the
       environment (see your DOS manual).

       SHOW87 displays all 8087 information, including the instruction
       pointer, the operand pointer, the operation code; the control,
       status, and tag words; the precision, rounding, and infinity
       control settings; the stack top; the condition codes and their
       various interpretations; the exception settings and interrupt mask
       settings; and the register values.

       The condition code settings represent C3, C2, C1, and C0
       respectively.  The Comp, Test, and Exam fields display the meaning
       of the condition codes as returned by the FCOM, FTST, and FXAM
       instructions.

       Register values are displayed in one of two ways.  If the number
       has a tag setting of VALID, the number is displayed in decimal
       format.  If the number has a tag setting of SPECIAL or EMPTY, a
       hexadecimal dump of the number is displayed.  After the mantissa
       and exponent, the type of value (as interpreted by the FXAM
       instruction) is displayed.