VI.   EXTENDED MEMORY 



1.   MEMORY MAP OF F-PC


 
F-PC was built to handle a class of programming problems that
require very large memory and cannot be handled well on any normal 
64K implementation of Forth because of space constraints. 

The memory map of F-PC can be shown schematically as follows:


                |---------------------| ?CS:
         ^      |                     |
         |      |       Forth         |
         |      |       Kernel        |
         |      |                     |
         |      |---------------------|
         |      |       System        |
         |      |     Extensions      |
         |      |---------------------| HERE, DP @
         |      |     Dictionary      | PAD, DP + 80
         |      |     Free space      |
        64k     |         |           |
       bytes    |         v           |
         |      |         ^           |
         |      |         |           |
         |      |     Data stack      |
         |      |---------------------| SP0 @
         |      |        TIB          | TIB, 'TIB @
         |      |         |           |
         |      |         v           |
         |      |         ^           |
         |      |         |           |
         v      |    Return stack     |
                |---------------------| RP0  @, End code space.

                |---------------------| YSEG @, Start head space.
         ^      |       hash table    |
         |      |---------------------|
         |      |                     |
        64k     |       headers       |
       bytes    |                     |
         |      |---------------------| YHERE,  YDP @
         |      |       header        |
         v      |     free space      | YHERE + 65535
                |---------------------|

                |---------------------| TSEGB, TSEGE
         ^      |                     |
     64k bytes  |     Edit Buffer     |
         |      |                     |
         |      |---------------------| LSEG
         |      |  Line pointer list  |
         |      |---------------------| DSEG
         |      |  Lines deleted buf  |
         |      |---------------------| RSEG
         v      | Restore display buf |
                |---------------------|

                |---------------------| XSEG @, Start list space.
         ^      |                     |
         |      |       List of       |
         |      |                     |
        64k     |  Colon Definitions  |
       bytes    |                     |
        or      |     and Strings     |
       more     |                     |
         |      |---------------------| XHERE,  XDP @
         |      |                     |
         |      |       header        |
         |      |     free space      | 
         v      |                     |
                |---------------------|




F-PC allows the list (colon space) segment to be much larger than
64K bytes.  Strings have also been moved out of code space back 
into LIST space, which means there is effectively unlimited space 
for text messages.  In fact the only real limitation in size comes 
from the fact that there are only 64k available for heads.  
Calculations indicate there is room for about 3300 definitions on 
top of the current system of about 2000 words.  This calculation 
is based on an average name length of 5 characters, with an 
average header length of 12 bytes.  With 5300 total definitions, 
less than 30k of code space would be used for code fields of colon 
definitions, leaving the remaining 30+k of code space for 
variables and arrays.  Not an infinitely large application 
obviously but probably large enough for most (99%) applications. 

F-PC places a segment (ES) and and offset (IP) on the return stack
for each nest operation. Only the starting relative segment is 
compiled into the code field, and the conversion to absolute 
segment is performed by NEST.  This makes the code fully 
relocatable as is required by the DOS environment.  Some 
performance could be gained by using absolute segment addressing, 
and performing a conversion at save and load time to and from 
relative and absolute, but I have not done this, and don't plan to 
for now.  The performance gain would come from having a simpler 
NEST, what would not need to perform the relative to absolute 
conversion at runtime.  This system looses about 20% in 
nest/unnest performance due exclusively to that conversion. 

CS and DS always point to the code space, and so all assembly 
language operations work with data in the code segment unless a 
special operator like @L or !L is used to reach an external memory 
area.  This means there is no penalty to be paid for most Forth 
operations. 

Here is the data structure used for a colon definition in F-PC:
 


                                     ----------------
            HEAD SPACE               [ VIEW offset  ] VIEW
                                     [ LINK pointer ] LINK
                                     [      83 hex  ] NAME
                                     [   H          ]
                                     [   E          ]
                                     [   X + 80 hex ]
                Points to CODE space [ CFA pointer  ] --------v
                                     ----------------         |
                                                              |
                                     ----------------         |
            CODE SPACE               [     CALL     ] CFA <---<
                                     [     NEST     ]
                Points to LIST space [ LIST POINTER ] BODY >--v
                                     ----------------         |
                                                              |
                                     ----------------         |
            LIST SPACE               [ cfa of (LIT) ] LIST <--<
                                     [     16       ]
                                     [ cfa of BASE  ]
                                     [ cfa of   !   ]
                                     [ cfa of UNNEST]
                                     ----------------


2.   EXTENDED MEMORY WORD SET



A complete set of words are defined in F-PC to let the user
accessing the extended memory very conveniently.  The standard 
Forth memory accessing words are retained for addressing the 
code/data segment in the memory.  Generic extended memory words 
are appended with the letter L, and they require address 
specifications in segment/offset pairs.  Words addressing the list 
space have X prefix and words addressing the head space have Y 
prefix. 

Generic Extended Memory Words are those which require explicit 
segment information with the 16 bit address offset.  They are the 
basic word set from which other segment specific memory words are 
derived.  This word set includes the following words: 

@L        ( seg addr -- n )        Fetch 16 bit integer.

!L        ( n seg addr -- )        Store 16 bit integer.

C@L       ( seg addr -- b )        Fetch a byte.

C!L       ( b seg addr -- )        Store a byte.

CMOVEL    ( seg addr seg' addr' n -- )
                                   Move n bytes from seg-addr to
                                   seg'-addr'.

CMOVEL>   ( seg addr seg' addr' n -- )
                                   Move n bytes in revered order.

LFILL     ( seg addr n b -- )      Fill n bytes at seg-addr 
                                   with b.

LDUMP     ( addr n -- )            Dump n byte from segment pointed
                                   to by DUMPSEG with addr offset.


Following are words addressing the list space: 


X@        ( addr -- n )            Fetch an integer in list space 

X!        ( n addr -- )            Store integer to list space 

XC@       ( addr -- b )            Fetch byte.

XC!       ( b addr -- )            Store byte.

X,        ( n -- )                 Compile integer to top of
                                   the list dictionary. 

XC,       ( b -- )                 Compile byte to the list 
                                   dictionary.

XDUMP     ( addr n -- )            Dump n bytes in the list 
                                   segment.

?XS:      ( -- seg )               Return the base of the list 
                                   segment.

XDP       ( -- addr )              Pointer to top of list 
                                   dictionary. 

XHERE     ( -- addr )              Address of top of list 
                                   dictionary. 

XPERFORM  ( addr -- )              Execute word at addr.



The corresponding words addressing into the head space are: 


Y@        ( addr -- n )            Fetch integer from head space. 

Y!        ( n addr -- )            Store integer to head space. 

YC@       ( addr -- b )            Fetch byte.

YC!       ( b addr -- )            Store byte.

Y,        ( n -- )                 Compile integer to head 
                                   dictionary.

YCSET     ( b addr -- )            Set bits in a byte.

YDUMP     ( addr n -- )            Dump n bytes from addr in the
                                   head space. 

YDP       ( -- addr )              Pointer to top of head 
                                   dictionary.

YHERE     ( -- addr )              Address of top of head 
                                   dictionary.



3.   MEMORY ALLOCATION

 

Finally, two very important words which allows you to allocate and 
deallocate extended memory by asking the DOS for unused free 
memory:


ALLOC     ( n1 -- n2 seg flag )    Request n bytes of free memory
                                   from DOS.  Flag=0 if ok, 8 if
                                   not enough memory.  Seg is the
                                   segment base of the allocated
                                   memory.  n2 byte actually
                                   allocated.

DEALLOC   ( seg -- flag )          Release a block of memory to 
                                   DOS.  Seg should be the same
                                   as obtained from ALLOC.
                                   Flag=0 if ok, 9 if seg is not
                                   valid.