SCRNLIB  

















           
                                  By Dave Millis     
                                     P.O. Box  2371
                                     Glenview, Illinois 60025

















          Copyright 1987 by Dave Millis.  All rights reserved




                                                                          2
          SCRNLIB release 1

          INTRODUCTION

               SCRNLIB is a library of text screen routines for the Micro-
          soft and Turbo C compilers.  Most of the routines were written in
          assembly language for the optimum in speed and performance. 
          These routines remedy some of the deficiencies of C by allowing
          screen output in color and allowing for the use of windows.  

               I was a Turbo Pascal user for two years before I started to
          program heavily in C on the PC.  In February 1987, I purchased
          the Microsoft 'C' Compiler 4.0.  I always appreciated the
          flexibility and sheer power of C, but I missed the many simple
          text output functions of Turbo Pascal.  I then decided to write
          the functions I needed.  After working on this part-time for
          several months I collected all the routines into a file called
          SCRNLIB.LIB.  These routines were tested by several friend and
          co-workers who offered some constructive criticism and
          suggestions.  They even found a couple of bugs.  With the
          correction of the bugs; the addition of some procedures; and some
          minor modifications so the routines will work with both Turbo C
          and the Microsoft 'C' Compiler, SCRNLIB release 1 was completed.

               I am an active programmer and I have a bachelor's degree in
          computer science.  I am now primarily using C and assembly and I
          generate a multitude of routines that can be beneficial to many
          programmers.  I am using SCRNLIB to see if there is an interest
          in these fast, efficient routines.  If there is, later versions
          will include more direct memory access screen procedures, more
          sophisticated windowing, and many other helpful routines.

               By now you might be asking-

          DO I NEED SCRNLIB?

               Well, I feel SCRNLIB is the best way to output text to the
          screen with a color attribute.  By "color attribute" I mean the
          method that the characters are displayed on the screen.  For
          monochrome display cards, this means underlined, bold, and
          inverse video text.  The C programming langauge does not provide
          these functions in a nice workable way.  One can use ANSI to help
          with screen manipulations, however this would require ANSI.SYS be
          installed on every machine using these programs and the output
          would be slower than if SCRNLIB was used.  The SCRNLIB routines
          do not require ANSI.SYS be installed and should run on all
          systems with standard video hardware (ie. MA, HMA, CGA, EGA)
          including most third party video boards.  Since these routines
          were written in assembly, they run as fast as possible.  There is
          no doubt that other software producers will develope libraries or
          C source code collections that will allow for some of these same
          functions; however, If they are not written in assembly, they

          Software and Documentation Copyright 1987 by Dave Millis


                                                                          3
          SCRNLIB release 1

          will not be as fast as SCRNLIB's routines.

               SCRNLIB also allows other input/output operations.  For
          example, inpstr is a function that enables string inputs from the
          keyboard.  This function is necessary because the input functions
          in standard C does not allow echoing of the input with the
          currently set color attribute.

               If Windows are desired, SCRNLIB provides a great way to
          generate and maintain them.

          WINDOWING

               SCRNLIB provides for a specified area of the screen to be
          the only area written to or effected by many screen operations. 
          The area, referred to from now on as the active window, is easily
          defined and "remembered" by the program.  Once defined, the
          active window can be cleared, written to, and scrolled up and
          down using the normal screen functions provided in SCRNLIB
          without effecting the rest of the screen.  Output functions, such
          as printsh and putsch, continue output at the beginning of the
          next line of the active window when the right end of the active
          window is encountered.  The windows can also be saved and
          restored later anywhere on the screen. 

          Window Example:
               Say you want to open a window 30 x 5 characters in size to
          display a message and ask for input from the user of your
          program.  Lets also say you want this window to disappear and
          restore the screen to its original condition when you're done
          with it.  This is what you would do:

          1) Save the current screen below where the window will go.  This
             is done with the scrnsav command:

               int x;               /*number of char. in the input string*/
               char undrwindo[152]; /*define a character string large      
                                     enough to save the screen in*/

           --> scrnsav(undrwindo,25,10,54,14); /*save portion of screen */
               getpos();   /* read current cursor position (into global    
                              variables xposn and yposn  */

             see the Command section for a full explanation of all commands

          2) Next, set the active window:

               window(25,10,54,14,0);/*declare active window w/ no border*/

          3) To have this window stand out from the rest of the screen, we

          Software and Documentation Copyright 1987 by Dave Millis


                                                                          4
          SCRNLIB release 1

             will change the foreground and background color attributes:

               setattr(1,4);  /* blue on red */
               cls();
               gotoxy(27,12);

             This sets the color attribute, clears the 30 x 5 active screen
             and positions the cursor over 2 and down 2 form the top left
             corner of the window.  At this point the screen looks
             unchanged except for a 30 x 5 red square in the center.

          4) Writing the message is straight forward:

               printsh("What is your mother's maiden name? ");

             This is not the best way to present this message, but it
             illustrates how the windows work.  The problem is the message
             is longer than the width of the screen.  What happens is the
             sentence up through "maiden" is printed, then "name? " is
             printed on the next line starting at 25,13.

          5) Input is handled with the inpstr function:

               x=inpstr(mommaname);

          6) Finally, now that we have the information we require, we need 
             to restore the screen to its original condition and position
             to its old position:

               scrnrst(undrwindo,25,10);
               gotoxy(xposn,yposn);


             While windows are not an extensively used function in a lot of
          programs, the functions in SCRNLIB provides a lot of practical
          applications.  For example, If you want to generate a program
          that actively uses the entire screen except for the 25 row where
          the function keys or other information is always displayed, an
          active window 80 x 24 can be defined.  This way only the top 24
          rows will be written to and when the bottom of the active window
          is reached the top 24 rows will scroll up, leaving row 25
          unchanged.


          USING SCRNLIB WITH TURBO-C

               When compiling a program in the integrated environment,
          SCRNLIBx.LIB must be specified in a project file.  For example,
          to run DEMO.C with the small memory model, DEMO.PRJ would look
          like:

          Software and Documentation Copyright 1987 by Dave Millis


                                                                          5
          SCRNLIB release 1


               DEMO
               \TURBOC\LIB\SCRNLIBS.LIB

          (assuming that the SCRNLIBx libraries are in the \TURBOC\LIB
          directory)

          MORE TECHNICAL INFORMATION

               In release 1, all but three of the routines were written in
          assembly, using the Microsoft Macro Assembler 4.0.  In the
          interest of speed and efficiency, the error checking was kept to
          a minimum, as is typical of C.  It is up to the programmer to
          make sure that the proper variables are passed and the proper
          amount of memory is allocated for the arrays used.  See the
          section of commonly made errors for an explanation of the errors
          most often made in using SCRNLIB.

               In all routines that require an X and Y location, it must be
          noted that the top left corner of the screen is 0,0 (not 1,1). 
          This means the bottom right corner is 79,24.

               There are several global variables used by SCRNLIB that are
          accessible to the programmer too:  oldcurs, scxlow, scxhigh,
          scylow, scyhigh, txtattr, xposn and yposn.  These keywords should
          not be used in other contexts.  There exact meanings are as
          follows:

               oldcurs contains the start and stop scan lines of the cursor
          saved with the cursoff function and used by the curson function. 
          It is uninitialized at the start.

               scxlow and scylow define the upper left corner of the active
          window.  scxhigh and scyhigh define the location of the lower
          right corner of the active window.  The default values defined in
          the header file are: scxlow=0, scylow=0, scxhigh=79, scyhigh=24; 
          this is just the entire screen.  These values can be changed
          individually in a program, or through the window command.

               txtattr contains the current text color attribute (default
          is 07).     

               xposn and yposn are the current X and Y position of the
          cursor set when the function getpos is executed.  These
          variables, along with the getpos function, exist for the use of
          the programmer to easily get the cursor location.  xposn and
          yposn are only changed by the getpos function and therefore can
          be used to store the cursor location.



          Software and Documentation Copyright 1987 by Dave Millis


                                                                          6
          SCRNLIB release 1

          COMMONLY MADE ERROR WITH SCRNLIB

               1) Probably the most common problem results from not declar-
          ing string variables large enough to hold all the data put in
          them.  This over writes other portions of the program and causes
          it to crash.  This usually occurs with the scrnsav function and
          one should carefully read about this function before using it.

               2) A stack overflow is a common problem when numerous screen
          saves are preformed.  This is because many local variables are
          stored in the stack area and the screen data strings are very
          large.  This problem is also not detected using the default
          settings in Turbo-C.  If your program behaves peculiarly, turn on
          the stack overflow checking in the Code generation menu in the
          Options-Compiler menu.  The easiest way to correct this problem
          is to use global arrays (ie. declare the arrays outside of any
          functions-this includes function main).  If the arrays aren't too
          large, you can use the MS link and use the /stack option to
          increase the size of the stack.  I have not had success using
          EXEMOD to increase the size of the stack on   Turbo-C (TLINK
          linked) files with the stack overflow checking on.
           
               3) Trying to address the last column or the last row of the
          screen with 80 or 25 respectively does not work since the bottom
          right corner is 79,24.  This is because the first column and the
          first row are both defined as zero (0).

               4) Forgetting to include the SCRNLIB.H file at the beginning
          of the program can cause problems.

          DISCLAIMER

               I do not guarantee that the SCRNLIB functions will do
          anything.  However, I have tried to write the best, most effi-
          cient, and most portable functions that I could, and have tested
          them extensively on eight different makes and models of MS-DOS
          based microcomputers.  I also do not guarantee that SCRNLIB will
          not do anything harmful to anything nor anybody.  Any discrep-
          ancies or problems should be brought to my attention so that I
          could improve upon them before the next release.  At this time, I
          believe SCRNLIB is in perfect working condition.  THE USERS OF
          SCRNLIB ARE SOLELY RESPONSIBLE ITS EFFECTS IN THEIR CODE. 

          TRADE MARKS

          Turbo Pascal and Turbo C are registered trade marks of Borland
          International, Inc.

          MS-DOS, MS, Microsoft, and Microsoft 'C' Compiler are a
          registered trade mark of Microsoft Corp.

          Software and Documentation Copyright 1987 by Dave Millis


                                                                          7
          SCRNLIB release 1

          REFERENCE

               Even though these routines were written in assembly they
          conform to the C calling standard and are used as normal C
          procedures and functions.  The names have been chosen to describe
          the function and so they appear as a natural extension of the C
          language.

          **************************
          beep

          PROTOTYPE:

               void beep(void);

          DESCRIPTION:

               I admit this is a very unimpressive procedure to start with,
          but I do use it quite often.  This routine simply sound the
          standard 800 Hz sound for 1/4 seconds.

          **************************
          cls

          PROTOTYPE:

               void cls(void);

          DESCRIPTION:

               This clears the active screen using the current attributes.


          **************************
          cursoff

          PROTOTYPE:

               void cursoff(void);

          DESCRIPTION:

               This turns off the cursor and saves the old cursor type in
          the global variable oldcurs.  This allows for the old cursor to
          be restored.  Also allowed is the ability to turn off the cursor
          then change to a different form of cursor, using setcurs, then
          use curson to restore the original cursor.  Remember that cursoff
          must be executed before curson will restore the old cursor.

          also see: curson,setcurs

          Software and Documentation Copyright 1987 by Dave Millis


                                                                          8
          SCRNLIB release 1

          **************************
          curson

          PROTOTYPE:

               void curson(void);

          DESCRIPTION:

               Restore the cursor stored in the global variable oldcurs.

          also see: cursoff,setcurs


          **************************
          getkey

          PROTOTYPE:

               char getkey(void);

          DESCRIPTION:

               This get a character from the keyboard.


          **************************
          getpos

          PROTOTYPE:

               void getpos(void);

          DESCRIPTION:

               Gets the current position of the cursor and puts the X and Y
          positions in the global variables xposn and yposn respectively. 
          These two variables, xposn and yposn, are only affected by this
          function (and a direct assignment), so they can be used to
          reference the position where getpos was last executed.











          Software and Documentation Copyright 1987 by Dave Millis


                                                                          9
          SCRNLIB release 1

          **************************
          gotoxy

          PROTOTYPE:

               void gotoxy(int xloc,int yloc);

          DESCRIPTION:

               gotoxy positions the cursor at the screen position defined
          by xloc and yloc.  The X position and Y position are xloc and
          yloc respectively.  This function is not limited by the active
          screen.


          **************************
          inpstr

          PROTOTYPE:

               int inpstr(char *str);

          DESCRIPTION:

               inpstr gets a string input from the keyboard and echoes the
          input on the screen using the current attributes.  The string of
          input is stored in *str.  The returned integer is the number of
          characters entered.


          **************************
          keywait

          PROTOTYPE:

               char keywait(void);

          DESCRIPTION:

               keywait clears the keyboard then waits for a single
          keystroke from the keyboard.  The returned character is the ASCII
          value of the first byte of input from the key board.  If the key
          pressed is a special function key, such as the function keys or
          the arrow keys, the return character will be 00h.  Since these
          special keys input a series of two characters, a character will
          remain in the keyboard buffer and the function getkey can be used
          to get the second character. 




          Software and Documentation Copyright 1987 by Dave Millis


                                                                         10
          SCRNLIB release 1

          **************************
          movxy

          PROTOTYPE:

               void movxy(int xdis,int ydis);

          DESCRIPTION:

               This moves the cursor vertically and horizontally from its
          current position.  xdis and ydis are the displacements from the
          current cursor position in the X and Y position respectively.



          **************************
          printmch

          PROTOTYPE:

               void printmch(char *chr,int numprn);

          DESCRIPTION:

               printmch prints a single character a specified number of
          times horizontally on the screen using the current attributes. 
          If the number of characters exceeds the space to the right side
          of the screen the remaining characters will rap around the
          beginning of the next line.  If the printing proceeds to the
          bottom right corner of the screen, the screen will not scroll and
          the remaining characters will not be printed.  This procedure is
          not limited by the active screen.  *chr is the character to be
          printed and numprn is the number of times *chr is to be printed.
          This function, along with printmcv, was primarily written to draw
          frames and lines on the screen, usually outside the active
          screen.  
               printmch, along with all the printing routines, uses the
          BIOS to output to the screen.  In future releases, there will be
          the option of doing output using the BIOS or direct memory
          access.  There will be a global variable that will dictate which
          method is to be used.  This variable can be changed in the
          program, so a command line option can be added to your programs
          to set the output method.

          also see: printmcv






          Software and Documentation Copyright 1987 by Dave Millis


                                                                         11
          SCRNLIB release 1

          **************************
          printmcv

          PROTOTYPE:

               void printmcv(char *chr, int numprn);

          DESCRIPTION:

               printmcv prints a single character a specified number of
          times vertically on the screen using the current attributes.  If
          the number of characters exceeds the space to the down the rest
          of the screen, the remaining characters are not printed.  *chr is
          the character to be printed and numprn is the number of times
          *chr is to be printed.  This procedure is not limited by the
          active screen.  This function, along with printmch, was primarily
          written to draw frames and lines on the screen, usually outside
          the active screen.

          also see:printmcv


          **************************
          printsh

          PROTOTYPE:

               void printsh(char *str);

          DESCRIPTION:

               printsh prints a string horizontally in the active window
          using the current attributes.  If the end of the active window is
          reached, the string continues on the next line of the active
          window.  If the end of the active window is reached the window
          will scroll up and the rest of the string will be printed.  All
          of the back slash (\) functions are supported as they are in the
          standard C printf procedure;  however, the % functions for
          printing numbers and other strings are not supported yet.  To
          generate output in the same fashion as printf the sprintf
          function can be used alone with printsh:

               sprintf(txt,"a=%d  b=%d",a,b);
               printsh(txt);

          Remember to include stdio.h when using sprintf.  
               Support for numbers and additional strings is currently one
          of my primary projects.
           
          also see printsv,putsch

          Software and Documentation Copyright 1987 by Dave Millis


                                                                         12
          SCRNLIB release 1

          **************************
          printsv

          PROTOTYPE:

               void printsv(char *str);

          DESCRIPTION:

               printsv prints the given string vertically in the active
          screen using the current attributes.  If there is not a enough
          space from the current cursor position to the bottom of the
          window the remainder of the string is truncated.  The only back
          slash commands supported are the \a and \b.  Like the printsh
          routine, the % format specifications are not supported, yet.

          also see printsh,putsch

          **************************
          putsch

          PROTOTYPE:

               void putsch(char *chr);

          DESCRIPTION:

               putsch prints a single character at the cursor position with
          the current attribute.  This function only works in the active
          window and advances to the next line of the active window after
          printing a character in the last active column.  All the back
          slash commands are supported.

          also see printsh,printsv

          **************************
          scrldn

          PROTOTYPE:

               void scrldn(int);

          DESCRIPTION:

               scrldn scrolls the active screen down the number of rows
          specified by int.  The current background attribute is used for
          the blank lines added to the top of the screen as the screen
          scrolls.

          also see scrlup

          Software and Documentation Copyright 1987 by Dave Millis


                                                                         13
          SCRNLIB release 1

          **************************
          scrlup

          PROTOTYPE:

               void scrlup(int);

          DESCRIPTION:

               scrlup scrolls the active screen up the number of rows
          specified by int.  The current background attribute is used for
          the blank lines added to the bottom of the screen.

          also see scrldn


          **************************
          scrnoff

          PROTOTYPE:

               void scrnoff();

          DESCRIPTION:

               scrnoff blanks the screen.

          also see scrnon
          **************************
          scrnon

          PROTOTYPE:

               void scrnon();

          DESCRIPTION:

               scrnon turns the screen back on after a scrnoff has been
          executed.

          also see scrnoff










          Software and Documentation Copyright 1987 by Dave Millis


                                                                         14
          SCRNLIB release 1

          **************************
          scrnrst

          PROTOTYPE:

               void scrnrst(char *str,int xl,int yl);

          DESCRIPTION:

               scrnrst restores a saved screen that was saved with scrnsav
          or scrnsavd.  str is the character array that stores the screen
          information, xl and yl makeup the x and y position of the top
          left corner of where the window is to be restored.

               scrnrst(d) can also be used with scrnsav(d) to move windows.
          A window or an area of the screen can be saved and then restored
          at a different location by specifying a different xl and yl in
          the restore cammand.  The dimensions of the screen remain the
          same as they are stored in the data string.

          also see scrnrstd,scrnsav,scrnsavd


          **************************
          scrnrstd

          PROTOTYPE:

               void scrnrstd(char *str,int xl,int yl);

          DESCRIPTION:

               scrnrstd works exactly like scrnrst.  The only difference is
          that scrnrstd uses direct memory access to restore the screen. 
          This provides a great speed enhancement over scrnrst, which uses
          the BIOS, but it may not be as portable to other computers.

          also see scrnrst,scrnsav,scrnsavd













          Software and Documentation Copyright 1987 by Dave Millis


                                                                         15
          SCRNLIB release 1

          **************************
          scrnsav

          PROTOTYPE:

               void scrnsav(chr *str,int xl,int yl,int xh,int yh);

          DESCRIPTION:

               scrnsav saves a rectangular portion of the screen.  The
          information from this portion of the screen is stored in the
          character string str.  xl and yl define the upper left corner and
          xh and yh define the lower right corner of the rectangle. 

               Calculation to determine the size of *str:

               size = (2 x (xh - xl + 1) x (yh - yl + 1)) + 2)

          This is simply the size of the window times 2, plus 2.  The
          reason for this is 2 bytes must be stored for each character on
          the screen, one for the character and one for the attribute, then
          the first 2 bytes of the string contain the size of the array
          (more specifically the X size and Y size).

               It is VERY important that *str is large enough to hold all
          the data.  Unpredictable results will occur if this space is too
          small.  It does not make any difference if this space is too
          large.

          also see scrnrst,scrnrst,scrnsavd


          **************************
          scrnsavd

          PROTOTYPE:

               void scrnsavd(chr *str,int xl,int yl,int xh,int yh);

          DESCRIPTION:

               scrnsavd works exactly like scrnsav.  The only difference is
          that scrnsavd uses direct memory access to save the screen.  This
          provides a great speed enhancement over scrnsav, which uses the
          BIOS, but it may not be as portable to other computers.

          also see scrnrst,scrnrstd,scrnsav




          Software and Documentation Copyright 1987 by Dave Millis


                                                                         16
          SCRNLIB release 1

          **************************
          setattr

          PROTOTYPE:

               void setattr(int fgrnd,int bgrnd);

          DESCRIPTION:

               setattr sets the current color attribute to be used for the
          screen output functions.  fgrnd is an integer from 0-15 that
          specfies the foreground color.  These numbers correspond to:

            0 - Black                    8 - Gray   
            1 - Blue   (underline)       9 - Bright Blue (bright underline)
            2 - Green                   10 - Bright Green
            3 - Cyan                    11 - Bright Cyan
            4 - Red                     12 - Bright Red
            5 - Magenta                 13 - Bright Magenta
            6 - Brown                   14 - Yellow or Bright Brown
            7 - White                   15 - Bright White

          The descriptions in parentheses are for monochrome cards.
               bgrnd is an integer also from 0-15 where 0-7 specifies the
          background color.  0-7 correspond to the same colors as the
          foreground colors above.  8-15 correspond to a the same
          background color as 0-7 respectively, but causes the foreground
          color to blink.  


          **************************
          setcurs

          PROTOTYPE:

               void setcurs(int curstrt, int curstop);

          DESCRIPTION:

               setcurs set the cursor type.  curstrt is the first scan line
          and curstop is the final scan line that makes up the cursor. 
               The cursor is defined by the number and positions of lines
          that make it up.  For example, the cursor on a CGA is made up of 
          lines 6 and 7 (curstrt=6, curstop=7).  A box cursor on a CGA
          would be: curstrt=0, curstop=7.  The total number of line on a
          monochrome is 14 (0-13).  If curstrt is larger than curstop, the
          scan lines will wrap around and the cursor will appear as two
          sets of lines.

          also see cursoff,curson

          Software and Documentation Copyright 1987 by Dave Millis


                                                                         17
          SCRNLIB release 1

          **************************
          window

          PROTOTYPE:

               void window(int xl,xin yl,int xh,int yh,int brdrtype);

          DESCRIPTION:

               window sets the active window.  xl and yl define the top
          left corner and xh and yh are the lower right corner of the
          window.  brdrtype is the type of border that will be drawn around
          the window: 0 is no border, 1 is a single line boarder, and 2 is
          a double line border.  This border is drawn OUTSIDE of the active
          screen.  This means that if a border is specified, the total
          boundaries of the screen will be: xl-1,yl-1,xh+1,yh+1.  One word
          of warning, do not try and draw a border around a window that has
          an edge of the ACTIVE screen as one of its borders.  This will
          usually cause the border to be printed at the other edge of the
          screen (It wraps around).































          Software and Documentation Copyright 1987 by Dave Millis


                                                                         18
          SCRNLIB release 1

          REGISTRATION

               I wrote SCRNLIB with the purpose of making programming a
          little bit easier and a little bit more fun.  With this in mind,
          I would like to encourage everyone who uses SCRNLIB to freely
          copy it and upload it to other bulletin boards providing that: 1)
          No fee is charged for such copying and distribution and 2)
          SCRNLIB is distributed ONLY in its ORIGINAL form, unmodified in
          anyway.  

               I do ask, however, that those who find SCRNLIB useful become
          registered users and obtain a license for its use.  Only
          registered users may use SCRNLIB in the development of their own
          programs and may sell or distribute these programs to others. 
          Registered users will also receive technical support and will be
          informed of any major developments and improvements.

               To register, just send $10 along with the attached
          registration form and in return I will mail you : 1) the Latest
          Version of SCRNLIB including libraries that work with each of the
          Small, Medium, Compact, and Large memory modules. 2) The Latest
          Documentation. 

               If you try SCRNLIB and feel it's not quite for you, please
          still send us your opinion of the product and any suggestions.  I
          welcome and encourage any input anyone has. 
          ________________________________________________________________
          cut along dashed line and mail with check for $10 per license
          and $1 postage and shipping for each disk requested to DAVE
          MILLIS PO BOX 2371, GLENVIEW, ILLINOIS  60025
          - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

          I HAVE ENCLOSED $_______ FOR _____ COPIES OF SCRNLIB TO BE
          REGISTERED  TO:

          NAME_______________________________

          COMPANY____________________________
           
          ADDRESS________________________________________________________

          CITY_______________________________

          STATE__________ ZIP CODE____________

          PHONE (  )______________________    (  )_______________________

          CURRENT RELEASE IN YOUR POSSESSION _________

          ___ PLEASE CONTACT ME ABOUT QUANTITY PRICING OR SITE LICENSING.

          Copyright 1987 by Dave Millis.  All rights reserved.


                                                                         19
          SCRNLIB release 1

          FUTURE RELEASES

               All the printing routines use the BIOS to output to the
          screen.  In future releases, there will be the option of doing
          output using the BIOS or direct memory access.  There will be a
          global variable that will dictate which method is to be used. 
          This variable can be changed in the program, so a command line
          option can be added to your programs to set the output method.

               I currently have several more functions that I have not
          tested thoroughly enough yet to include with this release.  They
          include functions that:  set the border color; check and set the
          video mode (SCRNLIB functions work in 40 character mode also);
          allow for a max number of characters to be input with the string
          input function; support more sophisticated windowing; ... and
          many more.



































          Copyright 1987 by Dave Millis.  All rights reserved.