Samson

                          offers:


                 _____  _       _
                |  __ \(_)     | |
                | |  | |_  __ _| |_   _ _ __
                | |  | | |/ _` | | | | | '_ \
                | |__| | | (_| | | |_| | |_) |
                |_____/|_|\__,_|_|\__,_| .__/
                                       | |
                     Version 3.03      |_|
                     ------------




          PLEASE READ THE DOCS, DIALUP IP IS NO EASY THING!

    PLEASE TRY THE OPTION 'TEST', IT IS INCREDIBLY HELPFUL. YOU CAN
    TEST EVERYTHING LOCALLY WITHOUT WASTING ANY MONEY ON PHONECALLS.


         ITS NOT PUBLIC DOMAIN, ITS NO SHAREWARE, NO FREEWARE,
          GIFTWARE OR CARDWARE AND HAS NO COPYLEFT OR -RIGHT.

             ITS SIMPLY A PROGRAMM TO USE, IF YOU LIKE.

             AND EVEN BETTER: IT NOW COMES WITH SOURCES!
               (If you have troubles with the program,
                first take a look at the sourcecode.)



 P U R P O S E:
 --------------

 This programm is intended to establish a dialup IP connection (SLIP or PPP)
 to another computer. It is assumed that a modem or a similiar device is
 connected to a serial line of your amiga. (An ISDNMASTER with approriate
 device does work, too)



 R E Q U I R E M E N T S:
 ------------------------

 - Installed and *tested* AmiTCP or AS225
 - appropriate Sana2 Driver for your intended connection
 - min. OS 2.04



 H O W   T O   B E G I N:
 ------------------------

 To start, you should do the dialup manualy, first. If you have figured
 out the commands for the modem and its results, and the questions of the
 remote site and the expected answers, you can use dialup with the
 appropriate options:

   LOGINPROMPT, LOGINNAME, PASSWORDPROMPT, PASSWORD, CONNECTSTRING, etc..

 A few of them are required, but most of them are optional and only neccesary,
 if you have a strange modem or remotesite.

 To make small steps from the manual to the automatic dialup, you can
 save your modem settings together with the phonenumber in the modem. If you
 do this, you can already use the defaults for MODEMSETTINGSCONNECT=MSC (ATZ1)
 and PHONENUMBER=PN (ATDS1). The modemcommands for saving config and
 phonenumbers are:

    AT&Z1=xxxx and AT&W1 

 If you have configured dialup correctly (SANADEVICE=SAD and SANAUNIT=SAU),
 the ONLINE and OFFLINE CLI-commands of the SANA-device are obsolete,
 cause dialup handles this by itself.


 N O T E S:
 ---------

 The program is residentable (pure with the help of cres.o)

 HINT: To test the program, use the option TEST. This performs a modem
 ====  internal loopback instead of a real CONNECT. You can see what will 
       go on during CONNECT, HANGUP, etc..
       With SLIP you can even ping yourself or ftp, etc..
       THIS WORKS WITH AMITCP, TOO, IF YOU REMOVE THE ROUTE FOR 'OWNHOST' TO
       THE LOOPBACKINTERFACE. USE: 'route delete <yourhostname>' or see the
       script at the end of the docs!


 S A V I N G   C O N F I G U R A T I O N:
 ----------------------------------------

 It is possible to set any option in ENV:Dialup (Setenv Dialup "PASSWORD=ItsMe")

 BEWARE: ONLY the FIRST LINE gets parsed!

 To check the settings (from ENV:Dialup) and its parsing, use:

    'dialup DEfaults ALL'



 D E S C R I P T I O N   O F   P A R A M E T E R S:
 ==================================================

 The template is:

 
                Dialup [COMMAND] [OPTIONS]


  WARNING:
  ========

   Please  note, that COMMAND is optional, too. This means, that if you accept
   the default command (TOGGLE), any misspelled option gets the COMMAND instead
   of the default one and probably pops up the usage requester. Every other
   wrong  option  (or  even  the  first,  when you specified a COMMAND, gets a
   PHONENUMBER.  This  is  not  my  fault, this is the documented behaviour of
   dos.library/ReadArgs() on /M paramters.



 COMMAND=CMD
 ===========

 The default is TOGGLE.
 The command can be specified without keyword. The first word of the
 commandline, which is not a keyword or switch of the template, is
 taken as the command.

 After any successfully performed command the global environment varialble
 'SLIPCARRIER' is set to 'ON' or 'OFF'.

 Possible commands:

 CONNECT=CO        Try to build a modem connection.
                   Basically this performs:

                       ATZ1, ATDS1, <loginchat>, sana online

                   If you want to be sure, that the connection is
                   established, when you start ftp or some other 
                   networking stuff, write a script which calls

                       Dialup CONNECT QUIET

                   before the net application. QUIET suppress' the
                   warning, if you are already connected.
                   See 'C H A T   O P T I O N S' for the loginchat.
                   Result: 1 if success, 5 if modem is already online

 HANGUP=HA         Break a connection. This even works during full
                   data transfer. (Cause it sucks :-) the serial line)
                   Basically this performs:

                       +++ ATZ1 sana offline

                   If you have a feed, which calls you when packets
                   arrive, you will be called back. To make the modem
                   take the call by itself, the NORECONNECT option must
                   not be set.
                   Result: 0 if success

 TOGGLE=TO         Toggles between CONNECT and HANGUP, depending on
                   carrier
                   Result: see CONNECT/HANGUP

 TAKE=TA           Sends a ATA\r (MODEMOFFHOOKCMD=MOH) to the modem
                   after RINGS=RGS\K\N rings (MODEMRING=MRG\K) are
                   detected and makes sana device online.
                   If a carrier is detected on startup, only the sana
                   device is made online.
                   Result: 3 if success

 QUERY=QU          Querys the modem for some information, even when
                   connected. This will work only with the NODTRIGNORE
                   switch not set (or you configured the modem to
                   ignore DTR anyway).
                   Basically this performs:

                       sana offline  +++  ATI2  ATO  sana online

                   See MODEMQUERYCMD for the type of information
                   gathered from modem. To get a nice status report from
                   modem you could use:

                   > dialup QUery RePortFile "CON:100/100/400/200/..
                                    ..Dialup Query/CLOSE/INACTIVE/WAIT"
                   Result: 2 if success

 OFFLINE=OF        sana offline
                   Result: 0 if success

 ONLINE=ON         sana online
                   Result: 0 if success

 CARRIERDETECT=CD  sana offline, if no carrier and online if carrier.
                   Meaningfull options: AUTOANSWER=AA and if this is 
                   set RINGS=RGS and MODEMSETTINGSCONNECT=MSC
                   Result: 0 if offline, 5 if online

 CHECK=CH          Possible at any time! It only sets a returncode:
                   Result: 0 if no carrier, 5 if carrier

                   In addition to this the global environment variable
                   'SLIPCARRIER' is set to 'ON' or 'OFF' after this and any
                   other successfully performed command.

             Note:
                   For checking the serial line without hitting
                   the hardware directly, it is neccessary to
                   offline/online the slip device to open the
                   serial.device. This normaly doesn't disturb an
                   ongoing transmission.

 DEFAULT=DE        Query any option for its default. Helpfull to see
                   what will be sent to modem, and chated with your
                   remote site. Use GIVEALLSETTINGS=ALL if you want
                   to see all the default parameters (including
                   ENV:DIALUP) or name a specific.

                       1> setenv DIALUP "MSC=ATsomething"
                       1> Dialup DEFAULT MODEMSETTINGSCONNECT
                       MODEMSETTINGSCONNECT=MSC/K: ATsomething

                   or 

                       1> Dialup DEFAULT GIVEALLSETTTINGS
                       CONNECTSTRING=CS/F: 19200/V42b
                       SANAUNIT=SAU/K/N: 0
                       SANADEVICE=SAD/K: Networks/rhcslip.device
                       NORECONNECT=NRC/S: OFF

                       [ .. ]

                       RINGS=RGS/K/N: 1
                       MODEMCONNECTTIME=MCT/K/N: 40
                       REDIALDELAY=RDD/K/N: 60
                       PHONENUMBER=PN/K/M: ATDS1 
                       MODEMSETTINGSCONNECT=MSC/K: ATZ1


 O P T I O N S:
 ==============

 General notes on paramters:

  - All options can be kept set for any of the above commands, but not all
    have a meaning to a specific command.

  - To send special chars, use \n for LF, \r for CR and \t for TAB.
    To send a single \ use \\.

  - For any expected string you can use patterns:

        Pattern Matches
        ------- -------
           ?    any single character
           c*   zero or more occurrences of character c
           c+   one or more occurrences of character c
           \?   a question mark (?)
           \*   an asterisk (*)
           \+   a plus sign (+)
      
        Any other character must match exactly.
        The following table lists some examples:

        Pattern Matches
        ------- -------
          abc   only abc
          ab*c  ac, abc, or abbc
          ab+c  abc, abbc, or abbbc
          ab?*c a string starting with ab and ending in c, for
                example, abxyzc
          ab\*c only ab*c

  - Multiple matching strings:

        If there is more than one possible string you can specify all
        of them, sparated by '|'. To specify '|' use '?'.
        Example:  MOK="OK|DONE" or MODEMLINEBUSY="NO CARRIER|BUSY"

    I thoght a long time about implementing the pattern matching
    through dos calls, but the parsing and specifying of parameters
    would have been a pain:

      (#?BUSY\n#?)|(#?NO CARRIER\n#?)|(#?CONNECT#?19200#?\n)|etc.

    Write me a mail, if you really would like to have it.



 B A S I C    O P T I O N S:
 ---------------------------


 PHONENUMBER=PN/K/M      The phonenumber(s!) to dial.
                         If the parameter has a leading 'AT' or '!' no ATD
                         is sent before the number. ('!' will be stripped)
                         Default: S1                    -> ATDS1

                         Example: 1234                  -> ATD1234
                                  ATDP1234              -> ATDP1234
                                  !foobar               -> foobar

                                  pn S1 pn=S1 pn ATDP1234\
                                           -> ATDS1 ATDS1 ATDP1234
                                 If the call fails with BUSY, it would wait
                                 the REDIALDELAY and try again. If this
                                 fails, too, it immediately trys 1234.

                Warning: Everything what cannot be identifyed as an option
                =======  or a COMMAND will get a phonenumber. This is not
                         my fault, this is the documented behaviour
                         of dos.library/ReadArgs() on /M paramters.


 SANADEVICE=SAD/K,       Sana device to use. You have to specify
                         'Networks/yoursana.device', if it is in DEVS:Networks.
                         Default: "NetWorks/rhcslip.device"


 SANAUNIT=SAU/K/N,       Sana unit to use.
                         Default: 0


 SANACONFIGFILE=SCF/K,   Config file of the sana device. It must match:

                         "SERNAME/A,SERUNIT/A/N,SERBAUD/A/N,IPSTR/A,..
                         ..CD=CARRIERDETECT/S,7WIRE/S,EOFMODE/S,MTU/K/N,THEREST/F   

                         Examples:

                              ppp%d.config, ppp0.config, sys:devs/myconfig

                         Default: "ENV:SANA2/slip0.config"
                         (This file gets read by *any* slip device)


 REDIALDELAY=RDD/K/N     Seconds to wait after a BUSY (MLB\K) before calling
                         the *same* number(s) again. If you specify 0 it will
                         NOT retry on BUSY.
                         Default: 180


 RINGS=RGS/K/N           Number of rings to wait before the modem should
                         take an icomming call. This takes effect only
                         after a HANGUP or CARRIERDETECT with AUTOANSWER!
                         With the TAKE command this in the number of RINGs
                         to receive from the modem, before takeing the
                         call. For TAKE it is possible to specify 0.
                         Default: 1



 O P E R A T I N G   M O D E S:
 ------------------------------


 AUTOANSWER=AA/S         Take any incomming call after HANGUP, sana stays
                         online. The parameter RINGS tells the modem how
                         many rings it should wait before offhook.
                         Default: OFF


 NODTRIGNORE=NDI/S       Disable the sending of AT&D0 to the modem before a
                         CONNECT and AT&D2 after HANGUP. Normaly AT&D0 is
                         necessary, to not drop the line befor makeing
                         sana online.
                         Default: OFF


 NOSERINIT=NSI/S,        To avoid initialisation of serial line with the
                         parameters from 'ENV:SANA/slip0.config' (in fact
                         SANACONFIGFILE=SCF/K; it is read anyway, to get
                         the device(name) to open)
                         Default: OFF


 NORECONNECT=NRC/S,      No autoanswer during CONNECT (e. g. carrier lost,
                         remote site calls back).
                         Modem takes phone after first ring until you do
                         a HANGUP without AutoAnswer.
                         Default: OFF




 R E P O R T   A N D   D E B U G   O P T I O N S:
 ------------------------------------------------


 CONNECTSTRING=CS/K      This string is expectd as the connectstring from
                         the modem. If its not found, a requester pops
                         up, telling you the actual connect message.

                         If you specify CONNECT you will never see a
                         requester(If your modem gives at leas this answer
                         for a connect).

                         With this parameter it is possible to use patterns.
                         See top note for information on patterns.
                         Default: "CONNECT*?19200/V42b"


 REPORTFILE=RPF/K        Where to put the report of the serial communication.
                         Note: I've never observed that dialup looses *ANY*
                         character. If you have troubles with the serial
                         communication, it is sometimes helpfull to send
                         the output to a file and view it with:

                             1> type <reportile> hex

                         Another good use is to specify a window like

                         RPF="CON:100/100/400/200/Dialup/CLOSE/INACTIVE"

                         When you press the (toolmanager) hotkey to start
                         dialup, you can see whats going on. If there is no
                         error, it is closed after successful connection. If
                         an error occours, and you started it with '< NIL:'
                         somehow, a requester pops up, telling you the failure.
                         But during this time the RPF window keeps open and you
                         can examine every detail of the report. I realy like
                         this!
                         Default: stdout

                         
 QUIET/S                 Be quiet to stdout and suppress all non fatal messages.
                         Default: OFF


 STDEER/S                No requesters anymore. Errors and warnings are sent
                         to '*' (console) as long as '*' could be opened and
                         even if there is an interactive inputstream
                         (e.g. shell) for the program.
                         Default: OFF


 VERBOSE/S               Reports all internal function calls with strings sent
                         to serial line and all expected returns. To avoid
                         intermixing these messages with the serial
                         communication itself, a console widow gets the
                         default for RPF.
                         Default: OFF


 TEST/S                  This is a very helpfull option. Instead of dialing
                         a number, it does AT&T1. This is a modem internal
                         loopback mode. This enables you to do a ping to
                         yourself *over* the modem. You can even do a ftp to
                         your machine and check the max. transmission speed.
                         After this you can QUERY the modem and look for any
                         errors. This is true for AmiTCP, too. See script at
                         the end. The tcp-test (ping, etc.) is not possible
                         with ppp, however, cause it uses a more complicated
                         transmission concept and doesn't accept this simple
                         loopback.
                         Default: OFF


 GIVEALLSETTIGNS=ALL/S   This switch is only valid with the DEFAULT command!
                         It shows all current defaults. ENV:Dialup takes
                         effect!



 C H A T   O P T I O N S:
 -----------------------

    Note:   The sequence of the chat after CONNECT is:
    =====
            - [Wait and] Send WAKEUPSTRING
            - Wait for LOGINPROMPT
            - Send LOGINNAME or $HOSTNAME.
            - Wait for PASSWORDPROMPT, if not ""
            - Send PASSWORD
            - IF SNDLOGINNAME specified, wait for SNDLOGINPROMPT
            - IF SNDLOGINNAME specified, send     SNDLOGINNAME
            - IF SNDPASSWORD  specified, wait for SNDPASSWORDPROMPT
            - IF SNDPASSWORD  specified, send     SNDPASSWORD=SPW
            - Wait for LOGINOK=LOK if not ""


 WAITBEFORWUS=WBW/K/N    Seconds to wait befor sending WUS
                         Default: 3

 WAKEUPSTRING=WUS/K      String is sent after connect, before 'ogin:' (LIP)
                         is expected. Remember:
                         Use \n for LF, \r for CR and \t for TAB.
                         To send a single \ use \\.
                         No default.



 LOGINPROMPT=LIP/K       Prompt of the remote site to enter your name.
                         To skip login and password communication use
                         LIP="".
                         Default: "ogin:"


 LOGINNAME=LIN/K         Name to send after receiving the LOGINPROMPT. If
                         not specified, it will be taken from the environment
                         variable HOSTNAME.
                         No default. (or ${HOSTNAME})


 LOGINTIMEOUT/K/N        Seconds to wait for the loginprompt of the remote
                         site.
                         Default: 3




 PASSWORDPROMPT=PWP/K    Prompt of the remotesite to enter your password.
                         With this parameter it is possible to use patterns,
                         too. See LOGINPROMPT=LIP
                         To skip password communication use PWP="".
                         Default: "assword:"


 PASSWORD=PW/K           String to send after the PASSWORDPROMPT is received.
                         No default.




 SNDLOGINNAME=SLIN/K     This gets sent, if specified at all, after receiving
                         what is set for                     (no default)


 SNDLOGINPROMPT=SLIP/K   Default: ogin:


 SNDPASSWORD=SPW/K       This gets sent, if specified at all, after receiving
                         what is set for:                     (no default)


 SNDPASSWORDPROMPT=SPWP/K Default: "assword:"




 LOGINOK=LOK/K,          Message of the remote site after succesfull login.
                         Use LOK "" to skip this check.
                         Default: "Packet mode enabled"
 

 LOGINOKTIMEOUT=LOT/K/N  The timeout (in seconds) for the answer (LOK) to a
                         successfull login.
                         Default: 3



 M O D E M   A D J U S T M E N T:
 -------------------------------

 MODEMSETTINGSCONNECT=MSC/K  Command string to send to the modem before 
                         any attempt to connect. If you don't want to
                         send something use MSC ""
                         Default: ATZ1


 MODEMCONNECTTIME=MCT/K/N  The time in seconds, the modem needs to dial and
                         handshake with the remote site.
                         Default: 61


 MODEMSETTINGHANGUP=MSH/K Command string to send to modem after HANGUP.
                         To avoid this completely use MSH "".
                         Default: ATZ1


 MODEMQUERYCMD=MQC/K     Hayes commands to query modem. This command is sent
                         to the Modem to query the modemstatus ( or
                         anything else you want to know ).
                         You even can change the configuration of the
                         modem, during it is online.
                         Default: AT&VI2


 MODEMREADYCMD=MRC/K     Command, the modem answers with MODEMCMDOK=MOK/K (OK)
                         Default: AT


 MODEMHANGUPCMD=MHC/K    Command to make the modem drop line.
                         Default: ATH0


 MODEMNOCARRIER=MNC/K    Answer of modem on failed CONNECT
                         Default: NO CARRIER


 MODEMLINEBUSY=MLB/K     Message of modem when line busy.
                         Default: BUSY


 MODEMLINEDEAD=MLD/K     Message of modem when it doesn't get a dialtone.
                         Default: NO DIALTONE


 MODEMRING=MRG/K         Message of modem when a call comes in.
                         Default: RING


 MODEMANYCONNECT=MAC/K   Message of modem if a connection of any kind has been
                         established.
                         Default: 'CONNECT?*'     (see LOGINPROMPT)


 MODEMCMDOK=MOK/K        Answer from Modem if command is ok.
                         Default: OK


 MODEMAACMD=MAAC/K       Make modem take phonecall after RINGS=RGS/K/N
                         Default: ATS0=%d


 MODEMOFFLINECMD=MOC/K   Make modem accept commands again (offline)
                         Default: +++


 MODEMONLINECMD=MLC/K    Bring modem online again
                         Default: ATO


 MODEMTESTCMD=MTC/K      modem to internal loop-back mode
                         Default: AT&T1


 MODEMOFFHOOKCMD=MOH/K   make modem off hook and answer the call.
                         Default: ATA


 MODEMTESTOFFCMD=MTO/K   switch of  modem loopback
                         Default: AT&T0


 MODEMCMDOK=MOK/K        Answer from Modem if command is OK
                         Default: OK



 A d d i t i o n a l   n o t e s:
 --------------------------------

  The stackusage is about 3000 Bytes and the memoryusage is less
  than 30K Bytes.

  As long as dialup is started from a console (input not NIL:), the
  program messages and the input from the serial line are sent to it.
  If you start it without console, but don't want to see any requester,
  use option STDERR.

  If you use VERBOSE, a default window is opened for the serial
  input. You can override this by specifying RPF CON:////dialup..

  The best use for this program is to make it startable with a hotkey.
  (e.g. ToolManager) Commandline:

      'Dialup REPORTFILE T:dialup.report'.

  Think about making it resident, if you can afford the memory.

  To stop the program at ANY time press ^C in the shell or start it a second
  time. If you start the program a second time ( e.g. after a BUSY, waiting
  for the REDIALDELAY ) it sends a ^C to its first occurence.  So, if you
  have the programm bound to a hotkey, just press it again to stop the
  (re)dialing.

  To reset the modem I use:

      'Dialup HANGUP NODTRIGNORE MODEMSETTINGSHANGUP ATZ'

  or short:

      'Dialup ha ndi msh atz'

  To get a system, taking incomming calls after every reboot, add

      'Dialup CARRIERDETECT AUTOANSWER QUIET RINGS=n'

  to your user-startup. But this only works if no programm is
  causing slip packets beeing sent to the modem, otherwise the
  modem connect could get disturbed.


  I always load the whole network sw in user startup:

   AS225:
   ------

    8<------------------------------------------
      INET:c/config > ENV:HOSTNAME HOSTNAME
      INET:c/config > ENV:USER USER
      INET:c/ifconfig lo0 127.1
      INET:c/ifconfig s0 $hostname -trailers
      INET:c/Route add default <yourslipsite> 0

      Dialup CARRIERDETECT

      IF WARN
          Ping <yourslipsite>
          IF NOT WARN
              Say "Connected to Intearnet"
          EndIF
      EndIF
  8<------------------------------------------


   AmiTCP:
   -------

    8<------------------------------------------
      Run < NIL: > NIL: AmiTCP:AmiTCP
      WaitForPort AMITCP
      Wait 2 secs
      RX "ADDRESS AMITCP;'SET CON NIL:'" ; stops this 'slip.device online/offline' messages.

      AmiTCP:bin/ifconfig lo/0 localhost
      AmiTCP:bin/ifconfig Devs:Networks/rhcslip.device/0 xxx.yyy.zz.uuu aaa.bbb.ccc.ddd netmask 255.255.255.0
    
      ;AmiTCP:bin/route add troja.mppmu.mpg.de localhost ; remove to enable ping over modem!
      AmiTCP:bin/route add default 134.107.2.51
      AmiTCP:bin/route add 134.107.2.6
 
      Run < NIL: > NIL: AmiTCP:bin/inetd
      Mount TCP:

      Dialup CARRIERDETECT

      IF WARN
          Ping <yourslipsite>
          IF NOT WARN
              Say "Connected to Intearnet"
          EndIF
      EndIF
    8<------------------------------------------


 Then simply start dialup anytime later and you get connected.


 Have fun! Questions and bugreports (?? :-) to:

             Thomas Kobler
             Libellenstr. 29
             80939 München
             Germany

             kobler@mpiw13.mppmu.mpg.de
             +49 89 3241329 (and +49 89 32308311 at work)
             try to 'talk' to me at samson@troja.mppmu.mpg.de or 
                             (kobler@pctok.mppmu.mpg.de at work)


  After all the time I spent on this stuff, I feel that it would be nice, if
  you would send me something: ranging from an email over nice gifts to
  some financial donations. Its up to you.