The Circuit Analysis Program (CAP) is an analysis tool for determine the
steady-state AC behaviour of electrical/electronic networks.
The network may contain resistors, capacitors, inductors, controlled cur-
rent sources (e.g. transistors, op-amps etc.) and independent current sour-
ources.

CAP was originally issued for the HP85, but has been adapted for the ST
after a lot of re-writing and testing.
Although CAP does not have the capabilies of programs like e.g. SPICE, in
small AC circuit analysis however, the output results are satisfactory and
in most cases accurate enough to predict the actual circuit behaviour.

Output can be any node voltage, branch voltage, branch current, branch
power or ratio's thereof.
Tabulated or plotted outputs are available with linear or logarithmic fre-
quency sweeps.

CAP is primary intended for electrical engineers or those who are familiar
with electrical networks and basic electrical/electronic theory.

All files belonging to CAP must be located in folder CAP, including folder
GUIDE, which contains several help-files.
Files with the extension CIR are circuit examples, which can be loaded and
analysed after frequencies and output quantities are selected and calcula-
tions have been performed.

NOTE: Hardcopy of full screen can be made by ALTERNATE+HELP.

We will offer CAP as a public domain program for non-commercial usage and
therefore assume no responsibility and shall have no liability, consequen-
tial or otherwise of any kind arising from the use of this program.




Ger Gruiters

Rank Xerox   Venray The Netherlands

----------------------------  Structure of files ---------------
G6.DOC         851             \CAP\GUIDE
G4.DOC        1114             \CAP\GUIDE
G5.DOC         878             \CAP\GUIDE
G3.DOC        1042             \CAP\GUIDE
G1.DOC         387             \CAP\GUIDE
G7.DOC         998             \CAP\GUIDE
G8.DOC         768             \CAP\GUIDE
G10.DOC        757             \CAP\GUIDE
G9.DOC         643             \CAP\GUIDE
G2.DOC        1035             \CAP\GUIDE
BJT.PIC      32000             \CAP
CAP.PIC      32000             \CAP
CAP.PRG      40980             \CAP
CAPNXT.RSC   20904             \CAP
EX1.CIR        584             \CAP
EX2.CIR        584             \CAP
EX3.CIR        584             \CAP
OPAMP.PIC    32000             \CAP
PARAM.PIC    32000             \CAP
README.DOC    1639             \CAP
WIENBRDG.CIR  1358             \CAP


----------------------------  Documentation   -------------------
1.0 General program usage
    =====================


 -  Select New cir from Menu "Circuit" , select Menu "New cir"
    next and enter a new circuit, or load 'old' circuit from 
    disk (filename.cir).


-   Select frequencies and output quantities before calculation.


-   Plotting is done after calculation.


-   Tables are output automatically during calculation.

2.0 Example of circuit description
    ==============================

    1  IS       0 TO 1  1 AMPS
                0 DEG
    2  L        1 TO 2  2 E-4 H
    3  R        2 TO 3  .33 OHM
    4  C        3 TO 0  2.2 E-4 F
    5  R        2 TO 0  20 OHM

Note in the above example that circuit elements are described by their connec-
ting nodes, their values, and a branch or element number. It is this branch
number which is specified when requesting branch voltages, currents, or pow-
ers for output. You would also specify this number when deleting an element.
Due to the way the program orders itself, as you add independent current sour-
ources they are added to the top of the list. As you add any other elements they
are added to the bottom of the list.

CAP is divide into three sections a) Input of circuit, b) Selection of output
quantities and frequency sweep, and c) Plotting.
These sections are completely independent in that you can change any parameter
of any section and retain all other parameters.

3.0 Input of circuit
    ================

Circuit elements are input from the New circuit Menu, one element at a time
with the required information being the element type, the connecting nodes
and the value of the element, (i.e., 10 Ohm, .1 Henrys, etc.). The first
thing that must be done is to number the nodes. A node, for the purposes of
this program is any point where two ore more circuit elements meet. The no-
des must be consecutive integers, consecutive numbered nodes need not have
any special topological relationship to each other.
While inputting each element, the program will ask for the connecting nodes
with the following question: NODES: FROM, TO?. The FROM node is the node
where the current leaves the element.
For the non-source elements (resistors, inductors and capacitors), it is
not important if you don't know the direction of the current flow. Simply
assume one. If you assume wrong, the current will be computed 180 degrees
from the expected direction.
Study the example's EX1.CIR and EX2.CIR.


4.0 Selection of Output Quantities and Frequency Sweep
    ==================================================

After a circuit has been input, but before calculation beings, you will need to
select those quantities you wish to observe and the frequencies at which to ob-
serve them. There are two ways that the program can provide output. printed
table of up to 50 quantities per frequency, or a displayed plot.
Only one method can be selected at a time.

Available output quantities are node voltages, branch voltages, branch currents
branch power and ratio of any two quantities. Node voltage zero is not avail-
able for output, but is always 0 volts at 0 degrees. A branch voltage is the
voltage across an element. It is the node voltage at the positive node minus
the node voltage at the negative node. The positive node for a controlled or
independent current source, by convention, is the node where the current leaves
the source (the TO node). The positive node for resistors, inductors and capa-
citors again by convention, is the node where current enters the element ( the
FROM node.


All output quantities are given in magnitude and phase format. For power this
means that real power, is measured in watts at 0 degrees.
Reactive or imaginary power, measured in VARS, is +90 degr. for inductors and
-90 degr. for capacitors.
For non-
source elements power is defined as power absorbed. For source elements
power is defined as power delivered. For any given circuit the complex sum of
power delivered by the sources will equal the complex sum of the powers absor-
bed by the elements.

The frequency sweep is selected by specifying a minimum frequency, a maximum
frequency, and an increment. If the increment is positive each new frequency
will be the old frequency plus the increment. If the increment is negative,
you have specified a logarithmic sweep with each new frequency equal to the
old frequency times the absolute value of the increment.


5.0 Plotting
    ========

Plotting is accomplished after calculations are performed. The magnitude
and phase of the output quantity selected are stored for up to 50 frequen-
cies. With the same set of data you may make any number of plots.

You need not select any plotting parameter. Automatic labeling and scaling are
default. The automatic labeling puts out the following information: whether
you're plotting magnitude or phase, the output quantity, and whether dB's
are selected for ratios. If automatic labeling is not sufficient you may
select any 18 characters. If you wish to select different scaling parame-
ters you may select the maximum. minimum and the space between the tic marks.
These parameters may be selected independently for the X and directions.
You may even leave one direction automatic and select the other.

6.0       Additional explanation for some commands
          ========================================

New cir  : Enter a new circuit, same input as add element.
Add elem : Add circuit element to an already existing circuit.

RES         When R NODES :FROM, TO? is displayed,
IND      1) Enter the node where currents enters the resistor followed by
CAP         a comma.
         2) Enter the node where current leaves the resistor.
            When VALUE? is displayed enter the resistance in Ohms.
            The same is done when entering an inductor or capacitor where
            the value is entered in the resp. quantity.

IS          When IS NODES: FROM, TO? is displayed,
         1) Enter the node where current enters the source, followed by
            a comma.
         2) Enter the node where the current leaves the source.

            When AMPLITUDE is displayed, enter the amplitude in Amperes.
            When PHASE is displayed, enter the phase in degrees.

6.1    continued

VCIS   : Add a voltage controlled current source

         When CONTROLLING NODES: +, -? is displayed,
      1) Enter the number of the positive controlling node followed by a 
         comma.
      2) Enter the number of the negative controlling node.
      
         When CONTROLLED NODES: FROM, TO? is displayed,
      1) Enter the node where the current enters the controlled source
         followed by a comma.
      2) Enter where the current leaves the controlled source.

         When gm is displayed,
         Enter the transconductance in Siemens.

Del elem:To delete circuit elements when ELEMENT #? is displayed.
         Enter the element #, as it is numbered in the circuit descrip-
         tion (0 for none). 

6.2  continued

TABLE  : Select tabular output quantities.
PLOT   : Select plotted output quantities.

Note that both TABLE and PLOT clear any previous selected output quantity.

dB     : Default dB is on and all ratios are output in dB.

FREQS  : When MIN FREQ? is displayed,
       
      1) Enter minimum or starting frequency in Herz

         When MAX FREQ? is displayed,

      1) Enter the maximum or ending frequency in Herz

         When INC[(-) FOR LOG]? is displayed,

      1) Enter an additive frequency increment
         OR
      2) Enter the negative of a multiplicative frequency increment.            

6.3  continue

When output quantities are selected enter the number of the branch or node
as defined by the circuit description. Note that branch power S is a com-
plex number (S=V*I) and will be output in magnitude and phase format.

If you wish to calculate ratio's (in most cases):
 
1) First select the numerator (e.g Node Voltage  2 in previous example).
2) Click next Ratio "/" (becomes shaded) 
3) Select the denominator (e.g. Node Voltage 1 in previous example).

If PLOT is selected ONLY 1 ratio or value can be selected at the time.
If TABLE is selected up to 21 ratios or quantities can be selected.

The SUPERIMPOSE function superimposes the next plot over the last plot
(dashed line), using the next plot's scaling parameters.