This README file of NCP.ZIP accompanies MAXNCP.NLM for NetWare v3.10a.
The following files are included:

	MAXNCP.NLM	1581	10-17-90
	PATCHMAN.NLM	4174	10-29-90
	PATCHMAN.DOC	3300	11-01-90

If a user has an application that uses all that is available of the NCP 
search table, this patch is a good work around until you go to 3.11 or
get a later revision of the application.

This patch is designed for Netware 386 version 3.10a.  The patch manager
NLM must be loaded prior to loading MAXNCP.NLM.  Loading MAXNCP.NLM will
increase the upper limit of NCP searches from 1000 to 5000.  After loading
the NLM, use the SET command to increase the NCP search limit variable.
Example at the server console type:

load patchman                  (if patchman has not been loaded)
load maxncp                    (resets the upper limit for ncp searches)
set Maximum Outstanding NCP Searches=5000


WARNING !!!!!!!!!

Increasing the number of NCP searches will decrease the ammount of RAM
available to NETWARE.  Using this patch will either decrease your number of
connections to less than 100 or require that additional RAM be added.
The following formula will help in determining how much additional 
RAM will be needed to maintain the same amount of working RAM on your
server:

24000 x (Maximum Outstanding NCP Searches / 1000) x Number of Stations

EXAMPLE:
For 100 stations and 5000 NCP Searches, the additional RAM would be:
24000 x (5000 / 1000) x 100 = 12 Meg of RAM

*****************************************************************************
                                  DISCLAIMER 
 
     Novell, Inc. makes no representations or warranties with respect to this
software patch, and specifically disclaims any express or implied warranties
of merchantability, title, or fitness for a particular purpose. 
     Novell's intentions for this software patch is to provide a temporary
work-around to the anomalies described in this file.  Such work-arounds are
typically addressed in future releases of NetWare. 
     Novell will not be responsible for any data loss that may result from
implementing this patch.  Novell strongly recommends a backup be made before
any patch is applied.   Technical support for this patch is provided at the
discretion of Novell.  
*****************************************************************************