M e ga C A D

                        The Efficient Program for
                        Drawing and Constructing

            MegaCAD is a highly efficient CAD program for professional use.
        This program is not a public domain software  or  "freeware".   All
        rights  are  reserved by the program's author.  MegaCAD's Shareware
        Version is restricted in various points as  in  comparison  to  the
        full  version.   Several  additional modules provided with the full
        version are not included.  Nevertheless this is not a demo version,
        but a fully functioning programm.

            The software was developed by MEGATECH Software GmbH.  MEGATECH
        is a software house for graphical computer programs located in West
        Berlin,   FRG,   specialised  in  the  field  of  construction  and
        production.

            Much capital has to be invested for the development of good CAD
        programs  of  this  quality,  so  they  obviously cannot be sold as
        low-cost programs at dumping prices.  Furthermore, it always  takes
        quite  some  time to become familiar with a program of this quality
        and complexity.  It may take only a couple  of  minutes  to  get  a
        first impression, but before buying it, you would surely want to be
        totally convinced of its efficiency and  whether  the  software  is
        suited for your daily use.

            Many  CAD programs have to be sold at a high consumer price due
        to costly sales negotiations  and  program  demonstrations  by  the
        supplier.

            Shareware  is  a  unique  marketing  concept  which avoids high
        marketing costs and simultaneously offers the possibility of buying
        software  without  any  risks.   Many software companies in the USA
        have been using this concept successfully for  a  couple  of  years
        now.

            This  shareware version is meant to convince the buyer that the
        full version is an excellent product.  The interested customer  has
        the unique opportunity to test MegaCAD on his own hardware.  Surely
        you don't mind that the  shareware  version  is  restricted  as  in
        comparison to the full version.

            Many  PC  users  will  find  the capabilities of this shareware
        version to be sufficient.  For professional use, though, it will be
        necessary  to  acquire  the full version in order to be able to use
        the product in an economical manner.

            It is permitted and also desirable to hand  on  the  absolutely
        free  and therefore non-commercial shareware version.  In this case
        it is not allowed to charge  a  commission  for  copying  or  other
        services.

            Commercial distribution or charge-free handing-on in connection
        with hardware or software is only allowed with  written  permission
        from MEGATECH Software GmbH  or the distributor Kirschbaum Software
        GmbH.   Among  other  reasons  this  measure  is   to   avoid   the
        distribution of no longer current shareware versions.  Although the
        information provided on  MegaCAD's  Shareware  Diskette  should  be
        sufficient,  we  would  like to ensure professional consultation by
        the shareware supplier.

        For more information please contact :

         Kirschbaum Software GmbH
         Kronau 15, D-8091 Emmering b. Wbg.
         West Germany

         Tel. 08067/1016    
         Fax. 08067/1053


            As Megacad is continuosly being developed,  the  functions  and
        the arrangement of the software are subject to change without prior
        notice.  Our shareware users' requests and experiences are of vital
        importance  for  further  development  of  our  software.   We  are
        therefore open to your suggestions and/or complaints.
          

	  Differences in the full version vs.
          the shareware version

          1.  Dimensioning module with no restrictions
          
          2.  Hatching module with no restrictions

	  3.  Text with various fonts
 
	      Additional fixed fonts using vectors, and a program
	      enabling you to generate and edit fonts of your own.

	  4.  Plotter driver

              Drawing output on all common plotters, with a plotter 
              program for the arrangement of drawings and details of 
	      drawings, simulated on the screen.


          5.  Laser Driver

              for all HP compatible laser printers.


          6.  Printer Driver

	      for high resolution output up to 360*360, in color on
              all common printers.  


          7.  Interface for Desk-top Publishing Program

              graphical adoption in HP GL format

          8.  No restrictions on editing functions

	  9.  Memory space not restricted by paging on hard disk
              or EMS memory after 4.0

          10. Coordinate Interface not restricted

	  11. Reading and generating of DXF formats

	  12. Window driven menu program

	  In order to work with the modules mentioned above, the full
	  version of Megacad must be purchased.
          

          Important Information for a Fast Lead-in
          ========================================

          -   Program Installation

                  On  the  Shareware  Diskette  you  will  find  the   file
              'INSTALL.BAT'.   This program is used for installing MegaCAD.
              For installation you have to enter the graphic card  in  use,
              and where MegaCAD is to be stored.

                  Insert  Shareware Diskette 1 into disk drive A:  and type
              the following at the DOS-prompt :
 

              A:INSTALL  <ENTER>


	      MegaCAD requires a hard disk for installation.

                  Basic requirements for the use of MegaCAD include DOS 2.1
              or  higher,  a Microsoft compatible mouse, at least 512 KByte
              RAM, and an EGA or Hercules graphic card.

                  Versions for other graphic cards (such as  Olivetti)  are
              available on request.

                  We  strongly  recommend  the use of a fixed disk, as only
              with a hard disk is it possible  to  make  full  use  of  the
              program's efficiency.  In addition you should use an AT, even
              better a 386.  MegaCAD automatically uses  the  co-processors
              8087,  80287  and 80387 if installed, increasing the speed 10
              to 20-fold, depending on the application.


	  -   Getting started

	      Type
	      MEGA <ENTER>
	      at the DOS-prompt for EGA or Hercules graphic card.

                  During  the  installation  a  file  named  MEGACAD.INI is
              created where  search  paths  for  drawings  and  macros  are
              stored.   This file is automatically created on installation,
              but it can be modified using an editor.

	  -   Example for CONFIG.DAT:

          PRT:C: MEGACAD PRT *.PRT   /* Drawing path                */
          MAC:C: MEGACAD MAC *.MAC   /* macro path                  */
	  CDL:C:\MEGACAD CDL *.CDL   /* coordinates file path	    */
	  FNT:C:\MEGACAD TFONT*.FNT  /* path text font		    */
	  MAS:C:\MEGACAD TFONT*.FNT  /* path measure font	    */
	  TMP:C:\*.TMP		     /* disk drive TEMP file	    */
          SPE:8                      /* mouse speed                 */
          MOV:10                     /* number of moved elements    */
          CAL:1                      /* calculator                  */
	  DEG:360		     /* 'degrees' per full circle   */
	  MOD:MODE : 0 VGA	     /* graphic mode		    */
          BIO:0012 0000 0000 0000    /* BIOS +calls                 */
          DIM:639 479 16 30 80       /* card parameter              */
          RET:10.8*8.1               /* display monitor             */

            Some mice are too fast or too slow.  You can modify  the  speed
        of  the mouse movement by entering a number between 1 and 10 in the
        line starting with SPE, 1 being the slowest speed, 10 the  highest.
        The value is preset to maximum speed.

            And  now  a short software description.  Please excuse that for
        now, only a description outline is available.

            Every user will certainly find it  easy  to  get  started  with
        MegaCAD  due  to  the  consequent  use  of  graphic symbols.  It is
        unfortunately not possible to realize all of the possibillities  of
        the  program  by  the window driven shell alone, or even by reading
        the following abridged instruction manual.


       Abridged MegaCAD Instructions on Diskette
       =========================================
          
       The Mouse Control
 
            All Microsoft compatible mice are supported.  The mouse buttons
        are  always occupied by the functions 'select' and 'delete' (cancel
        function).

            The left button is always used for choosing one of the  options
        on the menue or for confirming a drawing function.

            The right button cancels a function, either going back one step
        for a new choice, or cancelling the function altogether.



                              º
                    ÚÄÄÄÄÄÄÄÄÄÊÄÄÄÄÄÄÄÄÄÄ¿
                    ³                    ³
                    ³                    ³
		    ³	    MOUSE	 ³
                    ³                    ³
                    ³                    ³
                    ³                    ³
                    ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
                    ³ ÚÄÄÄÄÄÄ¿  ÚÄÄÄÄÄÄ¿ ³
		    ³ ³left  ³	³right ³ ³
                    ³ ÀÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÙ ³
                    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                         ³          ³
                   ÚÄÄÄÄÄÙ          ÀÄÄÄÄÄ¿

           selection button   cancelling button

        Starting the program

            The program is started by entering MEGA.  Please note that  the
        mouse driver must be loaded !

            The  entry  menue  and  the  mouse  cursor  appear,  which will
        displayed as 'Û'.


			     "Entry Menu"
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°M°                                                  ³
         ³°E°                                                  ³
         ³°N°                      Û                           ³
         ³°U°                                                  ³
         ³°E°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
         > STATUS-INFO                         TEST.PRT  X:
	 > COMMAND-INFORMATION				 Y:


            On the left side of the screen/display  monitor  you  find  the
        menue selection strip.  This strip is used for choosing the various
        selection menues.

            The lower two lines are reserved for program output.

            In the last line the program tells you, what it expects you  to
        do next, depending on the current function.

            One  line  above  this  there  is  a  short  explanation of the
        currently active command.  If, for example, you choose  the  option
        'points' and the mode 'end points' is active, this line reads

                'points - end points'

            The  current  drawing  or  macro name is also displayed on this
        line.

            In the lower right-hand corner of the screen the coordinates of
        the cursor position are displayed.  The position appears in X and Y
        coordinates.



        The Selection Strip

            This field is not part of the drawing area,  but  is  used  for
        selecting  functions.   In  order to choose a selection menue, move
        the mouse cursor to the menue field.  A window  with  the  function
        options is displayed.

            The  window  is  erased  my  moving  out of the menues into the
        drawing area, or by pressing the left button on the mouse.


         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°M°                                                  ³
         ³°E°                                                  ³
         ³°N°                                                  ³
         ³°U°                                                  ³
         ³°E°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
	 ³°°°Å <--- Origin				       ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
         > STATUS-INFO                         TEST.PRT  X:
	 > COMMAND-INFORMATION				 Y:


            When the program is started, the origin is  located  on  a  1:1
        scale in the bottom left corner of the screen.


	  Mode Selection

            When  a  function is active, the mode strip appears in place of
        the selection strip on the left side of the screen.  This  area  is
        always  accessible when it appears.  This gives you the opportunity
        of selecting the position of your  drawing  elements  according  to
        various  criteria.   For  further information on mode selection see
        the chapter "Modes".


                        
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°M°                                                  ³
         ³°O°                                                  ³
	 ³°D°  <------	Û For mode selection, move the	       ³
	 ³°U°		  mouse into this area		       ³
         ³°S°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ³°°°                                                  ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


	  The 'Mode' Options

            The mode selection strip on the left side of the screen appears
        in  all  active  drawing  functions like points, lines, rectangles,
        circles, arcs, and in generating text, inserting macros and  saving
        macros while setting a reference point.

            When  accessed  by  the  mouse  on  the  lower left, this strip
        displays a list of graphical symbols  which  describe  mathematical
        operations  the  program performs upon command.  These mathematical
        operations are to help you construct a drawing.  For instance,  the
        program  finds  the  end  or  centre  point  of  an element.  After
        selecting a symbol you only need to select the desired  element  by
        mouse;  the position is found automatically.

            It  is  at  all  times possible to re-select the options in the
        mode strip.  You could, for example, begin a line as the center  of
        an  arc,  then switch to the 'end points' option, and catch the end
        point of a rectangle line, etc.

            On the mode strip you also find the  options  'return  to  main
        menue'  (top),  'back  one  menue  item',  and 'change line type or
        layer'.


            In the following illustration, the fields of  the  mode  select
        window  are  represented by numbers, there are graphical symbols on
        the screen.  The following descriptions refer to the numbers in the
        sketch.

				ÚÄÄÄÄÄÄÂÄÄÄÄÄÄ¿
	  cursor free	    --> ³      ³      ³ <--   cursor on grid
				³  1   ³   8  ³
				ÃÄÄÄÄÄÄÅÄÄÄÄÄÄ´
	  catch points	    --> ³      ³      ³ <--   catch center point
				³  2   ³   9  ³
				ÃÄÄÄÄÄÄÅÄÄÄÄÄÄ´
	  catch end point   --> ³      ³      ³ <--   distance to element
				³  3   ³  10  ³
				ÃÄÄÄÄÄÄÅÄÄÄÄÄÄ´
	  catch elements    --> ³      ³      ³ <--   distance from element
				³  4   ³  11  ³
				ÃÄÄÄÄÄÄÅÄÄÄÄÄÄ´
	  catch intersect.  --> ³      ³      ³ <--   intersect. point, 2 elements
				³  5   ³  12  ³
				ÃÄÄÄÄÄÄÅÄÄÄÄÄÄ´
	  catch tangent point-> ³      ³      ³ <--   tangent point, 2 elements
				³  6   ³  13  ³
				ÃÄÄÄÄÄÄÅÄÄÄÄÄÄ´
	  keyboard input     -> ³      ³      ³ <--   multiple generation
				³  7   ³  14  ³
				ÀÄÄÄÄÄÄÁÄÄÄÄÄÄÙ
          1.  With  this  field  the  catching of grid points is turned of.
              You can now move the mouse cursor freely in the drawing  area
              and position or select any arbitrary drawing element.

          2.  The catching of points is activated by the second field.  The
              cursor of the mouse turns into a square.  All  points  within
              this square are automatically found by the program.

          3.  Calculation of end points of lines and arcs.  The area around
              the selected lines and and arcs is taken into account.  It is
              not necessary to select the element exactly at the end point;
              just get close to it.
                          

          4.  'Elements'  is  a  special function.  This function helps you
              with element points that are not clearly defined, but are  to
              be  connected  to  another drawing element.  If, for example,
              the end point of a line is not clearly defined, but is to lie
              on an arc at a freely defined position, select this function.
              Move the mouse cursor to the immediate proximity of the point
              where the line is to be connected to the arc.  After pressing
              the left button, the program automatically finds a  point  in
              the  cursor  area  located  on the arc, and connects the line
              with the arc.  This is of  course  possible  with  all  other
              drawing elements.


          5.  This  field  causes the calculation of intersecting points of
              two drawing elements.  The possibilities  are:   intersecting
              points  of two lines, a line and a circle, a line and an arc,
              two circles, and a circle and an arc.  Move the mouse  cursor
              to the immediate proximity of the desired intersecting point,
              then press the left button of the mouse.  If no  intersecting
              point is found, the following message is displayed :



                      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
		      °° no elements in cursor area	°°
                      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
		      °°°°°°°°°°°°°°°°°°°°°°°°°° cancel °°
                      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°


                        
          6.  Finding  a  tangent  point  of  a line and a circle (or arc).
              Move the mouse cursor  to  the  immediate  proximity  of  the
              tangent  point  and  press the left button of the mouse.  The
              point is calculated.  If the program does not find a  tangent
              point,  an  error  message  is displayed.  If a tangent point
              must exist in that area, try again.

          7.  With this option you can  enter  an  X-Y  coordinate  for  an
              element   point   via  keyboard.   The  following  coordinate
              dialogue window appears:



                             ²²²²²²²²²²²²²²²²²²²
			     ²²     Input     ²²
			     ²² POLAR ON/OFF  ²²
                             ²²²²²²²²²²²²²²²²²²²
			     ²² X-Value: 0.00 <--
			     ²² Y-Value:      ²²
			     ²² INCREMENTAL   ²²
                             ²²²²²²²²²²²²²²²²²²²
			     ²² OK ²²² cancel ²²
                             ²²²²²²²²²²²²²²²²²²²


              With this method all points  can  be  exactly  described,  or
              lines  can  be  defined  from  coordinate to coordinate.  The
              entries are confirmed in the 'OK' field.  Exit  the  function
	      by selecting the 'cancel' field.

              To  enter  element  points  in  polar coordinates, select the
              field 'polar'.  In general, the inputted data refers  to  the
	      origin  X0,  Y0.
	      It  is  also possible to enter the coordinates
              incrementally.  Select the field 'incremental'.  The  program
              now  asks you to set a reference point.  Choose the reference
              point via mode selection from which the values entered are to
              be calculated.

              Now  enter the distance of the element point from the origin,
              and the angle.  Confirm  the  entry  by  selecting  the  'OK'
              field.  Exit the function by selecting the 'back' field.


          8.  This field turns the grid on.  This is also the default state
              for all drawing functions  unless  turned  off  in  the  grid
              window.   All  selected  element  points are now put onto the
              defined grid.


          9.  With this selection  you  can  catch  the  center  points  of
              drawing  elements.   The  program  finds  the center of lines
              (including rectangle lines), circles and arcs.

          10. With this option you  can  catch  an  element  with  a  fixed
              distance  (angle, when applied to arcs) from the end point of
              the element.  This distance or angle is entered, The  desired
              end point is selected beforehand in its immediate proximity.


          11. With  this  function  you  can  catch  a  point  with a given
              distance to an element.  A point on the element  is  selected
              in the selected area of the element, and a perpendicular with
              the given distance is created on this point.  The  end  point
              of the perpendicular is the resulting point.


          12. This  field  causes the calculation of intersecting points of
              two drawing elements.   The  possibilities  for  intersecting
              points  are:  two lines;  a line and a circle;  a line and an
              arc;  two circles;   and  a  circle  and  an  arc.   The  two
              elements   are  selected  one  after  another.   The  desired
              intersecting point is calculated.


          13. Finding a tangent point of a line  and  a  circle  (or  arc).
              Both elements are selected one after another.


          14. With  this  option  you can create multifold elements.  Enter
              the number of elements and  their  distance  to  each  other.
              Several  elements  are  then  generated with their respective
              distances from one another.


	  Mode Selection of an Object

            The mode selection of an object (drawing element) is  necessary
        for  selecting  objects  for  editing,  such  as  deleting elements
        individually, the entire screen, all elements in one  window,  etc.
        In   contrary   to  the  previously  described  mode  selection  of
        coordinates,  there  is  no  calculation  of  coordinates,  but   a
        manipulation  of  existing  drawing  elements.   This  manipulation
        consists mainly of functions like changing the  color,  line  type,
        text  attributes,  the  shifting  of  elements, the selection of an
        outline for hatching, etc.

            In all these functions the mode selection can be  performed  in
        the mode field in the lower left-hand corner.


              Example:  Changing the colors of elements

              Select  the  option EDIT in the main menue, then the function
              COLOR in the EDIT window.  Define the new color and  activate
              the  function by selecting the text 'COLOR'.  The program now
              asks for the element to be manipulated.  When the mode  field
              is  accessed,  the  mode  selection  window appears.  If, for
              example, you select the option SCREEN, all  elements  on  the
              screen are changed to the new color.

              Elements  can  be  masked  off  via the upper fields the mode
              selection window to prevent a certain element type from being
              changed.


	  The Main Menu :
	  ================

            All the basic functions of MegaCAD are listed in the main menu,
        which is accessed by moving the mouse into the selection  strip  on
        the left  side of the screen.  All options are selected by pressing
        the left button of the mouse.


	     °° Points	     °°
	     °° Lines	     °°
	     °° Circles      °°
	     °° Arcs	     °°
	     °° Text	     °°
	     °° Dimensioning °°
	     °° Hatching     °°
	     °° Grid	     °°
	     °° Macro	     °°
	     °° Drawing      °°
	     °° Seperate     °°
	     °° Erase	     °°
	     °° Redraw	     °°
             °° Zoom         °°
             °° Edit         °°
             °° Layer        °°
	     °° Defaults     °°
             °° Group        °°
             °° Exit         °°



            In the following chapter you will find a  detailed  description
        of each menu item.


	  1.  Points

              The  following options can be selected in the point selection
              window:

              -   points individually
              -   points as segments on elements
	      -   points with given angle on circles
              -   star-shaped dot patterns
	      -   points as corners of polygons
	      -   points as a net between elements


              1.  Points individually (free)

                   The  definition  of  points  FREE  is  determined by the
                   possibilities of the mode options.

                   After selecting the options you can  define  the  points
                   as:

                  -   free points
                  -   points on a grid
                  -   center points of lines, arcs and circles
		  -   points as end points of lines and arcs
                  -   points on elements in the cursor area
                  -   points as intersecting points
		  -   points as tangential points of a line and a
                      circle
                  -   points by direct entry of coordinates
                  -   points in polar coordinates

                   The  mode  'select' is activated by selecting the option
                   FREE.


              2.  Points as segments on elements

                   Each element, be it a line, a circle or an arc,  can  be
                   split  into  several  segments  of  the same size by the
                   SEGMENT function.  Enter the desired number of  segments
                   and select the elements.


	      3.  Points with a defined angle on circles

                   Select  this  function  in  order  to  define  points on
                   circles with a defined angle as in relation to the  zero
                   angle.  Enter the desired angle of the point, and select
                   the circle.


              4.  Star-shaped dot patterns

                   With  this  function  a  star-shaped  dot   pattern   is
                   generated.   Please  note  the  instructions in the help
                   window.


              5.  Points as a polygon
 
                   This function creates a polygon  consisting  of  points.
                   After  entering  the  values  in  the window, the center
                   point has to be defined via mode selection.


	      6.  Points as a net between elements

                   This function  generates  a  net  of  dots  between  two
                   elements,  such  as  lines, circles and arcs.  Enter the
                   desired number of net  segments,  and  then  select  the
                   elements  in  the  proximity of one of their end points.
                   The end  points  should  be  located  opposite  to  each
                   another.

		  Attention! In the shareware version, the number of
			     segments is limited to five.


	  2.  Lines

              There are many different ways of defining lines in MegaCAD In
              the line window you will find the following options:

              -   lines, modus selection FREE
              -   lines tangent circle circle
              -   lines horizontal
              -   lines horizontal/vertical
              -   bisecting line of an angle
	      -   line at distance
              -   net of lines
              -   freehand line
              -   tangent, point and line
              -   tangent, circle with angle
              -   line vertical
              -   rectangle
              -   angle, two lines
              -   perpendicular to line
              -   polygon consisting of lines
              -   spline


	      1.  Lines, mode selection FREE
                  
                   The definition of a line FREE is also determined by  the
                   possibilities   of  mode  options.   By  selecting  mode
                   options, lines can be defined as:

                  -   free from cursor position to cursor position
                  -   from grid point to grid point
                  -   from center point of element to center point of 
                      element
                  -   from element to element in cursor area
                  -   from end point of one element to end point of 
                      another element
                  -   connection of intersecting points of elements 
                  -   connection of tangent points of a line and a 
                      circle
                  -   parallel lines
                  -   end point with free coordinate entry
                  -   start and end point in polar coordinates

                   All possibilities are interchangeable , thus a multitude
                   of line definitions are available.


              2.  Line as a tangent to two circles 

                   With  this  option  a  tangent  betwenn  two  circles is
                   gereated.  The created tangent  depends  on  the  points
                   selected  on  the circle.  Press the mouse button on the
                   circles in the proximity of the tangent points.


	      3.  Horizontal lines
           
                   Draws a horizontal line.  The line  is  limited  by  the
                   screen,  i.e.   it  is  constructed  from one end of the
                   screen to the other.  The line can be positioned by mode
                   selection.


              4.  Lines horizontal/vertical

                   Draws  horizontal  and  vertical  lines.   The lines are
                   limited by the screen, i.e.  they are  constructed  from
                   one  end  of  the screen to the other.  The lines can be
                   positioned by mode selection.


	      5.  Line at bisecting angle

                   Creates a line between  two  lines  at  half  the  angle
                   between  those  two  lines.   The  length of the line is
                   entered, which can be negative, causing the line  to  be
                   generated in the opposite direction.

                                          
	      6.  Parallel line in given distance

                   This  function creates a line at a defined distance from
                   a line.  The distance of the new line is entered.   Then
                   select  the  reference  line  and move the mouse to that
                   side of the line,  on  which  the  new  line  is  to  be
                   created.  Then press the left button of the mouse again.


              7.  Net of lines

                   This  function  generates  a  net  of  lines between two
                   elements, which can be lines, circles  or  arcs.   Enter
                   the  desired  number  of  net  segments  and  select the
                   elements in the proximity of  an  end  point.   The  end
                   points should be located opposite to each other.

		  Attention! In the shareware version, the number of
			     segments is limited to five.


              8.  Freehand line

                   Creates   a  'curved'  line  by  moving  the  mouse  and
                   simultaneously keeping the  left  button  pressed.   The
                   line  can  be  generated either in grid modus or in free
                   modus.  The line is saved as an individual element.

                  
              9.  Tangent point to circle
                  
                   With this option a tangential line to a circle origining
                   in  a  point  is  created.   First, select the point The
                   created tangent depends on where the circle is selected,
                   so press the mouse button on the circle in the proximity
                   of the tangent point.


	      10. Tangent on circle with angle

                   With this option, a tangential line with a  given  angle
                   is  created  on  a  circle.  First the angle is entered.
                   The created tangent  depends  on  where  the  circle  is
                   selected, so press the mouse button on the circle in the
                   proximity of the tangent point.  The line is then  drawn
                   and limited from one end of the screen to the other.


              11. Line vertical

                   Draws  a  vertical  line.   The  line  is limited by the
                   screen, i.e.  it is constructed  from  one  end  of  the
                   screen to the other.  The line can be positioned by mode
                   selection.


              12. Rectangle

                   This function draws a rectangle from a defined  starting
                   point.   The  starting point is set by the mouse cursor.
                   Then the rectangle can be drawn up to the  desired  size
                   by  moving  the  mouse  in  all  four  directions.   The
                   rectangle is confirmed by pressing the  left  button  of
                   the mouse.

                   For   setting  the  start  and  end  points,  again  all
                   possiblities of mode selection are available.


              13. Angle line to line

                   Draws a line at a defined angle  to  a  reference  line.
                   The  lines  created  always  have the same length as the
                   reference line.  The angle can be entered as a  positive
                   or  negative  value.  The created line is defined by the
                   angle and the selected point on the reference line.


              14. Perpendicular to line

                   'Perpendicular to line' draws a line which meets the the
                   reference  line  at  a  90ø  angle.   The  length of the
                   perpendicular line is entered as a positive or  negative
                   value.    The  location  of  the  perpendicular  on  the
                   reference line is defined by this entry.


              15. Polygon of lines

                   This function generates a polygon consisting  of  lines.
                   After  entering  the  values  in  the window, the center
                   point  of  the  polygon  has  to  be  defined  by   mode
                   selection.   The  radius of the polygon can refer to the
                   inside or outside  of  the  polygon,  depending  on  the
                   selection in the input window.


	      16. Splines

		  MegaCAD offers five sorts of splines.

                  Attention! The shareware version offers option 1 
                             only.

                   A  spline is defined by any number of supporting points.
                   Set the supporting points via mode  selection.   MegaCAD
                   then  prompts you for the number of supporting points to
                   be calculated in between  the  ones  entered.   Here  we
                   recommend  any  number between 10 and 30.  The spline is
                   stored as an individual element.

	  3.  Circles

	      In MegaCAD there are many ways to define a circle.
              In combination with the possibilities of free mode  selection
              a great number of definition options are available.

              The selection is performed on a selection menu with graphical
              symbols.  We chose this form of selection in order to support
              easy  learning  of  the program (according to our experience)
              and to meet  the  demand  for  easy  operation  with  maximum
              efficiency.

              In  the  following  illustration,  the  options  for defining
              circles are  represented  by  numbers,  there  are  graphical
              symbols  on  the screen.  The following descriptions refer to
              the numbers in the sketch.
			       ÚÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄ¿
     Centerpoint and radius--> ³       ³       ³ <-- two points aun radius
			       ³   1   ³   8   ³
			       ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
     Center and edge point --> ³       ³       ³ <-- Centerpoint and tangent
			       ³   2   ³  10   ³
			       ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
     through three points  --> ³       ³       ³ <-- 2 points, tangent to line
			       ³   3   ³  11   ³
			       ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
     Tangent L. L. with R. --> ³       ³       ³ <-- 2 points,tangent to circle
			       ³   4   ³  12   ³
			       ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
     Tangent C. C. with R. --> ³       ³       ³ <-- tangent to three lines
			       ³   5   ³  13   ³
			       ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
     Tangent L. C. with R. --> ³       ³       ³ <-- with distance to circle
			       ³   6   ³  14   ³
			       ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
     Point + tangential L. --> ³       ³       ³ <-- Input X-Y-R
			       ³   7   ³  15   ³
			       ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
     Point + tangential C. --> ³       ³       ³ <-- Input M,A,R Polar
			       ³   8   ³  16   ³
			       ÀÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÙ


	      1.  Centerpoint and radius

                   The circle is defined by  entering  a  radius  and  then
                   selecting the centerpoint using the mouse.

              2.  Center point and edge point

                   The  circle  is defined by selecting the centerpoint and
                   an arbitrary edge point using the mouse.  The radius  is
                   calculated automatically.

	      3.  Through three points

                   The  circle  is defined by selecting three points on its
                   perimeter.    The    radius    value    is    calculated
                   automatically.


              4.  Tangent to two lines with defined radius

                   A  circle tangential to two lines is created.  The lines
                   are selected by mouse.  The radius, which is also needed
                   for  the  calculation, is entered either via keyboard or
                   is determined by mode selection.


              5.  Tangent to two circles with defined radius

                   A circle is defined as a tangential circle to two  other
                   circles.   The  circles  are  selected  by  mouse.   The
                   radius, which is also needed  for  the  calculation,  is
                   entered  either  via  keyboard  or is determined by mode
                   selection.


              6.  Tangent to a line and a circle with defined radius

                   A circle is defined as a tangential circle to a line and
                   a  circle.   The  line  and  the  circle are selected by
                   mouse.   The  radius,  which  is  also  needed  for  the
                   calculation,  is  entered  either  via  keyboard  or  is
                   determined by mode selection.



	      7.  Point and tangential to a line and radius

                   The  circle crosses a point and is tangential to a line.
                   The elements are selected by mouse.  The  radius,  which
                   is  also  needed  for the calculation, is entered either
                   via keyboard or is determined by mode selection.

	      8.  Point and tangential to a circle and defined radius

                   The circle crosses  a  point  and  is  tangential  to  a
                   circle.   The  elements  are  selected  by  mouse.   The
                   radius, which is also needed  for  the  calculation,  is
                   entered  either  via  keyboard  or is determined by mode
                   selection.

              9.  Two points and defined radius

                   The circle crosses two points.  The points are  selected
                   by  mouse.   The  radius,  which  is also needed for the
                   calculation,  is  entered  either  via  keyboard  or  is
                   determined by mode selection.



              10. Center point and tangent

                   The  circle  is  defined  by  its  center  point  and is
                   tangential to a line.  The line is  selected  by  mouse.
                   The  centerpoint  is  entered  either via keyboard or is
                   determined by mode selection.


              11. Point and tangent point on a line

                   The circle crosses two points its perimeter.  One of the
                   points  must  be  a line (tangent point).  The radius is
                   calculated automatically.  The points  are  selected  by
                   mouse.

              
              12. Point and tangent point on a circle

                   The  circle  crosses two points.  One of the points must
                   be  on  a  circle  (tangent  point).   The   radius   is
                   calculated  automatically.   The  points are selected by
                   mouse.


	      13. Circle to three tangential lines

                   The circle is tangential to three lines.  The radius  is
                   calculated  automatically.   The  lines  are selected by
                   mouse.


              14. With distance to existing circle

                   This  function  draws  a  circle  around  or  within  an
                   existing  circle.   The  radius  of  the  new  circle is
                   determined by the distance  from  the  previous  circle.
                   The distance can be entered positive for an outer circle
                   or negative for an inner circle, or  it  is  defined  by
                   mode selection.


	      15. Input X-Y-R

                   The circle is defined by entering the coordinates of the
                   center point and the radius via keyboard.


	      16. Input (M,A,R polar)

                   The circle is defined by entering the  center  point  in
                   polar coordinates plus the radius via keyboard.

                  
		  Attention! All functions that cannot be accessed, are
			     available only in the full version.


	  4.  Arcs
              With  MegaCAD  there  are  many  ways  of defining arcs.  The
              number of definition possibilities is enhanced  by  the  free
              mode selection.


              The  selection  is  performed  in  a  selection  window  with
              graphical symbols.

              In the following illustration, the options for defining  arcs
              are  represented  by  numbers, there are graphical symbols on
              the screen.  The following descriptions refer to the  numbers
              in the sketch.

                                 ÚÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄ¿
       Centerpoint R. A. A.  --> ³	 ³	 ³ <-- Centerpoint R. A. A. T.
                                 ³   1   ³   8   ³
                                 ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
       Centerpoint D. A. A.  --> ³	 ³	 ³ <-- Tangent L. C. R. A. A.
                                 ³   2   ³   9   ³
                                 ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
       two points and angle  --> ³	 ³	 ³ <-- By Distance to arc, D+-
                                 ³   3   ³  10   ³
                                 ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
       three points	     --> ³	 ³	 ³ <-- Tangent C. C. R. A. A.
                                 ³   4   ³  11   ³
                                 ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
       Center and edge point --> ³	 ³	 ³ <-- touching 3 lines, A. A.
                                 ³   5   ³  12   ³
                                 ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
                                 ³       ³       ³
       Tangential to circle  --> ³   6	 ³  13	 ³ <-- Tangential to end of Line
                                 ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
                                 ³       ³       ³
       Arc polar	     --> ³   7	 ³  14	 ³ <-- Tangential to two lines
                                 ÀÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÙ


              1.  Center point, radius, start and end angles 

                   Defines  an  arc  after  entering  the center point, the
                   radius and the start and end angles  of  the  arc.   The
                   entry   can   be  performed  via  keyboard  or  by  mode
                   selection.


              2.  Center point, diameter, start and end angles

                   Defines an arc by entering  the  center  point  and  the
                   diameter, plus the start and end angles of the arc.  The
                   entry  can  be  performed  via  keyboard  or   by   mode
                   selection.

              3.  Two points and angle

                   This  arc is defined by entering both end points and the
                   angle enclosed  by  the  two  points.   The  points  are
                   selected via mouse, with free modus selection.


              4.  Three points

                   The  arc  is defined by entering both end points and one
                   point  on   the   arc.    The   radius   is   calculated
                   automatically.


	      5.  Centerpoint and edge point

                   Here,  the  centerpoint and one of the end points of the
                   arc are entered.  The second end point  is  defined  via
                   selection  by mouse.  MegaCAD now asks you, which of the
                   two possible arcs you  want.   Select  the  desired  arc
                   using the mouse.


              6.  Tangent to circle

                   This  function draws an arc as a tangential continuation
                   of another arc.  The program asks you to select the arc.
                   Then the following appears in the dialogue window:


             ±±±±±±±±±±±±±±±±±±±
	     ±±   ARCS	      ±±
             ±±   Tangential  ±±
             ±±±±±±±±±±±±±±±±±±±
	     ±± Radius : 5.00 <--    Enter Radius
	     ±± Angle  : 0.00 ±± <-- Starting and increment angle
             ±±               ±±
	     ±±   +	  -   ±± <-- Increase or reduce size
	     ±± Angle  : 10.0 ±± <-- Current angle
             ±±±±±±±±±±±±±±±±±±±
	     ±±  OK  ± Cancel ±± <-- leave function with Cancel
             ±±±±±±±±±±±±±±±±±±±


                   First  the  arc  radius  and  angle  are entered.  It is
                   possible to state the immediate end angle.  The  program
                   then  draws  the  arc  up to the end angle entered.  If,
                   however, you enter  a  small  angle  of  let's  say  one
                   degree,  the  end  angle can be modified by pressing the
                   '+' or '-' keys after selecting the 'OK' field.

                   The arc is confirmed by selecting the 'OK' field and  is
                   then  drawn  in  its final position.  Exit this function
                   via the 'cancel' field.

              7.  Arc in polar coordinates
                   Same as in '1.', except the center  point  is  in  polar
                   coordinates.


              8.  Center point, radius, start and end angles, tangent

                   Defines  an arc by entering the center point, the radius
                   and the start and end angles.  The  entry  is  performed
                   via keyboard.  The program displays a dialogue window.


              9.  Tangent, line, circle, radius, start and end angles

                   This arc is defined as a tangent to a circle and a line.
                   The radius and the start and end angles are entered  via
                   keyboard  or by mode selection.  Both elements, the line
                   and the circle, are selected using the mouse.
                  

	      10. With distance from arc D+-

                   Draws an arc with a defined distance  from  an  existing
                   arc.   The  distance  can  be  entered  as a positive or
                   negative value.  The entry can be performed via keyboard
                   or by mode selection.


	      11. Tangent, two circles, radius, start and end angles

                   This  arc  is  defined as a tangent to two circles.  The
                   radius and the start and  end  angles  are  entered  via
                   keyboard  or  by  mode  selection.   The two circles are
                   selected using the mouse.


	      12. Touching three lines, start and end angles

                   Drawing an arc as a tangent to three lines.   The  start
                   and end angles of the arc are to be entered.  The radius
                   is calculated by the program.  Select  the  lines  using
                   the mouse.


              13. Tangent to a line

                   This  function draws an arc as a tangential continuation
                   of a line.  The program prompts you  to  select  a  line
                   using the mouse.  Then the dialogue window is displayed.
                   First, the  radius,  then  the  angle  of  the  arc  are
                   entered.   It is possible to enter the actual end angle.
                   The program then draws the arc up to the entered  angle.
                   If,  however,  you  enter a small angle of let's say one
                   degree, the end angle can be  modified  to  the  desired
                   size  by  pressing  the '+' and '-' keys after selecting
                   the 'OK' field.

                   The arc is confirmed by selecting the 'OK' field and  is
                   then  drawn in its final position.  Exit the function by
                   selecting the 'cancel' field.


              14. Tangent to two lines

                   Two lines are selected  by  mouse,  and  the  radius  is
                   entered.  Then the start and end angles are entered.  If
                   the start and end angles are not  entered,  the  desired
                   arc is selected using the mouse.


	  5.  Input and display of text

              The  MegaCAD  program  enables you to enter and place text in
              any position and angle in the drawing area on the screen.  In
              the  shareware  version  you  can select among four different
              fonts.   Moreover,  the  attributes  of  all  fonts  can   be
              modified.

              In  order to enter text, select the option "text" on the main
              menue.  The  following  entry  possibilities  appear  in  the
              'text' window:



                          ²²²²²²²²²²²²²²²²²²²²²
			  ²²	 Text	   ²²²²
                          ²²²²²²²²²²²²²²²²²²²²²
			  ²² Font - No	:    ²²
                          ²²²²²²²²²²²²²²²²²²²²²
			  ²² Text-height:  1 <--
			  ²² Text-width : .5 ²²
			  ²² Text-angle : 90 ²²
			  ²² DistanceL.X: .2 ²²
			  ²² DistanceL.Y:0.0 ²²
			  ²² angle-pos. :  0 ²²
                          ²²²²²²²²²²²²²²²²²²²²²
			  ²² line of text    ²²
			  ²² block of text   ²²
			  ²²	  cancel     ²²
                          ²²²²²²²²²²²²²²²²²²²²²


              The  text  font is defined by entering a number between 1 and
              4.

              The height and width of the text, as well as the angle of the
              letters can be modified.

              The  height  and  the  width  are entered in millimeters, the
              angle of the letter in degrees.

              The distance L.X defines the  distance  from  one  letter  to
              another in millimeters on the X axis.

              The  distance  L.Y defines the distance from letter to letter
              in millimeters on the Y axis.   This  entry  enables  you  to
              create text in a staircase shape.

              The  angle position defines the angle of the text relative to
              the X axis.  If, for example, you wish to  place  text  in  a
              perpendicular position, enter an angle of 90 degrees.

              Confirmation  of  'text-line'  prompts  you  for the entry of
              text.  MegaCAD displays a text entry window:


            ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
          -->²                                                          ²²
            ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
	    ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²² OK ²²² cancel ²²²²²
            ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²


              You can now enter the text, line by  line.   After  selecting
              the  OK-field, the text can be positioned on the screen.  For
              this puspose, the line of text is represented by a  rectangle
              which  has the exact size of the text and can be moved around
              the  screen  with  the  mouse.   All  snap  options  in  mode
              selection are accessible.

              Confirm  the  position  for  the  text  by  pressing the left
              button, cancel without writing the text by pressing the right
              button.

              Note that not all fonts contain small letters.

              The  option  'text-block' works exactly the same, except that
              here a full  screen  editor  with  capabilities  of  merging,
              copying, replacing etc.  is used for the input.  Whole blocks
              of text can saved or loaded and then placed on the screen.

	    ATTENTION: In the full version of MegaCAD, a window driven
		       font editor is included with which you create
		       as many fonts as you like according to your own
		       imagination.


	  6: Dimensioning

              Dimensioning is invoked by selecting the appropriate field in
              the main window.  The dimensioning window with many different
              possiblities and settings is displayed.

              The following options are available in this version :

	      - horizontal dimensioning
	      - vertical dimensioning
	      - parallel dimensioning
	      - dimensioning a diameter
	      - dimensioning a radius
	      - dimensioning an angle

	      - dimension value left, right or middle
	      - type of arrows
	      - dimensioning of distance
	      - absolute dimensioning
	      - incremental dimensioning

              - edit dimensioning
              - modify dimensioning positions
              - modify dimensioning dimension

              When  you  select  a  non-active  function,  a  corresponding
              message appears.

              These  options  are  selected  using the mouse.  Just like in
              other functions, the  mode  selection  is  a  great  help  in
              defining   the  dimensioning.   The  dimensioning  number  is
              displayed as a rectangle for positioning.

	      An example:
                   You  wish   to   dimension   incrementally,   with   the
                   dimensioning  number  in  the  center.   You  would like
                   circles as 'dimensioning arrows'.

                   1.  Using  the  mouse,  select  the  dimensioning  arrow
                       'circle'.
                   2.  Select the option 'incremental'.
                   3.  Select the field 'dimensioning number center'.

                   The basic operation mode is now set.  You can now select
                   the method of dimensioning (horizontal, etc.).

                   The  program  now  switches  into  the  mode  area.   By
                   selecting   the   center  points,  the  end  points,  or
                   whatever, dimensions are set.

                   Exit the function by pressing the right  button  of  the
                   mouse.   The dimensioning window for modification of the
                   dimensioning method appears.


	  7.  Hatching (Crosshatch shading)

              With MegaCAD there are many ways of hatching of an area.   We
              are  going to explain the option of hatching a outline, since
              this is the main application.

              The function hatching is selected via the  'hatching'  symbol
              on  the  main  menue.   Then  the  hatching  selection window
              appears.  In this window  you  select  the  desired  hatching
              type.
               
              Attention!  In the shareware version only type 7 is 
                          available.  

              Enter  the  desired distance of the hatching, plus the angle.
              The function is activated via the 'OK'  field.   The  program
              switches  to  mode  selection.   Move  the mouse to the lower
              left-hand corner of the screen.  The mode selection window is
              displayed.    Select  the  option  'outline'.   You  are  now
              prompted to select the start and end elements of the outline.
              Please note that only a closed outline can be used to build a
              crosshatch.

              MegaCAD now selects the outline automatically.  If there  are
              intersecting  points  with  other  elements  on  the outline,
              MegaCAD asks for  the  next  element  on  the  outline.   The
              element found last is marked with a circle.

              Islands  are  selected  after the outer outline for hatching,
              circles must  be  selected  twice.   When  all  outlines  are
              selected,  press the right button of the mouse.  A crosshatch
              can be erased as a whole or as  individual  elements.   (each
              line in the crosshatch).


          8.  Screen grids and catching grids

              Grid   points   provide  a  visual  help  while  constructing
              drawings.  They serve as an orientation for the  dimensioning
              system of the drawing area.

              For  easier  operation,  the  setting  of  grid points can be
              modified.  MegaCAD  displays  grid  points  as  simple  pixel
              points.

              The calibration of the grid is entered in millimeters.

              Using  the  'catching'  function, the program finds the point
              positioned closest to the cursor when the left button of  the
              mouse  is  pressed in a drawing function.  This point is used
              as an element point.

              The calibraton is chosen by selecting the corresponding field
              in the window using the mouse.

              The  turning  on/off  of  the  catching  and  grid options is
              performed by selecting the two fields using the  mouse.   The
              on/off entry alternates accordingly.

              Moreover you find the following options in the grid window:

              -   define measuring units
              -   modify keyboard reference point 
              -   move/shift grid reference point
	      -   set number of decimal digits
	      -   set screen to match drawing sheet sizes according to DIN
              -   create star-shaped grids
              -   create angle grids

          
         12.  The macro management

              Macros in the MegaCAD program are complete drawings which are
              simply managed separately as macros.  Often used drawings are
              thus integrated easily and quickly into any other drawing.

              Macros  can  be placed and integrated anywhere in the drawing
              area.  They can also be enlarged or reduced and rotated by an
              angle.

              In  order to create a macro, select the option 'macro' on the
              main menue.  All drawings created by this function are  named
              with the extension .MAC on the data medium.

              If  you  wish  to declare an existing drawing as a macro, you
              can just copy file at  the  DOS  prompt  DOS  (COPY  NAME.PRT
              NAME.MAC).   Please  note  the description at the end of this
              chapter.


             ²²²²²²²²²²²²²²²²²²²
	     ²² Macro	      ²²  <ÍÍÍ The Macro-selection menu
	     ²² 	      ²²       ========================
             ²²               ²²
	     ²² Management    ²²
	     ²² View	      ²²
	     ²² Create/edit   ²²
	     ²² Insert	      ²²
	     ²² Save	      ²²
	     ²² Delete	      ²²
	     ²² Print	      ²²
	     ²² clip	      ²²
             ²²²²²²²²²²²²²²²²²²²
	     ²²    cancel     ²²
             ²²²²²²²²²²²²²²²²²²²


                   Macro file list

                   The selection of a macro via the file list is invoked by
                   selecting  the  field  'file  list'  using the mouse.  A
                   window with all existing macros on the data  carrier  is
                   displayed.    The   macros   must   be  located  in  the
                   subdirectory created for this  purpose  at  installation
                   time.

                   If  more macros exist than can be displayed at one time,
                   switch to the next or previous  page  by  selecting  the
                   fields <-- or -->.

                   A  macro  is  chosen  by  selecting  the macro name.  by
                   pressing by pressing the left button of the mouse or  by
                   pressing the return key while the name is inverted.  The
                   name  of  the  selected  macro  appears  in  the   lower
                   right-hand  corner of the window.  If you want to choose
                   a different macro, simply select a new macro name.

                   Finish the selection by selecting  the  field  'return'.
                   The  macro can now be inserted into the selection window
                   or into the drawing area, depending on the function  you
                   chose.
               
             ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄ¿
             ³          ³ ÚÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄ´
             ³          ³ ³     test1.MAC                          ³
             ³          ³ ³     test2.MAC                          ³
             ÃÄÄÄÄÄÄÄÄÄÄÅÄ´     test3.MAC                          ³
             ÃÄÄÄÄÄÄÄÄÄÄÁÄ´     test4.MAC                          ³
             ³°°°         ³     test5.MAC                          ³
             ³°M°         ³                                        ³
             ³°O°         ³                                        ³
             ³°D°         ³                                        ³
             ³°U°         ³                                        ³
             ³°S°         ³                                        ³
             ³°°°         ³                                        ³
             ³°°°         ³                                        ³
             ³°°°         ³                                        ³
             ³°°°         ³                                        ³
	     ³°°°	  ³ <--   -->	  return	   .MAC    ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

                        
                   View macros:

                   The function 'View macros' displays the desired macro in
                   the macro selection window located in the  upper  screen
                   area.    This  selection  window  always  appears  after
                   choosing the option 'macro' on  the  main  menue.   Five
                   macros can be displayed in the window at one time.  Once
                   the macros are chosen, they are saved and preserved even
                   after  exiting the program;  they are available upon re-
                   initiation of the program.  New macros are  inserted  by
                   modifying the window contents.



                   Now how do we get a macro into the selection window?

                   The program lets you choose one of four possibilities :


             ²²²²²²²²²²²²²²²²²²²
	     ²² Macro	      ²²
	     ²² View	      ²² <---  After selecting the function
	     ²² 	      ²²       view, this window appears.
	 ÍÍ> ²² Keyboard      ²²       Select the desired method
	 ÍÍ> ²² Window	      ²²       of input.
	 ÍÍ> ²² File list     ²²
	 ÍÍ> ²² File display  ²²
             ²²               ²²
             ²²               ²²
             ²²               ²²
             ²²²²²²²²²²²²²²²²²²²
	     ²²    cancel     ²²  <---	Exit this fuction by selecting this
	     ²²²²²²²²²²²²²²²²²²²	field.



	      1.  View macros with keyboard input

                   This  function  calls  a dialogue window for the program
                   name.  You can now enter  the  desired  macro  name  via
                   keyboard.   The  macro  is then selected by pressing the
                   mouse on the 'OK' field.



             ²²²²²²²²²²²²²²²²²²²
	     ²² Macro	      ²²
	     ²² View	      ²²
             ²²²²²²²²²²²²²²²²²²²
	     ²² File name :   ²²
	     ²² 	   <--²² <ÍÍ  Enter macro name here
             ²²²²²²²²²²²²²²²²²²²
	     ²² OK ²²² cancel ²² <ÍÍ  Quit function with 'cancel'.
	     ²²²²²²²²²²²²²²²²²²²


                   Now MegaCAD prompts  you  to  select  the  area  in  the
                   selection  window  (at  the top of the screen) where the
                   macro is to be displayed.  Select the lower part of  the
                   fields with the macro names :

             ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄ¿
             ³          ³          ³          ³          ³         ³
             ³          ³          ³          ³          ³         ³
             ³          ³          ³          ³          ³         ³
             ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
             ÃÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄ´
             ³°°°            ^          ^                          ³
	     ³°M°	     ³		³ Select one of these	   ³
	     ³°E°			  fields !		   ³
             ³°N°                                                  ³
             ³°U°                                                  ³
             ³°E°                                                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
	      L: <<Select Window>>"  R: <<Select window>>



                   After  selecting  the field, the macro is drawn, and the
                   selection menue is displayed.

	      2.  View macro via window:

                   Here the macro selected in the selection window is to  a
                   different position.


	      3.  Select a macro from the file list:

                   The  selection  of a macro is also possible via the file
                   list.  A selection window with all existing macro  names
                   is  displayed  as  explained  in  'file list'.  Select a
                   macro and place it into the desired window.


	      4.  View macrosacro in a 'file display':

                   This  function  displays  macros  in  a   window.    The
                   selection window appears, containing the graphics of the
                   existing macros.  Select the macro using the mouse,  and
                   position it in the drawing.


              Creating macros

                   In  order to create a macro, the 'create macro' function
                   must be invoked.  Macros are  managed  separately  aside
                   drawings.

                   The selection of macros to be created is performed again
                   by the functions 'keyboard', 'window' and 'file list'.

                   New macro names can be entered, or existing  macros  can
                   be modified or over-written.

                   New  macros  are created by entering a macro name in the
                   'keyboard' function.

                   Existing macros can be selected by all three functions.

                   When selecting an existing macro, the  following  window
                   appears:


             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
	     ²² File already exists !	²²
             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
	     ²²      Overwrite		²² <---  Move mouse cursor to
	     ²²      change		²² <---  a field and select
	     ²²      new name		²² <---
             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²


                   You  can  choose,  whether a macro should be overwritten
                   (i.e.  the existing macro is deleted and a  new  one  is
                   created),  whether you wish to modify (edit) a macro, or
                   whether you want to enter another name.

                   If you choose to over-write or modify, and there already
                   is a current drawing or macro, MegaCAD asks, whether the
                   existing drawing should be saved.


             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
	     ²²²²²Save current file ?²²²²²
             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
	     ²²²  YES  ²²²²²²²²²  NO   ²²² <ÍÍ Select yes or no
             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²


                   ATTENTION! If NO is selected, all current data is lost !


                   Inserting macros

                   In  order  to  insert a macro into a drawing, choose the
                   'insert' option.

                   The selection of the macro to be inserted  is  performed
                   by the functions 'keyboard', 'window', and 'file list'.

                   After  having  selected  the  macro  name,  you have the
                   option of modifying  the  macro  size  and  angle.   The
                   entries  are performed in the window shown below.  If no
                   modifications are desired, immediately select  the  'OK'
                   field  in  the  window.  If the angle is to be modified,
                   enter the angle.  The macro is saved  on  a  1:1  scale.
                   This scale can be changed by entering a factor.

                   > factor 0.5 corresponds to a scale 1:2
	           > factor 0.1  corresponds to a scale 1:10
	           > factor 2.0  corresponds to a scale 2:1
	           > factor 10.0 corresponds to a scale 10:1


             ²²²²²²²²²²²²²²²²²²²
	     ²² Macro	      ²²
	     ²² insert	      ²²
             ²²²²²²²²²²²²²²²²²²²
	     ²² rotate macro  ²²
	     ²² Angle :  0.00 <--
             ²²²²²²²²²²²²²²²²²²²
	     ²² modify size ? ²²
	     ²² Factor:  1.00 ²²
             ²²²²²²²²²²²²²²²²²²²
	     ²² Macro name    ²² < if more than one macro was chosen
	     ²²²²²²²²²²²²²²²²²²²   for selection
	     ²² OK ²²² cancel ²²
             ²²²²²²²²²²²²²²²²²²²


                   After  having  entered  the  desired  data, the macro is
                   inserted.

                   Each macro is given a reference point during the  saving
                   process.   Now  place the mouse cursor onto the position
                   where the macro is to be inserted.  The macro  reference
                   point is positioned onto the mouse position.

                   You  can  let  MegaCAD calculate the reference point For
                   this, all mode selection options  are  available.   With
                   this method, you can select the center point, end point,
                   etc.  of an element to serve as a reference point.

                   After having  defined  the  position  of  the  macro  by
                   pressing  the  left  mouse  button,  the macro is drawn.
                   Upon completion MegaCAD asks, whether the macro has been
                   inserted correctly.


             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
	     ²²²²² Macro ok ?	     ²²²²²
             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
	     ²²²  YES  ²²²²²²²²²  NO   ²²² <ÍÍ Select yes or no
             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²


                 
                   If you select 'NO', the macro is deleted.  In both cases
                   the window for modification of the macro  data  appears.
                   Once  the  macro is selected, in can be integrated again
                   until  you  select  the   'cancel'   function   in   the
                   modification window.


                   Saving macros

                   This function is needed for saving an existing macro.

                   Before  saving  a  macro,  a  reference  point has to be
                   selected.  This reference point is used for  positioning
                   a  macro into a drawing.  MegaCAD automatically asks for
                   the reference point.  A reference point can  be  defined
                   by  the  options in the mode window.  After defining the
                   reference point, it has to be confirmed.  Only then  the
                   macro is saved under the entered name.


             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
             ³°°°                                                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ³°M°                                                  ³
             ³°O°                                                  ³
             ³°D°                                                  ³
             ³°U°          ²²²²²²²²²²²²²²²²²²²²²²                  ³
	     ³°S°	   ²² Reference pt ok ?²²		   ³
             ³°°°          ²²²²²²²²²²²²²²²²²²²²²²                  ³
	     ³°°°	   ²² YES  ²²²²²  NO  ²²²		   ³
             ³°°°          ²²²²²²²²²²²²²²²²²²²²²²                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
	     > Save-Macro-Grid			    Test.MAC  X:45
	     L: <<Reference pt>> R: <<Reference pt>>	      Y:111



                   Print macros

                   With  this function a simple hard copy is sent to an IBM
                   graphics printer.  Please note that your printer has  to
                   be set up accordingly, and be turned on.


          13. Creating drawings

              In  order  to create drawings, select the option 'drawing' on
              the main menue.  All drawings created in  this  function  are
              saved with the extension '.PRT'.

             ²²²²²²²²²²²²²²²²²²²
	     ²² Drawing       ²²  <ÍÍ The drawing selection - menu
             ²²               ²²      ============================
             ²²               ²²
	     ²² Management    ²²
	     ²² View	      ²²
	     ²² Create	      ²²
	     ²² Save	      ²²
	     ²² Delete	      ²²
	     ²² Print	      ²²
	     ²² Clip	      ²²
             ²²²²²²²²²²²²²²²²²²²
	     ²²    cancel     ²²
             ²²²²²²²²²²²²²²²²²²²



                   Drawing file list

                   The  selection  of  a  drawing  via  the  file  list  is
                   performed by selecting the field 'file list'.  A  window
                   with all currently existing drawings is displayed.

                   If more drwings exist than can be displayed at one time,
                   switch to the next or previous  page  by  selecting  the
                   fields <-- or -->.

                   The  desired  drawing is chosen by selecting the drawing
                   name.  The selection is performed by pressing  the  left
                   button  of  the  mouse  or by pressing the 'return' key.
                   The name of the selected drawing appears  in  the  lower
                   right-hand  corner of the window.  If you wish to choose
                   a different drawing, simply select a new name.

                   Confirm the selection by selecting the field 'return'.
               
             ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄ¿
             ³          ³ ÚÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄ´
             ³          ³ ³     test1.PRT                          ³
             ³          ³ ³     test2.PRT                          ³
             ÃÄÄÄÄÄÄÄÄÄÄÅÄ´     test3.PRT                          ³
             ÃÄÄÄÄÄÄÄÄÄÄÁÄ´     test4.PRT                          ³
             ³°°°         ³     test5.PRT                          ³
             ³°M°         ³                                        ³
             ³°O°         ³                                        ³
             ³°D°         ³                                        ³
             ³°U°         ³                                        ³
             ³°S°         ³                                        ³
             ³°°°         ³                                        ³
             ³°°°         ³                                        ³
             ³°°°         ³                                        ³
             ³°°°         ³                                        ³
	     ³°°°	  ³ <--   -->	  cancel	   .PRT    ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

                        
                   View drawings

                   The  function  'view  drawings'  displays  the   desired
                   drawing  in  the drawing selection window located in the
                   upper screen area.  This selection window always appears
                   after  choosing  the option 'drawing' on the main menue.
                   Five drawings are displayed in the window at  one  time.
                   Once  the  drawings  are  chosen,  they  are  saved  and
                   preserved even after  exiting  the  program;   they  are
                   available  when  the program is restarted.  New drawings
                   are inserted by modifying the window contents.


                   How do we get a drawing into the selection window?

                   The program lets you choose one of three possibilities :


             ²²²²²²²²²²²²²²²²²²²
	     ²² Drawing       ²²
	     ²² View	      ²² <---  After selecting the function
	     ²² 	      ²²       view, this window appears.
	 ÍÍ> ²² Keyboard      ²²       Select the desired method
	 ÍÍ> ²² Window	      ²²       of input.
	 ÍÍ> ²² File list     ²²
             ²²               ²²
             ²²               ²²
             ²²               ²²
             ²²²²²²²²²²²²²²²²²²²
	     ²²    cancel     ²²  <---	Exit this fuction by selecting this
	     ²²²²²²²²²²²²²²²²²²²	field.



	      1.  View drawings with keyboard input

                   This function calls a dialogue window  for  the  program
                   name.   You  can  now enter the desired drawing name via
                   keyboard.  The drawing is then selected by pressing  the
                   mouse on the 'OK' field.



             ²²²²²²²²²²²²²²²²²²²
	     ²² drawing       ²²
	     ²² View	      ²²
             ²²²²²²²²²²²²²²²²²²²
	     ²² File name :   ²²
	     ²² 	   <--²² <ÍÍ  Enter macro name here
             ²²²²²²²²²²²²²²²²²²²
	     ²² OK ²²² cancel ²² <ÍÍ  Quit function with 'cancel'.
	     ²²²²²²²²²²²²²²²²²²²


                   Now  MegaCAD  prompts  you  to  select  the  area in the
                   selection window (at the top of the  screen)  where  the
                   macro  is to be displayed.  Select the lower part of the
                   fields with the macro names :

             ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄ¿
             ³          ³          ³          ³          ³         ³
             ³          ³          ³          ³          ³         ³
             ³          ³          ³          ³          ³         ³
             ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
             ÃÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄ´
             ³°°°            ^          ^                          ³
	     ³°M°	     ³		³ Select one of these	   ³
	     ³°E°			  fields !		   ³
             ³°N°                                                  ³
             ³°U°                                                  ³
             ³°E°                                                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ³°°°                                                  ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
	      L: <<Select Window>>"  R: <<Select window>>



                   After selecting the field, the drawing is drawn, and the
                   selection menue is displayed.



                   Select a drawing from the file list:

                   The selection of a drawing is also possible via the file
                   list.  A selection window with all existing drawings  is
                   displayed as explained in 'file list'.  Select a drawing
                   and place it into the desired window.




                   Creating drawings

                   In order to  create  a  drawing,  the  'create  drawing'
                   function must be invoked.

                   The  selection of the drawing to be created is performed
                   again by the functions 'keyboard',  'window'  and  'file
                   list'.

                   New drawings can be entered, or existing drawings can be
                   modified or over-written.

                   New drawings are created  by  entering  a  name  in  the
                   'keyboard' function.

                   Existing   drawings   can   be  selected  by  all  three
                   functions.

                   When selecting an existing drawing, the following window
                   appears:


             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
	     ²² File already exists !	²²
             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
	     ²²      Overwrite		²² <---  Move mouse cursor to
	     ²²      change		²² <---  a field and select
	     ²²      new name		²² <---
             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²


                   You  can choose, whether a drawing should be overwritten
                   (i.e.  the existing drawing is deleted and a new one  is
                   created), whether you wish to modify (edit) the drawing,
                   or whether you want to enter another name.

                   If you choose to over-write or modify, and there already
                   is a current drawing or macro, MegaCAD asks, whether the
                   existing drawing should be saved.


             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
	     ²²²²²Save current file ?²²²²²
             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
	     ²²²  YES  ²²²²²²²²²  NO   ²²² <ÍÍ Select yes or no
             ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²


	      ATTENTION!  If NO is selected, all current data is lost !


                   Saving drawings

                   This function is needed for saving  an  existing  macro.
                   Megacad  prompts  for a name, if one hasn't already been
                   entered.

                   if 'overwrite'  was  specified,  the  existing  file  is
                   overwritten.


                   Print drawing

                   See print macro



	  11. Separating drawing elements

              The  separating of drawing elements is used for later editing
              of drawings.  With this function, elements can  be  seperated
              at certain places.  The superfluous parts can be discarded in
              the process.

              For  circles,  which  have  not  yet  been   separated,   two
              separation points are needed.

              The  separating  of  a  circle now serves as an example.  The
              circle is divided into two halves by a line.  Only  one  half
              of the circle is needed for the drawing.  The following steps
              are necessary:


	      -   Select the 'separate' function on the menue.
              -   Select the circle to be separated.
	      -   Select the first intersecting point.
	      -   Select the second intersecting point.
              -   Exit the function by pressing the right mouse 
                  button.
	      -   Select the 'delete' function.
	      -   Delete the superfluous arc by selecting it using the
                  mouse.


          12. Deleting elements

              There are three methods for deleting elements:

              1.  Deleting individual elements
	      2.  Deleting individual elements with masks
              3.  Deleting a section on the screen

            ²²²²²²²²²²²²²²²²²²²
	    ²²	  Delete     ²²
            ²²²²²²²²²²²²²²²²²²²
	    ²² Text	  ON ²² <--
	    ²² Points	  ON ²² <--
	    ²² Lines	  ON ²² <--  Mask elements not to be
	    ²² Rectangles ON ²² <--  deleted
	    ²² Circles	  ON ²² <--
	    ²² Arcs	  ON ²² <--
	    ²² Dimensions ON ²² <--
            ²²²²²²²²²²²²²²²²²²²
	    ²²	individual   ²² <-- delete individual elements (Masked or free)
	    ²²	Screen	     ²² <-- delete whole visible area
	    ²²	section      ²² <-- delete all elements in section
	    ²²	Group	     ²² <-- Delete all elements in group
	    ²²	layer	     ²² <-- Delete all elements in layer
	    ²²	undo -1      ²² <-- Undo last delete operation
	    ²²	  cancel     ²² <-- quit function
            ²²²²²²²²²²²²²²²²²²²



                1)   With  this  option  all  elements  can   be   deleted
                      individually  from  the  drawing area.  The option is
                      invoked by selecting  the  'individual'  field.   The
                      element  to  be  deleted is selected using the mouse.
                      Exit the function by pressing the right button.

                2)    With this option, all drawing elements on the  screen
                      can  be  deleted.   All  elements  located completely
                      within the boundaries of the screen are deleted.

                3)    With this option, all drawing elements in  a  certain
                      section  can be deleted.  The section is drawn like a
                      rectangle.  All elements  located  completely  within
                      the  section  are  deleted by pressing the left mouse
                      button.

                   When using any of the delete functions, individual kinds
                   of  drawing  elements can be excluded (masked).  Masking
                   therefore means that these elements cannot  be  deleted.
                   This possibility is of great help in many cases.  If you
                   wish to delete points, and these points are  located  on
                   other  elements,  such  as  circles  or  lines,  you can
                   exclude these elements.  In doing this, you  can  ensure
                   that only the points are deleted.


          13. Redrawing of the screen contents

              'Redraw'  erases the whole drawing area and re-constructs the
              drawing, taking the active layers into account.


	  14. Details with zoom

              The zoom function provides the the possibility of  getting  a
              close  up  look  at  some  part  of  the drawing.  It is also
              possible reduce the size of the drawing by half.

              The zoom function affects only the display on the screen  and
              has no influence whatsoever on the drawing itself.

              After  accessing the 'zoom' option, the zoom selection window
              appears:

             ²²²²²²²²²²²²²²²²²²²²²
             ²²      Zoom       ²²
             ²²²²²²²²²²²²²²²²²²²²²
	     ²² def ²show ²zoom ²²  <-- Save, view and call Zoom areas
	     ²²  1  ²  1  ²  1	²²
             ²²  2  ²  2  ²  2  ²²
             ²²  3  ²  3  ²  3  ²²
             ²²  4  ²  4  ²  4  ²²
             ²²  5  ²  5  ²  5  ²²
             ²²²²²²²²²²²²²²²²²²²²²
	     ²²  Factor 0.5	²²  <-- Reduce size by 1/2
	     ²²  Autozoom	²²  <-- Optimal Drawing size
	     ²²  Total	(1:1)	²²  <-- set scale to 1:1
	     ²²  Direct zoom	²²  <-- direct zooming of an area
	     ²²  Pan		²²  <-- change displayed area
             ²²²²²²²²²²²²²²²²²²²²²
	     ²²     cancel	²²  <-- Quit zoom
             ²²²²²²²²²²²²²²²²²²²²²



	      1.  Saving and viewing zoom areas

                   The field 'def, show, zoom' in the selection  window  is
                   used  for  saving zoom areas and for quick displaying of
                   saved zoom areas (see also 'function keys').

                   In order to define an area, select  the  'def'  function
                   with  the  desired  number from 1 to 5.  The program now
                   prompts you to define the desired section.   Select  one
                   of the corner points of the new zoom area with the mouse
                   by moving to the position and pressing the left  button.
                   Now  a  rectangle  can  be  drawn  by  moving the mouse.
                   Enclose the area you wish to enlarge,  and  again  press
                   the  left  mouse  button.  The zoom area thus defined is
                   now saved.

                   In order to display zoom areas which have  already  been
                   defined,  select  appropriate  number  field  below  the
                   'show' field.  A rectangle with the corresponding number
                   area appears.

                   A  saved  zoom  area  is invoked by selecting the number
                   field  below  the  field  'zoom'.   MegaCAD  immediately
                   displays the zoom area on the screen.


	      2.  Reducing the scale

                   If  you  wish to see the periphery of the area displayed
                   on the screen, select  the  option  'factor  0.5'.   The
                   drawing  scale  is  doubled  each  time  this  field  is
                   selected.  Thus you can gain an  overall  view  of  your
                   entire  drawing.   If  a grid is active, it is no longer
                   displayed if the scale gets too big.


              3.  Automatic zooming

                   It is often necessary to see the entire drawing  on  the
                   screen.   This  is  why  'autozoom'  was included in the
                   program.  The scale  is  automatically  set  to  such  a
                   factor, that the drawing fills the entire screen.


	      4.  1:1 scale

                   This option automatically switches the screen display to
                   a 1:1 scale.  The display appears in the same area as at
                   the start of the program.  The zero point of the drawing
                   area is again located in  the  lower  left-hand  corner.
                   This  is  the  scale in which all drawings are saved and
                   initially displayed.


	     5.   Pan
                   Use this fuction to shift  the  displayed  part  of  the
                   drawing.   When  invoked, select the point on the screen
                   which is to become the new center point.

          
          15. Editing

              The 'edit' option consists of several functions for modifying
              drawings  and  drawing elements.  The following functions are
              accessible:

              -   edit text
	      -   change text lines to text blocks
              -   shift elements between groups
              -   shift elements between layers
	      -   copy and move drawing elements
              -   reduce and enlarge drawing elements
              -   mirror drawing elements
              -   rotate drawing elements
              -   information about drawing elements
	      -   coordinate interface
              -   round drawing elements
              -   bevel drawing elements
              -   trim drawing elements
              -   modify drawing elements
              -   stretch drawing elements
	      -   break up drawing elements
                   
          16. Group

              The 'group' option enables you to assign drawing elements  to
              groups.   This function allows for complete drawing groups to
              be manipulated.  256 groups can be formed, all of  which  can
              be  activated  as  you  please.  Thus, you can assign drawing
              elements to different groups,  and  then  modify  or  edit  a
              complete group.

          17. Fixed

              When  this  field  is  selected,  MegaCAD saves all currently
              valid settings, such as text  attributes,  grid  calibration,
              etc.   These  values  are  then  set  initially the next time
              MegaCAD is called.

          18. Layer

              The 'layer' option enables you to assign drawing elements  to
              layers.   The  256  availabe  layers  can be activated as you
              please.  During construction  you  can  place  elements  into
              different  layers;   during construction they can be switched
              to be 'visible' or 'invisible'.

          19. Exit

              The 'exit' option ends the program.  If the  current  drawing
              has  not  yet beeen saved, you are asked, whether the drawing
              is to be saved.



          20. The function keys

              For quicker processing of drawings,  various  functions  have
              been  placed  on function keys.  Although the menue strip can
              be accessed very quickly, the selection via function keys has
              proven  to  be  more  useful  in  certain  cases.  This makes
              working with MegaCAD even faster.

              The following key combinations are possible:

              a        = automatic zoom of all elements
	      w        = immediate zooming by drawing rectangle
              h        = reduce image by factor 0.5 (half zoom)
              ALT + p  = pan zoom
	      ALT + 1  = save set scale as zoom 1
	      ALT + 2  = save set scale as zoom 2
	      ALT + 3  = save set scale as zoom 3
	      ALT + 4  = save set scale as zoom 4
	      ALT + 5  = save set scale as zoom 5
	      ALT + 0  = set scale to initial values
	      1        = invoke saved zoom 1
	      2        = invoke saved zoom 2
	      3        = invoke saved zoom 3
	      4        = invoke saved zoom 4
	      5        = invoke saved zoom 5
	      R        = redraw
              c        = direct access to 'delete' function 
              t        = direct access to 'separate' function
              ALT + t  = direct access to 'trim' function
              ALT + r  = direct access to 'round' function
	      ALT + b  = MODE tangential point 1/2
	      ALT + s  = MODE intersecting point 1/2
	      ALT + 1  = MODE element distance
	      ALT + e  = MODE end point distance
	      f        = MODE free
	      g        = MODE grid
	      p        = MODE point
	      s        = MODE intersecting point simple
	      c        = MODE center point
	      b        = MODE tangential point
	      l        = MODE element
	      e        = MODE end point
	      k        = MODE keyboard
	      SHIFT    = MODE selection (window selection)
              ALT + S  = style selection
              
              ALT + ... means pressing the ALT key plus another key, 
              while the ALT key is still pressed.

              The functions are always active, when no  window  is  on  the
              screen which means only one function can be directly accessed
              at a time.  Exit the direct functions by pressing  the  right
              button of the mouse.


              Example:

              You  are drawing a few lines.  Now a circle crossed by a line
              is to be separated directly, and one of the  arcs  is  to  be
              deleted.

              1)   Press  ALT  + T.  Select the circle as the element to be
                   separated,   using   the   mouse.    Then   select   the
                   intersecting points as separating points.  First, select
                   the  intersecting  point  via  mode   selection.    Exit
                   function by pressing the right mouse button.

              2)   Now  the  arc  which  is  not  needed  anymore  is to be
                   deleted.  Select the delete function directly via ALT  +
                   C.   The  mouse  arrow  turns  into a small square.  Now
                   select  the  arc  using  the  mouse,  and  the  arc   is
                   instantaneously  deleted.  Exit function by pressing the
                   right mouse button.

              3)   Now  you  can  go  on  drawing  lines  without   further
                   selection, since you never left the function for drawing
                   lines.

              One more useful application of  the  function  keys  lies  in
              accessing  the zoom saving areas.  After having defined areas
              in the zoom function, these areas are accessible at all times
              by the keys ALT + 1-5.  Thus, you can jump from one zoom area
              to another within one drawing  function,  without  having  to
              exit the selected function.

          ------------------------------------------------------------
         
          (c) 1989, 1990 copyright by
          MEGATECH-Software GmbH
          West Berlin