XPANDISK.SYS and XPANBOSS
                        Device Driver and Command

                           Michael J. Mefford
                         1988 No. 18 (Utilities)
                                                 

Purpose:     Permits varying the amount of expanded memory allocated to 
a RAM disk without rebooting, when used on systems equipped with memory 
that conforms to the Lotus/Intel/Microsoft specification. 

Format:  In CONFIG.SYS file:

              DEVICE=XPANDISK.SYS [/Dn][/Sn][/En][/Mn][/An]

         At DOS command prompt:

              XPANBOSS [d:][/Dn][/Sn][/En][/Wn][/Rn][/Mn][/An]

Remarks:     XPANDISK makes use of an Expanded Memory Manager. The 
DEVICE=XPANDISK.SYS entry must, therefore, follow the DEVICE=EMM.SYS 
(driver name will differ with  manufacturer) line already in the 
CONFIG.SYS file. XPANBOSS varies the parameters of the RAMdisk d: 
created by XPANDISK.  Note that while this does not require rebooting, 
changing parameters other than /R (Read-Only) does reformat d:, whose 
contents are thereby lost.  A confirmation warning is given to allow 
saving the RAMdisk files before the reformatting.  The optional switch 
parameters for XPANDISK.SYS and XPANBOSS.COM are as follows: 

    /Dn  Disk size, variable from 16K to 32,768K; default 64K.
    /Sn  Sector size, 128, 256, or 512 bytes; default 265 bytes.
    /En  Number of RAMdisk root directory entries; default 64.
    /Mn  Minimizes RAMdisk size (to 16K); use when running
          large spreadsheets or databases.
    /An  Expands RAMdisk to fill all extended memory.
    /Wn  Eliminates warning that changing RAMdisk
          parameters loses contents; use in batch file operation.
    /Rn  Make RAMdisk read-only; use after loading possible
          Trojan horse programs.  RAMdisk d: may be returned
          to read-write by entering d:XPANBOSS.

    Note:  DOS assigns the next available drive letter as d:.  Be sure 
that this does not cause a conflict if you are using a SUBST drive. 

    Note:  XPANDISK and XPANBOSS allow the same parameter comments 
permitted by the VDISK.SYS extended/conventional device driver.  Thus, 
for example, you could enter 

         DEVICE=XPANDISK.SYS /disk size=120K /sector=128

and DOS would understand this as

         DEVICE=XPANDISK.SYS /D120/S128