VIDEO ALIGNMENT DIAGNOSTICS
                      By Larry & Garry Kraemer
                         Copyright (C) 1987
 
This Diagnostic program will help you check the STATIC and DYNAMIC
convergence of your color monitor.  By using this program you will
have the capability of STATIC/DYNAMIC convergence for the RED, GREEN,
and BLUE guns.  Monitors that have INLINE GUNS will not require DYNAMIC
Convergence since all guns lie in one horizontal plane.
 
The authors assume no responsibility for any damage or conditions
which result from the use of this program or from the attempt to
align your specific monitor.  The authors have made an honest attempt
to give you all the necessary details for the alignment, but once
again you are responsible for any and all conditions which may result.
 
ESCAPE key exits all menus and terminates program.
 
                       USE IT AT YOUR OWN RISK!!!