Your SMILEQ20 file should contain the following files:

          SMILEQ.EXE    -   SMILE Quick viewer.
          SMILEL.EXE    -   SMILE List viewer.
          SMILESS.EXE   -   SMILE Slide Show.

          SMILEQ20.DOC contains documentation for all programs.
          Please DO NOT distribute these programs separately.

          These ANSI display utilities allow the user to view
          files containing ANSI sequences, Music strings (in BASIC
          "PLAY" format), and Sounds (using a custom SOUND code).
     
          NO ANSI DRIVER is required to view ANSI screens as all
          programs contain a built-in ANSI translator.  Keyboard
          reassignment codes are ignored.





         ÚÄÄ¿
         ³SMILE Quick  Ver 2.0   Copyright (c) 1991.....Michael Arnett
         ÀÄÄÙ 
     
          Syntax:

          SMILEQ file1 [file2]... [/B][/C][/F][/M][/N#][/S#][/T#]

          Enter SMILEQ at the DOS prompt to view a list of available
          parameters.
     
          SMILEQ displays files specified on the command line using
          (optional) /switch features.  SMILEQ will default to an ANS
          extension if none is given.  Wild cards are supported in
          filespec designations.  
            
          See list of COMMAND LINE SWITCHES for definitions.
     




         ÚÄÄ¿
         ³SMILE List  Ver 1.0   Copyright (c) 1992.....Michael Arnett
         ÀÄÄÙ 

          Syntax:

          SMILEL  [/B][/C][/F][/M][/S#][/T#]

          A scrolling pick list of *.ANS files is presented for
          display.  Available memory determines the number of files
          that can be listed.  600 files were listed, in a test, with
          about 580K of free memory.  Other options available from
          this list include:

               Changing Drives, Directories and File mask. 
               Sorting list on Name, Extension, Size, etc.
               Expand Directory window to show file information.

           Scroll through the list using the Cursor Keys, PgUp, PgDN,
           Home, End kyes, or mouse.  Highlight the file you want to
           view and press ENTER or CLICK the Left Mouse button.  Press
           ESC or Right Mouse button to Exit.

           See list of COMMAND LINE SWITCHES for definitions.





         ÚÄÄ¿
         ³SMILE Slide Show   Ver 1.0   Copyright (c) 1992...Michael Arnett
         ÀÄÄÙ 

          Syntax:
     	   
          SMIELSS  Filespec [/B][/C][/M][/N#][/S#][/T#]

          SMILE Slide Show reads file names for display from a specified
          file (Filespec).  Display of files will cycle until CANCLED.  

          SMILEQ List.dat
     		 
          would instruct SMILESS to read file names from the file
          LIST.DAT.  The format for LIST.DAT is as follows:
     	   
             file1.ans [ switches ] 
             file2.ans [ switches ] 
             file3.ans [ switches ] 
             etc...
     	   
          FILELST.DAT files, built by "The SMILE Viewer", can be
          used with SMILE SLIDE SHOW.  

          Command line options listed above may be designated on the 
          command line for GLOBAL, use or a unique set of options may
          be chosen for each file name specified.  For example:

               SMILEQ List.dat      { All options set to default   }

               file1.ans  /C        { view in EGA/VAG mode         }
               file2.ans            { default options reset        }
               file3.ans  /S2400    { Simulate 2400B rate display  }
               file4.ans            { default options reset        }


          Wildcards are *NOT* supported withSMILE Slide Show.
     	   
          See list of COMMAND LINE SWITCHES for definitions.     
     




         ÚÄÄ¿
         ³COMMAND LINE SWITCHES (optional)
         ÀÄÄÙ 
     
          /B ... Disable screen Blanking (clearing) before each
                 file is displayed.  

              [*]SUPPORTED in SMILEQ, SMILEL, and SMILESS     
              [*]DEFAULT: clear screen before each file is displayed
          
          /C ... Toggles EGA/VGA monitors between 25 Line TEXT mode
                 and 43/50 Line TEXT mode.  Screen is returned to 
                 START-UP mode when you exit SMILEQ.  If you're PC is in 
                 43/50 Line mode and you start SMILEQ with this switch, 
                 25 Line mode will be toggled on.

              [*]SUPPORTED in SMILEQ, SMILEL, and SMILESS     
              [*]DEFAULT: Start-up mode
     	   
          /F ... Delete/Rename file after viewing.  An option box
                 is popped up after the screen is displayed.

              [*]SUPPORTED in SMILEQ and SMILEL          
              [*]DEFAULT: File Rename/Delete option is OFF

          /M ... Disable Music and SOUND codes.
       
              [*]SUPPORTED in SMILEQ, SMILEL, and SMILESS
              [*]DEFAULT: Music ON
     	  
          /N#... Nonstop display between screens.  # specifies the
                 number of seconds to delay. (0..60) Nonstop delay 
                 defaults to 3 seconds if no number is specified.
      	   
              [*]SUPPORTED in SMILEQ and SMILESS
              [*]DEFAULT: Prompt for keypress between each screen
     	   
          /S#... Set Simulated BAUD rate display speed.  # specifies 
                 desired BAUD rate.  Valid speeds are 19200, 9600,
                 2400 1200, and 300.  If no rate, or an invalid rate 
                 is specified, Speed defaults to 2400.
     	   
              [*]SUPPORTED in SMILEQ, SMILEL, and SMILESS
              [*]DEFAULT: 0 (Fastest display)
     
          /T#... Define an ESC translate character.  "#" desigantes
                 the Decimal value of a character.  Some BBS software
                 strips all ESC characters from ANSI screens.  This 
                 switch allows you to specify what that character 
                 will be.  SMILEQ will translate any combination of 
                 the character and "[" to a true ESC.  Valid entries
                 are 1 to 254.
                 (DEC 96 and DEC 250  are translated automatically)

              [*]SUPPORTED in SMILEQ, SMILEL, and SMILESS
              [*]DEFAULT: none





         ÚÄÄ¿
         ³VIEWING FILES:
         ÀÄÄÙ 
     
          The SMILE viewers now have support for unlimited characters
          per line.  Multiple lines of MUSIC may be entered between
          ESC[ and CTRL-N.  There is no limit on actual file size.  
     
          DEFAULT MODE: 

          Pressing ESC will CANCEL the display and/or stop the
          program.  Any other key will PAUSE the display and a 
          "More (Y/n)" prompt will be displayed.
     
          NONSTOP MODE: 

          Pressing ESC during screen display will CANCEL the display
          and stop the program.  Any other key will PAUSE for
          specified number of DELAY seconds.  Pressing ESC during the
          PAUSE counter will stop the counter and display the next 
          screen.

     
          To try and support users where local Bulletin Boards
          convert ESC characters, SMILEQ will translate the following
          as ESC sequences:
     
          ú[   ( Dec 250 + [ ) 
          ù[   ( Dec 249 + [
          `[   ( Dec 96 + [ )

          The /T# switch may also be used to define a custom ESC 
          translate character.

          Screens should display if multiple codes are used in a file
          but this should probaby be avoided.
          
          
          Since old habits die hard, support for the GT Power BBS
          message base "pause character" continues to be supported.
          The CTRL-E character (Dec 5) placed as the first character
          of a line will cause SMILEQ to pause as described in the
          DEFAULT and NONSTOP modes above.
     
     
     
     

         ÚÄÄ¿
         ³MUSIC:
         ÀÄÄÙ 

          Syntax: ESC[MF T120 O2C8D8E8F8G8 (CTRL-N)
     
          Music strings in the BASIC Play format are supported.
          Multiple strings per line may be entered.  
     
          Music strings should begin with the characters "<esc>[M"
          where <esc> is a true ESC character (DEC 27, Hex 1B).
          Please refer to your BASIC manual for information on the
          BASIC Play commands.  The following are all valid for
          beginning a Music string in SMILEQ: MF, MB, MN, ML, MS, M .
          Although MB (Music Background) is valid, true backgroud    
          music is NOT supported.
     
          Music strings should end with the musical note character
          CTRL-N (DEC 14, Hex 0E).  If this character is missing,
          SMILEQ will look for the next ESC character or the
          end-of-file marker to terminate the music string.  This
          option was added to try and catch as many incorrectly
          formated music strings as possible.  However, for
          compatiblity with other viewers, I suggest you always end
          your music strings with CTRL-N (DEC 14)
     

     
         ÚÄÄ¿
         ³SOUND:
         ÀÄÄÙ 
          [*]Thanks to Julie Ibarra, author of ANSIPLAY for this idea
     
          Syntax: 
          Freq; Duration; Cycle1; Delay1; Variation; Cycle2; Delay2
     
          Custom Sounds are supported in SMILEQ by using a SOUND CODE
          similar to that found in BASIC, but emulates the custom
          SOUND CODE found in the program ANSIPLAY more closely.
          However, a second Cycle\Delay option was added to the SOUND 
          CODE used in SMILEQ, providing a looping effect.  The frequency
          values used to produce the musical notes are listed somewhere
          down the page.  Duration timing was also adjusted in SMILEQ
          to more closely match that of the BASIC SOUND command.  The
          Duration of SOUNDs created for earlier versions of SMILEQ will 
          have to be edited.     

          The SOUND statement must begin and end in the same manner
          discussed above for a normal music string.  

          The SOUND CODE consists of the following parameters serparated 
          by a semicolons (;) :
     
          FREQ     : Frequency of note to be played.  The effective 
                     range of frequencies is 37 to 7904.  
                     (0..65535)
          
          DURATION : Time, in CLOCK TICKS, the note should be played.
                     (18.2 ticks per second)
                     (0..65535)
     		
          CYCLE1   : Number of times to repeat Frequency\Duration.
                     (0..65535)
     		
          DELAY1   : Delay Time between CYCLE1 (Milliseconds / 4).  
                     (0..65535)
     		
          VARIATION: Frequency value is changed by this number for
                     each CYCLE the note is played.  A negative number
                     will be subtracted, but if FREQ reaches 0 then 
                     VARIATION is added to FREQ for the remainder of the
                     cycles.
                     (-65535..65535)

          CYCLE2    : Number of times to repeat the first 5 parameters
                      <Freq;Duration;cycles;delay;variation>
                      (0..65535)

          DELAY2    : Delay Time between CYCLE2 (Milliseconds /4).
                      (0..65535)
     
          (NOTE: 1 second = 1000 milliseconds)
     		
     
          EXAMPLE: (Telephone jingle)
                   ESC[MF 800;1;2;50;-200;10;50 CTRL-N

                ESC[MF  Trigger sequencd
          Freq:    800  Note Frequency 
          Dura:      1  Play Note for 1 Clock Tick (18.2 ticks per second)
          Cyc1:      2  Repeat Frequency\Duration 2 times
          Dly1:     50  Delay 10/4 milliseconds before repeating 
          Vari:   -200  Decrease Note value by 200 each cycle 
          Cyc2:     10  Repeat first 5 parameters 10 times
          Dly2:     50  Delay 10/4 milliseconds before repeating
                CTRL-N  Terminate Character
          

          One advantage of the SOUND CODE is the ability to place a
          PAUSE in your ANSI screens without having to use a
          multitude of ESC[s codes.  Just use a SOUND CODE with the
          DELAY set very high to get a pause.  For example,
     
          ESC[MF ;;;60000
     
          would pause your ANSI Screen for 15 seconds (60000/4), or 
          until a key is pressed when viewing it with SMILE.  Remember,
          these SOUND CODES are not supported by bulletin boards...(yet)!

     
          Press Any Key to exit a DURATION or DELAY action.
     
          SOUND CODE Musical Note Frequency Values (7 Octives):
     

            C    C#   D    D#   E    F    F#   G    G#   A    A#   B
       
            65   69   73   78   82   87   92   98  104  110  116  123 
           131  139  147  156  165  175  185  196  208  220  233  247 
           262  278  294  312  330  350  370  392  416  440  466  494 
           524  556  588  624  660  700  740  784  832  880  932  988 
          1048 1112 1176 1248 1320 1400 1480 1568 1664 1760 1864 1976 
          2096 2224 2352 2496 2640 2800 2960 3136 3328 3520 3728 3952 
          4192 4448 4704 4992 5280 5600 5920 6272 6656 7040 7456 7904  


     

         ÚÄÄ¿
         ³DISCLAIMER:
         ÀÄÄÙ 
     
          SMILEQ 2.0, SMILEL 1.0 and SMILESS 1.0 are provided *AS IS* 
          without any warranty, expressed or implied.  All Rights are 
          reserved.  The author will assume no liability for damages 
          either from the direct use of this product or as a consequence
          of the use of this product.
     
     
     
         ÚÄÄ¿
         ³COMMENTS:
         ÀÄÄÙ 
     
          SMILEQ, SMILEL and SMILESS were written with
          Turbo Pascal 6.0 and TechnoJock Software Toolkits
                   
     
          GT Power is copyright by P&M Software
          ANSIPLAY is copyright by Julie Ibarra
     
         
          SMILE QUICK 1.0, SMILE LIST 1.0, and SMILE SLIDE SHOW 1.0 
          have been donated to MAKE A KID SMILE, INC. at no cost.
          All proceeds are used in support of donating computers for
          use by hospitalized children.  These programs are fully
          functional.  Please support the shareware concept and help
          use MAKE A KID SMILE.

          If you find this program useful, please consider supporting
          The MAKE A KID SMILE project with whatever you can afford.
          This would encourage further development of this program.  For
          a donation of $20 or more you will receive the latest versions 
          of SMILE Quick, SMILE List and SMILE Slide Show Viewers, and 
          The SMILING KIDS ANSI ART COLLECTION.  Please specify the 
          program you are ordering.  

                     Send donations to the following adress
                 and make all checks payable to MAKE A KID SMILE.  
                 For those outside the US we ask that you please
                 send a cashier's check or money order.


         
                           MAKE A KID SMILE 
                           c/o Ernest DeBakey
                           The Bechtel Tower, Suite 1480
                           3000 Post Oak Boulevard
                           Houston, TX 77056-6582     
     
     
          All comments and suggestions are welcomed and may be sent to:

                           Michael Arnett
                           2623 Halstead 
                           Spring, TX 77386

                           or 

                           GT Power Network EMAIL

                           The Gavel BBS, Houston Tx.
                               NetMail  001/030
                               EchoMail E10/037