SPS.COM ver 2.0 by Bob Montgomery, 4-23-87

This is a Terminate and Stay Resident (TSR) program which does  a
Selective  Print Screen (hence the name SPS). Once installed,  it
vectors  interrupt 5 (the print screen interrupt) to itself,  and
sits waiting for a print screen request. When you request a print
screen,  the  cursor is moved to the top of the screen,  and  the
prompt  'Set  start  position' appears in the  lower  right  hand
corner.  The  cursor  can be moved around  the  screen  with  the
following keys:

     Right arrow - move cursor right; stops at right edge
     Left arrow -  move cursor left; stops at left edge
     Up arrow -    move cursor up one line; stops at top line
     Down arrow    move cursor down one line; stops at bottom line
     Page Up       move cursor to top line
     Page Down     move cursor to bottom line
     ^Right arrow  move cursor to right edge of screen
     ^Left arrow   move cursor to left edge of screen
     Home          move cursor to upper left corner of screen
     End           move cursor to lower right corner of screen
     P             Print whole screen
     Escape        Cancel print screen

When the cursor is at the desired start position, press Enter and
the prompt 'Set end position' will appear in the lower right hand
corner.  Move the cursor to the desired end position,  and  press
Enter  again. The text within the rectangle defined by the  start
and end positions will then be printed.

If  you don't want to do a print screen, press Escape  to  cancel
the operation and return to the interrupted program. If you  want
to print the whole screen, press the P (upper or lower case) key.

Before the printer starts printing, the prompt in the lower right
corner  is  removed  and the original text is  restored.  If  the
printer  is  not  ready (or deselected), a  prompt  'Printer  not
ready'  will  appear  in the lower right  corner  after  about  2
seconds. Then after about 10 seconds, if the printer is still not
ready,  the  print  screen operation aborts and  returns  to  the
interrupted  program.  If during the print screen  operation  the
printer  becomes  'not ready', a prompt will tell you  this,  and
give you about 10 seconds to fix the problem before aborting.

The  program only traps interrupt 5 (print screen) until  invoked
by  pressing Shift PrtSc. Then, it vector the timer and  keyboard
interrupts  (8 and 9) to itself, and saves the old vectors.  When
it is done, it puts the old vectors back, and quits. In this way,
it is essentialy 'not there' until called, and 'not there'  after
it  is  done. This means that it will not  interfere  with  other
programs,  and  not  cause  additional  processing  delays.  Once
invoked, it traps all keyboard input and does not pass it on,  so
the  interrupted  program, other TSRs, and BIOS never  know  that
keys have been pressed. Since the last thing BIOS knew before the
program  was invoked was that the Shift and PrtSc keys  had  been
pressed, the releasing of the Shift key is passed on so that BIOS
can do its housekeeping; releasing the PrtSc key does not  affect
the  BIOS housekeeping, so it is not passed on. This  means  that
the  program must service the keyboard each time it generates  an
interrupt 9, a job which is normally done by BIOS.

This program  solves  a number of problems, some  of  which  were
present with the previous version of SPS by Paul Trioano.

     1. Passing  keys  on is sometimes a problem,  because  other
        programs (like CED) will save the keypresses, and act  on
        them  after the interrupting program quits.
     2. Sending  the  screen characters directly is  sometimes  a
        problem,  since  some screens contain  control  character
        (below  20h) and make them appear as blanks  by  changing
        the attribute to black on black; HDIR is an example. This
        will  cause  the printer output to not  match  the  video
        screen.
     3. Routing  interrupts  thru  a program  when  not  required
        takes  extra processing time, and can cause  interference
        with other programs.

The source code is included, and is liberally commented to  allow
those  interested to understand how it works. It uses  only  BIOS
calls  and no DOS calls; DOS calls will not work in TSR  programs
because DOS is not re-entrant. It has been tried on the XT and AT
with no problems, so will probably work on all machines with  IBM
compatible  BIOS. If you have any problems or comments,  leave  a
message  with the Black Hole BBS in Orlando, Florida, (305)  260-
6397. Enjoy.

Bob Montgomery