MULTIDGT.DOC -- Multidigit Arithmetic Procedures
================================================

  From `BLUEBOOK of ASSEMBLY ROUTINES for the IBM PC & XT'
        by Christopher L. Morgan
        Copyright (C) 1984 by The Waite Group, Inc.

   Purpose: These routines perform addition, subtraction, multiplication, 
     and division upon multidigit integers (16-bit).
 
   Contents:
   ---------
   MBINADD --  Multidigit binary addition
   MBINDIV --  Multidigit binary division
   MBINMUL --  Multidigit binary multiplication
   MBINSUB --  Multidigit binary subtraction

  Overview: These routines use 16-bit integers as `digits', but could easily
    be modified to use 8-bit integers, instead. Many operations are performed
    using 8- or 16-bit arithmetic operations on the individual `digits'. The
    exception here is the division routine, which uses binary arithmetic.

 ____________________________ MULTIDIGIT ROUTINES ____________________________
          
Routine to perform multidigit binary addition.

  Function: This routine adds two multidigit binary numbers.

  Input: Upon entry, DS:SI points to the first number, DS:DI points to the
    second number, and DS:BX points to the location where the result will be
    stored. The size of thes multidigit numbers is controlled by the constant,
    ISIZE. All three numbers contain 16 * ISIZE number of bits and are stored
    in ISIZE number of 16-bit words in memory.

  Output: Upon exit, DS:BX points to where the result is stored.

  Registers used: Unmodified; SI, DI, BX, CX, & AX are saved & restored.

  Segments referenced: Upon entry, the data segment must contain the constant,
    ISIZE and storage for three multidigit numbers, two for input and one for
    output.
______________________________________________________________________________

Routine to perform multidigit binary division.

  Function: This routine divides two multidigit binary numbers, returning
    both a quotient and a remainder.

  Input: Upon entry, DS:SI points to the divisor, DS:BX points to where the
    dividend is upon entry and where the remainder will be upon exit, and
    DS:DI points to the location where the quotient will be upon exit. The
    size of thes multidigit numbers is controlled by the constant,ISIZE.
    The divisor and quotient contain 16 * ISIZE number of bits and the dividend
    and remainder have double that precision.  Both the divisor and quotient
    are stored in ISIZE number of 16-bit words in memory, and the dividend 
    and remainder are stored in 2 * ISIZE number of 16-bit words of memory.

  Output: Upon exit, DS:BX points to where the quotient is stored and
    DS:DI points to where the remainder is stored.

  Registers used: Unmodified; SI, DI, & CX are saved & restored.

  Segments referenced: Upon entry, the data segment must contain the constant,
    ISIZE and storage for the multidigit numbers described above.
______________________________________________________________________________

Routine to perform multidigit binary multiplicaton.

  Function: This routine multiplies two multidigit binary numbers.

  Input: Upon entry, DS:SI points to the first number, DS:DI points to the
    second number, and DS:BX points to the location where the result will be
    stored. The size of thes multidigit numbers is controlled by the constant,
    ISIZE. All three numbers contain 16 * ISIZE number of bits and are stored
    in ISIZE number of 16-bit words in memory.

  Output: Upon exit, DS:BX points to where the result is stored.

  Registers used: Unmodified; SI, DI, BX, CX, & AX are saved & restored.

  Segments referenced: Upon entry, the data segment must contain the constant,
    ISIZE and storage for three multidigit numbers, two for input and one for
    output.
______________________________________________________________________________

Routine to perform multidigit binary subtraction. 

  Function: This routine subtracts two multidigit binary numbers.

  Input: Upon entry, DS:SI points to the first number, DS:DI points to the
    second number, and DS:BX points to the location where the result will be
    stored. The size of thes multidigit numbers is controlled by the constant,
    ISIZE. All three numbers contain 16 * ISIZE number of bits and are stored
    in ISIZE number of 16-bit words in memory.

  Output: Upon exit, DS:BX points to where the result is stored.

  Registers used: Unmodified; SI, DI, BX, CX, & AX are saved & restored.

  Segments referenced: Upon entry, the data segment must contain the constant,
    ISIZE and storage for three multidigit numbers, two for input and one for
    output.
______________________________________________________________________________
>>>>> Physical EOF MULTIDGT.DOC <<<<<