MICEPT INSTRUMENTS INC.                               MICEPT INSTRUMENTS INC.

                             Cross Assemblers (Series II)                             Cross Assemblers (Series II)
                                     Version 2.20                                     Version 2.20

                                    USER'S MANUAL                                    USER'S MANUAL

























                              Micept Instruments Inc.
                              377 Julien St.
                              Cap De La Madeleine, PQ
                              Canada  G8T 6W6

















          DISCLAIMER          DISCLAIMER

          Micept  Instruments  Inc.  disclaims all  warranties  as  to this
          software  and the  documentation,  whether  express  or  implied,
          including,   without  limitation,   any  implied   warranties  of
          merchantability   and  of   fitness  for   any  purpose.   Micept
          Instruments  Inc. assumes  no liability  for  damages, direct  or
          consequential, which may results from the use of this software or
          the documentation.

          Information in this document is subject to change without notice.

          Copyright (C) 1991, 1992 by Micept Instruments Inc.


          COPYRIGHT INFORMATION          COPYRIGHT INFORMATION

          This version of  the software is  distributed as shareware.  This
          version  may  be  freely copied  and  distributed  for evaluation
          purposes  as  long  as NO  FEE  IS  CHARGE  FOR  USE, COPYING  OR
          DISTRIBUTION (EXCEPT FOR A NOMINAL DISTRIBUTION FEE PROVIDED THAT
          IT IS NO MORE THAN $5 TOTAL) and  as long as THE SOFTWARE PACKAGE
          IS NOT MODIFIED IN ANY WAY.

          USE  OF THIS  SOFTWARE  BEYOND  A  REASONABLE  EVALUATION  PERIOD
          REQUIRES REGISTRATION.

          The   entire   package,   consisting   of   the   main  programs,
          documentation  file and various  utility files are  all copyright
          (C) 1991, 1992 by Micept Instruments Inc. All rights reserved.


          Rockwell 6502 is a registered trademark of Rockwell International
          Corporation.
          MS-DOS is a trademark of Microsoft Corporation.
          IBM, PC, XT, AT are trademarks of International Business Machines
          Corporation.
          All   brand  and  product  names  are  trademarks  or  registered
          trademarks of their respective companies.






                                  TABLE OF CONTENTS                                  TABLE OF CONTENTS


          1. INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . .   1

          2. INSTALLATION . . . . . . . . . . . . . . . . . . . . . . .   1

          3. SYSTEM REQUIREMENTS  . . . . . . . . . . . . . . . . . . .   1

          4. FILES IN THE PACKAGE . . . . . . . . . . . . . . . . . . .   1

          5. FORMAT OF COMMANDS . . . . . . . . . . . . . . . . . . . .   2

          6. COMMAND LINE . . . . . . . . . . . . . . . . . . . . . . .   2
               6.1 Invocation . . . . . . . . . . . . . . . . . . . . .   2
               6.2 Options in more details  . . . . . . . . . . . . . .   3
               6.3 Error codes returned to DOS  . . . . . . . . . . . .   4
               6.4 Object code file formats . . . . . . . . . . . . . .   5
               6.5 Environment variable . . . . . . . . . . . . . . . .   5

          7. SOURCE LINE FORMAT . . . . . . . . . . . . . . . . . . . .   5
               Label  . . . . . . . . . . . . . . . . . . . . . . . . .   5
               Opcode . . . . . . . . . . . . . . . . . . . . . . . . .   6
               Operand  . . . . . . . . . . . . . . . . . . . . . . . .   6
               Comment  . . . . . . . . . . . . . . . . . . . . . . . .   6

          8. EXPRESSIONS IN THE OPERAND FIELD . . . . . . . . . . . . .   6
               8.1 Symbols  . . . . . . . . . . . . . . . . . . . . . .   6
               8.2 Constants  . . . . . . . . . . . . . . . . . . . . .   7
                    Numeric constants . . . . . . . . . . . . . . . . .   7
                    Character constants . . . . . . . . . . . . . . . .   7
                    The location counter  . . . . . . . . . . . . . . .   8
               8.3 Operators  . . . . . . . . . . . . . . . . . . . . .   8
               8.4 How expressions are evaluated  . . . . . . . . . . .   8

          9. ASSEMBLER DIRECTIVES . . . . . . . . . . . . . . . . . . .   9
               ACLIST . . . . . . . . . . . . . . . . . . . . . . . . .   9
               DB . . . . . . . . . . . . . . . . . . . . . . . . . . .   9
               DW . . . . . . . . . . . . . . . . . . . . . . . . . . .  10
               END  . . . . . . . . . . . . . . . . . . . . . . . . . .  10
               EQU  . . . . . . . . . . . . . . . . . . . . . . . . . .  10
               LIST . . . . . . . . . . . . . . . . . . . . . . . . . .  10
               LLEN . . . . . . . . . . . . . . . . . . . . . . . . . .  10
               NOACLIST . . . . . . . . . . . . . . . . . . . . . . . .  11
               NOLIST . . . . . . . . . . . . . . . . . . . . . . . . .  11
               ORG  . . . . . . . . . . . . . . . . . . . . . . . . . .  11
               PAGE . . . . . . . . . . . . . . . . . . . . . . . . . .  11
               PLEN . . . . . . . . . . . . . . . . . . . . . . . . . .  11
               REDEF  . . . . . . . . . . . . . . . . . . . . . . . . .  12
               RSB  . . . . . . . . . . . . . . . . . . . . . . . . . .  12
               RSW  . . . . . . . . . . . . . . . . . . . . . . . . . .  12
               SET  . . . . . . . . . . . . . . . . . . . . . . . . . .  12
               SETDP  . . . . . . . . . . . . . . . . . . . . . . . . .  13
               TITLE  . . . . . . . . . . . . . . . . . . . . . . . . .  13






          Micept Instruments Inc. - Cross Assemblers (Series II)        iii



          10. SPECIAL SECTION ON THE MICROPROCESSORS  . . . . . . . . .  14
               10.1 Motorola 6800 . . . . . . . . . . . . . . . . . . .  14
               10.2 Motorola 6803 . . . . . . . . . . . . . . . . . . .  14
               10.3 Motorola 6805 . . . . . . . . . . . . . . . . . . .  15
               10.4 Motorola 6809 . . . . . . . . . . . . . . . . . . .  15
               10.5 Rockwell 6502 . . . . . . . . . . . . . . . . . . .  16
               10.6 Rockwell 65C02  . . . . . . . . . . . . . . . . . .  16

          11. BUG REPORTING PROCEDURE . . . . . . . . . . . . . . . . .  16

          12. UPDATE POLICY . . . . . . . . . . . . . . . . . . . . . .  17

          13. REGISTRATION  . . . . . . . . . . . . . . . . . . . . . .  17

          APPENDIX A - EXPANDED VERSION . . . . . . . . . . . . . . . .  18

          ORDERING INFORMATION  . . . . . . . . . . . . . . . . . . . .  19

          ORDER FORM  . . . . . . . . . . . . . . . . . . . . . . . . .  20

          INDEX . . . . . . . . . . . . . . . . . . . . . . . . . . . .  21






          Micept Instruments Inc. - Cross Assemblers (Series II)          1



          1. INTRODUCTION          1. INTRODUCTION

          This  software are shareware distributed versions of high quality
          Macro  Cross Assemblers  which you get  when you  register. These
          versions  however do not support macros, conditional assembly and
          included files like their expanded versions do. This software are
          basic two-pass assemblers for the Motorola 6800, 6803, 6805, 6809
          the Rockwell 6502 and the Rockwell 65C02 microprocessors.

          These powerful cross  assemblers for the MS-DOS  operating system
          support  the  complete instruction  set  and  a complete  set  of
          directives. These assemblers can produce formatted  listing files
          and  object code  in  both the  Intel  Hex and  the  Motorola Hex
          formats.

          The supported assembler directives are  the same as the ones used
          by  the microprocessor manufacturers, but you can customized them
          to your liking using the REDEF directive.


          2. INSTALLATION          2. INSTALLATION

          Make  a working  copy of your  disk, using  the COPY  or DISKCOPY
          utility supplied with MS-DOS. Save the original disk for backup.

          No particular  installation is required  except that you  have to
          copy the executable files you will need to the disk you are going
          to use.


          3. SYSTEM REQUIREMENTS          3. SYSTEM REQUIREMENTS

               - IBM PC/XT/AT or compatible computer
               - DOS 2.0 or later
               - 256K Bytes of RAM required (more for bigger symbol table)


          4. FILES IN THE PACKAGE          4. FILES IN THE PACKAGE

               README#2       The file containing the latest information
               ORDER#2.FRM    The file containing the ready to print
                              registration form
               MCASM#2.DOC    This file !
               MA03.EXE       The executable file of the 6803 Cross
                              Assembler
               MA05.EXE       The executable file of the 6805 Cross
                              Assembler
               MA09.EXE       The executable file of the 6809 Cross
                              Assembler






          Micept Instruments Inc. - Cross Assemblers (Series II)          2



               MA65.EXE       The executable file of the 6502 Cross
                              Assembler
               MA65C.EXE      The executable file of the 65C02 Cross
                              Assembler
               MA68.EXE       The executable file of the 6800 Cross
                              Assembler


          5. FORMAT OF COMMANDS          5. FORMAT OF COMMANDS

          The following rules are used in this manual:

               1.   Words  in  capital  letters are  keywords  and  must be
                    entered as shown. They  may be entered in uppercase  or
                    lowercase characters.

               2.   Items in square brackets ([]) are optional.

               3.   Symbolic fields are enclosed in < >.

               4.   An  ellipsis  (...)  indicates  that  an  item  may  be
                    repeated as many time as you wish.

               5.   All punctuation, except the one  mentioned before, must
                    be included where shown.

               6.   xxx is a two or three character string representing the
                    microprocessor identification.
                    This string is:

                    03  : for the Motorola 6803 microprocessor
                    05  : for the Motorola 6805 microprocessor
                    09  : for the Motorola 6809 microprocessor
                    65  : for the Rockwell 6502 microprocessor
                    65C : for the Rockwell 65C02 microprocessor
                    68  : for the Motorola 6800 microprocessor


          6. COMMAND LINE          6. COMMAND LINE

          6.1 Invocation

               These assemblers can be invoked as follow:

               MAxxx [<options>] <sourcefile> [<objfile> [<listfile>]]

               Where  <options>  can  be  one  or  more  of  the  following
               separated by spaces:






          Micept Instruments Inc. - Cross Assemblers (Series II)          3



               -l : Produce a listing file
               -o : Produce NO object file
               -t : Produce NO symbol table in the listing
               -i : Produce object in Intel Hex
               -q : Quiet mode
               -p<n> : Set listing page length (in lines per page)
               -w<n> : Set listing width (in characters per line)
               -r<n> : Set object record size (in bytes)
               -c : Produce complete object in listing for long constants

               <sourcefile>  : Source file name.  Default extension ".xxx".
               <objfile>     : Object file name.  Default extension ".OBJ".
               <listfile>    : Listing file name. Default extension ".LST".

               If the  assembler is  invoked with an  error in  the command
               line, a help screen is displayed on the console.

               For <objfile> and  <listfile>, if no name is  specified, the
               source file name  with the default  extensions will be  used
               and the files will be created in the current directory.


          6.2 Options in more details

               c -  Complete  object code  in listing  for  long constants.
                    This is used to see  all object codes generated by long
                    constants,  like strings and  series of data.  A source
                    line may  then  generate  more than  one  line  in  the
                    listing because only a few  object codes can be written
                    on one line of listing.

               i -  Intel Hex format. This option causes the object file to
                    be produced  in the  Intel Hex  format rather  than the
                    default Motorola Hex format.

               l -  Listing  file.  This  option enables  the  output  to a
                    listing file. The listing produced has page headers and
                    footers inserted  at appropriate  intervals. Even  when
                    the option is invoked, the  output to the listing  file
                    will be controlled by the LIST and NOLIST directives.

               o -  Object file disabled. This option suppresses the output
                    to an object file.

               p -  Page length. This  option sets the number of  lines per
                    page in  the  listing  file. When  a  listing  file  is
                    produced, since page headers and footers  are inserted,
                    a  page length is required. If this option, immediately
                    followed  by a numeric  constant, is invoked,  the page
                    length will  be set  to that value.  The value  must be






          Micept Instruments Inc. - Cross Assemblers (Series II)          4



                    between 20  and 120  or it will  be ignored.  Even when
                    this  option is  invoked, the  page length  may be  set
                    again anywhere in the file  by the PLEN directive.  The
                    default page length is 66 lines.

               q -  Quiet mode. This  option turns off the  display of line
                    numbers  during  assembly.  Normally  a running  count,
                    incremented  by  50s,  of the  numbers  of  lines being
                    assembled is displayed on the console.

               r -  Record size  in the object  file. This option  sets the
                    number of bytes in each object file  record. The number
                    selected is the number of counted bytes in the selected
                    format. The number must be between 8 and 255 or it will
                    be ignored.  If the m  option is invoked, the  r option
                    must appear  after it in  the command line to  have any
                    effect. The default record size in Intel Hex is 24. The
                    default record size in Motorola Hex is 27.

               t -  Table of symbols  suppressed in the listing  file. This
                    option suppresses the output of the symbol table in the
                    listing file.  Of course if output to  the listing file
                    is disabled at the end of the listing, the symbol table
                    will not appear at the end of the listing file anyway.

               w -  Width of the listing file. This option sets  the number
                    of characters  per line  in the listing  file. If  this
                    option, immediately followed by a numeric constant,  is
                    invoked, the line length will be set to that value. The
                    value must be between 60 and 132 or it will be ignored.
                    Even when  this option is invoked, the  line length may
                    be  set   again  anywhere  in  the  file  by  the  LLEN
                    directive. The default line length is 80 characters.

               Note:     Each option must be preceded  by a dash (-) in the
                         command line, to distinguish it from a file name.


          6.3 Error codes returned to DOS

               Condition                                    Error code
               -------------------------------------------------------
               Normal completion, without errors            0
               Normal completion, with assembly errors      1
               Abnormal completion, insufficient memory     2
               Abnormal completion, file access error       3






          Micept Instruments Inc. - Cross Assemblers (Series II)          5



          6.4 Object code file formats

               Each assembler supports two object file formats:

               1. Intel Hex
               2. Motorola Hex (S1-S9)


          6.5 Environment variable

          Each assembler  environment can  be customized by  the use  of an
          environment  variable. The  variable, if  set,  will specify  the
          default  command  line  options. The  options  specified  in that
          variable will not  replace but be added to the options invoked in
          the command line. Options are specified  in the same manner as if
          they  were invoked  in  the  command line.  The  setting of  this
          variable can be  automatically done if the set  command is placed
          in the AUTOEXEC.BAT file.

          The  variable is called MAxxxOPT and can  be set by the following
          command:

               set MAxxxOPT=-l -i -r10h

          That command would invoked  the l, i and r options  each time the
          assembler is invoked.

          Note: Any error in this environment variable will be ignored.


          7. SOURCE LINE FORMAT          7. SOURCE LINE FORMAT

          Lines in  the  source file  consist  of  up to  four  fields,  as
          follows:

               [Label] [Opcode] [Operand] [Comment]

               Each line of the file may  be up to 256 characters long.  An
               arbitrary  number of  white  space  (spaces  or  tabs)  must
               separate each field.

               Label:

               Labels are  symbols and  follow the same  rules. If  a label
               starts in  the first column,  it must be terminated  with at
               least one white space (space or tab)  or the end of the line
               but it may follow the rules of a label starting in any other
               column. If  a label starts in  any other column, it  must be
               terminated with a colon (:) followed with at least one white






          Micept Instruments Inc. - Cross Assemblers (Series II)          6



               space  (space or  tab) or the  end of  the line.  The ending
               colon is never part of the symbol.

               A  line  may  consist  of  a  label  alone.  With  a  normal
               instruction mnemonic  the assembler  assign a  value to  the
               label equal to the current location counter.


               Opcode:

               The operand field  contains the instruction mnemonic  or the
               assembler directive that is to be performed. This field must
               not start in the first column.


               Operand:

               The operand field  may or may not be  required, depending on
               the  opcode or directive  being assembled. If  present, this
               field will contain a certain number of operand, separated by
               commas. There  must not  be any white  space (space  or tab)
               between these operand.


               Comment:

               The  optional comment field is used for annotation purposes.
               This field is  ignored by the assembler, but  is included in
               the  listing. No  character  is  necessary  to  designate  a
               comment  which  does  not  begin  in  the first  column.  An
               asterisk (*)  may be used  in the first column  to designate
               that the  whole line is a  comment and should be  ignored by
               the assembler.


          8. EXPRESSIONS IN THE OPERAND FIELD          8. EXPRESSIONS IN THE OPERAND FIELD

          Expressions are combinations of constants, symbols, operators and
          parentheses that are evaluated as an integer value.


          8.1 Symbols

               Symbols are strings of characters that contain letters (A-Z,
               a-z), numbers (0-9), points (.) and underscores (_) but they
               must begin with a letter. A symbol may be of any length, but
               only  the first  8 characters  are significant  and will  be
               listed in the symbol table. Since all  lowercase letter will
               be  converted to  uppercase,  symbols which  are capitalized






          Micept Instruments Inc. - Cross Assemblers (Series II)          7



               differently will be the same. A symbol can not be a reserved
               word.

               examples:      LOOP
                              loop_2
                              key.buffer

               The reserved words are the one representing:

                    - the mnemonics and assembler directives.
                    - the microprocessor's registers.


          8.2 Constants

               Numeric constants:

               Numeric constants must  always begin with a  prefix followed
               by  the  number. The  radix  is  determine  by  this  prefix
               according to the following table:

               Format         Prefix
               ---------------------------
               Binary         %
               Octal          @
               Decimal        nothing
               Hexadecimal    $

               examples:      %10010001
                              @7774
                              -18
                              255
                              $6f
                              $FE


               Character constants:

               A  character   constant  consists  of  one  ASCII  character
               surrounded by single quote marks (').

               Note:     To  put a  single  quote  mark  into  a  character
                         constant,  two  consecutive single  quotes  may be
                         used to represent one such character.

               examples:      'a'
                              '*'
                              ''''






          Micept Instruments Inc. - Cross Assemblers (Series II)          8



               The location counter:

               The current value  of the location counter can be used in an
               expression. It is represented by the asterisk (*).


          8.3 Operators

               The  operators  allowed  in expressions  are  shown,  in the
               following table, in descending order of precedence:

               Order  Operator   Type             Description
               ----------------------------------------------------------
               1.     ()         expression       parentheses
               2.     -          unary            unary negative
                      ~                           one's complement
               3.     &          binary           bitwise AND
                      !                           bitwise OR
                      ^                           bitwise EXCLUSIVE OR
               4.     *          multiplicative   multiplication
                      /                           division
                      %                           remainder
               5.     +          additive         addition
                      -                           subtraction
               6.     <<         shift            shift left
                      >>                          shift right
               7.     =          relational       equal
                      <                           less than
                      >                           greater than
                      <=                          less than or equal
                      >=                          greater than or equal


          8.4 How expressions are evaluated

               In  an expression  parenthetical  expressions are  evaluated
               first,  the  innermost parentheses  before  the outer  ones.
               Next, operations  involving higher precedence  operators are
               done first. Where several operators have the same precedence
               they  are  evaluated from  left  to right  except  for unary
               operators  which are  evaluated  from  right  to  left.  All
               intermediate values are truncated to a 16-bit integer value.
               The result of the expression is also a 16-bit integer value.






          Micept Instruments Inc. - Cross Assemblers (Series II)          9



          9. ASSEMBLER DIRECTIVES          9. ASSEMBLER DIRECTIVES

               ----------------------------------------------------------
               Assembly Control
                    ORG          Set assembly origin
                    END          End of source
                    REDEF        Redefine an assembler directive
               ----------------------------------------------------------
               Symbol Definition
                    EQU          Equate symbol value
                    SET          Set symbol value (temporary)
               ----------------------------------------------------------
               Memory Allocation
                    DB           Define constant byte(s)
                    DW           Define constant word(s)
                    RSB          Reserve storage for byte(s)
                    RSW          Reserve storage for word(s)
               ----------------------------------------------------------
               Listing Control
                    TITLE        Set title of page(s)
                    LLEN         Set line length (characters per line)
                    PLEN         Set page length (lines per page)
                    PAGE         Advance to top of next page
                    LIST         List the assembly
                    NOLIST       Do not list the assembly
                    ACLIST       List all object codes for long constants
                    NOACLIST     Do not list all object codes
               ----------------------------------------------------------

          Note:     Some of  these directives  have a  different name  with
                    each microprocessor, so consult the  special section on
                    the microprocessor you are using.


               ACLIST

               Purpose:  This  directive  restores   the  listing  of   the
                         complete object code for long constants.

               Format:   ACLIST


               DB

               Purpose:  This  directive allocates  and initializes  one or
                         more bytes.

               Format:   [<label>] DB <expression>[,<expression>...]






          Micept Instruments Inc. - Cross Assemblers (Series II)         10



               Remarks:  <expression> must be  an 8-bit integer value  or a
                         string surrounded by single quote marks (').


               DW

               Purpose:  This directive  allocates and  initializes one  or
                         more words.

               Format:   [<label>] DW <expression>[,<expression>...]

               Remarks:  <expression> must be a 16-bit integer value.


               END

               Purpose:  This directive designates  the end  of the  source
                         file.

               Format:   END

               Remarks:  No line in the source file will be read after this
                         directive.


               EQU

               Purpose:  This directive assigns  the value of  <expression>
                         to <label>.

               Format:   <label> EQU <expression>

               Remarks:  The <label> entry can not be redefined.


               LIST

               Purpose:  This directive restores the output in the listing.

               Format:   LIST

               Remarks:  If a  listing is  not being  made, this  directive
                         will start one.


               LLEN

               Purpose:  This directive  sets the number of  characters per
                         line,   in   the   listing,   to   the   value  of
                         <expression>.






          Micept Instruments Inc. - Cross Assemblers (Series II)         11



               Format:   LLEN <expression>

               Remarks:  The  number of characters per line must be between
                         60 and 132. The default is 80 characters per line.


               NOACLIST

               Purpose:  This  directive  suppresses  the  listing  of  the
                         complete object code for long constants.

               Format:   NOACLIST


               NOLIST

               Purpose:  This  directive  suppresses  the  output  in   the
                         listing.

               Format:   NOLIST


               ORG

               Purpose:  This directive  sets the  location counter to  the
                         value of <expression>.

               Format:   ORG <expression>

               Remarks:  <expression>   must  not   involved  any   forward
                         references.


               PAGE

               Purpose:  This directive starts a new page in the listing. 

               Format:   PAGE


               PLEN

               Purpose:  This  directive sets the number of lines per page,
                         in the listing, to the value of <expression>.

               Format:   PLEN <expression>

               Remarks:  The  number of lines  per page must  be between 20
                         and  120. The default  is 66 characters  per line.
                         The first  and the  last 3 lines  of the  page are






          Micept Instruments Inc. - Cross Assemblers (Series II)         12



                         left blank. The fourth and fifth line are used for
                         the date, page number and page title.


               REDEF

               Purpose:  This directive redefines the <directive> assembler
                         directive to the <directive2> directive.

               Format:   REDEF <directive>,<directive2>

               Remarks:  This  allows you to  change the  name of  each and
                         every directive to satisfy  your particular source
                         file needs. You  can also use it to  make your own
                         set of universal directives.


               RSB

               Purpose:  This directive  reserves a  block of  <expression>
                         byte(s) for storage.

               Format:   [<label>] RSB <expression>

               Remarks:  The number of bytes reserved must be between 1 and
                         32767.


               RSW

               Purpose:  This directive  reserves a  block of  <expression>
                         word(s) for storage.

               Format:   [<label>] RSW <expression>

               Remarks:  The number of words reserved must be between 1 and
                         16383.


               SET

               Purpose:  This directive  assigns the value  of <expression>
                         to <label>.

               Format:   <label> SET <expression>

               Remarks:  The <label> entry can be redefined.






          Micept Instruments Inc. - Cross Assemblers (Series II)         13



               SETDP

               Purpose:  This directive indicates  that the DP register  of
                         the  Motorola 6809 is suppose to contain the value
                         <expression>.

               Format:   SETDP <expression>

               Remarks:  This  directive  only applies  to  the 6809  Cross
                         Assembler. It is  used to determine if  the direct
                         addressing mode can be used or not.


               TITLE

               Purpose:  This directive sets  the title of the  current and
                         following page(s) to the <text> string.

               Format:   TITLE <text>

               Remarks:  <text> is truncated to the first 60 characters.






          Micept Instruments Inc. - Cross Assemblers (Series II)         14



          10. SPECIAL SECTION ON THE MICROPROCESSORS          10. SPECIAL SECTION ON THE MICROPROCESSORS

          10.1 Motorola 6800

               The reserved word in this assembler is:
               X


               Assembler directives:

               For this  microprocessor, the standard  assembler directives
               have been predefined as following:
               EQU
               ORG
               END
               FCB    instead of DB
               FDB    instead of DW
               FCC    a second definition of DB
               SET
               RMB    instead of RSB
               RSW    is not supported, because it is not necessary


          10.2 Motorola 6803

               The reserved word in this assembler is:
               X


               Assembler directives:

               For this  microprocessor, the standard  assembler directives
               have been predefined as following:
               EQU
               ORG
               END
               FCB    instead of DB
               FDB    instead of DW
               FCC    a second definition of DB
               SET
               RMB    instead of RSB
               RSW    is not supported, because it is not necessary






          Micept Instruments Inc. - Cross Assemblers (Series II)         15



          10.3 Motorola 6805

               The reserved word in this assembler is:
               X


               Assembler directives:

               For this  microprocessor, the standard  assembler directives
               have been predefined as following:
               EQU
               ORG
               END
               FCB    instead of DB
               FDB    instead of DW
               FCC    a second definition of DB
               SET
               RMB    instead of RSB
               RSW    is not supported, because it is not necessary


          10.4 Motorola 6809

               The reserved word in this assembler is:
               A, B, CC, D, DP, PC, S, U, X, Y


               Assembler directives:

               For this  microprocessor, the standard  assembler directives
               have been predefined as following:
               EQU
               ORG
               END
               FCB    instead of DB
               FDB    instead of DW
               FCC    a second definition of DB
               SET
               RMB    instead of RSB
               RSW    is not supported, because it is not necessary
               SETDP  (special and reserved to the 6809)


               Note:  If the  operand is preceded  by a  '<' character,  it
                      forces direct addressing.






          Micept Instruments Inc. - Cross Assemblers (Series II)         16



          10.5 Rockwell 6502

               The reserved word in this assembler is:
               A, X, Y, P, PC, SP


               Assembler directives:

               For this  microprocessor, the standard  assembler directives
               have been predefined as following:
               EQU
               ORG
               END
               BYTE      instead of DB
               WORD      instead of DW
               SET
               RESERVE   instead of RSB
               RSW       is not supported, because it is not necessary


          10.6 Rockwell 65C02

               The reserved word in this assembler is:
               A, X, Y, P, PC, SP


               Assembler directives:

               For this  microprocessor, the standard  assembler directives
               have been predefined as following:
               EQU
               ORG
               END
               BYTE      instead of DB
               WORD      instead of DW
               SET
               RESERVE   instead of RSB
               RSW       is not supported, because it is not necessary


          11. BUG REPORTING PROCEDURE          11. BUG REPORTING PROCEDURE

          Although each software is extensively tested prior to release, no
          software is  perfect  and may  contain  a  few bugs.  It  is  the
          intention  of  Micept  Instruments Inc.  to  correct  any genuine
          problem  that will  be considered  as a  problem by  the company,
          although  this  is  not  a  warranty that  any  problem  will  be
          corrected.






          Micept Instruments Inc. - Cross Assemblers (Series II)         17



          If you have any comments or suggestions, please send them  to the
          following address or mail them to us on CompuServe.

          If you think you  have found a bug in this  software, please take
          the time to report it. Any report will be helpful, but you should
          follow these directions:

               1.   Provide the name and version of the software.

               2.   Provide  a brief description of the problem and provide
                    a copy  or listing of  the problem source  file. Please
                    try to isolate the problem  area in the source and only
                    provide that part of the source file.
               3.   Send it to:  Micept Instruments Inc.  CIS:[72130,2513]
                                 377 Julien St.
                                 Cap De La Madeleine, PQ
                                 Canada  G8T 6W6


          12. UPDATE POLICY          12. UPDATE POLICY

          Micept Instruments  Inc. will  not  notify users  of new  version
          releases as improvements are made constantly. If registered users
          would  like to  keep  current  they may  send  us their  original
          distribution disk (the  one with  our label)  along with  payment
          (see order form) to receive the most current version.

          13. REGISTRATION          13. REGISTRATION

          The  registration fee, for  each Macro  Cross Assembler  (one per
          microprocessor) will  licence one  copy of  the expanded  version
          that you  will receive, for  use on any  one computer at  any one
          time. The printed manual is optional but recommended and includes
          a special section on each of the microprocessors of the series.

          Do not  be misled  by the very  low prices  of these  Macro Cross
          Assemblers. They are of very high quality, fast and reliable. The
          only reason why we can offer them to  you at such a low price, is
          because of the distribution method we have chosen, shareware.

          Site registrations  are available  (see ordering  information and
          order form).






          Micept Instruments Inc. - Cross Assemblers (Series II)         18



                            APPENDIX A - EXPANDED VERSION                            APPENDIX A - EXPANDED VERSION


          Registered users get this expanded version of the software.
          The version supports:

               - up to 16 nested included files
               - up to 16 nested conditional assembly
               - up to 16 nested macros
               - unlimited number of include files
               - unlimited number of macros (limited by memory)


          The expanded directive set includes the following:

          ----------------------------------------------------------
          Conditional Assembly
               IF        Assemble if not equal to zero
               IFN       Assemble if equal to zero
               IFC       Assemble if string1 equals string2
               IFNC      Assemble if string1 not equal to string2
               ELSE      Reverse condition
               ENDIF     End of conditional assembly
               FAIL      Print error message
          ----------------------------------------------------------
          Include files
               INCLUDE   Include file
          ----------------------------------------------------------
          Macro Directives
               MACRO     Define a macro
               ENDM      End of macro definition
               EXITM     Skip to the end of a macro definition
          ----------------------------------------------------------
          Listing Control
               FLIST     List false conditions
               FNOLIST   Do not list false conditions
               EXPAND    Expand macros
               NOEXPAND  Do not expand macros
          ---------------------------------------------------------- 






                                 ORDERING INFORMATION                                 ORDERING INFORMATION

          Cat.      Description                                  License
          No.                                                    Fee
          ==============================================================

                    Series I
                    --------------------------------------------
          MA44      Macro Cross Assembler for the Intel 8044      $10.00
          MA48      Macro Cross Assembler for the Intel 8048      $10.00
          MA51      Macro Cross Assembler for the Intel 8051/52   $10.00
          MA80      Macro Cross Assembler for the Intel 8080      $10.00
          MA85      Macro Cross Assembler for the Intel 8085      $10.00
          MA96      Macro Cross Assembler for the Intel 8096      $10.00
          MAZ80     Macro Cross Assembler for the Zilog Z80       $10.00

          SERIES-I  Complete series containing the Macro          $49.00
                    Cross Assemblers for the Intel 8044,
                    8048, 8051/52, 8080, 8085, 8096 and
                    the Zilog Z80 (manual not included)

          MANUAL-I  Manual for the Macro Cross Assemblers of      $20.00
                    the series I and containing a special
                    section for each of the microprocessors


                    Series II
                    --------------------------------------------
          MA03      Macro Cross Assembler for the Motorola 6803   $10.00
          MA05      Macro Cross Assembler for the Motorola 6805   $10.00
          MA09      Macro Cross Assembler for the Motorola 6809   $10.00
          MA65      Macro Cross Assembler for the Rockwell 6502   $10.00
          MA65C     Macro Cross Assembler for the Rockwell 65C02  $10.00
          MA68      Macro Cross Assembler for the Motorola 6800   $10.00

          SERIES-II Complete series containing the Macro          $49.00
                    Cross Assemblers for the Motorola 6800,
                    6803, 6805, 6809, and the Rockwell 6502
                    and 65C02 (manual not included)

          MANUAL-II Manual for the Macro Cross Assemblers of      $20.00
                    the series II and containing a special
                    section for each of the microprocessors


                    Complete package
                    --------------------------------------------
          MICRO-8   Package containing all the Macro Cross       $119.00
                    Assemblers of the series I and series II
                    (both manuals included)

          -----------------------------------------------------------------
          Note:     The manual is optional but recommended. Only one manual
                    is required by series.






                                      ORDER FORM                                      ORDER FORM
                                                              #92-MC220-001

          Qty  Cat. No.  Description              Unit Price     Price
          ---  --------  -----------------------  ----------     ----------

          ___  ________  _______________________  $_____.___     $_____.___

          ___  ________  _______________________  $_____.___     $_____.___

          ___  ________  _______________________  $_____.___     $_____.___

          ___  ________  _______________________  $_____.___     $_____.___

          ___  ________  _______________________  $_____.___     $_____.___

          ___  ________  _______________________  $_____.___     $_____.___

          ___  ________  _______________________  $_____.___     $_____.___

          ___  ________  _______________________  $_____.___     $_____.___

                                                       Subtotal  $_____.___

                         Add $6.00  Shipping + handling          $_____.___
                         (outside North America Add $10.00)
                                                       Subtotal  $_____.___

                                 Canada residents Add GST        $_____.___

                                                       Subtotal  $_____.___

                    Quebec residents Add Provincial Sales Tax    $_____.___

                                             Total  U.S. dollars $_____.___

               Payments in Canadian Dollars: Total  Can. dollars $_____.___

               Exchange rate ______

          Send your check or money order to:      Micept Instruments Inc.
                                                  377 Julien St.
          Specify disk format:                    Cap De La Madeleine, PQ
          ___ 5 1/4 or ___ 3 1/2                  Canada  G8T 6W6

          Name:     _______________________________________
          Company:  _______________________________________
          Address:  _______________________________________
                    _______________________________________

          *    Prices are in U.S. dollars. We accept only U.S. and Canadian
               funds.  All other will  be refused. Prices  and availability
               are subject to change without notice. 






                                        INDEX                                        INDEX


          ACLIST  . . . . . . . . . .  9     LLEN  . . . . . . . . . . . 10
          Assembler directives  . . .  9     Location counter  . . . . .  8
          Binary  . . . . . . . . . .  7     Manual  . . . . . . . . . .  2
          Bug reporting procedure . . 16     Microprocessors . . . . . . 14
          Character constants . . . .  7          Motorola 6800  . . . . 14
          Characters per line . . . .  4          Motorola 6803  . . . . 14
          Codes returned to DOS . . .  4          Motorola 6805  . . . . 15
          Command line  . . . . . . .  2          Motorola 6809  . . . . 15
          Comment . . . . . . . . . .  6          Rockwell 6502  . . . . 16
          Constants . . . . . . . . .  7          Rockwell 65C02 . . . . 16
          Copyright information . . .  i     Motorola 6800 . . . . . . . 14
          DB  . . . . . . . . . . . .  9     Motorola 6803 . . . . . . . 14
          Decimal . . . . . . . . . .  7     Motorola 6805 . . . . . . . 15
          Default options . . . . . .  5     Motorola 6809 . . . . . . . 15
          Directives  . . . . . . . .  9     Motorola Hex  . . . . . . .  5
               ACLIST . . . . . . . .  9     NOACLIST  . . . . . . . . . 11
               DB . . . . . . . . . .  9     NOLIST  . . . . . . . . . . 11
               DW . . . . . . . . . . 10     Numeric constants . . . . .  7
               END  . . . . . . . . . 10     Object
               EQU  . . . . . . . . . 10          code . . . . . . . . .  3
               LIST . . . . . . . . . 10          code format  . . . . .  5
               LLEN . . . . . . . . . 10          file . . . . . . . . .  3
               NOACLIST . . . . . . . 11          file record size . . .  4
               NOLIST . . . . . . . . 11     Octal . . . . . . . . . . .  7
               ORG  . . . . . . . . . 11     Opcode  . . . . . . . . . .  6
               PAGE . . . . . . . . . 11     Operand . . . . . . . . . .  6
               PLEN . . . . . . . . . 11     Operators . . . . . . . . .  8
               REDEF  . . . . . . . . 12     Options . . . . . . . . . .  3
               RSB  . . . . . . . . . 12     Order form  . . . . . . . . 20
               RSW  . . . . . . . . . 12     Ordering information  . . . 19
               SET  . . . . . . . . . 12     ORG . . . . . . . . . . . . 11
               SETDP  . . . . . . . . 13     PAGE  . . . . . . . . . . . 11
               TITLE  . . . . . . . . 13     Page length . . . . . . . .  3
          Disclaimer  . . . . . . . .  i     PLEN  . . . . . . . . . . . 11
          DW  . . . . . . . . . . . . 10     Quiet mode  . . . . . . . .  4
          END . . . . . . . . . . . . 10     Record size . . . . . . . .  4
          Environment variable  . . .  5     REDEF . . . . . . . . . . . 12
          EQU . . . . . . . . . . . . 10     Registration  . . . . . . . 17
          Expanded version  . . . . . 18     Reserved words  . . . . . .  7
          Expressions . . . . . . . 6, 8     Rockwell 6502 . . . . . . . 16
          Files . . . . . . . . . . .  1     Rockwell 65C02  . . . . . . 16
          Hexadecimal . . . . . . . .  7     RSB . . . . . . . . . . . . 12
          Index . . . . . . . . . . . 21     RSW . . . . . . . . . . . . 12
          Installation  . . . . . . .  1     SET . . . . . . . . . . . . 12
          Intel Hex . . . . . . . . 3, 5     SETDP . . . . . . . . . . . 13
          Introduction  . . . . . . .  1     Site registration . . . . . 17
          Invocation  . . . . . . . .  2     Source line . . . . . . . .  5
          Label . . . . . . . . . . .  5     Special sections  . . . . . 14
          Lines per page  . . . . . .  3     Symbol table  . . . . . . .  4
          LIST  . . . . . . . . . . . 10     Symbols . . . . . . . . . .  6
          Listing file  . . . . . . 3, 4     System requirements . . . .  1






          Micept Instruments Inc. - Cross Assemblers (Series II)         22



          Table of contents . . . . . ii
          TITLE . . . . . . . . . . . 13
          Update policy . . . . . . . 17