.FQ

l-@10i--TL----+-T--2----T----3--T-+----4T---+---T5----+-T--6----T----C--T-+----r










         
         
         
         
                                    FossComm
         
                                  version 0.04
         

                                  August 22, 1988

         
                             Program Documentation





                     Copyright (C) 1988  Daan van der Weide
                              All rights reserved


l-@10i--TL----+-T--2----T----3--T-+----4T---+---T5----+-T--6----T----J--T-+----r
         
.N:2
         
.F:------------------------------------------------------------
         
.F:FossComm...page $$$...FossComm
         
.F:
         


           FosComm ÿis ÿan interface between a compiled BASIC ÿprogram 
         and a so-called FOSSIL ÿdriver. ÿIt enables the ÿuser to take 
         advantage ÿof ÿall the functions regarding the ÿcommunication 
         ports, ÿfrom ÿa BASIC program. ÿIn this way it is possible to 
         avoid ÿthe problems/shortcomings of the ÿBASIC communications 
         handler. 

           FossComm ÿis based on the document 'Fundamentals of ÿFOSSIL 
         implementation and use, ÿdraft version 5, February 11, ÿ1988' 
         by Rick Moor. ÿPlease make sure that your fossil driver meets 
         this draft. 
         
         
           FossComm can be used with any of the following compilers :

                MicroSoft Quickbasic 1.00, 2.00, 3.00 and 4.00, 6.00
                IBM BasCom           1.00, 2.00

         
         LICENSE AND REGISTRATION
         ------------------------

           FossComm is distributed as a 'shareware' ÿprogram. ÿÿPlease 
         help ÿme get it known by giving away unmodified copies of the 
         program and documentation to other people, ÿeither by copying 
         the ÿdisk ÿor ÿmaking it available for downloading on ÿa ÿBBS 
         system. 

           FossComm is copyright (C) 1988 by Daan van der Weide. It is 
         not public domain or free software. ÿNon-registered users are 
         granted ÿa limited license to use FossComm on a ÿtrial ÿbasis 
         for ÿdetermining ÿwhether ÿor not it is ÿsuitable ÿfor ÿtheir 
         needs. ÿÿRegistration allows the use of FossComm in ÿprograms 
         for sale and/or distribution. 
         
           The registration fee is 50 guilders (25 US$). Users who pay 
         the ÿregistration ÿfee ÿwill be sent a disk woth ÿthe ÿlatest 
         version and documentation ans some example programs. 

           It ÿis ÿalso ÿpossible ÿto ÿobtain ÿthe ÿsource ÿcodes ÿfor 
         FossComm. ÿIn that case the registration fee is 100 ÿguilders 
         (50 US$). 
         
           Register your usage of FossComm by sending the registration 
         fee to :

                        Daan van der Weide
                        Kastelenstraat 229-3
                        1082 EG  Amsterdam
                        the Netherlands

                        telephone : (0)20 463647

           Your ÿÿcomments ÿregarding ÿthe ÿFossComm ÿprogram ÿor ÿany 
         suggestions ÿyou ÿhave for extensions or for ÿother ÿprograms 
         that would be useful to you are welcome. 


           Daan van der Weide makes no warranties whatsoever regarding 
         the FossComm computer program or the documentation. 
         

         USING FOSSCOMM IN YOUR PROGRAMS
         -------------------------------

           The ÿFossComm ÿmodule contains a number of ÿfunctions ÿthat 
         handle the access of RS232 ÿcommunication boards as ÿprovided 
         by a driver conform the FOSSIL standard. 

           Below follows a list of the functions supported and the 
         parameters that should be specified, as well as the eventual 
         return values. To incorporate the module within your compiled 
         program specify the name FOSSCOMM.OBJ when linking your 
         program. Example : 
         
           LINK MYPROG+FOSSCOMM,MYPROG;

         
         CREDITS
         -------

           I would like to mention a few people who have supported and 
         still are supporting the development :

           Ronald Koridon who adapted RBBS 16.1a to run using FossComm 
         and who is my primary 'guinea-pig'; Arjen Lentz, John Janssen 
         sysops ÿthat are using the RBBS 16.1a FOSSIL version as well. 
         the RBBS version as well to run. (they've probably upgraded 
         by now ...)


         FEEDBACK
         --------

           As you may know, any software developer depends on his 
         users to modify, adjust and extend his product. Therefore 
         I'm very interested in all comments, notes and critics 
         towards the FossComm product. I can be reached either by 
         telephone or, better, at the RBBS system listed below. Thank 
         you very much !

                              RBBS Gaasperdam (4 lines)
                              sysop Ronald Koridon
                              Amsterdam, the Netherlands

                              31  (0)20 978493  node 1
                                        913890  node 2
                                        974420  node 3
                                        972763  node 4

         

         Revision history
         ----------------

         v0.01

                This is the first alpha-test version only released to
         people involved in testing.

         
         v0.02

                Extended FOSSIL calls implemented to access keyboard 
         and to do video I/O etc. Not released.

         
         v0.03

                Adaptions ÿaccording ÿto draft 5 are ÿmade. ÿÿFOSSPEED 
         changed, so that parity, ÿdatabits and the number of stopbits 
         may be specified as well. ÿThe documentation is extended, and 
         a number of functions was added. 

         v0.04
         
                I ÿthink ÿthe ÿproduct is solid enough to ÿrelease ÿit 
         generally, especially because there's 'official' RBBS support 
         for FossComm. ÿA ÿnumber of BBS systems are running for a few 
         months now without any problems. 
         
         

         -------------------------------------------------------------
         FOSINIT
         -------------------------------------------------------------
         
         PURPOSE :
         
           Initializes ÿthe ÿFOSSIL ÿdriver, ÿand checks ÿwhether ÿthe 
         FOSSIL driver ÿis installed. ÿThis function should be ÿcalled 
         before any other FOS calls are made. DTR is raised by this 
         call. The baudrate is NOT set by this call.
         
         
         FORMAT  :
         
           FOSINIT(port%, result%)

         
         RETURNS :
         
           0    no error, driver initialized
          -1    error initializing driver

         
         EXAMPLE :

           100 PORT% = 1
           110 CALL FOSINIT(PORT%,RESULT%)
           120 IF RESULT% = -1 THEN PRINT "ERROR INITIALIZING FOSSIL"
         
         
         REMARKS :
         
           The ÿnumber of the comport that may be initialized ÿdepends 
         on ÿthe particular FOSSIL driver you're using. ÿRefer to ÿthe 
         documentations of your driver for the values. 

           Should ÿa second call to this function occur, ÿall buffers, 
         flow-contol parameters etc. ÿare reset to their initial state 
         and no error is returned. 
         
         
         -------------------------------------------------------------
         FOSEXIT
         -------------------------------------------------------------
         
         PURPOSE :

           This ÿfunction should be called whenever the communications 
         port ÿin ÿno longer needed. ÿNo FOS calls to ÿthe ÿparticular 
         comport can be made anymore once this call has been made. DTR 
         is not affected by this call. 


         FORMAT  :

           FOSEXIT(COMPORT%)

         

         -------------------------------------------------------------
         FOSSPEED
         -------------------------------------------------------------
         
         PURPOSE :

           Sets ÿÿthe ÿÿbaudrate ÿand ÿthe ÿadditional ÿline ÿÿcontrol 
         parameters ÿfor ÿthe communication port. ÿIf a ÿnon-supported 
         baudrate ÿis specified, ÿthe baudrate variable is set to ÿ-1, 
         and no call to the FOSSIL drive is made. 


         FORMAT  :

           FOSSPEED(comport%, speed%, parity%, databits%, stopbits%)

           where speed% can be one of the following :

           300,600,1200,2400,4800,9600,19200,38400

           parity% can be :

           0  for    no parity
           1  for   odd parity
           2  for    no parity
           3  for  even parity

           databits% can be :

           0  for     5 databits
           1  for     6 databits
           2  for     7 databits
           3  for     8 databits

           stopbits% can be :

           0  for     1 stopbit
           1  for    1« stopbit if databits% = 0 i.e. 5 bits or
                      2 stopbits for all other values for databits%.
         
         
         RETURNS :

           speed% ÿis set to -1 ÿif an illegal baudrate was specified, 
         otherwise speed% is not affected. 

         

         -------------------------------------------------------------
         FOSTXCHAR
         -------------------------------------------------------------
         
         PURPOSE :

           Transmits a character using the specified port. ÿIf there's 
         room ÿin the transmit buffer, ÿthe return will be ÿimmediate, 
         otherwise ÿit ÿwill ÿwait until there is room ÿto ÿstore ÿthe 
         character in the transmit buffer. 


         FORMAT  :

           FOSTXCHAR(comport%, char%, result%)


         REMARKS :

           For the values of the result% ÿparameter, ÿplease refer ÿto 
         the description of the FOSSTATUS function.

         
         -------------------------------------------------------------
         FOSRXCHAR
         -------------------------------------------------------------
         
         PURPOSE :

           If there's a character available in the receive buffer, the 
         character ÿwill be returned. ÿWhen no character is available, 
         it will wait until one becomes available. 
         
         
         FORMAT  :

           FOSRXCHAR(comport%, char%, result%)


         REMARKS :

           For the values of the result% ÿparameter, ÿplease refer ÿto 
         the description of the FOSSTATUS function. 

         

         -------------------------------------------------------------
         FOSSTATUS
         -------------------------------------------------------------
         
         PURPOSE :

           Requests status information about the state of the comport.


         FORMAT  :

           FOSSTATUS(comport%, status%)

           status bits returned are :

           15 14 13 12 11 10 09 08 07 06 05 04 03 02 01 00      mask
           -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
              XX XX          XX XX XX          XX
               |  |           |  |  |           |
               |  |           |  |  |           |
               |  |           |  |  |           + bit is always set
               |  |           |  |  |
               |  |           |  |  +----- Carrier Detect       &H0080
               |  |           |  |
               |  |           |  +-------- Input data available &H0100
               |  |           |
               |  |           +----------- RX buffer overrun    &H0200
               |  |
               |  +----------------------- Room available       &H2000
               |
               +-------------------------- Output buffer empty  &H4000
         
         
         -------------------------------------------------------------
         FOSDTR
         -------------------------------------------------------------
         
         PURPOSE :

           Raises or lowers the DTR signal on the specified comport.


         FORMAT  :

           FOSDTR(comport%, state%)

           state% can be :

           0  to indicate that DTR should be lowered
           1  to indicate that DTR should be raised
         
         

         -------------------------------------------------------------
         FOSTXFLUSH
         -------------------------------------------------------------
         
         PURPOSE :

           Forces ÿthe ÿtransmission of all characters that ÿcurrently 
         are in the transmit buffer. ÿThe ÿfunction ÿdoes ÿnot ÿreturn ÿ
         until all characters are transmitted !!! 


         FORMAT  :

           FOSTXFLUSH(comport%)

         
         -------------------------------------------------------------
         FOSTXPURGE
         -------------------------------------------------------------
         
         PURPOSE :

           This function purges all pending characters in the transmit 
         buffer. Any characters not transmitted are discarded. 


         FORMAT  :

           FOSTXPURGE(comport%)

         
         -------------------------------------------------------------
         FOSRXPURGE
         -------------------------------------------------------------
         
         PURPOSE :

           Purges the ÿreceive buffer. ÿAny input data in ÿthe receive 
         buffer is discarded. 


         FORMAT  :

           FOSRXPURGE(comport%)

         

         -------------------------------------------------------------
         FOSTXCHARNW
         -------------------------------------------------------------
         
         PURPOSE :
        
           This function is similar to the FOSTXCHAR function, ÿexcept 
         that ÿif ÿthe ÿdriver ÿis unable to buffer ÿthe ÿcharacter ÿ- 
         because ÿthe ÿtransmit ÿbuffer ÿis full - ÿthe ÿcall ÿreturns 
         immediately indicating the success of the call in the result% 
         parameter. 


         FORMAT  :

           FOSTXCHARNW(comport%, char%, result%)

           result% can be :

           0  if the character could *NOT* be transmitted
           1  if the character was transmitted

         
         -------------------------------------------------------------
         FOSREADAHEAD
         -------------------------------------------------------------
         
         PURPOSE :

           Peeks ÿinto ÿthe receive buffer and returns ÿthe ÿcharacter 
         that ÿwill ÿbe ÿreturned upon the next ÿFOSRXCHAR ÿcall, ÿÿor 
         returns -1 if the receive buffer is empty. 


         FORMAT  :

           FOSREADAHEAD(comport%, char%)

           char% is -1  if the receive buffer is empty
         
         

         -------------------------------------------------------------
         FOSFLOWCTL
         -------------------------------------------------------------
         
         PURPOSE :

           Enables or disables the flow control on the transmission. 
         Two kinds of flow control are supported :

           15 14 13 12 11 10 09 08 07 06 05 04 03 02 01 00
           -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
                                   XX XX XX XX XX XX XX XX
                                   FORCED HIGH  |  |  |  |
                                                |  |  |  |
                                                |  |  |  +-- Xon/Xoff
                                                |  |  |      on
                                                |  |  |      transmit
                                                |  |  |
                                                |  |  +----- CTS/RTS
                                                |  |
                                                |  +-------- DSR/DTR
                                                |
                                                +----------- Xon/Xoff
                                                             on
                                                             receive
         
           When ÿthe ÿcorresponding ÿbit is set, ÿthat ÿtype ÿof ÿflow 
         control ÿis enabled. ÿApplications should set the upper ÿfour 
         bits in the lower nibble as well, i.e. bits 4, 5, 6 and 7. 
         
           When ÿthe ÿbit is cleared, ÿthat type of ÿflow ÿcontrol ÿis 
         disabled. 

           Enabling Xon/Xoff on transmission will suspend transmission 
         upon ÿreceiving ÿan Xoff character. ÿThe FOSSIL ÿdrives ÿwill 
         resume transmission as soon as an Xon character is received. 

           Enabling ÿCTS/RTS, ÿwill suspend transmission when ÿCTS ÿis 
         lowered. ÿAs soon as CTS is raised, ÿtransmission is resumed. 
         The ÿFOSSIL driver will drop RTS whenever a certain amount of 
         the ÿreceive buffer is filled. ÿAs soon as the receive buffer 
         contains ÿless characters than the predetermined ÿpercentage, 
         RTS is raised again. 

           Enabling ÿDSR/DTR, ÿÿwill suspend transmission when DSR ÿis 
         lowered. ÿAs soon as DSR is raised, ÿtransmission is resumed. 
         The FOSSIL driver will drop DTR whenever a certain amount ÿof 
         the receive buffer is filled. ÿAs soon as the receive ÿbuffer 
         contains ÿless characters than the predetermined ÿpercentage, 
         RTS is raised again. 
         
           Enabling Xon/Xoff on receive, ÿwill cause the FOSSIL driver 
         to ÿsend an Xoff character whenever a certain amount ÿof ÿthe 
         receive buffer is filled. ÿAn Xon character will be sent, ÿas 
         soon ÿas the receive buffer contains less characters than the 
         predetermined percentage. 

         

         FORMAT  :

           FOSFLOWCTL(comport%, state%)

         
         EXAMPLES :
         
           state% is :
         
           &H00F0 to disable all flow control types
           &H00F1 to enable Xon/Xoff on transmission
           &H00F2 to enable CTS/RTS
           &H00F4 to enable DSR/DTR
           &H00F8 to enable Xon/Xoff on reception
         
         
         -------------------------------------------------------------
         FOSCTRLCK
         -------------------------------------------------------------
         
         PURPOSE :

           Enables/disables extended Ctrl-C/Ctrl-K ÿchecking, ÿÿand/or 
         enables/disables the transmitter. 


           15 14 13 12 11 10 09 08 07 06 05 04 03 02 01 00
           -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
                                                     XX XX
                                                      |  |
                                                      |  +--- CtrlCK
                                                      |  
                                                      +------ TX
         
           Bit ÿ0 controls whether the extended Ctrl-K/Ctrl-C checking 
         is ÿenabled ÿ(bit ÿset) ÿor disabled (bit not ÿset). ÿÿBit ÿ1 
         controls ÿwhether ÿthe transmitter is active or not, ÿin ÿthe 
         same way Xon/Xoff characters do affect the transmitter.

           If the extended Ctrl-C/Ctrl-K checking is enabled, any 
         subsequent call to this this routine will return an internal 
         flag maintained by the FOSSIL driver, that indicates whether 
         Ctrl-C/Ctrl-K has been pressed. When enabled, the Ctrl-
         C/Ctrl-K character does *NOT* appear in the receive buffer.

         
         FORMAT  :

           FOSCTRLCK(comport%, state%)
         
         
         EXAMPLES :
         
           COMPORT% = 1
           STATE% = &H0001
           FOSCTRLCK(COMPORT%, STATE%)
           IF STATE% AND &H0001 THEN PRINT "CTRL-C/CTRL-K RECEIVED"
         
         

         -------------------------------------------------------------
         FOSWDOG
         -------------------------------------------------------------
         
         PURPOSE :
         
           Enables or disables 'watchdog' processing. When watchdog is 
         enabled, ÿthe state of the carrier detect (DCD) ÿline on ÿthe 
         particular comport is constantly monitored, ÿand whenever the 
         signal drops, i.e. the connection is terminated the system is 
         rebooted. ÿThis option is typically used in combination ÿwith 
         external ÿÿprograms ÿshelled ÿfrom ÿa ÿmain ÿÿprogram. ÿÿÿThe 
         FOSINIT/FOSEXIT calls do *NOT* affect this monitoring. 

         FORMAT  :

           FOSWDOG(comport%, state%)

           state% = 1 to enable the watchdog process
           state% = 0 to disable the watchdog process

         
         -------------------------------------------------------------
         FOSBOOT
         -------------------------------------------------------------
         
         PURPOSE :
         
           Boots ÿthe ÿsystem. ÿÿThis function enables ÿa ÿprogram ÿto 
         perform either a soft- or a warmboot. 


         FORMAT  :

           FOSBOOT(type%)

           type% = 0  for a 'cold'start (incl. POST & memory tests)
           type% = 1  for a 'warm'start (only DOS reboots)

         

         -------------------------------------------------------------
         FOSREAD
         -------------------------------------------------------------
         
         PURPOSE :

           Read a block of data from the receive buffer. The number of 
         characters ÿactually ÿtransferred ÿis ÿput ÿinto ÿthe ÿBYTES% 
         variable after the call. 
         
         
         FORMAT  :

           FOSREAD(comport%, bytes%, buffer$)


         EXAMPLE :

           '
           'create a 32 byte buffer
           '
           BUF$="12345678901234567890123456789012"
           '
           PORT%  = 1
           BYTES% = 32
           '
           CALL FOSREAD(PORT%, BYTES%, BUF$)
           '
           PRINT "BYTES READ : ";BYTES%
           PRINT "DATA READ  : ";LEFT$(BUF$,BYTES%)

         

         -------------------------------------------------------------
         FOSWRITE
         -------------------------------------------------------------
         
         PURPOSE :

           Write a block of data to the transmit buffer. The number of 
         characters ÿactually ÿtransferred ÿis ÿput ÿinto ÿthe ÿBYTES% 
         variable after the call. 
         

         FORMAT  :

           FOSWRITE(comport%, bytes%, buffer$)


         EXAMPLES :

           '
           'create some string
           '
           BUF$="Welcome to MailPro !"+CHR$(10)+CHR$(13)
           '
           PORT%  = 1
           BYTES% = LEN(BUF$)
           '
           CALL FOSWRITE(PORT%, BYTES%, BUF$)
           '
           PRINT "BYTES WRITTEN : ";BYTES%
         
         
         -------------------------------------------------------------
         FOSBREAK
         -------------------------------------------------------------
         
         PURPOSE :

           Starts or ends the transmission of a break state.


         FORMAT  :

           FOSBREAK(comport%, state%)

           state% = 1 to start a break
           state% = 0 to end a break



         -------------------------------------------------------------
         FOSTIMERTICK
         -------------------------------------------------------------
         
         PURPOSE :

           This ÿfunction returns information about the current ÿtimer 
         interrupt. ÿIt returns the interrupt number the timer is tied 
         to, ÿÿthe ÿnumber ÿof ticks per second, ÿand ÿthe ÿnumber ÿof 
         milliseconds per tick. 
         
         
         FORMAT  :

           FOSTIMERTICK(Intno%, Ticks%, Msecs%)

         
         -------------------------------------------------------------
         FOSSCANKEY
         -------------------------------------------------------------
         
         PURPOSE :

           Scans ÿthe keyboard and returns the next character ÿin ÿthe 
         keyboard buffer. If no characters are available a value of -1 
         will be returned. 

           The values returned will match the IBM-style of keycoding.

         
         FORMAT  :

           FOSSCANKEY(Key%)


         -------------------------------------------------------------
         FOSGETKEY
         -------------------------------------------------------------
         
         PURPOSE :

           Returns ÿthe next character in the keyboard buffer. ÿIf ÿno 
         characters are available, ÿthe functions waits until a key is 
         pressed. 

         
         FORMAT  :

           FOSGETKEY(Key%)

         

         -------------------------------------------------------------
         FOSLOCATE
         -------------------------------------------------------------
         
         PURPOSE :

           Locates the cursor on the screen. The screen is treated to 
         have co”rdinates as follows :

         ( 0, 0)
                +---------------------------------------------+
                |                                             |
                |  Hello World, this is supposed to be a      |
                |  picture of a screen...                     |
                |                                             |
                |                                             |
                |                                             |
                |                                             |
                |                                             |
                +---------------------------------------------+ 
                                                               (24,79)
         
         FORMAT  :

           FOSLOCATE(Row%, Col%)
         

         -------------------------------------------------------------
         FOSGETLOC
         -------------------------------------------------------------
         
         PURPOSE :

           Returns the current position of the cursor.
           
         
         FORMAT  :

           FOSGETLOC(Row%, Col%)
         
         

         -------------------------------------------------------------
         FOSDISPANSI
         -------------------------------------------------------------
         
         PURPOSE :

           Displays ÿa character and allows ANSI screen processing ÿto 
         occur (if available). ÿOn DOS machines the FOSSIL routine ÿto 
         perform this function probably will call a DOS function to do 
         the ÿANSI processing. ÿKeep in mind that DOS function are not 
         re-entrant. In such cases, this routine may not be assumed to 
         be re-entrant either. 

         
         FORMAT  :

           FOSDISPANSI(Char%)
         

         -------------------------------------------------------------
         FOSDISPBIOS
         -------------------------------------------------------------
         
         PURPOSE :

           Displays a charactes using the system BIOS. This means that 
         DOS ÿoutput redirection does not work when this call is ÿused 
         to produce screen output. 

         
         FORMAT  :

           FOSDISPBIOS(Char%)