===========================================================
                DDDDD           DDDDD               SSSS
                 D   Dunfield    D   D             S
                 D   D           D   Development    SSSS 
                 D   D           D   D                  Systems
                DDDDD           DDDDD               SSSS
          ===========================================================
          MM   MM  IIIIIII    CCCC   RRRRRR     OOO             CCCC
          M M M M     I      C    C  R     R   O   O           C    C
          M  M  M     I     C        R     R  O     O         C
          M     M     I     C        RRRRRR   O     O  -----  C
          M     M     I     C        R   R    O     O         C
          M     M     I      C    C  R    R    O   O           C    C
          M     M  IIIIIII    CCCC   R     R    OOO             CCCC
          ===========================================================
    
    
    
    
    
                             A compact 'C' compiler
                                      for
                               C-FLEA processors.
    
    
                                Technical Manual
    
    
    
    
    
                                  Release 3.02
    
                               Revised 09-Feb-94
    
    
    
    
    
    
    
    
    
    
    
    
                       Copyright 1988-1994 Dave Dunfield
                              All rights reserved

    MICRO-C C-FLEA Compiler                                          Page: 1


    1. INTRODUCTION
    
          This C-FLEA developers kit includes pre-configured implementations
       of  the  MICRO-C  compiler,  ASMCF  cross  assembler,   and   related
       utilities. The  package  provides  everything  you  need  to  perform
       software development in  either  'C'  or  assembler  for  the  C-FLEA
       virtual processor.
    
       1.1 Memory configuration
    
             The code produced by this compiler runs on the  C-FLEA  virtual
          processor,  which  can  be  emulated  by  several  different  host
          microprocessors. The exact memory layout may vary depending on the
          host. In the default system, the program is placed  in  memory  at
          address $1000, and the stack grows down from $0FFF, while data  is
          allocated beginning at $0000.
    
             You may run the code in other configurations, by re-configuring
          the memory setup in the PREFIX.ASM and MIDDLE.ASM files located in
          the LIBCF sub directory.
    
             Virtually any memory  configuration  within  the  limits  of  a
          single 64K address space can be  handled  by  our  PC  based  EMCF
          Virtual Machine Simulator.
    
       1.2 Code Portability
    
             With few exceptions, this compiler follows the  syntax  of  the
          "standard" UNIX compiler (within  its  subset  of  the  language).
          Programs written in MICRO-C should compile with few changes  under
          other "standard" compilers.
    
          1.2.1 Unsupported Features:
    
                MICRO-C does not currently support the following features of
             standard 'C':
    
                    Long / Double / Float / Enumerated data types,
                    Typedef and Bit fields.
    
          1.2.2 Additional Features
    
                MICRO-C provides a few additional  features  which  are  not
             always included in "standard" 'C' compilers:
    
                    Unsigned character variables, Nested comments, 16 bit
                    character constants, Inline assembly code capability.

    MICRO-C C-FLEA Compiler                                          Page: 2


       1.3 The compiling process
    
             There are five  programs  which  work  together  to  completely
          compile a MICRO-C program:
    
             The PREPROCESSOR (MCP) takes  the  original  'C'  source  file,
          performs MACRO expansion and incorporates the contents of  INCLUDE
          files  to  get  a  "pure"  'C'  output  file.  A   less   powerful
          pre-processor is also contained inside the COMPILER, which  allows
          this step to  be  skipped  for  programs  which  use  only  simple
          pre-processor functions.
    
             The COMPILER (MCCCF) reads  a  file  containing  a  'C'  source
          program, and translates it into an  equivalent  assembly  language
          program.
    
             The OPTIMIZER (MCOCF) reads the assembly language  output  from
          the compiler identifying and replacing "general" code produced  by
          the compiler with  more  efficent  code  which  is  equivalent  in
          specific cases. This step is  optional,  allowing  you  to  choose
          between faster compile time and greater program efficency.
    
             The SOURCE LINKER (SLINK) combines the assembly language output
          from the compiler with any  required  routines  from  the  runtime
          library, to create an entire program file.
    
             The ASSEMBLER  (ASMCF)  assembles  this  program  file  into  a
          downloadable binary image in either INTEL  or  MOTOROLA  hex  file
          format.

    MICRO-C C-FLEA Compiler                                          Page: 3


    2. THE COMMAND CO-ORDINATOR
    
          'CC' is a utility which co-ordinates  the  execution  of  programs
       required for each step of the compilation process to provide a simple
       "one step" compilation  command.  This  MICRO-C  package  includes  a
       version of  the  command  co-ordinator  which  handles  the  commands
       necessary to compile for the C-FLEA  processor  (MCP,  MCCCF,  MCOCF,
       SLINK, ASMCF).
    
       2.1 The CCF command
    
             The format of the 'CCF' command is:
    
                              CCF <name> [options]
    
          2.1.1 Command line options
    
                -A      - produce ASSEMBLER (.ASM) output file
                -C      - Include 'C' source as comments in ASM files
                -F      - Fold identical string constants.
                -I      - Output INTEL hex file (default is MOTOROLA)
                -K      - KEEP all temporary files (do not delete)
                -L      - Generate assembly .LST file
                -M      - Invoke xasm MACRO processor (See XASM manual)
                -O      - OPTIMIZE the output code (using MCOCF)
                -P      - use the extended PRE-PROCESSOR (MCP)
                -Q      - QUIET mode (suppress informational messages)
                -X      - produce eXtended ASM file (includes libraries)
                H=mcdir - specify MICRO-C home directory
                T=mctmp - specify prefix for TEMPORARY files
    
                name=xx - Predefine macro symbol (use with -P only)
    
                When executing the sub-commands, CCF will search the MICRO-C
             home directory, as well as any  directories  specified  in  the
             'PATH' environment variable. Libraries are  accessed  from  the
             MICRO-C home directory only.
    
                The environment variable 'MCDIR' is  examined  to  determine
             the path to  the  MICRO-C  home  directory.  If  MCDIR  is  not
             defined, CCF will assume the string  '\MC'.  You  may  override
             this directory by using the 'h=' option on the command line.
    
                Intermediate  results  from  each  command  are  stored   in
             "temporary" files, which are fed as input to the next  command.
             Temporary files will be deleted once they are no longer needed,
             except in the case where a command fails.  When  this  happens,
             any temporary file which  was  being  used  as  input  to  that
             command will not be deleted, allowing you to examine it for the
             cause of the error.

    MICRO-C C-FLEA Compiler                                          Page: 4


                The environment variable 'MCTMP' is examined to determine  a
             prefix to prepend to temporary file  names.  If  MCTMP  is  not
             defined, CCF  assumes  the  default  prefix  of  '$'.  You  may
             override this prefix by using the 't=' option  on  the  command
             line.
    
                Here are example 'SET' commands suitable  for  inclusion  in
             the AUTOEXEC.BAT file, of an IBM/PC based MICRO-C system  which
             has the home directory in 'C:\MC', and a TEMP  directory  on  a
             RAMDISK as drive 'D':
    
                    SET MCDIR=C:\MC
                    SET MCTMP=D:\TEMP\      (Note trailing '\')
    
                The '-A' option causes  CCF  to  bypass  the  assembler  and
             linker, and produce an assembly source file (<name>.ASM) as the
             output file. If the '-C' option is also used,  this  file  will
             contain the 'C' source code in the form of comments. NOTE:  The
             source code inserted by '-C' will  restrict  the  optimizer  to
             operate only on sections of code produced by a single 'C' line.
    
                The '-F' option causes the compiler to  "fold"  its  literal
             pool (the area of memory where string  constants  are  stored).
             This means that identical strings  not  contained  in  explicit
             variables, will occur only once in memory. Since most  programs
             never modify such strings, it is usually safe to do this.  Note
             however that this is a violation of the 'C' standard ("The  'C'
             Programming Language"  page  181  -  "All  strings,  even  when
             written identically, are distinct"),  and  it  is  possible  to
             write programs which will not work properly when this option is
             used.
    
                The '-X' option is similar to '-A', except that the  program
             is passed through the source linker, resulting in a ".ASM" file
             containing the complete program,  including  startup  code  and
             library functions.
    
                The  '-M'  option  causes  CCF  to  invoke  the  xasm  MACRO
             processor, allowing macros to be used in your  inline  assembly
             code (See XASM manual). For the sake of efficency, this is done
             BEFORE the program is passed through the  source  linker.  This
             means that macros  in  files  from  the  library  will  NOT  be
             processed. If library files  contain  macros,  they  should  be
             processed BEFORE they are placed in the library.
    
                If any of the programs executed  by  CCF  fail  to  complete
             properly, CCF will show the message "PGM  failed  (RC)",  where
             PGM is the name of the offending program, and  RC  is  the  DOS
             return code value. Common RC values under MSDOS are:
    
                2   - Command not found (Check MCDIR and PATH setup)
                3   - Path not found    (Check MCDIR and PATH setup)
                254 - Program found errors during processing
                255 - Program was invoked with incorrect arguments

    MICRO-C C-FLEA Compiler                                          Page: 5


    3. THE MICRO-C PROGRAMMING LANGUAGE
    
          The following pages contain a brief summary of  the  features  and
       constructs implemented in MICRO-C.
    
          This document does not  attempt  to  teach  'C'  programming,  and
       assumes that the reader is familiar with the language.
    
       3.1 Constants
    
             The following forms of constants are supported by the compiler:
    
                <num>       - Decimal number        (0 - 65535)
                0<num>      - Octal number          (0 - 0177777)
                0x<num>     - Hexidecimal number    (0x0 - 0xffff)
                '<char>'    - Character             (1 or 2 chars)
                "<string>"  - Address of literal string.
    
             The following "special" characters may be used within character
          constants or strings:
    
                \n          - Newline (line-feed)   (0x0a)
                \r          - Carriage Return       (0x0d)
                \t          - Tab                   (0x09)
                \f          - Formfeed              (0x0c)
                \b          - Backspace             (0x08)
                \<num>      - Octal value <num>     (Max. three digits)
                \x<num>     - Hex value <num>       (Max. two digits)
                \<char>     - Protect character <char> from input scanner.
    
       3.2 Symbols
    
             Symbol names  may  include  the  characters  'a'-'z',  'A'-'Z',
          '0'-'9', and '_'. The characters '0'-'9' may not be  used  as  the
          first character in the  symbol  name.  Symbol  names  may  be  any
          length, however, only the first 15 characters are significant.
    
             The "char" modifier may be used to declare a symbol as an 8 bit
          wide value, otherwise it is assumed to be 16 bits.
    
                              eg: char input_char;
    
             The "int" modifier may be used to declare a symbol as a 16  bit
          wide value. This is assumed if neither "int" or "char" is given.
    
                                  eg: int abc;
    
             The "unsigned" modifier may be used to declare a symbol  as  an
          unsigned positive only value. Note that unlike some 'C' compilers,
          this modifier may be applied to a character (8 bit) variable.
    
                            eg: unsigned char count;

    MICRO-C C-FLEA Compiler                                          Page: 6


             The "extern" modifier causes the compiler to be  aware  of  the
          existance and  type  of  a  global  symbol,  but  not  generate  a
          definition for that symbol. This allows the module being  compiled
          to reference a symbol which is defined  in  another  module.  This
          modifier may not be used with local symbols.
    
                            eg: extern char getc();
    
             A  symbol  declared  as  external  may  be  re-declared  as   a
          non-external at a later  point  in  the  code,  in  which  case  a
          definition for it will be generated. This allows  "extern"  to  be
          used to inform the compiler of a function or variable type so that
          it can be referenced  properly  before  that  symbol  is  actually
          defined.
    
             The "static" modifier causes global  symbols  to  be  available
          only in the file where they are defined.  Variables  or  functions
          declared  as  "static"  will  not  be   accessable   as   "extern"
          declarations in other object files, nor will they cause  conflicts
          with duplicate names in those files.
    
                         eg: static int variable_name;
    
             When applied to local symbols,  the  "static"  modifier  causes
          those variables to be allocated in  a  reserved  area  of  memory,
          instead of on the processor stack. This has the  effect  that  the
          contents of the variable will be retained  between  calls  to  the
          function. It also means that the variable  may  be  initialzed  at
          compile time.
    
             The "register" modifier indicates to the  code  generator  that
          this is a high priority variable, and should be kept where  it  is
          easy to get at. Since  its  interpretation  depends  on  the  code
          generator, it is often  ignored  in  simple  implementations.  See
          "Functions" for a  special  use  of  "register"  when  defining  a
          function.
    
                          eg: register unsigned count;
    
             Symbols declared with a preceeding '*' are assumed to be 16 bit
          pointers to the declared type.
    
                             eg: int *pointer_name;
    
             Symbol names declared followed by square brackets  are  assumed
          to be arrays with a number of dimensions equal to  the  number  of
          '[]' pairs that follow. The size of each dimension  is  identified
          by a constant value  contained  within  the  corresponding  square
          brackets.
    
                          eg: char array_name[5][10];

    MICRO-C C-FLEA Compiler                                          Page: 7


          3.2.1 Global Symbols
    
                Symbols  declared  outside  of  a  function  definition  are
             considered to  be  global  and  will  have  memory  permanently
             reserved for them. Global symbols are defined by  name  in  the
             output file, allowing other modules to access them.
    
                Note that the compiler IS case  sensitive,  however  if  the
             assembler you are using is NOT, you  must  be  careful  not  to
             declare any global symbols with names that differ only in case.
    
                All non-initialized global variables are  generated  at  the
             very end of the output file, after the literal pool is  dumped.
             Since non-initialized globals do not generate object code, this
             allows them to be excluded from the image file when it is saved
             to disk.
    
                Global variables may be initialized with one or more values,
             which are expressed as a single array of  integers  REGUARDLESS
             of the size and shape of the variable. If more than  one  value
             is expressed, '{' and '}' must be used.
    
                   eg: int i = 10, j[2][2] = { 1, 2, 3, 4 };
    
                When arrays are declared, a null dimension may  be  used  as
             the dimension size, in which case the size of  the  array  will
             default to the number of initialized values.
    
                         eg: int array[] = { 1, 2, 3 };
    
                Initialized global variables are automatically saved  within
             the code image,  insuring  that  the  initial  values  will  be
             available at run time. Any non-initialized elements of an array
             which has been partly initialized will be set to zero.
    
                Non-initialized global variables are not preset in any  way,
             and will be undefined at the beginning of program execution.
    
          3.2.2 Local Symbols
    
                Symbols declared within a function definition are  allocated
             on the stack, and  exist  only  during  the  execution  of  the
             function.
    
                To simplify the allocation and de-allocation of stack space,
             all local symbols must be declared  at  the  beginning  of  the
             function before any code producing statements are encountered.
    
                MICRO-C does not support initialization of non-static  local
             variables in the declaration statement. Since  local  variables
             have to be initialized every time the function is entered,  you
             can get the same effect  using  assignment  statements  at  the
             beginning of the function.
    
                No type is assumed for  arguments  to  functions.  Arguments
             must be explicitly declared, otherwise they will  be  undefined
             within the scope of the function definition.

    MICRO-C C-FLEA Compiler                                          Page: 8


          3.2.3 More Symbol Examples
    
            /* Global variables are defined outside of any function */
            char a;                     /* 8 bit signed */
            unsigned char b;            /* 8 bit unsigned */
            int c;                      /* 16 bit signed */
            unsigned int d;             /* 16 bit unsigned */
            unsigned e;                 /* also 16 bit unsigned */
            extern char f();            /* external function returning char */
            static int g;               /* 16 bit signed, local to file */
            int h[2] = { 1, 2 };        /* initialized array (2 ints) */
    
            main(a, b)                  /* "int" function containing code */
            /* Function arguments are defined between function name and body */
                int a;                  /* 16 bit signed */
                unsigned char *b;       /* pointer to 8 bit unsigned */
            {
            /* Local variables are defined inside the function body */
            /* Note that in MICRO-C, only "static" locals can be initialized */
                unsigned c;             /* 16 bit unsigned */
                static char d[5];       /* 8 bit signed, reserved in memory */
                static int e = 1;       /* 16 bit signed, initial value is 1 */
            /* Function code goes here ... */
                c = 0;                  /* Initialize 'c' to zero */
                strcpy(d, "Name");      /* Initialize 'd' to "name" */
            }

    MICRO-C C-FLEA Compiler                                          Page: 9


       3.3 Arrays & Pointers
    
             When MICRO-C passes an array to a function, it actually  passes
          a POINTER to the array. References to arrays which  are  arguments
          are automatically performed through the pointer.
    
             This allows the use of pointers and arrays to be interchangable
          through the context of a function call. Ie: An array passed  to  a
          function may be declared and used as  a  pointer,  and  a  pointer
          passed to a function may be declared and used as an array.
    
       3.4 Functions
    
             Functions are  essentially  initialized  global  symbols  which
          contain executable code.
    
             MICRO-C accepts  any  valid  value  as  a  function  reference,
          allowing  some  rather  unique  (although  non-standard)  function
          calls.
    
          For example:
    
                function();     /* call function */
                variable();     /* call contents of a variable */
                (*var)();       /* call indirect through variable */
                (*var[x])();    /* call indirect through indexed array */
                0x5000();       /* call address 0x5000 */
    
             Since this is a single pass compiler, operands to functions are
          evaluated and pushed on the stack in the order in which  they  are
          encountered, leaving the last operand closest to the  top  of  the
          stack. This is the opposite order from which  many  'C'  compilers
          push operands.
    
             For functions with a fixed number of arguments,  the  order  of
          which operands  are  passed  is  of  no  importance,  because  the
          compiler looks after generating  the  proper  stack  addresses  to
          reference variables.  HOWEVER,  functions  which  use  a  variable
          number of arguments are affected for two reasons:
    
          1) The location of the LAST arguments are known (as fixed  offsets
             from the stack pointer) instead of the FIRST.
    
          2) The symbols defined as arguments  in  the  function  definition
             represent the LAST arguments instead of the FIRST.
    
             If a function is declared as "register", it  serves  a  special
          purpose and causes the accumulator to be loaded with the number of
          arguments passed whenever the function is called. This allows  the
          function to know how many  arguments  were  passed  and  therefore
          determine the location of the first argument.

    MICRO-C C-FLEA Compiler                                          Page: 10


       3.5 Structures & Unions
    
             Combinations of other variable  types  can  be  organized  into
          STRUCTURES or UNIONS, which allow them  to  be  manipulated  as  a
          single entity.
    
             In a structure, the  individual  items  occur  sequentially  in
          memory, and the total size of the structure  is  the  sum  of  its
          elements. Structures are usually  used  to  create  "records",  in
          which related items are grouped together. An array  of  structures
          is the common method of implementing an "in-memory" database.
    
             A union is similar to a structure, except that  the  individual
          items are overlaid in memory, and the total size of the  union  is
          the size of its largest element. Unions are usually used to  allow
          a single block of memory to be accessed as different 'C'  variable
          types. An example of this would be in handling a message  received
          in memory, in which a "type" byte indicates how the  remainder  of
          the message data should be interpreted.
    
             Here are some example of how structures are  defined  and  used
          (unions are defined and used in an identical manner,  except  that
          the word 'union' is substituted for 'struct'):
    
            /* Create structure named 'data' with 'a,b,c & d' as members */
            struct {
                int a;
                int b;
                char c;
                char d; } data;
    
            /* Create structure template named 'mystruc'... */
            /* No actual structure variable is defined */
            struct mystruc {
                int a;
                int b;
                char c;
                char d; };
    
            /* Create structure named 'data' using above template */
            struct mystruc data;
    
            /* Create structure template 'mystruc', AND define a */
            /* structure variable named 'data' */
            struct mystruc {
                int a;
                int b;
                char c;
                char d; } data;

    MICRO-C C-FLEA Compiler                                          Page: 11


            /* Create an array of structures, a pointer to a structure */
            /* and an array of pointers to a structure *
            struct mystruct array[10], *pointer, *parray[10];
    
            /* To set value in structure variable/members */
            data.a = 10;            /* Direct access */
            array[1].b = 10;        /* Direct array access */
            pointer->c = 'a';       /* Pointer access */
            parray[2]->d = 'b';     /* Pointer array access */
    
            /* To read value in structure variable/members */
            value = data.a;         /* Direct access */
            value = data[1].b;      /* Direct array access */
            value = pointer->c;     /* Pointer access */
            value = parray[2]->d;   /* Pointer array access */
    
          3.5.1 Notes on MICRO-C structure implementation:
    
                Structures and Unions as implemented in MICRO-C are  similar
             to the implementation of the original UNIX  'C'  compiler,  and
             are bound by similar limitations, as  well  as  a  few  MICRO-C
             specific ones.  Here  is  a  list  of  major  differences  when
             compared to a modern ANSI compiler:
    
                All structure and member names MUST  be  unique  within  the
             scope of the definition. A special case  exists,  where  common
             member names may be used in  multiple  structure  templates  if
             they have EXACTLY the same type and offset into the  structure.
             This also saves symbol table memory, since only one copy of the
             member definition is actually kept.
    
                MICRO-C does NOT pass entire structures to functions on  the
             stack. Like  arrays,  MICRO-C  passes  structures  by  ADDRESS.
             Structure variables which are function arguments  are  accessed
             through pointers. For source code compatibility with  compilers
             which do pass the entire structure, if you declare the argument
             as a direct (non-pointer) structure, the direct ('.')  operator
             is used to dereference it, even though it is actually a pointer
             reference.
    
                If you  MUST  have  a  local  copy  of  the  structure,  use
             something like:
    
                func(sptr)
                    struct mystruc *sptr;
                {
                    struct mystruc data;
                    memcpy(data, sptr, sizeof(data));
                    ...
                }

    MICRO-C C-FLEA Compiler                                          Page: 12


                To obtain the size of a structure from  its  template  name,
             use the 'struct'  keyword  in  conjunction  with  the  'sizeof'
             operator.   In   the   above   example,   you   could   replace
             'sizeof(data)' with 'sizeof(struct mystruc)'.
    
                To obtain the size of a structure member, you  must  specify
             it in the context of a structure reference with another symbol:
    
              sizeof(variable.member) or sizeof(variable->member)
    
                NOTE: The current compiler allows almost any symbol  to  the
             left of the '.' or '->' operator in a 'sizeof', however  future
             versions of the compiler may insist on a structure variable  or
             a pointer to structure variable.
    
                Pointers to structures are internally stored as pointers  to
             'char', and therefore will only increment/decrement by  1  when
             ++/-- is used. To advance a pointer by the size of a structure,
             use:
    
                         ptr += sizeof(struct mystruc)
    
                The 'struct' and 'union' keywords  are  not  accepted  in  a
             TYPECAST. This is most commonly used to setup a  pointer  to  a
             structure. Since MICRO-C stores its pointers to  structures  as
             pointers to char, you can use (char*) as the typecast, and  get
             the same functionality.
    
                A structure name by itself (without  '.member')  acts  in  a
             manner similar to a character array name.  With  no  operation,
             the address of the structure is returned. You can also use '[]'
             to access  individual  bytes  in  the  structure  by  indexing,
             although doing so is highly non-portable.
    
                MICRO-C allows static or global structures to be initialized
             in the declaration, however the initial values are read  as  an
             array of bytes, and are assigned directly to  structure  memory
             without regard for the type or size of its members:
    
                struct mystruc data = { 0, 1, 0, 2, 3, 4 };
                /* A=0:1, B=0:2, C=3, D=4 */
    
                You can use INT and CHAR to switch back  and  forth  between
             word/byte initialization within the value list:
    
                struct mystruct data = { int 0, 1, char 2, 3 };
                /* A=0, B=1, C=2, D=3 */
    
                MICRO-C does not WORD ALIGN structure elements. When using a
             processor which requires word alignment, it is the  programmers
             responsibility to maintain alignment, using filler  bytes  etc.
             when necessary.

    MICRO-C C-FLEA Compiler                                          Page: 13


       3.6 Control Statements
    
             The following control statements are implemented in MICRO-C:
    
                if(expression)
                    statement;
    
                if(expression)
                    statement;
                else
                    statement;
    
                while(expression)
                    statement;
    
                do
                    statement;
                while expression;
    
                for(expression; expression; expression)
                    statement;
    
                return;
    
                return expression;
    
                break;
    
                continue;
    
                switch(expression) {
                    case constant_expression :
                        statement;
                        ...
                        break;
                    case constant_expression :
                        statement;
                        ...
                        break;
                        .
                        .
                        .
                    default:
                        statement; }
    
                label: statement;
    
                goto label;
    
                asm "...";
    
                asm {
                    ...
                    }

    MICRO-C C-FLEA Compiler                                          Page: 14


    3.6.1 Notes on Control Structures
    
        1)  Any "statement" may be a single statement or a compound
            statement enclosed within '{' and '}'.
    
        2)  All three "expression"s in the "for" command are optional.
    
        3)  If a "case" selection does not end with "break;", it will
            "fall through" and execute the following case as well.
    
        4)  Expressions following 'return' and 'do/while' do not have
            to be contained in brackets (although this is permitted).
    
        5)  Label names may preceed any statement, and must be any
            valid symbol name, followed IMMEDIATELY by ':' (No spaces
            are allowed). Labels are considered LOCAL to a function
            definition and will only be accessable within the scope
            of that function.
    
        6)  The 'asm' statement used to implement the inline assembly
            language capability of MICRO-C accepts two forms:
                asm "...";      <- Assemble single line.
                asm {           <- Assemble multiple lines.
                    ...
                    }

    MICRO-C C-FLEA Compiler                                          Page: 15


       3.7 Expression Operators
    
             The following expression operators are implemented in MICRO-C:
    
    3.7.1 Unary Operators
    
        -           - Negate
        ~           - Bitwise Complement
        !           - Logical complement
        ++          - Pre or Post increment
        --          - Pre or post decrement
        *           - Indirection
        &           - Address of
        sizeof      - Size of a object or type
        (type)      - Typecast
    
    3.7.2 Binary Operators
    
        +           - Addition
        -           - Subtraction
        *           - Multiplication
        /           - Division
        %           - Modulus
        &           - Bitwise AND
        |           - Bitwise OR
        ^           - Bitwise EXCLUSIVE OR
        <<          - Shift left
        >>          - Shift right
        ==          - Test for equality
        !=          - Test for inequality
        >           - Test for greater than
        <           - Test for less than
        >=          - Test for greater than or equal to
        <=          - Test for less than or equal to
        &&          - Logical AND
        ||          - Logical OR
        =           - Assignment
        +=          - Add to self assignment
        -=          - Subtract from self assignment
        *=          - Multiply by self assignment
        /=          - Divide by and reassign assignment
        %=          - Modular self assignment
        &=          - AND with self assignment
        |=          - OR with self assignment
        ^=          - EXCLUSIVE OR with self assignment
        <<=         - Shift left self assignment
        >>=         - Shift right self assignment

    MICRO-C C-FLEA Compiler                                          Page: 16


    NOTES:
    
        1)  The expression "a && b" returns 0 if "a" is zero, otherwise the
            value of "b" is returned. The "b" operand is NOT evaluated if
            "a" is zero.
    
        2)  The expression "a || b" returns the value of "a" if it is not 0,
            otherwise the value of "b" is returned. The "b" operand is NOT
            evaluated if "a" is non-zero.
    
    3.7.3 Other Operators
    
        ;           - Ends a statement.
        ,           - Allows several expressions in one statement.
                    + Separates symbol names in multiple declarations.
                    + Separates constants in multi-value initialization.
                    + Separates operands in function calls.
        ?           - Conditional expression (ternary operator).
        :           - Delimits labels, ends CASE and separates conditionals.
        .           - Access a structure member directly.
        ->          - Access a structure member through a pointer.
        { }         - Defines a BLOCK of statements.
        ( )         - Forces priority in expression, indicates function calls.
        [ ]         - Indexes arrays. If fewer index values are given than the
                      number of dimensions which are defined for the array,
                      the value returned will be a pointer to the appropriate
                      address.
    
                    Eg:
                        char a[5][2];
    
                        a[3] returns address of forth row of two characters.
                        (remember index's start from zero)
    
                        a[3][0] returns the character at index [3][0];

    MICRO-C C-FLEA Compiler                                          Page: 17


       3.8 Inline Assembly Language
    
             Although 'C' is a powerful and  flexible  language,  there  are
          sometimes instances where a particular operation must be  peformed
          at the assembly language level. This most  often  involves  either
          some processor feature for which there  is  no  corresponding  'C'
          operation, or a section of very time critical code.
    
             MICRO-C provides access to assembly  language  with  the  'asm'
          statement, which has two basic forms. The first is:
    
                                  asm "..." ;
    
             In this form, the entire  text  contained  between  the  double
          quote characters (") is output as a single line to the  assembler.
          Note that a  semicolon  is  required,  just  like  any  other  'C'
          statement.
    
             Since this is a standard 'C' string, you can  use  any  of  the
          "special" characters, and thus you could output multiple lines  by
          using '\n' within the string. Another important characteristic  of
          it being a string is that it will be protected from  pre-processor
          substitution.
    
             The second form of the 'asm' statement is:
    
                                     asm {
                                      ...
                                       }
    
             In this form, all lines between '{' and '}' are output  to  the
          assembler. Any text following the opening '{' (on the  same  line)
          is ignored. Due to  the  unknown  characteristics  of  the  inline
          assembly code, the closing '}' will only be recognized when it  is
          the first non-whitespace character on a line.
    
             The integral pre-processor will not perform substitution on the
          inline assembly code, however  the  external  pre-processor  (MCP)
          will substitute in this form. This allows you to  create  assembly
          language "macros" using MCP, and have parameters substituted  into
          them when they are expanded:
    
            /*
             * This macro issues a 'SETB' instruction for its parameter
             */
            #define setbit(bit) asm {\
                SETB bit\
            }
    
            /*
             * This macro WILL NOT WORK, since the 'bit' operand to the SETB
             * instruction is contained within a string and is therefore
             * protected from substitution by the pre-processor
             */
            #define setbit(bit) asm " SETB bit";

    MICRO-C C-FLEA Compiler                                          Page: 18


       3.9 Preprocessor Commands
    
             The  MICRO-C  compiler  supports  the  following  pre-processor
          commands. These commands are recognized only if they occur at  the
          beginning of the input line.
    
             NOTE:  This  describes  the  limited  pre-processor  which   is
          integral to the  compiler,  see  also  the  section  on  the  more
          powerful external processor (MCP).
    
          3.9.1 #define <name> <replacement_text>
    
                The "#define" command allows a global name  to  be  defined,
             which will be replaced with the indicated text whenever  it  is
             encountered in the input file. This occurs prior to  processing
             by the compiler.
    
          3.9.2 #file <filename>
    
                Sets the filename of the currently  procssing  file  to  the
             given  string.  This  command   is   used   by   the   external
             pre-processor (MCP) to insure that error messages indicate  the
             original source file.
    
          3.9.3 #include <filename>
    
                This command causes the indicated file to be opened and read
             in as the source  text.  When  the  end  of  the  new  file  is
             encountered, processing will continue with the  line  following
             "#include" in the original file.
    
          3.9.4 #ifdef <name>
    
                Processes the following lines (up to #else or  #endif)  only
             if the given name is defined.
    
          3.9.5 #ifndef <name>
    
                Processes the following lines (up to #else or  #endif)  only
             if the given name is NOT defined.
    
          3.9.6 #else
    
                Processes the following lines (up to  #endif)  only  if  the
             preceeding #ifdef or #ifndef was false.
    
          3.9.7 #endif
    
                Terminates #ifdef and #ifndef
    
                NOTE: The integral pre-processor does not support nesting of
             the #ifdef and #idndef constructs. If you wish  to  nest  these
             conditionals, you must use the external pre-processor (MCP).

    MICRO-C C-FLEA Compiler                                          Page: 19


       3.10 Error Messages
    
             When MICRO-C detects an  error,  it  outputs  an  informational
          message indicating the type of problem encountered.
    
             The error message is preceeded by the filename and line  number
          where the error occured:
    
                           program.c(5): Syntax error
    
             In the above example, the error occured in the file "program.c"
          at line 5.
    
             The following error messages are produced by the compiler:
    
          3.10.1 Compilation aborted
    
                The preceeding error was so severe than the compiler  cannot
             proceed.
    
          3.10.2 Constant expression required
    
                The compiler requires a constant  expression  which  can  be
             evaluated at compile time (ie: no variables).
    
          3.10.3 Declaration must preceed code.
    
                All local variables must be defined at the beginning of  the
             function, before any code producing statements are processed.
    
          3.10.4 Dimension table exhausted
    
                The compiler has encountered more  active  array  dimensions
             than it can handle.
    
          3.10.5 Duplicate local: 'name'
    
                You have declared the named  local  symbol  more  than  once
             within the same function definition.
    
          3.10.6 Duplicate global: 'name'
    
                You have declared the named global symbol more than once.
    
          3.10.7 Expected '<token>'
    
                The compiler  was  expecting  the  given  token,  but  found
             something else.
    
          3.10.8 Expression stack overflow
    
                The compiler has found a more complicated expression than it
             can handle. Check that it is of  correct  syntax,  and  if  so,
             break it up into two simpler expressions.

    MICRO-C C-FLEA Compiler                                          Page: 20


          3.10.9 Expression stack underflow
    
                The compiler has made an error in  parsing  the  expression.
             Check that it is of correct syntax.
    
          3.10.10 Illegal indirection
    
                You have attempted to perform an indirect operation ('*'  or
             '[]') on an entity which is not a pointer or array. This  error
             will also result if you attempt to index  an  array  with  more
             indices than it has dimensions.
    
          3.10.11 Illegal initialization
    
                Local variables may not be initialized  in  the  declaration
             statement. Use assignments at the  beginning  of  the  function
             code to perform the initialization.
    
          3.10.12 Illegal nested function
    
                You may not declare a  function  within  the  definition  of
             another function.
    
          3.10.13 Improper type of symbol: 'name'
    
                The named  symbol  is  not  of  the  correct  type  for  the
             operation that you are attempting. Eg: 'goto' where the  symbol
             is not a label.
    
          3.10.14 Improper #else/#endif
    
                A #else or #endif statement is out of place.
    
          3.10.15 Inconsistant member offset: 'name'
    
                The named structure member is multiply defined,  and  has  a
             different offset from its first definition.
    
          3.10.16 Inconsistant member type: 'name'
    
                The named structure member is multiply defined,  and  has  a
             different type from its first definition.
    
          3.10.17 Inconsistant re-declaration: 'name'
    
                You have attempted to redefine  the  named  external  symbol
             with a type which does not match its previously declared type.
    
          3.10.18 Incorrect declaration
    
                A statement occuring outside of a function definition is not
             a valid declaration for a function or global variable.

    MICRO-C C-FLEA Compiler                                          Page: 21


          3.10.19 Invalid '&' operation
    
                You have attempted to reference  the  address  of  something
             that has no address. This error also occurs when you attempt to
             take the address of an array without giving it a  full  set  of
             indicies. Since the address is already returned in  this  case,
             simply drop the '&'. (The error occurs because you  are  trying
             to take the address of an address).
    
          3.10.20 Macro expansion too deep
    
                The compiler has encountered a nested macro reference  which
             is too deep to be resolved.
    
          3.10.21 Macro space exhausted
    
                The compiler has encountered  more  macro  ("#define")  text
             than it has room to store.
    
          3.10.22 No active loop
    
                A "continue" or "break" statement was  encountered  when  no
             loop is active.
    
          3.10.23 No active switch
    
                A "case" or "default"  statement  was  encountered  when  no
             "switch" statement is active.
    
          3.10.24 Not an argument: 'name'
    
                You have declared the named variable as an argument, but  it
             does not appear in the argument list.
    
          3.10.25 Non-assignable
    
                You have attempted an operation which results in  assignment
             of a value to an entity which cannot be assigned. (eg: 1 = 2);
    
          3.10.26 Numeric constant required
    
                The compiler requires a constant expression which returns  a
             simple numeric value.
    
          3.10.27 String space exhausted
    
                The compiler has encountered more literal  strings  than  it
             has room store.
    
          3.10.28 Symbol table full
    
                The compiler has encountered more symbol definitions than it
             can handle.

    MICRO-C C-FLEA Compiler                                          Page: 22


          3.10.29 Syntax error
    
                The statement shown does not follow syntax rules and  cannot
             be parsed.
    
          3.10.30 Too many active cases
    
                The compiler has run out of space  for  storing  switch/case
             tables. Reduce the number of active "cases".
    
          3.10.31 Too many defines
    
                The compiler has encountered more '#define' statements  than
             it can handle. Reduce the number of #defines.
    
          3.10.32 Too many errors
    
                The compiler is aborting because of excessive errors.
    
          3.10.33 Too many includes
    
                The compiler has encountered more  nested  "#include"  files
             than it can handle.
    
          3.10.34 Too many initializers
    
                You have specified more initialization values than there are
             locations in the global variable.
    
          3.10.35 Type clash
    
                You have attempted to use a  value  in  a  manner  which  is
             inconsistant with its typing information.
    
          3.10.36 Unable to open: 'name'
    
                A "#include" command specified the named file,  which  could
             not be opened.
    
          3.10.37 Undefined: 'name'
    
                You have referenced a name which is not defined as  a  local
             or global symbol.
    
          3.10.38 Unknown structure/member: 'name'
    
                You have referenced a  structure  template  or  member  name
             which is not defined.
    
          3.10.39 Unreferenced: 'name'
    
                The named  symbol  was  defined  as  a  local  symbol  in  a
             function, but was never used in that function. This error  will
             occur at the end of  the  function  definition  containing  the
             symbol declaration. It is only a warning, and  will  not  cause
             the compile to abort.

    MICRO-C C-FLEA Compiler                                          Page: 23


          3.10.40 Unresolved: 'name'
    
                The named symbol was forward  referenced  (Such  as  a  GOTO
             label), and was never defined. This error will occur at the end
             of the function definition containing the reference.
    
          3.10.41 Unterminated conditional
    
                The end of file was encountered  when  a  "#if"  or  "#else"
             conditional block was being processed.
    
          3.10.42 Unterminated function
    
                The  end  of  the  file  was  encountered  when  a  function
             definition was still open.

    MICRO-C C-FLEA Compiler                                          Page: 24


       3.11 Quirks
    
             Due  to  its  background  as  a  highly  compact  and  portable
          compiler, and its target application in embedded systems,  MICRO-C
          deviates from standard 'C' in  some  areas.  The  following  is  a
          summary of the major infractions and quirks:
    
             When using the INTERNAL  pre-processor,  the  operands  to  '#'
          commands are parsed based on separating spaces, and any portion of
          the line not required is ignored.  In  particular,  the  '#define'
          command only accepts a definition up to  the  next  space  or  tab
          character.
    
            eg: #define APLUSONE A+1        <-- uses "A+1"
                #define APLUSONE A +1       <-- uses "A"
    
             Comments are stripped by the token scanner, which occurs  AFTER
          the '#' commands are processed.
    
            eg: #define NULL    /* comment */   <-- uses "/*"
    
             Note that since comments can therefore be included in "#define"
          symbols, you can use "/**/" to simulate spaces between tokens.
    
            eg: #define BYTE unsigned/**/char
    
             Include filenames are not delimited by '""'  or  '<>'  and  are
          passed to the operating system exactly as entered.
    
            eg: #include \mc\stdio.h
    
             NOTE:  The  above  quirks  DO  NOT  APPLY  when  the   EXTERNAL
          pre-processor (MCP) is used.
    
             The appearance of a variable name in the argument  list  for  a
          function  declaration  serves  only  to  identify  that  variables
          location on the stack. MICRO-C will not define the variable unless
          it is explicitly declared (between the argument list and the  main
          function body). In other words, all arguments to a  function  must
          be explicitly declared.
    
             MICRO-C is more  strict  about  its  handling  of  the  ADDRESS
          operator ('&') than most other compilers. It will produce an error
          message if you attempt to take the address of  a  value  which  is
          already a fixed address (such as an array name without a full  set
          of indicies). Since an address is already produced in such  cases,
          simply drop the '&'.
    
             The 'x' in '0x' and '\x' is accepted in lower case only.

    MICRO-C C-FLEA Compiler                                          Page: 25


             When operating on pointers, MICRO-C only scales  the  increment
          (++), decrement (--) and index ([]) operations to account for  the
          size of the pointer:
    
            eg: char *cptr;     /* pointer to character */
                int  *iptr;     /* pointer to integer */
                ++cptr;         /* Advance one character */
                ++iptr;         /* Advance one integer */
                cptr[10];       /* Access the tenth character */
                iptr[10];       /* Access the tenth integer */
                cptr += 10;     /* Advance 10 characters */
                iptr += 10;     /* Advance ONLY FIVE integers */
    
            NOTE: A portable way to advance "iptr" by integers is:
    
                iptr = &iptr[10];   /* Advance 10 integers */
    
             Since  structures  are  internally  represented  as  arrays  of
          "char", incrementing a pointer to a structure  will  advance  only
          one (1) byte in memory. To advance to the "next" instance  of  the
          structure, use:
    
                        ptr += sizeof(struct template);
    
             The INDEXING operator '[]' is not commutative  in  MICRO-C.  In
          other words 'array[index]' cannot be expressed as 'index[array]'.
    
             MICRO-C does  not  support  "complex"  declarations  which  use
          brackets '()' for other than function parameters. These  are  most
          often used in establishing pointers to functions:
                    int (*a)();     /* Pointer to function returning INT */
                    (*a)();         /* Call address in 'a' */
    
             Since MICRO-C allows you to call any value by following it with
          '()', you can get  the  desired  effect  in  the  above  case,  by
          declaring 'a' as a simple pointer to int, and calling it with  the
          same syntax:
                    int *a;         /* Pointer to INT */
                    (*a)();         /* Call address in 'a' */
    
             MICRO-C will not output external  declarations  to  the  output
          file  for  any  variables  or  functions  which  are  declared  as
          "extern", unless that symbol is actually  referenced  in  the  'C'
          source code. This prevents "extern" declarations in system  header
          files (such as "stdio.h") which are used as  prototypes  for  some
          library functions from causing those functions to be  loaded  into
          the  object  file.  Therefore,  any  "extern"  symbols  which  are
          referenced only by inline assembly code must be  declared  in  the
          assembly code, not by the MICRO-C "extern" statement.

    MICRO-C C-FLEA Compiler                                          Page: 26


             Unlike some  'C'  compilers,  MICRO-C  will  process  character
          expressions using only  BYTE  values.  Character  values  are  not
          promoted to INT unless there is  an  INT  value  involved  in  the
          expression. This results in much more efficent code  when  dealing
          with characters, particularily  on  small  processors  which  have
          limited 16 bit instructions. Consider the statement:
    
                                 return c + 1;
    
             On some compilers, this will sign extend the character variable
          'c' into an integer value, and then ADD an integer  1  and  return
          the  result.  MICRO-C  will  ADD  the  character  variable  and  a
          character 1, and then promote the result to INT  before  returning
          it (results of expressions as  operands  to  'return'  are  always
          promoted to int).
    
             Unfortunately, programs have been written  which  rely  on  the
          automatic promotion of characters to INTs to  work  properly.  The
          most common source of problems is code  which  attempts  to  treat
          CHAR variables as UNSIGNED values (many older  compilers  did  not
          support UNSIGNED CHAR). For example:
    
                                return c & 255;
    
             In a compiler which always evaluates character  expressions  as
          INT, the above statement will extract the value of 'c' as positive
          integer ranging from 0 to 255.
    
             In MICRO-C, ANDing a character with 255  results  in  the  same
          character, which gets promoted to an integer  value  ranging  from
          -128 to 127. To force the promotion  within  the  expression,  you
          could CAST the variable to an INT:
    
                              return (int)c & 255;
    
             The same objective can be achieved  in  a  more  efficent  (and
          correct) manner by declaring the variable 'c' as UNSIGNED CHAR, or
          by CASTing the variable to an UNSIGNED value:
    
                              return (unsigned)c;
    
             Note that this is not only more clearly shows the intent of the
          programmer, but also results is more efficent code generated.

    MICRO-C C-FLEA Compiler                                          Page: 27


             A related quirk arises because most processors do not support a
          simple efficent method for adding or subtracting a  SIGNED  8  bit
          quantity and a 16 bit quantity. The code generators supplied  with
          MICRO-C make the assumption that character values being  added  or
          subtracted to/from integers will contain only POSITIVE values, and
          thus use UNSIGNED  addition/subtraction.  This  allows  much  more
          efficent code to be generated, as the carry/borrow  from  the  low
          order byte of the operation is simply propagated to the high order
          byte of the result (an operation  supported  in  hardware  by  the
          CPU).
    
             For those rare instances where you do wish  to  add/subtract  a
          potentially negative character value to/from an int, you can force
          the expression to be performed  in  less  efficent  fully  16  bit
          arithmetic by casting the character to an int.
    
                int i;
                char c;
                ...
                i += c;         /* Very efficent... C should be positive */
                i += (int)c;    /* Less efficent... C can be negative */
    
             Read the notes at the end of the section  entitled  "Structures
          and Unions" for information on  limitations  or  differences  from
          standard 'C' in MICRO-C's implementation of structures and unions.

    MICRO-C C-FLEA Compiler                                          Page: 28


    4. ADVANCED TOPICS
    
          This section provides information on the more advanced aspects  of
       MICRO-C, which  is  generally  not  needed  for  casual  use  of  the
       language.
    
       4.1 Conversion Rules
    
             MICRO-C keep track of the "type" of  each  value  used  in  all
          expressions. This type identifies certain characteristics  of  the
          value,  such  as   size   range   (8/16   bits),   numeric   scope
          (signed/unsigned), reference (value/pointer) etc.
    
             When an  operation  is  performed  on  two  values  which  have
          identical "types", MICRO-C assigns that same "type" to the result.
    
             When the  two  value  "types"  involved  in  an  operation  are
          different, MICRO-C calculates the "type" of the result  using  the
          following rules:
    
          4.1.1 Size range
    
                If both values are  direct  (not  pointer)  references,  the
             result will be 8 bits only if  both  values  were  8  bits.  If
             either value was 16 bits, the result will be 16 bits.
    
                If one value is a pointer, and  the  other  is  direct,  the
             result will be a pointer to the same size value as the original
             pointer.
    
                If both values were pointers, the result will be  a  pointer
             to 16 bits only if both original  pointers  referenced  16  bit
             values. If either pointer referenced an 8 bit value, the result
             will reference an 8 bit value.
    
          4.1.2 Numeric Scope
    
                The result of an expression is considered to be signed  only
             if both original values were signed. If  either  value  was  an
             unsigned value, the result is unsigned.
    
          4.1.3 Reference
    
                If either of the original values was a pointer,  the  result
             will be a pointer.
    
             Note that this "calculated" result type  is  used  for  partial
          results within an expression. Whenever a symbol such as a variable
          or function is referenced, the type of that symbol is  taken  from
          its declaration, no matter what "type" of value  was  last  stored
          (variable) or returned (function).
    
             The TYPECAST  operation  may  be  used  to  override  the  type
          calculated for the result of an expression if necessary.

    MICRO-C C-FLEA Compiler                                          Page: 29


       4.2 Assembly Language Interface
    
             Assembly language programs may be called from 'C' functions and
          vice versa. These programs may be in the form of  inline  assembly
          language statements in the 'C' source code, or  separately  linked
          modules.
    
             INLINE code may use all virtual processor registers freely.
    
             Global variables defined in 'C' exist at absolute addresses and
          may be referenced directly by name from assembly language.  Global
          names which are referenced  by  both  assembly  language  and  'C'
          should not be longer than 15 characters.
    
             When MICRO-C calls any routine ('C'  or  assembler),  it  first
          pushes all arguments to the routine onto the processor  stack,  in
          the order in  which  they  occur  in  the  argument  list  to  the
          function. This means that the LAST argument  to  the  function  is
          LOWEST on the processor stack.
    
             Arguments are always pushed as 16 bit values. Character  values
          are extended to 16 bits, and arrays are passed as 16 bit  pointers
          to the array. (MICRO-C knows that arrays which are  arguments  are
          actually  pointers,  and  automatically  references  through   the
          pointer).
    
             After pushing the arguments, MICRO-C then generates  a  machine
          language subroutine  call,  thereby  executing  the  code  of  the
          routine.
    
             Once the called routine returns, the arguments are removed from
          the stack by the calling program.
    
             When the called function executes, the first thing usually done
          is to reserve space on the stack for any local variables which are
          required.

    MICRO-C C-FLEA Compiler                                          Page: 30


             It is the responsibility of the called function to  remove  any
          saved registers and local variable space from the stack before  it
          returns. If a value is to be returned to the calling  program,  it
          is expected to be in the 16 bit ACCUMULATOR.
    
             Local variables in a function may be referenced as offsets from
          the stack pointer. Note that offsets  must  be  adjusted  for  the
          number of additional bytes which are  pushed  and  popped  on  the
          stack during the execution of  the  function.  The  address  of  a
          particular local variable is calculated as:
    
                                "stack pointer"
                                       +
                   (# bytes pushed during function execution)
                                       +
               (size of all preceeding local variables in bytes)
    
             Arguments to a  function  may  also  be  referenced  as  direct
          offsets from the stack pointer, in much  the  same  way  as  local
          variables are. The address of a particular argument is  calculated
          as:
    
                                "stack pointer"
                                       +
                   (# bytes pushed during function execution)
                                       +
                     (size of all local variables in bytes)
                                       +
                     (Size of return address on stack (2))
                                       +
                      (# arguments from LAST argument) * 2
    
             If a function has been declared  as  "register",  MICRO-C  will
          load the accumulator with  the  number  of  arguments  which  were
          passed, each time the function is called. This allows the function
          to determine the location of the  first  argument,  which  may  be
          calculated as:
    
                                "stack pointer"
                                       +
                           (accumulator contents) * 2
                                       +
                   (# bytes pushed during function execution)
                                       +
                     (size of all local variables in bytes)
                                       +
                     (Size of return address on stack (2))
    
             Examine  the  supplied  library  functions,  as  well  as  code
          produced by the compiler to gain more insight into the  techniques
          of accessing local variables and arguments.

    MICRO-C C-FLEA Compiler                                          Page: 31


       4.3 Compiling for ROM
    
             The output from the compiler is entirely "clean",  and  may  be
          placed in Read Only Memory (ROM).
    
             The compiler places all initialized  global  variables  in  the
          output file as part of the code image. When the program is  stored
          in ROM, those variables are also stored in ROM, and  will  not  be
          modifiable.
    
             When the program is to be placed in ROM, you may not initialize
          any variables which you intend to modify  later.  Those  variables
          must be explicitly initialized by code executed at  the  beginning
          of the program.
    
             Variables which you do not intend to  modify  (such  as  tables
          etc.)  may  be  initialized  in  the  declaration,  and  will   be
          permanently saved in the ROM as part of the static code image.
    
             The addresses for code and data storage are established by  the
          startup files in the runtime library, You may examine  and  modify
          these files to suit your own particular memory allocation needs.

    MICRO-C C-FLEA Compiler                                          Page: 32


    5. THE MICRO-C COMPILER
    
          The heart of the MICRO-C programming environment is the  COMPILER.
       This program reads a  file  containing  a  'C'  source  program,  and
       translates it into an equivalent assembly language program.
    
          The compiler includes its  own  limited  pre-processor,  which  is
       suitable for  compiling  programs  requiring  only  non-parameterized
       MACRO substitution, simple INCLUDE file capability, and  single-level
       CONDITIONAL processing.
    
       5.1 The MCCCF command
    
             The format of the MICRO-C C-FLEA Compiler command line is:
    
                   MCCCF [input_file] [output_file] [options]
    
             [input_file] is the name of  the  source  file  containing  'C'
          statements to read. If no filenames are  given,  MCCCF  will  read
          from standard input.
    
             [output_file] is the name of the file to  which  the  generated
          assembly language code is written. If less than two filenames  are
          specified, MCCCF will write to standard output.
    
          5.1.1 Command Line Options
    
                -c      - Includes the 'C' source code in the output file
                          as assembly language comments.
    
                -f      - Causes the compiler to "Fold" its literal pool.
                          (Identical strings not contained in explicit
                          variables only once in memory).
    
                -l      - Enables MCCCF to accept line numbers.
                          (At beginning of line, followed by ':').
    
                -q      - Instructs MCCCF to be quiet, and not display the
                          startup message when it is executed.

    MICRO-C C-FLEA Compiler                                          Page: 33


    6. THE MICRO-C PREPROCESSOR
    
          The MICRO-C Preprocessor is a source code filter,  which  provides
       greater capabilities than the preprocessor which is integral  to  the
       MICRO-C compiler. It has been implemented as a  stand  alone  utility
       program which processes the source code before it is compiled.
    
          Due to the higher complexity of  this  preprocessor,  it  operates
       slightly slower than the the integral MICRO-C preprocessor.  This  is
       mainly due to the fact that it reads each line from the file and then
       copies it to a new line while performing the macro substitution. This
       is necessary since each macro may contain parameters  which  must  be
       replaced "on the fly" when it is referenced.
    
          The integral MICRO-C preprocessor is very FAST,  because  it  does
       not copy the input line. When it encounters a '#define'd  symbol,  it
       simply adjusts the input scanner pointer to point to  the  definition
       of that symbol.
    
          Keeping the extended preprocessor as a stand alone utility  allows
       you  to  choose  between  greater   MACRO   capability   and   faster
       compilation. It also allows the system to continue  to  run  on  very
       small hardware platforms.
    
          The additional capabilities of the extended preprocessor are:
    
            - Parameterized MACROs.
    
            - Multiple line MACRO's.
    
            - Nested conditionals.
    
            - Ability to undefine MACRO symbols.
    
            - Library reference in include file names.

    MICRO-C C-FLEA Compiler                                          Page: 34


       6.1 The MCP command
    
             The format of the MICRO-C Preprocessor command line is:
    
                    MCP [input_file] [output_file] [options]
    
             [input_file] is the name of  the  source  file  containing  'C'
          statements to read. If no filenames are given, MCP will read  from
          standard input.
    
             [output_file] is the name of the file to  which  the  processed
          source code is written. If less than two filenames are  specified,
          MCP will write to standard output.
    
          6.1.1 Command Line Options
    
                MCP accepts the following command line [options]:
    
                -c      - Instructs MCP to keep comments from  the input
                          file (except for those in '#' statements which
                          are always removed). Normally, MCP will remove
                          all comments.
    
                -l      - Causes the output file to contain line numbers.
                          Each line in the output file will be  prefixed
                          with the line number of the  originating  line
                          from the input file.
    
                l=path  - Defines the directory path which will be taken
                          to reference  "library"  files when  '<>'  are
                          used around an  '#include'  file name.  Unless
                          otherwise specified, the path defaults to:
                                        '\mc'
    
                -q      - Instructs MCP to be quiet, and not display the
                          startup message when it is executed.
    
          <name>=<text> - Pre-defines a non-parameterized macro  of  the
                          specified <name> with the string value <text>.

    MICRO-C C-FLEA Compiler                                          Page: 35


       6.2 Preprocesor Commands
    
             The following commands are recognized by the MCP utility,  only
          if they occur at the beginning of the source file line:
    
          6.2.1 #define <name>(parameters) <replacement text>
    
                Defines a global macro name which will be replaced with  the
             indicated <replacement text> wherever it occurs in  the  source
             file.
    
                Macro  names  may  be  any  length,  and  may  contain   the
             characters 'a'-'z', 'A'-'Z', '0'-'9' and '_'.  Names  must  not
             begin with the characters '0'-'9'.
    
                If the macro name is IMMEDIATELY followed by a list of up to
             10 parameter names contained in brackets, those parameter names
             will be substituted with parameters passed to the macro when it
             is referenced. Parameter names follow the same rules  as  macro
             names.
    
                     eg: #define min(a, b) (a < b ? a : b)
    
                If any spaces exist between the macro name and  the  opening
             '(', the macro will not be  parameterized,  and  all  following
             text (including '(' and ')') will be  entered  into  the  macro
             definition.
    
                If the very last character of a  macro  definition  line  is
             '\', MCP will continue the definition with the next  line  (The
             '\' is not included). Pre-processor statements included as part
             of a macro definition will not be processed by MCP, but will be
             passed on and handled by the integral MICRO-C preprocessor.
    
          6.2.2 #undef <symbol>
    
                Undefines the named macro symbol. further references to this
             symbol will not be replaced.
    
                NOTE: With MCP, macro definitions operate on a STACK. IE: If
             you define a macro  symbol,  and  then  re-define  it  (without
             '#undef'ing it first), subsequently '#undef'ing it  will  cause
             it to revert to its  previous  definition.  A  second  '#undef'
             would then cause it to be completely undefined.

    MICRO-C C-FLEA Compiler                                          Page: 36


          6.2.3 #forget <symbol>
    
                Similar  to  '#undef',  except  that  the  symbol  and   ALL
             SUBSEQUENTLY DEFINED SYMBOLS will be undefined.
    
                Useful for releasing any local symbols (used only  within  a
             single include file).
    
                For example:
    
                        #define GLOBAL "xxx"    /* first global symbol */
                            ...                 /* more globals */
                        #define LOCAL   "xxx"   /* first local symbol */
                            ...                 /* more locals */
                        /* body of include file goes here */
                        #forget LOCAL           /* release locals */
    
          6.2.4 #ifdef <symbol>
    
                Causes the following lines (up to '#else' of '#endif') to be
             processed and included in the source file  only  if  the  named
             symbol is defined as a macro.
    
          6.2.5 #ifndef <symbol>
    
                Causes the following lines (up to '#else' of '#endif') to be
             processed and included in the source file  only  if  the  named
             symbol is NOT defined as a macro.
    
                NOTE: '#ifdef/#ifndef#else/#endif' may be nested.
    
          6.2.6 #else
    
                Toggles the state of the "if_flag", controlling  conditional
             processing. Only has effect in the highest level  of  suspended
             processing. IE: Nested conditionals will work properly.
    
                If the previous  '#ifdef/#ifndef'  failed,  processing  will
             begin again following the '#else'.
    
                If the previous '#ifdef/#ifndef' passed, processing will  be
             suspended until the '#endif' is encountered.
    
                NOTE: Since '#else' acts as a toggle, it may be used outside
             of any '#ifdef/#ifndef' to unconditionally  suspend  processing
             up to '#endif'. You can also use multiple '#else's in a  single
             conditional,  to  swap  back  and  forth   between   true/false
             processing without re-testing the condition.
    
          6.2.7 #endif
    
                Resets  the  "if_flag"  controlling  conditionals,   causing
             processing to resume. Only has effect in the highest  level  of
             suspended  processing.  IE:  Nested  conditionals   will   work
             properly.

    MICRO-C C-FLEA Compiler                                          Page: 37


          6.2.8 #include <filename>
    
                Causes MCP to open the named file and include  its  contents
             as part of the input source.
    
                If the filename is contained within '"' characters, it  will
             be opened exactly as  specified,  and  (unless  it  contains  a
             directory path) will reference a file in the current directory.
    
                If the filename is contained within the characters  '<'  and
             '>', it will be  prefixed  with  the  library  path  (See  'l='
             option), and will therefore reference a file  in  that  library
             directory. The default  library  directory  is  assumed  to  be
             '\mc'.
    
                For example:
    
                        #include "header.h"     /* from current directory */
                        #include <stdio.h>      /* from library directory */

    MICRO-C C-FLEA Compiler                                          Page: 38


       6.3 Error messages
    
             When MCP detects an error during processing of an include file,
          it displays an error message, which is preceeded by  the  filename
          and line number where the error occurs. If more than 10 errors are
          encountered, MCP will terminate.
    
             The following error messages are reported by MCP:
    
          6.3.1 Cannot open include file
    
                A '#include' statement on the  indicated  line  specified  a
             file which could not be opened for reading.
    
          6.3.2 Invalid include file name
    
                A '#include' statement on the  indicated  line  specified  a
             file  name  which  was  not  contained  within  '"'   or   '<>'
             characters.
    
          6.3.3 Invalid macro name
    
                A '#define' statement on the indicated line contains a macro
             name which does not follow the name rules.
    
          6.3.4 Invalid macro parameter
    
                A '#define' statement on the indicated line contains a macro
             parameter name which does not follow the name rules.
    
                A reference to a macro does not have a proper ')'  character
             to terminate the parameter list.
    
          6.3.5 Too many errors
    
                More  than  10  errors  has  been  encountered  and  MCP  is
             terminating.
    
          6.3.6 Too many macro definitions
    
                MCP has encountered more '#define' statements  than  it  can
             handle.
    
          6.3.7 Too many macro parameters
    
                A '#define' statement on the indicated line  specifies  more
             parameters to the macro than MCP can handle.
    
          6.3.8 Too many include files
    
                MCP has encountered more nested '#include'  statements  than
             it can handle.

    MICRO-C C-FLEA Compiler                                          Page: 39


          6.3.9 Undefined macro
    
                A '#undef' or '#forget'  statement  on  the  indicated  line
             references a macro name which has not been defined.
    
          6.3.10 Unterminated comment
    
                The END OF FILE has  been  encountered  while  processing  a
             comment.
    
          6.3.11 Unterminated string
    
                A quoted string  on  the  indicated  line  has  no  end.  To
             continue a string to  the  next  line,  use  '\'  as  the  last
             character on the line. The '\' will  not  be  included  in  the
             string.

    MICRO-C C-FLEA Compiler                                          Page: 40


    7. THE MICRO-C OPTIMIZER
    
          The MICRO-C optimizer is an output code filter which examines  the
       assembly code produced by the compiler, recognizing known patterns of
       inefficent code (using the "peephole" technique), and  replaces  them
       with more optimal code  which  performs  the  same  function.  It  is
       entirely table driven, allowing it to be modified for  virtually  any
       processor.
    
          Due its many table lookup operations, the  optimizer  may  perform
       quite slowly when processing a large  file.  For  this  reason,  most
       people prefer not to optimize during the debugging of a program,  and
       utilize the optimizer only when creating the final copy.
    
       7.1 The MCOCF command
    
             The format of the MICRO-C Optimizer command line is:
    
                   MCOCF [input_file] [output_file] [options]
    
             [input_file] is the name of the source file containing assembly
          statements to read. If no filenames are  given,  MCOCF  will  read
          from standard input.
    
             [output_file] is the name of the file to  which  the  optimized
          assembly  code  is  written.  If  less  than  two  filenames   are
          specified, MCOCF will write to standard output.
    
          7.1.1 Command Line Options
    
                MCOCF accepts the following command line [options]:
    
                -d      - Instructs MCOCF to produce a 'debug' display on
                          standard output showing the  source code  which
                          it is removing and replacing in the input file.
                          NOTE: If you do not specify an  explict  output
                                file, you will get the  debug  statements
                                intermixed with  the  optimized  code  on
                                standard output.
    
                -q      - Instructs  MCOCF  to be quiet,  and not display
                          the startup message when it is executed.

    MICRO-C C-FLEA Compiler                                          Page: 41


    8. THE SOURCE LINKER
    
          Many small development environments have assemblers which  do  not
       directly support an object linker. This causes  a  problem  with  'C'
       development, because the library functions must be  included  in  the
       source code, with several drawbacks:
    
        1)  There is no way to automatically tell which library functions
            to include, therefore, you must do it manually.
    
        2)  'C' library functions must be  re-compiled every  time,  in
            order to avoid conflict between compiler generated labels.
    
          The MICRO-C Source Linker (SLINK) helps overcome  these  problems,
       by automatically  joining  previously  compiled  (assembly  language)
       source code from the library  to  your  programs.  Only  those  files
       containing functions which you  reference  are  joined  (Taking  into
       consideration functions called  by  the  included  library  functions
       etc...). As the files  are  joined,  compiler  generated  labels  are
       adjusted to be unique within each file.
    
       8.1 The SLINK Command
    
             The format of the SLINK command line is:
    
                   SLINK input_file... output_file [options]
    
             "input_file" is the name of  the  source  file  containing  the
          compiler output from your program.  Several  input  files  may  be
          specified, in which case they will all be processed into a  single
          output file.
    
             "output_file" is the name of  the  file  to  which  the  linked
          source code is written.

    MICRO-C C-FLEA Compiler                                          Page: 42


          8.1.1 Command line options
    
                SLINK accepts the following command line [options]:
    
                ?       - Display command line help summary.
    
                i=name  - Specify name of the External Index File.
    
                -l      - Instructs SLINK to list each library used.
    
                l=path  - Identifies the directory path which will be
                          taken to reference "library" files. If not
                          specified, it defaults to: '\mc\slib'
    
                p=char  - Identifies the PREFIX character of compiler
                          generated symbols. Defaults is '?'.
    
                -q      - Inhibit display of the startup message.
    
                t=string- Prefix to prepend to temporary filenames.
                          If not specified, default is "$".
    
                -w      - Sort WORD data to beginning of allocated bulk
                          unitialized storage (See $DD: directive).
    
       8.2 Multiple Input Files
    
             SLINK accepts multiple input files on  the  command  line,  and
          processes each file to build the output file. This allows  you  to
          "link" together several previously compiled (or assembly language)
          modules into one final program.
    
             Any external references  which  are  not  resolvable  from  the
          library are assumed to be resolved by  one  of  the  input  source
          files. Since SLINK does not have knowledge of the  public  symbols
          defined  in  the  input  files,  the  absence  of  an   externally
          referenced symbol will not be detected  until  the  assembly  step
          (where it will cause an undefined symbol error).

    MICRO-C C-FLEA Compiler                                          Page: 43


       8.3 The External Index File
    
             SLINK uses a special file from the library to  determine  which
          symbols are in which files. This  files  is  called  the  EXTERNAL
          INDEX FILE, and is  found  in  the  library  directory  (see  'l='
          option), under the name "EXTINDEX.LIB".
    
             This  file  contains  entries  which  cross-reference  external
          symbols to files. Each entry is as follows:
    
            1)  Any lines beginning with '<' contain the names of files
                which are to be processed and included at the BEGINNING
                of the program (Before your source file). This the best
                way to include the startup code and any runtime library
                routines which are required  at  all  times,  and  also
                provides a method of initializing any segments used.
                    eg: <6809rl.asm
    
            2)  Any lines beginning with '^' contain the names of files
                which are to be processed AFTER the program and library
                source files, but BEFORE any  uninitialized  data areas
                are output. This is the best way to set up the location
                and storage class of the uninitialized data  if it does
                not immediately follow the executable program code, and
                also providing any postamble needed by the segments.
    
            3)  Any lines beginning with '>' contain the names of files
                which are to be processed at the END  of  the  program,
                after all other information is output. This is the best
                way to define heap memory storage,  and  to provide any
                post-amble needed by the assembler.
    
            4)  Any lines beginning with '-' contain the names of files
                which are to  be  included  if  any  of  the  following
                symbols  (Up to another '<', '^', '>', '-' or '$')  are
                referenced.
                    eg: -printf.asm format.asm fgets.asm fget.asm
    
                NOTE: In most cases, the library functions will contain
                indications of any external references that they do, in
                which case SLINK will automatically include those files
                even of the names are not mentioned on the '-' line. In
                the example above, the following would suffice:
                        -printf.asm
    
            5)  The names  of  each  symbol  which  may  be  referenced
                externally must follow the '<', '^', '>' or  '-' entry.
                Symbols must occur one per line,  with  no  leading  or
                trailing spaces.
                    eg: printf
                        fprintf
                        sprintf

    MICRO-C C-FLEA Compiler                                          Page: 44


            6)  A line beginning with '$' is used to define the pseudo-
                opcode used by SLINK to reserve uninitialized  data  at
                the end of the output file.  Only  one  line  beginning
                with '$' should be entered into the EXTINDEX.LIB  file.
                The remainder of this line, including all  spaces  etc.
                is entered between each symbol name,  and  the  decimal
                size (in bytes) which is written to the output file.
                    eg: '$ RMB '    <- Quotes are for clarity
    
            A complete example:
    
                    -printf.asm
                    printf
                    fprintf
                    sprintf
                    -scanf.asm
                    scanf
                    fscanf
                    sscanf
                    <PREFIX.asm
                    ^MIDDLE.ASM
                    >SUFFIX.ASM
                    $ RMB
    
            In summary, the output file is written from:
    
                1 - The '<' (prefix) files              *
                2 - The program source files            *\
                3 - Library files referenced (if any)   * > See note
                4 - Segments 1-9 from above ...         */
                5 - The '^' (middle) files
                6 - Segments 1-9 from middle files      * See note
                7 - Uninitialized data definitions      (if any)
                8 - The '>' (suffix) files
                9 - Segments 1-9 from sufix file(s)     * See note
    
            * NOTE: If these files contain multiple segments (see later),
                    all segments are grouped and written  in  seguential
                    order. IE: Seg 0 from all files is written, followed
                    by Seg 1, etc.

    MICRO-C C-FLEA Compiler                                          Page: 45


       8.4 Source file information
    
          8.4.1 SLINK Directives
    
                SLINK interpretes several "directives" which may be inserted
             in the  input  source  files  to  control  the  source  linking
             process. These directives must be on a separate line, beginning
             in column 1, and must be in  uppercase.  They  are  removed  by
             SLINK during processing, and thus will not cause conflict  with
             the normal syntax used by the assembler.
    
                                   $SE:<0-9>
    
                The '$SE' directive is used  by  SLINK  to  define  multiple
             output segments. Up to 10 segments are allowed, with segment  0
             being the default which  is  selected  when  a  file  is  first
             encountered.  Other  segments  (1-9)  when  selected  via  this
             directive are written to temporary files, and re-joined at  the
             end of processing in  sequential  order.  this  allows  you  to
             separate sections of the source file (such as initialized data,
             literal pool etc.) into distinct areas of memory.
    
                              $DD:<symbol> <size>
    
                The '$DD' directive is used  to  define  uninitialized  data
             storage areas, which will be allocated by SLINK between the '^'
             (middle) and '>' (suffix) files. This allows  you  to  allocate
             unitialized data outside of the bounds of the executable image,
             and thus exclude it from being saved to disk. This  action  may
             be thought  of  as  an  additional  (11'th)  segment  which  is
             available for uninitialized data only,  and  which  avoids  the
             temporary file read/write overhead associated with use  of  the
             other segments. This directive  is  normally  placed  into  the
             source file by the "def_global" routine  in  the  MICRO-C  code
             generator.
    
                                  $EX:<symbol>
    
                The '$EX' directuve is used by SLINK to identify any symbols
             which are externally referenced. Whenever a '$EX' directive  is
             found, SLINK  searches  the  EXTINDX.LIB  file  for  the  named
             symbol, and marks the corresponding files for inclusion in  the
             program. This directive is normally placed into the source file
             by the "def_extern" routine in the MICRO-C code generator.
    
                If you  are  writing  assembly  language  programs  for  the
             library, be sure to  include  "$SE:<0-9>"  directives  for  any
             segments you wish to access, "$DD:<symbol>  <size>"  directives
             for  any  uninitialized  data  you  wish   to   allocate,   and
             "$EX:<symbol>" directives for any symbols which you  externally
             reference. If you wish to place an assembly language comment on
             the same line, make sure it is separated from the remainder  of
             the directive by at least one space or tab character.

    MICRO-C C-FLEA Compiler                                          Page: 46


                Also, note that '<' (prefix) files may contain "$SE",  "$DD"
             and "$EX" directives, '^' (middle) files may contain "$SE"  and
             "$DD" but not "$EX", and '>' (suffix) files may  only  contains
             "$SE" directives. Basically, the rule is that "$EX"  cannot  be
             used after the libraries are included and "$DD" cannot be  used
             after the uninitialized data is output. Since  the  middle  and
             suffix files  are  ALWAYS  included,  simply  insure  that  all
             external references and data declarations needed by any of them
             are performed in the '<' (prefix) file.
    
          8.4.2 Compiler generated labels
    
                As it processes each source file, SLINK scans each line  for
             symbols which consist of the '?' character (See  'p='  option),
             followed by a number. If it finds such as symbol, it inserts  a
             two character sequence ranging from 'AA' to  'ZZ'  between  the
             '?', and the number. This sequence will be incremented for each
             source file processed,  and  thus  insures  that  the  compiler
             generated symbols will be unique for each file.
    
                If you  are  writing  assembly  language  programs  for  the
             library, you must be careful to  avoid  using  identical  local
             symbols in any of the library files, one way to do this  is  to
             use symbols which meet the above criteria.
    
       8.5 The SCONVERT command
    
             SCONVERT is a utility  which  assists  in  converting  existing
          assembly language  source  files  into  a  format  which  is  more
          suitable for use by the SLINK. Two main functions are performed:
    
          1) All comments are removed, and  all  spacing  is  reduced  to  a
             single space. This minimizes the size of the  file,  and  helps
             decrease linkage time.
    
          2) All symbols defined in the file which  are  not  identified  as
             "keep" symbols are converted to resemble the  MICRO-C  compiler
             generated symbols. This allows  SLINK  to  adjust  them  to  be
             unique within each source file.
    
             The format of the SCONVERT command line is:
    
    
                 SCONVERT [input_file] [output_file] [options]
    
             [input_file] is the name of  the  source  file  containing  the
          original assembly language program.  If  no  filenames  is  given,
          SCONVERT will read from standard input.
    
             [output_file] is the name of the file to  which  the  converted
          source code is written. If less  that  two  filenames  are  given,
          SCONVERT will write to standard output.

    MICRO-C C-FLEA Compiler                                          Page: 47


          8.5.1 Command line options
    
                SCONVERT accepts the following command line [options]:
    
                ?       - Display command line help summary.
    
                c=char  - Identifies the character used to begin a comment
                          at the trailing end of a source line. If no 'c='
                          is defined, SCONVERT will terminate processing at
                          the first blank or tab which follows the operand
                          field.
    
                C=char  - Identifies the charcter which indicates a comment
                          line in the source code. Defaults to '*'.
    
                k=name  - Identifies a symbol name to KEEP. This symbol will
                          not be converted. Multiple 'k=' are permitted.
    
                K=file  - Identifies a file containing the names of symbols
                          to KEEP, one per line. Multiple 'K=' are permitted.
    
                p=char  - Identifies the PREFIX character which is to be used
                          for the converted symbols. Defaults to '?'.
    
                -q      - Instructs SCONVERT to be quiet, and not issue its
                          startup message.
    
                SCONVERT identifies symbols in the input source file as  any
             string beginning with 'A-Z', 'a-z', '_' or '?', and  containing
             these charcters plus the digits '0-9'. If your assembler source
             files uses any other characters in its symbols, you  must  edit
             your sources and change the symbols.
    
       8.6 The SRENUM command
    
             SRENUM  is  a  small  utility  which  re-numbers  the  compiler
          generated symbols within a assembly language source file. This  is
          useful if you have made added symbols to the  file  by  hand,  and
          wish to make it "pretty" before adding it to the library etc.
    
             The format of the SRENUM command is:
    
                  SRENUM [input_file] [output_file] [options]
    
          8.6.1 Command line options
    
                SRENUM accepts the following command line [options]:
    
                ?       - Display command line help summary.
    
                p=char  - Identifies the PREFIX character which is to be used
                          to recognize compiler generated symbols.
    
                -q      - Instructs SRENUM to be quiet, and not issue its
                          startup message.

    MICRO-C C-FLEA Compiler                                          Page: 48


       8.7 The SINDEX command
    
             SINDEX is a utility  which  assists  in  the  creation  of  the
          EXTINDEX.LIB file used by SLINK. When you run SINDEX, it  examines
          all of the '.ASM' files in the current  directory,  and  writes  a
          EXTINDEX.LIB file which contains a '-' type entry for  each  file,
          and  external  symbol  entries  for  any  labels  which  it  finds
          conforming to the 'C' naming conventions (Starts with 'a-z', 'A-Z'
          or '_', and contains only 'a-z', 'A-Z', '0-9' or '_').
    
             Once  you  have  run  SINDEX,  you  must  manually   edit   the
          EXTINDEX.LIB file, and remove any file or symbol entries which you
          do not wish to have available as external references, as  well  as
          insert any necessary entries for '<', '^', '>' and '$' commands.
    
          8.7.1 Command line options
    
                SINDEX accepts the following command line options:
    
                ?       - Display command line help summary.
    
                i=name  - Specify name for index file to be written.
                          Dafault is "EXTINDEX.LIB".
    
                You may also instruct SINDEX to search for  a  file  pattern
             other than '*.ASM' by passing it as a command line parameter.
    
                                eg: SINDEX *.ACF
    
       8.8 The SLIB command
    
             Once you have constructed your source  library,  you  may  from
          time to time want to make minor changes to it, either  adding  new
          functions, or removing old ones ones.
    
             You could make such changes simply by editing the  EXTINDEX.LIB
          file, however you would have to be very  careful  not  to  add  or
          delete the wrong entry, and you would have to  manually  determine
          if adding or removing the file would adversly affect the remainder
          of the library. For example, you could accidently add a  duplicate
          of another symbol name, or remove a symbol which is referred to by
          another file.
    
             To simplify maintenance of source libraries, you can  make  use
          of the "Source Librarian", a utility program which  automates  the
          addition and removal of source files, and automatically reports of
          any inconsistancies occuring in the source library.
    
             To use SLIB, you must first position yourself to the  directory
          containing the source library. And then  execute  SLIB  using  the
          command options described later to indicate the action to be taken
          on the library. If you do  not  specify  any  actions,  SLIB  will
          simply examine the library and report its size and content.

    MICRO-C C-FLEA Compiler                                          Page: 49


             You may use multiple command options in a single  SLIB  command
          if you wish to add and/or remove more than one file at a time.
    
             After  executing  any  command,  SLIB  will   report   on   any
          inconsistancies which it finds in the library. If any  are  found,
          and you have used a command which caused changes, SLIB will prompt
          for permission before writing the updated library file.
    
          8.8.1 Command line options
    
                The following options control the action(s)  which  will  be
             performed by SLIB on the source library index file.
    
                ?       - Display command line help summary.
    
                ?=file  - Display information about named source file.
    
                a=file  - Add specified file as standard functions.
    
                i=index - Use the specified INDEX file, if not specified,
                          the filename 'EXTINDEX.LIB' is assumed.
    
                m=file  - Add named source file as a MIDDLE file.
    
                p=file  - Add named source file as a PREFIX file.
    
                -q      - Quiet mode: SLIB will not display informational
                          messages or ask for permission to update index.
    
                r=file  - Remove the named file from the index.
    
                s=file  - Add named source file as a SUFFIX file.
    
                -w      - Write inhibit:  SLIB will not write the updated
                          library index.  This is useful if you just want
                          to see what would happen if you add or remove a
                          file.

    MICRO-C C-FLEA Compiler                                          Page: 50


       8.9 Making a source library
    
             To make a complete source linkable library, follow these  basic
          steps:
    
          1) If you have assembly language library functions, run the SINDEX
             utility to create an index file with the names of  any  symbols
             defined in them. Edit this file and remove all names which  are
             LOCAL to the files. Only the global function and variable names
             should remain. NOTE: Also leave in any other symbols  or  names
             which you don't want changed by SCONVERT.
    
          2) Use SCONVERT to convert  the  assembly  language  sources  into
             library format, using the index file created above as your KEEP
             file (K=EXTINDEX.LIB). You may send the output  files  directly
             to your source library directory.
    
          3) Edit the converted assembly  language  sources  to  change  any
             declarations for uninitialized data into '$DD' directives,  and
             to add any '$SE' and '$EX' directives which may be needed.
    
          4) Compile all of your 'C' library functions to assembly language,
             using a code generator which outputs the appropriate directives
             for SLINK. Send the ASM output files  to  your  source  library
             directory.
    
          5) From within your library  directory,  run  the  SINDEX  utility
             again. This will create  an  index  file  (EXTINDEX.LIB)  which
             contains the names of all global symbols.
    
          6) Edit the index file and remove any non-public symbol names. You
             should also change the headers for the '<', '^' and '>'  files,
             and add the '$' record for reserved memory information.
    
          7) Run the SLIB utility, to check the new  library  for  duplicate
             symbols,  unresolved  external   references   and   any   other
             inconsistancies.

    MICRO-C C-FLEA Compiler                                          Page: 51


    9. THE MAKE UTILITY
    
          The MAKE utility provides a method of automating the  building  of
       larger programs consisting of more that one module. The main  benefit
       of MAKE is that it keeps track of  the  files  that  each  module  is
       dependant on, and will rebuild a module if any of  those  files  have
       been modified since  the  module  was  last  built.  This  frees  the
       programmer from  the  task  of  remembering  which  files  have  been
       changed, and the commands needed to rebuild the dependant modules.
    
       9.1 MAKEfiles
    
             To use MAKE, you must first create a MAKEFILE, which is a  text
          file containing entries for each module in the program. Each entry
          consists of a DEPENDANCY list, and a series of COMMANDS.
    
          9.1.1 MAKEfile Entries
    
                A dependency list in MAKE is a line which contains the  name
             of the module, followed by a ':', followed by the names of  any
             files on which it depends. The module name MUST begin in column
             1.
    
                When MAKE is invoked, it will process each dependancy  list,
             and  will  execute  any  following  commands  (up  to   another
             dependancy list) if (1) the module does not exist,  or  (2)  if
             any of the files to the right of the ':' have a timestamp which
             is later than that of the module. For example:
    
                main.asm : main.c main.h \\mc\\stdio.h
                    \\mc\\mccCF main.c main.tmp
                    \\mc\\mcoCF main.tmp main.asm
                    -del main.tmp
    
                In the above example, the 'main.asm' would  be  rebuilt  (by
             compiling and optimizing 'main.c') if either it did not already
             exist, or any of 'main.c', 'main.h' or '\mc\stdio.h' was  found
             to have a later timestamp.
    
                The '-' preceeding the 'del' command prevents it from  being
             displayed. Unless the '-q' option is enabled, MAKE will display
             any commands not preceeded by '-' as they are executed.
    
                NOTE: To enter a single '\' in the MAKEFILE,  you  must  use
             '\\', this is because like 'C',  MAKE  uses  '\'  to  "protect"
             special  characters  which  otherwise  are  used  for   special
             functions (such as '\', '$' and '#'). The first '\'  "protects"
             the second one, allowing it to pass through as source text.

    MICRO-C C-FLEA Compiler                                          Page: 52


          9.1.2 Macro Substitutions
    
                Sometimes in a MAKEFILE, you have a single file or directory
             path that you use  over  and  over  again.  If  it  is  a  long
             directory path, this may  involve  a  lot  of  typing,  and  it
             becomes inconvenient to change that name (if you want to use  a
             different directory etc.) because it is repeated many times.
    
                MAKE includes a MACRO facility, which allows you  to  define
             variable names which will be replaced with a text  string  when
             used in subsequent MAKEfile lines. Names are defined by placing
             them in the MAKEfile, followed by '=',  and  the  text  string.
             Macro names being defined MUST begin in  column  one,  and  may
             consist of the characters ('a'-'z', 'A'-'Z', '0'-'9', and '_').
    
                Whenever MAKE encounters a '$' in the  file,  it  takes  the
             name immediately following, and performs the macro replacement:
    
                mcdir = \\mc
                main.asm : main.c main.h $mcdir\\stdio.h
                    $mcdir\\mccCF main.c main.tmp
                    $mcdir\\mcoCF main.tmp main.asm
                    del main.tmp
    
    
                When a macro name is immediately  followed  by  alphanumeric
             text, use a single '\' to  separate  it  from  the  text.  This
             "protects"  the  first  character  of  the  text   from   being
             interpreted as part of the macro name:
    
                mcdir = \\mc\\
                main.asm : main.c main.h $mcdir\stdio.h
                    $mcdir\mccCF main.c main.tmp
                    $mcdir\mcoCF main.tmp main.asm
                    del main.tmp
    
                There  are  several  predefined  macro  symbols  which   are
             available:
    
    
                $*      = The full name of the dependant module (name.type).
                $@      = The name only of the dependant module.
                $.      = The full name of each file in the dependancy list,
                          separated from each other by a single space.
                $,      = The full name of each file in the dependancy list,
                          separated from each other by a single comma.
                $:      = The name only of each file in the dependancy list,
                          separated from each other by a single space.
                $;      = The name only of each file in the dependancy list,
                          separated from each other by a single comma.

    MICRO-C C-FLEA Compiler                                          Page: 53


                File names in the dependancy list which are preceeded by '-'
             will not be included in the '$. $, $: $;' macro expansions:
    
                mcdir = \\mc
                main.asm : main.c -main.h -$mcdir\\stdio.h
                    $mcdir\\mccCF $. $@.TMP
                    $mcdir\\mcoCF $@.TMP $*
                    del $@.TMP
    
          9.1.3 MAKEfile Comments
    
                Whenever MAKE encounters the '#' character in the  MAKEFILE,
             it treats the remainder of the line as a comment, and does  not
             process it:
    
                # Define Directories
                mcdir = \\mc
    
                # Build the MAIN module
                main.asm : main.c -main.h -$mcdir\\stdio.h  # Dependants
                    $mcdir\\mccCF $. $@.TMP                 # Compile
                    $mcdir\\mcoCF $@.TMP $*                 # Optimize
                    del $@.TMP                              # Delete tmp
    
          9.1.4 Ordering the MAKEfile
    
                MAKE processes the MAKEfile is sequential fashion, with  the
             entries near the top being processed before  the  entries  near
             the bottom. To insure that each module is built  properly,  any
             files appearing in the dependancy list for a module  which  are
             themselves dependant  on  other  files,  should  have  MAKEfile
             entries which occur BEFORE the entries for  the  modules  which
             are dependant on them:
    
                # Define Directories
                mcdir = \\mc
                # Build the MAIN module
                main.asm : main.c -main.h -$mcdir\\stdio.h
                    $mcdir\\mccCF $. $@.TMP
                    $mcdir\\mcoCF $@.TMP $*
                    del $@.TMP
                # Build the SUB module
                sub.asm : sub.c -sub.h
                    $mcdir\\mccCF $. $@.TMP
                    $mcdir\\mcoCF $@.TMP $*
                    del $@.TMP
                # Link the final file & generate listing
                # NOTE: If either of the above modules is rebuilt,
                #       this entry will be guarenteed to execute.
                prog.hex : main.asm sub.asm
                    $mcdir\\slink $. $@.asm l=\mc\libCF
                    $mcdir\\asmCF $@ -fs

    MICRO-C C-FLEA Compiler                                          Page: 54


       9.2 Directives
    
             Like 'C', MAKE recognizes several "directives" in the MAKEfile.
          These  directives  are  only  recognized  if  they  occur  at  the
          beginning of the input line:
    
          9.2.1 @include <filename>
    
                This command causes the indicated file to be opened and read
             in as the source  text.  When  the  end  of  the  new  file  is
             encountered, processing will continue with the  line  following
             "@include" in the original MAKEfile.
    
          9.2.2 @ifdef <name> [name...]
    
                Processes the following lines (up to @else of  @endif)  only
             if one of the given MACRO names is defined. NOTE: <name> should
             not be preceeded by '$', otherwise its CONTENTS will be tested.
    
          9.2.3 @ifndef <name> [name...]
    
                Processes the following lines (up to @else of  @endif)  only
             if one of the given MACRO name is NOT defined.
    
          9.2.4 @ifeq <word1> <word2> [word3...]
    
                Processes the following lines (up to @else of  @endif)  only
             if the first word matches one of the remaining  words  exactly.
             This is useful for testing the value of a defined MACRO symbol.
    
          9.2.5 @ifne <word1> <word2>
    
                Processes the following lines (up to @else or  @endif)  only
             if the first word does not match any of the following words.
    
          9.2.6 @else
    
                Processes the following lines (up to  @endif)  only  if  the
             preceeding @ifdef, @ifndef, @ifeq or @ifne was false.
    
          9.2.7 @endif
    
                Terminates @ifdef, @ifndef, @ifeq and @ifne.
    
          9.2.8 @type <text>
    
                Displays the following text.
    
          9.2.9 @abort [text]
    
                Terminates MAKE with an 'Aborted!' message. Any text on  the
             remainder of the line will be appended to the message.

    MICRO-C C-FLEA Compiler                                          Page: 55


       9.3 The MAKE command
    
             The format of the MAKE command line is:
    
                           MAKE [makefile] [options]
    
             [makefile] is the name of the MAKEfile to process. If  no  name
          is given, MAKE assumes the default name 'MAKEFILE'.
    
          9.3.1 Command Line Options
    
                MAKE accepts the following command line [options]:
    
                ?       - Causes MAKE to output a short summary  of  the
                          available command line options.
    
                -d      - Instructs MAKE to operate in "debug" mode, and
                          display the commands which it  would  execute,
                          without actually executing them. This provides
                          a method of quickly testing the MAKEFILE.
    
                -q      - Instructs MAKE to be quiet, and not display the
                          informational messages and commands executed as
                          it progresses.
    
        <name>=<text>   - Pre-defines a macro  of  the  specified  <name>
                          with the string value  <text>.  This  OVERRIDES
                          any definition within the MAKEfile,  which  may
                          be used to establish a "default" value.

    MICRO-C C-FLEA Compiler                                          Page: 56


       9.4 The TOUCH command
    
             TOUCH is a small utility program which sets  the  timestamp  of
          one or more files to the current or  specified  time/date.  It  is
          useful as a  method  of  forcing  MAKE  to  recognize  a  file  as
          "changed", even when it has not.
    
             For example, if  you  had  decided  to  "undo"  several  recent
          changes by restoring a backup of 'main.c', the restored file  will
          probably have a timestamp which is  older  than  the  last  module
          which was built. In this case, MAKE would be unaware that the file
          has changed, and would therefore not rebuild the module.
    
             The TOUCH command could then be used to "update" the  timestamp
          of 'main.c' to the current time, causing MAKE to recognize it as a
          changed file.
    
                                  TOUCH main.c
    
             You could also use TOUCH to force rebuilding of several files:
    
                           TOUCH main.c sub1.c sub2.c
    
             Or even ALL '.C' files:
    
                                   TOUCH *.c
    
             TOUCH can also be used to set the timestamp of  a  file  to  an
          arbritrary value, this may be useful  to  PREVENT  a  change  from
          causing an update:
    
                         TOUCH main.c t=0:00 d=31/10/80
    
             NOTE: Use of the 't=' or 'd=' parameters to  TOUCH  allows  the
          possibility that a changed file  will  go  unnoticed.  CAUTION  is
          advised.
    
             The MSDOS  implementation  of  TOUCH  supports  '-h'  and  '-s'
          options, which cause it to set  the  timestamp  of  HIDDEN  and/or
          SYSTEM files. If these options are not used, TOUCH will not affect
          those types of files.

    MICRO-C C-FLEA Compiler                                          Page: 57


    10. EDT - Text editor
    
       10.1 Introduction
    
             EDT is a fully  featured,  in-memory,  text  editor,  which  is
          suitable for entry and editing of MICRO-C and ASM source programs.
          It operates in either a line-by-line, or a visual screen format.
    
             In line-by-line mode, EDT performs no direct  screen  accesses,
          and may be operated over a serial port using CTTY.
    
             EDT is invoked with the command 'EDT <filename>'. If the  named
          file already exists, EDT will load and edit it, otherwise a  blank
          file is presented. If the optional '-v'  qualifier  is  specified,
          EDT will start-up in line-by-line mode, otherwise it starts up  in
          visual mode.
    
                eg:     edt thefile.dat         <- Visual mode
                        edt myfile.dat -v       <- Line by Line
    
       10.2 Line mode operation
    
          10.2.1 Line ranges
    
                Most commands accept a "line-range"  which  is  an  optional
             specification controlling the range  of  lines  for  which  the
             command  has  effect.  Unless  otherwise  stated,  the  default
             line-range assumed for each command is the "current" line (*).
    
                The "current" line is the line at which EDT is positioned in
             line by line mode, and is also the line on which the cursor  is
             positioned in visual mode.
    
                The following are the valid line range formats:
    
                   *        - The "current" line
                   /        - The entire file
                   =        - The tagged lines
                   0        - The end of the file
                   <n>      - Line number <n>, (<n> >= 1)
                   <r>,<r>  - Range between beginning of two other ranges.
    
                The '+' and '-' characters may be used to add or subtract  a
             constant value from a line range.
    
                    eg: '0-12' <- 12 lines from end of file
    
                If '+' or '-' is used but no range is specified,  an  offset
             from the current line is assumed.
    
                  eg: '+12' <- 12 lines from the current line.
    
                The  line  range  specification   is   entered   immediately
             preceeding the command name.
    
                         ie: '<r><command> <operands>'

    MICRO-C C-FLEA Compiler                                          Page: 58


          10.2.2 Line mode commands
    
             C - Copy text
    
                   The 'C'opy command performs a copy of the active range of
                lines, placeing the copy directly ahead of the current line.
    
                Examples:
    
                    C               - Duplicate current line
                    1,10C           - Copy lines 1 to 10 inclusive
                    =C              - Copy tagged lines
                    /C              - Duplicate entire file (must be at end)
    
             D - Delete text
    
                   The 'D'elete command deletes the active range of lines.
    
                Examples:
    
                    D               - Delete current line
                    -5,+5D          - Delete 11 lines -5 to +5 from current
                    /D              - Delete entire file
    
             F - File information
    
                   This command displays information about  the  file  being
                edited, includes the filename, the size of the file in lines
                and characters, and the size and position of  the  specified
                line range.
    
                Examples:
    
                    F               - Display file & current line information
                    =F              - Display file & tagged lines information
    
             I - Insert new text
    
                   The 'I'nsert command prompts for  'Input:',  and  inserts
                all lines typed directly ahead of the active range. Enter  a
                null line to exit.
    
                Examples:
    
                    I               - Insert ahead of current line
                    /I              - Insert at start of file
                    0I              - Insert at end of file

    MICRO-C C-FLEA Compiler                                          Page: 59


             L - List text in simple form
    
                   The 'L'ist command displays the active  range  of  lines.
                The  display  does  not  include  line  numbers  or  special
                indications.  'L'ist  is  faster  and  mode  efficent   that
                'P'rint.
    
                Examples:
    
                    L               - List current line
                    /L              - List entire file
                    -10,+10L        - List 21 lines, centered on current
    
             M - Move text
    
                   The 'M'ove command moves the active range of lines to the
                location directly ahead of the current line.
    
                Examples:
    
                    =M              - Move tagged lines
                    +1M             - Interchange active & next line
    
             P - Print text (Enhanced 'L'ist)
    
                   The 'P'rint command displays the active range  of  lines.
                This display includes the line number which may be  preceded
                by a special indication flag ('*' for current line, '='  for
                tagged lines).
    
                Examples:
    
                    P               - Display current line
                    /P              - Display entire file
    
             Q - Quit (exit) editor
    
                   The 'Q'uit command exits the editor.  This  command  will
                not allow an exit if unsaved  changes  are  present  in  the
                file.
    
                Examples:
    
                    Q               - Quit editor
    
             QQ - Unconditional 'Q'uit
    
                   The 'QQ'uit command exits the editor unconditionaly.
    
                Examples:
    
                    QQ              - Quit unconditionaly.

    MICRO-C C-FLEA Compiler                                          Page: 60


             R <filename> - Read file
    
                   The 'R'ead command  reads  the  entire  contents  of  the
                specified file, and inserts it directly ahead of the  active
                range.
    
                Examples:
    
                    Rabc            - Insert file 'abc' at current
                    /Rabc           - Insert file 'abc' at start
                    0Rabc           - Append file 'abc' at end
    
             S<dc><search><dc><replace> - Substitute
    
                   The 'S'ubstitute command searches  the  active  range  of
                lines, and replaces all occurrances of the  string  <search>
                with the string <replace>. The <dc> delimiter character  may
                be any character not contained within the <search> string.
    
                Examples:
    
                    S'abc'def       - Change 'abc' to 'def' in current
                    /S'abc'def      - Change 'abc' to 'def' in entire file
                    =S'abc'def      - Change 'abc' to 'def' in tagged lines
    
             T - Tag lines
    
                   The  'T'ag  command  tags  the  active  range  of  lines,
                allowing them to be referred  to  by  '='  in  a  subsequent
                command range.
    
                Examples:
    
                    T               - Tag current line
                    1,10T           - Tag lines 1 to 10
                    *,+5T           - Tag six lines starting at current
    
             V - Switch Visual Mode
    
                   The 'V' command causes EDT to switch visual  modes.  This
                enters visual mode if EDT was previously  in  line  by  line
                mode, and enters line by line mode if previously  in  visual
                mode.
    
                Examples:
    
                    V               - Switch visual modes

    MICRO-C C-FLEA Compiler                                          Page: 61


             W [filename] - Write to file
    
                   The 'W' command writes the active range of lines  to  the
                named file, or to the original file edited  if  no  name  is
                specified. Use of this command also resets the FILE  CHANGED
                flag, allowing exit via 'q'.
    
                   The default line range assumed for 'W'rite is the  entire
                file.
    
                Examples:
    
                    W               - Write entire file
                    *W              - Write current line
                    Wabc            - Write entire file to 'abc'
                    =Wabc           - Write tagged lines to 'abc'
    
             X [filename] - Write file and eXit
    
                   This command behaves  exactly  as  the  'W'rite  command,
                followed immediatly by  a  'Q'uit  command.  It  provides  a
                shorthand way of saving your file and leaving the editor.
    
                Examples:
    
                    X               - Write file & exit
                    Xabc            - Write to 'abc' and exit
    
             ?<text> - Search for text
    
                   The '?' command  moves  the  active  line  to  the  first
                occurance of the specified string within the active range.
    
                   The default range assumed for '?' is one  character  past
                the current cursor position (in visual mode)  or  the  first
                character of the active line (In line by line mode), through
                to the end of the file.
    
                Examples:
    
                    ?string         - Find next occurance of "string"
                    /?string        - Find first occurance of "string"
    
             $<command> - Execute DOS command
    
                   The '$' command executes the specified DOS command.
    
                Examples:
    
                    $dir            - Execute 'dir' command

    MICRO-C C-FLEA Compiler                                          Page: 62


             <no command> - Goto line
    
                   If a line range is given  without  a  command,  EDT  will
                reposition the "current"  line  to  the  beginning  of  that
                range.
    
                Examples:
    
                    100             - Move to line 100
                    /               - Move to start of file
                    0               - Move to end of file
                    =               - Move to tagged line(s)
    
       10.3 Visual mode operation
    
             When in VISUAL mode, EDT presents  a  window  on  the  terminal
          screen which displays the contents  of  a  section  of  the  file.
          Editing of the file may be performed directly on  the  screen  via
          special function keys, and the screen is updated so that  you  see
          your changes as they are being performed.
    
             Any  control  characters  which  exist  in  the  file  will  be
          displayed as the  corresponding  printable  character  in  reverse
          video.
    
             If the end of the file is within the area shown on the  screen,
          the message '*EOF*' is displayed in reverse video.
    
          10.3.1 Entering text
    
                Text may be entered into the file being  edited,  simply  by
             typeing it at the terminal keyboard. EDT  automatically  places
             the text in the file, and updates the screen to reflect the new
             contents. The position of the  terminal  cursor  indicates  the
             position at which the text will be entered.
    
          10.3.2 Positioning the cursor
    
                The arrow keys on the terminal  may  be  used  to  move  the
             cursor around the displayed image. Moving beyond the bottom  of
             the screen causes EDT to scroll forward one line, and shift the
             screen up. Moving beyond the top of the screen  causes  EDT  to
             scroll backward one half screen, and redisplay the text.
    
                EDT will perform sideways scrolling of the display to  allow
             the cursor to access the entire width of lines which are larger
             than 80 columns.

    MICRO-C C-FLEA Compiler                                          Page: 63


          10.3.3 Visual mode function keys
    
                The following keys on  the  IBM  PC  keyboard  have  special
             meaning to EDT:
    
             Right arrow
    
                   Moves the cursor forward one  character  positon  in  the
                file, if at the end of a line, the cursor  will  advance  to
                the first position of the next line.
    
             Left arrow
    
                   Moves the cursor backward one character  positon  in  the
                file, if at the beginning of a line, the cursor will  backup
                to the last position of the previous line.
    
             Up arrow
    
                   Moves the cursor up one  line.  If  at  the  top  of  the
                screen, the display will scroll  backwards  by  one  half  a
                screen page.
    
             Down arrow
    
                   Moves the cursor down one line. If at the bottom  of  the
                screen, the display will scroll forward by one line.
    
                   The cursor may appear to jump back and  forth  as  it  is
                moved up and down, if it ancounters lines which are  shorter
                than the current character  position  within  the  line,  or
                lines which contain tabs. This is because whenever possible,
                the cursor is  returned  to  the  same  number  of  physical
                characters from the start of the line as is was on the first
                line from which the UP or DOWN arrow was pressed.
    
             Page up
    
                   This key pages backward one  screen.  (Top  line  becomes
                bottom)
    
             Page down
    
                   This key pages forward one screen. (Bottom  line  becomes
                top)
    
             Home
    
                   Moves the cursor to the beginning of the line. If  it  is
                already at the beginning of a  line,  it  is  moved  to  the
                beginning of the previous line.
    
             End
    
                   Moves the cursor to the end of the line.  If  already  at
                the end of a line, it is moved to the end of the next line.

    MICRO-C C-FLEA Compiler                                          Page: 64


             CTRL-PgUp
    
                   This key moves the cursor to the beginning of  the  first
                line in the file.
    
             CTRL-PgDn
    
                   This key moves the cursor to the end of the file.
    
             CTRL-Right Arrow
    
                   Moves the cursor to the beginning of the next word.
    
             CTRL-Left Arrow
    
                   Moves the cursor to the beginning of the previous word.
    
             Ins
    
                   Toggles between character INSERT and OVERWRITE  mode.  In
                INSERT mode,  all  characters  typed  at  the  terminal  are
                inserted into the text. In OVERWRITE mode, only the  NEWLINE
                character and data entered at the end of a line is inserted,
                all other characters will overwrite the existing text.
    
             Delete
    
                   Deletes the character under the  cursor,  without  moving
                the cursor.
    
             Backspace
    
                   Moves the cursor backward to the previous character, then
                deletes that character.
    
             CTRL-Home
    
                   Redraws the screen image of the file.  This  is  normally
                used in the case of  the  screen  being  corrupted  by  data
                transmission  errors,  or  asynchronus  messages  from   the
                operating system or its users.
    
             F1
    
                   Toggles ON/OFF the display of NEWLINE characters  at  the
                end of each line of text.
    
             F2
    
                   Displays  the  current  cursor  position,  including  the
                actual and character offsets from the start of line.
    
             F3
    
                   Brings the line the cursor  is  on  to  the  top  of  the
                screen.

    MICRO-C C-FLEA Compiler                                          Page: 65


             F4
    
                   Tags one or more lines for a later operation. The  tagged
                lines  are  displayed  in  special  video  if  the  terminal
                supports it. Once one line is tagged, pressing this  key  on
                another line causes all lines between  them  to  be  tagged.
                Pressing it again on the first  line  of  the  tagged  range
                removes the tags.
    
             F5
    
                   Deletes from the cursor position to the end of  the  line
                (inclusive).
    
             F6
    
                   Deletes from the cursor position to the end of  the  line
                (exclusive).
    
             F7
    
                   Inserts the deleted line text (From  Function  key  8  or
                Function key 9) at the current cursor position.
    
             F10 or Keypad '+'
    
                   Prompts for a line mode command, and executes it. See the
                section on line mode operation.
    
             F9 or Keypad '-'
    
                   Re-executes the last line mode command entered.

    MICRO-C C-FLEA Compiler                                          Page: 66


    
                      +----------------------------------+
                      |                                  |
                      |  ******************************  |
                      |  * The MICRO-C/C-FLEA library *  |
                      |  ******************************  |
                      |                                  |
                      +----------------------------------+
    
    
    
    
    
    
    
    
    
    
    11. The MICRO-C/C-FLEA Library
    
          The  library  functions  described  on  the  following  pages  are
       currently available in the MICRO-C library as "standard" functions.

    ABORT                                                             ABORT
    
    
    
    PROTOTYPE:
    
        abort(char *message)
    
    
    ARGUMENTS:
    
        message - Pointer to message to display
    
    
    RETURN VALUE:
    
        N/A - Function never returns
    
    
    DESCRIPTION:
    
          This function writes the string passed as an argument to  standard
       error, and then terminates the program. This provides a simple method
       of terminating a  program  on  an  error  condition  with  a  message
       explaining why.
    
    
    EXAMPLES:
    
        abort("Invalid operand\n");

    ABS                                                                 ABS
    
    
    
    PROTOTYPE:
    
        int abs(int number)
    
    
    ARGUMENTS:
    
        number  - Any integer value
    
    
    RETURN VALUE:
    
        The absolute value of "number"
    
    
    DESCRIPTION:
    
          The "abs" function returns the absolute value of the argument.  If
       "number" is a positive value, it is returned unchanged. If  negative,
       the negate of that value is returned (giving a positive result).
    
    
    EXAMPLES:
    
        difference = abs(value1 - value2);

    ATOI                                                               ATOI
    
    
    
    PROTOTYPE:
    
        int atoi(char *string)
    
    
    ARGUMENTS:
    
        string  - Pointer to a string containing a decimal number
    
    
    RETURN VALUE:
    
        16 bit integer value
    
    
    DESCRIPTION:
    
          The "atoi" function converts an ASCII string containing  a  signed
       decimal number (-32768 to 32767) to a 16 bit value which is returned.
       An unsigned number of the range (0 to 65535) may also  be  used,  and
       the result if assigned to an "unsigned" variable will be correct.
    
    
    EXAMPLES:
    
        value = atoi("1234");
        value = atoi("-1");

    CHKCH                                                             CHKCH
    
    
    
    PROTOTYPE:
    
        int chkch()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        0       - No character available from serial port.
        !0      - Character read from serial port.
    
    
    DESCRIPTION:
    
          The "chkch" function checks to see if a character is ready  to  be
       received from the console serial port. If no character is  available,
       a zero (0) is returned, otherwise the character is read and its value
       is  passed  back.  The  CARRIAGE  RETURN  character  (0x0D)  will  be
       translated into a NEWLINE (0x0A) for compatibility with 'C'.
    
    
    EXAMPLES:
    
        if(chkch() == 0x1B)     /* Escape KEY pressed ? */
            return;

    CHKCHR                                                           CHKCHR
    
    
    
    PROTOTYPE:
    
        int chkchr()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        0-255   - Character read from serial port.
        -1      - No character was available.
    
    
    DESCRIPTION:
    
          The "chkch" function checks to see if a character is ready  to  be
       received from the console serial port. If no character is  available,
       a -1 is returned, otherwise the character is read and its "raw" value
       is passed back (without translation).
    
    
    EXAMPLES:
    
        if(chkchr() == '\r')        /* Return KEY pressed ? */
            return;

    CONCAT                                                           CONCAT
    
    
    
    PROTOTYPE:
    
        register concat(char *dest, char *source, ...)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        source  - Pointer to source string
        ...     - Additional sources may be given
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "concat" function concatinates the given source  strings  into
       one destination string. The destination string must be  large  enough
       to hold all of the source strings plus the string  terminator  (zero)
       byte. No value is returned.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "stdio.h").
    
    
    EXAMPLES:
    
        concat(filename,"/tmp/", input_name);

    EXIT                                                               EXIT
    
    
    
    PROTOTYPE:
    
        exit()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        N/A - Function never returns
    
    
    DESCRIPTION:
    
          This function terminates the execution of the program, and returns
       control to the on-board monitor.
    
    
    EXAMPLES:
    
        exit();     /* Return to monitor */

    FREE                                                               FREE
    
    
    
    PROTOTYPE:
    
        free(char *ptr)
    
    
    ARGUMENTS:
    
        ptr     - Pointer to a previously allocated memory block
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "free" function releases (de-allocates) a block of memory that
       was obtained via a call to "malloc", and returns it to the heap. This
       makes it available for use by other memory allocations.
    
    
    EXAMPLES:
    
        if(!(ptr = malloc(BUFSIZ)))     /* Allocate a temporary buffer */
            abort("Not enough memory");
        /* ... Use the memory block ... */
        free(ptr);                      /* Release temporary buffer */

    GETCH                                                             GETCH
    
    
    
    PROTOTYPE:
    
        int getch()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        Value of a character read from the serial port.
    
    
    DESCRIPTION:
    
          This function reads a single character  from  the  console  serial
       port, and returns it as a positive value in the range of 0 to 255. If
       the character is a carriage  return  (0x0D),  is  translated  into  a
       NEWLINE (0x0A) for compatibility with 'C'.
    
    
    EXAMPLES:
    
        while(getch() != 0x1B);     /* Wait for an ESCAPE character */

    GETCHR                                                           GETCHR
    
    
    
    PROTOTYPE:
    
        int getchr()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        Value of a character read from the serial port.
    
    
    DESCRIPTION:
    
          This function reads a single character  from  the  console  serial
       port, and returns it as a positive value in the range of  0  to  255.
       The  character  is  read  in  "raw"  format,  with  no   translations
       performed.
    
    
    EXAMPLES:
    
        while(getchr() != '\r');        /* Wait for a RETURN */

    GETSTR                                                           GETSTR
    
    
    
    PROTOTYPE:
    
        char *getstr(char *buffer, int size)
    
    
    ARGUMENTS:
    
        buffer  - Pointer to string to receive line
        size    - Maximum size of line to read
    
    
    RETURN VALUE:
    
        The number of characters received into the line.
    
    
    DESCRIPTION:
    
          The "getstr" function reads a string of character from the  serial
       port and places them into the specified character buffer until either
       a NEWLINE character is encountered, or the limit of "size"  character
       is read.
    
          The string is terminated with the standard  NULL  (00)  character.
       The trailing NEWLINE '\n' character is NOT  included  in  the  output
       buffer.
    
          The BACKSPACE or DEL keys can be used to edit the input line.
    
    
    EXAMPLES:
    
        getstr(input_line, 80);

    INPx                                                               INPx
    
    
    
    PROTOTYPE:
    
        int inp1();
        int inp2();
        int inp3();
        int inp4();
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        8 bit value (0-255) read from the input port.
    
    
    DESCRIPTION:
    
          These functions read an 8 bit value from a parallel I/O port.
    
    
    EXAMPLES:
    
        if(inp1() & 0x01)
            outp2(inp2() | 0x01);

    ISALNUM                                                         ISALNUM
    
    
    
    PROTOTYPE:
    
        int isalnum(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is alphabetic or numeric
        0 if 'c' is not alphabetic or numeric
    
    
    DESCRIPTION:
    
          Returns  TRUE  (1)  if  the  passed  character  'c'  is  an  ASCII
       alphabetic letter in either upper or  lower  case  or  if  'c'  is  a
       numeric digit, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        while(isalnum(*ptr))        /* Copy over symbol name */
            *name++ = *ptr++;

    ISALPHA                                                         ISALPHA
    
    
    
    PROTOTYPE:
    
        int isalpha(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is alphabetic
        0 if 'c' is not alphabetic
    
    
    DESCRIPTION:
    
          Returns  TRUE  (1)  if  the  passed  character  'c'  is  an  ASCII
       alphabetic letter in either upper or lower case, otherwise FALSE  (0)
       is returned.
    
    
    EXAMPLES:
    
        flag = isalpha(input_char);

    ISASCII                                                         ISASCII
    
    
    
    PROTOTYPE:
    
        int isascii(int c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is an ASCII character
        0 if 'c' is not an ASCII character
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character  'c'  is  a  valid  ASCII
       character (0x00-0xFF), otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        if(!isascii(*ptr))
            abort("Invalid character data");

    ISCNTRL                                                         ISCNTRL
    
    
    
    PROTOTYPE:
    
        int iscntrl(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a "control" character
        0 if 'c' is not a "control" character
    
    
    DESCRIPTION:
    
          Returns TRUE (1) is the passed character 'c' is an ASCII "control"
       character (0x00-0x1F or 0x7F), otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        putch(iscntrl(c) ? '.' : c);    /* Display controls as '.' */

    ISDIGIT                                                         ISDIGIT
    
    
    
    PROTOTYPE:
    
        int isdigit(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is numeric
        0 if 'c' is not numeric
    
    
    DESCRIPTION:
    
          Returns TRUE (1) is the passed character 'c'  is  an  ASCII  digit
       ('0'-'9'), otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        value = 0;
        while(isdigit(*ptr))
            value = (value * 10) + (*ptr++ - '0');

    ISGRAPH                                                         ISGRAPH
    
    
    
    PROTOTYPE:
    
        int isgraph(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a non-space printable character
        0 if 'c' is a space or not printable
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character 'c' is a printable  ASCII
       character other than  a  space  character,  otherwise  FALSE  (0)  is
       returned.
    
    
    EXAMPLES:
    
        putch(isgraph(c) ? c : '.');

    ISLOWER                                                         ISLOWER
    
    
    
    PROTOTYPE:
    
        int islower(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is lower case alphabetic
        0 if 'c' is not lower case alphabetic
    
    
    DESCRIPTION:
    
          Returns  TRUE  (1)  if  the  passed  character  'c'  is  an  ASCII
       alphabetic letter of lower case, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        flag = islower(input_char);

    ISPRINT                                                         ISPRINT
    
    
    
    PROTOTYPE:
    
        int isprint(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a printable character
        0 if 'c' is not printable
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character 'c' is a printable  ASCII
       character, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        while(isprint(*ptr))
            ++ptr;

    ISPUNCT                                                         ISPUNCT
    
    
    
    PROTOTYPE:
    
        int ispunct(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a printable non-alphanumeric character
        0 if 'c' is not printable or alphanumeric
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character 'c' is a printable  ASCII
       character which is not a letter of the alphabet or a  numeric  digit,
       otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        while(ispunct(*ptr))
            ++ptr;

    ISSPACE                                                         ISSPACE
    
    
    
    PROTOTYPE:
    
        int isspace(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a space character (space, tab or newline)
        0 if 'c' is not a space character
    
    
    DESCRIPTION:
    
          Returns TRUE (1) if the passed character 'c' is one  of  a  space,
       tab or newline, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        while(isspace(*ptr))
            ++ptr;

    ISUPPER                                                         ISUPPER
    
    
    
    PROTOTYPE:
    
        int isupper(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is upper case alphabetic
        0 if 'c' is not upper case alphabetic
    
    
    DESCRIPTION:
    
          Returns  TRUE  (1)  if  the  passed  character  'c'  is  an  ASCII
       alphabetic letter of upper case, otherwise FALSE (0) is returned.
    
    
    EXAMPLES:
    
        flag = isupper(input_char);

    ISXDIGIT                                                       ISXDIGIT
    
    
    
    PROTOTYPE:
    
        int isxdigit(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        1 if 'c' is a hexidecimal digit
        0 if 'c' is not a hexidecimal digit
    
    
    DESCRIPTION:
    
          Returns TRUE (1) is the passed character 'c'  is  an  valid  ASCII
       hexidecimal digit ('0'-'9', 'A'-'F', 'a'-'f'), otherwise FALSE (0) is
       returned.
    
    
    EXAMPLES:
    
        value = 0;
        while(isxdigit(*ptr))
            value = (value * 16) +
                (isdigit(*ptr) ? *ptr++ - '0' : toupper(*ptr++) - ('A'-10));

    LONGJMP                                                         LONGJMP
    
    
    
    PROTOTYPE:
    
        longjmp(int savenv[2], int rvalue)
    
    
    ARGUMENTS:
    
        savenv  - Save area for program context
        rvalue  - Value to be returned by "setjmp"
    
    
    RETURN VALUE:
    
        N/A - Function never returns
    
    
    DESCRIPTION:
    
          The  "longjmp"  function  causes  execution  to  transfer  to  the
       "setjmp" call which  set  up  the  "savenv"  variable.  The  "setjmp"
       function will appear to return the value of "rvalue".
    
          NOTE-1: "longjmp" may  only  be  used  from  within  the  function
       calling "setjmp" or a function which has been called  "beneath"  that
       function. IT MUST NOT BE USED AFTER THE FUNCTION CALLING "SETJMP" HAS
       TERMINATED.
    
          NOTE-2: If "rvalue" is zero, the function  calling  "setjmp"  will
       assume that it is returning from initialization. Unless you want this
       unusual behavior, you should not pass  a  return  value  of  zero  to
       "longjmp".
    
          See also SETJMP.
    
    
    EXAMPLES:
    
        if(getch() == ('C'-'@'))        /* If Control-C entered... */
            longjmp(savearea, 1);       /* Return to main function */

    LONGMATH                                                       LONGMATH
    
    
    
    PROTOTYPES:
    
        int longadd(char *num1, char *num2);
        int longsub(char *num1, char *num2);
        longmul(char *num1, char *num2);
        longdiv(char *num1, char *num2);
        int longshr(char *num1);
        int longshl(char *num1);
        longcpy(char *num1, char *num2);
        longset(char *num1, unsigned value);
        int longtst(char *num1);
        int longcmp(char *num1, char *num2);
        extern char Longreg[];
    
    ARGUMENTS:
    
        num1    - First LONG operand, receives result if generated
        num2    - Second LONG operand, is not altered
        value   - 16 bit value to initialize LONG number
    
    
    RETURN VALUE:
    
        longadd - 0 = Ok, 1 = addition overflowed
        longsub - 0 = Ok, 1 = subtraction underflowed
        longshr - Carry out of shift (1/0)
        longshl - Carry out of shift (1/0)
        longtst - 0 = Number is zero, !0 = Number is not zero
        longcmp - 0 = (num1 == num2), 1 = (num1 > num2), -1 = (num1 < num2)
    
    
    DESCRIPTION:
    
          This set of functions performs basic arithmetic functions on  LONG
       numbers:
    
        longadd(num1, num2)     ->  num1 += num2
        longsub(num1, num2)     ->  num1 -= num2
        longmul(num1, num2)     ->  num1 *= num2 , Longreg = num1 * num2
        longdiv(num1, num2)     ->  num1 /= num2 , Longreg = num1 % num2
        longshr(num1)           ->  num1 >>= 1
        longshl(num1)           ->  num1 <<= 1
        longcpy(num1, num2)     ->  num1 = num2
        longset(num1, value)    ->  num1 = (long) value
        longtst(num1)           ->  Test (num1 != 0)
        longcmp(num1, num2)     ->  Compare num1 and num2
    
          As shipped, a LONG number is 32 bits (4 bytes)  in  size,  however
       this can be changed by altering the LONGMATH.ASM in the library.
    
          For a complete example of using  these  functions,  refer  to  the
       LONGCALC.C example program included with the package.

    MALLOC                                                           MALLOC
    
    
    
    PROTOTYPE:
    
        char *malloc(int size)
    
    
    ARGUMENTS:
    
        size    - Size of memory block to allocate (in bytes).
    
    
    RETURN VALUE:
    
        0       - Memory allocation failed
        !0      - Pointer to allocated memory block
    
    
    DESCRIPTION:
    
          The "malloc" function allocates a block of memory of the specified
       size from the heap, and returns a pointer to  it.  This  memory  will
       remain allocated until it is  explicitly  released  with  the  "free"
       function.
    
    
    EXAMPLES:
    
        if(!(ptr = malloc(BUFSIZ)))     /* Allocate a temporary buffer */
            abort("Not enough memory");
        /* ... Use the memory block ... */
        free(ptr);                      /* Release temporary buffer */

    MAX                                                                 MAX
    
    
    
    PROTOTYPE:
    
        int max(int value1, int value2)
    
    
    ARGUMENTS:
    
        value1  - Any integer value
        value2  - Any integer value
    
    
    RETURN VALUE:
    
        The greater of "value1" or "value2"
    
    
    DESCRIPTION:
    
          The "max" function returns the higher of its two argument values.
    
    
    EXAMPLES:
    
        biggest = max(a, b);

    MEMCPY                                                           MEMCPY
    
    
    
    PROTOTYPE:
    
        memcpy(char *dest, char *source, unsigned size)
    
    
    ARGUMENTS:
    
        dest    - Pointer to the destination
        source  - Pointer to the souce
        size    - Number of bytes to copy
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "memcpy" function will copy the specified number of bytes from
       the source to the destination.
    
    
    EXAMPLES:
    
        memcpy(buffer1, buffer2, 256);

    MEMSET                                                           MEMSET
    
    
    
    PROTOTYPE:
    
        memset(char *block, char value, unsigned size)
    
    
    ARGUMENTS:
    
        block   - Pointer to a block of memory
        value   - Value to initialize memory with
        size    - Number of bytes to initialize
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          Sets a block of memory  beginning  at  the  pointer  "block",  for
       "size" bytes to the byte value "value".
    
    
    EXAMPLES:
    
        memset(buffer, 0, 100);

    MIN                                                                 MIN
    
    
    
    PROTOTYPE:
    
        int min(int value1, int value2)
    
    
    ARGUMENTS:
    
        value1  - Any integer value
        value2  - Any integer value
    
    
    RETURN VALUE:
    
        The smaller of "value1" or "value2"
    
    
    DESCRIPTION:
    
          The "min" function returns the lower of its two argument values.
    
    
    EXAMPLES:
    
        least = min(a, b);

    NARGS                                                             NARGS
    
    
    
    PROTOTYPE:
    
        int nargs()
    
    
    ARGUMENTS:
    
        None
    
    
    RETURN VALUE:
    
        The number of arguments passed to the calling function
    
    
    DESCRIPTION:
    
          Returns the number of arguments passed to a "register" function.
    
          NOTE: When  calling  a  "register"  function,  MICRO-C  loads  the
       accumulator with the number of arguments just prior  to  calling  the
       function. This "nargs" routine is  simply  a  null  definition  which
       returns with the same value in the accumulator as was there  when  it
       was called. Therefore "nargs" MUST BE  THE  FIRST  ARITHMETIC  ENTITY
       EVALUATED WITHIN  THE  REGISTER  FUNCTION  or  the  contents  of  the
       accumulator will be lost. Some examples of "register" definitions and
       the use of "nargs" may be found in the library source code.
    
    
    EXAMPLES:
    
        first_arg = nargs() * 2 + &arguments;

    OUTPx                                                             OUTPx
    
    
    
    PROTOTYPE:
    
        outp1(char value);
        outp2(char value);
        outp3(char value);
        outp4(char value);
    
    
    ARGUMENTS:
    
        value   - 8 bit value to be written to port.
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          These functions write an 8 bit value to a parallel I/O port.
    
    
    EXAMPLES:
    
        if(inp1() & 0x01)
            outp2(inp2() | 0x01);

    PEEK                                                               PEEK
    
    
    
    PROTOTYPE:
    
        int peek(unsigned address)
    
    
    ARGUMENTS:
    
        address - 16 bit memory address
    
    
    RETURN VALUE:
    
        The 8 bit value read from the given memory address
    
    
    DESCRIPTION:
    
          The "peek" function reads and returns a byte (8 bits) from  memory
       as an integer value between 0 and 255.
    
    
    EXAMPLES:
    
        while(peek(0)); /* Wait for flag to clear */

    PEEKW                                                             PEEKW
    
    
    
    PROTOTYPE:
    
        int peekw(unsigned address)
    
    
    ARGUMENTS:
    
        address - 16 bit memory address
    
    
    RETURN VALUE:
    
        The 16 bit value read from the given memory address
    
    
    DESCRIPTION:
    
          The "peekw" function reads and  returns  a  word  (16  bits)  from
       memory as an integer value between 0 and 65535 (-1).
    
    
    EXAMPLES:
    
        var = peekw(0));

    POKE                                                               POKE
    
    
    
    PROTOTYPE:
    
        poke(unsigned address, char value)
    
    
    ARGUMENTS:
    
        address - 16 bit memory address
        value   - Value to be written to memory
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "poke" function writes a byte (8 bit) value to memory.
    
    
    EXAMPLES:
    
        poke(0, 0);     /* Write 0 to location 0 */

    POKEW                                                             POKEW
    
    
    
    PROTOTYPE:
    
        pokew(unsigned address, int value)
    
    
    ARGUMENTS:
    
        address - 16 bit memory address
        value   - Value to be written to memory
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "pokew" function writes a word (16 bit) value to memory.
    
    
    EXAMPLES:
    
        pokew(0, 0);    /* Write 0 to locations 0 and 1 */

    PRINTF                                                           PRINTF
    
    
    
    PROTOTYPE:
    
        register printf(char *format, arg, ...)
    
    
    ARGUMENTS:
    
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
    
          The "printf" function performs a formatted print to console serial
       port. The 'format' string is written to  the  serial  port  with  the
       arguments substituted  for  special  "conversion  characters".  These
       "conversion characters" are identified by a preceeding '%',  and  may
       be one of the following:
    
                    b       - Binary number
                    c       - Character
                    d       - Decimal (signed) number
                    o       - Octal number
                    s       - String
                    u       - Unsigned decimal number
                    x       - Hexidecimal number
                    %       - A single percent sign (No argument used)
    
          A numeric "field width" specifier may be placed in between the '%'
       and the conversion character, in which case the value will be  output
       in a field of that width. If the "field width" is a negative  number,
       the output will be left justified in the field, otherwise it is right
       justified. If the field width contains a leading '0', then the output
       field will be padded with zero's, otherwise spaces are used.
    
          If no "field width" is given, the output  is  free  format,  using
       only as much space as required.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "stdio.h").
    
    
    EXAMPLES:
    
        printf("Hello world!!!\n");
        printf("%u interrupts have occured!\n", int_count);

    PUTCH                                                             PUTCH
    
    
    
    PROTOTYPE:
    
        putch(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        None
    
    
    DECRIPTION:
    
          This function writes the character 'c' to the console serial port.
       The NEWLINE character is translated into a LINE-FEED, followed  by  a
       CARRIAGE return, which causes the printing position to advance to the
       first column of the next line.
    
    
    EXAMPLES:
    
        putch('*');
        putch('\n');

    PUTCHR                                                           PUTCHR
    
    
    
    PROTOTYPE:
    
        putchr(char c)
    
    
    ARGUMENTS:
    
        c       - Any character value
    
    
    RETURN VALUE:
    
        None
    
    
    DECRIPTION:
    
          This function writes the character 'c' to the console serial port.
       The character is written in "raw" format, with no translations of any
       kind.
    
    
    EXAMPLES:
    
        putchr('*');
        putchr('\r');

    PUTSTR                                                           PUTSTR
    
    
    
    PROTOTYPE:
    
        putstr(char *string)
    
    
    ARGUMENTS:
    
        string  - Pointer to a character string
    
    
    RETURN VALUE:
    
        0 if successful, otherwise an operating system error code
    
    
    DESCRIPTION:
    
          The "putstr" function writes the specified string  to  the  serial
       port. The zero terminating the string is NOT written.
    
    
    EXAMPLES:
    
        putstr("Text message");

    RAND                                                               RAND
    
    
    
    PROTOTYPE:
    
        unsigned rand(unsigned limit)
    
    
    ARGUMENTS:
    
        limit   - Maximum value to return
    
    
    RETURN VALUE:
    
        A pseudo-random number in the range of 0 to (limit-1)
    
    
    DESCRIPTION:
    
          The "rand" function calculates the next value of  a  pseudo-random
       sequence, based on a 16 bit unsigned "seed" value, which it maintains
       in the global variable "RANDSEED". The new value is stored as the new
       seed value, and is then divided by the "limit" parameter,  to  obtain
       the remainder, which is returned. This results in a random number  in
       the range of zero (0) to (limit - 1).
    
          Any  particular  sequence  may  be  repeated,  by   reseting   the
       "RANDSEED" value.
    
    
    EXAMPLES:
    
        value = rand(52);

    SETJMP                                                           SETJMP
    
    
    
    PROTOTYPE:
    
        int setjmp(int savenv[2])
    
    
    ARGUMENTS:
    
        savenv  - Save area for program context
    
    
    RETURN VALUE:
    
        0 is returned when actually called
        Value passed to "longjmp" is returned otherwise
    
    
    DESCRIPTION:
    
          When called, the "setjmp" function stores  the  current  execution
       state of the program into the passed integer array, and  returns  the
       value zero.
    
          The "longjmp" function may then be used to return the  program  to
       the "setjmp" call. In this case, the value returned by "setjmp"  will
       be the value which was passed to "longjmp". This allows the  function
       containing "setjmp" to determine which call to  "longjmp"  transfered
       execution to it.
    
          See also LONGJMP.
    
    
    EXAMPLES:
    
        switch(setjmp(savearea)) {
            case 0 : printf("Longjmp has been set up"); break;
            case 1 : printf("Control-C Interrupt");     break;
            case 2 : printf("Reset command executed");  break;
            default: printf("Software error trap");     break; }

    SPRINTF                                                         SPRINTF
    
    
    
    PROTOTYPE:
    
        register sprintf(char *dest, char *format, arg, ...)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        format  - Pointer to format string
        arg     - Argument as determined by format string
        ...     - Additional arguments may be required
    
    
    RETURN VALUE:
    
        None
    
    
    DESCRIPTION:
    
          The "sprintf" routine performs a formatted print to  a  string  in
       memory. The "format" string is written to the destination string with
       the arguments substituted for special "conversion characters".
    
          See "printf" for more information on format strings.
    
          NOTE: This function uses a variable number of arguments, and  must
       be declared as "register" (See "stdio.h").
    
    
    EXAMPLES:
    
        sprintf(header_file, "/lib/%s.h", header_name);

    SQRT                                                               SQRT
    
    
    
    PROTOTYPE:
    
        int sqrt(unsigned value)
    
    
    ARGUMENTS:
    
        value   - Number for which to calculate square root
    
    
    RETURN VALUE:
    
        The integer square root (rounded up) of the argument value
    
    
    DESCRIPTION:
    
          The  SQRT  function  returns  the  smallest  number   which   when
       multiplied by itself will give a number equal to or larger  that  the
       argument value.
    
    
    EXAMPLES:
    
    /*
     * Draw a circle about point (x, y) of radus (r)
     */
    circle(x, y, r)
        int x, y, r;
    {
        int i, j, k, rs, lj;
    
        rs = (lj = r)*r;
        for(i=0; i <= r; ++i) {
            j = k = sqrt(rs - (i*i));
            do {
                plot_xy(x+i, y+j);
                plot_xy(x+i, y-j);
                plot_xy(x-i, y+j);
                plot_xy(x-i, y-j); }
            while(++j < lj);
            lj = k; }
    }

    STRCAT                                                           STRCAT
    
    
    
    PROTOTYPE:
    
        char *strcat(char *dest, char *source)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        source  - Pointer to source string
    
    
    RETURN VALUE:
    
        Pointer to zero terminating destination string
    
    
    DESCRIPTION:
    
          This function concatinates the source string onto the tail of  the
       destination string. The destination string must be  large  enough  to
       hold the entire contents of both strings.
    
    
    EXAMPLES:
    
        strcat(program_name, ".c");

    STRCHR                                                           STRCHR
    
    
    
    PROTOTYPE:
    
        char *strchr(char *string, char chr)
    
    
    ARGUMENTS:
    
        string  - Pointer to a character string
        chr     - Character to look for
    
    
    RETURN VALUE:
    
        Pointer to the first occurance of 'chr' in 'string'
        Zero (0) if character was not found
    
    
    DECRIPTION:
    
          Searches  the  passed  string  got  the  first  occurance  of  the
       specified character. If the character is  found,  a  pointer  to  its
       position in the string is returned. If the character is not found,  a
       null pointer is returned.
    
          The null (0) character is treated as valid data by this  function,
       thus:
          strchr(string, 0);
    
       would return the position of the null terminator of the string.
    
    
    EXAMPLES:
    
        comma = strchr(buffer, ',');

    STRCMP                                                           STRCMP
    
    
    
    PROTOTYPE:
    
        int strcmp(char *string1, char *string2)
    
    
    ARGUMENTS:
    
        string1 - Pointer to first string
        string2 - Pointer to second string
    
    
    RETURN VALUE:
    
        0   - Strings match exactly
        1   - String1 is greater than string2
        -1  - String2 is greater than string1
    
    
    DESCRIPTION:
    
          This function compares two strings character by character. If  the
       two strings are identical, a zero  (0)  is  returned.  If  the  first
       string is greater than the second (as far as ASCII is  concerned),  a
       one (1) is returned. If the second string is greater, a negative  one
       (-1) is returned.
    
    
    EXAMPLES:
    
        if(!strcmp(command, "quit"))
            exit(0);

    STRCPY                                                           STRCPY
    
    
    
    PROTOTYPE:
    
        char *strcpy(char *dest, char *source)
    
    
    ARGUMENTS:
    
        dest    - Pointer to destination string
        souce   - Pointer to source string
    
    
    RETURN VALUE:
    
        Pointer to zero terminating destination string
    
    
    DESCRIPTION:
    
          This function copies the source string to the destination  string.
       All data is copied up to and including the zero byte which terminates
       the string. The destination string must be large enough to  hold  the
       entire source.
    
    
    EXAMPLES:
    
        strcpy(filename, argv[1]);

    STRLEN                                                           STRLEN
    
    
    
    PROTOTYPE:
    
        int strlen(char *string)
    
    
    ARGUMENTS:
    
        string  - Pointer to a character string
    
    
    RETURN VALUE:
    
        The length of the string
    
    
    DECRIPTION:
    
          Returns the length in character of the passed string.  The  length
       does not include the zero byte which terminates the string.
    
    
    EXAMPLES:
    
        length = strlen(command);

    TOLOWER                                                         TOLOWER
    
    
    
    PROTOTYPE:
    
        char tolower(char c)
    
    
    ARGUMENTS:
    
        c   - Any character value
    
    
    RETURN VALUE:
    
        The value of 'c', converted to lower case
    
    
    DESCRIPTION:
    
          Returns the value of 'c' converted to lower case. If 'c' is not  a
       letter of upper case, no change is made, and the  original  value  of
       'c' is returned.
    
    
    EXAMPLES:
    
        input_char = tolower(getch());

    TOUPPER                                                         TOUPPER
    
    
    
    PROTOTYPE:
    
        char toupper(char c)
    
    
    ARGUMENTS:
    
        c   - Any character value
    
    
    RETURN VALUE:
    
        The value of 'c', converted to upper case
    
    
    DESCRIPTION:
    
          Returns the value of 'c' converted to upper case. If 'c' is not  a
       letter of lower case, no change is made, and the  original  value  of
       'c' is returned.
    
    
    EXAMPLES:
    
        putch(toupper(output_char));




                            MICRO-C C-FLEA Compiler

                               TABLE OF CONTENTS


                                                                         Page

     1. INTRODUCTION                                                        1

        1.1 Memory configuration                                            1
        1.2 Code Portability                                                1
        1.3 The compiling process                                           2

     2. THE COMMAND CO-ORDINATOR                                            3

        2.1 The CCF command                                                 3

     3. THE MICRO-C PROGRAMMING LANGUAGE                                    5

        3.1 Constants                                                       5
        3.2 Symbols                                                         5
        3.3 Arrays & Pointers                                               9
        3.4 Functions                                                       9
        3.5 Structures & Unions                                            10
        3.6 Control Statements                                             13
        3.7 Expression Operators                                           15
        3.8 Inline Assembly Language                                       17
        3.9 Preprocessor Commands                                          18
        3.10 Error Messages                                                19
        3.11 Quirks                                                        24

     4. ADVANCED TOPICS                                                    28

        4.1 Conversion Rules                                               28
        4.2 Assembly Language Interface                                    29
        4.3 Compiling for ROM                                              31

     5. THE MICRO-C COMPILER                                               32

        5.1 The MCCCF command                                              32

     6. THE MICRO-C PREPROCESSOR                                           33

        6.1 The MCP command                                                34
        6.2 Preprocesor Commands                                           35
        6.3 Error messages                                                 38

     7. THE MICRO-C OPTIMIZER                                              40

        7.1 The MCOCF command                                              40

     8. THE SOURCE LINKER                                                  41

        8.1 The SLINK Command                                              41


    MICRO-C C-FLEA Compiler                                Table of Contents

                                                                         Page
        8.2 Multiple Input Files                                           42
        8.3 The External Index File                                        43
        8.4 Source file information                                        45
        8.5 The SCONVERT command                                           46
        8.6 The SRENUM command                                             47
        8.7 The SINDEX command                                             48
        8.8 The SLIB command                                               48
        8.9 Making a source library                                        50

     9. THE MAKE UTILITY                                                   51

        9.1 MAKEfiles                                                      51
        9.2 Directives                                                     54
        9.3 The MAKE command                                               55
        9.4 The TOUCH command                                              56

     10. EDT - Text editor                                                 57

        10.1 Introduction                                                  57
        10.2 Line mode operation                                           57
        10.3 Visual mode operation                                         62

     11. The MICRO-C/C-FLEA Library                                        66