.-------------------------------------------------------------------------.
|                                                                         |
|                       RPCXLib  version 1.0 (11/08/93)                   |
|                                                                         |
|                                                                         |
|                    (c) 1993  Rolf van Gelder, EINDHOVEN                 |
|                                                                         |
|_________________________________________________________________________|

1     INTRODUCTION --------------------------------------------------------


      RPCXLib is a CLIPPER LIBRARY with GRAPHIC FUNCTIONS.

      Because RPCXLib is fully written in ASSEMBLER its functions are
      VERY FAST !
      Therefore the library is also INDEPENDENT of the Clipper version and
      can be used in combination with Clipper Summer'87, Clipper 5.0,
      Clipper 5.01, Clipper 5.2x, etc.

      RPCXLib is the successor of the shareware function R_ShowPCX(),
      a function to show PCX-files on the screen.

      This function has been CONSIDERABLY IMPROVED and EXTENDED and is
      included in the new RPCXLib library. 

      RPCXLib is a Shareware product :

      You have the opportunity to try the program at no charge to see if
      it meets your needs.
      If you continue to use the program after evaluation,
      please complete the included registration form (RPCXLib.FRM)
      and send it with the applicable registration fee to the author.


      FEATURES :


      *    RShowPCX function to display a PCX graphic file :

           -     very FAST !

           -     of UNLIMITED SIZE

           -     on a SPECIFIC screen location

           -     on EGA/VGA and SUPERVGA screens

           -     up to a resolution of 640 x 480 x 256 (SUPERVGA)

           -     with AUTOMATIC DETECTION and USE of almost all
                 SUPERVGA adapters

           -     with support of the INTERNATIONAL VESA STANDARD

      *    Functions to mix ones own CLIPPER COLOURS
           YOU CAN COMPOSE 262.144 DIFFERENT COLOURS !

      *    Functions to slowly DIM the screen

      *    Functions to determine the GRAPHIC CONFIGURATION of a PC :
           Is there a EGA, VGA, MCGA or SUPERVGA adapter available ?
           When there is a SUPERVGA adapter available you can, in most
           cases, determine the brand

       *   A NORTON GUIDE with a description of all functions in the library



2     GRAPHIC ADAPTERS AND VIDEO MODES ------------------------------------


      The minimum requirements for using RPCXLib is a PC with an EGA card;
      CGA and Hercules adapters are not supported.

      To show PCX-files (using the function R_ShowPCX()) you can use
      EGA, VGA and SuperVGA adapters.

      EGA :
      When you have an EGA adapter you are able to show 16 colour PCX-files
      up to a dimension of 640 x 350 pixels.
      (Maximum resolution: 640 x 350 x 16)

      VGA :
      When you have a STANDARD VGA adapter you are able to show 16 colour
      PCX-files up to a dimension of 640 x 480 and 256 colour files up to
      a dimension of 320 x 200 pixels.
      (Maximum resolution: 640 x 480 x 16 or 320 x 200 x 256)

      SuperVGA :
      When you have a SUPERVGA adapter (which is supported by RPCXLib)
      you are able to show 256 colours PCX-files up to a dimension of
      640 x 480 pixels. Provided that the used adapter supports the
      640 x 480 x 256 video mode.
      (Maximum resolution: 640 x 480 x 256)

      RPCXLib detects and uses the following SuperVGA adapters :

      -    Ahead Systems, type A & B
      -    ATI Wonder Card
      -    Chips & Technologies
      -    Everex VGA
      -    Genoa GVGA
      -    NCR 77C22
      -    Oak Technologies OTI-67
      -    Paradise VGA
      -    Trident 8800
      -    Trident 8900
      -    Tseng Labs ET3000
      -    Tseng Labs ET4000
      -    VESA BIOS Extensions
      -    Video 7

      When your adapter is NOT listed above you probably still can use
      the SuperVGA features of RPCXLib.
      This can be done using the VESA BIOS EXTENSIONS driver.

      VESA (Video Electronics Standards Association) is a standardization
      in the field of graphic adapters.
      For almost any SuperVGA card there is a little (TSR) program that
      emulates the VESA standard. By using this program, RPCXLib will
      work together with your (not listed) SuperVGA adapter.
      The VESA emulation programs mentioned above are often included in
      the software package that comes with the SuperVGA card.
      When this is not the case you can probably find the program in the
      Public Domain / Shareware circuit.



3     EGA/VGA COLOUR PALETTES ----------------------------------------------


      In RPCXLib the are some functions to change the colour palette of your
      EGA/VGA adapter. You can use these functions to compose your own
      Clipper colour palette.

      Clipper uses 16 pre-defined colours. Each Clipper colour is paired with
      a so-called colour register. A colour register contains the "composition"
      of a specific colour. This composition consists of a RED, GREEN and BLUE
      component (values ranging from 0 to 63).
      Some examples (values actually used by Clipper) :

                       ------- Components  -------
                       RED        GREEN       BLUE

      BLACK            0          0           0
      BRIGHT WHITE     63         63          63
      NORMAL WHITE     42         42          42
      GREY             21         21          21
      BRIGHT RED       63         0           0
      RED              42         0           0
      GREEN            0          42          0
      BLUE             0          0           42
      MAGENTA          42         0           42

      The composition of the Clipper colours can be found in the header
      file (RPCXLib.CH).

      Clipper DOESN'T use register numbers 0-15 but :

      Registers #  0 -  7   : normal colours
      Registers # 56 - 63   : bright colours

      All Clipper colours and matching register numbers are listed in
      the header file RPCXLib.CH.

      Example :
      To determine the register number of the Clipper colour MAGENTA you
      can use the pre-defined PL_MAGENTA constant that substitutes the
      correct register number.

      The use of the palette functions is described in the next chapter.



4     FUNCTIONS IN RPCXLIB ------------------------------------------------

4.1   Function R_DefPal : Installs the default Clipper colour palette

      Syntax
           R_DefPal ()

      Parameters
           (None)

      Returns
           NIL

      Description
           By calling the R_DefPal () function the 16 Clipper colours are
           initialized to their default values. This function is for example
           useful at the end of an application : it makes sure that the
           the colour palette is reset to its original state (after possible
           changes you made to the palette).

      Example
           See the demo program PCXDemo.PRG


4.2   Function R_GetRGB : Determines the composition of a specific colour

      Syntax
           R_GetRGB ( nRegNr, @nRed, @nGreen, @nBlue )

      Parameters
           nRegNr      Number of the colour register of which the composition
                       has to be determined
                       (range : 0-63)

           @nRed       Variable (BY REFERENCE !) to which the RED component
                       is returned
                       (range : 0-63)

           @nGreen     Variable (BY REFERENCE !) to which the GREEN component
                       is returned
                       (range : 0-63)

           @nBlue      Variable (BY REFERENCE !) to which the BLUE component
                       is returned
                       (range : 0-63)

      Returns
           NIL         (The values are returned BY REFERENCE to the variables
                       nRed, nGreen and nBlue)

      Description
           R_GetRGB () determines the actual colour composition of a specific
           colour register. To determine the composition of the Clipper colours
           you may use the pre-defined register numbers in RPCXLib.CH.

      Example
           && Determine the components of the Clipper colour MAGENTA

           *-- RPCXLib definitions
           #include "RPCXLib.CH"

           LOCAL     nRed, nGreen, nBlue

           [...]

           R_GetRGB ( PL_MAGENTA, @nRed, @nGreen, @nBlue )

           ?'Magenta : RED ',nRed,' GREEN ',nGreen,' BLUE ',nBlue


4.3   Function R_IsEGA : Determines if an EGA card is present

      Syntax
           lIsEGA := R_IsEGA ()

      Parameters
           (None)

      Returns
           lIsEGA      .T. :      EGA card is present or can be emulated
                       .F. :      No EGA card present

      Description
           This function can determine if the PC supports EGA.
           That might be important for the function R_ShowPCX ().

      Example
           IF R_IsEGA ()
                 R_ShowPCX ( 'STANDEGA.PCX' )
                 [...]
           ELSE
                 Alert ( 'EGA adapter required to display this picture.' )

           ENDIF


4.4   Function R_IsMCGA : Determines if a MCGA card is present

      Syntax
           lIsMCGA := R_IsMCGA ()

      Parameters
           (None)

      Returns
           lIsMCGA     .T. :      MCGA card present or can be emulated
                       .F. :      No MCGA card present

      Description
           This function can determine if the PC supports MCGA.

      Example
           See PCXDemo.PRG


4.5   Function R_IsSVGA : Determines if a SuperVGA adapter is available

      Syntax
           lIsSVGA := R_IsSVGA ()

      Parameters
           (None)

      Returns
           lIsSVGA     .T. :      PC has a, by RPCXLib supported, SuperVGA
                                  adapter
                       .F. :      PC doesn't have a supported SuperVGA adapter

      Description
           This function determines if the PC has a SuperVGA adapter which
           is supported by RPCXLib.

      Example
           IF R_IsSVGA ()
                 R_ShowPCX ( 'SUPERPIC.PCX' )
                 [...]
           ELSE
                 IF R_IsVGA ()
                       R_ShowPCX ( 'STANDVGA.PCX' )
                       [...]
                 ELSEIF R_IsEGA ()
                       R_ShowPCX ( 'STANDEGA.PCX' )
                       [...]
                 ELSE
                       Alert ( 'Minimum requirement is an EGA adapter !' )

                 ENDIF
           ENDIF

      Remark
           This function is a pseudo function and is declared in RPCXLib.CH.


4.6   Function R_IsVGA : Determines if a VGA card is present

      Syntax
           lIsVGA := R_IsVGA ()

      Parameters
           (None)

      Returns
           lIsVGA      .T. :      VGA card is present or can be emulated
                       .F. :      No VGA card present

      Description
           This function can determine if the PC supports VGA.

      Example
           IF R_IsVGA ()
                 R_ShowPCX ( 'STANDVGA.PCX' )
                 [...]
           ELSE
                 Alert ( 'Minimum requirement is a VGA adapter !' )

           ENDIF


4.7   Function R_PCXInfo : Gets information of a specific PCX-file

      Syntax
           nRet :=
           R_PCXInfo ( cPCXFile, @nWidth, @nHeight, @nColors, @nAdapter )

      Parameters
           cPCXFile    Filespec of the PCX-file to be examined
                       Format  : [drive:][\path\]filename.PCX
                       Example : C:\PICTURES\TREE.PCX
                       The extension (.PCX) may not be omitted !

           @nWidth     Variable (BY REFERENCE !) to which the WIDTH of the
                       picture is returned

           @nHeight    Variable (BY REFERENCE !) to which the HEIGHT of the
                       picture is returned

           @nColors    Variable (BY REFERENCE !) to which the NUMBER OF COLOURS
                       of the picture is returned (16 or 256)

           @nAdapter   Variable (BY REFERENCE !) to which the CODE of the
                       REQUIRED ADAPTER is returned

                       These codes are defined in RPCXLib.CH :

                       1 = PL_EGA       EGA adapter required
                       2 = PL_VGA       Standard VGA adapter required
                       3 = PL_SVGA      SuperVGA adapter required

Returns
           nRet        Return code of R_PCXInfo()

                       The values and descriptions of this return code are
                       defined in RPCXLib.CH :

                       0 = PL_OKAY                  Okay
                       1 = PL_INVALID_PARAMETER     Invalid parameter passed
                       2 = PL_OPEN_PCX              Error opening PCX-file
                       3 = PL_READ_PCX              Error reading PCX-file
                       4 = PL_NO_PCXFILE            File is no valid
                                                    PCX-file
                       5 = PL_INVALID_BPP           Invalid number of
                                                    Bits-Per-Pixel

      Description
           Using the R_PCXInfo() function makes it possible to get information
           about a PCX-file before displaying it.
           For example you can see what kind of graphic adapter is needed
           to display the specific picture.

      Example
           See PCXDemo.PRG


4.8   Function R_RestPal : Restores a saved Clipper colour palette

      Syntax
           R_RestPal ( cPalet )

      Parameters
           cPalet      A 48 byte string with the 16 colours of the Clipper
                       colour palette (saved by de R_SavePal() function).

      Returns
           NIL

      Description
           With R_RestPal () a previously saved Clipper colour palette
           can be restored.

      Example
           See the R_SavePal () function


4.9   Function R_SavePal : Saves the actual Clipper colour palette to a string

      Syntax
           cPalet := R_SavePal ()

      Parameters
           (None)

      Returns
           cPalet      A 48 byte string with the actual values of the
                       16 Clipper colours

      Description
           With the R_SavePal () function you can save the actual values
           of the Clipper colours (temporarily) to a string.
           This saved palette can be restored using the R_RestPal () function.

      Example
           *-- RPCXLib definitions
           #include "RPCXLib.CH"

           LOCAL     cPalet := R_SavePal ()         && Save Clipper palette
           [...]

           && Change the Clipper MAGENTA-colour to another colour
           R_SetRGB ( PL_MAGENTA, 20, 43, 5 )
           [...]

           && Restore the previous saved Clipper palette
           R_RestPal ( cPalet )


4.10  Function R_SetRGB : Changes the composition of a specific colour

      Syntax
           R_SetRGB ( nRegNr, nRed, nGreen, nBlue )

      Parameters
           nRegNr      Number of the colour register to change
                       (range 0-63; codes are in RPCXLib.CH)

           nRed        Units RED to be used   (range : 0-63)

           nGreen      Units GREEN to be used (range : 0-63)

           nBlue       Units BLUE to be used  (range : 0-63)

      Returns
           NIL

      Description
           Function R_SetRGB makes it possible to define ones own 16 Clipper
           colours. They can be replaced by self mixed colours.
           There are 64 x 64 x 64 = 262.144 (!) possible colours so almost
           any desired colour can be composed and used in applications.

      Example
           && Replace the Clipper colour GREEN by a self mixed colour.
           && The new colour is composed of 5 units RED, 30 units GREEN
           && and 30 units BLUE

           *-- RPCXLib definitions
           #include "RPCXLib.CH"

           R_SetRGB ( PL_GREEN, 5, 30, 30 )

           A nice example of interactive mixing of colours can be found
           in RPCXDemo.PRG.


4.11  Function R_ShowPCX : Shows a PCX-file on EGA/VGA/SuperVGA screens

      Syntax
           nRet := R_ShowPCX ( cPCXFile [, nYPos [, nXPos [, cDriver ] ] ] )

      Parameters
           cPCXFile    Filespec of the PCX-file to be examined
                       Format  : [drive:][\path\]filename.PCX
                       Example : C:\PICTURES\TREE.PCX
                       The extension (.PCX) may not be omitted !

           nYPos       Vertical screen position of the upper left corner
                       of the display area (in pixels).
                       If omitted the picture will be CENTRED VERTICALLY.

           nXPos       Horizontal screen position of the upper left corner
                       of the display area (in pixels).
                       If omitted the picture will be CENTRED HORIZONTALLY.

           cDriver     Filespec of the RPCXLib SuperVGA driver file.
                       Format  : [drive:][\path\]filename.ext

                       When a picture should be displayed in SuperVGA mode
                       the function R_ShowPCX must be able to locate the
                       SuperVGA driver file.
                       This file is included in the RPCXLib package and is
                       called RPCXLib.GDR.

                       If the driver file is not located in the current
                       DOS-directory this parameter should be used to
                       indicate where the driver file can be found.

Returns
           nRet        Return code of R_ShowPCX()

                       The values and descriptions of this return code are
                       defined in RPCXLib.CH :

                        0 = PL_OKAY                 Okay
                        1 = PL_INVALID_PARAMETER    Invalid parameter passed
                        2 = PL_OPEN_PCX             Error opening PCX-file
                        3 = PL_READ_PCX             Error reading PCX-file
                        4 = PL_NO_PCXFILE           File is no valid
                                                    PCX-file
                        5 = PL_INVALID_BPP          Invalid number of
                                                    Bits-Per-Pixel
                        6 = PL_INVALID_DIM          PCX-file has invalid
                                                    dimensions (> 640 x 480)
                        7 = PL_UNKNOWN_SVGA         Unknown SuperVGA card
                        8 = PL_OPEN_DRIVER          Error OPENING RPCXLib.GDR
                                                    driver
                        9 = PL_READ_DRIVER          Error READING RPCXLib.GDR
                                                    driver
                       10 = PL_SVGA_NOTSUPPORTED    SuperVGA-card not
                                                    supported (yet)
                       11 = PL_BUFFER_MEMORY        Not enough memory
                                                    for internal buffer

      Description
           R_ShowPCX() displays a PCX-file on a specific screen location.
           This function is perfect to show Company Logo's, Graphs,
           Wallpapers etc.

           The function chooses the most suitable video mode depending
           on the dimensions and number of colours of the picture to show.
           When needed the appropriate SuperVGA driver is loaded
           automatically.

           The next scheme shows the relationship between the dimension of
           the picture and the adapter that will be used :


                                      PCX-file                     
                                         ³                          
                          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿           
                          ³                             ³           
                        16 colours                    256 colours       
                  ÚÄÄÄÄÄÄÄÁÄÄÄÄÄÄ¿              ÚÄÄÄÄÄÄÄÁÄÄÄÄÄÄ¿    
                  ³              ³              ³              ³    
           <= 640 x 350   <= 640 x 480   <= 320 x 200   <= 640 x 480
                 EGA            VGA            VGA         SuperVGA 

           After the picture is displayed the R_ShowPCX() returns to the
           calling program while leaving the picture on the screen (the
           graphic video remains active).
           The calling program should take further action : for example
           wait for a keypress (with the INKEY()-function). When a key
           is pressed by the user the original video mode (TEXTMODE) should
           be restored using the R_VMSet()-function.
           This principle is demonstrated in the following example.

      Example
           && Shows a PCX-file PICTURE.PCX on the screen
           && on position (y,x) = (10,50)

           *-- RPCXLib definitions
           #include "RPCXLib.CH"

           *-- Return code R_ShowPCX()
           LOCAL       nRet

           *-- Array with error messages
           LOCAL       aPCXErrors := PL_ERRMSG

           *-- Save the actual video mode
           LOCAL       nVidMode   := R_VMGet ()

           [...]

           nRet := R_ShowPCX ( 'PICTURE.PCX', 10, 50 )

           IF nRet = PL_OKAY
                 *-- Picture displayed, still on the screen

                 *-- Wait for a keypress ... (max 10 seconds)
                 Inkey ( 10 )

                 *-- Restore video mode
                 R_VMSet ( nVidMode )

           ELSE
                 *-- Oops, error while displaying the picture

                 *-- Display the error message
                 ALERT ( 'Error R_ShowPCX() : ' + aPCXErrors [nRet] )

           ENDIF

           && Continuation of the program
           [...]


           See for more detailed examples PCXDemo.PRG.


4.12  Function R_VGACard : Determines which SuperVGA adapter is present

      Syntax
           nSVGACard := R_VGACard ()

      Parameters
           (None)

      Returns
           nSVGACard   Code of the detected SuperVGA adapter.
                       These codes are defined in RPCXLib.CH.

      Description
           This function tries to determine which SuperVGA adapter is
           available in the PC.

      Example
           && Determines the SuperVGA adapter

           *-- RPCXLib definitions
           #include "RPCXLib.CH"

           *-- Code of SuperVGA adapter
           LOCAL       nSVGACard

           *-- Array with the names of the known SuperVGA adapters
           LOCAL       aSVGANames := PL_SVGA_NAMES

           nSVGACard := R_VGACard ()
           ? 'SuperVGA in this PC : ', aSVGANames [nSVGACard]


4.13  Function R_VMGet : Determines the actual video mode

      Syntax
           nVidMode := R_VMGet ()

      Parameters
           (None)

      Returns
           nVidMode    The actual video mode

      Description
           Determines which video mode is active at the moment.
           This function can be used in combination with R_ShowPCX().

      Example
           See the example of R_ShowPCX().


4.14  Function R_VMSet : Changes the actual video mode

      Syntax
           R_VMSet ( nVidMode )

      Parameters
           nVidMode    The video mode to be used

      Returns
           NIL

      Description
           Changes the actual video mode. This function can be used in
           combination with R_ShowPCX().

      Example
           See the example of R_ShowPCX().



5     REGISTRATION --------------------------------------------------------

      RPCXLib is a Shareware product. It is available through Users Groups,
      Bulletin Boards, etc.
      You have the opportunity to try the program at no charge to see
      if it meets your needs. If you continue to use the program after
      evaluation, please complete the included registration form
      (RPCXLib.FRM) and send it to:

                        Ing. R.P.B. van Gelder
                        Binnenwiertzstraat 27
                        5615 HG  EINDHOVEN
                        THE NETHERLANDS


      The price for registration is :

      If you want to receive the library by E-MAIL : US $ 15,00

      If you want to receive the library by POST   : US $ 20,00

      .---------------------------------------------------------------------.
      | REGISTERED USERS OF RSHOWPCX ONLY PAY THE EXTRA COSTS               |
      |                                                                     |
      | RECEPTION BY E-MAIL : $  5,00                                       |
      | RECEPTION BY POST   : $ 10,00                                       |
      |_____________________________________________________________________|

      Payment :

      Just include the appropriate amount of money (in cash) with the
      registration form and send it to the address as mentioned above.


5.1   BENEFITS OF REGISTRATION --------------------------------------------

      1) A registered version of RPCXLib will be sent to you by E-MAIL or
         by POST.

         .--------------------------------------------------------------.
         | THE REGISTERED VERSION DOESN'T DISPLAY THE REGISTRATION      |
         | MESSAGE AND DOESN'T HAVE THE 3 AND 8 SECONDS DELAYS.         |
         |______________________________________________________________|

      2) Run-time royalty-free license. You will be free to integrate
         RPCXLib functions into your Clipper applications without having
         to pay any royalty or fee for doing so. You may also distribute
         or market any such applications royalty-free.

      3) Support through E-Mail

         E-Mail addresses :

         Internet: RCROLF@urc.tue.nl
         Bitnet  : RCROLF@heitue5


5.2   USER GROUPS / SHAREWARE DISTRIBUTORS --------------------------------

      PC User Groups are welcome to add RShowPCX to their libraries under
      the following conditions :

      1) It must be completely unmodified

      2) A diskette/copying fee of $5 of less is charged; and

      3) This documentation file MUST be included.

      I would appreciate notification that you have added RPCXLib
      to your library.

      IF YOU RECEIVED RPCXLIB THROUGH EITHER A USER GROUP OR A SHAREWARE
      DISTRIBUTOR, PLEASE REMEMBER THAT THE DISKETTE FEE YOU PAYED DOES NOT
      CONSTITUTE LICENSING THE SOFTWARE, AND YOU ARE STILL OBLIGATED TO 
      REGISTER IF YOU DECIDE TO USE RPCXLIB.



6     DISCLAIMER ----------------------------------------------------------

      The copyright owner disclaims all warranties and is not liable for
      damages of any kind. By using RPCXLib you agree to this.