BYE-PC Resident Modem Driver
                           with
                       DOS Interface

              Manual Version 1.0 - February, 1987


























     This  document  describes  the operation of BYE-PC  and  the
application interfaces required to access functions that  control
modem  operations.  It  is  not intended as a reference  to  8086
assembly language or the 'C' programming language,  but serves to
provide a description of the operation and uses of BYE-PC.


                           by

                     MCODE Software
                    3444 Dresden Drive
                 Montgomery, Alabama, 36111
                      (205)244-7230








             Copyright (C) 1986, 1987 MCODE Software

     All  of  the  source code is copyrighted material  by  MCODE
Software.  The  author  retains  all rights to  the  source  code
provided in this package. This code may not be distributed in any
modified form without written or verbal consent from the  author.
Any  form of sale other than MCODE Software is  prohibited.  This
software  may  not  be offered for sale by any means or  form  to
others without written permission from MCODE Software.













                         DISCLAIMER

     The  author has taken great care to insure that this  manual
and  associated software provide accurate information in  regards
to the documentation and source code provided.  Any references to
particular  compilers,  linkers  or other development  tools  are
believed to be true by the author.  No warranty is made regarding
the  fitness  or validity of such material for any  circumstance.
Hardware  and  software compatibility is not guaranteed  for  any
particular  types of machines other than those mentioned in  this
manual.  This software has been tested extensively under specific
operating  environments and is believed to operate  as  described
within  this  manual.  In  no event will MCODE  software  or  the
authors  be held liable for damages of any kind,  in regard to or
arising  from the use of accompanying software or and  documenta
tion.  No  representation to the suitablity for this product  for
any use is made by the author.


     BYE-PC is a Tradmark of MCODE Software.  IBM, IBM PC, PC XT,
PC  AT,  DOS  and PCDOS are Tradmarks of  International  Business
Machines Corp.   Microsoft C,  MSDOS, ASM, and MASM are Tradmarks
of Microsoft Corp.  Hayes, Smartmodem, Smartmodem 300, Smartmodem
1200 are trademarks of Hayes Microcomputer Products Inc.  CP/M is
a tradmark of the Digital Research Corp.






                  TABLE OF CONTENTS


Introduction.........................................

Compiler Information.................................

Configuring BYE-PC for your system...................

BYE-PC Program Structure.............................

Interface to application programs....................

Caller status word...................................

Getting Started......................................

Program Operating structure..........................

Interface functions..................................

Compiling BYE.ASM Source Code........................

Telebit Trailblazer(tm) 9600bps high speed modem.....
.PA
                     INTRODUCTION


     Welcome  to BYE-PC!  Your support is greatly appreciated and
we sincerely thank you for using our product. It is our hope
that you will benifit and learn from the provided source code. If
you  are  an accomplished programmer and already  under-stand  the
operations  of  interrupt driven software,  please send  us  your
comments,   advice  or  any  other  suggestions  concerning  this
package.  We  hope that you will enjoy using this package as much
as  we have in providing it.  Contact us if you  are  having  any
problems  setting  up the system and we will try to  provide  you
with  an  answer or solution.  It is recommended  that  a  $30.00
donation  be  made  to the author if you use this  program  on  a
regular  basis.  Registered users will receive technical  support
only.  PLEASE  DON'T  BOTHER TO CALL IF YOU ARE NOT A  REGISTERED
USER!

     MCODE  Software  will  provide  all  registered  users  with
updates  for  an  unlimited period of time.  Users  that  request
updates will have to provide for any shipping and disk cost at  a
very minimal fee. Also, we plan to keep the latest copies of BYE-
PC  and  related  programs available for downloads at  any  time.
Please keep in touch with us via the Board Walk RBBS distribution
point in Montgomery,  Alabama at (205)277-3882 or write to us  at
MCODE  Software.  There are still many new features in the making
and  we  want you to receive the latest versions as soon  as  re
leased.


WHAT IS BYE-PC?

     BYE-PC  is a memory resident modem driver that is  interrupt
driven to provide fast reliable serial communications with  phone
modems.  BYE-PC  is  a  complete implementation of the  BYE  CP/M
version  offered  in  the  public domain for  use  on  eight  bit
systems.  The  CP/M implementation does not support rs232  driven
interrupts and is much slower than BYE-PC. BYE-PC allows for full
keyboard  type ahead from the remote station.  Characters may  be
received during other processes without polling the receive  port
for a data ready signal.

     Please  be  sure and read  the  supplementary  documentation
files that exsists.  These files contain important information on
recent updates that may have occured:

               READ.ME        ----      Latest modifications

Any recent modifications that occur since the last manual  publi
cation,  are contained in the file READ.ME.  Please read the copy
right notice and license agreement in the file COPYRGHT.BYE.
.PA
WHAT WILL BYE-PC DO?

     An  IBM  PC,  PC XT,  or PC AT host computer running  BYE-PC
allows a remote callers access to DOS. A series of interrupts are
overtaken  and/or chained that patch the modem i/o  signals  into
the  BIOS.  Since  DOS makes calls through the BIOS,  almost  any
program  that does not access the serial port or screen  directly
will run under BYE-PC. Although the large majority of programs do
not  adhere to these rules,  most programs that are well  behaved
and write to 'stdin' and 'stdout' will run properly under BYE-PC.
For instance,  DEBUG may run remotely to allow viewing the system
internally,  or file archive utilities such as ARC,  ZOO, etc...,
may be used.

    Once a caller has established a connection, BYE-PC allows the
option to execute a .COM or .EXE file.  This allows any number of
programs,  such  as bulletin boards,  to receive  control  before
allowing  users to enter DOS.  Since any DOS commands may be exe
cuted  while  running BYE-PC,  users  have  complete  control.  A
security shell is provided that parses all DOS commands prior  to
execution by COMMAND.COM. This allows selective commands to check
internal status before execution to eliminate unwanted  commands,
paths, drives or DOS functions.

     Currently  all  application programs that provide access  to
BYE-PC such as XMODEM,  CHAT,  STAT,  and RBBS, are created using
the Microsoft C compiler.   A standard interface is provided that
allows  C  programs  direct control  over  the  host  system.  An
application  may  disconnect,  check  status,  or  change  values
within BYE-PC through an additional software interrupt.  Assembly
language  routines  may  call  BYE-PC functions as  easily  as  C
applications through the system control interrupt (SCI).

     Since  all  data  is  received  from  hardware   interrupts,
characters are stored in a buffer within BYE-PC as each interrupt
occurs.  All  requests for data are made through the SCI and  the
provided  C  interface BYEXFACE.C.  These topics are  covered  in
greater detail in the following sections of this manual. Hardware
interrupts  occur  with changes of state in the  rs-232  serial
port  card.  In  the event of a carrier  loss,  an  interrupt  is
generated  that  warm  boots the system to prepare for  the  next
call.
.PA
                   COMPILER INFORMATION

     Currently, all of our assembly and C source code modules are
compiled  using Microsoft Compilers. We feel that these compilers
are  amoung  some  of the best available for the  PC  market  and
strongly  recommend their use with our packge.   We have not used
any  other  C compilers or assemblers available on the market  to
compile  our  code with.  Since the  C language  for  8086  based
machines varies so widely in its library extensions,  it would be
very difficult to adapt the code to all versions.

     Either  MASM or ASM may be used to compile BYE-PC  directly.
Once the .OBJ file is created,  LINK and EXE2BIN are then used to
create  the  resulting .COM file.  Version 3.0 or 4.0  of  the  C
compiler  will  compile  all C modules in any  of  the  available
memory models with without difficulties.  MASM is required on all
of the assembly modules used in conjuntion with C  programs.  The
file  MODEL.H contains the macros used to setup the C environment
needed  for  all  assembly language files.  If  you  develop  any
assembly source code,  we strongly recommend using MODEL.H in all
of the modules to set up the segments and pointers argument list.

     Any  C compiler that suports access to  software  interrupts
should  work with BYE-PC.  All modem i/o,  modem  control,  modem
status, and line control are performed through software interrupt
66h.  If your compiler supports this feature,  only the interface
functions  should  require  changes.   All  application  programs
provided in this package are device independant. All of the modem
functions are dependant upon BYEXLIBx.LIB to provide the  necces
sary  interface  functions.  These libraries contain all  of  the
functions needed to access BYE-PC functions within C programs.

     How to compile BYEx.xx.ASM:

          1) Compile .ASM source code using ASM

          2) Link using LINK to generate and .EXE file

          3) use EXE2BIN to convert to a .COM file

          4) delete the .EXE extension file

     Using MAKE:

            C>make bye {return}

     A  MAKE  file 'BYE' is provided to  automatically  link  the
object code and produce the .COM file.  This will also delete the
copy of the .EXE file since it is of no use.  Once the BYExxx.COM
file is generated,  rename it to BYE.COM and place it in the root
directory of the RBBS system disk.
.PA
               CONFIGURING BYE-PC FOR YOUR SYSTEM


     In  order  to run BYE-PC on your system you  will  need  the
appropriate modem and serial port for you system.  A standard DCE
configuration  port is required to the modem.  This port must  be
configured  for COM1 using IRQ4 or,  COM2 using IRQ3 respectivly.
Almost  all serial cards availble for PC's will be configured  in
this fashion at purchase and should not require altering.  If you
are not sure of you boards configuration, consult you serial port
manual and check the jumper locations on you board.

     A  Hayes Smartmodem(tm) with AT command sets is required  to
work  with  BYE-PC  or a manual modem such as  a  Universal  Data
Systems 212B.  If a manual modem is used, BYE-PC will monitor the
data  carrier detect (DCD) to determine when a call occurs.  Once
carrier is acknowledged,  BYE-PC will begin switching baud  rates
of  the port and looking for a sycronization character  (carriage
return or Ctrl-C). Smart modems return a result code that informs
BYE-PC of the baud rate currently on line.

     Configuring  BYE-PC  is  basically a matter of  setting  the
various equates in the source code file BYExx.x.ASM. All of these
equates are found after the title 'program configuration section'
of the source code file.  If you choose to execute a .COM or .EXE
file  upon receiving a valid carrier,  you will need to edit  the
path/file name at the end of the source code listing at the label
'child  name'.  You  may enter a full path/drive name  if  needed
here, however, make sure it not over 63 characters in length. The
following sections expains the various equate settings.

.PA
Selecting a COM port

     BYExx.x is configured to use COM1 on the distribution  disk.
However,  may  alter  this  to  COM2 by  changing  the  following
three equates:


     RS232_INT - This is used to select the interrupt  vector
                 location. COM1 uses interrupt vector 0Ch, while
                 COM2 requires interrupt location 0Bh.

     IRQ_BASE  - This is the interrupt request register base port
                 address. COM1 (IRQ4) uses i/o address 10h, while
                 COM2 (IRQ3) uses i/o port 08h.

     PORT_BASE - This is the 8255 serial i/o port base  address.
                 COM1 is at 03F8h, and COM2 is at address 02F8h



Selecting Modem Type

     If you are using a smart modem,  you will need to make  sure
the  equate SMART_MDM is set to YES.  The next three equates  are
used  to  describe  the highest baud rate  your  modem  supports.
Select ONE of the equates labeled BPS_300,  BPS_1200,  or BPS_2400
and  set it to YES.  If you wish to use BYE-PC with a high  speed
modem,   the   Telebit   Trailblazer(tm)   modem   will   support
transmission speed in excess of 18k bps with a maximum throughput
of  9600  baud.  If you have a Trailblazer,  set the TELEBIT  and
USE_RTS equates to YES.

The  Trailblazer(tm)  requires  handshaking via RTS  and  CTS  to
provide  flow control.  Since the possiblity exists for  data  to
overflow the receive queue,  handshaking is required for reliable
operation.  If  the  receive  data queue  becomes  full,  RTS  is
asserted  low until the receive data queue is 1/4th full  of  the
total queue size.  This allows BYE-PC to catch up with the  modem
receive data until it can accept more data.


Sending 'nulls' to Remote

     If you do not have a 2400bps modem,  you may want to disable
this feature.  If enabled, this will send the requested number of
nulls  (0 to 9) after a line feed is recevied.  This  feature  is
mainly a leftover from the teletype days, but it is still used by
high speed callers.  This allows the remote end to settle after a
line  feed  before  sending any other data on a new  line.


Executing a Program on Carrier Detect

     If  you wish to execute a program,  such as a bulletin board
service,  upon carrier detect,  set the LOGON_EXE equate to  YES.
You will have to set the drive/path/file name at the end very end
of the source code. The default value is "A:SYSTEM\XBBS\XBBS.EXE"
for the source code mailed out.  If LOGON_EXE is set to YES, BYE-
PC will attempt to execute this program from drive A:.  If it  is
not  found,   an  error  message  is  displayed  and  control  is
transferred to DOS.


Warm Booting After Local Execute

     The  equate NBOOT is used mainly for debugging  applications
that  run  under BYE-PC such as bulleting board system.  If  this
equate is set to YES,  BYE-PC will re-boot after pressing  Ctrl-C
and  running the LOGON_EXE file locally.  If NO,  BYE-PC will not
re-boot  but  cut off data sent to and from the modem  and  allow
entry into DOS.  This allows BYE-PC to remain resident,  but  not
send  or receive any data from the modem.  This is a very  useful
feature  for  debugging application programs that run under  XBBS
such  as  XBBS.  You may perform any operations  in  DOS,  except
loading  other  resident programs,  that you normally  use  while
creating  applications  to  run  under  BYE-PC   (i.e.   editing,
compiling, etc..).


Setting the Default Time Limit

     The  default time limit for callers initially is set for  60
minutes.  This  is  usually  set to by XBBS  or  other  programs,
however,  before  allowing entry into DOS or upon logging on  the
system.  The equate TIME, allows setting the initial time allowed
on the system per caller. You may set this value to 0 if you wish
unlimited time per call.
.PA
Special Function Keys

     BYE-PC  has several special ALT function  keys.  These  keys
allow  direct  control over all programs operating under  BYE-PC.
These keys are mapped as follows:

          ALT-B     Toggles the remote caller on/off while in
                    DOS. If off, no data is sent or received
                    from the remote.

          ALT-C     Displays Caller online when using XBBS.

          ALT-O     Send 'system going down in 2 min(s)' msg.
                    This is used to tell the caller to log off.

          ALT-H     Hangup on the caller and re-boot system.

          ALT-Q     Enter 'message from sys/op' mode. This dis-
                    ables data from the remote, and allows the
                    sys/op to type a message to the remote. To
                    exit, press ESC or the [End] key.

          ALT-Z     Clear the screen locally.

          ALT-U     Gives the caller online unlimited time for
                    session active.

          ALT-S     Temporarily gives a caller sys/op privledges
                    by setting the CSW to ffffh.

     These  keys  may  be re-mapped if you wish  by  setting  the
K_{function}  keys  to different ALT_c keys.  Simply  change  the
equates  to reflect the new ALT_c keys.  Be careful not to  cause
any  conficts  in  changing these keys if you must  change  them.
Normally you should not have to change any of these values.
.PA
BYE-PC interface via INT 66


     BYE-PC  provides  all  functions  needed  to  support  modem
control  and i/o functions used by application programs that  run
under  BYE-PC.  The  most common program to run under  BYE-PC  is
XMODEM.  XMODEM  requires  many  interface  functions  for  modem
control  and data i/o transfer.  The accompanying source code  on
disk  1,  BYEXFACE.C,  contains  all  of the funcions  needed  to
support C applications under BYE-PC. Make a listing of all of the
source  code and study the functions carefully.  This is used  by
all C programs for modem control and i/o.

     These  functions can be called from most any  language  that
allows  access to software interrupts.  Assembly language  allows
the most direct control of software interrupts.  BYE-PC currently
uses  software  interrupt  66h  for all  modem  control  and  i/o
functions.  The  following  is  a complete list of  all  INT  66h
functions currently provided by BYE-PC:

-----------------------------------------------------------------------
INT66 APPLICATIONS PROGRAM INTERFACE (API) -- This interrupt provides
 modem i/o for applications which need direct control of the modem.

   Altered registers  :  AX, BX, CX, DX
                         ES (only when funct 21 called)

   Preserved registers:  CS, DS, SS, DI, SI, SP, BP

-----------------------------------------------------------------------

 Functions Provided:

   AH=0       Get character from modem in AL.
                   AL=character returned
                   AH=0 null (no keybd scan codes)
                   AX = EOF if no data.

   AH=1       Put character in AL to modem.
                   AL=character to send.

   AH=2       Hang up the modem (DTR off):
                   AL=0 turn off dtr
                   AL=1 turn on dtr

   AH=3       Get carrier detect status in AX:
                   AX=0 no carrier detect found
                   AX=1 carrier detect found

   AH=4       Set carrier detect check status:
                   AX=0 ignore carrier detect status
                   AX=1 check carrier detect status

   AH=5       Flush the rx queue of all data.
.PA
   AH=6       Get # of chars in rx queue:
                   AX=0 rx queue size

   AH=7       Get Baud rate of this call in AX:
                  (0=300bps, 1=1200bps, 3=2400bps)

   AH=8       Set Control Break/Pause (CTRL-C/CTRL-S) flag state:
                   AL=0 CTRL_NOBRK  - disable remote ^C & ^S breaks
                   AL=1 CTRL_BRK    - enable remote breaks
                   AL=2 CTRL_NOTOUT - disable ^S pause timeout
                   AL=3 CTRL_TOUT   - enable ^S timeout
                   AL=4 CTRL_NOTRAP - dont trap ^C & ^S characters
                   AL=5 CTRL_TRAP   - allow ^C & ^S to be trapped out

   AH=9       Set <stdout> merged with modem:
                   AL=0 disable output modem
                   AL=1 enable output to modem

   AH=10      Set <stdin> merged with modem:
                   AL=0 disable input from modem  (rx-queue active)
                   AL=1 enable input from modem   (rx-queue active)

   AH=11      Get BYE-PC version/revison level in AX:
                   AL=Current Revision level
                   AH=Current Version level

   AH=12      Get number of nulls requested in AX:
                   AX=Number of nulls requested

   AH=13      Set number of nulls to AX:
                   AL=Number of nulls to send

   AH=14      Warm Boot the system through bios Ctrl-Alt-Del.

   AH=15      Get the user caller status
                   AX=Status level (0-FFFFh).

   AH=16      Set the user caller status
                   CX=Status level (0-FFFFh).

   AH=17      Set the time limit caller is allowed on line.
                   AL=number of minutes (0-255, 0=Unlimited).

   AH=18      Get the time caller has been on line
                   AX=number of minutes online (0-255).

   AH=19      Set the receive data interrupt mode
                   AL=Mode (0=Off, 1=On)

   AH=20      Get the time limit caller is allowed on line.
                   AX=number of minutes allowed online (0-255).

   AH=21      Get far pointer to caller name buffer.
                   ES:BX -> far ptr to name buffer
.PA
   AH=22      Get far pointer to terminal configuration buffer
                   ES:BX -> far ptr to terminal config buffer



CALLER STATUS WORD STRUCTURE


The caller status word is a sixteen bit word used by SHELL, XMDM,
and other application programs to check for command priorities which
are set by an RBBS program before the user can enter DOS. The MSW of
the status word bits have been reserved for any applications that
may be developed in the future. The LSW bits have the followine
meaning:

        CSW (Caller status word):

        {LSW (least significant word)}

        ----MSB----  ----LSB----
        D7 D6 D5 D4  D3 D2 D1 D0
        |  |  |  |   |  |  |---|--- {reserved for future use}
        |  |  |  |   |  |---------- PATH restriction disable.
        |  |  |  |   |------------- CD command allowed enable.
        |  |  |  |----------------- XMDM S {file} allowed.
        |  |  |-------------------- XMDM R {file} allowed.
        |  |----------------------- Shell DOS command allowed.
        |-------------------------- Shell EXIT command allowed.


        {MSW (most significant word)}

        ----MSB----  ----LSB----
        D7 D6 D5 D4  D3 D2 D1 D0
          {unused}   |  |  |  |
                     |--|--|--|---  Max Drive allowed (0-15).



     The   settings  of  the  CSW  has  no  effect  upon   BYE-PC
operations,  it  is intended for use as a global flag word  which
various  applications  may refer to.  This allows any  number  of
applications  running under BYE-PC to check status levels set  by
other  programs before performing an operation.  Its main purpose
is to inform XMODEM and SHELL if a user has sufficient status  to
perform file transfers or change directories/paths.

.PA
BYEXLIXs.C Interface Functions

     The  following  pages  describe each  function  provided  in
BYEXLIBx.C  and how to use each one.  This is provided as a quick
reference  when  developing code that use BYE-PC control  or  i/o
functions.  Do  not  attempt to address the  serial  port  either
directly  or  through the BIOS in any application  program.  This
will  cause  severe problems with the interrupts and  very  likly
crash the system. The following libraries contain the modules for
all memory models supported by MSC:

          BYEXLIBS.LIB   {small memory model}
          BYEXLIBM.LIB   {medium memory model}
          BYEXLIBC.LIB   {compact memory model}
          BYEXLIBL.LIB   {large memory model}

All  of the source code in these library files requires MASM  5.0
to  create.  This  version  contatins  macros  which  allow  easy
creation of assembly modules for use with MSC.

     All  applicactions must use INT66 for all modem control  and
i/o  for  data transfer.  XMDM.C provided  with  the  development
package  shows  how to use BYE-PC interrupt functions in  detail.
You  may  wish to develop your own interface in Pascal  or  other
language however.  If you develop an interface module for another
lauguage  than  C,  please  contact us if you  wish  to  make  it
available to other programers of BYE-PC applications.








                       'BYEXLIBx.LIB'

                    FUNCTIONS DESCRIPTION

                   FOR MSC 3.0, 4.0, & 5.0











NOTE:  These  functions  describe BYEXLIBx.LIB version  2.00.  Any
       previous versions released are no longer in use.


FUNCTION:      int _bye_check(lver, hver, lrev, hrev)

PARAMETERS:   int lver, hver;     lowest/highest version
               int lrev, hrev;     lowest/highest revision

PURPOSE:      Allows  checking  to ensure that BYE-PC is  loaded
               and resident in memory and of the correct  version
               and  revision level.  This function must be called
               before any '_bye' functions are called or,  a hard
               system crash will result and require power down to
               reload the system.

RETURN:       0 = BYE-PC loaded and is an acceptable version
               1 = BYE-PC is not loaded yet
               2 = BYE-PC is loaded  but,  invalid version#
               3 = BYE-PC is loaded but, invalid revision#

EXAMPLE:

#include <stdio.h>
#include "byexface.h"

#define MIN_VER 1       /* minimum BYE-PC version# required  */
#define MIN_REV 2       /* minimum BYE-PC revision# required */
#define MAX_VER 9       /* maximum BYE-PC version# allowed   */
#define MAX_REV 99      /* maximum BYE-PC revision# allowed  */

main()             /* must at least be version 1.02 */
    {              /* but, any version after and up */
    int rtn;       /* to 9.99 will work.            */

    if ((rtn = _bye_check(MIN_VER, MAX_VER, MIN_REV, MAX_REV)) != 0)
        {
        printf("\nERROR: BYE-PC ");
        switch(rtn)
            {
            case 1:
                printf("is not loaded!\n");
                break;
            case 2:
                printf("loaded is the wrong Version!\n");
                break;
            case 3:
                printf("loaded is the wrong Revision!\n");
                break;
            default:
                printf("returned invalid error code!\n");
                break;
            }
        exit(1);
        }




FUNCTION:      int _bye_getc()

PARAMETERS:    void

PURPOSE:       Returns a character from the receive data queue if
               avilable.  This is for directly reading a a stream
               of data from the modem.  Make sure that data  sent
               and  received  from  the  screen/keyboard  is  off
               before using _bye_getc() and _bye_putc().

RETURN:        Returns  an 8 bit character from the receive  data
               queue.  If  no  data is available an EOF value  is
               returned.

EXAMPLE:

#include <stdio.h>
#include "byexface.h"

/*
** Collect a 128 bytes of binary data from the receive queue.
** This function will not return until all data has been
** received. Before we can receve the data we must disable
** data sent to the screen and key presses from going to
** the modem. We must also disable trapping of ^S and ^C
** so that they may pass a valid binary data characters.
*/

main()
     {
     char buf[140];
     int i;

    _bye_setbreak(CTRL_NOTRAP); /* dont trap/filter ^C & ^S data */
    _bye_stdout(0);             /* turn on console Rx & Tx */
    _bye_stdin(0);

    for(i = 0; i < 128; i++)       /* read 128 bytes of data */
          {
          while(!_bye_rxsize())    /* wait for data to appear */
               ;
          buf[i] = _bye_getc();    /* place data in buffer */
          }

    _bye_stdin(1);              /* turn on console Rx & Tx */
    _bye_stdout(1);
    _bye_setbreak(CTRL_TRAP);   /* enable trap ^C & ^S data */
    exit(0);                    /* exit back to DOS */
    }






FUNCTION:      int _bye_putc(c)

PARAMETERS:    int c;    character to transmit to modem

PURPOSE:       Transmit the character 'c' to the modem . A return
               return  value  of EOF indicates a  serious  error.
               Either the serial port is defective, the modem is
               no longer functioning or a cable problem exists.

RETURN:        EOF = Transmit timeout error
               0 = Character transmitted.

EXAMPLE:

#include <stdio.h>
#include "byexface.h"

/*
** Disable the remote callers ^S and ^C keys and send a string
** to the remote caller. This will prevent the caller from
** being able to pause or break the program from running. Note,
** however, that the local console can still press Ctrl-Break
** and stop the program. Carefully coded applications should
** trap for Ctrl-Break on the local keyboard as well.
*/

main()
     {
     char buf[64];
     int i;

    _bye_setbreak(CTRL_NOTRAP); /* dont trap/filter ^C & ^S data */
    strcpy(buf, "This a string from BYEXFACE ....\n");

    for(i = 0; i < strlen(buf); i++)    /* send for string len */
          _bye_putc((int)buf[i]);       /*  send a byte of data */

    _bye_setbreak(CTRL_TRAP);   /* enable trap ^C & ^S data */
    exit(0);                    /* exit back to DOS */
    }















FUNCTION:      int _bye_dtr(f)

PARAMETERS:    int f;    toggle dtr line (0=inactive, 1=active)

PURPOSE:       This function is used to hangup the modem by
               toggling the DTR/CTS line to the modem.

RETURN:        void



FUNCTION:      int _bye_warmboot()

PARAMETERS:    void

PURPOSE:       Hangup on the caller and warm boot the system
               via Alt-Ctrl-Del bios routine. This causes
               BYE-PC to turn execution over to the BIOS for
               a system re-boot. Note that this function calls
               _bye_dtr() before warm booting to ensure that
               the modem is hung up.

RETURN:        void



EXAMPLE:

#include <stdio.h>
#include "byexface.h"

main()
    {
    printf("\n\nGoodbye...Please Call Again...\n\n");

    _bye_warmboot();
    }


















FUNCTION:      int _bye_getcd()

PARAMETERS:    void

PURPOSE:       This function is used to hangup return the stat-
               us of the carrier detect (CD) line to the modem.
               This is used to test for carrier detect while
               carrier check is disabled. This allows checking
               for carrier while writing to disk files with
               carrier check disabled via _bye_setcd().

               NOTE: This use rs-232 pin 20 to check from the
               modem and it must be connected for this function
               to operate properly.

RETURN:        0 = no carrier detect found
               1 = carrier detect found (CD).

EXAMPLE:

#include <stdio.h>
#include "byexface.h"

/*
** display the current status of the carrier detect line
*/

main()
    {
    rtn = _bye_getcd();       /* read CD status line */
    if (rtn)
          printf("Carrier Found...\n");
    else
          printf("No Carrier Found...\n");
    }




















FUNCTION:      void _bye_setcd(f)

PARAMETERS:    int f;    (0=ingnore CD, 1=re-boot if CD false)

PURPOSE:       This function is used to disable carrier checking
               from the modem. It's main purpose is to prevent
               the system from re-booting while writing to a file
               on disk. Carrier checking should be disabled and
               checked via '_bye_getcd()' while writing to disk.

RETURN:        void

EXAMPLE:

#include <stdio.h>
#include "byexface.h"

/* Open file 'temp.dat' and fill it with 1k of binary data.
** Make sure that the system does not re-boot if carrier is
** lost while writing to disk.
*/

main()
     {
     int i, c;
     FILE *fp;

     if ((fp = fopen("TEST.DAT", "wb")) == NULL)
          exit(1);
     _bye_setbreak(CTRL_NOTRAP);
     _bye_setcd(0);                /* disable carrier checking */
     _bye_stdin(0);
     _bye_stdout(0);
     for (i = 0; i < 1024; i++)    /* write 1k of data */
          {
          while(!_bye_rxsize() && _bye_getcd());
          if (!_bye_getcd())       /* check for carrier good */
               {
               printf("\n** CARRIER LOST - CLOSING FILE **\n");
               break;
               }
          else
              {
              c = _bye_getc();          /* get a character */
              fprintf(fp, "%c", c);     /* write to disk */
              }
          }
     fclose(fp);              /* now close the file */
     _bye_setcd(1);           /* re-enable carrier checking */
     _bye_setbreak(CTRL_TRAP);
     _bye_stdin(1);
     _bye_stdout(1);
     }


FUNCTION:      void _bye_rxflush()

PARAMETERS:    void

PURPOSE:       This function clears all data from the rx-queue
               and resets the count to zero.

RETURN:        void



FUNCTION:      int _bye_rxsize()

PARAMETERS:    void

RETURN:        Size of receive data queue.

PURPOSE:       Returns the size of the receive data queue in
               bytes. The maximum size of the receive data queue
               depends on the configuration BYE-PC.

EXAMPLE:

#include <stdio.h>
#include "byexface.h"

/* Allow a 128 bytes of data to collect in the receive data
** queue and move it to a local buffer for checksum calculation.
*/

main()
     {
     int i;
     unsigned checksum;
     char buf[130];

     _bye_rxflush();            /* make sure rx-queue is empty */
     _bye_setbreak(CTRL_NOTRAP);
     _bye_stdin(0);        /* disable screen & keybd patch */
     _bye_stdout(0);

     while(_bye_rxsize() < 128);    /* let 128 bytes collect */
     for (i = 0; i < 128; i++)          /* move it to buffer */
          buf[i++] = _bye_getc();

     checksum = 0;                      /* compute checksum */
     for (i = 0; i < 128; i++)
          checksum += buf[i];

     _bye_stdin(1);        /* re-enable screen & keybd merge */
     _bye_stdout(1);
     _bye_setbreak(CTRL_TRAP);
     }


FUNCTION:      int _bye_baud()

PARAMETERS:    void

PURPOSE:       Returns the baud rate of the call on line. When
               BYE-PC logs on a caller, the baud rate is de-
               termined and stored for access by '_bye_baud()'.
               This is mainly used for calculating file trans-
               mission times for file transfer protocols.

RETURN:        0 = 300 bps
               1 = 1200 bps
               2 = 2400 bps
               3 = 9600 bps

EXAMPLE:

#include <stdio.h>
#include "byexface.h"

/*
** Display the baud rate of the caller presently on line
*/

main()
    {
    int bps;

    switch(_bye_baud())       /* get baud rate from BYE */
        {
        case 0:
            bps = 300;
            break;
        case 1:
            bps = 1200;
            break;
        case 2:
            bps = 2400;
            break;
        default:
            bps = 9600;
            break;
        }
    printf("\nBaud Rate for this call: %d bps\n", bps);
    }










FUNCTION:      void _bye_setbreak(f)

PARAMETERS:    int f;    (break state flag)

         Valid States:

         CTRL_NOBRK  = 0 -> ignore ^C and ^S keys from remote
         CTRL_BRK    = 1 -> check for ^C and ^S keys
         CTRL_NOTOUT = 2 -> disable 1 min timeout on ^S
         CTRL_TOUT   = 3 -> enable 1 min timeout on ^S
         CTRL_NOTRAP = 4 -> disable all key trapping (^C & ^S).
         CTRL_TRAP   = 5 -> enable key trapping (^C & ^S).

PURPOSE:       This function is used to control ^S & ^C keys from
               the remote caller and to disable timeout on ^S.
               This function must be disabled before transferring
               binary files, to prevent ^S and ^C data from
               being interpretted.

RETURN:        void

EXAMPLE:

#include <stdio.h>
#include "byexface.h"

main()
     {
     int i, c;
     FILE *fp;

     if ((fp = fopen("TEST.DAT", "wb")) == NULL)
          exit(1);
     _bye_setbreak(CTRL_NOTRAP);   /* dont trap ^C & ^S */
     _bye_setcd(0);                /* disable carrier checking */
     for (i = 0; i < 1024; i++)    /* write 1k of data */
          {
          while(!_bye_rxsize() && _bye_getcd());
          if (!_bye_getcd())       /* check for carrier good */
               {
               printf("\n** CARRIER LOST - CLOSING FILE **\n");
               break;
               }
          else
              {
              c = _bye_getc();          /* get a character */
              fprintf(fp, "%c", c);     /* write to disk */
              }
          }
     fclose(fp);              /* now close the file */
     _bye_setcd(1);           /* re-enable carrier checking */
     _bye_setbreak(CTRL_TRAP);
     }


FUNCTION:      void _bye_stdin(f)

PARAMETERS:    int f;    (bios keyboard rx-data merge flag)
                         (1=data rx'ed merged to stdin)
                         (0=data rx'ed is not merged)

PURPOSE:       This function is used to control merging data
               to the keyboard at the bios level. All modem data
               received is treated the same as keys pressed at
               the local keyboard. This is provided to disable
               the INT16 bios patch so data can be transferred.

RETURN:        void

EXAMPLE:

#include <stdio.h>
#include "byexface.h"

/* Allow a 128 bytes of data to collect in the receive data
** queue and move it to a local buffer for checksum calculation.
*/

main()
     {
     int i;
     unsigned checksum;
     char buf[130];

     _bye_rxflush();            /* make sure rx-queue is empty */
     _bye_setbreak(CTRL_NOTRAP);
     _bye_stdin(0);        /* disable screen & keybd patch */
     _bye_stdout(0);

     while(_bye_rxsize() < 128);    /* let 128 bytes collect */
     for (i = 0; i < 128; i++)          /* move it to buffer */
          buf[i++] = _bye_getc();

     checksum = 0;                      /* compute checksum */
     for (i = 0; i < 128; i++)
          checksum += buf[i];

     _bye_stdin(1);        /* re-enable screen & keybd merge */
     _bye_stdout(1);
     _bye_setbreak(CTRL_TRAP);
     }









FUNCTION:      void _bye_stdout(f)

PARAMETERS:    int f;    (bios screen tx-data merge flag)
                         (1=data sent to screen tx'ed)
                         (0=data sent to screen not tx'ed)

PURPOSE:       This function is used to control merging data
               sent to the screen. If enabled, all characters
               printed to the screen via INT10 TTY, are sent
               to the modem as well. If disabled, prints to
               stdout are sent to screen only.

RETURN:        void

EXAMPLE:

#include <stdio.h>
#include "byexface.h"

/* Allow a 128 bytes of data to collect in the receive data
** queue and move it to a local buffer for checksum calculation.
*/

main()
     {
     int i;
     unsigned checksum;
     char buf[130];

     _bye_rxflush();            /* make sure rx-queue is empty */
     _bye_setbreak(CTRL_NOTRAP);
     _bye_stdin(0);        /* disable screen & keybd patch */
     _bye_stdout(0);

     while(_bye_rxsize() < 128);    /* let 128 bytes collect */
     for (i = 0; i < 128; i++)          /* move it to buffer */
          buf[i++] = _bye_getc();

     checksum = 0;                      /* compute checksum */
     for (i = 0; i < 128; i++)
          checksum += buf[i];

     _bye_stdin(1);        /* re-enable screen & keybd merge */
     _bye_stdout(1);
     _bye_setbreak(CTRL_TRAP);
     }









FUNCTION:      unsigned _bye_vers()

PARAMETERS:    void

PURPOSE:       Return the version/revison level of BYE-PC
               currently running.

RETURN:        lsb = revision number
               msb = version number



FUNCTION:      void _bye_version(ver, rev)

PARAMETERS:    int *ver, *rev;     (buffers to place version in)

PURPOSE:       Sets the version/revison level of BYE-PC in the
               int buffer addresses passed.

RETURN:        void



EXAMPLE:

#include <stdio.h>
#include "byexface.h"

/*
** Ask BYE-PC for the version number currently operating.
*/

main()
     {
     int rev, ver;
     unsigned x;

       /* try the hard way first.... */

     x = _bye_vers();
     ver = (int)(x >> 8);
     rev = (int)(x & 0x00ff);
     printf("\nBYE-PC Version %1d.%-2.2d\n", ver, rev);

       /* or use '_bye_version()' for easier access */

     _bye_version(&ver, &rev);
     printf("\nBYE-PC Version %1d.%-2.2d\n", ver, rev);
     }






FUNCTION:      int _bye_getnulls()

PARAMETERS:    void

PURPOSE:       Return the number of nulls presently active. This
               causes BYE-PC to send 'n' (0-9) to the remote
               station after each feed (LF) printed through the
               BIOS write to video INT10.

RETURN:        Number of nulls active 0 through 9.



FUNCTION:      void _bye_setnulls()

PARAMETERS:    void

PURPOSE:       Sets the number of nulls sent to the remote after
               each line feed printed.

RETURN:        void



EXAMPLE:

#include <stdio.h>
#include <conio.h>
#include "byexface.h"

/*
** Ask BYE-PC for the number of nulls active and ask the user
** what to set it too.
*/

main()
     {
     int n;

     n = _bye_getnulls();
     printf("\nCurrent Nulls Setting: d\n", n);

     printf("\nEnter new value <RET=0>: ");
     n = getch();
     if (n >= '0' && n <= '9')
          {
          n -= '0'
          _bye_setnulls(n);
          }
     printf("\nNulls Set to %d\n", _bye_getnulls());
     }




FUNCTION:      int _bye_getcsw()

PARAMETERS:    void

PURPOSE:       Return the present caller status word (CSW)
               setting. (Refer to CSW section of manual).

RETURN:        16 bit CSW



FUNCTION:      void _bye_setcsw(s)

PARAMETERS:    int s;   (16 bit caller status word)

PURPOSE:       Sets the caller status word to a new value.

RETURN:        void



EXAMPLE:

#include <stdio.h>
#include <conio.h>
#include "byexface.h"

/*
** Read the CSW and display the present status, then enable file
** transmit and receive flags.
*/

#define B_FILE_TX   4
#define B_FILE_RX   8

main()
     {
     int s;

     s = _bye_getcsw();
     printf("\nOld Caller Status Word: %-4.4x\n", s);

          /* set transmit and receive flags */

     s = s | B_FILE_TX | B_FILE_RX;
     _bye_setcsw(s);

     printf("\nNew Caller Status Word: %-4.4x\n", s);

     printf("\nFILE Transmit/Receive Enabled...\n");
     }




FUNCTION:      int _bye_gettimer()

PARAMETERS:    void

PURPOSE:       Return the number of minutes caller has been on
               line and since carrier detect was acknowleged.

RETURN:        number of minutes online (0-255)



EXAMPLE:

#include <stdio.h>
#include <conio.h>
#include "byexface.h"

/*
** Tell caller how long he has been online and how much time
** is remaining.
*/

main()
     {
     int l, t;

     l = _bye_gettimeon();         /* original time limit */
     t = _bye_gettimer();          /* time already used   */

     if (!l)
          printf("\nUnlimited Time...\n");
     else
          {
          printf("\nMaximum Time Allowsd: %u\n", l);
          printf("\nMinutes Since Logon : %u\n", t);
          printf("\nTime remaining      : %u\n", t - l);
          }


















FUNCTION:      void _bye_settimeon(mins)

PARAMETERS:    int minutes; (0-255 max time limit, 0=unlimited)

PURPOSE:         Set the time in minutes that the caller may  re-
                 main on line. The time limit becomes effective
                 as soon as this function is called. If the time
                 limit is set to 0, the time limit is unlimited.

RETURN:        void



FUNCTION:      int _bye_gettimeon()

PARAMETERS:    int minutes; (0-255 max time limit, 0=unlimited)

PURPOSE:       Return the original time limit value set by
               _bye_settimeon(). This value is not decremented
               by the system timer, this only allows you to
               read what the time limit was set to.

RETURN:        void


EXAMPLE:


#include <stdio.h>
#include <conio.h>
#include "byexface.h"

/*
** Tell caller how long he has been online and set the limit
** for 5 minutes longer before disconnect.
*/

main()
     {
     int s;

     printf("\nMinutes Online: %d\n", _bye_gettimer());

     printf("\nYou now have five minutes left...\n");

     _bye_settimeon(5);
     }








FUNCTION:      void _bye_setname(s)

PARAMETERS:    char *s;  (ptr to string up to 63 characters)

PURPOSE:       This function loads the string pointed to by 's'
               into the resident portion of BYE.COM.  This allows
               the  ALT-C key to display the caller on line while
               in DOS. The string must be null terminated.

RETURN:        void



FUNCTION:      void _bye_getname(s)

PARAMETERS:    char *s;  (ptr to string up to 63 characters)

PURPOSE:       This function loads the buffer pointed to by 's'
               from the resident portion of BYE.COM.  This allows
               allows reading the users name currently online  by
               other programs while in DOS.

RETURN:        void



EXAMPLE:

#include <stdio.h>
#include "byexface.h"

/* Allow a 128 bytes of data to collect in the receive data
** queue and move it to a local buffer for checksum calculation.
*/

main()
     {
     int i;
     char buf[65];

    _bye_setname("John, Doe");    /* set callers name */

        /* now read it back */

    _bye_getname(buf);
    printf("Caller on line:%s\n", buf);
    }