HZComm - FOSSIL implementation for the Heath/Zenith-100 computer
	----------------------------------------------------------------


	This file desribes the implementation specific features of this 
	FOSSIL driver.  For information on use and/or implementation of
	a FOSSIL driver, see the enclosed FOSSIL.DOC.

	This version of HZComm has been tested with Opus Version 0.00 
	and Seadog Version 4.0.

	This TSR program provides complete support for the FOSSIL spec.,
	version 3.  It should be run once, upon system boot up.  The 
	program will try to determine if it has already been installed,
	and will not reinstall if it's already in memory.

	HZComm and ZPC
	--------------

	Some care should be taken if you intend to have HZComm and ZPC
	resident at the same time.  HZComm should be loaded AFTER ZPC.
	This seems to work for all programs that use either utility,
	except SETZPC.  The method SETZPC uses to locate ZPC in memory
	seems to be confused by the presence of HZComm.  ZPC itself has
	the same problem, and will not detect that it is already in
	memory if it is reinvoked.  This is a good way to eat up large
	chunks of memory in a hurry.  So the moral is, load ZPC then
	HZComm.  If you need to configure ZPC, don't load HZComm until
	you're done.


	HZComm Implementation Notes
	---------------------------

	HZComm recognizes two serial ports, Serial-A (J1, COM1 to IBM
	types), and Serial-B (J2, COM2).  The port number passed to
	HZComm should be 0 for Serial-A and 1 for Serial-B.  As of the
	current release, only one port can be active at any one time,
	and the port number argument is only used for functions 4 and
	20.  All other function ignore the port number argument.
	
	Because of a design "quirk" in the 2661 EPCI that the '100 uses
	for serial I/O, the DCD input to the computer is basically
	worthless.  The HZComm driver assumes that the DCD output from
	your modem (normally pin 8) is connected to the DSR input on
	the '100 serial port.  This is pin 22 on Serial-A and pin 6 on
	Serial-B.  Don't forget that that Serial-A requires swapped pins
	2 and 3, as well as other changes.

	Function 0 - standard

	Function 1 - standard

	Function 2 - standard

	Function 3 - standard

	Function 4 - The control-C flag checking is not implemented.

	Function 5 - standard

	Function 6 - standard

	Function 7 - standard - the timer on the '100 is 100Hz

	Function 8 - standard

	Function 9 - standard

	Function 10 - standard

	Function 11 - standard

	Function 12 - standard

	Function 13 - standard, with caveats:

		HZComm actually stuffs the IBM style keycodes in the BIOS 
		typeahead buffer.  That way Opus Version 0.00 (which expects 
		IBM keycodes but uses DOS calls to get them) works as 
		expected.  When this call is made the keycodes are retrieved
		from the BIOS buffer and returns them to the caller.  When
		a new version of Opus comes out that uses this call, a new
		version of HZComm will be released that doesn't mess with
		the BIOS at all.  In that case, keyboard entries will ONLY
		be available through this call.

	Function 14 - standard, with same caveats as Function 13.

	Function 15 - standard, with caveats:

		XON/XOFF is supported in the driver for output.  If it ever
		becomes necessary for HZComm to be able to impose flow
		control on input, this function may be revised.  The UART 
		used in the '100 stops transmitting by itself when CTS is 
		removed.  RTS would only be needed in the case of input
		flow control.  This MAY be implemented in a future release.

	Function 16 - standard (I think)

	Function 17 - standard

	Function 18 - standard

	Function 19 - standard, The use of ZANSI is recommended.

	Function 20 - standard

		The watchdog activation/deactivation is not effected by inits 
		(function 4) and uninits (function 5).  This is so that a
		watchdog may be set before running a program that does not
		monitor the serial port.

	Function 21 - standard

	Function 22 - standard, maximum of 4 routines added to chain.

	Function 23 - standard, both "types" of boot are identical


	Version History
	---------------

	03/01/87	Version 2.31

	First public release.  Supports all functions required to support
	Fido, Opus V0.00 and SEADog V4.0.


	03/12/87	Version 3.0

	First release of FOSSIL draft version 3 implementation.