ZMODHOST: By Ed Richter, sysop U.S Computer PC Board in Garland,
Texas phone 214-276-9336.

This arc file contains the following files:

ZMODEM.BAT      Menu system for DSZ from Omen Technology
CHOOSE.COM      Set Errorlevel for branching in zmodem.bat
                This was written by Joe Campbell and published
                in MS DOS Power Users Guide Volume I, Second
                Edition by Jonathan Kamin and published by
                SYBEX.
CHOOSE.TXT      Debug script file used to create Choose.com
ZMODHOST.DOC    This file.


    This program requires DSZ.COM from Omen Technology to add
additional external protocol capability to Procomm Plus.    

    To create Choose.com from chose.txt use Debug with this
command line:
             DEBUG < CHOOSE.TXT

    Install:
             Put the following files on the same directory,
             ZMODEM.BAT, CHOOSE.COM, DSZ.COM. Use the setup
             command in Procomm+ and install ZMODEM in both
             the upload and download directory. You will need
             ANSI.SYS installed in your config.sys file to
             display the graphics characters in the menu. If
             you don't like ansi.sys remove the box around
             the menu.

    Operate:
             Select ZMODEM from your up or download menu,
             enter the filename(s) in the Procomm+ window,
             and follow directions on the menu.

    The ZMODEM.BAT file included is setup to receive file on
    E:\ so no drive information is entered in the Procomm+
    window. You will need to change all receive options to
    your preferred directory. You may also eliminate the drive
    selection from the command lines in the bat file and enter 
    it in the Procomm+ window.

    The drive selection for uploading is done from the Procomm+
    window. If you have a designated directory to upload from
    you can add the drive selection to the command line in the
    bat file.

    The DSZ.DOC in the 07/11/88 release states that the "CON"
    parameter must be used to run Procomm+ in Host Mode. This
    program will accommadate that. The default setting is for
    Procomm+ in Terminal mode. This can be changed by selecting
    the "Y(es)" option on the main menu. If you are dialing 
    into Procomm+ Host Mode and wish to use DSZ protocols you
    will need to use this option.

    Choose.com will set the errorlevel based on input from the
    keyboard. It assigns errorlevels to each letter on the
    command line. The assignments are from right to left and 
    start with errorlevel = 0.
    The command line   CHOOSE ABCDEFGHIJ will result in the
    key "J" causing an ERRORLEVEL = 0, "I" ERRORLEVEL 1, etc
    "A" ERRORLEVEL 9. It accepts all 26 alpha characters in
    either upper or lower case.
   
    The program uses the SET= command to store the variable HOST
    in your enviroment string. If you receive an "Out of Enviroment
    Space" message you will need to eliminate 3 characters from
    your current enviroment or expand it with the 
    
             SHELL=x:\COMMAND.COM /P /E:xxx

    line in your config.sys file where x is the drive\path for
    command.com and xxx is the number of bytes used for the 
    enviroment string. ZMODEM.BAT clears the HOST variable 
    before returning to Procomm+


    I have tested each of options in Procomm+ mode. I have not
    yet tried Procomm+ Host mode but since it simply requires
    the addition of the CON parameter to the command line there
    should be no problems. If you encounter any please pass the
    fix along so we may all benefit. Enjoy and Thanks