BRIK(1)                    USER MANUAL                    BRIK(1)


     NAME
          brik - calculate 32-bit CRC

     SYNOPSIS
          brik -h
          brik -gcGCbafvsqWHT file ...

     DESCRIPTION
          Brik generates and verifies 32-bit CRC values (checksums).
          It is designed to generate CRCs for text files that are the
          same on all computer systems that use the ASCII character
          set, provided each text file is in the usual text file
          format for each system. Brik will also optionally use binary
          CRCs calculated using every byte in a file.  Such binary
          CRCs are portable across systems for binary files that are
          moved from system to system without any newline conversion.
          Brik can be asked to decide by examining each file whether
          to calculate a text mode or binary mode CRC for it.

          Changes from version 1.0 are summarized at the end of this
          document.

          The general usage format is:

               brik -gcGCbafvsqWHT [ file ] ...

          The brackets mean that file, which is the name of a file, is
          optional.  The three dots indicate that more than one
          filename may be typed (separated by blanks).  Exactly one of
          the options -c, -C, -g, -G, or -h, is required.  The -h
          option gives a help screen.

          In addition to -h, the Brik options available (as they
          appear on the help screen) are:

          -g   look for Checksum: header, generate CRC for rest of
               file

          -c   get CRC from header, verify CRC of rest of file

          -G   generate CRC for entire file (add -b for binary files)

          -C   verify all file CRCs from output of -G (-f is not
               needed)

          -b   use binary mode -- read file byte by byte, not line by
               line

          -a   automatically decide whether each file is text or
               binary

          -f   read filenames (wildcards ok) from specified files

          -v   be verbose, report all results (else only errors are
               reported)

          -s   be silent, say nothing, just return status code

          -q   be quiet, don't print header for -G

          -W   after generating CRC with -g, write it to original
               header

          -H   after generating CRC with -g, print header to stdout

          -T   include trailing empty lines, normally ignored (text
               mode only)

          VERIFYING CRC HEADERS

          The primary intended use of Brik is to verify Checksum:
          headers in Usenet postings and in C and Pascal source files.
          A Checksum: header looks like this:

               Checksum: 9485762645b   (verify with "brik")

          The word Checksum: must occur at the beginning of a line.
          It is followed by a colon, an optional blank, a ten-digit
          decimal 32-bit CRC, and any arbitrary optional string such
          as the comment shown above.  The CRC value may be followed
          by a one-character suffix identifying the type of the CRC.
          These suffixes are described later.

          When Brik is invoked with the syntax

               brik -c file ...

          it will search for the Checksum: header in each specified
          file, read the CRC value from that header, calculate the
          CRC-32 for all lines in the file (except trailing empty
          lines) that occur *after* the header line, and report an
          error if the two values do not match.

          CALCULATING CRC HEADERS

          The command

               brik -g file ...

          tells Brik to look for the Checksum: header in each
          specified file, calculate the CRC of the lines in the file
          following the header, and print the CRC and filename without
          changing the file in any way.  You can also ask Brik to
          update the Checksum: header with the following command:

               brik -gW file ...

          This causes Brik to update the Checksum: header in the file
          with the newly-calculated CRC.  If there is not enough space
          for the CRC in the existing header, Brik reports an error
          and does not change the existing header.  To initially add a
          Checksum: header to a file, insert a line of the following
          form into the file with a text editor:

               Checksum: XXXXXXXXXX  -- this is an optional comment

          The word Checksum must be at the beginning of a line.  The
          ten `X' characters shown can be any ten characters.  They
          will be later replaced by the calculated CRC value.  They do
          not need to be `X'.  The comment following them is optional
          and can be any arbitrary string of characters after the CRC
          field, separated from it by blanks.  As an example, in a C
          source file called main.c, you might have:

               /*
               Checksum: XXXXXXXXXX  (verify or update with brik)
               */

          Once a header like this exists in the file, invoke Brik as
          follows:

               brik -gW main.c

          This will cause the ten `X' characters to be replaced with
          the calculated checksum, giving something like this:

               /*
               Checksum: 1922837484  (verify or update with brik)
               */

          Later you can use the command

               brik -c main.c

          to verify that the contents of the file following the header
          have the same CRC as the stored value.

          If Brik is invoked with the -c or -g options and it cannot
          find a Checksum: header in a file, it prints a row of
          question marks.  If it is invoked with the -gW option and it
          does not find enough character positions after the Checksum:
          string to hold the CRC, it does not fill in the CRC and
          prints an error message.

          Brik can be asked to generate a complete Checksum: header
          but print it to standard output instead of writing it to the
          file.  Do this by adding the -H option.  If both -W and -H
          are given, the Checksum: header will be written both to the
          file and to standard output.

          WHOLE-FILE CRCS

          A "whole-file" CRC calculation is done for the entire
          contents of a file, without looking for a Checksum: header.
          The command

               brik -G file ...

          asks Brik to do this calculation for all specified files.
          The output from this command is a list of files and their
          whole-file CRCs.  It is sent to the standard output stream,
          which in most cases is your screen.  The output should be
          saved in a file by redirecting it.  For example, the command

               brik -G *.h *.c > crc.lst

          on an MS-DOS system might yield the following in the output
          file crc.lst:

               # CRC-32        filename
               # ------        --------

               2566277976      getopt.c
                100594287      brik.c
               1151475469      vms.c
               3929503738      turboc.c
               2424271922      addbfcrc.c
               1943472856      assert.h
               2601923477      brik.h

          The output of the -G option is in free format.  The output
          file may be edited by hand.  Empty lines and lines beginning
          with '#' will be ignored by Brik when it is later asked to
          read this file.

          This list of filenames and whole-file CRCs may be verified
          by a command like this:

               brik -C crc.lst

          This makes Brik read the file crc.lst, get the CRCs and
          filenames from it, do the CRC calculation again for each
          file, and report an error if it does not match the CRC
          recorded inside crc.lst.

          **IX and MS-DOS users (and others who can pipe the output of
          one command into another) could use a command like the
          following to see if Brik's -G and -C options are working:

               brik -G file ... | brik -C

          This invokes "brik -G" on some files, sending the output to
          a pipe where it becomes the input of "brik -C".  If no
          filename is specified, Brik reads from standard input, so
          "brik -C" will read from the pipe and concurrently verify
          all the CRCs that are being generated by "brik -G".

          Whole-file CRCs are normally generated in text mode, in
          which a file is treated as lines of text.  You can also
          generate whole-file CRCs in binary mode.  See below.

          BINARY VERSUS TEXT MODE

          Brik can work in two different modes.  The most common mode,
          used unless you specify otherwise, is text mode.

          In this mode Brik reads all files line by line, and forces
          each line of text to be terminated by a newline character of
          constant value before doing a CRC calculation.  Thus, no
          matter what newline character is used by your system, the
          CRC calculation will be unaffected.  This means that whether
          your operating system uses linefeeds to terminate lines
          (e.g. **IX), or a carriage return and a linefeed (e.g. MS-
          DOS) or a carriage return only (e.g. Macintosh) or nothing
          but a record length field (e.g. VAX/VMS), the CRC
          calculation in text mode gives the same results.

          If a file is not intended to be a text file, the text mode
          CRC calculated by Brik may not be reliable and may be
          different on different systems.  If Brik is calculating a
          text mode CRC on a file that appears to contain binary data,
          it still calculates the text-mode CRC but adds a "*"
          character after the CRC to indicate to warn the user.

          Brik can be asked to operate in binary mode by adding a -b
          option.  Binary mode is applicable only to the -G command,
          which acts on whole files.  Thus

               brik -G file ...

          finds whole-file CRCs of all specified files in text mode,
          while

               brik -Gb file ...

          does the same in binary mode.  In binary mode Brik simply
          reads and calculates the CRC for all bytes in a file.  If a
          file is moved from one system to another without any newline
          conversion or any other changes, Brik should calculate the
          same binary mode CRC for it on both systems.

          The output from "brik -Gb" includes a trailing b suffix in
          each CRC, so "brik -C" will correctly use binary mode for
          such CRCs and it is never necessary to type "brik -Cb"
          instead.

          In its auto-check mode, Brik will itself examine each file
          and determine whether it is a text or binary file and
          calculate a CRC accordingly.  To do this, use the -a option.
          Although Brik can determine the type of each file with a
          high degree of reliability, it is still possible for it to
          come to a wrong conclusion about some files.

          The output from "brik -Ga" will include a trailing b
          character in the CRC for those files that appeared to be
          binary to Brik.  You may find both text and binary CRCs in
          the output.

          TRAILING EMPTY LINES

          The normal behavior of Brik in text mode is to ignore any
          trailing empty lines in a file.  An empty line is a line
          that contains nothing, not even blanks or tabs.  (Just
          hitting a carriage return when you are editing a text file
          usually produces an empty line.)  If manipulating a text
          file causes trailing empty lines to be added or deleted, the
          CRC calculated by Brik will be unaffected.  You can override
          this if necessary with the -T option, which makes Brik
          include trailing empty lines in the CRC calculation.  For
          example,

               brik -gWT

          will update the Checksum: header with a CRC that includes
          all lines in a text file.  Similarly

               brik -GT

          will find whole-file CRCs that include all lines in a text
          file.

          When Brik is given the -T option, it adds a T suffix to each
          generated CRC.  Then, when the CRC is verified with -c or
          -C, Brik will correctly include trailing empty lines when
          needed without having to be explicitly told to do so.

          In binary mode Brik always reads all bytes in a file, so it
          does not ignore trailing empty lines, and the -T switch is
          not needed.

          The effects of the -T and -b options are mutually exclusive.
          If both are given, whichever is used later overrides the
          first.  So -bT is equivalent to -T and -Tb is equivalent to
          -T.

          FILENAME CONVENTIONS

          Under MS-DOS and VAX/VMS, wildcards are allowed on the
          command line and will be expanded by Brik.  Under **IX,
          wildcards are expected to be expanded by the shell and are
          not expanded by Brik.  If no filename is given, Brik reads
          its standard input.  By default this is keyboard input, but
          it is expected that input will usually be redirected to come
          from a file or a pipe.  Also, if a filename is explicitly
          specified as a dash ("-"), it stands for standard input.

          The following five commands (valid under the **IX operating
          system)

               brik -c myfile            # "myfile"
               brik -c < myfile          # stdin = "myfile"
               cat myfile | brik -c      # stdin = a pipe
               brik -c - < myfile        # "-" = stdin = "myfile"
               cat myfile | brik -c -    # "-" = stdin = a pipe

          all have the effect of verifying the Checksum: header in the
          file myfile.

          Standard input can also be read when using the -C option.
          For example, suppose we have already given the command

               brik -G *.c *.h > crc.lst

          to create a file called "crc.lst" that contains a list of
          whole-file CRCs.  We can now verify the integrity of these
          files with any of the following commands:

               brik -C crc.lst          # "crc.lst"
               brik -C < crc.lst        # stdin = "crc.lst"
               brik -C - < crc.lst      # "-" = stdin = "crc.lst"
               cat crc.lst | brik -C    # stdin = a pipe
               cat crc.lst | brik -C -  # "-" = stdin = a pipe


          INDIRECT FILE NAMING

          The -f option allows you to have filenames in a list rather
          than on the command line.  For example, suppose you want to
          generate whole-file CRCs of files whose names are selected
          by some other program.  You could use find (under **IX) or
          Stuff (under MS-DOS) to generate a list of filenames.  When
          the -f option is given, Brik reads filenames, one per line,
          from the file(s) specified.  Thus you could do the
          following:

               find . -mtime +3 -print > flist
               brik -Gf flist > crc.lst

          The first command asks find to generate a list of names of
          all files that were modified more than 3 days ago, and sends
          the output to the file flist.  The contents of flist might
          now look like this, as an example:

               ./sez.doc
               ./brik.doc
               ./stuff.doc
               ./looz.doc

          The second command above asks Brik to read the file called
          flist, get a list of filenames from it, one per line, and
          generate the whole-file CRC of each of these files.  We
          additionally redirect the output of "brik -Gf" to the file
          called crc.lst.  Given the above contents of flist, the
          following two commands are exactly equivalent:

               brik -Gf flist >crc.lst
               brik -G ./sez.doc ./brik.doc ./stuff.doc ./looz.doc >crc.lst

          The advantage of the -f option is that once you have
          filenames in a file, you need not type them again at the
          command line.  The -f option also allows you to feed Brik
          through a pipe filenames generated by another program.
          Consider this command:

               find . -mtime +3 -print | brik -Gf - > crc.lst

          Under **IX this concurrently invokes both find and Brik.  As
          find generates a filename and sends it to its standard
          output (a pipe), Brik reads the filename from its standard
          input and generates its whole-file CRC.  The following
          pipeline

               find . -mtime +3 -print | brik -Gf - | brik -C -

          invokes find to generate filenames, Brik to print the
          whole-file CRCs of those files, and Brik again to
          immediately verify them.

          Under MS-DOS and VAX/VMS (and any other operating system
          under which Brik has been installed to expand wildcards
          itself), a file specified by the -f option can itself
          contain wildcards in the filenames.  For example, suppose
          the file "wildfile" contains the following lines:

               /bin/*.exe
               /bin/*.com
               /doc/*.doc

          Now if we invoke Brik with the command

               brik -Gf wildfile

          it will read filespecs from "wildfile," expand wildcards in
          each filespec, and generate whole-file CRCs for all matching
          files.

          If you are checking whole-file CRCs with the -C option, you
          do not normally need to use the -f option.  When used with
          -C, the -f option introduces an additional level of file
          naming indirection. For example, the command

               brik -C crc.lst

          takes a list of CRCs and filenames from "crc.lst" and
          verifies them.  However, the command

               brik -Cf master.lst

          does not do the same thing.  Instead, it takes a list of
          files from "master.lst," looks inside each of those files
          for a list of CRCs and filenames, and verifies them.

          As an example of the use of -Cf, consider this sequence:

               brik -Gb /bin/*.exe > exelist
               brik -Gb /bin/*.com > comlist
               brik -GT /doc/*.doc > doclist
               brik -G  /doc/*.man > manlist

          Now we have four files called "exelist," "comlist,"
          "doclist," and "manlist" containing whole-file CRCs of
          various types.  We can test the integrity of files listed in
          these in four separate commands like this:

               brik -C exelist
               brik -C comlist
               brik -C doclist
               brik -C manlist

          But we could also do this in a single step by first creating
          a file called "biglist" that contains the names of these
          four files:

               exelist
               comlist
               doclist
               manlist

          and then use -Cf thus:

               brik -Cf biglist

          This causes Brik to read filenames from "biglist," look
          inside each of those files ("exelist," "comlist," "doclist,"
          and "manlist") and check the CRCs found there.  A **IX
          example to do the same thing in a more compact way might be:

               cat exelist comlist doclist manlist | brik -Cf -

          The above examples are somewhat contrived, however.  We
          could also use the following command:

               brik -C exelist comlist doclist manlist


          SILENT VERSUS VERBOSE VERSUS QUIET

          Brik accepts options -s, -q, and -v that control the degree
          of verbosity.

          Normally Brik prints a message only if it detects an error.
          For example, if you give the command

               brik -c *.c *.h

          and Brik finds that all Checksum: headers contain CRCs that
          match the calculated value, it prints nothing.

          The -v switch makes Brik print a message for each file
          tested that contains the word "ok" if stored and calculated
          CRCs matched and "BAD" if they did not.

          In all messages reporting file CRCs, Brik prints the actual
          CRC it calculated, or a row of question marks if it could
          not calculate one.  Brik fails to calculate a CRC if it is
          trying to calculate a header-based CRC (commands -c and -g)
          but does not find a Checksum: header in a file.

          The -s switch tells Brik to be silent.  This will cause
          nothing to be printed if Brik does not find a Checksum
          header or if CRCs don't match.  However, the status code on
          exit is still set.  The -s option is useful for invoking
          Brik from within a shell script (**IX) or a batch file (MS-
          DOS) and later testing the error code it returned when it
          exited.

          The -s switch does not suppress the error message printed if
          Brik is given a filename and the file cannot be found.  For
          example, if the command

               brik -cs myfile

          is given but "myfile" does not exist, Brik will print an
          error message even though the -s option was given.

          The -q switch makes Brik slightly quieter.  Its only effect
          is to suppress the introductory comments that are otherwise
          generated by the -C option.

          VAX/VMS BUGS

          o    Under VAX/VMS, file manipulation is unpredictable and
               the VAX/VMS C runtime library in particular is very
               unreliable.  One result is that under VAX/VMS, the -gW
               option will work only for stream-LF files, which are
               the only type of file that VAX/VMS seems to handle
               correctly.  Fortunately, the -c option will correctly
               work for VAX/VMS standard text files.

          o    The VAX/VMS implementation of Brik simply ignores
               filenames that correspond to nonexistent files instead
               of giving an error message.  VMS users are invited to
               fix this bug (probably somewhere in the nextfile()
               function in the file vms.c) and send me the fix.

          o    To avoid annoying error messages, Brik under VAX/VMS
               always exits with a status code of 1.

          o    Due to a problem in the VAX/VMS command interpreter, if
               any uppercase option characters are typed (e.g. -C, -G,
               -T), Brik will not recognize them as uppercase unless
               they are enclosed in double quotes.  An example of a
               correct command under VAX/VMS:

                 brik "-GT" *.*

               An example of a command that won't work:

                 brik -GT *.*

          USAGE HINTS

          This section discusses some ways of using Brik.

          -    Brik is currently used to create and verify checksums
               of articles posted on the Usenet newsgroup
               comp.binaries.ibm.pc.  While reading Usenet news with
               rn, for example, you can verify the Checksum: header of
               such an article with the command:

                 | brik -cv

               This feeds the current article to Brik as standard
               input and asks it to verbosely verify the checksum.

          -    C and Pascal source files that are being distributed
               can be given their own Checksum: headers.  The
               advantage of this over listing CRCs separately is that
               each file contains its checksum no matter where it
               goes.  The recipient can easily verify that each source
               file was received intact.  This is especially valuable
               when source files are being sent by electronic mail
               through an IBM mainframe-based network, such as BITNET,
               that can cause corruption of text files.

               Create the Checksum header with a text editor and
               initialize its value with the command:

                 brik -gW file ...

               The recipient can verify the checksum with the command:

                 brik -cv file ...

          -    To keep track of any unexpected filesystem corruption
               or unauthorized changes to system files, Brik can be
               used to create a list of checksums.  This should be
               done using the -b option (all binary checksums) or the
               -a option (use text or binary as appropriate).  Under
               **IX this can be done with a command like this one:

                 find /bin /usr/bin /lib /usr/lib /usr/new \
                  -type f -print | \
                 grep -v '^/usr/bin/beta' | \
                 grep -v '^/usr/new/lib/news' | \
                 brik -Gbf - > crc.list

               This example uses find to print the pathnames of
               certain files, grep to filter out certain directory
               subtrees, and then Brik to print checksums of all
               selected files.  Periodically a background job can be
               run to compare the file list against current files and
               report any discrepancies:

                 brik -C crc.lst | mail -s 'brik output' postmaster

               Under MS-DOS, create a list of checksums with the help
               of Stuff, a find-like file finder program that is
               distributed with zoo 2.01:

                 stuff /bin /msdos /turboc | brik -Gaf - > crc.list

               This is a simple mechanism that can be used to detect
               unexpected file changes caused by hardware problems or
               malicious programs such as viruses and worms.  Be
               warned, however, that since Brik uses a published CRC
               algorithm, very clever deviant programs are possible
               that could change a file without affecting its CRC.

               To avoid too many false alarms, only files that do not
               change much (such as system binaries) should be
               selected.

     CHANGES
          Changes from version 1.0 are as follows.

          -    The CRC calculation has been recoded in 8086 assembly
               code suitable for Turbo C/MS-DOS.  As a result Brik 2.0
               under MS-DOS is much faster than version 1.0.

          -    The new -a flag makes Brik automatically determine for
               each file whether it is text or binary and calculate
               the CRC accordingly

          -    When Brik is asked to calculate a text mode CRC but the
               file appears to be binary, it now does not print a
               warning message but instead adds a "*" suffix to the
               calculated CRC to indicate that the CRC may not be
               reliable.

          -    The new -H flag makes Brik print the formatted
               Checksum: header to standard output.

          -    Detection of binary files is now more reliable under
               MS-DOS.  If a control Z character occurs near the
               beginning of a binary file, Brik will not be fooled by
               the apparent end-of-file but will in most cases
               reliably detect that the file is binary.

          -    The new -q flag suppresses the introductory comments
               from the output of the -G command.

     BUGS
          Brik is designed to work with computer systems that use the
          7-bit ASCII character set and 8-bit bytes with the eighth
          (parity) bit set to zero.

          Brik has not been tested with computer systems that use
          ASCII characters with the eighth bit set or those that use
          EBCDIC characters.  Although it will calculate a CRC on such
          machines, the probability of this CRC being the same as the
          one calculated on machines that use 7-bit ASCII is
          approximately 0.00000000023.

     DIAGNOSTICS
          Error messages are intended to be self-explanatory.

          The exit status returned is 1 if Brik was invoked with
          incorrect arguments, else it is the number of files found
          with missing or invalid CRCs, but not greater than an
          operating-system-dependent maximum value.

     COPYRIGHT
          Both this documentation and Brik are Copyright 1989 Rahul
          Dhesi, all rights reserved.  Permission is granted to copy,
          use, and distribute for any commercial or noncommercial
          purpose in accordance with the requirements of version 1.0
          of the GNU General Public license.

          Note:  This software has not been endorsed by the Free
          Software Foundation, the creator of the GNU license, and I
          am not affiliated with that organization.

     AUTHOR
          Rahul Dhesi
          UUCP: {iuvax,pur-ee}!bsu-cs!dhesi
          Internet: dhesi@bsu-cs.bsu.edu

     BRIK(1)                    USER MANUAL                (1989/07/11)