D I S K O T I M*

                                   USER MANUAL


                         for PC-DOS* and MS-DOS* Systems





                        Copyright (C) 1983 by Ray Hallman

                 No part of this publication may be reproduced, 
                 transmitted,    transcribed,   stored   in   a 
                 retrieval   system  or  translated  into   any 
                 language or computer or computer language,  in 
                 any   form  or  by  any   means,   electronic, 
                 mechanical,   magnetic,   optical,   chemical, 
                 manual or otherwise, except as provided herein 
                 without   prior  written  permission  of   Ray 
                 Hallman,  10120  Pasture Gate  Lane  Columbia, 
                 Maryland, 21044  ( COMPUSERVE --> 71445,1060 )

                                   Disclaimer

                 Ray   Hallman  makes  no   representation   or 
                 warranties with respect to the contents hereof 
                 and   specifically   disclaims   any   implied 
                 warranties  or merchantability or fitness  for 
                 any particular purpose.   Further, Ray Hallman 
                 reserves the right to revise this  publication 
                 and  to make changes from time to time in  the 
                 content  hereof  without obligation to  notify 
                 any person of such revision or changes.


                                  Version 1.1

                                  May 28, 1983




        *DISKOTIM is a trademark of Ray Hallman
        *MS-DOS is a trademark of MICROSOFT.
        *PC-DOS is a trademark of I.B.M.















                                                           DISKOTIM - 2





                                TABLE OF CONTENTS

        1.   WARRANTIES, GUARRANTEES, and LIABILITIES

        2.   LICENSE AGREEMENT

        3.   GENERAL DESCRIPTION AND FEATURES OF "DISKOTIM"

        4.   LOADING INSTRUCTIONS

        5.   MAIN MENU

        6.   DISK DRIVE SPEED TESTS

        7.   DISK DRIVE HEAD POSITION AND TRACK SELECTION

        8.   SELECTION OF "QUAD DENSITY" AND BACK TO "DUAL DENSITY" DRIVE 
             PARAMETERS.

        9.   USE OF TEST DISKETTES WITH DISKOTIM

        10.  QUITTING FROM THE DISKOTIM PROGRAM BACK TO THE SYSTEM

        11.  SOME COMMENTARY ON THE DRIVE SPEED ADJUSTMENT

        12.  SOME COMMENTARY ON THE DRIVE ALIGNMENT PROCEDURES


































                                                           DISKOTIM - 3


        1.   WARRANTIES, GUARRANTEES, and LIABILITIES


             THE  PROGRAM  IS  PROVIDED "AS IS" WITHOUT WARRANTY  OF  ANY 
        KIND,  EITHER EXPRESSED OR IMPLIED, INCLUDING, BUT NOT LIMITED TO 
        THE  IMPLIED  WARRANTIES  OF MERCHANTABILITY AND  FITNESS  FOR  A 
        PARTICULAR  PURPOSE.   THE  ENTIRE  RISK AS TO  THE  QUALITY  AND 
        PERFORMANCE OF THE PROGRAM IS WITH YOU.  SHOULD THE PROGRAM PROVE 
        DEFECTIVE, YOU ASSUME THE ENTIRE COST OF ALL NECESSARY SERVICING, 
        REPAIR OR CORRECTION.

             IN  NO  EVENT  WILL RAY HALLMAN BE LIABLE  TO  YOU  FOR  ANY 
        DAMAGES,  INCLUDING  ANY  LOST  PROFITS,  LOST SAVINGS  OR  OTHER 
        INCIDENTAL  OR  CONSEQUENTIAL DAMAGES ARISING OUT OF THE  USE  OR 
        INABILITY  TO  USE  SUCH  PROGRAM EVEN IF RAY  HALLMAN  HAS  BEEN 
        ADVISED OF THE POSSIBILITY OF SUCH DAMAGES,  OR FOR ANY CLAIM  BY 
        ANY OTHER PARTY.

             Information  in  this document is subject to change  without 
        notice  and  does  not represent commitment on the  part  of  RAY 
        HALLMAN.   The  software described in this document is  furnished 
        under license agreement.  The software may be used or copied only 
        in  accordanced with the terms of the agreement.   It is  against 
        the law to copy this software on magnetic tape,  disk,  diskette, 
        or  any  other medium for any purpose other than the  purchaser's 
        own  personal  use  and then only after  having  agreed  to  said 
        license agreement.

             I sincerely hope that you find the program package contained 
        herein  to  be  of  use to you.   I have  decided  to  make  this 
        available  to you and any users of the "distributor system"  from 
        which  you  obtained it because I have personally  received  much 
        good  software from such systems and would like to repay some  of 
        this  benefit.   Also,  it is my hope that this will promote good 
        will among good programmers to distribute their good efforts in a 
        similar  manner.   As others before me have said,   "if you  find 
        this  program helpful and would like to continue to promote  this 
        kind  of effort you may contribute something to my  above  stated 
        address".   I  would be delighted to receive $10 or so by  return 
        mail.   This  would  certainly  encourage me  to  continue  these 
        efforts  as  I do have some other good ideas!   I do have  a  few 
        copies  of the distribution version of this program with hardcopy 
        manual  which I will send to you for a donation of  $15.   Please 
        bear  in mind that there is no obligation as long as its only for 
        your own use.   Thanks!  In any case your comments on this either 
        by telephone, email, or mail would be pleasantly accepted.

                             Sincerely, Ray Hallman















                                                           DISKOTIM - 4


        2.   LICENSE AGREEMENT

        YOU  SHOULD READ THE FOLLOWING TERMS AND CONDITIONS BEFORE MAKING 
        USE OF THE PROGRAMS CONTAINED IN THIS PACKAGE.  USING THE PROGRAM 
        PACKAGE  INDICATES  THAT  YOU  ACCEPT  THE  FOLLOWING  TERMS  AND 
        CONDITIONS.

             1.   RAY  HALLMAN provides these program softwares  "as  is" 
                  without  warranty of any kind.   The entire risk as  to 
                  the quality and performance of these programs is yours.

             2.   If  the  programs prove defective,  you  (and  not  RAY 
                  HALLMAN  or any distributor) assume the entire cost  of 
                  all necessary servicing, correction, or repair.

             3.   You may: A) Use these program softwares on a machine at 
                  a single location,  B) Copy these program softwares for 
                  backup  or modification purposes in support of your use 
                  of them at a single location.

             4.   You may NOT:  A) Use,  copy,  modify, or transfer these 
                  program softwares, or any copy, modification, or merged 
                  portion,  in  whole  or in part,  except  as  expressly 
                  provided for in this license,  B) Sub-license,  assign, 
                  or transfer the license or these program softwares.

             5.   This   program  is the property of RAY  HALLMAN,  10120 
                  Pasture Gate Lane, Columbia, Maryland, 21044  (301-730-
                  5624)  (  COMPUSERVE --> 71445,1060 )  all  rights  are 
                  retained  except as provided herein.  A limited license 
                  for  use of versions released prior to May.,  1983   is  
                  granted.   These  early  versions  may  be  distributed  
                  to  software users only,  providing that both the  .EXE 
                  file  and the .DOC files are not separated or  modified 
                  and no costs other than media are charged.   Reports of 
                  bugs will be appreciated. No maintenance is committed.

             ANY  ATTEMPT  TO DO ANY OF THE ABOVE (SECTION 4)  WILL  VOID 
        THIS AGREEMENT.

             RAY  HALLMAN's ENTIRE LIABILITY AND YOUR EXCLUSIVE REMEDY IS 
        THAT YOU MAY TERMINATE THIS AGREEMENT BY RETURNING THESE  PROGRAM 
        SOFTWARES.

             IN  NO  EVENT  WILL RAY HALLMAN BE LIABLE FOR  ANY  DAMAGES, 
        INCLUDING  ANY LOST PROFITS,  LOST SAVING,  OR ANY OTHER  DAMAGES 
        ARISING  OUT  OF  THE  USE OR  INABILITY  TO  USE  THESE  PROGRAM 
        SOFTWARES.















                                                           DISKOTIM - 5


        3.   GENERAL DESCRIPTION AND FEATURES OF "DISKOTIM"

             Congratulations on your acceptance of "DISKOTIM" which shows 
        your  excellent  judgment  of exceptional  value.   For  you  are 
        getting two valuable test and diagnostic tools for 5" drives:

             1.   A  handy  Diskette Drive speed measurement  tool  which 
                  indicates  very  precisely the Rotation Speed in a  non 
                  destructive manner without writing on the diskette.

             2.   A very useful Drive Stepper Utility that enables you to 
                  exercise  your drives without the expensive Disk  Drive 
                  Test Set usually required for this purpose.

             "DISKOTIM"  will work with any Single Sided or Double  Sided 
        Floppy  Drive connected to any IBM-PC Compatible Computer  System 
        running  under  PC-DOS  (MS-DOS).   The program  is  really  self 
        explanatory due to its verbose menu driven format.   THIS PROGRAM 
        UTILITY HAS NOT BEEN TESTED WITH THE PC-jr AND IS NOT EXPECTED TO 
        WORK SINCE THERE IS NO DMA CIRCUIT IN THE PC-jr.  

             This  instruction  booklet  explains  every  detail  of  the 
        program  usage and even goes so far as to provide some commentary 
        on  Drive  Speed Adjustment and Alignment although you  the  user 
        must assume all risk and liability for such adjustment.   In  any 
        case you can easily see if your drive is operating at the correct 
        speed  and thereby eliminate this very important area of concern.  
        The disk drive time check can be done in only a few moments using 
        any PC-DOS (MS-DOS) formatted diskette whenever there is a doubt.  
        No  copy protection scheme is employed so that you may  copy  the 
        program  to your hard-disk for easy usage.   The program does not 
        measure  the  speed  of  hard-disks  which  are  inherently  more 
        accurate  and  therefore  rarely  need  attention.   Some  Floppy 
        Diskette Drives made by some manufacturers are however  notorious 
        in  this  regard as you may see using this program - if  you  are 
        unfortunate to own one of the bad ones.

             The  "Drive Stepping" Utility is more complicated in purpose 
        and  while you may easily exercise your drives with no  risks  of 
        damage  to  them,  the real value comes when used in  conjunction 
        with  a  special  alignment  diskette  which  may  be   purchased 
        separately.  More about this in a later section of this manual.

             Finally,  these  utilities  will  work well with  all  drive 
        position  assignments A:,  B:,  C:,  and D:  from the  easy  menu 
        selection.   No read/write tests are provided by "DISKOTIM" since 
        you  may  verify  read/write using the  normal  "FORMAT"  utility 
        provided with the PC-DOS/MS-DOS System.















                                                           DISKOTIM - 6


        4.   LOADING INSTRUCTIONS



                                    DISKOTIM

                                  IBM DISKETTE

                              LOADING INSTRUCTIONS


        This  program  will  not auto-boot as shipped.   To make  a  self 
        booting disk, use the following procedure:

             1.   Boot  the  IBM-PC compatible machine with  your  system 
                  diskette.

             2.   If  you  have  a  2 disk  system,  place  the  DISKOTIM 
                  diskette in drive B.   (see NOTE below)

             3.   Transfer   your  DISKOTIM.EXE  file  to  the   "SYSTEM" 
                  diskette by entering the following command:

                  COPY B:DISKOTIM.EXE  A:   & CARRIAGE RETURN <ENTER>

             4.   "DISKOTIM"  is started simply by booting the disk  made 
                  in step 3 above and then typing DISKOTIM.

             5.   It  is  strongly  suggested that you  store  away  your 
                  original  copy  now and not use the  original  for  any 
                  testing to protect against accidental loss of DISKOTIM.


        NOTE:     For  single drive systems,  the DOS SYSTEM Diskette  is 
                  considered  as drive A:,  and the DISKOTIM Diskette  as 
                  drive  B:.    Follow  the  prompts  displayed  by  your 
                  Computer System.


























                                                           DISKOTIM - 7


        5.   MAIN MENU

             The  Main  Menu  is displayed as a result of either  of  two 
        operator actions:

             1.   When  the  program  is  initially  invoked  by   typing 
                  "DISKOTIM"  from the Operator Console after the  system 
                  is booted.

             2.   When  "H" is entered from the console after the  prompt 
                  "Next Command?"


        The Main Menu presents 3 groups of commands:

             1.   Commands A, B, C, and D are the Time/Speed Tester.
             2.   Commands I, O, K, L, i, o, k, and l are the Stepper.
             3.   Commands H and Q provide Helps and Quits.


        The Main Menu:

                                      DISKOTIM
                     PERSONAL COMPUTER DISK TESTING UTILITY, V 1.1
                "DISKOTIM" HAS 14 BASIC COMMANDS:
                        A       DISPLAYS THE ROTATION SPEED OF DRIVE A:
                        B       DISPLAYS THE ROTATION SPEED OF DRIVE B:
                        C       DISPLAYS THE ROTATION SPEED OF DRIVE C:
                        D       DISPLAYS THE ROTATION SPEED OF DRIVE D:

                        I       STEPS DRIVE A: IN ONE TRACK
                        O       STEPS DRIVE A: OUT ONE TRACK

                        K       STEPS DRIVE B: IN ONE TRACK
                        L       STEPS DRIVE B: OUT ONE TRACK

                        i       STEPS DRIVE C: IN ONE TRACK
                        o       STEPS DRIVE C: OUT ONE TRACK

                        k       STEPS DRIVE D: IN ONE TRACK
                        l       STEPS DRIVE D: OUT ONE TRACK

                        H       HELPS by re-printing the entry INSTRUCTIONS
                        Q       Quits and RETURNS to the SYSTEM

        Next Command?

















                                                           DISKOTIM - 8


        6.   DISK DRIVE SPEED TESTS

             The  Drive  Rotation  Time (Inverse Speed) Test  Utility  is 
        entered when A, B, C, or D is Keyed from the Main Menu.  When "A" 
        is entered the following appears:



                              DISKTIME for DRIVE A:



                        Insert a Formatted diskette in A


                              Then strike any key.



             At this point the program waits for the operator to indicate 
        that  a diskette is present in Drive A.   When any key is struck, 
        the rest of the Disk Drive Timing Screen appears:



                           STRIKE ANY KEY TO END TEST


                       DISK ROTATION TIME IN MILLISECONDS


                             D I S K - O - T I M E

        197       198       199       200       201       202       203
         |....:....|....:....|....:....!....:....|....:....|....:....|
                                       !


             As  can  be seen above,  The Disk rotation is  specified  in 
        milliseconds by the little "exclamation point" symbol shown under 
        the  200  value.   When the rotation speed is  slow,  the  symbol 
        "needle pointer" moves to the right.   The ideal speed setting is 
        200  milliseconds  as shown.   For most drives,  it is OK if  the 
        meter  reading is within + or - 1 ms or in the range 199  to  201 
        milliseconds.   On  the  following  2  pages,  the  entire  Timer 
        Function  displays are presented for Commands A,  B,  C,  and  D, 
        which are the four Drive Speed Functions.
















                                                           DISKOTIM - 9


                              DISKTIME for DRIVE A:


                        Insert a Formatted diskette in A


                              Then strike any key.



                           STRIKE ANY KEY TO END TEST


                       DISK ROTATION TIME IN MILLISECONDS


                             D I S K - O - T I M E

        197       198       199       200       201       202       203
         |....:....|....:....|....:....!....:....|....:....|....:....|
                                       !

        =================================================================

                              DISKTIME for DRIVE B:


                        Insert a Formatted diskette in B


                              Then strike any key.



                           STRIKE ANY KEY TO END TEST


                       DISK ROTATION TIME IN MILLISECONDS


                             D I S K - O - T I M E

        197       198       199       200       201       202       203
         |....:....|....:....|....:....!....:....|....:....|....:....|
                                       !


















                                                           DISKOTIM - 10


                              DISKTIME for DRIVE C:


                        Insert a Formatted diskette in C


                              Then strike any key.



                           STRIKE ANY KEY TO END TEST


                       DISK ROTATION TIME IN MILLISECONDS


                             D I S K - O - T I M E

        197       198       199       200       201       202       203
         |....:....|....:....|....:....!....:....|....:....|....:....|
                                       !

        =================================================================

                              DISKTIME for DRIVE D:


                        Insert a Formatted diskette in D


                              Then strike any key.



                           STRIKE ANY KEY TO END TEST


                       DISK ROTATION TIME IN MILLISECONDS


                             D I S K - O - T I M E

        197       198       199       200       201       202       203
         |....:....|....:....|....:....!....:....|....:....|....:....|
                                       !


















                                                           DISKOTIM - 11


        7.   DISK DRIVE HEAD POSITION AND TRACK SELECTION

             The  Drive  Execiser Function may be invoked from  the  main 
        menu by entering any of I,  O,  K,  L,  i, o, k, or l.  If "I" is 
        entered the following display is seen on your monitor:


                              STEPPER for DRIVE A:





                        Use I key to STEP IN one Track

                        Use O key to STEP OUT one Track

            Use R key to RESTORE Drive if required after Disk Error

            Use S key to toggle other SIDE of disk, same track position

            Use Q/D Keys to Set QUAD/DUAL Density Drive Parameters


            STRIKE ANY OTHER KEY TO END TEST AND RETURN TO MAIN MENU



         Drive Operating on Side One at Track Number (HEX): 00


        -----------------------------------------------------------------

             As can been seen from the display,  you are presented with a 
        "mini"  Menu  that  is  a list of choices  that  will  cause  the 
        following  different operations or actions for Drive "A:" in this 
        case.   The "I" key "STEPS" the Drive Head Carriage in one  track 
        while the "O" key "STEPS" it out from the center hub.   The track 
        number  is  indicated in HEX at the display bottom.   Under  some 
        circumstances,  disk  errors may occur which can cause  the  head 
        carriage  to get "out of step" with where the computer controller 
        "thinks"  it is.   The "R" command will restore the Drive  in  an 
        attempt  to correct this situation.   The "S" command toggles the 
        "Side Select Bit" from side 1 to side 2 and if pushed again  will 
        toggle  it  back again.   This is useful when comparing the  head 
        response  and  alignment between the 2 sides of  a  double  sided 
        drive.  This is explained in more detail below.  The displays for 
        the other 3 drives are presented on the next two pages.
















                                                           DISKOTIM - 12


                              STEPPER for DRIVE B:




                        Use K key to STEP IN one Track

                        Use L key to STEP OUT one Track

            Use R key to RESTORE Drive if required after Disk Error

            Use S key to toggle other SIDE of disk, same track position

            Use Q/D Keys to Set QUAD/DUAL Density Drive Parameters


            STRIKE ANY OTHER KEY TO END TEST AND RETURN TO MAIN MENU



         Drive Operating on Side One at Track Number (HEX): 00


        -----------------------------------------------------------------

                              STEPPER for DRIVE C:




                        Use i key to STEP IN one Track

                        Use o key to STEP OUT one Track

            Use r key to RESTORE Drive if required after Disk Error

            Use s key to toggle other SIDE of disk, same track position

            Use q/d Keys to Set QUAD/DUAL Density Drive Parameters


            STRIKE ANY OTHER KEY TO END TEST AND RETURN TO MAIN MENU



         Drive Operating on Side One at Track Number (HEX): 00


















                                                           DISKOTIM - 13


                              STEPPER for DRIVE D:




                        Use k key to STEP IN one Track

                        Use l key to STEP OUT one Track

            Use r key to RESTORE Drive if required after Disk Error

            Use s key to toggle other SIDE of disk, same track position

            Use q/d Keys to Set QUAD/DUAL Density Drive Parameters


            STRIKE ANY OTHER KEY TO END TEST AND RETURN TO MAIN MENU



        Drive Operating on Side One at Track Number (HEX): 00  disk error!


        -----------------------------------------------------------------

             Notice  that in the display for drive D:  we show the  error 
        message  "disk error!" that may occur.   This indicates that  the 
        drive  head carriage position is not successfully being  verified 
        by  the drive controller.   When using the Special Alignment Disk 
        you may get this error message.  This is OK and should be ignored 
        since  those  skilled  in  the  art  of  Floppy  Drive  Alignment 
        procedures  can  verify  through experience  that  the  drive  is 
        operating on the proper track.  This is known by the pattern seen 
        using  an oscilloscope during an alignment procedure - more about 
        this later.



        8.   SELECTION OF "QUAD DENSITY" AND BACK TO "DUAL DENSITY" DRIVE 
             PARAMETERS.

             During  the "Stepper Function" the "Q" and "D" (also "q" and 
        "d")  keys  will  function to select the  QUAD  Density  or  Dual 
        Density  drive parameters required for stepping the drive to  the 
        proper track positions.  Use the "Q" and "q" keys to set the QUAD 
        Density   parameters.    You  may  return  to  the  DUAL  Density 
        parameters by using the "D" and "d" keys.  The "Stepper Function" 
        comes up in the DUAL Density mode which is the default mode.
















                                                           DISKOTIM - 14



        9.   USE OF TEST DISKETTES WITH DISKOTIM

             You  may  use  any  test diskette with  "DISKOTIM"  for  the 
        "STEPPER"  Function.   You will however,  get the  "disk  error!" 
        display  for  most  test diskettes since the controller  will  be 
        unable  to verify that the correct track is operating.   You will 
        learn  to ignore this because the familiar test pattern  on  each 
        track will be recognized.   The instruction sheet packed with the 
        test  diskette  will tell you what the test patterns are on  each 
        track.   Test  diskettes are expensive (in the $50 range) and can 
        be obtained from several sources among them are:

             The DYSAN CORPORATION
             5201 Patric Henry Drive
             Santa Clara, California  95050
             (800) 538-8133

             For  DUAL  Density  Drives with 48 tracks/inch  specify  P/N 
        224/2A  which  can  be used for single and  double  sided  Floppy 
        Drives.

             For  QUAD  Density  Drives with 96 tracks/inch  specify  P/N 
        802020-206-30  which  can  be used for single  and  double  sided 
        Floppy Drives also.

             For  the  "TIMER"  Function of "DISKOTIM" you  may  use  any 
        diskette  that  is formatted under the PC-DOS (MS-DOS)  operating 
        system.  The diskette may be write protected if desired since the 
        "TIMER" test is NON Destructive in that it doesn't ever write  on 
        the diskette to measure the floppy drive rotation time.
































                                                           DISKOTIM - 15


        10.   QUITTING FROM THE DISKOTIM PROGRAM BACK TO THE SYSTEM

             You  may exit any test function by striking any  key.   This 
        returns  you to the main menu.   The "Q" command will then return 
        you  to the "SYSTEM" for normal operations.   It is advisable  to 
        "cold  start"  the  computer system after  using  the  "DISKOTIM" 
        program  since certain parameters in the computer may be  changed 
        for  the  convenience of the test program.   You can be  sure  of 
        correct  initial conditions only by a cold restart after  running 
        any test program - this is just S. O. P.

             Finally,  this  program  should not be executed on a  multi-
        user,  multi-tasking  machine such as the Columbia Data  Products 
        Multi-Personal Computer when other users are on the System  since 
        this may alter the other User's processes.

             Other   messages   seen  occasionally  during  the  use   of 
        "DISKOTIM" are presented below:


                        (C) Copyright RAY HALLMAN 1983


                    ***** QUITTING SEQUENCE BY OPERATOR *****


                    ***** SEQUENCE ABORTED BY OPERATOR *****


                ... DONE!


             ***** ERROR *****   Try again!


             ***** NOT IMPLEMENTED! *****


             The  above messages need no discussion and occur as a result 
        of operator action.























                                                           DISKOTIM - 16


        11.  SOME COMMENTARY ON THE DRIVE SPEED ADJUSTMENT

             The  drive  speed  adjustment is easy to  perform  for  most 
        Floppy Drives if you know what you are doing!  The main  mistakes 
        that can cause you the most trouble are:

             1.   Getting the adjustment so far out of alignment that the 
                  controller doesn't function properly.

             2.   Adjusting the wrong adjustment!

             You  must be careful to make small adjustments only.   Also, 
        make sure that you see some effect when you turn the pot 1/4 turn 
        - if  you don't see a change in the time display there is  either 
        something  really wrong with your drive or you are on  the  wrong 
        adjustment!   This  adjustment  is usually found near  the  drive 
        motor  power  wires.   Refer to the Maintenance manual  for  your 
        drives.

        12.  SOME COMMENTARY ON THE DRIVE ALIGNMENT PROCEDURES

             In  general,  you can't make Floppy Drive Alignments  unless 
        you are a qualified repair shop or at least know allot about  the 
        floppy  drives.   The Maintenance Manual for your drives  usually 
        gives  all  the details for this procedure using a  special  test 
        diskette such as the ones mentioned in section 9.

             In  addition  to  the test diskette,  you will need  a  good 
        dual  trace oscilloscope with differential input capability  such 
        as the Tektronix 465.

             The  kinds of checks that are usually made to Floppy  Drives 
        in  the  field  are:

                        C. E. Lobes              track 10
                        Index to Data            track 1 and 22
                        Azimuth                  track 22
                        I.S.V.                   track 5
                        Output Amplitude         track 27
                        Speed                      ---
                        Resolution               track 27

             Tracks  shown  are  for the DUAL Density test  diskette  for 
        example  only - tracks and other instructions are available  with 
        the test diskette.












       example  only - tracks and other instructions are available  with 
        the test diskette.