fixmanul.doc 4-94






                                               


                                               


                                               


                                               


                                               


                                               


                              FIX 4.02 USER'S MANUAL


                                    April 1994


                                               


                                               


                                               


                                               


                                  NovaLogic(TM)
                                13585 SW Pommel Ct
                             Beaverton, OR 97005-7231
                                               
                              voice: (503) 524-9184
                         internet: novalogic@teleport.com
                                               














::

                                               
                                               
                                               
                                               
                                       - i -


                                     CONTENTS
                                               
            Introduction .......................................   1
            
            Uses for FIX .......................................   1
            
            Syntax .............................................   2
            
            Online Help ........................................   2
            
            Specify Strings ....................................   2
            
            Special String Conditions ..........................   3
            
            Specify Input/Output Files .........................   4
            
            Set Alternate Mode of Operation ....................   5
            
            Output .............................................   6
            
            Automatic Protection Re-writing Files ..............   7
            
            Return Code ........................................   9
            
            Requirements .......................................   9
            
            Limits .............................................  10
            
               Appendix A - File FIXing Primer .................  11
            
               Appendix B - Comparison FIX Configurations ......  12
            
               Appendix C - Complementary Batch Utilities ......  13
            
                                               
                              DISCLAIMER OF WARRANTY
                                               
            THIS SOFTWARE AND MANUAL ARE OFFERED "AS IS" AND WITHOUT
            WARRANTIES AS TO PERFORMANCE OR MERCHANTABILITY.  THE FIX
            PROGRAM AND BATCH UTILITIES ARE SOLD WITHOUT ANY EXPRESS
            OR IMPLIED WARRANTIES WHATSOEVER.  BECAUSE OF THE
            DIVERSITY OF CONDITIONS AND HARDWARE UNDER WHICH THESE
            PROGRAMS MAY BE USED, NO WARRANTY OF FITNESS FOR A
            PARTICULAR PURPOSE IS OFFERED.  THE USER IS ADVISED TO
            TEST THE PROGRAMS THOROUGHLY BEFORE RELYING ON THEM.  THE
            USER MUST ASSUME THE ENTIRE RISK OF USING THE PROGRAMS.
            ANY LIABILITY OF LICENSOR/PUBLISHER OR AUTHOR WILL BE
            LIMITED EXCLUSIVELY TO PRODUCT REPLACEMENT OR REFUND OF
            THE PURCHASE PRICE.
            
           Copyright (C) 1993,1994 NovaLogic.  All rights reserved.






::

            
            
            
            
                               Fix User's Manual          Page 1 of 13


            
           INTRODUCTION
           ------------
            FIX is a simple file maintenance utility that will find
            and replace occurrences of any byte string in any size or
            type of MS-DOS[1] file (see Appendix A).  Its virtues are
            flexibility, speed, and built-in data protection.  There
            are 3 configurations of FIX with progressively greater
            functionality (see Appendix B):
            
             (1) FIX 4.02S, the SHAREWARE configuration, provides
                 basic full function but includes a randomly appearing
                 promotional screen;
                 
             (2) FIX 4.02R, the REGISTERED configuration, eliminates
                 the promotional screen, supports 3 alternate modes of
                 operation and delimited findstrings, and includes a
                 larger set of complementary .BAT utilities (see
                 Appendix C);
                 
             (3) FIX 4.02L, the LICENSED configuration, adds multifile
                 capability by accepting the wildcards (?) and (*) in
                 input and output filenames, and adds the ability to
                 guarantee the replacestring is exclusive.
                 
            See the text file FIXLICEN.DOC for the license available
            for each these configurations of FIX.  To register or
            license FIX - print out and use the order form/mailer in
            file FIXORDER.FRM.
            
            
           USES FOR FIX
           ------------
            The most obvious use for FIX is changing the occurrences
            of a misspelled or incorrect word in some body of text.
            While this can be done with your editor or word processor,
            it can be done more quickly using FIX if it's the only
            change to be made.
            
            But FIX can do something that most editors or word proces-
            sors can't, and that is make mass changes to non-printing
            control characters.  This permits changing all single
            spaced lines to double spaced in a large text file, or re-
            formatting a large source code file by shifting all inden-
            ted lines right, or left, by 1 tab.  For more examples see
            ____________________
                 [1] FIX is a trademark of NovaLogic.  NovaLogic is a
            trademark of John F Crist.  MS-DOS and Windows are
            trademarks of Microsoft Corp.  IBM-PC, PC-AT and PS/2 are
            trademarks of IBM Corp.  8086, 8088, 80286, 80386, 80486 &
            Pentium are trademarks of Intel Corp.






::

            
            
            
            
                               Fix User's Manual          Page 2 of 13


            the included .BAT utilities.  FIX may also be used on
            binary files to "patch" small portions of code or data.
            
            The power of FIX becomes more apparent in the LICENSED
            configuration which enables the user to address a set of
            files.  This makes it possible to correct a word which may
            have occurred any number of times in each of the multiple
            files which comprise some very large document.  Or you may
            update the version and date information that appear in the
            headers of a large set of source modules that make up a
            computer program.  Judicious application of Licensed FIX
            can save the user many keystrokes in maintaining a large
            set of related files.
            
            
           SYNTAX
           ------
           
            FIX  [-c|-q|-f]  FINDSTRING  REPLACESTRING
                               [d:][path]FILENAME  [d:][path][outfIle]
            
            The mandatory command line arguments are: (1) findstring,
            (2) replacestring and (3) filename.  Optionally the user
            may specify an output filename, and may also specify disk
            drive(s) and directory path(s) for input and/or output
            files.  FIX also accepts an optional mode switch[2] as the
            first argument, and the LICENSED configuration accepts the
            wildcard characters (?) and (*) in filenames.  Command
            line arguments are separated by one or more spaces.
            
            
           ONLINE HELP
           -----------
            An online help screen may be displayed by entering the
            command  >fix  with no arguments.  Additional help
            specific to any of the alternate operating modes  may be
            displayed by including the mode switch as the only
            argument:  >fix -q.
            
            
           SPECIFY STRINGS
           ---------------
            A byte string may be specified by:
            
             (1) enclosing it in quotes - "string", or enclosing in
                 brackets or braces to impose certain conditions.
             (2) a sequence of decimal byte values separated by
                 commas - 115,116,114,105,110,103
            ____________________
                 [2] Supported in the REGISTERED and LICENSED
            configurations of FIX.






::

            
            
            
            
                               Fix User's Manual          Page 3 of 13


             (3) a sequence of hex byte values terminated by 'h'
                 or 'x' - 737472696e67h [3]
             (4) or by any combination of these - "st"114,105,6e67h
                 
            Single quote marks may enclose double quotes or vice
            versa.  The null string may be specified by adjacent
            quotes ("").  This provides for convenient representation
            of any contiguous sequence of printable characters or
            unprintable bytes.  Examples of string specification:
            
              Command Line String Specs       Resulting String Change
              -----------------------------   -----------------------
              fix  'Smith'  'SMITH'  file     Smith -> SMITH
              fix  "'no'"  '"no"'  file       'no' -> "no"
              fix  'impossible'  ''  file     delete word impossible
              fix  13,10  13,10,13,10  file   1X spaced lines -> 2X
              fix  0d0ah  0d0a0d0ah  file     1X spaced lines -> 2X
              fix  13,10't'  13,10'T'  file   t -> T, if t starts line
              fix  0909h  090909h  file       2X horizontal tab -> 3X
            
            
           SPECIAL STRING CONDITIONS
           -------------------------
            Special string conditions may be specified in the FIX
            command line, accomplished by the use of string delimiting
            marks other than quote marks ("")('').  Brackets specify a
            "delimited" [findstring] in the REGISTERED and LICENSED
            configurations of FIX.  And the LICENSED configuration
            also supports 2 special conditions for replacestrings:
            braces specify an "exclusive" {replacestring}; and
            brackets specify an "exclusive-delimited" [replacestring].
            The following describes each of these 3 special string
            conditions in more detail.
            
            Brackets specifying a [findstring] define a DELIMITED
            FINDSTRING.  This requires that a matching string be
            "delimited" - immediately preceded and followed by
            delimiting characters - in order to be selected from a
            body of text.  For example the findstring spec [to] would
            select the "to" in " go to ", but not the "to" in
            " tomorrow ".  A delimiting character is defined here as
            any byte value that is not in the alphanumeric characters:
            (0-9), (A-Z), (a-z), or (_).
            ____________________
                 [3] Each byte must be represented by 2 hexidecimal
            digits regardless of byte value; the 2 hex digits are
            entered conventionally with the high order digit first.
            However, the bytes are entered in "string" order - low
            byte to high byte as arrayed in memory - not the high to
            low byte order conventionally representing a multi-byte
            binary number.






::

            
            
            
            
                               Fix User's Manual          Page 4 of 13


            
            Braces specifying a {replacestring} define an EXCLUSIVE
            REPLACESTRING.  Exclusivity requires the only occurrences
            of replacestring in the addressed file(s) to be those that
            are inserted by FIX.  This is accomplished in two passes
            through the file set.  In the first pass FIX scans all
            addressed files for pre-existing occurrences of
            findstring.  If any are found the run is aborted.  If none
            are found, FIX makes a second pass through the file set to
            replace findstrings with the replacestring now known to be
            "exclusive".
            
            Brackets specifying a [replacestring] define an EXCLUSIVE-
            DELIMITED REPLACESTRING.  FIX may insert replacestring in
            the file(s) only if the files contain no pre-existing
            "delimited" replacestrings (non-delimited replacestrings,
            however, are allowed).  Again FIX makes 2 passes through
            the file set to satisfy the replacestring condition.
            
            Delimited [findstring] and exclusive-delimited [replace-
            string], together, are useful for changing variable names
            in computer programs, especially when the variable names
            are short and the program source file(s) are large.  These
            special string conditions assure that: (1) only variable
            names will be changed, and (2) the new name is not already
            in use for some other variable.  Example:  fix [i] [j] *.c
            
            Note that a string with special conditions may still be
            specified by a combination of means including quoted,
            decimal and hex elements; however, if any of a string's
            elements are specified in brackets [] or braces {}, the
            special condition is imposed on the entire string.  For
            example the string spec:  "st"7269h[ng]  will treat the
            entire [string] as delimited
            
            To provide the user some flexibility, certain special
            characters may serve as alternatives or back-ups to the
            quote marks, brackets or braces used to specify strings.
            The following groups of delimiter pairs are equivalent in
            effect:  (""  ''  !!  @@),   ([]  ##  $$),   ({}  %%  ^^).
            
            
           SPECIFY INPUT/OUTPUT FILES
           --------------------------
            The behavior of FIX in response to user specification of
            input and output files conforms to conventions established
            by the familiar "COPY" command of MS-DOS.  When the disk
            drive [d:] or directory path [path] is left unspecified,
            they default to the current drive or directory.  And when
            the user does not specify the output filename [outfl], it
            defaults to the input filename.






::

            
            
            
            
                               Fix User's Manual          Page 5 of 13


            
            There is, however, an exception to conformance to the COPY
            behavior model.  It is not possible to COPY a file onto
            itself, but it is often convenient to FIX a file onto
            itself within the current directory.  FIX provides the
            capability of re-writing a file in-place, while preserving
            it's original contents in a .BAK file.  This is accom-
            plished by omitting any output filespec when working on a
            file in the current directory.  Example:  fix 'a' 'b' text
            
            
           SET ALTERNATE MODE OF OPERATION
           -------------------------------
            The REGISTERED and LICENSED configurations of FIX provide
            three alternate modes of operation.  These may be invoked
            by inserting an optional "mode switch" as the first
            argument in the command line.
            
             QUERY MODE (switch: -q, or -?):
                 Query Mode enables the user to cancel changes to a
                 file after informing the user of the number of
                 strings that that will be changed.  FIX makes a first
                 pass through the input file to count occurrences of
                 findstring, then presents this number to the user
                 along with 3 options: (Yes/Cpy/Esc).  If the user
                 responds "Y" then occurrences of findstring will be
                 changed to replacestring in a second pass through the
                 file.  With the "C" response, FIX makes no changes to
                 text but will copy the input file to the output file.
                 Pressing the <Esc> key will cancell any further
                 action on the current file and proceed to the next
                 file in sequence.  The query mode helps the user to
                 avoid the "surprise" of unintended changes.
                 
             COUNT MODE (switch: -n, or -#):
                 Count Mode displays the count of findstring
                 occurrences in each file without making changes to
                 the file.  It's action is similar to that of the
                 "grep -c" command of the UNIX operating system,
                 except that string content here is not confined to
                 the printable ASCII characters.  Count mode command
                 syntax:  FIX -C  FINDSTRING  [drive:][path]FILENAME.
                 Count mode presents the user with another means for
                 examining a set of files before committing to change.
                 
             DOS FILTER MODE (optional switch: -f):
                 Filter Mode enables FIX to work with piped ( | ) or
                 redirected (<),(>) I/O rather than with file set(s)
                 specified in the command line.  The mode switch
                 forces FIX into Filter Mode and assures correct error
                 messages if there is a syntax problem.  However, if






::

            
            
            
            
                               Fix User's Manual          Page 6 of 13


                 FIX senses piped or re-directed input (Standard Input
                 other than the system console), it will switch to
                 Filter Mode automatically without the mode switch
                 being set.  Once in Filter Mode, FIX reads input text
                 from the Standard Input Device and writes output text
                 to the Standard Output Device.  If Standard Output
                 has not been redirected from the console, the FIX
                 activity report is suppressed so that only the output
                 text will appear on the screen.  If Standard Output
                 has been re-directed, FIX writes it's activity report
                 to the system console screen as usual.
                 
                 In Filter Mode FIX can work in series with other
                 Filter programs such as SORT and FIND provided with
                 MS-DOS.  This provides the user with the power and
                 flexibility of performing ad hoc text manipulations
                 as a piped series of filter operations.  Filter Mode
                 syntax:  [filter | ]  FIX  [-c|-f]  FINDSTRING
                 REPLACESTRING  [<infile]  [>outfile]  [ | filter].
                 Note that Count Mode and (implicit) Filter Mode are
                 compatible.
                 
                 
           OUTPUT
           ------
            FIX processing results in 2 bodies of text: (1) the origi-
            nal text, and (2) text that has been altered by replacing
            occurrences of findstring with replacestring.  FIX always
            leaves both bodies of text in file(s) at the conclusion of
            processing.  The attributes and identities of these files
            vary depending on the results of processing, and the
            user's intentions expressed in command line filespecs.
            
            The following rules apply to the attributes and identity
            of resulting text files:
            
             (1) A file containing original text always bears the
                 date/time stamp of the original text.
             (2) A file containing text that has been changed is
                 always stamped with the date/time of FIX processing.
             (3) When the user specifies different directories, or
                 different names, for the input and output files:
                  a) except for being read, the input file is
                     untouched;
                  b) a separate output file is always generated
                     regardless of changes to the text, and it over-
                     writes any pre-existing file with the same name.
             (4) When the user specifies only the input filename(s) in
                 order to FIX the file or set of files onto itself:








::

            
            
            
            
                               Fix User's Manual          Page 7 of 13


                  a) if no changes are made to text (no occurrences of
                     findstring), the input file and directory remain
                     untouched;
                  b) if text is changed, the input file is renamed
                     with a .BAK extension and the output text is
                     given the input filename; the .BAK file replaces
                     any pre-existing file with the same name.
                     
            FIX displays a one line report for each file that is pro-
            cessed. It includes: the input filename, the output
            filename (if different from the input filename), and the
            number of occurrences of findstring that were changed.
            Additionally, if wildcards were used to process a set of
            files, the report includes the sequence number of each
            infile and, at the conclusion of processing, the total
            number of strings and files that were changed.
            
            
           AUTOMATIC PROTECTION WHEN RE-WRITING FILES
           ------------------------------------------
            In order to insure protection of original data when
            FIX'ing a file or set of files onto itself in the current
            directory, the FIX program must impose certain constraints
            on the filespecs it will accept:
            
             (1) It is not possible to FIX a file with a .BAK
                 extension onto itself within the current directory.
                 
                   fix  'a'  'A'  filename.bak               : No
                   fix  'a'  'A'  filename.txt               : ok
                   fix  'a'  'A'  filename.bak  newdir       : ok
                   fix  'a'  'A'  filename.bak  newname.bak  : ok
                 
                 If the input file has a .BAK extension and is FIX'ed
                 onto itself, the changed file text would over-write
                 the original data in its own .BAK file.
            
            The LICENSED configuration of FIX supports the wildcard
            characters (?), (*) in filename specification.  Here again
            the behavior of FIX conforms to the COPY model.  Wildcards
            used in specification of the infile are applied in search-
            ing the directory for matching filenames.  Wildcards in
            the output filespec are applied to the actual name of the
            input file to generate a corresponding name for the output
            file.  See the MS-DOS 5.0 User's Guide, "Using Wildcards",
            for more detail.
            
            Wildcards introduce the need for additional interlocks to
            protect original data from filespec mishaps when perform-
            ing operations entirely within the current file directory.
            FIX imposes two more constraints which eliminate the






::

            
            
            
            
                               Fix User's Manual          Page 8 of 13


            possibility of over-writing original data (within a single
            FIX run) when processing multiple files:
            
             (2) When FIX'ing a set of files onto itself within the
                 current directory you may not use wildcard characters
                 in the filename extension:
                 
                   fix  'a'  'A'  flname.tx?           : No
                   fix  'a'  'A'  *.txt                : ok
                   fix  'a'  'A'  flname.tx?  outdir   : ok
                 
                 Wildcards in the filename extension when FIX'ing-to-
                 self would permit a back-up file to be overwritten by
                 a subsequent back-up file in the same run.
                 
             (3) When using wildcards in infilespec and outfilespec to
                 FIX a set of files onto another set of files within
                 the current directory, the two specified sets of
                 filenames may not intersect (include names in
                 common):
                 
                   fix  'a'  'A'  file*.*    ????name.*    : No
                   fix  'a'  'A'  file*.??a  *.??b         : ok
                 
                 Intersecting filespecs would permit an output file to
                 over-write an input file that is yet to be processed
                 in the same run.
             
                 Intersecting filespecs is an insidious problem
                 encountered with complicated wildcard filespecs.
                 It can be avoided by assuring that infilespec and
                 outfilespec have at least one parallel character
                 position with different (non-wildcard) characters -
                 see 2nd example in (3) above.
                 
                 Note that the outfilespec (*.*) creates a special
                 case when no drives or paths are specified.  It is
                 FIX'ing-to-self made explicit, and so is treated
                 under constraints (1) and (2) above.
            
            FIX checks for each of these three kinds of data threat-
            ening filespec errors, and stops and issues a message when
            they are detected.  It must be emphasized, however, that
            these three interlocks can prevent over-writing: (1) only
            the original data addressed by infilespec, (2) only with-
            in a single invocation of FIX.  The user must define file-
            specs so that important "other" files (not addressed by
            infilespec) are not overwritten.  And the user must be
            aware, when FIX'ing-to-self, that 2 runs changing the same
            file will over-write original data in the .BAK file.
            






::

            
            
            
            
                               Fix User's Manual          Page 9 of 13


            As a matter of routine you should make back-up copies of
            important data before any kind of processing which, like
            FIX, transforms the contents of a file.  Do not rely
            solely on software's safety features and "being careful".
            
            
           RETURN CODE
           -----------
            The FIX program returns the number of strings processed in
            an 8 bit "return code" which is passed to MS-DOS at the
            conclusion of processing.  The purpose is to report the
            results of processing back to a parent program.  This
            return code may be accessed in a batch (.BAT) program by
            examining the ERRORLEVEL variable after FIX is run.
            
            An ERRORLEVEL of N, with N = 0, 1, 2, 3, ..., 252
            indicates the run was successful with N occurrences of
            findstring changed to replacestring across all files
            examined.  (Or, when the -n switch in the command line has
            invoked "count only" mode, N represents the number of
            occurrences found.)  In the special case when N = 252, the
            return code indicates that 252 or more strings were
            changed.  The return code for a successful run may not
            exceed the upper bound of 252 regardless of the number of
            strings changed.
            
            The 3 remaining possible values for the 8 bit return code
            are reserved for actual errors as follows:
            
               253  FDh  : Syntax Error
               254  FEh  : Wildcard Filespec Threatens Original Data
               255  FFh  : File Access Error
            
            
           REQUIREMENTS
           ------------
            FIX will run on any of the IBM-PC, PC-AT, PS/2 or com-
            patible series of personal computers based on the Intel
            8086, 8088, 80286, 80386, 80486 or Pentium micro-
            processors.
            
            FIX runs in the MS-DOS operating system, version 2.1 or
            higher.  It also runs in any operating environment that
            supports programs written for MS-DOS, this includes OS/2,
            Windows and Windows NT.
            
            FIX requires a computer with 128K system memory.  It
            occupies only 64K of memory when running.
            
            







::

            
            
            
            
                               Fix User's Manual          Page 10 of 13


           LIMITS
           ------
            The size of file which may be processed is limited only by
            the computer's available disk space.  For a file to be
            processed successfully there must be enough free space on
            the output drive to hold the new copy of the file's text
            after all specified string changes have been made.  If the
            available disk space is found to be insufficient, proces-
            sing is halted, the partial output file is deleted, and
            the error message "Insufficient disk space" is displayed.
            
            The buffers provided in FIX to hold findstring and re-
            placestring are each 128 bytes in size.  As a practical
            consideration, however, these strings are limited by the
            maximum possible length of the command line which is 127
            bytes in MS-DOS.  So the maximum length of either string
            is 127 bytes less the "overhead" characters required to
            represent the string itself, less the number of characters
            required to represent and separate the other string and
            all other elements of the command line.
            
            The number of strings which FIX may find and replace in a
            single file, or over multiple files, is unlimited.  How-
            ever, the largest integer value which may be formatted for
            display on the screen is 655,359.  If a string count
            exceeds this limit, a field of asterisks "*******" is
            displayed.
            
            When replacestring is longer than findstring there is a
            limit to the expansion possible for a given block (or
            record) of text.  The limiting expansion ratio is approx-
            imately 3:1 for each 20K-byte block.  This means that the
            number of string occurrences replaced, times the differ-
            ence of replacestring length minus findstring length, may
            not exceed 40K-bytes for any 20K-byte block of original
            text.  If the text expansion ratio is exceeded, processing
            is halted, the partial output file is deleted, and the
            error message "File expansion too great" is displayed.
            


















::

            
            
            
            
                                Fix User's Manual         Page 11 of 13


                                    APPENDIX A
                                               
                                FILE FIXING PRIMER


            When using FIX to make changes to a file you must be aware
            of the file's purpose and content, and limit changes
            accordingly to avoid "corrupting" the file.  The following
            describes 3 broad categories of MS-DOS file with necessary
            limitations on the ways they may be changed:
            
             (1) ASCII Text Files - contain the printable ASCII (or
                 extended ASCII) characters, together with ASCII print
                 control characters.  They can be TYPE'd to your video
                 screen, and read.  The filename extensions .DOC, .TXT
                 or .ASC usually indicate the file contains ASCII
                 text.  Computer program source code files are another
                 example of plain ASCII text.  Any text change that
                 remains within the ASCII character set is permitted.
                 Printable ASCII character strings are specified for
                 FIX by enclosing them in quotes.  The ASCII control
                 characters must be specified by their decimal or
                 hexidecimal byte values.
                 
             (2) Fixed Field Data Files - are made up of records, or
                 contain certain fields, which are fixed in length and
                 must remain so.  Data base files, spread sheet files,
                 and many word processor files are examples of fixed
                 field data.  The data may be ASCII or binary.  When
                 you change a fixed length field, replacestring length
                 in bytes must equal findstring length.
                 
             (3) Binary or Executable Files - contain machine code,
                 instructions to be read/acted upon by a microproces-
                 sor.  When TYPE'd to the screen a binary file
                 displays garbage characters.  Examples include files
                 with the .COM or .EXE name extension which are
                 invoked at the command line when you run a program.
                 Changes to these files must be made cautiously,
                 normally with explicit instructions from the
                 program's author.  Not only must (a) replacestring
                 length equal findstring length, but (b) the changed
                 bytes in replacestring must constitute legitimate
                 microprocessor instructions, and (c) the instructions
                 must be appropriate within the larger context of the
                 program's logic.  "Strings" in binary files are
                 commonly represented by the hexidecimal value of each
                 byte.
                 
            







::

            
            
            
            
                                Fix User's Manual         Page 12 of 13


                                    APPENDIX B
                              COMPARISON OF FEATURES
                           THREE CONFIGURATIONS OF FIX


                                                FIX Configuration
                                       -------------------------------
                                         4.02S      4.02R       4.02L
            Performance Features:      Shareware  Registered  Licensed
                                       ---------  ----------  --------
                 Randomly Appearing
                   Promotional Screen ..  [Yes]      [   ]       [   ]
            
                 Three Alternate
                   Modes of Operation ..  [   ]      [Yes]       [Yes]
            
                 Larger Set of
                   Batch Utilities .....  [   ]      [Yes]       [Yes]
            
                 Delimited
                   Findstring Option ...  [   ]      [Yes]       [Yes]
            
                 Two Exclusive
                   Replacestring Options  [   ]      [   ]       [Yes]
            
                 Accepts Wildcards
                   in Filenames ........  [   ]      [   ]       [Yes]
            
            Commercial Features:
            
                *PRICE from NovaLogic
                   incl Shipped Disk ...   $5        $11       $19/1st
            
                 Current Version
                   of Software .........  [ @ ]      [Yes]       [Yes]
            
                 6 Months Email or
                   Telephone Support ...  [   ]      [Yes]       [Yes]
            
                 1 Year Updates at
                   Shipped Disk Cost ...  [   ]      [Yes]       [Yes]
            
                 Use in Commercial
                   Applications ........  [   ]      [   ]       [Yes]
            
                 Site License for
                   Multiple Computers ..  [   ]      [   ]       [Yes]
            ______________________
            [*] Prices 1April94; subject to change.
            [@] Shareware config current if ordered from NovaLogic.







::

            
            
            
            
                                 Fix User's Manual        Page 13 of 13


                                    APPENDIX C
                                               
                          COMPLEMENTARY BATCH UTILITIES


            A set of batch (.BAT) utilities which invoke FIX is
            included in the distribution file set.  They perform pre-
            specified editing functions on ASCII text files.  Their
            purpose is to extend the usefulness of the FIX program;
            and also to provide models for users' development of .BAT
            programs or key macros for their own common editing tasks.
            
            Entering the command "FIXUTILS" at the command prompt will
            display an on-line help screen providing an overview of
            the utilities.  Following are utility names and functions:
            
                 X2LINES   - Doubles the spacing of each line of
                             text.
                 D2LINES   - Changes each double spaced line to a
                             single spaced line.
                 X2TABS    - Replaces each (horizontal) tab with 2
                             tabs.
                 D2TABS    - Replaces each adjacent pair of tabs with
                             a single tab.
                 INDENT    - Inserts 1 tab at the beginning of each
                             line (except 1st line).
                 UPINDENT# - Adds 1 more indentation tab to the begin-
                             ning of each indented line (except 1st).
                 DEINDENT# - Deletes 1 indentation tab from the begin-
                             ning of each indented line (except 1st).
                 SPACE2#   - Reduces each contiguous sequence of
                             spaces to 2 spaces (an iterative appli-
                             cation which acts on feedback from FIX).
                 SHIFTBRL# - Shifts braces ({),(}) in C source file(s)
                             to the left 1 tab.
                 SHIFTBRR# - Shifts braces ({),(}) in C source file(s)
                             to the right 1 tab.
            
            The command line syntax, which is common across all of
            these utilities, is:
            
                 UTILNAME [d:][path]FILENAME  [d:][path][outfile]
            
            For on-line help that is specific to the utility, enter
            the utility name with no arguments.
            
            ______________________
            [#] Provided with Registered and Licensed configurations
                of FIX.








::