1.                HARD DISK PREPARATION program 3.33
                  KFH ASSOCIATES,           1985
                  2771, Middleborough
                  SAN JOSE, CA 95132

                   FOR IBM PC   AND  XT & COMPATIBLES
                   AT needs HDPREPAT.exe
                         DOS 2.0/2.1/3.0/3.1

                   ALSO  XEBEC 1210A
                         DTC   5150BX
                         ADAPTEC 2002A
                         W DIGITAL 1002
                         ETC. PC CONTROLLER BOARDS

                  ** If you think the program is useful  to you,
                     $35.00 donation to    H. King   at above
                     address will register for updating service

 a. 3.3 reduce the program size and enhcanced the option 3 option
 b. Enhanced the track entering and display feature
 c. Added the scan track feature to locate the already marked track
    in option 7 and 8.

2.  The program READ in the hard disk drive parameters from the
    controller to determine the available number of heads and cylinders
    for each attached drive, if the controller follows the IBM BIO
    convention. Otherwise, the program defaults to 2 head and 100
    cylinders for each drive. When this happens, the controller usually
    has problem. You can use option 9 to change this settings, if you
    have an Adaptec controller.

3.  Hard disk preparation uses the controller default parameters in the
    BIOS.

Instructions:

The program is manual driven and self explanatory. The following is a
summary.

Options:

1. Select the drive to be operated on. Drive 0 is the first hard disk
   drive attached to the controller (usually the C:), Drive 1 is the
   second one (usually the D:).

2. Perform the controller FORMAT of the specified drive by option 1.
   See option 3. Run FDISK and Dos FORMAT after this step.
   Bad track locations can be input at this step and the program
   will use the input to mark the bad ones accordingly.

3. Perform the controller FORMAT of the specified drive by option 1
   and scan the disk for bad tracks and mark them bad. Run FDISK and
   DOS FORMAT after this step. This option 3 is preferred to option 2.
   In the begining of this step, you can enter the bad tracks if you
   already know them.  This step marks  any bad track found,
   the ones you entered,  at the end of the process.

4. Move the head to track 0 for the specified drive.

5. Exit this program.

6. Set the interleave number for the controller FORMAT. The default is
   6 which is used by IBM PC/XT. Do not use other number unless you
   have enough knowedge on the controller. Adaptec controller can use
   interleave 2.

7. If you know a specific track and head location is bad, you can use
   this option to mark the track bad. Use DOS FDISK AND FORMAT after
   this step.

   Option allows the program to scan the drive and lists tracks that
   already marked bad.

8. If you want to remark a bad track to reuse the track, you can use this
   option. This option can not physically correct the defect track.

   Option allows the program to scan the drive and lists tracks that
   already marked bad.

9. Use this option to define the number of heads and cylinders for each
   drive for this program to use. This parameter does  overwrite
   the controller defined parameter and affect the controller FORMAT
   operation. The BIOS parameters are not affected. Warning: The DOS
   FORMAT uses BIOS parameters.

   However, the ADAPTEC 2002A is an exception, the overwrite parameters
   are recognized by DOS Fdisk and Format programs.

A. The same operation as the option 3, except during the verify process
   more data patterns are used. The process can take twice longer then
   the option 3. Usually, the option 3 is good enough.


Note:

   At option 2,3,7 and 8, head and track location input feature allows
   the number entering easier and can be edited later. Once the total track
   location display is on, you can use the cursor key to move the
   pointer (reversed video) to different line/column and use command
   to change (C),  remove (R), Re-enter every thing (N), go ahead to
   proceed (Y). The editing options are displayed at the bottom of the
   screen for reference.

   If a new item need to be added, use cursor key to move the pointer
   to a location that does not have any entry, hit "C" - change, head
   number and cylinder number can then be added.