+-------------+
                         |  RAMIT!!!   |
                         +-------------+



     If you're  running an  8-bit hard disk controller (generally
     designed for  both PCs and ATs) on a 16 bit machine (like an
     AT or  AT&T PC6300)  then RAMIT!  may be  able to  help  you
     improve your disk transfer speed.




     What is RAMIT?
                              RAMIT is  a program to run the disk
                              code supplied  with an PC type disk
                              controller out  of RAM  rather than
                              from the disk controller's ROM.

     What does that do?
                              By running  out of  RAM rather than
                              ROM, some  machines can  achieve  a
                              real  performance   gain  in   disk
                              transfer time.

     Does this apply to
     me?
                              RAMIT can  make a  difference in  a
                              number of  situations.   To see any
                              disk performance improvement,

                              1. You  must be  using a  hard disk
                              controller which  has its  own BIOS
                              ROM code.  This includes unmodified
                              Western Digital,  Mountain, Perstor
                              and  Plus  [Hardcard]  controllers.
                              Undoubtedly there are many others.

                              2. You  must have  a machine  which
                              runs code  faster from RAM than the
                              I/O bus.  This includes all 16 bits
                              machines (AT  types) and many other
                              compatibles (e.g. AT&T PC6300).

                              3.  You must be willing to reformat
                              your hard  disk to  get the benefit
                              of this  speedup.   Naturally, this
                              requires a full backup and restore.

     Still Interested?
                              Read on.





RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988







              +-----------------------------------+
              |  OK, so what does RAMIT! do!!!!   |
              +-----------------------------------+


RAMIT! is a TSR which relocates your disk controller ROM into
high-speed RAM and 'fixes up' MSDOS to run the disk code from
RAM.

RAMIT! operates as follows:

     1. RAMIT!  verifies that  there  is  a  valid  ROM  BIOS  at
     C800:0000.

     2. RAMIT! copies the disk ROM contents to RAM.

     3. RAMIT!  disassembles the  ROM to  find out  what  it  had
     placed in vector locations 4C and 64.  These are the primary
     entry points  into the  ROM code.   If  RAMIT! is  unable to
     determine  these  values,  then  it  aborts  with  an  error
     message.   This is  generally  attributable  to  an  unusual
     instruction sequence  used to  'steal' the vectors.  Contact
     the author for unusual ROMs.

     If you'd rather do the disassembly yourself, the original 4C
     and 64  vector addresses  can be  specified on  the  command
     line.   This is  the dirty  way to support controllers whose
     initialization sequence  is simply  too messy  for automatic
     decoding.

     If RAMIT! 'knows' about your ROMs, it knows which 4C, 64 and
     edit parameters  to use.   RAMIT  calculates a  CRC for  the
     resident portion  of a  ROM and scans an internal table.  If
     your ROM  is not in the table, contact the author and supply
     a floppy disk with the ROM on it.

     4. RAMIT!  'fixes' MSDOS or PCDOS by finding where DOS keeps
     the vector  originally placed  by  the  disk  ROM  BIOS  and
     redirecting it to the RAM copy.

     5. RAMIT!  exits, leaving  only a  copy of  the vendor's ROM
     code.   All RAMIT! code is removed.  Most unused ROM code is
     also removed.   The  amount of  memory taken  depends on the
     size and  complexity of the disk controller ROM BIOS.  In no
     event will it be more than 8K of code.












RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988








                +----------------------------+
                |  Well how do I run RAMIT?  |
                +----------------------------+




Find out your current performance level

     Before seeing whether RAMIT! can make a difference, you must
     know how your system performs before RAMIT! is installed.

     If your  disk/PC combination  is not explicitly mentioned in
     the README.RAM  file in  this archive  (and you  can't  find
     another PC close enough), then you may have to experiment to
     find the best interleave factor.

     SPINTEST is a publicly available utility which computes disk
     transfer rate.   It  can be  used to  see when  the  optimum
     interleave has been established.

     Another program, ATDISK, often distributed as part of the PC
     Tech Journal utilities will calculate the transfer rate.

     Finally, the  CORETEST program  from Core International will
     compute the  transfer rate.   Any  of these  programs can be
     used to  determine when  the  optimum  interleave  has  been
     found.

     First, run SPINTEST to get the transfer rate and interleave.
     Then  reduce   the  interleave  until  you  suddenly  see  a
     reduction in  the transfer  rate.  At that point you've gone
     too far!  Back off by increasing the interleave slightly and
     reformat for the last time.

     MAKE SURE  THAT YOU'VE  INSTALLED RAMIT  BEFORE RUNNING  ANY
     PERFORMANCE TEST.   IF YOU HAVEN'T YOU'RE JUST MEASURING THE
     PLAIN  VANILLA  PERFORMANCE  OF  YOUR  CONTROLLER  ROM-BASED
     SOFTWARE!!!

     The following may serve as an example:
          Set IL=6; Spintest says 6 revolutions to read a track.
          Set IL=5; Spintest says 5 revolutions to read a track.
          Set IL=4; Spintest says 4 revolutions to read a track.
          Set IL=3; Spintest says 18 revolutions to read a track.

          At this  point, going  to an  interleave of 3 does more
          harm than good.  Back off and use an interleave of 4.



     An easier  way is  to install  RAMIT and  use one of several
     programs which  promise to determine the optimum interleave.



RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988







     ILEAVE19.ARC (a public domain program) and Gibson Research's
     SPINRITE (definitely  not in the public domain) are two such
     programs.  Please note that it is critical to install RAMIT!
     before running  these test  programs  otherwise,  you'll  be
     getting the best value without RAMIT!.


Testing RAMIT! the first time

     At first,  RAMIT! should  be run  in TEST  mode.   This will
     indicate whether RAMIT! is likely to work on your machine.

     Type

          RAMIT /T

     and examine  the output.   There  should be  three  messages
     indicating that  0000:xxxx  has  been  overwritten.    Don't
     worry, in TEST mode the memory is not actually modified.

     If RAMIT!  fails or  the messages  don't appear,  check  the
     README.RAM file in this archive.  If your drive and computer
     isn't on  the list,  be careful.   Things  may very well not
     work.

     If you  get no error messages, RAMIT! will probably work for
     you.

     The following  is a sample installation using the /V option.
     (Specifying /T assumes /V.)

        > RAMIT /V
          RAMIT!    [V1.6]  Copyright (c)  1988 Hanover  Systems.
          All rights reserved.                   ]  Version

          Disk controller vector 1B at C800:0A79 moved to segment
          0DB2
          Overriding segment address at 0000:1ECB  +  Expect 2
          Overriding segment address at 0000:2618  +  Messages
          Disk controller vector 25 at C800:09A8 moved to segment
          0DB2
          Overriding segment address at 0000:261C  ] Expect 1 Msg

          Editing segment reference at 06C0        +
          Editing segment reference at 06EC        |
          Editing segment reference at 0AD2        |
          Editing segment reference at 0B59        |  From
          Editing segment reference at 0CF4        |  C800
          Editing segment reference at 0D55        |  Segment
          Editing segment reference at 0E17        |  References
          Editing segment reference at 0F19        |
          Editing segment reference at 1128        |
          Editing segment reference at 125E        +




RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988







          [OEM Disk BIOS] (c) copyrignt XYZZY company.





Installing RAMIT!

     WARNING: BEFORE  INSTALLING RAMIT! MAKE SURE THAT YOU HAVE A
     FULL  BACKUP  OF  YOUR  HARD  DISKS.    RAMIT!  CHANGES  THE
     OPERATION OF  YOUR HARD  DISK CONTROLLER.   WHILE RAMIT! HAS
     NOT CAUSED  ANY PROBLEMS  SO FAR, IT HASN'T BEEN RUN ON YOUR
     MACHINE!!!!  TAKE PRECAUTIONS AND MAKE A BACKUP!!!!

     RAMIT! is installed for normal use by typing

          RAMIT

     You should  see two  messages: the  standard RAMIT!  version
     header and  an identification  for the  disk controller  ROM
     BIOS.

     Continue normal  operation with  RAMIT! for  a while.    You
     should not  see any  performance change.    Just  make  sure
     things are still working.

     RAMIT! should be placed in the AUTOEXEC.BAT file as near the
     top as  possible.   The earlier  it's executed, the more the
     AUTOEXEC.BAT programs  will  benefit  from  any  performance
     improvement.





Tuning up your disk performance

     To see  a real  performance difference, you'll probably have
     to reformat  your disk.   This  requires a low-level format,
     not just a DOS format (i.e. the FORMAT command).

     For Western  Digital customers,  enter  DEBUG.    Old  cards
     require that  AX be  set to the interleave.  On newer cards,
     the ROM  code prompts  for the interleave.  Start the format
     by typing 'G =C800:5'.

     OMTI customers can use the OMTIDISK utility.  As part of the
     low-level format, you get to specify the interleave.

     Many other manufacturers use a similar scheme.  Refer to any
     documentation  from  the  disk  controller  manufacturer  to
     figure how to perform a low-level format.





RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988







     Keep  lowering   the  interleave,   formatting  and  running
     SPINTEST until performance suddenly gets worse.  Then do one
     more format at the best interleave obtained.

     If you've got a unique computer/controller situation, please
     drop me  a line  on how  it went.   I'll  include it  in the
     README.RAM file  so the next guy doesn't have to do all this
     work over again.





RAMIT! Command Format

     The syntax for RAMIT! is

          RAMIT  [/T]  [/V]  [/Ex]  [/Wfilename]
                 [/4C:offset]  [/64:offset] [/S:size]

     where

          /E1  Specifies  EDIT-1  mode.    In  EDIT-1  mode,  the
               following instruction sequences get patched:

                 CMP  word reg,0C800h
               
               If found,  the 0C800h constant is patched to match
               the segment where RAMIT! has placed the ROM image.

               Some controllers examine their own CS to determine
               whether  they're   strapped  for  the  primary  or
               secondary addresses.  For example, the OMTI BIOS-7
               (Universal) constantly checks its CS with C800.

          /E2  Specifies  EDIT-2   mode.      In   EDIT-2   mode,
               instructions  matching  either  of  the  following
               patterns  are  changed  to  reflect  the  new  RAM
               segment:

                   CMP   byte reg,0C8h   or    POP   AX/BX/CX/DX
                    JE or JNE                   CMP   xH,0C8h

               This is required for the WD Super BIOS.

          /V   Specifies VERBOSE  mode.   In VERBOSE mode, RAMIT!
               will  print   additional  status  messages  as  it
               analyzes and  installs  the  disk  controller  ROM
               BIOS.

          /S:  Specifies the  [hex] size  of the ROM [in 512 byte
               blocks].   This value  overrides that given in the
               ROM itself.   Some  controllers 'lie'  about their
               true size.



RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988








          /T   Specifies TEST  mode.   In TEST  mode, RAMIT! will
               perform its analysis BUT WILL NOT MAKE ANY CHANGES
               TO DOS,  OR INSTALL  A RAM  COPY OF  THE ROM BIOS.
               TEST mode  is  provided  so  that  RAMIT!  can  be
               checked on  new controllers  or versions  of  DOS.
               TEST mode forces VERBOSE mode.

               A successful  TEST will produce no error messages,
               and identify THREE overwritten locations;  two for
               vector 1B and another for vector 25.

               If this  is not  the case,  RAMIT  may  not  work.
               Contact the author for more instructions.

          /W   Indicates that  the disk controller ROM BIOS is to
               be  written  out  to  the  file  specified.    The
               'filename' immediately follows the /W; for example
               '/WDISK.ROM'.

               This feature is provided so RAMIT! can capture new
               or  updated   disk  controller   ROMs  for  future
               support.     If  you   have  a  non-standard  disk
               controller, and  it won't install with RAMIT!, use
               the /W  option to  make a disk copy and send it to
               me.   I'll try  to extend  RAMIT!  for  your  disk
               controller.

          /4C: Explicitly  specifies an offset which the BIOS had
               stuffed into  vector location  4C.    Rather  than
               disassembling the  ROM code,  this  value  can  be
               specified on the command line.

          /64: Explicitly  specifies an offset which the BIOS had
               stuffed into  vector location  64.    Rather  than
               disassembling the  ROM code,  this  value  can  be
               specified on the command line.




















RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988







         +---------------------------------------------------+
         | A Quick Tutorial on hard disk controller software |
         +---------------------------------------------------+

Getting started.

     When your  computer is  started, on-board  software in  Read
     Only Memory (ROM) is started.  This software, called the ROM
     BIOS, performs  a cursory  check of  the  machine  and  then
     initializes all  the devices  it knows about (CRT, keyboard,
     floppy etc).

     If you  have the  manufacturer's hard disk controller or the
     manufacturer can  support the third party controller in your
     machine, the ROM BIOS will take control of it.  If, however,
     you're using  another board,  the original  ROM BIOS doesn't
     know how to handle it.

     So that  you computer doesn't just stare at you, not knowing
     how to  boot from  your hard  disk, IBM  set up  a procedure
     whereby anybody  could gain  control automatically  from the
     ROM BIOS and provide their own hard disk software.

     To quote from the IBM Technical Reference,

          "The ROM  BIOS provides a facility to integrate adapter
          cards with  on-board ROM  code into the system.  During
          POST  [Power  On  Self  Test],  interrupt  vectors  are
          established for  the BIOS  calls.   After  the  default
          vectors are in place, a scan for additional ROM modules
          takes place.   At  this point,  a ROM  routine  on  the
          adapter  card   may  gain  control    The  routine  may
          establish or  intercept vectors to hook themselves into
          the system.

          "The absolute addresses hex C8000 through hex F4000 are
          scanned in  2K blocks in search of a valid adapter card
          ROM.  A valid ROM is defined as follows:

          "Byte 0: Hex 55.
          "Byte 1: Hex AA.
          "Byte 2:  A length indicator representing the number of
          512-byte blocks in the ROM (length/512).   ...

          "When the  POST identifies  a valid  ROM, it does a far
          call to  byte 3  of the ROM (which should be executable
          code).   The adapter  card may now perform its power-on
          initialization tasks.   The  feature ROM  should return
          control to the BIOS routines by executing a far return.

     All of  the cards  supported by RAMIT! use this technique to
     initialize the  disk drive  itself, and  'steal' vectors  in
     order to gain control when a disk command is required.




RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988









Doing Disk I/O.

     When DOS  or a program want to do disk I/O, it loads up some
     registers with  the I/O parameters and executes an 'INT 13h'
     instruction.  The CPU ends up calling whatever routine whose
     address is in memory for 'vector 13'.

     At  power-on  time,  the  ROM  BIOS  puts  its  floppy  disk
     handler's address in this memory location.

     If external  ROM  code  on  the  disk  controller  board  is
     present, at  initialization time  it will  copy the  default
     (ROM BIOS)  address to a private location (normally location
     100h) and  supply its  own  address  for  vector  13.    The
     controller's ROM  will then  receive control  after the 'INT
     13h' instruction.   It will examine the parameters passed in
     the registers.   If  the request  is not intended for one of
     its disks,  then the  controller  ROM  code  will  pass  the
     request along  to whatever  address it  found for  vector 13
     originally.  This would normally be the ROM BIOS floppy disk
     handler.

     In this way, the disk controller's ROM code gets a chance to
     process every  disk I/O request.  This provides a simple way
     for anyone  to make  a disk controller which works in nearly
     all PC-compatibles.

     Of course,  there's no  reason why  the hard disk controller
     would be  the only piece of code to take over the vector 13!
     In fact,  MSDOS and  PCDOS both  do this  regularly.    They
     provide a  handler to  scan all  disk I/O  for errors.   The
     message

          I/O Error
          Abort, Retry or Ignore?

     is a  DOS error trapped in this way.  Other programs such as
     disk  caches   will  also   trap  this  vector.    The  only
     requirement is  that  each  intercepting  program  which  is
     unable to service a request fully must pass it along via the
     vector 13 handler which was in place before the intercepting
     program took over.

     This all seems very logical and is, in fact, a very powerful
     mechanism  to  handle  disk  I/O  in  a  device  independent
     fashion.









RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988








Ok, then where's the problem?
-----------------------------

The speed difference between system RAM and PC-bus ROM.

     The code  which resides on the disk controller card is 'out'
     on the  PC bus.   It is as 'reachable' and executable as any
     code on in RAM or on the mother-board ROMs (where the system
     ROM BIOS lives).

     For a  16 bit  machine,  there  is  an  enormous  difference
     between on-board  RAM/ROM and  PC bus ROM:  each instruction
     fetched from  the on-board RAM/ROM is read in a 16 bit chunk
     at the  machine's maximum  speed.   Each instruction fetched
     from the  PC bus  is  fetched  in  two  separate  operations
     because the PC bus is only 8 bits wide.  In addition, the PC
     bus often operates at one half the speed of the main memory,
     or less.  Consequently, it can take anywhere from two to ten
     times as  long to execute code based on the PC bus as on the
     mother-board.

     For example,  suppose you have a Western Digital PC (not AT)
     controller on  an AT type clone running at 12 Mhz.  First, a
     16 bit  instruction fetch  must be  converted into two 8 bit
     PC-bus fetches.   This  automatically doubles  any  request.
     Next, our clone manufacturer tried to be very compatible, so
     his PC-bus runs at 6MHz, just like the original IBM AT.  Add
     in a  few wait  states and we will end up taking three times
     as long to execute a simple instruction from PC-bus ROM than
     from mother-board ROM or RAM.



So what if it's slower, the disk is slower still?
-------------------------------------------------

     Up to  a point  this is  true.   Unfortunately, if  the disk
     controller software  cannot get  commands out to the disk in
     time, it  may miss  a whole  revolution.  At that point your
     computer is  quite useless,  waiting for  the disk  to  come
     around again.   The  proper spacing  of data  around a  disk
     track is  determined by the disk 'interleave'.  If you don't
     know what interleaving is or why it's so important, read the
     next section.

     The best  interleave is  determined by the raw transfer rate
     of the  machine and its hardware.  You can move data only so
     fast from  disk to  memory.   It is  also determined  by the
     speed  of   the  controlling  software  which  controls  the
     hardware.   If you can speed the disk controller's software,
     you won't  need as  much  time  to  execute  those  critical
     functions and  you  may  be  able  to  run  with  a  smaller
     interleave.



RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988







     By way  of example,  I have  a AT&T  PC6300.  The 'generous'
     retailer who  formatted my  disk used  the wrong interleave.
     Consequently, it  took 18  revolutions to  read  a  mere  17
     sectors from  my hard  disk!!   After reading  one sector, I
     wasn't getting  ready to  read the next in time, so I had to
     wait a  whole revolution!.   (PS.  there are  17 sectors per
     track  on   most  hard  disks;  26  per  track  for  an  RLL
     controller.)

     Thanks to  a program  by Steve Gibson, SPINTEST, I found the
     ideal interleave  was 6.  After reformatting my disk, it now
     took 'only'  6 revolutions  to read  a track,  a three  fold
     improvement which  was immediately  noticeable when  loading
     large programs.

     Trying any interleave lower ('better') than 6 put me back to
     17 or 18 revolutions to read a track.

     When I  ran the  Western Digital  controller code from high-
     speed RAM  rather than  the slow-speed PC bus, I was able to
     use an  interleave of 4.  This allowed a track to be read in
     only 4  revolutions.  Without any additional hardware, I was
     able to  read raw  data 50%  faster just by running from RAM
     over ROM.

     With the  OMTI RLL  (5527) controller,  I was able to reduce
     the interleave from 6 to 3 on my AT&T machine.

     The only trick was getting my machine to run from RAM rather
     than ROM.  That's what RAMIT! does.



Great!  Give me an example!
---------------------------

     For WD  controllers (with  the simple BIOS), leaving the ROM
     BIOS chip in, and W3 still strapped, I would use:

          RAMIT

     This figures  everything out for itself and installs the ROM
     BIOS into RAM.

     For controllers  I have examined, RAMIT! will be able to run
     without parameters.    I  have  made  entries  into  RAMIT!s
     internal table  so it knows the /4C, /64 and /Ex parameters.
     Unfortunately, if your ROM differs by even a single bit from
     the one I examined, RAMIT! will not recognize it by its CRC.
     In this case, you'll have to rely on the disassembler or the
     command line overrides.






RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988







     For the  OMTI 5527 RLL controller with the universal BIOS, I
     use

          RAMIT  /E1  /4c:a79  /64:9a8

     The /E1  (edit) converts C800 constants to whatever-segment-
     the-ROM-has-been-copied-to;   the /4c:  and  /64:  give  the
     original offsets  that  the  BIOS  had  stuffed  into  those
     respective vectors.



     For the WD controller with the Super Bios, I use

          RAMIT  /E2  /4c:31a  /64:26d

     The /E2  (edit) converts  the  tests  for  segment  C800  to
     whatever-segment-the-ROM-has-been-copied-to;   the /4c:  and
     /64: give  the original  offsets that  the BIOS  had stuffed
     into the respective vectors.

     Alas, the  WD RLL  controller is much more efficient because
     it has  a much  larger  on-board  buffer.    This  evidently
     reduces  the   CPU  interaction   and  thereby  lessens  the
     opportunity  to  improve  the  controller's  performance  by
     running from RAM.































RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988







           +-----------------------------------------+
           |  A quick tutorial on disk interleaving  |
           +-----------------------------------------+


What is interleaving?

     Interleaving is  the  technique  where  consecutive  logical
     sectors are places several physical sectors apart around the
     track.   The interleave  factor is  the  number  of  sectors
     between consecutive  logical sectors.   For  example,  a  10
     sector track  with an  interleave of  1  would  arrange  its
     sectors

          1,2,3,4,5,6,7,8,9,10

     while one with an interleave of 3 would be arranged

          1,8,5,2,9,6,3,10,7,4


Why bother interleaving?

     Controllers interleave  because they cannot transfer data to
     memory as  fast as  they can  read it  off the  disk.   Some
     controllers won't  transfer anything  unless the error check
     codes are correct which cannot be determined until after the
     entire sector is read.

     If the  sectors were  placed sequentially  on disk,    after
     reading one sector,there  would   not  be  enough  time  to
     transfer it  before the  next one  came along under the read
     heads.   (Obviously, the  disk isn't  going to stop spinning
     just because  the  controller  isn't  ready.)    By  putting
     sequential sectors  the proper  distance apart,  the desired
     sector is just about to be read when the controller is ready
     to process it.

What is wrong with having the wrong interleave?

     With the  proper interleave,  after reading and transferring
     sector 'n',  sector 'n+1'  is just about to come by.  If the
     interleave is  too large,  we'll have  to skip over at least
     one sector  which is  not 'n+1'.   This  will waste whatever
     time it  takes to  skip over that sector.  If the interleave
     is too  small, we've  already missed  sector 'n+1'.  We must
     wait a  whole revolution  of the  disk before we get another
     shot at  it.  If we were to read all 17 sectors (on a normal
     disk), we'd require 17 revolutions.








RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988







What should the PC6300 interleave be?

     If you  have the  standard  [MFM]  WD  disk  controller,  an
     interleave of 6 works best.  This is readily verified with a
     number of public domain disk test programs.

     An interleave of 6 requires 6 revolutions to read one track.

     If you  have the  OMTI RLL  controller, an  interleave of  4
     works best.



What should an AT interleave be?

     If you  have the  standard WD disk controller, an interleave
     of 3  works best.   This  is the  standard low-level  format
     value.


How do I change my interleave?

     Unfortunately, the  only way  to change this [at the moment]
     is  to   perform  a   low-level  reformat   of  your   disk.
     Instructions vary  according to  manufacturer.    For  many,
     enter  debug   and  jump   to  location  C800:0005.    After
     performing a  low-level format,  a  regular  DOS  format  is
     required.



How do I know how my interleave works?

     An excellent utility available at bulletin boards across the
     country is  SPINTEST.   This program  was written  by  Steve
     Gibson and reports how many revolutions are required to read
     a track.   Some experimentation is required to determine the
     optimal interleave  value.   As I  get reports for different
     controller/computer  combinations,  I'll  put  them  in  the
     associated README.RAM file.

















RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988







How is RAMIT! distributed!

RAMIT! is distributed as share-ware.  RAMIT! remains the
copyrighted product of Hanover Systems, Newtown CT.  Private
users are urged to register their copies for $25.  Commercial
users must register.  OEM and site licensing is available.

Registering will guarantee continued access to RAMIT! and
continued upgrades free of charge.





Further inquiries, ROM images or registrations may be directed to
the author

           Christopher Smith
           Hanover Systems
           19 Tunnell Road
           Newtown, CT. 06470-1242

           (203) 426-0024


































RAMIT!                  Copyright (c) Hanover Systems, 1987, 1988