NAME
     reboot - create file(s) and reboot utility

SYNTAX
     reboot [ [/ | -] fc ] [ file ... ]

DESCRIPTION
     REBOOT creates specified zero length file(s) and performs a reboot.

     The purpose is to allow conditional jumps in AUTOEXEC.BAT based on
     the existence of the files.  For example, if the following code is
     in AUTOEXEC.BAT:

		IF EXIST CLEAN GOTO NORES
		:
		DEL CLEAN
		:
		: invoke resident programs here
		:
		:NORES

     and the user entered "reboot c:\clean", the system would boot without
     loading the resident programs.

     The list of files may be specified on the command line (the filenames
     are to be separated by spaces).  If no files are specified on the
     command line, the environment variable "REBOOT" is examined for the
     list of files (again space separated).  If neither the command line nor
     the environment specifies the list of files, a default filename "C:\CLEAN"
     is used.


COMMAND LINE OPTIONS
     /f or -f	Create NO files prior to the reboot.

     /c or -c	Perform a COLD reboot.  The default is a WARM reboot, as if
	the user had entered CNTL-ALT-DEL.  A COLD reboot is as if the system
	has just been powered up or the reset switch used (for you IBM'ers,
	that's the big red switch on the right side of the computer :-).

RESTRICTIONS
     The command line options may not be included in the environment variable
     REBOOT.

     When using SET to define REBOOT, take care NOT to include spaces around
     the equal sign.  For example:

		SET REBOOT=C:\FOO C:\BAR

     is valid, however:

		SET REBOOT = C:\FOO C:\BAR

     sets a variable named "REBOOT " instead of the expected "REBOOT" and
     the first file name will be taken as " C:\FOO" instead of the expected
     "C:\FOO".