PRELIMINARY



			     PROGRAM SPECIFICATION


			  STORAGE MANAGEMENT EVALUATOR


				     (EVAL)



			  SPECIFICATION NO. XX-XXXXXX



				FEBRUARY 4,1988


























     1.0 SCOPE


This   document   describes  the  functional  characteristics  of  the	Storage
Management  Evaluator  (EVAL).	EVAL  is  a diagnostic program designed for use
with  the  IBM	AT   to  test  and  evaluate hard and floppy storage management
subsystems.  It  is  especially  suited  for  error  rate testing. The Features
section  describes  the operation and features of the program, including how to
invoke	EVAL,  diagnostic screen definition command structure error methodology
and  miscellaneous  features.  The  Commands section describes the command set,
giving	a  detailed explanation of each command. Appendix A and B describe each
status code, task file, and associated error reporting.






     2.0 FEATURES


     2.1 Invoking EVAL

EVAL  is  invoked  at  the PC-DOS command line,  or batch file command line, as
follows:

	       c>EVAL [cmd-file]

The  optional  cmd-file  parameter  specifies  a file from which EVAL will read
commands  until  it encounters an "end" command. All commands described in this
specification  may  be	used  in   command  files  except "edit", "run", "def",
"duw", and "dur".


     2.2 Floppy Diagnostic Screen

Figure	1 shows the main floppy diagnostic screen. The screen is divided into 4
windows,  a  command  line,  and  a  message  line.  The  command  line will be
described  in  3.0,  and  the  message	line will be referred to throughout the
specification. The following is a brief description of the 4 windows.


     2.2.1 Parameter Window

The  upper  left  window  of the screen is the parameter window. The parameters
shown  will  be  used  for  the  next disk operation. The parameters are: drive
type,  drive  number,  cylinder  number,  head number, sector number, and block
size.  The  parameters are updated dynamically during command execution, if the
operation changes a parameter (see individual commands in section 3).



     2.2.2 Status Window

The  status  window  (lower  left)  shows  the	latest	status	returned  after
execution  of  a  command which accesses the controller. The status information
includes  the  status  code,  status  registers  and cylinder, head, and sector
numbers  returned by the controller. Appendix B gives a detailed explanation of
status codes and associated errors.


     2.2.3 Error Count Window

The  error  count  window  (upper  right)  shows total error counts, as well as
individual  error  counts  for 5 groups of errors. The counts are kept for both
hard  and soft errors. See 2.5.1 for an explanation of hard and soft errors and
appendix B for a detailed explanation of error reporting.

     2.2.4  Error Report Window

The  error  report  window  (lower  right)  shows  the last 5 errors which have
occurred  since  the  diagnostic  began,  or since the last "zero" command was.
issued	Appendix B explains each error in full detail.


     2.3 Hard  Diagnostic Screen

Figure	2  shows  the main hard diagnostic screen. The screen is divided into 4
windows,  a  command  line,  and  a  message  line.  The  command  line will be
described  in  3.0,  and  the  message	line will be referred to throughout the
specification. The following is a brief description of the 4 windows.


     2.3.1 Parameter Window

The  upper  left  window  of the screen is the parameter window. The parameters
shown  will  be  used  for  the  next disk operation. The parameters are: drive
number,  cylinder  number,  head  number,  sector  number,  and block size. The
parameters  are  updated dynamically during command execution, if the operation
changes a parameter (see individual commands in section 3).


     2.3.2 Disk Type Window

The  disk  type  window  (lower left) shows the disk drive boundary parameters.
The  type  information	includes  the maximum cylinders, maximum heads, maximum
sectors,    precomp  cylinder  number,	retry  flag,  step rate, and interleave
value.


     2.3.3 Task File Window

The  task  file  window  (upper  right)  shows	the task file returned from the
controller  after  the	command  was  completed.  Appendix  A  gives a detailed
explanation of the task file and associated errors.





     2.3.4  Error Report Window

The  error  report  window  (lower  right)  shows  the last 5 errors which have
occurred  since  the  diagnostic  began,  or  since the last "zero" command was
issued. Appendix A explains each error in full detail.




     2.4 Command Structure

In  the  interactive  mode (commands being input from the keyboard), the cursor
will  reside  on  the command line, which begins with the CMD> prompt. Commands
are  typed  in lower or upper case. A carriage return  <CR>  ends command entry
and  initiates	command execution. Multiple commands may be entered on the same
line,  separated  by   commas. Commands are separated from parameters by one or
more of the following:	space  tab  =  /  :  (	)


     2.4.1 Command Types

From a command entry standpoint, there are 6 types of commands:

	 type 1 	  cmd
	 type 2 	  cmd|<choice>
	 type 3 	  cmd|<param>
	 type 4 	  cmd|<string>
	 type 5 	  cmd|<test>
	 type 6 	  cmd|<special>

The  six  types  of  commands may be freely mixed on the same line. See section
3.0 for complete listing.


     2.4.2 Command Line Repeat

A  command  line  may  be  repeated  up to 32,762 times, simply by entering the
desired  command  (or  a  string  of  commands)  followed by a #, followed by a
number.   After  the <CR> is entered, the commands on the line will be executed
repeatedly,  just  as  if  the	line were entered the number of times specified
behind	the  #.  In  addition, a repeat count is shown on the message line, and
decrements down with each command line execution.

If  the  Escape  key  is  hit  during  a  line	repeat,  the  repeat  count  is
automatically zeroed.

     Example:

	  CMD>r,incs #30

will perform a read, increment the sector count operation 30 times.





     2.5 Error Methodology


     2.5.1 Hard and Soft Errors

Errors	are separated into two categories - hard errors and soft errors. A hard
error  is defined as an error which is not recoverable after a specified number
of  retries  (see "rc"). A soft error is defined as an error which is recovered
during	retries.  In  other  words, a hard error persists through the specified
number of retries; a soft error does not.

A  hard  error	is  distinguished  in the error report window, and in the error
file by a 'H' prefix and a soft error is prefixed by a 'S'.


     2.5.2 Error logging

In  addition  to  showing  the	last 5 errors in the error reporting window, an
error  log  file  can  be  kept  on disk for later review. Upon invocation, all
errors	are  logged  to  a specified file (see "errlog"). The file may later be
dumped to the screen interactively (see "def").


     2.6  Buffer Screen

The  buffer  screen  can  be reached from the Floppy or Hard screen by giving a
dur  (dump  read buffer) or duw (dump write buffer). The buffer screen displays
one  sector  of  data  at a time that can be edited. The arrow keys are used to
select the byte to edit and the page keys are used to choose the sector.

     2.7 Help Screen

The  help screen can be reached from the floppy or hard screen by giving a help
command.  The  help  screen  displays all of the commands in alphabetical order
with a short description after it.







     3.0 COMMANDS

The  command  set in EVAL closely resembles that of VHD. Bellow one will find a
list  of  all  the  commands  by  type	and alphabetic. Before getting into the
commands we should look at the formats of the commands.


	 type 1 	  cmd
	 type 2 	  cmd|<choice>
	 type 3 	  cmd|<param>
	 type 4 	  cmd|<string>
	 type 5 	  cmd|<test>
	 type 6 	  cmd|<special>


	 cmd	     this is the command name

	 |	     one or more of the following delimiters:
			  space = : / ( ) tab
		     some examples :
			  h 3
			  h=3
			  h:3
			  h = 3
			  h/3	are all valid commands to set h to 3
			  h3	is not valid

	 <choice>    one of the following
			  true	    t
			  false     f
			  yes	    y
			  no	    n



	 <param>     a parameter value of one of the following forms
			  var1	    the value of var1 is used
			    .	    .
			    .	    .
			    .	    .
			  var8	    the value of var8 is used
			  0  ... 32762
			  0h ... 7FFFh
			  rstat     the value in the status register
			  rerr	    the value in the error register
			  rsecc     the value in the sector count register
			  rsecn     the value in the sector number register
			  rcyll     the value in the cylinder low register
			  rcylh     the value in the cylinder high register
			  rsdh	    the value in the SDH register
			  rdata     the value in the data register
			  rastat    the value in the alternate status register
			  rdin	    the value in the digital input register

	 <string>    a string of text

	 <test>      an expression to test that might look like this:
			  (var1 <= 4)
		     NOTE: there must be a space between the operands and
			   the operator i.e.  (var1 <=4) is not valid
		     operators can be of the form:
			  ==	    equal
			  !=	    not equal
			  <=	    less than or equal
			  >=	    greater than or equal
			  <	    less than
			  >	    greater than

	 <special>   can be any thing, check individual command description

   command type 	  command example
	  1		    r
	  2		    upd yes
	  3		    cyl 614
	  3		    s=var1
	  3		    c = 1DFh
	  4		    print(hello out there)
	  5		    while(var3 != var7)   this type can only be
						    used in a batch file
	  6		    etc 1e10

Commands  are  entered at the EVAL command prompt "CMD>". More than one command
can  be  entered  on  a line but each command must be separated by a coma. EVAL
reads and executes each command starting from the left most  command i.e.
	 CMD> h 0,s 3,c 26,sk

EVAL  allows  the  user  to  repeat  a string of commands a specified number of
times. In the example bellow 100 sectors will be read.
	 CMD> r,incs #100



			ALPHABETICAL LISTING OF COMMANDS
alt
	 alt|<choice>
	 Enable alternate sector during format
	 hard drive only

b
	 b|<param>
	 Set block size. Enter the number of sectors to read/write/verify
	 hard/floppy

bct
	 bct|<special>
	 Set bit terminate count
	 <special> is scientific notation    bct=3e9
	 stop execution after 300,000,000 bits have been read/write/verify
	 floppy drive only

c
	 c|<param>
	 set cylinder value for next operation
	 hard/floppy

cmd
	 cmd|<param>
	 write to command register of task file
	 hard drive only

cmp
	 cmp
	 compare read buffer to write buffer and flag all errors
	 hard/floppy

copy
	 copy
	 move read buffer to write buffer
	 hard/floppy

cyl
	 cyl|<param>
	 set total number of cylinders on drive
	 hard drive only

d
	 d|<param>
	 set drive number for next operations
	 hard drive	  0 <= param <= 1
	 floppy drive	  0 <= param <= 3



def
	 def
	 dump error file. change screen to display error log
	 hard/floppy

diag
	 diag
	 diagnostic command. send diagnostic command to controller
	 hard drive only

dt
	 dt|<param>
	 set drive type
		     0	  1.2 Meg floppy drive in a 1.2 Meg drive
		     1	  360 K   floppy drive in a 1.2 Meg drive
		     2	  360 K   floppy drive in a 360 K   drive
	 floppy drive only

dur
	 dur
	 dump read buffer. display contents of read buffer
	 hard/floppy
duw
	 duw
	 dump write buffer. display contents of write buffer
	 hard/floppy

ecmd
	 ecmd|<param>
	 write to 1005 esdi task file command register
	 1005 esdi hard drive controller only

ecc
	 ecc|<param>
	 set number of ECC bytes
	 hard drive only

ecct	ecct
	 test ECC and return the number of bits corrected
	 hard drive only

ecmd
	 ecmd|<param>
	 send <param> to esdi command reg
	 1005 only

edit
	 edit
	 enter a batch file from eval.
	 can not be used in a batch file.
	 hard/floppy



eelse
	 eelse
	 marks end of else statement in batch file
	 used in batch file only

eif
	 eif
	 marks end of if statement in batch file
	 used only in batch file

else
	 else
	 marks start of else statement in batch file. This block will
	 be executed only if the previous if command was false
	 used only in batch file

end
	 end
	 marks end of a batch file also used to exit the edit screen
	 used only in a batch file

er
	 er|<choice>
	 enable retries. will enable/disable retries on a hard drive
	 controller based on <choice>
		     true   enable retries
		     false  disable retries

errlog
	 errlog|<string>
	 enter name of error file to use
	 file will be opened in the append mode and a header is placed at
	 the top of the file depending if opened from floppy or hard window

esdi
	 esdi|<choice>
	 opens/closes a window for the 1005 esdi controller  esdi task file

etc
	 etc|<special>
	 error terminate count
	 <special> is scientific notation    ect=3e9
	 execution will stop after 10,000,000,000 errors have been found

ewhile
	 ewhile
	 marks end of while statement in batch file
	 used only in batch file



exfr
	 exfr|<param>
	 write to 1005 esdi transfer register
	 used only wilt 1005 esdi controller

fbs
	 fbs|<param>
	 format <sector number> as bad
	 hard drive only

fbt
	 fbt
	 format all of track as bad
	 hard drive only

fd
	 fd
	 format all of drive

floppy
	 floppy
	 goto floppy drive mode
	 hard drive only

ft
	 ft
	 format track

h
	 h|<param>
	 set head number
	 hard/floppy

hard
	 hard
	 goto hard drive mode
	 floppy drive only

heads
	 heads|<param>
	 set total number of heads
	 hard drive only

help
	 help
	 goto help screen

i
	 i|<param>
	 set interleave for next format command
	 hard/floppy



idc
	 idc
	 send idc command to controller with parameters of drive
	 hard drive only

if
	 if|<test>
	 marks start of if block. The if block will be executed
	 only when the condition of <test> is true.
	 used only in batch files

incc
	 incc
	 increment cylinder count
	 hard/floppy

inch
	 inch
	 increment head count
	 hard/floppy

incs
	 incs
	 increment sector count
	 hard/floppy

int
	 int|<choice>
	 enable / disable interrupts from controller
	 hard drive only

lrun
	 lrun|<string>
	 load and run a batch file <file name>
	 hard/floppy

ltt
	 ltt
	 write/read/compare all of disk
	 hard/floppy

multi
	 multi|<param>
	 set multi block transfer mode with <block size>
	 only on hard controllers that support this command

nop
	 nop
	 no operation does nothing



o
	 o|<param>
	 set the offset into the write buffer used with v command

pat
	 pat|<special>
	 fill write buffer with pattern  pat=incr,pat 6db
	 <special>
	   incr 	  fill write buffer with incriminating data

	   rand 	  fill write buffer with random numbers
			  this command will take about 3 mins to complete

	   ilt		  fill write with interleave pattern

	   X...X	  fill write buffer with hex pattern X...X
			  i.e. pat 6db will make a pattern of 6db6db6db...


pause
	 pause
	 wait for key press. Will prompt user to press any key
	 an escape key will stop execution of batch file or repeat line
	 hard/floppy

precomp
	 precomp|<param>
	 set precomp cylinder number
	 hard drive only

print
	 print|<string>
	 print message to lower left corner of screen	   print(HI MOM)
	 hard/floppy

quit
	 quit
	 exit EVAL
	 hard/floppy

r
	 r
	 read command. read number of sectors described by block size
	 hard/floppy


ra
	 ra
	 read all of drive
	 hard/floppy




rb
	 rb
	 read buffer. read buffer of controller
	 hard drive only

rc
	 rc|<param>
	 retry count. set number of retries before calling an error hard
	 floppy drive only

rcmd
	 rcmd|<param>
	 write <param> to command register
	 hard drive only

rcylh
	 rcylh|<param>
	 write <param> to cylinder high register
	 hard drive only

rcyll
	 rcyll|<param>
	 write <param> to cylinder low register
	 hard drive only
rdata
	 rdata|<param>
	 write <param> to data register
	 hard drive only

recal
	 recal
	 recalibrate drive. move heads to track zero
	 hard drive only

reset
	 reset
	 reset drive. does  a soft reset to drive.
	 in hard drive mode must be followed by 2 recals
	 hard/floppy

rfixd
	 rfixd|<param>
	 write <param> to fix disk register
	 hard drive only

rl
	 rl
	 read long command. Read all of block including ECC bytes
	 hard drive only



rm
	 rm
	 read mulit block
	 only on hard controller that support multi block

rsdh
	 rsdh|<param>
	 write <param> to SDH register
	 hard drive only

rsecc
	 rsecc|<param>
	 write <param> to sector count register
	 hard drive only

rsecn
	 rsecc|<param>
	 write <param> to sector number register
	 hard drive only

rtf
	 rtf
	 read task file. read task file from controller
	 hard drive only

run
	 run
	 run batch file. start execution of batch file
	 hard/floppy

rv
	 rv
	 read verify command. read block of sectors but do not transfer data
	 hard/floppy

rva
	 rva
	 read verify all. do a read verify on all of disk
	 hard/floppy


rwpre
	 rwpre|<param>
	 write <param> to write precomp register
	 hard drive only

s
	 s|<param>
	 set sector number for next command
	 hard/floppy



sectors
	 sectors|<param>
	 set total number of sectors per track
	 hard drive only

sk
	 sk
	 seek command. seek to track specified
	 hard drive only

skew
	 skew|<param>
	 set skew for next format
	 hard drive only

skt
	 skt
	 do a crescendo seek test
	 hard/floppy

show
	 show|<param>
	 display value to screen. will display value in lower right
	 corner of screen
	 hard/floppy

st	 st
	 start timer
	 this will zero the real time stop watch

ts	 time stamp
	 this will print the real time stop watch
	 to the screen and to the error file

upd
	 upd|<choice>
	 update command. enable/disable update of screen after every command
	 hard/floppy

v
	 v|<param>
	 set a value in write buffer at offset defined by o
	 v will also increment the offset value



var1...var8
	 var1...var8|<param>
	 set value of var1...var8
		     var1 = 2	    set var1 to 2
		     var1 += 3	    var1 = var1+3
		     var1 -= 1	    var1 = var1 - 1
		     var1 &= 4	    var1 AND 4
		     var1 |= 4	    var1 OR 4
  note : when using += ... |= there must be spaces seperating the operator
	 hard/floppy

w
	 w
	 write command. write number of sectors described by block size
	 hard/floppy

wa
	 wa
	 write all. send write buffer to all of drive
	 hard/floppy

wb
	 wb
	 write buffer. send write buffer to controller
	 hard drive only

while
	 while|<test>
	 mark start of while block The while block will be executed
	 as long as the condition of <test> is true.
	 used only in batch files

wid
	 wid
	 write the cylinder/head/sector number to the data sector on drive
	 hard drive only

wl
	 wl
	 write long command. write the write buffer to the drive
	 including ECC bytes
	 hard drive only

wm
	 wm
	 write multi block
	 only on hard controller that support multi block



wtf
	 wtf
	 write task file
	 send task file to controller
	 hard drive only

zero
	 zero
	 clear error counters
	 hard/floppy







     4.0 Batch Files

Commands  can  be  executed  from  a  batch  file  in one of two ways. First by
entering  the  name  of the batch file after EVAL at the DOS command line or by
using  the  edit  command.  In	either case the format of the batch file is the
same.  In  a  batch file all the command from the HARD or FLOPPY windows can be
used  except  : "edit", "run", "def", "duw", and "dur". While in the batch file
the  "if",  "else",  and  "while"  commands  can be used to control the flow of
commands.  A  batch  file  must  end  with  the "end" command or it will not be
loaded.  To execute a file one must type the "run" command. Below is an example
of a batch file:





							       Appendix    (A)

			      HARD DRIVE TASK FILE



Here  is a brief out line of the Task File for more information check the speck
sheet for the controller you are using.

		       D7					  D0
		     ÚÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄ¿
Error register	     ³ BB  ³ ECC ³  0  ³ ID  ³	0  ³ AC  ³ TK  ³ DM  ³
		     ÃÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄ´
Sector count	     ³	     number of sectors	to transfer	     ³
		     ÃÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄ´
Sector number	     ³		       sector number		     ³
		     ÃÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄ´
cylinder low	     ³		 cylinder number (low byte)	     ³
		     ÃÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄ´
cylinder high	     ³	0  ³  0  ³  0  ³  0  ³	0  ³  0  ³ cyl. MSB  ³
		     ÃÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄ´
SDH		     ³	1  ³ sec. size ³ DS  ³ HS3 ³ HS2 ³ HS1 ³ HS0 ³
		     ÃÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄ´
Status reg.	     ³ BSY ³ RDY ³ WF  ³ SC  ³ DRQ ³ CRD ³ IDX ³ ERR ³
		     ÀÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÙ


Error reg.
	 BB	     Bad Block
	 ECC	     Bad ECC bytes
	 ID	     ID not found
	 AC	     Aborted Command
	 TK	     Track zero error
	 DM	     Data Address Mark not found

Status reg.
	 BSY	     Busy flag
	 RDY	     Drive ready
	 WF	     Write Fault
	 SC	     Seek Complete
	 DRQ	     Data Transfer Request
	 CRD	     Corrected Data Flag
	 IDX	     Index pulse
	 ERR	     Error Flag
Sector count
	 The number of sectors to transfer

Sector number
	 The sector to start transfer at



							       Appendix    (A)

Cylinder low/high
	 The cylinder to start transfer at

SDH
	 sec.size    sector size
		     00    256 bytes
		     01    512 bytes
		     10   1024 bytes
		     11    128 bytes
	 DS	     drive select
	 HS3..HS1    head select




			       HARD DRIVE ERRORS

The format of the error messages from the hard drive looks like this
	 Err#  CMD# SR ER   C  H  S  CMD  MSG

Where
	 Err#	     is the error count
	 Cmd#	     is the command count
	 SR	     the value of the status register
	 ER	     the value of the error register
	 C	     the cylinder that the error occurred on
	 S	     the sector that the error occurred on
	 H	     the head that the error occurred on
	 CMD	     the command that was being executed
	 MSG	     a description of the error

Example:
	 Err#  CMD# SR ER   C  S  H  CMD  MSG
	   23	 45 01 80   7 1A  3   r    Bad Block mark





							       Appendix     (B)


     Floppy Status Codes:

  Status Code		Condition

       0	Successful operation

       2	Bad address mark.   Either a data AM or IDAM  was  bad.

       3	Diskette is write protected.

       4	Record not found.

       6	The media has been changed since the last operation.

       8	DMA  overrun.	 An  illegal  DMA  condition  has
		occurred.     The  diagnostic  is  in  an  unknown
		condition.  The system should be re-booted.

       9	DMA boundary exceeded.	 The system should be  re-
		booted.

      10	Bad CRC.  Either ID or data CRC did not match its
		associated field.

      20	Bad UPD 765 chip.

      40	Bad seek.

      80	Time-out error.  Response from the floppy control-
		ler was not received before the system timed out.
		Can occur if the drive door is open.











							     Appendix	  (B)


			     FLOPPY ERROR MESSAGES


     Messages not related to media records:


	  "Write protected" -
	  Results from a status code "3".

	  "Media change indicated" -
	  Results from a status code "6".

	  "DMA overrun!!!" -
	  Results from a status code "8".

	  "DMA boundary exceeded!!!" -
	  Results from a status code "9".

	  "Bad UPD 765 chip" -
	  Results from a status code "20".



     Messages related to media records:


	  Message is composed of three parts -

	  1) Type of operation - Read, Write, Reset, Format, Verify.

	  2) Location -  "c:n  h:n  s:n"

	  3) Type of error (in parentheses) -

	     "End of track"
	  "DAM not found"
	  "IDAM not found"
	  "Data CRC error"
	  "ID CRC error"
	  "Undefined"


							       Appendix    (B)



     Examples:

	  "Read error  c:0 h:1 s:10 (DAM not found)"

	  "Write error c:10 h:0 s:1 (ID CRC error)"









			    COMMAND LIST BY FUNCTION


				 Setup Commands

alt	    |<choice>	       enable alternate sectors T/F
b	    |<param>	       set block size
bct	    |<special>	       set bit terminate count	i.e.  btc=1e30
cyl	    |<param>	       set total number of cylinders
dt			       drive type { floppy }
ecc	    |<param>	       set number of ecc bytes
er	    |<param>	       retries enable T/F
errlog	    |<string>	       enter name of error file to use
esdi	    |<choice>	       1005 esdi mode
etc	    |<special>	       error terminate count  i.e.   etc=1e30
floppy	    |<choice>	       goto floppy drive mode
hard	    |<choice>	       goto hard drive mode
heads	    |<param>	       set total number of heads
i	    |<param>	       set interleave
idc			       send idc command
multi	    |<param>	       set multi block size
reset			       reset drive parameters
rc	    |<param>	       retry count { floppy }
sectors     |<param>	       set total number of sectors per track
skew	    |<param>	       set skew size
precomp     |<param>	       set precomp cylinder number
zero			       clear error counters


				Transfer Commands

cmd	    |<param>	       write to command register
copy			       move read buffer to write buffer
dur			       dump read buffer
duw			       dump write buffer
ecmd	    |<param>	       write to 1005 esdi command register
exfer	    |<param>	       write to 1005 esdi transfer register
fbs	    |<param>	       format bad sector  <sector number>
fbt			       format bad track
fd			       format drive
ft			       format track
ltt			       write/read/compare all of disk
pat	    |<special>	       fill write buffer with pattern pat=incr,pat=6db
o	    |<param>	       offset into write buffer (1 sector = 520)
r			       read command
ra			       read all
rb			       read buffer
rl			       read long command
rm			       read multi block
rv			       read verify command
rva			       all
v	    |<param>	       value to put into write buffer at offset
w			       write command
wa			       write all
wb			       write buffer
wid			       write cylinder/head/sector number to each setor
wl			       write long command
wm			       write multi block
wtf			       write task file





				Batch File Commands

edit			       enter batch file from eval
eelese			       end of else statement { batch file }
eif			       end of if statement { batch file }
else			       else statement { batch file }
end			       end of batch file
ewhile			       end of while statement { batch file }
if	    |<test>	       if statement { batch file }
lrun	    |<string>	       load and run <file name>
nop			       no operation
run			       run batch file
while	    |<test>	       while statement { batch file }



			     Head Movement Commends

c	    |<param>	       set cylinder count
d	    |<param>	       set drive number
h	    |<param>	       set head count
incc			       increment cylinder count
inch			       increment head count
incs			       increment sector count
recal			       recalibrate drive
s	    |<param>	       set sector count
sk			       seek command
skt			       seek test



			  Hard Drive Register commands

rcmd	    |<param>	       write <param> to command registor
rcylh	    |<param>	       write <param> to cylinder high registor
rcyll	    |<param>	       write <param> to cylinder low registor
rdata	    |<param>	       write <param> to data registor
rfixd	    |<param>	       write <param> to fix disk registor
rsdh	    |<param>	       write <param> to SDH registor
rsecc	    |<param>	       write <param> to sector count registor
rsecn	    |<param>	       write <param> to sector number registor
rwpre	    |<param>	       write <param> to write precomp registor



				      Other

cmp			       compare buffers
def			       dump error file
diag			       diagnostic command
ecct			       ecc test
help			       goto help screen
pause			       wait for key press
print	    |<string>	       print message to screen
quit			       exit eval
rtf			       read task file { hard }
show	    |<param>	       display value to screen
st			       start timer
ts			       time stamp
ta			       test all
upd	    |<choice>	       update command T/F
var1...var8 |<param>	       set value of var1...var8







			ALPHABETICAL LISTING OF COMMANDS

alt	    |<choice>	       enable alternate sectors T/F
b	    |<param>	       set block size
bct	    |<special>	       set bit terminate count	   bct=3e9
c	    |<param>	       set cylinder count
cmd	    |<param>	       write to command register
copy			       move read buffer to write buffer
cyl	    |<param>	       set total number of cylinders
d	    |<param>	       set drive number
def			       dump error file
diag			       diagnostic command
dt	    |<param>	       drive type { floppy }
dur			       dump read buffer
duw			       dump write buffer
ecmd	    |<param>	       write to 1005 esdi command register
edit			       enter batch file from eval
eelese			       end of else statement { batch file }
eif			       end of if statement { batch file }
else			       else statement { batch file }
end			       end of batch file
er	    |<choice>	       retries enable T/F
errlog	    |<string>	       enter name of error file to use
esdi	    |<choice>	       1005 esdi mode
etc	    |<special>	       error terminate count	etc=1e10
ewhile			       end of while statement { batch file }
exfer	    |<param>	       write to 1005 esdi transfer register
fd			       format drive
fds	    |<param>	       format drive with skew
floppy	    |<choice>	       goto floppy drive mode
ft			       format track
fts	    |<param>	       format track with skew
h	    |<param>	       set head count
hard	    |<choice>	       goto hard drive mode
heads	    |<param>	       set total number of heads
help			       goto help screen
i	    |<param>	       set interleave
idc			       send idc command
if	    |<test>	       if statement { batch file }
incc			       increment cylinder count
inch			       increment head count
incs			       increment sector count
o	    |<param>	       offset into write buffer (1 sector = 520)
pat	    |<special>	       fill write buffer with pattern  pat=incr,pat 6db
pause			       wait for key press
precomp     |<param>	       set precomp cylinder number
print	    |<string>	       print message to screen
r			       read command
ra			       read all
rb			       read buffer
rc	    |<param>	       retry count { floppy }
recal			       recalibrate drive
reset			       reset drive parameters
rl			       read long command
rtf			       read task file { hard }


run				run batch file
rv			       read verify command
rva			       all
s	    |<param>	       set sector count
sectors     |<param>	       set total number of sectors per track
sk			       seek command
show	    |<param>	       display value to screen
st			       start timer
ts			       time stamp
upd	    |<choice>	       update command T/F
v	    |<param>	       value to put into write buffer at offset
var1...var8 |<param>	       set value of var1...var8
w			       write command
wa			       write all
wb			       write buffer
while	    |<test>	       while statement { batch file }
wl			       write long command
wtf			       write task file
zero			       clear error counters