Part of the ENHANCER series of programs EGACHG.COM  Ver. 1.1, Feb 17, 1986

	 Copyright (C)	I. B. Miller	 1985, 1986

	If you find this of value and use it please send a
	 contribution ($25.00) suggested.

 To:  Enhancers 		     It is suggested that companies contribute
       231 Otonabee Ave.	      more for use on more than one machine.
       Willowdale, Ontario, Canada
       M2M-2S9			       Please contact me for a site license
					 Phone (416) 226-9753

      EGACHG is a program which provides a means to preset 12 palette color
combinations for EGACLR.COM a companion program which Controls the seventeen
palette registers on the enhanced color card ( Enhanced Graphics Adapter),
12 different user selected color combinations of any 16 of the 64 colors
available can be made active by use of the Alt key at the same time as any of
the number keys 1 to = at the top of the qwerty keyboard. EGACHG will change
the colors in the Palette registers so that you can see what is available but
unless you use EGACLR these will be lost at the next video reset called by
any program.

      The actual colors available to you depend on your actual hardware set
up and so may be different. As an example if you have only a regular monitor
you will have only standard colors though you will be able to swap them around.
In my experience THE limiting factor for text display is the monitor. Though
for graphic display memory size is  also a limiting factor.


General Information
-------------------

    With the Enhanced Monitor color coding is as follows.

	   Bit				  Hex
	   ---				  ---
	     1 is    Medium	Blue	 - 01
	     2 is    Medium	Green	 - 02
	     3 is    Medium	Red	 - 04
	     4 is Low	intensity Blue	 - 08
	     5 is Low	intensity Green  - 10
	     6 is Low	intensity Red	 - 20
	   1+4 is High	intensity Blue	 - 09	 Low and medium add to give
	   2+5 is High	intensity Green  - 12	  high	- this is the basic
	   3+6 is High	intensity Red	 - 24	  principle the card works on

   Following is the standard color palette combination.
   ----------------------------------------------------
	      B  B  G  C  R  M	B  W  G High intensity colors O
	      l  l  r  y  e  a	r  h  r --------------------- v
	      a  u  e  a  d  g	o  i  e  B  G  C  R  M	B  W  e
	      c  e  e  n     e	w  t  y  l  r  y  e  a	r  h  r
	      k     n	     n	n  e	 u  e  a  d  g	o  i  s
			     t		 e  e  n     e	w  t  c
			     a		    n	     t	n  e  a
						     a	      n
palette
 register # = 0  1  2  3  4  5	6  7  8  9  A  B  C  D	E  F 10
							      ^-this is the
						     Seventeenth or in hex it
					       is 10. It really cannot be used
					  in Enhanced Mode because of a seeming
					 bug in the EGA. I cannot believe IBM
					wanted it that way. Try it and see.

How the program works
---------------------

       The program works by loading in the entire EGACLR.COM file
  and then selecting the color controlling bytes which are all near
  the start as initial values for setting the colors. It then follows
  the user through the registersets updating them in memory and
  changing them and the colors on display as the user dictates.

       Once the user is finished changing colors to his liking and
  has pressed the End key EGACHG first checks to see how high in the
  sequence of possible EGACLR1.COM to EGACLR99.COM exists on the disk.
  once found it increments this and writes out a temporary file. After
  it has succeeded in the write it renames the original EGACLR.COM to
  EGACLR(whatever #).COM and then renames the temporary file to
  EGACLR.COM. In theory you could change names and have almost unlimited
  numbers of color combinations which can be made active by using these
  variants of EGACLR.COM, but in practice I find it adequate to have
  a few and use the command parameters with EGACLR.COM to change <alt 1>


Instructions
------------

      EGACHG has been written to work on the EGACLR.COM file on the
same drive as EGACHG.COM. Make sure both are present on the same disk.

Important:  Unless you use the EGACLR o command line to turn off auto reset,
	     or have not yet activated EGACLR, then EGACLR will proceed to
	     not allow this program to show the colors to you. You must
	     Deactivate (or not start) EGACLR before starting EGACHG.

	The program will proceed to load into itself the EGACLR.COM file.
It will then paint a window on the top half of the screen showing the
palette colors currently in use with EGACLR use of <Alt 1> which
I call registerset # 1. The program will next paint the bottom window
which is the working area and will display the current register of the 17
included in the current registerset as well as the current value in that
register displayed in both decimal and Hex. It will also show the RGB comp-
onents of the color corresponding to that value.

      The screen painted appears approximately as follows with of course the
addition of color.


 EGACHG.COM  A program to change colors to any 16 of 64 available on the EGA
     for use with a companion program EGACLR.COM which must be on same drive.
Register 0	  1	  2	  3	   4	    5	    6	    7
     _______________________________________________________________________
    |	     |	     |	      |        |	|	 |	  |	   |
    |	     |	     |	      |        |	|	 |	  |	   |
    | Blocks of colors appear here and change as palette registers change  |
    |________|_______|________|________|________|________|________|________|
    |	     |	     |	      |        |	|	 |	  |	   |
    |	     under the control of the operator	|	 |	  |	   |
    |	     |	     |	      |        |	|	 |	  |	   |
    |________|_______|________|________|________|________|________|________|

Register 8	  9	   A	    B	     C	      D        E	F
 Below is current color being worked on.
  ____________________________________________________________________________
  |									     |
  |									     |
  |									     |
  |__________________________________________________________________________|
PgUp & PgDn change registerset, Up & Dn change registers, + & - change colors,
End to quit & save , Q to quit & not save! ,W to write BAT file ,R,G,B to vary
Current Palette Registerset is :  5	10,11,12 are 0,-,=
Current Palette Register is :  01 Color is:   2   Color in Hex is :  02
  Current RGB values are :	   R= off
				   G=		 med
				   B= off


	From then on you are in the part of the program that does all the
work and the following keys are the only ones which will do anything.

  PgUp	    Moves Up one registerset from 1 to 12 then back to 1
  PgDn	    Moves Down one registerset from 12 to 1 then back to 12

  Up-Arrow  Moves up one Pallette register from 0 to 16 then back to 0
						0 to 10 Hex
  Dn-Arrow  Moves Down one Pallette register from 16 to 0 then back to 16
						  10 to 0 Hex

    +	    Increases value in Pallette register from 0 to 63 then back to 0
						      0 to 3F hex
    -	    Decreases value in Pallette register from 63 to 0 then back to 63
						      3F to 0 hex

    R	    Changes Red component of color through off, low, med, high & back
    G	    Changes Green component of color through off, low, med, high & back
    B	    Changes Blue component of color through off, low, med, high & back

    Q	    Allows you to quit without creating an output file

    S	    Standardizes colors In current Registerset

    W	    writes out a .BAT file to reset colors in Alt 1 . A sample appears
	    here.

   EGACLR 02A,126,202,337,404,505,614,707,818,919,A1A,B1B,C3C,D2D,E36,F3F,s00

  End	    Writes out all the values to an EGACLR.COM files while saving the
		previous ones as EGACLR1.COM up to EGACLR99.COM


Use the End key when you have completed your selection.
   the program will then update EGACLR.COM with your selected
   colors available from <alt 1> to <alt =>.

you may then activate the colors by entering   at the DOS prompt
   EGACLR R


Disclaimer
----------
     For obvious reasons the user is totally responsible for use of this
program and determining that it is suitable for use by him, and he uses this
program with no warranty from myself.

    It should work properly with the EGA from IBM or any card which later
maintains compatibility with it

    This program and EGACLR.COM are used by myself with LOTUS Development
programs and work well solving a colors shift bug (or less than perfect EGA
driver routine) but obviously LOTUS does not support it.

General
--------

	Again please note that if you have the regular monitor or the Enhanced
Monitor operating in regular mode none of the non-standard colors are available
to you!


Of Course
----------
	The program EGACHG.COM will allow you to work with many colors and
see them on screen interactively without any of the work involved in
remembering all the numbers and color coding schemes. I believe it will
make color control easy.


       If you have any comments or suggestions please contact
me either at Home in the evenings at	       (416) 226-9753
or at the following BBS's   PCanada(pc-1266)   (416) 751-6337
				SGV-BBS        (416) 673-0557

I am also on Compuserve as  72167,2563

					   Ivor B. Miller