VGAUTILS.DOC FILE FOR VGA MONITOR SETUP/TEST UTILITIES:
VGRID.EXE, VGRID-M.EXE, VBOX.EXE, VGACOLOR.EXE

Contained in this "package" (the file VGAUTILS.ARC) are four 
utilities that you can use to test and align your VGA display 
adapter/monitor combination, along with this file, VGAUTILS.DOC.  
VGRID.EXE, VGRID-M.EXE, and VBOX.EXE require a VGA or 100% 
compatible display adapter and a VGA or VGA-compatible 
multiscanning monitor.  They may work with certain "Super EGA" 
cards with 640 x 480 16 color modes that are compatible with VGA 
mode 18 (decimal) when used with a monitor capable of displaying 
this resolution.  Beyond this, I cannot make any claims for the 
compatibility of these programs with your equipment.

VGACOLOR.EXE requires a VGA or MCGA (or 100% compatible) display 
adapter, and a VGA or compatible monitor.

These programs were written and compiled in Microsoft QuickBASIC 
version 4.5.  They are to be considered as FREE software for 
everyone's use and enjoyment.  The descriptions of the programs 
are as follows:


VGRID.EXE

This program puts a white grid on your monitor screen in VGA mode 
18 (decimal), -the 640 x 480 16 color graphics mode.  The outer 
border of the grid is 640 pixels wide by 480 pixels high.  The 
individual boxes of the grid are 40 pixels on a side.  This 
screen pattern is useful for testing and aligning you VGA or 
multiscanning monitor for the following:

     FOCUS - The grid should, of course, be sharp all the way 
     across your monitor screen.  If it is not, the focus may 
     need to be adjusted.  Some poorly designed monitors may have 
     trouble maintaining focus in the corners when the center of 
     the screen is sharp.  

     VERTICAL AND HORIZONTAL SIZE - The accurate display of 
     graphics is important when using CAD or paint programs, -the 
     size and shape of displayed objects must be correct.  This 
     requires that the vertical and horizontal size controls of 
     your monitor be correctly set.  Since the borders of the 
     VGRID screen display measure the full 640 by 480 pixels 
     (width to height) of the VGA mode 18 screen, they should be 
     displayed at an aspect ratio of 4 units wide to 3 units high 
     (or 1.33 to 1, if you're so inclined).  If this is not the 
     case, adjust your monitor's vertical size control and/or the 
     horizontal size control for the correct screen aspect ratio. 
     You can set this by actually measuring the size of the grid 
     on the screen, or you can simply set your monitor so that 
     the individual boxes that make up the grid appear to be 
     square.  You can also set your monitor's screen height and 
     width visually using the program VBOX.EXE.

     CENTERING - If your monitor's horizontal and vertical 
     position controls are set correctly, the grid display should 
     be centered on the screen.  Adjust these controls accord-
     ingly if this is not the case.

     HORIZONTAL AND VERTICAL LINEARITY - The boxes that make up 
     the grid display should (ideally) appear as perfect squares 
     of the same size across the entire screen display.  If they 
     are not all the same size, the horizontal and vertical 
     linearity adjustments of your monitor may be incorrectly 
     set.  Please note that it may be impossible to achieve 
     perfect linearity across the screen, -sometimes a compromise 
     setting may have to be determined to achieve the best 
     overall display quality.

     CURVILINEAR DISTORTION - The horizontal and vertical lines 
     in the grid should appear perfectly straight.   They may, 
     however, be curved outward (barrel distortion) or inward 
     (pincushion distortion) in monitors that are out of adjust-
     ment or just plain poorly designed.  Some monitors have 
     provisions to correct for these problems, others may not.

     CONVERGENCE - In a color monitor, the three electron beams 
     for each of the primary colors (red, green, and blue) must 
     be aligned so that they meet ("converge") to form the 
     smallest possible point on the screen.  If convergence is 
     improperly set, there is a loss of sharpness in the form of 
     colored fringes on text and graphics.  The white grid 
     display of VGRID.EXE, when used in conjunction with the 
     magenta grid produced by VGRID-M.EXE, can be used to check 
     and set your monitor's convergence.


The VGRID display will remain on your screen until you press a 
key.


VGRID-M.EXE

VGRID-M.EXE can be used along with VGRID.EXE to check and align 
convergence in color monitors.  VGRID-M produces a display 
identical to that of VGRID, except that the grid is magenta 
instead of white.

The NEC Multisync II service manual recommends using magenta and 
white "crosshatch" displays (such as those produced by VGRID-M 
and VGRID) to set convergence.  The magenta grid display is used 
first to set the alignment of blue and red.  There are tabs along 
the neck of the monitor's CRT tube that move small permanent 
magnets which control the convergence of these beams in both the 
horizontal and vertical directions.  The idea is to get the 
horizontal and vertical magenta lines to appear as sharp as 
possible, without red or blue fringes.

Next, a white grid display (VGRID.EXE) is used to set the 
convergence of magenta (red + blue) with green.  A different set 
of tabs along the neck of the CRT are used this time, but the 
principle is the same as that used in the red/blue alignment.  
The white grid lines should appear as sharp as possible, with no 
colored fringes.  When this condition has been obtained, all 
three colors are properly converged.

The procedure for the convergence alignment of monitors other 
than the NEC Multisync II should be similar.  It is recommended 
that you obtain the service manual for your particular brand and 
model of monitor, and adhere to its recommendations for setting 
convergence and any other monitor adjustments.  Care must be 
taken, as there may be control tabs near those used for con-
vergence that are used to set other things (such as color purity) 
that you DON'T normally want to disturb.

CAUTION: Aligning convergence and other monitor settings usually 
requires that you remove the cover from your monitor, thus 
exposing yourself to the dangerous voltages that are inside.  
Care must be taken to avoid electrical shock!  Nonconducting 
plastic alignment tools (available at places like Radio Shack) 
should be used.  Again, the best advice is to obtain the service 
manual for your monitor, and follow its recommendations.  

It may be impossible to obtain perfect convergence across the 
full width of your monitor's screen.  Typically, convergence 
error is greater in the corners.  As is the case with linearity, 
a compromise setting may be necessary to obtain the best overall 
alignment across the entire display width.


VBOX.EXE

This is a program that generates a screen display especially made 
for setting the vertical and horizontal size controls of your 
monitor.  The circles should appear to be perfectly round, and 
the boxes should be perfectly square.  The border of the display 
measures 640 pixels wide by 480 pixels high, so the screen aspect 
ratio should be 4 to 3 (or 1.33 to 1).


VGACOLOR.EXE

This is a demo program that shows the capabilities of the
320 x 200 256 color mode (decimal mode 19) of the VGA or MCGA 
display adapters.  The 256 colors used can be chosen from a total 
"palette" of "256K" (actually 262,144) possible colors, which 
vary in hue (shade), intensity (brightness), and saturation.  
The colors of the palette are produced from all the possible 
combinations of the three primary colors (red, green, and blue), 
each of which can be varied through 64 steps of intensity (64 x 
64 x 64 = 262,144).  On monochrome monitors, these colors are 
displayed as 64 shades of gray.

The first screen shows the "default" color settings of the 256 
screen color attributes.  The numbers and letters along the top 
and left side of the color bar display are hexadecimal numbers.  
You can determine the hex attribute number of a displayed color 
bar by using the numeral displayed to the left of its horizontal 
display row as the first digit, and the numeral directly above 
its vertical display column as the second digit.

The top row (attributes 00H to 0FH) of the first screen is the same 
as the "default" color set used by the EGA.  The second row (10H 
to 1FH) shows the range of 64 gray levels possible in 16 evenly 
spaced steps.  Attributes 20H through F7H consist of 24 color 
groups, each consisting of nine shades of a color.  Three 
intensity levels and nine saturation levels are provided for each 
shade.  Attributes F8H through FFH are set to black for reasons 
known only to the designers of the VGA standard.

The second screen uses attributes 20H through FFH to show how the 
colors used can be varied in hue (shade) and intensity (bright-
ness).  Hue is varied along the vertical axis of the display.  
The primary colors (red, green, blue), secondary colors (yellow, 
magenta, cyan), and some intermediate shades are shown.   The 
"spacing" of the hues shown is not "even" in the sense of the 
numerical values of each color, but were chosen to visually 
present discrete "steps" of hue variation.  Exactly how 
this looks to you will depend on the contrast and brightness 
settings of your monitor, as well as your own eyes.  The 64 step 
range of intensity/brightness for each displayed hue is varied 
from left to right in 16 evenly spaced steps ranging from "0" 
(black) to full intensity.

The third screen uses attributes 20H through FFH to show how 
colors can be varied in saturation.  As in the previous screen, 
hue is varied in the vertical axis.  The 64 step range of color 
saturation is shown from left to right in 16 evenly spaced steps 
ranging from "no saturation" (pure white) to full color 
saturation.

VGACOLOR, besides being a demonstration of the capabilities of 
VGA/MCGA mode 19 (decimal) can be useful for setting the 
brightness and contrast settings of your monitor.  It is also 
an aid in convincing your spouse that the hundreds of dollars 
that you spent on a VGA adapter and monitor were worth it.


NOTES ON MONITOR VERTICAL/HORIZONTAL SIZE SETTINGS

Depending on the brand and model of your display adapter and 
monitor, the display vertical and horizontal size settings that 
you determine using VGRID.EXE or VBOX.EXE may only be valid for 
the VGA 640 x 480 mode.  Other screen resolutions may require 
that the monitor be readjusted for the proper display aspect 
ratio.

The reason for this is that different monitors can behave in 
dissimilar ways as the video horizontal and vertical scan rates 
are varied for different on-screen resolutions.  Normally, if 
nothing is done by the monitor to compensate for these changes, 
the size of the displayed image will vary considerably with scan 
frequency.  

Normally, this is not a problem with the standard VGA display 
modes and VGA-only monitors.  The VGA standard specifies a 
constant horizontal scan frequency of 31.5 KHz regardless of the 
video mode, with a vertical scan rate of either 60 or 70 Hz.  
Most VGA display adapters adhere to this, and most VGA monitors 
expect this range of scan rates, and all is well.

However, problems can arise with some of the non-standard, 
higher resolution "Super VGA" modes (800 x 600, 1024 x 768, and 
the like) found in some display adapters when those modes are 
used with the "multiscanning" or "multisync" monitors needed to 
display the higher resolutions.  In the Super VGA modes, the 
horizontal scan rate may be as high as 35 KHz, while the vertical 
scan frequency may be as low as a flickery 50 Hz (this is done to 
keep the overall video bandwidth down to something most monitors 
can handle).  Different monitors deal with these changes in 
horizontal and vertical scan frequencies in various ways.  Most 
multiscanning displays have some sort of "autosizing" circuitry 
built into them to maintain a constant image size despite changes 
in scanning rates.  In some of these monitors, the autosizing 
feature works very well, and once you have set the width and 
height for one display standard, it is also correctly set for 
other modes as well.  Other monitors have autosizing circuits 
that do not work as well, or they may lack this feature entirely.  
With these displays, you may have to reset the screen vertical 
and horizontal size controls when switching between different 
resolutions and display modes.

It is also possible that the centering of the image on your 
monitor screen may vary with the resolution being displayed.  
This is particularly true for the horizontal image position.  
Some multiscanning monitors (such as the NEC Multisync II) have a 
separate horizontal image centering control for each of several 
horizontal scan frequency ranges. 


QUESTIONS AND COMMENTS

You can leave questions or comments regarding these programs for 
me on CompuServe (73710,2014).


-Arthur Stoppe
 July, 1989