Mystic Pascal  User Manual                                      18


        5.  System Display

             The  System  Display screen contains  technical  information 
        about  the  current  state of the  Mystic  Pascal  system.   This 
        information is useful in storage allocation with the installation 
        program and when working with multi-tasking programs.

             This  screen  displays  the current  time-of-day  (The  PC's 
        onboard  clock  should  be correctly set.) and the  elapsed  time 
        since  Pascal  was started.   A storage map and a  table  of  the 
        currently  active  processes  are also  displayed.   The  Display 
        Screen  is  updated approximately once every second  when  it  is 
        being displayed. 




        5.1  Storage Map

             The storage map shows the several main storage areas used by 
        Mystic Pascal.   The starting address of each area is shown as an 
        absolute  20 bit (5 hex digit) number.   This information can  be 
        useful  when  using  the Install program to  modify  the  storage 
        configuration. 

        User Area

             The  user  area is reserved for variables  declared  in  the 
        user's  program.   Both  global variables and  procedures'  local 
        variables  are  allocated  in  this  region.   Pointer  variables 
        allocated  with the NEW procedure are placed in Dynamic  Storage, 
        not here.

        Laser

             The  large  area code-named "Laser"  contains  the  internal 
        symbolic  representation of the Pascal program.   Compiled object 
        code  and dynamic variables allocated with the NEW procedure  are 
        also  stored here.   The Laser may be up to a maximum of 640K  in 
        size.   The percent of this area which is currently allocated  is 
        displayed.

        Dynamic Storage

             Queue  messages and various system control blocks are stored 
        in  this area.   Dynamic storage may be up to 60K in  size.   The 
        percent of this area which is currently allocated is displayed.





        Section 5:   System Display


        Mystic Pascal  User Manual                                      19


        Feature Buffer

             This buffer is used by the advanced feature support.

        Screen Buffers

             The  non-displayed  CRT  screens are stored in  this  buffer 
        area.

        Optimizer Buffer

             The  optimizer  stores object code in this area  during  its 
        processing.

        System Stack

             This  is the 8086 stack segment.   A separate stack area  is 
        maintained for each concurrently executing process.

        System Data

             This is the main 8086 data segment.  

        System Code

             This  is  the 8086 code segment containing the  nucleus  and 
        compiler assembly code.

        Program Segment Prefix

             This  100H byte area is setup by DOS when Mystic  Pascal  is 
        started.   It  contains DOS system data areas and is not directly 
        used by Mystic Pascal.



















        Section 5:   System Display


        Mystic Pascal  User Manual                                      20


        5.2  Process Control Table

             This  is a display of the process control blocks  (PCB)  for 
        each   process  currently  allocated.    Seven  data  fields  are 
        displayed.

             The  nucleus'  process manager maintains  a  "pseudo-timer".  
        This  is  a  16 bit counter which  is  incremented  whenever  the 
        dispatcher  transfers control to another process.   The value  of 
        the  pseudo-timer is stored in a process control block when  that 
        process  is  dispatched.   This  provides a very fast  method  of 
        keeping  track of how recently each process has been  dispatched.  
        When the pseudo-timer wraps around to 0, all PCB timer fields are 
        also reset to 0.

             The  dispatcher can use this information to give  preference 
        to  those processes that have been waiting a relatively long time 
        for  a  chance to execute.   Each process is  assigned  a  static 
        priority  which is also considered by the dispatcher in selecting 
        a ready process.

        Process
             Name of the process.

        St
             Process current state
                  P = Pascal process STARTed by user
                  R = ready
                  W = waiting for queue message

        Count
             The number of times the process has been dispatched.

        SP
             The process's stack pointer.

        Time
             The pseudo-timer value when the process was last dispatched.

        Pr
             The  static priority of the process.   This value determines 
        what proportion of the processor time this process receives if it 
        is ready to execute.

        Dyn
             The  dynamic priority of the process.   This value  actually 
        determines  which ready process will be  next  dispatched.   This 
        value is equal to:  

                  static_priority + (current_pseudo_timer - time)


        Section 5:   System Display


        Mystic Pascal  User Manual                                      21


        6.  Help Windows

             The  Help  facility  is included in Mystic  Pascal  to  make 
        learning easier for students and to provide a very fast reference 
        source for experienced Pascal users.  The Help facility is always 
        available from any screen.  Four function keys are used for help:

             F7   Pascal Language Help
             F8   Standard Procedures & Functions Help
             F9   Editor Help
             F10  Function Key Help


             F7  Pascal Language Help

             Function  key F7 will display a menu window showing the Help 
        windows available.   Enter the letter or number key to select the 
        topic you want to see.  

             Enter  any character to leave a topic window and  enter  any 
        non menu character to leave the menu and return to the underlying 
        screen.

             F8  Standard Procedures & Functions Help

             Function  key F8 displays a menu window showing all  builtin 
        procedures  and functions.   Enter the letter or number to select 
        the topic you want to see

             F9   Editor Help

             Function key F9 displays a list of editor commands directly.  
        Hitting any key will remove the display.

             F10  Function Key Help

             Function  key  F10  displays  a list  of  all  function  key 
        assignments.   This is only a reminder list.   The other function 
        keys may not be invoked directly from this display window.













        Section 6:   Help Windows