Documentation on EGA.TPU unit. ( See EGA.INT )

CONSTANTS ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

EGACard     EGACard: boolean = false;
VGACard     VGACard: boolean = false;

            Default state of boolean expressions are false. Initialization of
            this unit calls an internal procedure ( DetectEGA ) which
            detects whether an EGA/VGA adapter is present. If an EGA adapter
            is detected, the EGACard constant is set to true. The unit goes
            on to determine if a VGA adapter is also present. If so the
            VGACard constant is also set to true. ie: EGA adapter only:
            EGACard = true, VGACard = false; VGA adapter: EGACard = true,
            VGACard = true.

EGA_Pal     EGA_Pal: PaletteType (graph unit)

            Default EGA palette settings. Used with EGA_ResetPalette;

PROCEDURES ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

All procedures utilize the EGA Graphics 1&2 Controller Chips and Sequencer
Chip for functions. Functions work equally well for the VGA due to downward
compatibility.

EGA_SetPlane_Write      procedure EGA_SetPlane_Write( Plane: byte );

                        Sets BitMask Register and MapMask Register for
                        writing to bit plane requested. Valid input for
                        plane is 0 to 3 only.

EGA_SetPlane_Read       procedure EGA_SetPlane_Read( Plane: byte );

                        Sets ReadMap Register for reading bit plane
                        requested. Valid input for plane is 0 to 3 only.

EGA_Reset_Write         procedure EGA_Reset_Write;

                        Resets BitMask register and MapMask register to
                        their default states. Should be final call to
                        procedures using the EGA_SetPlane_Write call.

EGA_Reset_Read          procedure EGA_Reset_Read;

                        Resets the ReadMap Register to its default state.
                        Should be called after all calls to the EGA_SetPlane_
                        Read procedure are completed.

EGA_ResetPalette        procedure EGA_ResetPalette;

                        Resets the EGA/VGA palette entries to their default
                        16 color values. Should be used if EGA_SetPalette
                        has been used before program termination.

EGA_SetRGBPalette       procedure EGA_SetRGBPalette( cn, r, g, b: integer );

                        Sets color number (cn) to the values of r (red),
                        g (green), b (blue). r g b must be in the range of 0
                        to 255 ( $00..$FF ). Typical values are one of four,
                        $00, $55, $AA, $FF on most 64 color systems. A
                        number between these ranges does nothing more or
                        less to the color displayed. This procedure uses the
                        EGA BIOS interrupt $10 so parameter tables are
                        saved.