L008
                                                    X!APPENDICIES"Y



!PRINTER SWITCH SETTINGS" ----------------------------------- A.1

!H TEST" ---------------------------------------------------- B.1

!CONTROL SEQUENCES" (a list) -------------------------------- C.1
     General Printer Control ------------------------------ C.1
     Horizontal Movement ---------------------------------- C.2
     Vertical Movement ------------------------------------ C.5
     Manipulation of Printable Characters ----------------- C.8
     Bit-Graphics ---------------------------------------- C.10

!ASCII CHARACTER CODES" (a list) ---------------------------- D.1

!NUMBERING SYSTEMS" ----------------------------------------- E.1

 





































                               APX


                                                     X!APPENDIX A"Y



!PRINTER SWITCH SETTINGS"


When you remove the carrier cover from your NEC 8023A, you will 
be  able  to see two(2) DIP switches.   They are covered  by  a 
clear  plastic strip which says !SW-1" and !SW-2".   Their position 
is to the right front of the printer.  Each of the switches has 
eight(8)  small levers which are used to determine  several  of 
the printer's power-on parameters.

To  use the enclosed software,  you need to make sure that  the 
levers  match the settings given in the following  chart.   The 
meaning  for  each setting is given in the  remainder  of  this 
appendix.




   !SW - 1"      8  -  7  -  6  -  5  -  4  -  3  -  2  -  1
  ----------------------------------------------------------
 |  CLOSED  |     |  X  |     |     |     |     |  X  |     |
  ----------------------------------------------------------
 |   OPEN   |  X  |     |  R  |  X  |  R  |  X  |     |  X  |
  ----------------------------------------------------------

 
   !SW - 2"      8  -  7  -  6  -  5  -  4  -  3  -  2  -  1
 
  ----------------------------------------------------------
 |  CLOSED  |     |  R  |     |     |    NOT    |     |  R  |
  ----------------------------------------------------------
 |   OPEN   |  R  |     |  R  |  R  |   USED    |  X  |     |
  ----------------------------------------------------------
 
                 !X = required   R = recomended"


















                               A.1


                                                     X!APPENDIX A"Y



!PRINTER SWITCH SETTINGS"


                   X!DIP SWITCH 1    (SW - 1)"Y


!LEVERS 1, 2, and 3   -   Character Set Selection"

These three(3) levers are used to select the character set  for 
your language.  We'll be using English.


             LEVER NUMBER   |   3   -   2   -   1
          ------------------------------------------
         |       JAPAN      |   O   |   O   |   O   |
          ------------------------------------------
     !*"   |   !UNITED STATES"  |   !O"   |   !C"   |   !O"   |
          ------------------------------------------
         |  UNITED KINGDOM  |   O   |   C   |   C   |
          ------------------------------------------
         |      GERMAN      |   C   |   O   |   O   |
          ------------------------------------------
         |      SWEDISH     |   C   |   O   |   C   |
          ------------------------------------------
                   !O" = Open   -   !C" = Closed


   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~


!LEVER 4   -   Length of Page"

With  this lever,  you choose the power-on setting for the page 
length.  You have two(2) choices.

                       CLOSED = 72 lines
                    !*    OPEN" = 66 lines


   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~


!LEVER 5   -   Default SELect Signal"

This  lever  determines whether or not the NEC 8023A  will  pay 
attention  to  a software signal from the computer to take  the 
printer on- or off-line.

                   CLOSED = ineffective (no)
                !*    OPEN" = effective (yes)



                               A.2


                                         (continued) X!APPENDIX A"Y



!PRINTER SWITCH SETTINGS" (continued)


                   X!DIP SWITCH 1    (SW - 1)"Y
                          (continued)

!LEVER 6   -   LF with a Full Buffer"

If you wish to have the NEC 8023A automatically print when  its 
RAM  memory gets full,   then you should have this lever in the 
closed position.  (Some software will require this setting, but 
generally  you  do not want the NEC 8023A to print  unless  the 
computer sends it a print signal.

                   CLOSED = effective (yes)
                !*    OPEN" = ineffective (no)



   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~



!LEVER 7   -   Print Command Code"

This  lever allows several commands other than the CR to  cause 
the printer to perform a carriage return.   If you expect  your 
IBM PC to operate correctly with the NEC 8023A, this lever MUST 
be set to closed.

      !*  CLOSED" = Carriage Return with CR, LF, VT, FF
           OPEN = Carriage Return with CR only



   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~



!LEVER 8   -   Line Feed following CR"

You  are  able  to select a LF automatically with  each  CR  by 
having this lever closed.   But,  with an IBM PC, you MUST have 
this lever open for proper opperation.

                CLOSED = Line Feed with each CR
             !*    OPEN" = CR only (no LF)






                               A.3


                                         (continued) X!APPENDIX A"Y



!PRINTER SWITCH SETTINGS" (continued)


                   X!DIP SWITCH 2    (SW - 2)"Y


!LEVER 1   -   ZERO (0) Print Format"

This lever gives you the option of having all zeroes(0) printed 
with or without a slash.  The slash is highly recommended since 
many programming mistakes are caused by confusing the zero  and 
letter O.

             !*  CLOSED" = Zero with a Slash
                  OPEN = Zero without a Slash


   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~


!LEVER 2   -   Memory Buffer Size"

Normally  you have 1K of RAM memory available in the NEC 8023A, 
(unless you have added the 2K memory option).   It is  possible 
that  for  certain applications,  you may want to disable  this 
memory  so that the printer will only be able to hold one  line 
of data at a time.  That's what this lever is for.

       !*  CLOSED" = One Line of Data only
            OPEN = 1K or 3K of RAM memory available


   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~


!LEVER 3 and 4   -   NOT USED at present"


   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~


!LEVER 5   -   Character Pitch"

You  have two(2) power-on options PICA  or  PROPORTIONAL.   The 
recommended  setting  is for PICA with Character Pitch  changes 
made by software means.

             CLOSED = PROPORTIONAL Character Pitch
          !*    OPEN" = PICA Character Pitch




                               A.4


                                         (continued) X!APPENDIX A"Y



!PRINTER SWITCH SETTINGS" (continued)


                   X!DIP SWITCH 2    (SW - 2)"Y
                          (continued)

!LEVER 6   -   Seven- or Eight-bit Data"

By  setting this lever to Open,  you can make use of the  char-
acter sets contained in the ROM memory of your NEC 8023A.  But, 
only  if  PRINT_CHARACTERS is not installed in your  computer's 
memory.   The setting of this lever makes no difference to  the 
operation of either PRINT_CHARACTERS or PRINT_SCREEN.

                   !*  CLOSED" = 7-bit Data
                        OPEN = 8-BIT Data



   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~



!LEVER 7   -   SELect or DESelect "

Normally you will want this lever set Closed so that you do not 
have  to  manually  SELect the printer when you  turn  on  your 
computer.

            !*  CLOSED" = SELected at Power-on
                 OPEN = Not SELected at Power-on



   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~   ~



!LEVER 8   -   Bidirectional or Unidirectional Printing"

With  this lever you are able to determine whether the  printer 
will  be  allowed to print Bidirectionally.   It's  recommended 
that  you  have  this lever set  open  to  allow  Bidirectional 
printing since it is much faster.

               CLOSED = Unidirectional Printing
            !*    OPEN" = Bidirectional Printing






                               A.5


                                                     !XAPPENDIX BY
 


H TEST"


The "H" test is a name of an adjustment procedure.  With it you
can  make  adjustments to the location of information which  is
printed  on consecutive passes of the print head when  printing
bidirectionally.   You  may notice that the dot-columns do  not
always line up properly (vertically) from one pass to the next.
Here  is  how you can adjust your printer so  that  these  dot-
columns line up more closely.

   !1)" Set the printer for PICA Character Pitch and the standard
   1/6" Line Spacing. (SW-2, LEVER 8 = CLOSED)

   !2)" From BASIC run this short program.

                         !10 FOR X=1 TO 10
                         20 FOR L=1 TO 80
                         20 LPRINT "H";
                         30 NEXT L
                         40 NEXT X
                         50 LPRINT CHR$(12)
                         60 END

   3)"  Look  at  the vertical bars of the H's and see  if  they
   align.  If they do you're finished.

   !4)"  If not,  then turn off the printer,  remove the  carrier
   cover,  and find the adjusting screw marked !VR1" (align).  It
   is under the plastic strip with DIP switches SW1 and SW2.

   !5)" Now,  by turning this screw first one way then the other,
   by  rerunning  the short BASIC program,  you should (by  the
   trial and error method) be able to establish a  satisfactory
   alignment.


                          !DO NOT WORRY!!"

   The  amount of adjustment that can be accomplished with this
   method is very small,  (less than a dot width), so you can't
   hurt  anything as long as you don't try to force the  screw.
   If you do not feel adequate to the task,  your dealer should
   do this adjustment for you.









                               B.1


                                                     !XAPPENDIX CY
 


CONTROL SEQUENCES"


Rather  than have a list of control sequences that starts  with
the  lowest  ASCII  code and catalog each  code  progressively,
this listing has the control sequences grouped according to the
use of the sequence.  Hopefully, this will help you gain under-
standing in the use of the various control sequences.

In general, each control sequence will be listed with its ASCII
symbol  first.   This will be followed by the decimal number(s)
and then  HEXidecimal number(s) which represent the sequence.


 !General Printer Control"

  These  sequences are used to determine the current state of
  the printer.
T36
 -------------------------------------------------------------T12
| Give  software  control for SELecting  and  DESelecting the |A
| printer.                                                    |
|                                                             |
|      !DC1  -  CHR$(17)  -  11H  -  SELect the printer"        |
|      !DC3  -  CHR$(19)  -  13H  -  DESelect the printer"      |
|                                                             |
| Both are made ineffective by closing SW-1, LEVER 5.         |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| Used to select the current print mode.                      |A
|                                                             |
|    !ESC [  -  CHR$(27)+CHR$(91)  -  1BH 5BH  -  Incremental"  |
|    !ESC ]  -  CHR$(27)+CHR$(93)  -  1BH 5DH  -  Logic Seek"   |
|                                                             |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| This is used to CANcel print data which has been previously |A
| received within the same line.                              |
|                                                             |
|      !CAN  -  CHR$(24)  -  18H  -  Cancel previous data"      |
|                                                             |
| This code is ignored in incremental print mode.             |T12
 -------------------------------------------------------------T36
A









                               C.1


                                         (continued) !XAPPENDIX CY
     


CONTROL SEQUENCES" (continued)


 !Horizontal Movement"

  These sequences either control or cause horizontal movement
  of the print head.
T36
 -------------------------------------------------------------T12
| Moves the print head to the Left Margin.                    |A
|                                                             |
|         !CR  -  CHR$(13)  -  0DH  -  Carriage Return"         |
|                                                             |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| Moves the print head to the left one(1) print position.     |A
|                                                             |
|            !BS  -  CHR$(08)  -  08H  -  Back Space"           |
|                                                             |
| This  control sequence is only effective in the incremental |
| printing mode.                                              |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| Moves the print head to the next Horizontal Tab Stop.       |A
|                                                             |
|          !HT  -  CHR$(09)  -  09H  -  Horizontal Tab"         |
|                                                             |
| This is ignored if no Horizontal Tabs are set.              |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| Sets the position of the Left Margin.                       |A
|                                                             |
|     !ESC L [XXX]  - CHR$(27)+CHR$(76)+"  ?    ?    ?  ""      |
|                  -   !1BH      4CH      3?H  3?H  3?H"        |
|                                                             |
| [!XXX"] =  3-digit decimal number which represents the column |
| in which you wish to place the Left Margin.                 |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| Control sequences which allow for variable width spaces.    |A
|                                                             |
|   !ESC (01) - CHR$(27)+CHR$(01) - 1BH 01H  -  1 dot space"    |
|   !ESC (02) - CHR$(27)+CHR$(02) - 1BH 02H  -  2 dot space"    |
|   !ESC (03) - CHR$(27)+CHR$(02) - 1BH 03H  -  3 dot space"    |
|   !ESC (04) - CHR$(27)+CHR$(04) - 1BH 04H  -  4 dot space"    |
|   !ESC (05) - CHR$(27)+CHR$(05) - 1BH 05H  -  5 dot space"    |
|   !ESC (06) - CHR$(27)+CHR$(06) - 1BH 06H  -  6 dot space"    |
|                                                             |
| These sequences are for use in Proportional Pitch only.     |T12
 -------------------------------------------------------------T36
A


                               C.2


                                         (continued) !XAPPENDIX CY
     


CONTROL SEQUENCES" (continued)


 !Horizontal Movement" (continued)
T36
 -------------------------------------------------------------T12
| Sets the position of Horizontal Tab Stops.                  |A
|                                                             |
|                  !ESC ( [XXX],nnn,...,[XXX]"                  |
|    !-  CHR$(27)+CHR$(40)+"  ?    ?    ?    ,   ------   .""   |
|    !-    1BH      28H      3?H  3?H  3?H  2CH  ------  2EH"   |
|                                                             |
| [!XXX"] =  3-digit decimal number which represents the column |
| in  which you wish to place a Horizontal Tab Stop.   Commas |
| must  be used to separate each number and the sequence must |
| end  with a period.   Up to thirty-two(32)  Horizontal Tabs |
| Stops may be set at one time.                               |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| The !RANGE" of [!XXX"] for these two(2) control sequences is:   |A
|                                                             |
|  !PICA    from 1 to 80    -    PROPORTIONAL    from 1 to 80"  |
| !ELITE    from 1 to 96    -     COMPRESSED     from 1 to 136" |
|                                                             |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
|  Removes (clears) selected Horizontal Tab Stops.            |A
|                                                             |
|                  !ESC ) [XXX],nnn,...,[XXX]"                  |
|    !-  CHR$(27)+CHR$(41)+"  ?    ?    ?    ,   ------   .""   |
|    !-    1BH      29H      3?H  3?H  3?H  2CH  ------  2EH"   |
|                                                             |
| [!XXX"] =  3-digit decimal number which represents the column |
| from which you wish to remove the Horizontal Tab Stop.  You |
| must  use  commas  to separate each position  and  end  the |
| control sequence with a period.                             |T12
 -------------------------------------------------------------T36
A

T36
 -------------------------------------------------------------T12
| Clears all current Horizontal Tab Stops.                    |A
|                                                             |
|           !ESC 2  -  CHR$(27)+CHR$(50)  -  1BH 32H"           |
|                                                             |T12
 -------------------------------------------------------------T36
A






                               C.3


                                         (continued) !XAPPENDIX CY
     


CONTROL SEQUENCES" (continued)


 !Vertical Movement"

  This  group of Control Sequences either control  or  cause
  vertical movement of the print head.
T36
 -------------------------------------------------------------T12
| Moves the print head vertically one(1) line.  The direction |A
| is dependent upon the current LF direction.                 |
|                                                             |
|         !LF   -   CHR$(10)   -   0AH   -   Line Feed"         |
|                                                             |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| Moves  the print head to the next Vertical Tab Stop set  in |A
| channel 2.                                                  |
|                                                             |
|       !VT   -   CHR$(11)   -   0BH   -   Vertical Tab"        |
|                                                             |
| If the print head is at or beyond the last tab stop, (or if |
| no Vertical Tabs are set), the print head will move to  the |
| next TOF in either direction.                               |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| A Vertical Tab command.   When combined with the  following |A
| one(1)  byte,  this command will to move the print head  to |
| either the named channel or the specified number of  lines. |
|                                                             |
|      !US + [XX]  -  CHR$(31) + [XX]  -  Unit Separator"       |
|                 !-    1FH    + [XX]"                          |
|                                                             |
| [!XX"] = a single byte which is configured to specify  either |
| the number of lines or a specific channel number.           |
|                                                             |
|                             bits                            |
|                       X7 6 5 !4 - 3 2 1 0"          Limits    Y |
|  !Channel Number"   -   0 0 0 !0" - 0 !x x x"   -  0 < total > 7  |
| !Number of Lines"   -   0 0 0 !1" - !x x x x"   -  0 < total > 16 |
|                                                             |T12
 -------------------------------------------------------------T36
A










                               C.4


                                         (continued) !XAPPENDIX CY
     


CONTROL SEQUENCES" (continued)


 !Vertical Movement" (continued)
T36
 -------------------------------------------------------------T12
| Moves the print head to the next TOF in either LF direction.|A
|                                                             |
|         !FF   -   CHR$(12)   -   0CH   -   Form Feed"         |
|                                                             |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| These sequences are used to select the Line Feed direction. |A
|                                                             |
|   !ESC f  -  CHR$(27)+CHR$(102)  -  1BH 66H  -  Forward LF"   |
|   !ESC r  -  CHR$(27)+CHR$(114)  -  1BH 72H  -  Reverse LF"   |
|                                                             |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| These  control sequences establish the number of lines  per |A
| inch (Line Spacing).                                        |
|                                                             |
| !ESC A  -  CHR$(27)+CHR$(65)  -  1BH 41H  -  1/6" Line Feed"  |
| !ESC B  -  CHR$(27)+CHR$(66)  -  1BH 42H  -  1/8" Line Feed"  |
| !ESC T [XX]  -  CHR$(27)+CHR$(84)+"  ?    ?  ""               |
|             !-    1BH      54H      3?H  3?H"                 |
|                                                             |
| [!XX"] = A 2-digit decimal number which represents the number |
| of 144ths of an inch for each Line Feed.                    |T12
 -------------------------------------------------------------T36
A






















                               C.5


                                         (continued)!X APPENDIX CY
     


CONTROL SEQUENCES" (continued)


 !Vertical Movement" (continued)

  The  following control sequences are used in combination to
  set the Vertical Format.
T36
 -------------------------------------------------------------T12
| The initial  Start Load command  when setting the  Vertical |A
| Format.                                                     |
|                                                             |
|      !GS   -   CHR$(29)   -   1DH   -   Group Separator"      |
|                                                             |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| The  End of Load command  when setting the Vertical Format. |A
|                                                             |
|     !RS   -   CHR$(30)   -   1EH   -   Record Separator"      |
|                                                             |T12
 -------------------------------------------------------------T36
A


                            !EXAMPLE"
       Sections of a program to set the Vertical Format

!LN |      BINARY   Bit Placement         |   HEX    |  ASCII  |
X#   7 6 5 4 3 2 1 0 - 7 6 5 4 3 2 1 0    |          |         |Y
         byte 1            byte 2"
0   !0 0 0 1 1 1 0 1   (GS code-1 byte)   -    1D    -    29"
1   0 1 0 0 0 0 0 !1" - 0 1 0 0 0 0 0 0  -!TOF-41"  40  -  !65"  64
2   0 1 0 0 0 0 0 0 - 0 1 0 0 0 0 0 0    -  40  40  -  64  64
3   0 1 0 0 0 0 0 0 - 0 1 0 0 0 0 0 0    -  40  40  -  64  64
4   0 1 0 0 !1" 0 0 0 - 0 1 0 0 0 0 0 0  -!VT- 48"  40  -  !72"  64
5   0 1 0 0 0 0 0 0 - 0 1 0 0 0 0 0 0    -  40  40  -  64  64
6   0 1 0 0 0 0 !1" 0 - 0 1 0 0 0 0 0 0  -!VT- 42"  40  -  !66"  64
7   0 1 0 0 0 0 0 0 - 0 1 0 0 0 0 0 0    -  40  40  -  64  64
    . . . . . . . . . . . . . . . . .
    . . . . . . . . . . . . . . . . .
20  0 1 0 0 0 0 0 0 - 0 1 0 0 0 0 0 0    -  40  40  -  64  64
21  0 1 0 0 0 0 !1 1" - 0 1 0 0 0 0 0 0  -!BOF-43"  40  -  !67"  64
22  0 1 0 0 0 0 0 0 - 0 1 0 0 0 0 0 0    -  40  40  -  64  64
23  0 1 0 0 0 0 0 0 - 0 1 0 0 0 0 0 0    -  40  40  -  64  64
24  0 1 0 0 0 0 0 !1" - 0 1 0 0 0 0 0 0  -!TOF-41"  40  -  !65"  64
25  !0 0 0 1 1 1 1 0   (RS code-1byte)    -    1E    -    30"







                               C.6


                                         (continued) !XAPPENDIX CY
     


CONTROL SEQUENCES" (continued)


 !Manipulation of Printable Characters"

  This  group of control sequences gives you control over the
  selection of Character Pitch, Character Sets, and how those
  characters will appear when printed.
T36
 -------------------------------------------------------------T12
| Sequences which select the Character Pitch.                 |A
|                                                             |
|   !ESC P  -  CHR$(27)+CHR$(80)  -  1BH 50H  -  Proportional"  |
|   !ESC N  -  CHR$(27)+CHR$(78)  -  1BH 4EH  -  Pica"          |
|   !ESC E  -  CHR$(27)+CHR$(69)  -  1BH 45H  -  Elite"         |
|   !ESC Q  -  CHR$(27)+CHR$(81)  -  1BH 51H  -  Compressed"    |
|                                                             |T12
 -------------------------------------------------------------T48
 -------------------------------------------------------------T12
| Control sequences giving you options which will enhance the |A
| appearance of the characters that will be printed.          |
|                                                             |
|     !SO  -  CHR$(14) - 0EH  -  Elongated" (dbl width)! ON"      |
|     !SI  -  CHR$(15) - 0FH  -  Elongated (cancell)   OFF"     |
|                                                             |T12
                                                          *
|    !DC2  -  CHR$(18) - 12H  -  Italics" (toggle)! - ON/OFF "    |A
|    !DC4  -  CHR$(20) - 14H  -  7-bit Elongated  OFF"          |
|                                                             |
|  !ESC !  -  CHR$(27)+CHR$(33) - 1BH 21H  -  Bold Print  ON"   |
|  !ESC "  -  CHR$(27)+CHR$(34) - 1BH 22H  -  Bold Print  OFF"  |
|                                                             |
| !ESC X  -  CHR$(27)+CHR$(88) - 1BH 58H  -  Underlining  ON"   |
| !ESC Y  -  CHR$(27)+CHR$(89) - 1BH 59H  -  Underlining  OFF"  |
|                                                             |T12
   *
|     DC2 and DC4 are used in place of SO and SI when you use |A
| the  printer set to receive 7-bit code and are  also  using |
| the Japanese character Set.  Since most of us in the U.S.A. |
| speak English, we don't need this possible code useage, and |
| so will be using DC2 as a toggle for Italic Characters,  if |
| PRINT_CHARACTERS is installed.                              |T12
 -------------------------------------------------------------T36




A





                               C.7


                                         (continued) !XAPPENDIX CY
     


CONTROL SEQUENCES" (continued)


 !Manipulation of Printable Characters" (continued)
T36
 -------------------------------------------------------------T12
| Control sequences  that  give access to  the  two(2)  Char- |A
| acter Sets which are stored in the NEC 8023A's ROM memory.  |
|                                                             |
|   !ESC # - CHR$(27)+CHR$(35) - 1BH 23H - GRAPHICS SYMBOLS"    |
|   !ESC $ - CHR$(27)+CHR$(36) - 1BH 24H - ASCII" (standard)    |
|                                                             |
| At power-on,  the ASCII Character Set  is established.   If |
| the printer is set to receive 8-bit data, the new Character |
| Set  will replace the characters which correspond to  ASCII |
| codes CHR$(160) to CHR$(223).   But,  if the printer is set |
| for  7-bit data, the ASCII codes from CHR$(32) to  CHR$(95) |
| will be replaced.                                           |T12
 -------------------------------------------------------------T36
A
 
 
 
 
 
 
 
 
 
 
 






















                               C.8


                                         (continued) !XAPPENDIX CY
     


CONTROL SEQUENCES" (continued)


 !Bit-Graphics"

T36
 -------------------------------------------------------------T12
| This  sequence places the printer into bit-immage  graphics |A
| and  prints the specified number of following bytes as  bit |
| information.                                                |
|                                                             |
|  !ESC S [XXXX] - CHR$(27)+CHR$(83)+ "  ?    ?    ?    ?  ""   |
|               !-   1BH      53H       3?H  3?H  3?H  3?H"     |
|                                                             |
| [!XXXX"] = a 4-digit decimal number which represents how many |
| of the following bytes will be printed as bit images.   The |
| number of dots per inch and line in each Character Pitch is |
|                                                             |
|  !PICA  80/in - 640/ln       PROPORTIONAL   160/in - 1280/ln" |
|  !ELITE 96/in - 786/ln        COMPRESSED    136/in - 1088/ln" |
|                                                             |     T12
 -------------------------------------------------------------T36
A






























                               C.9


                                         (continued) !XAPPENDIX CY
     


CONTROL SEQUENCES" (continued)


 !Bit-Graphics" (continued)


                            !EXAMPLE"

       To print the letter "M" using bit-image graphics:

   !1)" Lay out the letter on an 8 x 8 matrix.   Notice that  the
   letter is left justified in the matrix (most are).

                 X                               Y
                |   |   |   |   |   |   |   |   |T12
         bit 0    *                       *
                |X   |   |   |   |   |   |   |   Y|A
                |   |   |   |   |   |   |   |   |T12
         bit 1    *   *               *   *
                |X   |   |   |   |   |   |   |   Y|A
                |   |   |   |   |   |   |   |   |T12
         bit 2    *       *       *       *
                |X   |   |   |   |   |   |   |   Y|A
                |   |   |   |   |   |   |   |   |T12
         bit 3    *           *           *
                |X   |   |   |   |   |   |   |   Y|A
                |   |   |   |   |   |   |   |   |T12
         bit 4    *                       *
                |X   |   |   |   |   |   |   |   Y|A
                |   |   |   |   |   |   |   |   |T12
         bit 5    *                       *
                |X   |   |   |   |   |   |   |   Y|A
                |   |   |   |   |   |   |   |   |T12
         bit 6    *                       *
                |X   |   |   |   |   |   |   |   Y|A
                |   |   |   |   |   |   |   |   |T12
         bit 7
                |X   |   |   |   |   |   |   |   Y|A
   !2)" Translate this BINary information into either HEXadecimal
   or DECamal numbers.
    !HEXadecimal |7F |02 |04 |08 |04 |02 |7F |00 |"
      !DECimal   |127| 2 | 4 | 8 | 4 | 2 |127| 0 |"

   !3)"  Place  the  bit information at the end  of  the  control
   sequence.  We have eight(8) columns of graphics this time.

         !ESC S "0008"+CHR$(127)+CHR$(2)+CHR$(4)+CHR$(8)+
                      CHR$(4)+CHR$(2)+CHR$(127)+CHR$(0)"
T80


A

                              C.10


L000>                                                             !XAPPENDIX DY"


        !ASCII CHARACTER CODES"

L008
	!XDEC  HEX      BIN      CHR           DEC  HEX      BIN      CHRY"
	  0   00   0000-0000   NUL            48   30   0011-0000    0
	  1   01   0000-0001   SOH            49   31   0011-0001    1
	  2   02   0000-0010   STX            50   32   0011-0010    2
	  3   03   0000-0011   ETX            51   33   0011-0011    3
	  4   04   0000-0100   EOT            52   34   0011-0100    4
	  5   05   0000-0101   ENQ            53   35   0011-0101    5
	  6   06   0000-0110   ACK            54   36   0011-0110    6
	  7   07   0000-0111   BEL            55   37   0011-0111    7
	  8   08   0000-1000   BS             56   38   0011-1000    8
	  9   09   0000-1001   HT             57   39   0011-1001    9
	 10   0A   0000-1010   LF             58   3A   0011-1010    :
	 11   0B   0000-1011   VT             59   3B   0011-1011    ;
	 12   0C   0000-1100   FF             60   3C   0011-1100    <
	 13   0D   0000-1101   CR             61   3D   0011-1101    =
	 14   0E   0000-1110   SO             62   3E   0011-1110    >
	 15   0F   0000-1111   SI             63   3F   0011-1111    ?
	 16   10   0001-0000   DLE            64   40   0100-0000    @
	 17   11   0001-0001   DC1            65   41   0100-0001    A
	 18   12   0001-0010   DC2            66   42   0100-0010    B
	 19   13   0001-0011   DC3            67   43   0100-0011    C
	 20   14   0001-0100   DC4            68   44   0100-0100    D
	 21   15   0001-0101   NAK            69   45   0100-0101    E
	 22   16   0001-0110   SYN            70   46   0100-0110    F
	 23   17   0001-0111   ETB            71   47   0100-0111    G
	 24   18   0001-1000   CAN            72   48   0100-1000    H
	 25   19   0001-1001   EM             73   49   0100-1001    I
	 26   1A   0001-1010   SUB            74   4A   0101-1010    J
	 27   1B   0001-1011   ESC            75   4B   0100-1011    K
	 28   1C   0001-1100   FS             76   4C   0100-1100    L
	 29   1D   0001-1101   GS             77   4D   0100-1101    M
	 30   1E   0001-1110   RS             78   4E   0100-1110    N
	 31   1F   0001-1111   US             79   4F   0100-1111    O
	 32   20   0010-0000   SPC            80   50   0101-0000    P
	 33   21   0010-0001    !             81   51   0101-0001    Q
	 34   22   0010-0010    "             82   52   0101-0010    R
	 35   23   0010-0011    #             83   53   0101-0011    S
	 36   24   0010-0100    $             84   54   0101-0100    T
	 37   25   0010-0101    %             85   55   0101-0101    U
	 38   26   0010-0110    &             86   56   0101-0110    V
	 39   27   0010-0111    '             87   57   0101-0111    W
	 40   28   0010-1000    (             88   58   0101-1000    X
	 41   29   0010-1001    )             89   59   0101-1001    Y
	 42   2A   0010-1010    *             90   5A   0101-1010    Z
	 43   2B   0010-1011    +             91   5B   0101-1011    [
	 44   2C   0010-1100    ,             92   5C   0101-1100    \
	 45   2D   0010-1101    -             93   5D   0101-1101    ]
	 46   2E   0010-1110    .             94   5E   0101-1110    ^
	 47   2F   0010-1111    /             95   5F   0101-1111    _ 


	                              D.1


L000                                                             !XAPPENDIX DY"


        !ASCII CHARACTER CODES"

L008
	!XDEC  HEX      BIN      CHR           DEC  HEX      BIN      CHRY"
	 96   60   0110-0000    `            144   90   1001-0000    �
	 97   61   0110-0001    a            145   91   1001-0001    ‘
	 98   62   0110-0010    b            146   92   1001-0010    ’
	 99   63   0110-0011    c            147   93   1001-0011    “
	100   64   0110-0100    d            148   94   1001-0100    ”
	101   65   0110-0101    e            149   95   1001-0101    •
	102   66   0110-0110    f            150   96   1001-0110    –
	103   67   0110-0111    g            151   97   1001-0111    —
	104   68   0110-1000    h            152   98   1001-1000    ˜
	105   69   0110-1001    i            153   99   1001-1001    ™
	106   6A   0110-1010    j            154   9A   1001-1010    š
	107   6B   0110-1011    k            155   9B   1001-1011    ›
	108   6C   0110-1100    l            156   9C   1001-1100    œ
	109   6D   0110-1101    m            157   9D   1001-1101    �
	110   6E   0110-1110    n            158   9E   1001-1110    ž
	111   6F   0110-1111    o            159   9F   1001-1111    Ÿ
	112   70   0111-0000    p            160   A0   1010-0000     
	113   71   0111-0001    q            161   A1   1010-0001    ¡
	114   72   0111-0010    r            162   A2   1010-0010    ¢
	115   73   0111-0011    s            163   A3   1010-0011    £
	116   74   0111-0100    t            164   A4   1010-0100    ¤
	117   75   0111-0101    u            165   A5   1010-0101    ¥
	118   76   0111-0110    v            166   A6   1010-0110    ¦
	119   77   0111-0111    w            167   A7   1010-0111    §
	120   78   0111-1000    x            168   A8   1010-1000    ¨
	121   79   0111-1001    y            169   A9   1010-1001    ©
	122   7A   0111-1010    z            170   AA   1010-1010    ª
	123   7B   0111-1011    {            171   AB   1010-1011    «
	124   7C   0111-1100    |            172   AC   1010-1100    ¬
	125   7D   0111-1101    }            173   AD   1010-1101    ­
	126   7E   0111-1110    ~            174   AE   1010-1110    ®
	127   7F   0111-1111                175   AF   1010-1111    ¯
	128   80   1000-0000    €            176   B0   1011-0000    °
	129   81   1000-0001    �            177   B1   1011-0001    ±
	130   82   1000-0010    ‚            178   B2   1011-0010    ²
	131   83   1000-0011    ƒ            179   B3   1011-0011    ³
	132   84   1000-0100    „            180   B4   1011-0100    ´
	133   85   1000-0101    …            181   B5   1011-0101    µ
	134   86   1000-0110    †            182   B6   1011-0110    ¶
	135   87   1000-0111    ‡            183   B7   1011-0111    ·
	136   88   1000-1000    ˆ            184   B8   1011-1000    ¸
	137   89   1000-1001    ‰            185   B9   1011-1001    ¹
	138   8A   1000-1010    Š            186   BA   1011-1010    º
	139   8B   1000-1011    ‹            187   BB   1011-1011    »
	140   8C   1000-1100    Œ            188   BC   1011-1100    ¼
	141   8D   1000-1101    �            189   BD   1011-1101    ½
	142   8E   1000-1110    Ž            190   BE   1011-1110    ¾
	143   8F   1000-1111    �            191   BF   1011-1111    ¿


	                              D.2


L000                                                             !XAPPENDIX DY"
 

        !ASCII CHARACTER CODES"

L008
	!XDEC  HEX      BIN      CHR           DEC  HEX      BIN      CHRY"
	192   C0   1100-0000    À            240   F0   1111-0000    ð
	193   C1   1100-0001    Á            241   F1   1111-0001    ñ
	194   C2   1100-0010    Â            242   F2   1111-0010    ò
	195   C3   1100-0011    Ã            243   F3   1111-0011    ó
	196   C4   1100-0100    Ä            244   F4   1111-0100    ô
	197   C5   1100-0101    Å            245   F5   1111-0101    õ
	198   C6   1100-0110    Æ            246   F6   1111-0110    ö
	199   C7   1100-0111    Ç            247   F7   1111-0111    ÷
	200   C8   1100-1000    È            248   F8   1111-1000    ø
	201   C9   1100-1001    É            249   F9   1111-1001    ù
	202   CA   1100-1010    Ê            250   FA   1111-1010    ú
	203   CB   1100-1011    Ë            251   FB   1111-1011    û
	204   CC   1100-1100    Ì            252   FC   1111-1100    ü
	205   CD   1100-1101    Í            253   FD   1111-1101    ý
	206   CE   1100-1110    Î            254   FE   1111-1110    þ
	207   CF   1100-1111    Ï            255   FF   1111-1111    ÿ
	208   D0   1101-0000    Ð
	209   D1   1101-0001    Ñ
	210   D2   1101-0010    Ò
	211   D3   1101-0011    Ó
	212   D4   1101-0100    Ô
	213   D5   1101-0101    Õ
	214   D6   1101-0110    Ö
	215   D7   1101-0111    ×
	216   D8   1101-1000    Ø
	217   D9   1101-1001    Ù
	218   DA   1101-1010    Ú
	219   DB   1101-1011    Û
	220   DC   1101-1100    Ü
	221   DD   1101-1101    Ý
	222   DE   1101-1110    Þ
	223   DF   1101-1111    ß
	224   E0   1110-0000    à
	225   E1   1110-0001    á
	226   E2   1110-0010    â
	227   E3   1110-0011    ã
	228   E4   1110-0100    ä
	229   E5   1110-0101    å
	230   E6   1110-0110    æ
	231   E7   1110-0111    ç
	232   E8   1110-1000    è
	233   E9   1110-1001    é
	234   EA   1110-1010    ê
	235   EB   1110-1011    ë
	236   EC   1110-1100    ì
	237   ED   1110-1101    í
	238   EE   1110-1110    î
	239   EF   1110-1111    ï


	                              D.3<


                                                     !XAPPENDIX EY



NUMBERING SYSTEMS"



Most of us count using !DEC"imal numbers.  It !is a BASE 10 system"
which  means that it has 10 digits (0 through 9).   But a  com-
puter uses a !BASE 2" counting system that !is called BIN"ary.  (So
does your printer,  by the way).  Even though we probably won't
start using BINary arithmetic in our daily lives,  if we expect
to  make  any inroads into the understanding of  the  computer,
(and  the NEC 8023A),  it sure helps to have at lease  a  smat-
tering of knowledge about BINary numbers. So here goes.



The  binary  system has only two(2) digits for  counting.   You
probably  guessed as much.   The digits are 0 and  1.   In  the
computer  these used as OFF(0) and ON(1).   As I'm sure you can
imagine,  it is extremely difficult,  for humans at  least,  to
keep  track  of very large numbers using BINary without  making
lots of mistakes.



So,  somewhere along the line, the !HEX"adecimal numbering system
came into being.   It has 16 digits and so !is a BASE 16 system".
At first this might seem even more complicated than BASE 10  or
BASE 2.  It isn't, beleive me!



Most computers and printers have been designed to work with  at
least  one(1) byte of information at a time.   At least  that's
the  way  it  appears  to those of us  outside  of  the  micro-
processor.   Since  this is the case,  it means that we can use
eight(8)  BITS(binary digits) to represent this single byte  of
information.

Like this.             !xxxx-xxxx = 1 BYTE"



Now,  since there are only sixteen(16) posible combinations  of
1's  and  0's  for each half of any byte,  (half of a  byte  is
called  a nybble),  you can see how HEXadecimal  counting  came
into being.







                               E.1


                                                     !XAPPENDIX EY



NUMBERING SYSTEMS"

What  we need now is a single digit to represent each nybble of
a byte,  and that's exactly what we have with HEXadecimal  num-
bers.   But I only know 10 digits.  Do I have to make up six(6)
new ones to be able to use HEX?  No!  Someone else already did.
Well, what actually happened, is that it was decided to use the
first  six(6)  letters of the alphabet,  since most of  us  are
already familiar with them.


Here  is  a  table  that shows  the  relationship  between  the
three(3) numbering systems we have talked about.   The  DECimal
numbers  are in the first column,  (since you are familiar with
those),  the  BINary  numbers second,  (since that  is  what  a
computer  or printer uses),  and last HEXadecimal,  (a  meeting
place somewhere between us and the computer).

                     !DEC     BIN       HEX"
                      0      0000       0
                      1      0001       1
                      2      0010       2
                      3      0011       3
                      4      0100       4
                      5      0101       5
                      6      0110       6
                      7      0111       7
                      8      1000       8
                      9      1001       9
                     10      1010       A
                     11      1011       B
                     12      1100       C
                     13      1101       D
                     14      1110       E
                     15      1111       F


Now,  if we have 2 nybbles instead of the 1 shown in the table,
we can have a total 256 combinations.   One(1) byte.  Familiar?
That is the number of ASCII characters.  Exactly!


With the NEC 8023A, the main use for all this information, will
be when you're doing Bit-Graphics.  On the next page is a table
that  you may find useful for converting your  bit-images  into
either HEX or DEC data so it can be sent to the printer.


This  is certainly not an in-depth discussion of the  different
numbering systems, but then that is just a bit beyond the scope
of this manual.


                               E.2


                                                     !XAPPENDIX EY



NUMBERING SYSTEMS

                LEAST and MOST SIGNIFICANT BITS"
                 0-3       4-7

                            !DECIMAL"
L002Q
   X 0   1   2   3   4   5   6   7   8   9  10  11  12  13  14  15    1   2   3   4   5   6   7   8   9  10  11  12  13  14  15 Y
0 |X   |   |   |   |   |   |   |   | * | * | * | * | * | * | * | * ||   |   |   |   |   |   |   |   |   |   |   |   |   |   |   Y|
1 |X   |   |   |   | * | * | * | * |   |   |   |   | * | * | * | * ||   |   |   |   |   |   |   |   |   |   |   |   |   |   |   Y|
2 |X   |   | * | * |   |   | * | * |   |   | * | * |   |   | * | * ||   |   |   |   |   |   |   |   |   |   |   |   |   |   |   Y|
3 |X   | * |   | * |   | * |   | * |   | * |   | * |   | * |   | * ||   |   |   |   |   |   |   |   |   |   |   |   |   |   |   Y|
4 |X   |   |   |   |   |   |   |   |   |   |   |   |   |   |   |   ||   |   |   |   |   |   |   | * | * | * | * | * | * | * | * Y|
5 |X   |   |   |   |   |   |   |   |   |   |   |   |   |   |   |   ||   |   |   | * | * | * | * |   |   |   |   | * | * | * | * Y|
6 |X   |   |   |   |   |   |   |   |   |   |   |   |   |   |   |   ||   | * | * |   |   | * | * |   |   | * | * |   |   | * | * Y|
7 |X   |   |   |   |   |   |   |   |   |   |   |   |   |   |   |   || * |   | * |   | * |   | * |   | * |   | * |   | * |   | * Y|
    00  01  02  03  04  05  06  07  08  09  0A  0B  0C  0D  0E  0F   10  20  30  40  50  60  70  80  90  A0  B0  C0  D0  E0  F0
NL008
                          !HEXADECIMAL"
 -------------------------------------------------------------
                            !DECIMAL"

        X  1     2     4     8     16    32    64   128 Y
       |     |     |     |     |     |     |     |     |T12
 bit 0                                              *
       |X     |     |     |     |     |     |     |     Y|A
       |     |     |     |     |     |     |     |     |T12
 bit 1                                        *
       |X     |     |     |     |     |     |     |     Y|A
       |     |     |     |     |     |     |     |     |T12
 bit 2                                  *
       |X     |     |     |     |     |     |     |     Y|A
       |     |     |     |     |     |     |     |     |T12
 bit 3                            *
       |X     |     |     |     |     |     |     |     Y|A
       |     |     |     |     |     |     |     |     |T12
 bit 4                      *
       |X     |     |     |     |     |     |     |     Y|A
       |     |     |     |     |     |     |     |     |T12
 bit 5                *
       |X     |     |     |     |     |     |     |     Y|A
       |     |     |     |     |     |     |     |     |T12
 bit 6          *
       |X     |     |     |     |     |     |     |     Y|A
       |     |     |     |     |     |     |     |     |T12
 bit 7    *
       |X     |     |     |     |     |     |     |     Y|A
          01    02    04    08    10    20    30    80T48
                          !HEXADECIMAL"T66


 
A
                               E.3


                                                          !XINDEXY"



ASCII CODES list          D.1  |  LINE SPACING
ASPECT, SCREEN (notes)    2.6  |     Explanation            4.3
AUTOEXEC.BAT FILE              |     Print_Characters       3.5
   Print_Characters       3.3  |     Setting w/PRNT-SET    4.20
   Print_Screen           2.3  |  MARGIN, LEFT
BACKUP COPIES                  |     Explanation            4.6
   Policy                 1.3  |     Setting w/PRNT-SET    4.21
   Procedure              1.3  |  NUMBERING SYSTEMS         E.1
BINary NUMBERS      4.13, E.1  |   NUMBERS
BOTTOM OF FORM (BOF)     4.12  |     BINary                4.13
CHARACTER CODES, ASCII    D.1  |     DECimal                E.1
CHARACTER PITCH                |     HEXadecimal            3.1
   Explanation            4.2  |  OUT Command (notes)       3.5
   Setting w/PRNT-SET    4.20  |  PAGE LENGTH (TOF-BOF)    4.12
CONNECTING LINKS (notes)  3.5  |  PITCH,CHARACTER
CONTROL SEQUENCES         C.1  |     Explanation            4.2
COPY                      1.3  |     Setting w/PRNT-SET    4.20
DECimal NUMBERS           E.1  |  PRINTER CONTROL           C.1
DEMONSTRATION                  |  PRINTER HOOK-UP (notes)   2.6
   Print_Characters       3.2  |  PRINT_CHARACTERS
   Printer_Set           4.19  |     Autoexec.bat File      3.3
   Print_Screen           2.2  |     Demonstration          3.2
DEMOnstration DISKette         |     Explanation            3.1
   Making                 1.3  |     Extended ASCII Set     3.1
   Use of      2.2, 3.2, 4.19  |     Installation
DISKCOPY                  1.3  |        Method One          3.2
ESCape Code (notes)       4.1  |        Method Two          3.3
FINALWORD                5.13  |     Italics Characters     3.1
FORM LENGTH (TOF-TOF)    4.12  |     Program Use            3.1
   Setting w/PRNT-SET    4.22  |     Technical Information  3.4
FORMS                          |  PRINTER_SET
   Explanation            4.7  |     Program Use            4.1
   Setting                     |     Demonstration         4.19
      From BASIC         4.13  |  PRINTER SWITCH SETTINGS   A.1
      With PRINTER_SET   4.22  |  PRINT_SCREEN
FORMAT                    1.3  |     Access from BASIC
GROUP SEPARATOR (GS)      4.9  |        Explanation         2.4
HEXadecimal NUMBERS  3.1, E.1  |        Program Listing     2.5
HORIZONTAL TABS                |     Autoexec.bat File      2.3
   Explanation            4.4  |     Demontratrion          2.2
   Setting w/PRNT-SET    4.21  |     Explanation            2.1
H TEST                    B.1  |     Installation
INKEY$                    2.4  |        Method One          2.2
INTerrupt 5H              2.4  |        Method Two          2.3
INTerrupt 17H (notes)     3.5  |     Program Use            2.1
LEFT MARGIN                    |     Technical Information  2.6
   Explanation            4.6  |
   Setting w/PRNT-SET    4.21  |





                              X.1


                                                          !XINDEXY"
                                 
 

PROGRAM USE
   Print_Characters       3.1
   Printer_Set            4.1
   Print_Screen           2.1
RECORD SEPARATOR (RS)     4.9
REQUIREMENTS
   Computer               1.2
   Diskdrives             1.2
   Display                1.2
   Display Adapter        1.2
   Memory                 1.2
   Operating System       1.2
   Printer                1.2
SCREEN ASPECT (notes)     2.6
SINGLE DRIVE (notes)      1.3
SOFTWARE LIST             1.1
SWITCH SETTINGS           A.1
TABS
   Horizontal
      Explanation         4.4
      Setting w/PRNT-SET 4.21
   Vertical
      Explanation        4.16
      Setting w/PRNT-SET 4.22
TECHNICAL INFORMATION
   Print_Characters       3.4
   Print_Screen           2.6
TOP OF FORM (TOF)        4.12
   Setting w/PRNT-SET    4.22
TRANSPARENCIES (notes)    2.6
UNIT SEPARATOR (US)      4.16
VERTICAL FORMAT
   Explanation            4.7
   Setting
      From BASIC         4.13
      From PRINTER_SET   4.22
VERTICAL TABS
   Explanation           4.16
   Setting w/PRNT-SET    4.22
VOLKSWRITER              5.12
WORD PROCESSING           5.1
   FinalWord             5.13
   Volkswriter           5.12
   WordStar               5.2
WORDSTAR                  5.2








                              X.2


                                                    !XADVERTISINGY


T12
        tm
USERWARE"T48
I prefer to think of certain software products now available inA
the  market  place as being USERWARE.   Each of these  products
has several things in common.

!1)"  Each is designed for ease of use by the final user.

!2)"  The  user  is able to test the utility of the  software  on
    his/her own system before committing to purchase.

!3)"  The  distribution of the product is handled mainly  by  the
    user.

!4)"  The  author's contributions are  the  programming,  program
    updating, and user support.

!5)"  The  viability  of the software depends  on  the  continued
    support of those who use it.


The  USERWARE  method of distribution and support is unique  in
that it allows each of us involved to make contributions in the
areas for which we are individually suited.

Since  I  am the author,  my contributions are rather  obvious.
Programming,  updating and especially user support.  But, my on
going support is only possible if I continue to receive  regis-
tration  fees.   If registrations stop or slow to a trickle,  I
can  only assume that the  NEC 8023A UTILITIES  are  no  longer
viable and will therefore shift my attention elseware.

As the user of this product, and others like it, your continued
support  is in the form of suggestions for changes and or addi-
tions to the existing package.   And don't forget,  !YOU ARE THE
DISTRIBUTOR."  So distribute.  Please!!

Being a strong believer in USERWARE,  as a further contribution
to this method of distribution, etc.,  I will include a page of
advertising  for  other major products that fit this  catagory.
If you are the author of such a program, please contact me.












                               ADV


                                                    !XADVERTISINGY


T12
        tm
USERWARE"T36
                                   tmT12
                         CHASMT48
A
If you use assembly language or are even thinking of adding  it
to you repertoire of languages,  this is an indispensable piece
of  software.   CHASM  has  a definite advantage over  the  IBM
assembler, in that it much easier to use.

!Several strong points are:

1)" You  are able to assemble a COM program in a single step  as
   opposed  to the complicated and convoluted method needed for
   the IBM assembler.

!2)" Included are two(2) different, simple mechanisms for getting
   machine language routines into BASIC.

!3)" The program's manual and beginner's primer are very  clearly
   written and easily understood.

!4)" Unlike the support (?) available for the IBM assembler,  the
   author of CHASM is extremely supportive and accessible.

The  NEC 8023A UTILITIES  and other assembly language  programs
produced  by  SOFT & FRIENDLY were assembled  using  CHASM.   I
couldn'd do without it.

CHASM  will run easily in a 64K machine and is  available  from
the author.   The suggested registration (contribution) is $30.

To receive an evaluation copy send a blank,  formatted diskette
to the author.   An addressed,  postage-paid return mailer must
accompany the diskette.


                    !WHITMAN SOFTWARE
                    David Whitman
                    136 Wellington Terrace
                    Lansdale  PA  19446"












                               ADV


                                                    !XADVERTISINGY


T12
        tm
USERWARE"T36
                                   tmT12
                       NUMZAPT48
A
If you use the IBM/Microsoft BASIC compiler,  chances are  your
programs  are bigger and slower than they have to be.   If  all
unreferenced line numbers are removed from your source program,
and the /N switch is used,   BASCOM will optimize your program.
The result is tighter, more efficient code.

NUMZAP is a utility which carefully scans your source file, and
deletes  all the non-essential line numbers.   Performing  this
task  by hand would be prohibitively time comsuming and  you'ld
probably  introduce  errors into your program in  the  process.
NUMZAP will do the job in minutes, 100% error free.

An added advantage to using NUMZAP is that bigger programs  can
be compiled.  You may not be aware that there is a limit on the
size of programs which the compiler can handle.  BASCOM uses up
space  remembering the offset of each line number in your  pro-
gram.  If you have too many numbered lines, BASCOM will run out
of  room and you'll get an unending series of TC,  Too Complex,
error messages.   By eliminating the unneeded line numbers, you
give BASCOM more elbow room.

The suggested registration (contribution) is $15.   To  receive
an  evaluation  copy send a blank,  formatted diskette  to  the
author.   An addressed,  postage-paid return mailer must accom-
pany the diskette.  


                    !WHITMAN SOFTWARE
                    David Whitman
                    136 Wellington Terrace
                    Lansdale  PA  19446"

















                               ADV


                                                    !XADVERTISINGY


T12
        tm
USERWARE"T48
A
              PRINTER UTILITIES


SOFT  &  FRIENDLY is continually adding utilities  for  various
printers  available  on the market.   At the  writing  of  this
user manual, the list includes:


        !PRINT_SCREEN for:
                TOSHIBA 1350P
                EPSON RX-80

        PROWRITER UTILITIES" (PRNT-SCN,PRNT-CHR, and PRNT-SET)

        !SET_PRINTER for:" (a batch file printer setting utility)
                !TOSHIBA 1350P
                EPSON RX-80
                PROWRITER I & II
                OKIDATA 92
                NEC 8023A
                NEC PINWRITER P2-2"
 

By  the  time you read this list,  the number of programs  will
have surely increased.  To get an updated list, contact:


                     !SOFT & FRIENDLY
                     Michael L Hoyt
                     R 2  Box 65
                     Solsberry  IN  47459
                     812-825-7384"


















                               ADV