SETUP                                     Jeff Prosise
          Command
          Copyright (c) 1986, Ziff-Davis Publishing Co.
          ______________________________________________________

          Purpose:  Permits menu-oriented selection and immediate
                    transmission of printer control codes from
                    within a running application program.

          Format:   SETUP            (loads command into memory)
                    <Ctrl-Right Shift>          (activates menu)
                    <[Shift]<Fx>      (selects [deselects] mode)
                    <Esc>            (activates selection(s) and
                                 returns to application program)

                    Fx is a Function key (F1 through F10) that
                    sends the required control sequence to the
                    printer.  Shift-Fx toggles the selected
                    printer mode off.

          Remarks:  After loading SETUP (normally via your
                    AUTOEXEC.BAT file), the printer mode
                    selection menu program is displayed by
                    pressing the Ctrl-Right Shift key
                    combination.  This can be done from within
                    application programs that do not take over
                    the keyboard interrupts; the application is
                    simply suspended until you leave SETUP by
                    pressing the Esc key.  (Application programs
                    such as XyWrite III that do take over the
                    keyboard interrupts can be used with
                    SETUP.COM if they themselves provide the
                    option of temporarily returning to DOS
                    control.)

                    Printer permitting, more than one mode can be
                    selected at once by pressing additional
                    function keys.  The default printer choices
                    are for the Epson RX/FX series.  Option 1
                    shows how to modify the program for other
                    printers.

                    Notes:

                    1.   SETUP.COM is a memory-resident program
                         (approximately 3K in length), and so is
                         subject to conflicts with other memory-
                         resident software.  Several users have
                         reported that it is incompatible with
                         Prokey, for example.  Similarly, while
                         SETUP.COM is compatible with SideKick,
                         the combination of SuperKey and SideKick
                         has been reported to be incompatible.

          Option 1: If you have access to an IBM or Microsoft
                    macro assembler, the easiest way to modify
                    SETUP for other printers (or to use LPT2: or
                    LPT3: instead of LPT1:) is to modify the
                    SETUP.ASM file (available for download from
                    the PC Magazine Interactive Reader Service
                    (IRS) BBS (212) 696-0360) in any ASCII word
                    processor.  You can then make your
                    modifications and reassemble the file.
                                 Page -1-


                    Even if you do not have a macro assembler and
                    must therefore use DEBUG.COM to modify
                    SETUP.COM directly, print out and read the
                    SETUP.ASM file.  It is heavily commented, and
                    will give you a good idea of how the
                    different menu strings and printer control
                    strings are organized.  Note, however, that
                    the specific values shown in SETUP.ASM are in
                    decimal notation; values entered via DEBUG
                    must be in hexadecimal notation.

                    The following offset addresses, not those
                    originally published in PC Magazine, should
                    be used:

                    The menu color attributes (4F and 70) are at
                    offsets xxxx:013F and xxxx:0140.

                    To change the port number from LPT1: to LPT2:
                    (or LPT3:) change the default 00 at xxxx:0C7A
                    and at xxxx:0C84 to 01 (or 02).

                    The start of the menu text table (532 bytes,
                    beginning with C9) is at offset xxxx:0151.
                    The "P" in PRINTER SETUP MENU" is at
                    xxxx:0172.

                    The printer control strings themselves begin
                    at xxxx:09A1.  Each function key (and each
                    shifted function key, with the exception of
                    F19 and F20) can be assigned a string up to
                    16 bytes long.  Each string must include a
                    delimiter of FF (255 decimal) that marks the
                    end of the string.  The beginning of the
                    string for each successive function key
                    starts at an address that is a multiple of 16
                    bytes above the base address (xxxx:09A1) of
                    the table.  You must pad the strings with
                    zeros for any locations that are not used by
                    actual control codes, so that each string
                    begins on a 16-byte boundary.