EISACFG

                                 Version 1.41

                             Septemeber 22, 1992

                              Michael Brundridge
                            710 Birch Brook Drive
                             Leander, Texas 78641

                   Copyright 1991, 1992 Michael Brundridge
                             All rights reserved



























                                  Table of Contents

     1. Introduction . . . . . . . . . . . . . . . . . . . . . . . . . . .    1
          1.1 Features . . . . . . . . . . . . . . . . . . . . . . . . . .    1
          1.2 Terms in this manual . . . . . . . . . . . . . . . . . . . .    1

     2. Using shareware  . . . . . . . . . . . . . . . . . . . . . . . . .    2
          2.1 Disclaimer - agreement . . . . . . . . . . . . . . . . . . .    2
          2.2 Contacting the author  . . . . . . . . . . . . . . . . . . .    2


     3. Running EISACFG  . . . . . . . . . . . . . . . . . . . . . . . . .    3

     4. Quick-start  . . . . . . . . . . . . . . . . . . . . . . . . . . .    4

     5. Questions asked by EISACFG . . . . . . . . . . . . . . . . . . . .    5
          5.1 NAME Statement . . . . . . . . . . . . . . . . . . . . . . .    5
          5.2 CATEGORY Statement . . . . . . . . . . . . . . . . . . . . .    5
          5.4 SLOT Statement . . . . . . . . . . . . . . . . . . . . . . .    6
          5.5 AMPERAGE Statement . . . . . . . . . . . . . . . . . . . . .    6
          5.6 DMA Statement. . . . . . . . . . . . . . . . . . . . . . . .    7
             5.6.1 SHARED Statement  . . . . . . . . . . . . . . . . . . .    7
             5.6.2 TRANSFER SIZE Statement . . . . . . . . . . . . . . . .    7
             5.6.3 CYCLE TIMING Statement  . . . . . . . . . . . . . . . .    7
          5.7 IRQ Statement  . . . . . . . . . . . . . . . . . . . . . . .    8
             5.7.1 SHARED Statement  . . . . . . . . . . . . . . . . . . .    8
             5.7.2 TRIGGER Statement . . . . . . . . . . . . . . . . . . .    8
          5.8 PORT Statement . . . . . . . . . . . . . . . . . . . . . . .    9
             5.8.1 ENDING ADDRESS Statement  . . . . . . . . . . . . . . .    9
             5.8.2 SHARED Statement. . . . . . . . . . . . . . . . . . . .    9
             5.8.3 SIZE Statement. . . . . . . . . . . . . . . . . . . . .    9
          5.9 RAM ADDRESS Statement  . . . . . . . . . . . . . . . . . . .   10
             5.9.1 MEMORY Statement  . . . . . . . . . . . . . . . . . . .   10
             5.9.2 MEMTYPE Statement . . . . . . . . . . . . . . . . . . .   10
             5.9.3 SHARED Statement  . . . . . . . . . . . . . . . . . . .   11
             5.9.4 CACHED Statement  . . . . . . . . . . . . . . . . . . .   11
             5.9.5 TYPE Statement  . . . . . . . . . . . . . . . . . . . .   11
             5.9.6 DECODE Statement  . . . . . . . . . . . . . . . . . . .   11
         5.10 RAM ADDRESS Statement  . . . . . . . . . . . . . . . . . . .   12
            5.10.1 MEMORY Statement  . . . . . . . . . . . . . . . . . . .   12
            5.10.2 CACHED Statement  . . . . . . . . . . . . . . . . . . .   12
            5.10.3 TYPE Statement  . . . . . . . . . . . . . . . . . . . .   13
            5.10.4 DECODE Statement  . . . . . . . . . . . . . . . . . . .   13

     6. !ISA0001.CFG Listing . . . . . . . . . . . . . . . . . . . . . . .   14

     7. Using !ISA0001.CFG . . . . . . . . . . . . . . . . . . . . . . . .   16

     8. Renaming !ISA0001.CFG  . . . . . . . . . . . . . . . . . . . . . .   16






                                    - i -





     1. Introduction

     EISACFG is an easy to use program.  The main purpose of EISACFG is to
     generate GENERIC EISA CONFIGURATION FILES for the Industry Standard
     Architecture (ISA) based card being used in an Extended Industry Standard
     Architecture (EISA) based system.

     EISACFG will write a configuration file based on answers you supplied to
     the questions asked by EISACFG.


     1.1 Features

     o    Simple operation.

     o    Two modes, STANDARD and ADVANCED


     1.2 Terms in this manual

     The following conventions are used in this manual:

     o    The Enter or Return key on the keyboard is displayed as <Enter>.

          




























                                    - 01 -




     2. Using freeware

     Freeware distribution gives users the ability to use the software at no
     charge.

     Copyright laws apply to both Freeware and commercial software, and the
     copyright holder retains all rights, with a few specific exceptions as
     stated below.

     The author specifically grants the right to copy and distribute the
     software, to all groups.


     2.1 Disclaimer/Agreement

     Users of EISACFG must accept this disclaimer of warranty:

     EISACFG--is supplied as is.  The author disclaims all warranties,
     expressed or implied, including, without limitation, the warranties of
     merchantability and of fitness for any purpose. The author assumes no
     liability for damages, direct or consequential, which may result from the
     use of EISACFG.

     EISACFG is a "freeware program" and is provided at no charge to the user.
     Feel free to share it with your friends, but please do not give it away
     altered or as part of another system.

     There may be no Commercial use or distribution of EISACFG.
     
     If you need or wish to say thanks for this utility in a monetary manner,
     you can send $5 to a charitable organization of your choice.

     You are encouraged to pass a copy of EISACFG along to your friends for
     use.
     
     All trademarks referenced in this document are the property of their
     respective owners.


     2.2 Contacting the author

     There are several ways to contact Michael Brundridge, the author of
     EISACFG.

     The easiest way is through the Internet--Send a message to mikeb@dell.com
     or mikeb@pandora.dell.com.

                                    - or -

     By US Postal Mail--write to the address on the first page of this
     document.  He can also be contacted through



                                    - 02 -




     3. Running EISACFG

     The command string for running EISACFG is:

          EISACFG [options]

     The items in brackets are optional.  The easiest and suggested way to
     run EISACFG, from the command line:

     C:\>EISACFG<Enter>

     (<Enter> means to hit the Enter or Return key on the keyboard.)

     Options are single letters preceded by a forward slash (/), or a dash
     (-), i.e. -A or /A.

     C:\>EISACFG /A<Enter>

     EISACFG will display a banner page with version number and a HELP SCREEN
     by using the ?. /?, or -? option:

     C:\>EISACFG ?<Enter>
































                                    - 03 -




     4. Quick-start

     To get a feel for how to use EISACFG, just type EISACFG at the DOS prompt
     and press <Enter>.  It will display the banner page and the first
     question.


 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 ³                 Copyright  Michael Brundridge  1991, 1992                  ³
 ³             Generic ISA card EISA CONFIGURATOR - Version 1.41              ³
 ³                           Press ESC to QUIT                                ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ+>RUNNING STANDARD MODE<+ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
 Enter the card manufacturer's name below:

 Default: Generic ISA

 What is the card manufacturer's name?





































                                    - 04 -




     5. Questions asked by EISACFG


     5.1 NAME Statement:

     Enter the card manufacturer's name below:

     Default: Generic ISA

     What is the card manufacturer's name?

       Syntax:
       NAME = "descriptive name"

       The NAME statement contains text that identifies the product.  Part
       numbers and other information may also be included.  The NAME text
       field can contain up to 90 ASCII characters.

     ------------------------------------------------------------------------

     5.2 CATEGORY Statement:

     Choices:

     COM = Communications Device      NPX = Numeric Coprocessor
     KEY = Keyboard                   OSE = Operating System/Environment
     MEM = Memory Board               OTH = Other
     MFC = Multifunction Board        PAR = Parallel Port
     MSD = Mass Storage Device        PTR = Pointing Device
     NET = Network Board              SYS = System Board
     VID = Video Board

     Default: OTH

     Enter a three digit code for card CATEGORY from above?

       Syntax:
       CATEGORY = "3-character category"

       The CATEGORY statement contains a 3-character ASCII string that
       identifies the board's functional category.  The configuration utility
       displays the CATEGORY text field during system configuration.


       The CATEGORY statement must use one of the categories shown above









                                    - 05 -
 



     5.3 SLOT Statement:

     Choices: (Y)es, (N)o

     Default: Y

     Is the ISA card a 16-bit card?

       Syntax:
       SLOT = value [,"text"]...

       The SLOT statement identifies the type of slot in which the expansion
       board can be installed.  Options that can be entered in the value field
       include: ISA8, or ISA16

       The value entered in the SLOT field is the actual size of the board's
       card edge. For example, an expansion board with an 8 bit card edge is
       set to SLOT = ISA8, an expansion board with a 16 bit card edge is set
       to SLOT = ISA16, and so on.

     ------------------------------------------------------------------------

     5.5 AMPERAGE Statement:

     The question below for AMPERAGE is for the +5 Volt line and should be
     in milliamps.

     We suggest you try to locate this value so that the EISA config can
     inform you when you have reached the current limit of the power supply.

     Default: 0

     +5 Volt AMPERAGE draw in milliamps (i.e. 300)?

       Syntax:
       [AMPERAGE = value]

       The AMPERAGE statement, specifies the maximum amount of continuous 5V
       current (in milliamps) required by the base configuration of the
       expansion board.

       Devices that require +5 volt power should include an AMPERAGE
       statement. The configuration utility cannot perform an accurate power
       usage verification if expansion boards that do not specify their power
       requirement.









                                    - 06 -




     5.6 DMA Statement:

       (The DMA section specifies the choice of DMA channels, whether the
       channel can be shared, the channel's data size, the channel's cycle
       timing.)

     Enter the DMA from the list below, or press ENTER if not used:

     Choices: 1, 2, 3, 4, 5, 6, 7

     Default: NONE

     What is the DMA Channel?

       Syntax:
       DMA = value

       The DMA statement marks the beginning of a DMA Request Block and
       specifies the DMA channel number supported by the configuration.

     ------------------------------------------------------------------------

     5.6.1 DMA (SHARED) Statement:

     Choices: (Y)es, (N)o

     Default: N

     Will the DMA Channel be SHARED?

     ------------------------------------------------------------------------

     5.6.2 DMA (TRANSFER SIZE) Statement: [ADVANCED OPTION]

     Choices are:  BYTE, WORD

     Default: If DMA = 1-3 'BYTE', if DMA = 4-7 'WORD'

     What SIZE DMA transfer is used?

     ------------------------------------------------------------------------

     5.6.3 DMA (CYCLE TIMING) Statement: [ADVANCED OPTION]

     Choices are: DEFAULT, TYPEA, TYPEB

     Default: DEFAULT

     What type of bus cycle (TIMING) is used for DMA transfers?





                                    - 07 -




     5.7 IRQ Statement:

     Enter the IRQ from the list below, or press ENTER if not used:

     Choices: 3, 4, 5, 6, 7, 9, 10, 11, 12, 13, 14, 15

     Default: NONE

     IRQ being used?

       Syntax:
       IRQ = Interrupt number

       The IRQ statement specifies the interrupt number supported by the
       configuration.

       Each interrupt selected during system configuration is stored in
       nonvolatile memory with the appropriate SHARE and TRIGGER
       characteristics, as well as the EDGE/LEVEL interrupt controller
       setting.

     ------------------------------------------------------------------------

     5.7.1 IRQ (SHARED) Statement:

     Choices: (Y)es, (N)o

     Default: N

     Will the IRQ be SHARED?

     ------------------------------------------------------------------------

     5.7.2 IRQ (TRIGGER) Statement: [ADVANCED OPTION]

     Choices: EDGE, LEVEL

     Default: If SHARE = NO 'EDGE', if SHARE = YES 'LEVEL'

     How is the INTERRUPT controller TRIGGERED?














                                    - 08 -




     5.8 PORT Statement:

     Enter the BASE I/O PORT address for the card, or press ENTER if not used:

     Choices: 100H-FFFH

     Default: NONE

     Starting BASE I/O PORT Address (i.e. 300)?

       Syntax:
       PORT = rangelist

       The PORT statement may specify a single address, a range of addresses.

       NOTE: The I/O address should be 3 digits in length.  The real first
       usable address by an I/O card is 100.

     ------------------------------------------------------------------------

     5.8.1 PORT (ENDING ADDRESS) Statement:

     Ending BASE I/O PORT Address (i.e. 30F)?

       NOTE: The I/O address should be 3 digits in length.  The real first
       usable address by an I/O card is 100.
     ------------------------------------------------------------------------

     5.8.2 PORT (SHARED) Statement:

     Choices: (Y)es, (N)o

     Default: N

     Will the BASE I/O PORT be SHARED?

     ------------------------------------------------------------------------

     5.8.3 PORT (SIZE) Statement: [ADVANCED OPTION]

     Choices: BYTE, WORD

     Default: BYTE

     What SIZE is the PORT?









                                     - 09 -




     5.9 ADDRESS Statement: (for RAM)

     Enter the RAM location from the possible list below, paying attention to
     not cause a memory address conflict, or press ENTER if no RAM present:

     0C000 through FF000

     Default: NONE

     RAM location (i.e. 0C800)?

       ADDRESS Statement (Optional)

       Syntax:
       ADDRESS = list

       The ADDRESS statement specifies the starting address of the
       READ/WRITABLE memory on the card.

       NOTE: Make certain to proceed any address below 1MB with a 0 as shown
       in the example above. (i.e. if the address is C800 enter 0C800).

     ------------------------------------------------------------------------

     5.9.1 MEMORY Statement: (for RAM)

     Choices: 8K, 16K, 32K, 64K, 128K

     Default: 32K

     How much memory is located on the card?

       Syntax:
       MEMORY = length

       The length following the MEMORY statement specifies the maximum
       size of the memory (in Kilobytes) installed on the board.

     ------------------------------------------------------------------------

     5.9.2 MEMTYPE Statement: (for RAM)

     Choices:

     SYS = System             EXP = Expanded
     VIR = Virtual            OTH = Other

     Default: OTH

     MEMORY Type from above list?

       Syntax:
       [MEMTYPE = SYS ³ EXP ³ VIR ³ OTH]

                                    - 10 -




       The MEMTYPE field specifies whether the memory is SYStem (base and
       extended memory), EXPanded, OTHer (address used for memory mapped I/O
       or bank switched memory), or VIRtual (indicates the space is being
       used, but no physical memory occupies the address, i.e. address of a
       LIM page frame).

     ------------------------------------------------------------------------

     5.9.3 MEMORY (SHARED) Statement: (for RAM)

     Choices: (Y)es, (N)o

     Default: Y

     Will the MEMORY be SHARED?

     ------------------------------------------------------------------------

     5.9.4 MEMORY (CACHED) Statement: (for RAM)

     Choices: (Y)es, (N)o

     Default: N

     Should the RAM be CACHED?

       This will set the 80486 CPU up so it will allow the address to be
       cached.

       This option can cause problems.  If you turn it on and start having
       problems with other hardware, or even programs, try turning it OFF and
       running it again.

     ------------------------------------------------------------------------

     5.9.5 MEMORY (TYPE) Statement: (for RAM) [ADVANCED OPTION]

     Choices: BYTE, WORD

     Default: BYTE

     What type is the memory?

     ------------------------------------------------------------------------

     5.9.6 MEMORY (DECODE) Statement: (for RAM) [ADVANCED OPTION]

     Choices: 20 (Byte), 24 (Word)

     Default: 20

     How many DECODE lines are on the board?


                                    - 11 -




     5.10 ADDRESS Statement: (for ROM)

     Enter the ROM location from possible list below, paying attention to
     not cause a memory address conflict, or press ENTER if no ROM present:

     0C000 through FF000

     Default: NONE

     ROM location? (i.e. 0D000)?

       ADDRESS Statement (Optional)

       Syntax:
       ADDRESS = list

       The ADDRESS statement specifies the starting address of the
       READ ONLY memory on the card.

       NOTE: Make certain to proceed any address below 1MB with a 0 as shown
       in the example above. (i.e. if the address is D000 enter 0D000).
       
     ------------------------------------------------------------------------

     5.10.1 MEMORY Statement: (for ROM)

     Choices:  8K, 16K, 32K, 64K, 128K

     Default: 64K

     What is the ROM size?

       Syntax:
       MEMORY = length

       The length following the MEMORY statement specifies the maximum
       size of the ROM (in Kilobytes) installed on the board.

     ------------------------------------------------------------------------

     5.10.2 MEMORY (CACHED) Statement: (for ROM)

     Choices: (Y)es, (N)o

     Default: N

     Should the ROM be CACHED?

       This will set the 80486 CPU up so it will allow the address to be
       cached. This option can cause problems.  If you turn it on and start
       having problems with other hardware, or even programs, try turning it
       OFF and running it again.


                                    - 12 -




     5.10.3 MEMORY (TYPE) Statement: (for ROM) [ADVANCED OPTION]

     Choices: BYTE, WORD

     Default: BYTE

     What type is the ROM?

     ------------------------------------------------------------------------


     5.10.4 MEMORY (DECODE) Statement: (for ROM) [ADVANCED OPTION]

     Choices: 20 (Byte), 24 (Word)

     Default: 20

     How many DECODE lines does the ROM use?




































                                    - 13 -




     6. !ISA0001.CFG

     Below is a listing of the file created by EISACFG that will be used by
     your system vendor supplied EISA CONFIGURATOR program.


 
BOARD
  ID = "ISA0001"
  NAME = "Generic ISA board, Generated with EISACFG v.1.41"
  MFR = "TOKENRING (W/RPL ROM)"
  CATEGORY = "NET"
  SLOT = ISA16
  AMPERAGE =  650                        ;Max +5 VOLT current draw
  COMMENTS = "\n This is a GENERIC EISA CONFIG file to be used for ISA cards 
  where no .CFG file has been supplied by the card vendor.\n\n"

GROUP = "Generic ISA card setup"

FUNCTION = "Generic ISA card DMA Channel"
    COMMENTS = "Set generic ISA DMA Channel"
        CHOICE = "5"
           LINK
               DMA = 5
               SHARE = NO
               SIZE = WORD
               TIMING = DEFAULT

FUNCTION = "Generic ISA card IRQ setting"
    COMMENTS = "Set generic ISA IRQ setting"
        CHOICE = "10"
           LINK
               IRQ = 10
               SHARE = NO
               TRIGGER = EDGE

FUNCTION = "Generic ISA card PORT Address"
    COMMENTS = "Set generic ISA PORT Address"
        CHOICE = "A20H-A2FH"
           LINK
               PORT = A20H-A2FH
               SHARE = NO












                                    - 14 -




FUNCTION = "Generic ISA card RAM Address"
    COMMENTS = "Set generic ISA RAM ADDRESS"
        CHOICE = "0C8000H for 16K"
           LINK
               MEMORY = 16K
               ADDRESS = 0C8000H
               MEMTYPE = OTH
               WRITABLE = YES
               SHARE = YES
               CACHE = NO
               SIZE = BYTE
               DECODE = 20

FUNCTION = "Generic ISA card ROM Address"
    COMMENTS = "Set generic ISA ROM ADDRESS"
        CHOICE = "0D0000H for 32K"
           LINK
               MEMORY = 32K
               ADDRESS = 0D0000H
               MEMTYPE = OTH
               WRITABLE = NO
               SHARE = NO
               CACHE = NO

ENDGROUP





























                                    - 15 -




     7. Using !ISA0001.CFG

     After EISACFG has completed and generated the !ISA0001.CFG file you will
     need to place it where it is needed.  Most vendor supplied EISA
     CONFIGURATION programs will require the .CFG file to reside on the EISA
     CONFIGURATION Utility diskettes itself.

     Due to various EISA CONFIGURATION programs and even different version of
     the utility and the way they handle the moving/copying of a new .CFG file
     to the utility diskette, it is normally easier to just copy it using DOS
     directly to the diskette.


     8. Renaming !ISA0001.CFG

     If you wish to rename the .CFG file you will need to change the name
     within the !ISA0001.CFG and the filename also to match each other.

     With an ASCII edit, edit the !ISA0001.CFG and edit the line that looks
     like below:

         ID = "ISA0001"

     Edit the [ID = "ISA0001"] line to use the name you have selected, using
     the following Guidelines. The seven character ID consists of a three
     character manufacturer code, a three character hexadecimal product
     identifier, and a one character hexadecimal revision number.  For
     example, the forth revision of an expansion board manufactured by the
     DIAMOND Board company might have the ID DIA0104.

         ID = "DIA0104"

     After having made this change, rename the file to equal the name chosen
     and entered into the file.  Remember that the filename must be proceeded
     with an exclamation mark "!", i.e. !DIA0104.



















                                    - 16 -