Documentation for EGADUMP.COM
	
	
	Copyright 1989 Infinity Design Concepts Inc. All Rights Reserved
	1052 Parkway Drive
	Louisville, Kentucky 40217
	(502) 636-1234
	
	
	This program is a TSR (memory resident) utility that adds
	more capabilities to the DOS print screen functions. DOS
	by itself, will handle the text modes, but if the CGA graphics
	modes need to be dumped to the printer, then GRAPHICS.COM
	must be loaded. There is a severe limitation to GRAPHICS.COM's
	capabilites and that is, that it will not work on EGA graphics
	modes, that is the following modes;
	
		320x200 - 16 color	(mode d)
		640x200 - 16 color	(mode e)
		640x350 monochrome	(mode f)
		640x350 - 16 color	(mode 10)

	EGADUMP should be loaded AFTER graphics.com, since graphics.com
	will try to handle these modes if it gets control before
	EGADUMP. In order to be able to dump all screen modes to the
	printer, GRAPHICS.COM (or CGRAPHIC.COM) must be loaded
	in addition to EGADUMP.
	
	EGADUMP is set up to work with the IBM graphics printer, which
	means that if you have a printer that has an EPSON or IBM mode,
	EGADUMP will work with it. If your print screen works now in
	graphics mode, then it will work with EGADUMP.


	There are two printer strings used in EGADUMP;
	
		ESC,"L",n	- set up for double density graphics
		ESC,"3",n	- set to n/216" linefeeds
		

	Command line switches:
	
		The /I switch given when EGADUMP is loaded
		will cause black to be printed as black and white
		to be printed as white. The default for EGADUMP
		and GRAPHICS.COM is to reverse black and white
		when printing. The switch can be invoked as follows;
		
			EGADUMP /I
                
		The /F switch given when EGADUMP is loaded will
		cause a formfeed to be sent to the printer. The
		switch can be invoked as follows;
		
		        EGADUMP /F
			
                The switches /I or /F may be used in tandom and
		may be invoked as follows;
		
		        EGADUMP /I /F
					

	Technical:
	
		EGADUMP inserts itself into the Interrupt 5 (print screen)
		chain. When the print screen key is depressed,
		EGADUMP will get control (if it is loaded last) and
		determine which video mode is active. If it is
		one of the modes listed above, then EGADUMP will
		handle sending the screen to the printer. If it is not
		one of the above modes, then EGADUMP passes control
		back to the routine that would have been called, had
		EGADUMP not been loaded.