Asm68k	68000 Macro Assembler
				Version 1.0.1
				    Docs

			      Date:  20-Jan-87

===============================================================================

IMPORTANT:	This is the second beta release of this program. Correct
		object has been verified for correct source, and appears to
		operate well. Please send any bug reports to me promptly,
		either through MMS [(919) 779-6674] or Deep Thought,
		[(919) 471-6436], Compuserve [73277,260], the Mail or at my
		home address. Your help is greatly appreciated.

===============================================================================

				NOTICE:

	   THIS FILE AND THE PROGRAM IT DESCRIBES ARE COPYRIGHT © 1987,
	W. WESLEY HOWE. ALL RIGHTS RESERVED. A LICENSE FOR USE AND
	DISTRIBUTION WITHOUT PROFIT IS GRANTED TO POSSESSOR OF THIS FILE,
	PROVIDED DISTRIBUTION INCLUDES THE PROGRAM AND THIS FILE. NO
	RIGHT OF ALTERATION OF THE PROGRAM OR DOCUMENTATION IS CONVEYED
	WITH THIS LICENSE.

	   NO WARRANTY IS EXPRESSED OR IMPLIED HEREIN ON THE SUITABILITY
	OF THIS PROGRAM FOR ANY PURPOSE AT ALL. YOU MUST RELY ON YOUR OWN
	JUDGEMENT AS TO WHETHER THIS PROGRAM WILL OPERATE PROPERLY WITH
	YOUR COMPUTER FOR WHATEVER PURPOSE YOU MAY DESIRE TO USE IT FOR.

	   ADDRESS ALL QUESTIONS, COMMENTS OR CRITICISM TO:

				W. WESLEY HOWE
			       4800 LAKEMONT DR.
			      RALEIGH,  NC  27609


=============================================================================

				LIMITS:

	Source-line length:	    255 bytes (including newline)
	Sub-expression length:	     40 bytes
	Parenthesis nesting:	     16 levels
	Symbol length:		     31 bytes
	Macro Size:		  8,190 bytes
	Number of Macros:	        Available RAM
	Number of Symbols:	        Available RAM
	Available RAM:		270,336 bytes maximum heap utilized
	Macro Nesting:		      8 levels
	Include Nesting:	      8 levels
	Conditional Nesting:	     16 levels
	Macro Parameters:	     10 per invocation
	Sections:		    255 maximum
	Program size:		 91,364 bytes (loaded)
	Minimum free heap:	 26,796 bytes
	Total RAM necessary:	118,160 bytes
	Constant size:		    255 bytes
	Storage size:		 65,535 bytes
	Strings:		    255 bytes (or line length limit)
	Minimum stack:		  8,192 (recommended)
	Operating System:	 V. 1.2 Workbench (CLI Only ) (Release)

==============================================================================

   If you are an experienced 68000 Assembly language programmer, you will find
much of this material useful in understanding assembly language programming
on the AMIGA. If you are an experienced AMIGA assembly language programmer,
you may find much of the material boring, and will only want to use this as
a reference document. If you don't know assembly language, then this document
will not teach it, so you may need to buy (What? spend MONEY?) one of a number
of reference books on MC68000 assembly language programming that are available.

   In the following sections, Directives, Commands, Expressions and
Mnemonics are referred to. A Directive or Command is an instruction to
the assembler which causes a specific action to be performed. Some of these
add data to the object file, and some only affect the way assembly operations
are performed. A Mnemonic is the Pseudo-English abbreviation for an in-
struction the assembler is to translate into the appropriate numeric sequence
and include in the object file for the MC68000 processor to perform later,
when your program is run. An expression refers to any sequence of items
consisting of numbers, symbols with a numerical value, and the allowable math
operators which can be reduced to a single number value.

==============================================================================

			Math & Logic Operators:

	 +	Addition

	 -	Subtraction or Negation

	 ~	Bit-wise NOT

	<<	Bit-wise left shift

	>>	Bit-wise right shift

	 &	Bit-wise AND

	 |	Bit-wise OR
	 !	Bit-wise OR  (for compatability)

	 ^	Bit-wise XOR (Exclusive OR)

	 /	Integer Division

	%%	Integer Modulo (Remainder)

	 *	Integer Multiplication or
		Current Program Counter Location


   Like the Rotomola assembler, all expressions evaluate in strict Left-to-
Right order, as divided by parentheses. The Unary operators '-' and '~' need
to be offset from any adjacent operators with parentheses. Symbols and
constants may be mixed, and space or tab characters may be included. No
individual portion of the expression may exceed 40 characters (NOTE: a
'portion' would be any symbol or number alone.)

Some examples:		4+(7*2)			Yields  56
			4 + ( 7 * 2 )		Yields  56
			4+7*2			Yields  22
			-4*6			Yields -24
			6*-4			Error
			4(6*7)			Error
			('A'+1)			Yields  66
			"A" + 1			Yields 194
			'ASDF'+0		Error

===============================================================================

			Numbers and Constants:

	Binary:		A binary number is either [1] prefixed with the '%'
			(percent) character, or [2] followed immediately with
			the letter 'B' (UPPER or lower case). It may contain
			only the digits '1' or '0'.

	Octal:		An octal number is either [1] prefixed with the '@'
			(at) character, or [2] followed immediately with either
			the letter 'O' or the letter 'Q', in either case.
			Only the digits '0' through '7' are valid.

	Decimal:	A decimal number contains only the digits '0' through
			'9', and may be optionally followed immediately with
			the letter 'D' (either case.)

	Hexa-Decimal:	HexaDecimal numbers contain the digits '0' through '9',
			and the letters 'A' through 'F' (in either UPPER or
			lower case.) They may be [1] prefixed with the '$'
			(Dollar) character, or [2] they must start with a digit
			and be followed immediately with either the letter 'Q'
			or the letter 'X', in either UPPER or lower case. A
			leading '0' may be prefixed for the post-fix form.

   Leading zeros do not affect the value of any of the number forms, although
the 40 character limit applies to them also.

	Characters:	An INDIVIDUAL ascii character may be included by
			enclosing it in QUOTES. The single quote will yield
			the ascii value, and the double quote will yield the
			ascii value with bit 7 SET (or'd with 128). Multiple
			byte constants are not evaluated in this version.

Some Examples:	The number 1,000 (one thousand) may be represented
		any one of the following ways:

		1111101000B	01111101000b	%1111101000
		1750Q		01750o		@1750
		1000D		0001000d	1000
		3e8H		03E8h		$3e8

==============================================================================

			Assembly Line Format:

   An input assembly line follows the following models:

Label	Mnemonic	Operand , MoreOperands ;comment
 Label:	Mnemonic	Operand			Comment
	Mnemonic	Operand
Label:	Mnemonic
* a comment only

   Note that the LABEL either starts in the first column, or is followed by
a colon. The Mnemonic field is separated by at least one space or tab, and
never starts in the first column. Operands, where needed, follow, separated
from the Mnemonic by at least one space or tab. Multiple operands are
separated from each other by a comma (the comma flags the assembler that
there is another operand available.) An asterisk in the first position on the
line indicates a comment only line, or comments may follow complete operands
with a space or semicolon separator. Assembler directives occupy the Mnemonic
position, and comments are optional. Labels are allowed on all lines, and are
required for some assembler directives.

==============================================================================

				Constants:

   The following Assembler directives cause the inclusion of data in the
Object file:

	DB	Yields 8-bit values. Either STRINGS, Symbols, Labels, numbers
		or expressions may be evaluated. Multiple operands need to be
		separated by commas, and generate successive bytes up to
		a limit of 255 bytes (the line-length limit should prevent
		this from ever being reached.)

	DW	Yields 16-bit values, in Hi-Lo order. The format is the same
		as the DB directive, except STRINGS will not be evaluated.
		If the address is not a word address, a pad byte will be
		appended to the previous line, and a non-fatal error message
		will be issued.

	DL	Yields 32-Bit values. Otherwise equivalent to DW.

	DC	This directive is the same as DW. Appending .L or .B (in
		either case) will change the function to be the same as
		DL or DB, respectively.

	ASCII	This command yields a sequence of bytes equivalent to the
		ascii value of the operands (delimited by quotes) provided.
		Single quotes will yield the normal value, and double quotes
		will yield values with bit 7 SET. Within the delimited
		STRING, a '\' (backslash) character, followed by up to three
		decimal digits will cause inclusion of a byte with the same
		numerical value, or if followed by any other character will
		allow the inclusion of that character immediately following.
		(This is useful for including quotes and backslashes in the
		string.) A limit of 255 values applies.

	CSTRING	This command is the same as ASCII, except an additional byte
		with the value 0 is appended (as in the C language.)

	PSTRING	This is the same as ASCII also, except a leading byte with
		a value equal to the number of bytes following is prepended
		(as used in the PASCAL language).

	ISTRING This variant of ASCII will cause the final character to have
		it's most significant bit of the opposite (INVERTED) value
		from the rest of the characters in the string (as defined by
		the delimiting quotes). This form is popular among 8-bit
		machines, and some BASIC interpreters. It's usefulness with
		the new international 8-bit standard ASCII is questionable,
		but it may be helpful, so it hasbeen included anyway.

	DCB	This command accepts the .B .W and .L size specifiers (or
		defaults to WORD.) It generates as many values as the operand
		expression evaluates to (up to 255 bytes total), of the size
		specified. WORD and LONG sizes are forced to an even address
		alignment.

==============================================================================

			Symbol and Labels:

   A Label is an address designator. It is placed before a mnemonic or a
data location, and acquires a value equal to the relative program counter
value at that location. A standard Label may only be defined this way once
in a program, but may be referenced as many times as needed. It must start
with a letter, a period or the '_' (underscore) character, and may contain
only these characters, or the digits '0' through '9', without spaces up to
a total of 31 characters. When you define a label, it must appear as the
very first item on a line, or you must append a ':' (colon) character to it.
(You may have the colon in the first case also.) You must not use the colon
on the label other than when you define it, or you may get an erroneous
interpretation of your expression.

   A Symbol starts off looking like a label, and follows the same rules, except
the following commands modify it to acquire a new type and value:

	EQUATE	Sets a permanent, absolute value equal to the value of the
		expression following this directive. STRING values are not
		allowed.

	SETVAL	Sets an absolute value which is retained until a new value is
		set. You may not later use EQUATE on this label, but you can
		EQUATE a different label to the set value.

	EQUR	Gives a value to the symbol which may later be used in place
		of a standard data or address register. This is valid only
		for D0-D7 or A0-A7 (SP is a synonym for A7). You cannot use
		this value other than to reference a register in a MC68000
		mnemonic.

	REG	Accepts a register-list operand for use with the MOVEM
		mnemonic. A register-list looks like this:

			A2-A7/D1/D3-D7

		Which defines the registers A2 through A7, D1 and D3 through
		D7. In fact, all the registers except A0, A1, D0 and D2. Only
		the standard address and data registers may be defined in this
		fashion.

	MACRO	Assigns a sequence of input lines, with replacable parameters,
		which will later be substituted for any line which uses this
		symbol as a mnemonic or command. More on Macros later.

	These Directives must have a Label in the Label Field for assignment.

   You must avoid referencing a symbol before giving it a value, or the 
assembler will complain (sometimes), because the forward reference will make
it type the symbol as a label, which is an address, not a number. Labels, of
course, may be referenced before use, and it's value will be substituted on
the second pass. In fact, this is the only reason you need a two-pass
assembler.

=============================================================================

			Local (Numeric) Labels:

   A line may be labeled with a special Local Label which attaches itself to
a specific offset from the last proper line label, as previously described.
A Local Label is a sequence of up to three decimal digits followed by the
'$' (Dollar) character. Like a regular Label, if it does not start at the
beginning of the line, it must be followed by a colon.

   A Local Label may be referenced in an operand anywhere a line Label would,
but it's scope is only between one regular Label and the next. Each time a
new regular Label is used, the Local Label may then be redefined and reused
with a different value.

   An example:

Start	Jsr	Initialize_Data
001$	Jsr	Initialize_Serial
	Move.b	D1,ChangeFlag
	Cmp.b	#0ffh,D1
	Bne	1$

   Note that 001$ and 1$ will evaluate to the same location. You need not
start with one and may use any numbers you desire, as long as their value
does not exceed 999. Also, note that $1 and 1$ are interpreted differently;
the first is an absolute expression, and the second is a relative address.
Local Labels may not be used for Macro names, although they may be used
within Macros, and cannot be used to represent Numbers, EXTERNal or ENTRY
types.

==============================================================================

		   Conditional Assembly Directives:

   The following Commands allow assembly to proceed until a matching ENDIF
Directive is found, or disable assembly until the ENDIF is reached if the
condition is not met:

	IFEQ	Expression EQuals zero. (e.g. 4-4)
	IFGE	Expression Greater than or Equal to zero. (e.g. 4-4 or 4-3)
	IFGT	Expression Greater Than zero. (e.g. 4-3)
	IFLE	Expression Less than or Equal to zero. (e.g. 4-4 or 4-5)
	IFLT	Expression Less Than zero. (e.g. 4-5)
	IFNE	Expression is Not Equal to zero. (e.g. 4-5 or 4-3)

   The above conditionals are evaluated to 32 bits, but the condition decision
is based on their WORD (16-bit) value.

	IFD	Label following was already Defined (not just referenced.)
	IFND	Label following has Not yet been Defined.

	IFC	Both STRINGS following Compare (same length and characters.)
	IFNC	Both STRINGS do Not Compare (different length or characters.)

   The last two conditional commands need two operands, separated by a comma.
They may be delimited with Quotes (single or double), or by a left bracket
'<' and right bracket '>' pair, or the first string will start at the first
character which is not a space or a tab, and end at the first occurrence of a
comma or space or tab, and the second will start at the next character which
is not a comma or a space or a tab and will end at the first space, tab, semi-
colon or newline character. To enclose spaces in the string, you must use
either the quote or bracket delimiters. To enclose quotes, use the brackets,
and to enclose brackets, use the quotes. Both quotes and brackets cannot be
passed together unless you use the spaces, but then you can't have spaces in
the string. Just shows to go you, everything is a compromise. Any backslash
characters are not expanded before comparison.

   Each Conditional command DO level ends with an ENDIF command. DO levels
nest only to 16 levels, or a fatal error will be generated (whether the
assembly is on or off, each IFxx increases the level count, and each ENDIF
decreases the count; exceeding 16 or going below zero are fatal errors.) DO
levels are not active during a macro definition, but will be evaluated during
a macro expansion.

==============================================================================

			Other Assembler Directives:

	RESERVE	Creates an uninitialized data storage area, with a size equal
		to the expression following it. The size designators .B .W and
		.L (any case) may be used, or WORD is assumed. The expression
		following the Directive is expanded to the size specifier.
		This is the only Directive which is not limited in size to 255
		bytes for the result, but may yield up to 65,535 bytes.

	ENDSRC	Shuts off assembly for the current DO level. (See the section
		on conditional assembly for DO level explanation.) If you
		are not in a DO level, the source is read to the end of
		file, but no assembly action will occur.

	OPTION	This command accepts the following operands only:

			 M - Allows macro call lines to print in the
			     assembly listing. (If List is on.) This
			     is the default condition.

			NM - Hides macro call lines, showing expansion
			     lines only.

			 L - Turns on listing. (The default condition).

			NL - Shuts off Listing.

		(Neither of these commands override the command-line
		switches directly, they only control the flow of data.
		An assembly will still create a list file if not prohibited,
		Option NL will just make it an empty file. If the list
		file was disabled on the command line, Option L will
		not send the listing anywhere. None of the operands are
		case-sensitive.)

	TITLE	Accepts a STRING (delimited by quotes) which will label all
		pages, if paging is not disabled. The Maximum title length
		is 40 characters. Also cause pages to be numbered.

	ORIGIN	Sets the program counter to the value of the expression
		following the command. Origin remains relative on AMIGA
		output format.

	PAGEUP	Causes a page to end if paging is not disabled. A form-feed
		character is sent, and a page heading with the optional
		title (see TITLE) is printed.

	SECTION	this command causes a new section, or Hunk, to be created
		in the AMIGA output format. The first operand must be a
		name containing no spaces and having less than 40 total
		characters. The second operand, if given, should be
		separated by a comma and should be either CODE, DATA or
		BSS. If none is given, CODE is assumed. (only the first
		character is checked, however, so DUMMY will yield a
		DATA section definition.) Case is not significant on the
		section type, but case is important for the name. If the
		section name has been used before, assembly will proceed
		at the next location as was previously defined, and the
		resultant code, data or storage space will be coalesced into
		one Hunk. See the AmigaDOS manual for more information
		on Hunks.

	IDENTIFY   This command should be followed with a name, which will
		be given to the program unit (a program unit is a hunk or a
		collection of hunks to be fed to the linker.) Only the first
		name given will be used, subsequent uses are ignored. If the
		IDENTIFY command is not used during an assembly, the object
		file will be given a name that has 0 characters in it. (Null
		string.)

	EXTERN	Followed by one or more Labels or symbols (separated by commas.)
		These labels must not be defined within the  entire assembly
		source, and cause the assembler to generate the appropriate
		external reference instructions in the object file (AMIGA
		format only) for resolution by the linker.

	ENTRY	Followed by one or more Labels or Symbols. These labels, which
		need to be defined somewhere, allow locations within the
		program unit to be visible to the linker to resolve other
		program unit EXTERNal references. A program that consists of
		more than one object file will need to have an ENTRY in one
		unit for every EXTERN in the other units, or the program will
		'BOMB' and probably either lock-up the machine or cause the
		dreaded GURU to appear. References between different sections
		must be to ENTRY labels, since the AMIGA loader will place
		each section wherever it will fit, and resolve all these
		different addresses. If you never use the section command,
		the entire program will have to fit in the same place, and
		might not be able to be loaded if there is not a spot big
		enough for the whole thing (depending on how many tasks might
		also be running, etc.)

	EXECUTE	This command will pass the quote delimited string following
		it to AmigaDOS during the second pass. The current window
		is the input and output. A more detailed description of the
		Execute routine is located in the AmigaDOS manual, but
		basically the same things you can do from the CLI may be
		contained within the string and executed from within the
		assembler. The Source, Object and any open Include files
		will be locked, and cannot be accessed at this time. No
		use is made of the return value from the program called.
		This is your hook, let me have some ideas for any uses
		for it (hint: the Macro functions allow some very powerful
		uses, and any valid AmigaDOS device may be used for Source,
		Include and Object file-handles.)

	CNOP	This Directive causes null filler bytes to be inserted
		into the object file until the desired alignment is
		reached. There should be two values after the Directive,
		separated a comma. The second value given is the desired
		alignment value you want, and the first value is how
		many more to add beyond this point. There may not be more
		than 255 bytes generated in total to acheive the desired
		alignment, and no restrictions are imposed on what alignment
		values can be used. If you want to set the Program Counter
		5 bytes beyond the next PC location evenly divisible
		by 7 use the command like this:

			CNOP	5,7

		The predominant reason for using this command would be to
		align data at specific offsets, and to create data structures
		in specific formats.

===============================================================================

			Include Files:

   Up to 8 levels of include files may be inserted into the assembly with the
INCLUDE Directive. The syntax demands a Filename or Path, delimited by quotes.
Include file directory searches are supported by command-line parameters (De-
tailed in another section.) Include files may be called by Macros, and Macros
may be used by Include files, up to their respective nesting levels (8 each.)
The INCLUDE directive will cause the next source line to be read from the
named file as if the entire contents appeared in the original source file,
except line numbering will start at one again, and the line number will be
followed by a '+' (plus) sign. When the end of the Include file is reached,
the line number will revert to the one following the line which invoked the
INCLUDE Command.

   Special provisions have been made to allow automatic and command-line
inclusion of header and/or macro definition files before assembly starts,
and these files do not count in the nesting level limits for Include files.
A later section will describe command-line parameters and the configuration
file.

A SPECIAL NOTE: Several of the existing include files from Commodore do not
		Assemble correctly (particularly those in the exec directory.)
		Many of the source lines in these files contain comments
		which are delimited only by spaces and an asterisk. Asm68k
		is not restrictive about spaces within an expression, and
		tries to assemble the asterisk as a multiplication operator
		with the words in the comment being looked at as labels, and
		gives appropriate error messages. Make sure the comments are
		stripped or delimited by a semi-colon (as per the MOTOROLA
		spec.) A few of the files contain Macro error checks using
		an IFC \1,'' which will not assemble correctly with Asm68k.
		Use IFEQ NARG instead. the FUNCDEF file contains an expression
		4*-6, which will not be interpreted correctly as written.
		Change this one to 4*(-6). These changes will make both
		assemblers happy, and the include files more portable between
		applications.

===============================================================================

			 Macros:	

   The best feature of the assembler, and the hardest one to master, is the
use of the MACRO command. A Macro is simply a sequence of source lines which
may be saved and inserted as often as wanted just by using the name you gave
it as a command. A Macro may contain any of the other Directives and Mnemonics
the assembler recognizes except another MACRO definition command, although
you may use the name of a defined Macro in your Macro (up to 8 levels deep.)

   A Macro is defined (and it must be before being used) by placing the
MACRO in the Mnemonic Field, either before or after it's name. The name for
the Macro must follow the rules for Labels if it is on the left side, or if
it is on the right side it needs to be separated by at least one space or
tab from the MACRO Directive, and follow all the Label rules except it does
not need to be followed by a colon. All the subsequent lines up to the one
which contains the ENDMAC command will be saved for subsequent use.

   The real power of Macros comes from their use with replacable parameters.
When you issue a Macro name as a Command, up to ten parameters (numbered
from one to nine, with zero for ten) may be included in a comma, space or
bracket separated list after the name for use within the Macro text. To make
these parameters appear in the Macro expansion, place a '\' (backslash)
character followed immediately (no spaces) with the digit of the parameter you
want in the definition. When the macro is expanded, the text will include the
parameter placed on the calling line, and will be evaluated just as if the
source had included it as it appears. The parameters are gathered under the
same rules as the IFC and IFNC commands (bracket, quote or space delimiters.)

   The backslash character may be passed to the Macro by including two
backslashes in the calling line, and any non-numeric character following
a backslash other than a backslash will pass both the backslash and the
character following it to the Macro.

   Conditional Directives are effective within the Macro, under the same rules
as they follow elsewhere. If assembly is enabled, and the Directive MEXIT is
encountered, expansion of the Macro is suspended, and the next source line
will be the one following the Macro invocation line, after the assembler has
examined the remaining Macro text and resolved all the IFxx and ENDIF levels.

   To make Macros respond differently with different numbers of passed para-
meters, the special symbol NARG (not case-sensitive) has been reserved. It will
yield a value equal to the number of parameters found on the invocation line
within a Macro expansion, and zero elsewhere.

   One additional feature within Macros is the \@ (backslash followed by the
at character). While the Macro is being expanded, this combination is changed
to a period followed by three decimal digits. These digits increment starting
from zero every other time the \@ combination is expanded. This allows pairs
of unique symbol names to be generated within the Macro text, allowing branch
instructions to occur. Local (numeric) Labels are effective within the Macro,
but they do not attach to the Macro name, nor are they canceled by the Macro
invocation (unless the invocation line was labeled.)

==============================================================================

			Do Nothing Directives:

   The following directives are accepted by the assembler, but cause no action
and generate no code, just as if they were comments. They have been included
to allow use of source code written for other assemblers.

	MASK2		FORMAT		SPC		
	NOL		OFFSET


			Synonym Directives:

   The directives in the left column are substitute names for the directives
in the right column, and were included for source compatability:

		DS		RESERVE

		END		ENDSRC

		EQU		EQUATE

		SET		SETVAL

		TTL		TITLE

		ENDC		ENDIF

		ENDM		ENDMAC

		RORG		ORIGIN

		XDEF		EXTERN

		XREF		ENTRY

		RORIGIN		ORIGIN

===============================================================================

			Unimplemented Directives:

   The following Directives, found in some other assemblers, have not been
implemented in this version:

	IDNT		FAIL		LIST
	LLEN		PAGE		PLEN
	NOOBJ		NOLIST		NOPAGE

   A startup Macro file has been included with this package to allow some
compatability if these are needed.

===============================================================================

			Startup Configuration:

   If a file named Asm68k.cnf is found in the current directory, it is read
and acted on. The current version only looks for two items in this file,
the pagelength (which must be greater than 11) and the name of the startup
file. The format is:

	Page Length:	1 byte (11-255), binary
	File Path:	up to 31 bytes, ascii
	Terminator:	1 byte, binary, value 0

   Any remaining characters after the null byte are ignored. The assembler
next looks for the filename or path given, and if this file is found, it
is read and assembled as if it was the beginning of the Source file. All
lines from this file are numbered 0, and no warning or error occurs if the
file is not found (unless, of course, you were depending on these definitions
in your program, then you could have lots of error messages.)

   Beware when building this file that the null character must be at the end of
the pathname or you may crash the system. You can create a file from the
keyboard using the command:

		COPY con: to Asm68k.cnf

then typing a character for the pagelength (B is 66, the standard), following
it with the pathname for the startup file, followed with a control@ (CTRL key
and 2 key together), then ending it with a control\ (CTRL and \ keys together.)
If you make a mistake, you cannot edit the file, so do the control\ and start
over.

===============================================================================

			Invoking the Assembler:

   The assembler is only designed to be run from the CLI interface. If you
don't know how to find the CLI interface, read the manuals that came with
the machine before trying to use this program.

   The minimum invocation must be the program name Asm68k followed with a
source filename (separated by at least one space from the program name.)
This will yield an assembly, with an object file output in the AMIGA format,
and a listing file. The filenames for these files will be created by
stripping any extension (period followed by characters) from the source
filename and appending .o for the object filename and .lst for the listing
filename. Any error messages will list to the screen.

   Example:

		Asm68k MyProgram.a

   Outputs:

		MyProgram.o	(The relocatable binary object file)
		MyProgram.lst	(A combined source and hex object file)

   If this isn't what you want, a wide variety of "switches" are supported
to control the usage of the assembler, and the descriptions follow:

   (A switch is a parameter you type after the program name and source
filename, with an intervening space. These switches all start with the
minus sign '-' and may be followed immediately by a letter or letters as
shown below.)

	-O	Causes the OBJECT file to be generated (this is a default
		value.) It may be followed immediately with a filename
		containing no spaces, or type a space and then enclose the
		filename in double quotes if it contains spaces. You may also
		use the intervening space without quotes on a filename without
		spaces if you like. A given object filename will be used
		instead of the default filename normally used.

	-L	Causes the LISTING file to be generated (also a default.) The
		usage is just like the -O switch.

	-E	Causes ERROR messages to list to the named file. Use like
		above. On this switch, if no filename is given, a default
		filename will be formed like the object and listing names,
		using the extension .err

	-V	VERIFICATION file. Another name for the -E switch.

	-H	HEADER file. Causes a search for the filename given after the
		switch (as above) which will be read as a source file before
		the source file is read (but after the initialization file, if
		enabled.) Just like the initialization file, if the file is not
		found, no warning or error is issued directly. All the source
		from this file will also be numbered as line 0.

	-I	An INCLUDE directory search path list should follow this switch
		and should contain directory names (no spaces allowed) separated
		from each other with plus signs '+', commas or spaces. If
		spaces are used, then you must space the list off from the
		switch and enclose the entire list in double quotes. Use of
		this switch will cause the assembler to search for an INCLUDE
		file in each of the named directories if it is not found in
		the current one.

	-X	This switch should be followed immediately with up to 6
		characters, and will cause the default object filename to be
		formed by stripping the extension and appending a period and
		the characters following the X.

	-C	This switch has been included for compatability. It should
		be followed with only the following characters, as many as
		wanted, with no spaces:

			S	Generates a symbol table at the end of the
				list file (this is a default value.)

			D	Does nothing.

			C	Causes Case of all Labels and symbols to
				be ignored. With this switch activated,
				LABEL, Label and label will all be interpreted
				as the same name. This is not the default.

			X	Does nothing.

	-N	This switch turns things off (NO.) Like -C, you should follow
		it with a series of letters from the following list, without
		any spaces:

			S	Turns off the SYMBOL table normally produced
				at the end of the listing file.

			L	Stops the LISTING file from being generated.

			E	Inhibits the ERROR file, if you turned it on.

			V	A synonym for the E switch above.

			P	Inhibits the PAGINATION of the listing file.

			O	Inhibits the OBJECT file generation.

			Q	Inhibits the conversion of mnemonics to QUICK
				form. The default is to convert allowable
				values of ADD and SUB to the quick form if it
				is safe (values already defined.)

			X	Keeps the assembler from stripping the eXten-
				sion from the source filename when forming
				default filenames.

			R	Causes the assembler to generate the object
				code in a non-RELATIVE format. The format
				used is the Intel format, and the program
				counter is only output to 16-bits of
				significance. No symbol or relocation infor-
				mation is output, and no linker or loader
				is available to operate on this format.

	>	The right bracket, followed immediately with a filename, will
		cause the signon, progress and all error messages to be
		diverted by AmigaDOS to the named file when it is the first
		parameter after the program name. If it is not the first,
		the assembler will send the error messages to the named file.

   All the above switches may be used in either UPPER or lower case, and will
generate the same results. The source filename should be the first parameter
after the program name, but only to avoid confusion. It must be the only
parameter not associated with a switch, and may not be given twice. The source
filename is the only mandantory command-line parameter.

==============================================================================

			Other notes on use:

   Case is normally significant on Symbols, Labels and Macro names unless the
-CC switch is used. The Directives, Mnemonics and special symbols will be
recognized in any mixture of UPPER and lower case.

   The only truly reserved symbols are the following:

		NARG	MACRO	ENDMAC	ENDM	A0
		A1	A2	A3	A4	A5
		A6	A7	D0	D1	D2
		D3	D4	D5	D6	D7
		SP	CCR	USP	SR	PC

   All the other special Symbols, Mnemonics and Directive names  may be defined
and used as Labels, or may be implemented as Macros, but be careful when doing
this to avoid circular references, which will not be detected until the Macro
nesting level is exceeded, or a write error results from the disk being full.

   For example, if you redefine JSR as a Macro, and want to use it in the
Macro definition, don't call the assembler with the -CC switch, and be sure
to use a different case within the Macro text to get the assembler to recog-
nize the Mnemonic, which is case-insensitive, from the Macro name. This allows
the maximum flexibility for the assembler, with only a minimum of care from
the programmer.

==============================================================================

			Error Messages:

   The assembler uses as much logic as possible to generate a line of code
in spite of erroneous input. If a reliable evaluation can be made, a source
line will be interpreted regardless of errors, however some of these lines
may not be what you meant. Even the little bit of DWIM in this assembler
occupies a lot of code space. Because assembly of erroneous lines is attempted
where possible, you may find multiple error messages referring to the same
line. The listing file will only contain the first error detected, however the
screen list or error file will also list the errors in the order they were
detected. Some errors may generate errors later, especially if typing errors
cause the assembler to find an item it thinks is an undefined symbol in an
expression, and you later used this symbol for another purpose. The following
is a list of error messages, and explanations:

	  1: Error in Expression Value

		The expression being evaluated contained some garbage.

	  2: Duplicate Line Label

		An attempt at defining a Label twice was detected.

	  3: Undefined Label in Expression

		The symbol or label used in the expression was not defined
		anywhere in the source file.

	  4: Syntax Error

		The assembler could make no sense of what you were trying to
		tell it to do.

	  5: Operand Too Large

		The operand was greater than the value allowed for the
		operation being performed.

	  6: Invalid Register Specified

		The register called for in the current operation and what
		was found are not compatable.

	  7: Undefined Mnemonic or Command

		An item in the Mnemonic field is not a defined Macro or
		valid mnemonic or directive. May also be caused by using
		a label outside of column one without a colon following it.

	  8: Improper use of Unary Operator

		A Unary operator ('-' or '~') was found right after another
		math operator. The expression evaluator cannot handle this,
		so it is ignored and this message is output.

	  9: Operation Involves Division by Zero
		
		A Division or Modulo operation was attempted where the right
		hand value was zero or undefined. The result of this operation
		is set to zero.

	 10: Too Many Right Parentheses

		More right parentheses were found than left parentheses.

	 11: Missing Right Parenthesis

		More left parentheses were used than right parentheses.

	 12: Too Many Parenthesis Levels

		More than 16 levels of parentheses were attempted to
		be opened.

	 13: Invalid Character in Expression

		A character was found in the expression that is not
		any of the defined mathops, numbers, symbol characters
		or newline characters.

	 14: Closing Quote for Character Constant Absent

		No closing quote on a single character constant was found.
		Also caused by attempts to define multiple-character
		constants in an expression.

	 15: Operand Field Missing

		An operand was needed, and was not there.

	 16: Bit Operand Required

		The expression needs a bit operand, and what was found was
		not of the required type.

	 17: Invalid Bit Specified

		The data found cannot be used legally to specify a bit.

	 18: Immediate (#) Operand Needed

		The data given was not preceded by the '#' (pound) sign,
		and needed to be.

	 19: Branch or Jump Out-of-Range

		The address evaluated is outside of the range allowable for
		the branch of jump mnemonic specified.

	  ** Run from CLI Interface **

		The message output when no command-line was used (as from
		the workbench. A Fatal error.

	  ** Command Line Required **

		The message output when no arguments are present on the
		command-line (you need at least the source filename.)
		Also a Fatal error.

	  ** Unrecognized Switch **

		A switch or a character within a switch was not one of
		the valid switches. Not a Fatal error.

	  ** File Write Error **

		An error occurred during a file write, as reported from
		AmigaDOS. A Fatal error. May be caused by a full disk.

	  ** Source Filename Missing **

		The source filename was not present or was corrupt or was
		given twice. A Fatal error.

	  ** Parameter Too Long **

		An Item on the command-line was too long to be evaluated.
		Also Fatal.

	  ** Insufficient Free Memory **

		This error occurs when the memory pool does not contain
		enough memory in a size large enough for the request
		from the assembler to be filled. Execution stops
		immediately.

	  ** Include Files nested too deep **

		This error occurs when you try to open the ninth Include
		file before closing one.

	  ** Couldn't open Source file **

		AmigaDOS did not return information indicating that the source
		file was ready to be read from (or it isn't there.) No
		assembly will take place without a source file.

	  ** Error Closing Source file **

		Another error was reported when the source file was being 
		closed.

	  ** Couldn't open Object file **

		A Dos error occurred trying to open the object file.

	  ** Couldn't open Listing file **

		Same error from listing file open attempt.

	  ** Couldn't open Error listing file **

		Like above, but on error file attempt.

	  ** ENDMAC Command missing **

		The end of the source file was reached, and the assembler
		was still saving a macro definition.

	 34: Too Many Parameters present

		More parameters than the assembler has space to store
		were found.

	 35: Parameter Too Long

		An item in an expression or an operand was longer than the
		defined limit.

	 36: Closing Single-Quote Missing

		A string definition should be bounded on both ends with
		matching quotes.

	 37: No Label on Line

		No label was present for the Directive to act upon.

	 38: Macro called using Symbol label

		A symbol name found in the mnemonic field was attempted
		to be used as a Macro, and was found to be a Label.

	  ** Too many nested Macros **

		This Fatal error occurs when the ninth Macro call is
		issued before any of the previous Macro calls have ended.

	 40: Macro redefinition Error

		The name used with the MACRO command is already the name
		of a previously defined Macro.

	 41: ENDMAC command without MACRO definition

		You didn't use the MACRO command to define your Macro, or
		you issued the ENDMAC command twice. If you are attempting
		to get two or more exit points from a macro, use the
		MEXIT Directive.

	  ** INCLUDE file unable to be opened **

		This Error occurs when the filename associated with the
		INCLUDE command was not found after the include directory
		list was exhausted.

	  ** Source or Include file line too long **

		An input line read from disk contained more than 255
		characters in a row without a carriage return or
		linefeed.

	 44: Insufficient Macro parameters supplied

		An expansion was attempted and there were not enough
		parameters on the Macro call line.

	 45: Label Value changed between passes

		This unusual error occurs when the value of a Line Label
		is different on the second pass than it was on the first
		pass. The whole assembly file is probably corrupt, and
		it is likely that the message will repeat with every
		subsequent Line Label found. Forward references and
		absolute references to SETVAL Labels, or conditional
		compilation based on SETVAL Labels are the likely
		culprits behind this error.

	 46: Invalid Label - Item was Forward Referenced

		A Label which was referenced before it was used was later
		found in a context other than usage as a relative
		location.

	 47: Local Definition of External Symbol not allowed

		If you declared a Symbol to be EXTERNal, you cannot define
		it within the current assembly. Use the ENTRY Directive
		instead if this is what you want.

	 48: Unavailable Addressing Mode Used

		The addressing mode used for the Mnemonic on this
		line is not one which is allowable for that
		Mnemonic.

	 49: Invalid Item in External Reference Expression

		An external reference included an item which did not
		belong there. This also occurs on an attempt to
		generate PC relative references to external addresses.

	  ** Too Many Section Definitions (Limit = 255) **

		The message is self-explanatory.

	 51: Invalid Section Type - Section CODE used

		An item found after the section name was not one of the
		three valid section types - CODE, DATA or BSS. The
		type was set to CODE.

	 52: Instruction Alignment Error - Pad Byte Added

		All the 68000 Mnemonics and WORD and LONG oriented
		Directives need to be aligned on an even address. The
		Assembler attempts to correct this by adding a null
		byte to the previous instruction, and adjust the
		Program Counter and Label values accordingly.

	  ** Too Many Conditional Levels Attempted

		The seventeenth conditional Directive was found before an
		ENDIF Directive was.

	  ** Conditional End without Conditional Statement

		There are more ENDIF commands than matching conditional
		Directives.

	 55: Relative Reference Outside of Current Section

		An attempt to use a PC relative mode to a Line Label that
		was not declared as an ENTRY label was attempted. Also
		occurs on Data references to other sections without
		using the ENTRY type-definition.

	 56: Executable Code not allowed in Data & Bss Sections

		DATA sections may contain only initialized and uninitialized
		data locations, and BSS sections may contain only un-
		initialized (RESERVE) data.

	 57: Redefinition of Equate Label not Allowed

		You cannot change the value of a Label that has been EQUATEd.

	 58: Equate to previously SET Label Disallowed

		A Label that was set cannot later be upgraded to an equate
		in the same assembly. The assembler handles decisions on
		equated labels, whose value cannot change, differently
		than set labels, whose value may be redefined. Since the
		length of 68000 instructions vary with the address mode,
		a set label is always treated as a LONG value (unless
		otherwise specified) and an equated label is treated
		for the value it contains. Since the assembler always
		attempts to use the shortest instruction length possible,
		a change in the type of a label can cause bad code to be
		generated.

===============================================================================

			Addressing Modes:

   The following models show the valid address modes for the 68000 processor
as they are recognized by the assembler:

	( 'n' represents a digit from 0 to 7, X represents either 'D' or 'A'
	  for an address mode 'ALabel' represents a symbol with an absolute
	  or an external value, 'RLabel' represents a Line Label or an
	  ENTRY typed label, 'number' refers to an actual numerical value, and
	  the other items are what they are. Case is not significant except on
	  Label and Symbol Names. Defined REG Labels of the proper type may be
	  used in place of the register names.)

IMMEDIATE:

		#number		#ALabel

DATA REGISTER DIRECT:

		Dn

ADDRESS REGISTER DIRECT:

		An	SP

ADDRESS REGISTER INDIRECT:

		(An)	(SP)

ADDRESS REGISTER INDIRECT WITH POST INCREMENT:

		(An)+	(SP)+

ADDRESS REGISTER INDIRECT WITH PREDECREMENT:

		-(An)	-(SP)

ADDRESS REGISTER INDIRECT WITH DISPLACEMENT:

		number(An)	number(SP)	ALabel(An)

		ALabel(SP)

ADDRESS REGISTER INDIRECT WITH DISPLACEMENT AND INDEX:    (say that 50 times)

		number(An,Xn)	Alabel(An, Xn)	number(SP, Xn)

		ALabel(SP,Xn)

PROGRAM COUNTER RELATIVE WITH DISPLACEMENT:

		RLabel		RLabel(PC)	number(PC)

PROGRAM COUNTER RELATIVE WITH DISPLACEMENT AND INDEX:

		RLabel(Xn)	RLabel(PC, Xn)	number(PC, Xn)

SHORT ABSOLUTE:

		ALabel		number

(where the value is less than $007FFF or greater than $FF8000)

LONG ABSOLUTE:

		RLabel (to another section)

		ALabel		number

(where the value doesn't qualify for short mode)

SPECIAL:

		USP		CCR		SR


===============================================================================

			Release History:

   Version 1.0.1 Alpha1		released 02-Jan-87.

   Version 1.0.1 Beta1		released 11-Jan-87.
	Changes:	1. EQUATEd & SETVAL Labels now use their full
			   32-bit value in expressions.
			2. External 16-bit references are now handled
			   correctly (for those open-library calls.)
			3. Macro Parameters now parse correctly when
			   separated by commas.
			4. The REG and EQUR functions were swapped.

   Version 1.0.1 Beta2		released 20-Jan-87.
	Changes:	1. Conditional levels were increased to 16.
			2. The include directory spec switch was changed
			   to handle logical assignments correctly (e.g.
			   INCLUDE: now works.)
			3. DBcc and Bcc branches to an ENTRY Label no
			   longer generate an error.
			4. IFD and IFND did not function properly with
			   SET or EQUATED Labels.
			5. The assembler now passes external reference
			   information for the linker on EXTERN items
			   used as immediate operands.
			6. Several heavily used routines were rewritten
			   in assembly language and assembled with this
			   program.

===============================================================================

NOTE:	Amiga and AmigaDOS are trademarks of Commodore Business Machines.
	Intel is a trademark of the Intel Co.
	MC68000 is a trademark of Motorola Co.

===============================================================================

			<*|=|*>  THE END  <*|=|*>

==============================================================================