C310.ZIP

"AAF version of Sky King's Cessna 310, the Songbird"
(1st Edition) by Russell Mueller 1992
An add-on aircraft for Microsoft Flight Simulator 4.0b.
Created with Mallard's Aircraft & Adventure Factory
(AAF not required to fly)

Description:
	Model 310
	Cessna Aircraft Company
	Wichita, Kansas
	AAF Design by Russell Mueller

Files:
	C310.DOC	This file
	C310____.	Copy this file to your \FS4 subdirectory
	C310____.SIM	Copy this file to your \FS4 subdirectory
	C310.AFX	Packed files for AAF users
	REFC310.SIM	Reference SIM file for flight model
	C310MEIG.MOD	Mode file with 310 on runway at Meigs.

Description:
        The Cessna 310 is probably most remembered as being
   the plane used in the popular '50's (?) TV series, Sky King.
   The plane was nicknamed "Songbird", and the name was painted
   on the nose of the plane.  Some will also remember that
   Sky King had a Beech 18 in very early episodes.  Most of
   those who remember the show probably remember few details,
   myself included, except for Sky King's niece, Penny.
   Ah, but I digress.
        The reference I used for this model was excerpted from
   a 1966 model 310K Owner's Manual, so details may vary from the
   vintage of the plane used in the TV program.  For the 1966
   model, some performance specs are as follows:

  Maximum Take-off Weight		5200 LBS.
  Maximum Landing Weight		5200 LBS.
  Maximum Structural Cruising Speed	210 MPH
   (Level flight or climb)
  Maximum Speed
   Flaps Extended 15 degrees		180 MPH
   Flaps Extended 15-35 degrees		140 MPH
   Gear Extended			140 MPH
  Never Exceed Speed			257 MPH
  Normal Speed Range			85 - 210 MPH
  Engine Maximum Power			260 BHP at 2625 RPM
  Fuel Flow				0 to 23 GPH
Twin Engine Climb at 5200 LBS
  (Maximum Performance)
  Sea Level (59 F)			125 MPH (IAS), 1542 FT/MIN
  10,000 FT (23 F)			122 MPH (IAS),  818 FT/MIN
Single Engine Climb at 5200 LBS
  Sea Level (59 F)			119 MPH (IAS),  330 FT/MIN
  10,000 FT (23 F)			113 MPH (IAS),  -80 FT/MIN


Flying:
        Start the engine using the FS4 command 'M5', and then
   increase the throttle to maximum.  At about 95 knots,
   pull back on the stick.  You can use partial flaps for an
   earlier liftoff.  The plane will lift off by itself with
   partial or full flaps.
        The 310 is a moderately easy flying plane.  Take-off
   run may seem a little long, but is fairly accurate
   compared to the over-performing planes we usually fly in
   FS4.  The AAF model SIM is based on the Experimental Prop
   Plane in FS4/ASD.  I did take poetic license and increase
   the power to 600 HP to achieve the desired performance.
        The stall is variable dependent on attitude and power
   setting.  I have experienced everything from a mush to a 
   snap roll over the top.  This plane will bite if mishandled.
   Watch for that snap roll: it is beautiful.

Landing:
       No special requirements here.  You can easily make a
   powered landing at partial or zero throttle setting.  If
   using flaps, then you will need to carry some power all
   the way through to the landing flare.
       I like to fly with a ThrustMaster FCS or FCS Pro
   joystick, and set the sensitivity to maximum
   (4-E-B-8-ESC-ESC) for most planes.  It is a good technique
   to learn to handle planes gently without over-controlling.
   It is *NOT* a good means to get more control authority
   for any particular plane in FS4.

Max Cruise:
       My methodology for checking top speed is to use the
   autopilot, set an altitude, usually 10,000 feet, and then
   let the plane settle in level flight.  The model Cessna 310
   attained 175 knots using 600 hp in the SIM model.  This compares
   to a top speed of 210 MPH (181 knots) listed in the Owner's
   Manual, so I feel I got pretty close on this one.


Notes:
       The dimensions of the plane were taken from 3-view
   drawings and information in the 1966 Cessna Model 310K
   Owner's Manual, provided to me by Doug Peterson.

       Like others, I experienced some difficulty in the
   bleed-through of parts, and disappearance of certain parts at
   some angles.  I think this is a minor distraction compared to
   the fun of flying these unique planes in FS4.
       I took the liberty of adding a crown to the side of the
   plane to add a little nostalgia in reminiscing about Sky King.
   Because I reached the max parts limit in AAF, I was not able to
   add further detail such as paint stripes, props, and no prop
   circles.  And I was not able to make the front windscreen two
   panels as would have been proper.  I think it is a beautiful
   bird anyway.
        This model is not multi-player compatible (MP=151%),
   as the AAF part count is max'ed out at 182.  


Enjoy!
"AAF version of Sky King's Cessna 310, the Songbird"
Copyright 1992
by Russell Mueller
Compuserve ID [76662,1623]