***  REMM.SYS INFORMATION HEADLINE  ***

EPG Products (Memory Boards):
-----------------------------

This is a breakdown of AST (EPG) Memory Products which require certain
versions of the REMM.SYS Expanded Memory Manager.  This is not to be confused
with AST Premium Computer System's REMM.SYS drivers.  This breakdown does not
apply to AST Computer Systems.

    Product's Name      REMM    ASTEMM
    ----------------------------------
    Advantage/2-386      N/A     2.27
    Advantage Premium   4.30      N/A
    RAMpage/286         4.30      N/A
    RAMpage/2           4.30      N/A
    RAMpage/2-286       4.30      N/A
    SixPakPremium       4.30      N/A


If you are using an application program which requires an older version of
REMM.SYS (your software should state this in it's documentation), then you
should use an older version - rather than the most recent version.

SPECIAL NOTE: You can determine which products REMM.SYS is compatible with
              by its version number.  For REMM.SYS versions 4.0 and later, an
              ODD version is for AST EPG Memory Boards (i.e RAMpage, Advantage
              Premium, etc.).  An EVEN version is for AST Premium Computer
              Systems (i.e. the Premium/286, etc.).

              REMM.SYS v4.3 is for AST Memory Boards
              REMM.SYS v4.2 is for AST Computer Systems

              This REMM.SYS identification strategy does not apply to REMM.SYS
              versions prior to 4.0.

If any of these products are installed in an AST Premium computer system, then
you should use the REMM.SYS that was intended for use in that particular
computer.


SYSTEMS (AST Premium Computers):
--------------------------------

The following are versions of REMM.SYS that have been released specifically
for AST Premium Computer Systems.  They are not intended for use with any AST
Memory Board (except when the Memory Board is installed in an AST Premium
Computer System).  Released REMM's for the Premium/286 are:

    REMM.SYS v4.20 (EMS 4.0 Specification)
    REMM.SYS v4.00 (See Notes Below)
    REMM.SYS v3.50 (EMS 3.2 Specification)
    REMM.SYS v3.00

NOTES: If you are currently using REMM.SYS version 4.00, than you should
       consider updating your system to the latest version (specifically,
       version 4.20).  This way, you can be assured that you are using the
       most up-to-date version that AST has available (REMM.SYS version 4.20
       is fully LIM-EMS 4.0 compatible).

AST Premium Workstations use the same REMM.SYS versions that the Premium/286
does.  However, it is designed around LIM EMS v4.0, and thus will not work
with any versions of REMM.SYS prior to v4.0.  So, if you have an AST Premium
Workstation, you should be using the most current version of REMM.SYS that is
compatible with LIM-EMS v4.0 (i.e. REMM.SYS v4.20).

AST Premium/386 computer systems do not use a REMM.SYS device driver.  But
rather, it uses a driver called ASTEMM.SYS that converts 80386 Extended memory
(linear) into Emulated EMS 4.0 Expanded memory.  Thus, REMM.SYS should not be
an issue on a Premium/386 computer system.

AST FASTboard/386 accelorator boards for the Premium/286 must be used with
REMM.SYS version 4.27.  This board can not use the general Systems or EPG REMM
drivers, do to the special nature of the board.

                        REMM.SYS 4.X AND DESQVIEW 2.XX


Users of DESQview 2.01 (or above) may experience system lock-up when using a
version of REMM.SYS of 4.10 (or above).  The lock-up occurs when running an
interrupt-intensive application such as a serial communications program.

The reason that this particular combination causes this symptom lies in the
fact that the LIM 4.0 functions are being executed in software, requiring a
large amount of processing time.  This amount of overhead becomes critical
when processing time must also be devoted to servicing the stream of
interrupts generated by a communications program.  Any application that must
devote a great deal of time to both expanded memory operations and serial
communications will eventually be unable to keep pace and cease to function.

It is recommended that those users who operate in this environment and
experiencing problems, replace the 4.xx version of the REMM.SYS driver with a
3.xx version.  For AST Systems products, version 3.50 of REMM.SYS is
recommended.  For AST board-level expanded memory products version 3.10 of
REMM.SYS will operate in this environment.

Those users with expanded memory hardware which fully supports the LIM 4.0
Specification, (i.e., AST RAMpage Plus/286 or AST Premium/286 using Advanced
FastRAM), will not experience any of the difficulties outlined here.

Please note: It advisable to verify that the correct DESQview configuration
and operation procedures are followed.  Appendix E in the DESQview Manual
contains detailed information about running communications programs.

                             The Magic of Remm ...


The Rampage  Expanded Memory  Manager (REMM) is the device driver that must be
included in the config.sys file that allows expanded memory to be used  and
managed.  ALL expanded  memory whether  EMS  or  EEMS  is invisible to DOS.
That is - DOS, cannot acknowledge or test the memory of an expanded memory
board. It is the expanded memory manager and the application program that
utilize expanded memory.

The first  expanded memory  boards were  manufactured according to the
Expanded Memory  Specification (EMS)  developed  by  LOTUS,  INTEL,  &
MICROSOFT. Only  a  few  months  later,  AST  RESEARCH  announced  the
Enhanced Expanded Memory Specification (EEMS) and began shipping their EEMS
boards.  EEMS was  a true  superset of EMS. EEMS had all the same functions as
EMS, however, it provided quite a bit more power.

When REMM  initializes it  searches for  a 64KB window in the reserved area
between  640KB and  1MB. It  begins its  search at C000 and jumps upward in 
16KB increments.  When  REMM  finds  four  contiguous  16KB segments that are
available it creates its 64KB window. If REMM cannot find four  consecutive
16KB  blocks available  it will fail to install itself.

REMM cannot see into the future. Should a device or program attempt to use
the  same address range as REMM, then most likely REMM will crash.  It is the
task of the user to be aware of what other ROM's or programs make use of the
reserved memory between 640KB and 1 MB.

As REMM is initialized in the config.sys there are several steps that it
performs:

          1)   Command line parameters are handled.
          2)   Test to see if expanded memory is in system.
          3)   Determine  level   of  hardware  support  for  expanded memory.
          4)   Read Switch settings from the board (if appropriate).
          5)   Generate internal tables.
                    a) Handle Table
                    b) Allocation Table
          6)   Test Expanded Memory.
          7)   Done - Install INT 67.
          
          N.B. Boards are checked in Base I/O order.


                               Versions of REMM

Due to  the continual  development of  hardware and software, REMM has
undergone many  changes and  will continue  to do  so for some time to come.

REMM was  first shipped by AST Research along with their EEMS boards - the
Rampage!,  Advantage Premium,  and Rampage286  to name  a few. The REMM
driver  was bundled  along with  other software  utilities on the SUPERPAK
Diskette.

At that  time in  the market  place the  IBM standard  had set the BUS speeds
at  4.77 MHz  for the  PC &  XT; and 6 or 8 MHz for the AT. The PC/XT and 
AT-class EEMS  Boards manufactured  by  AST  were  made  to operate at  those
respective  clock rates. The REMM driver was written specifically with  those
environments in mind. Over time, enhancements were added  to improve overall
performance and compatibility. When AST decided to  manufacture the 
Premium/286, they  incorporated into  its architecture  the  FASTSLOTS  which 
provided  direct  access  to  the microprocessor at zero wait states.

To take  full advantage  of this  proprietary  architecture  a  system
specific version  of REMM  was required.  The first  system version of REMM
to  ship with  the Premium/286 was REMM version 3.5. This version enabled
expanded  memory according to the EEMS specification. When the LIM 4.0 
specification was announced, REMM was subsequently updated to version 4.x.  If
x  were an  even number  then REMM  was  specifically updated with  the
Premium  Systems architecture  in mind. If x were an odd number  then that 
version was  meant for the add-in memory boards made by  AST. For  best
performance,  it  is  important  that  only  a 'systems' REMM  be used with
AST's system products. This is especially true when using an AST expanded
memory card in addition to the FASTRAM card.

                        Premium/286 & REMM version 4.x

The address range of E000-EFFF in the Premium/286 is available for use by REMM
if and only if:

          A)   The version of REMM is capable of selecting the 'E' block.

          B)   All system memory is located on a FASTRAM card.

          C)   No other device is utilizing that same address range.

               (i.e. Expansion ROM's or Device Drivers)


                              Video Boards & REMM

One of  the most  common devices that occupy the reserved area between 640KB
and  1MB are  the various  video boards.  Below are  listed  the various
video  standards and  the most  appropriate exclusions  to use with REMM to
avoid any conflict.
                           ________________________
                          |                        |
                          | MONO      /X=B000-BFFF |
                          | CGA       /X=B800-BFFF |
                          | EGA       /X=A000-C3FF |
                          | VGA       /X=A000-C7FF |
                          |________________________|


                              REMM & AST-3G Cards

However, there  are now video adapter cards that emulate several modes and
may  require a  different  set  of  exclusions  because  of  their
versatility. One  good example  is the  AST-3G Cards. Below are listed the
various video modes and the most appropriate exclusion to use with REMM to
avoid any conflict.

                           ________________________
                          |                        |
                          | MONO      /X=A000-C3FF |
                          | CGA       /X=A000-C3FF |
                          | EGA       /X=A000-C3FF |
                          |________________________|


                                  REMM & VGA

The new  VGA boards are becoming more attractive to the computer world with
its  larger color  palette and  improved performance. The AST VGA boards
contain  ROM's whose  address range  is from C000-C7FF. Display memory 
occupies  the  range  from  A000-BFFF.  The  proper  exclusion statement would
be:

                           ________________________
                          |                        |
                          | VGA       /X=A000-C7FF |
                          |________________________|

                                    <more>

There are some VGA boards that are using some memory outside the range set
aside  for the  VGA standard. If this is the case then it would be best to use
the following exclusion:

                           ________________________
                          |                        |
                          | VGA       /X=A000-CFFF |
                          |________________________|



    N.B. Some VGA boards are 16 Bit Cards. Please see section - REMM in 16
                                   Bit Mode.


                      REMM - Networks - Emulation Boards

Network &  Emulation Boards can present a very interesting environment for
REMM.  For the most part, most of these boards contain ROM on them that allow 
for self-diagnostics  and initialization.  The ROM must be accessible to the
microprocessor and so usually occupies a small range of memory  above 640KB 
and below  1MB. It  is important  to determine where that  ROM resides and to
make REMM avoid it by use of the proper exclusion parameter. If the
manufacturer of the expansion board allows the ROM  to be addressed at various
locations then that aids in making all  these  devices  work  together  in 
harmony.  However,  once  the config.sys has  been installed  , these boards
may require a window of memory so  that they  can pass  data. REMM  may have 
installed itself successfully but  may have  been corrupted by another
intruding memory window. It  is most  important that  the system integrator be
aware of the memory requirements of all devices.


                              REMM in 16 Bit Mode

It is  only in  light of  recent technical  advances that  the current subject
be  discussed. There  are now  in the marketplace video boards that operate in
16 Bit mode. This is done to increase the performance of video in a system.
While this is a great benefit, it requires a bit of thought  in using  REMM.
REMM can operate in either 8 Bit or 16 Bit mode. REMM  has always  defaulted
to  8 Bit mode but may be used in 16 Bit mode  by use  of an  undocumented
parameter - /M. REMM can only be used in  16 Bit  mode if it is in a 128KB
segment by itself or sharing it with  another 16 bit device. 8 bit and 16 bit
devices cannot occupy the same 128KB segment.

When you  break up  the 1MB of addressable memory into 128KB segments, there
are a total of eight segments divided as follows:
                     _____________________________________
                    |                                     |
                    |   128KB Segments   Binary (default) |
                    |_____________________________________|
                    |                                     |
                    |    E000 - FFFF            0         |
                    |    C000 - DFFF            0         |
                    |    A000 - BFFF            0         |
                    |     512 - A000            1         |
                    |     384 -  512            1         |
                    |     256 -  384            1         |
                    |     128 -  256            1         |
                    |       0 -  128            1         |
                    |_____________________________________|

The eight segments are assigned a binary digit that comprise one byte.  The
eight  bits of 00011111 can be converted to the hexadecimal number of 1Fh.
This is the default mode of REMM which recognizes 0 - 640KB as being 16  bit
accessible  memory while  the area above 640KB and below 1MB are  accessible
in  8 bit mode. In order to access a segment in 16 bit mode  just place a one
in the segment that needs to be accessed in 16 bit  mode. Convert  the new 
binary number to a hexadecimal number.  This is the number that will be used
with the /M.parameter.


EXAMPLE:

Using an AST-VGA+ video adapter (16 bit card) and REMM, the proper statement
in the config.sys file would be:

                _______________________________________________
               |                                               |
               | DEVICE=REMM.SYS /M=7F /X=A000-C7FF /S=C800 /N |
               |_______________________________________________|

REMM will now operate in 16 bit mode and reside in the same segment as another
16 bit device - the AST-VGA+ video adapter card.


                                  Conclusion

In the  early days of computing with the IBM PC, life was very simple.  If
you  had an empty expansion slot and an expansion board it was easy to
upgrade  your system.  Drop the  board in and power up the CPU. Now however,
with  more boards  and the complex requirements made upon the operating
system,  more thought will be needed to fine tune the micro- computer to the
specific tasks required by the user.