#1[1z[1z





                  RDATE - Set Amiga clocks from a timeserver

     Rdate requires  that AmiTCP be running and uses the TCP protocol to access
 the "time" service on a specified  machine to  get the  correct time.  It then
 converts it  to your  local time  and sets  the Amiga's  software and hardware
 clocks. If the hardware clock can't be found the program will print  a message
 and set only the software clock. 

     In order  to perform  this small  miracle, the  program needs  to know two
 things.

 1. The name of the machine which will provide you with TCP time service as per
 RFC868. It  is important  to note  that the  program requires the TCP service.
 Some time service machines  only provide  the UDP  service (also  described in
 RFC868) but the program can't use UDP.

    The default  name used for the machine1 is "tick" which is a machine on the
 U. of S. campus (and which won't be much use to you if you are off  campus. If
 you have a machine in your db/hosts file whose name is tick and which provides
 time service then rdate will connect  to that  machine. Otherwise  you have to
 set the  environment variable TZ_TIMESERVER to the name of the server machine.
 This variable must be set with the setenv command. E.G.

    setenv TZ_TIMESERVER clock.domain.org

 If you have a machine named "clock" in your db/hosts file then

    setenv TZ_TIMESERVER clock

 is sufficient.

 2. You must specify which timezone you use to set your computer clock by. This
 is done by setting the environment variable TZ_CHU and can be done with either
 the setenv command or the Manx "set" command.

     The environment  variable TZ  is not  used because  it does  not allow for
 timezones such as that in Newfoundland which is half an hour ahead of Atlantic
 Standard Time.

     The general format of the  string  that  specifies  your  timezone  in the
 TZ_CHU environment variable is:

     [-]hh[:mm][D]

     This means  that the  time is  specified as a number of hours which can be
 preceded by an optional minus sign  (for  EAST  of  Greenwich)  and optionally
 followed by  a number  of minutes (e.g. 3:30 for Newfoundland) and all of this
 can have an optional letter  after  it  to  specify  that  your  timezone uses
 daylight savings  time. The dates of the start and end of DST are different in
 various parts of the world. You indicate which  is  used  in your  zone by one
 of the  following letters. If you are in the northern hemisphere then you must
 specify the letter in  lower case, and if you  are in  the southern hemisphere
 then you  must specify  it in  upper case.  The letters  and the  dates of the
 start and end of DST are listed below:
[1z





d or D: North America. Start first Sunday in April  and end  last Sunday in
     October.

u or U: U.K. Start last Sunday in March and end last Sunday in October (the
     actual dates are set by  act  of  parliament  each  year  but  this is
     usually what they pick).

e  or  E:  Europe.  Start  last  Sunday  in  March  and  end last Sunday in
     September.

 c or C: China(!). Start 12th April and end 12th September.

     If you specify upper case for the southern  hemisphere then  the start and
 end of DST are reversed. In all cases the start and end occur at 2am.

     The best thing to do is to add a setenv command in your
 s:startup-sequence file.  If you  use any  of my  other programs,  such as the
 C_BBS packet program or the CHU program, then  you won't  have to  do anything
 extra with  them because  they all  use   the same  routine to  check for your
 timezone and adjust to UTC. I use the command:

  setenv TZ_CHU 6

 in my s:startup-sequence file because I am in the Central  Standard  Time zone
 (6 hours  west of  Greenwich) and  we do  not   use daylight  savings time. In
 Germany, which is one hour ahead  of  UTC and  uses European  daylight savings
 time you would use:

     setenv TZ_CHU -1e

     I am  not sure  what DST  is used in Australia or New Zealand but if as an
 example, they use the same DST as the U.K. (except  that they start in October
 and end  in March) then an upper case 'U' is specified along with the timezone
 correction.

 (The odd name "TZ_CHU" is derived from a program I wrote which  reads the time
 from  Canadian  radio  station  CHU  and  sets  the amiga battery clock fairly
 precisely).

     Once you have the name of the time server and  your local  timezone set up
 properly  then  all  you  have  to  do,  apart from making sure that AmiTCP is
 running, is to run the rdate program. It is only set up to run from the CLI.

 The program prints out how many seconds the current time on the  Amiga differs
 from the  actual time reported by the timeserver and then it sets the clock to
 the correct time.
c