REALISTIC PRO-2005 SCANNER MODIFICATIONS


     THE 2005 SCANNER IS EASILY MODIFIED TO INCLUDE ALL THE
     800 Mhz FREQUENCIES. THE NEW COVERAGE WILL COVER 25-520,
     760-1300 Mhz.THE MODIFICATION REQUIRES THE TOP COVER TO
     BE REMOVED, THAT'S JUST THE TWO SCREWS IN THE BACK.  THE
     SPEAKER WILL UNPLUG FROM THE PC-BOARD,SO IT WON'T BE IN
     THE WAY.  THE TWO DIODES ARE MOUNTED ON THE BACK OF BOARD
     THREE, THAT'S THE ONE THE LCD AND KEYPAD ARE ON. THE
     DIODES NUMBERS ARE D502 AND D503. THEY ARE MOUNTED DIRECTLY
     BEHIND THE 3 BUTTON ON THE KEYPAD. TANDY WAS NICE ENOUGH TO
     STICK THEM IN AN OPENING THAT GIVES ENOUGH ROOM FOR
     DESOLDERING OR A PAIR OF SNIPS.  THIS STATEMENT IS FOR YOUR
     INFORMATION ONLY IN CASE SOMEDAY THE FCC LEGALIZES THIS,
     THIS MODIFICATION WILL MAKE THE SCANNER OPERATE AT MAXIMUM
     FREQUENCY CAPACITY. PLEASE OBSERVE FCC RULES AND
     REGULATIONS REGARDING THE COMMUNICATIONS PRIVACY ACT.                               HAVE FUN!!