WELCOME TO ACIRAN V3.6
                        ----------------------

This README file contains important, last minute information
about Aciran V3.6 


TABLE OF CONTENTS
-----------------
  1. How to Get Help
  2. Installation
  3. Important Notes
  4. Additional Notes
  5. Files on the Disks


 1. HOW TO GET HELP
-------------------

  If you have any problems, please read this file, and the Aciran manual first.
  If you still have a question and need assistance, help is available from
  the following source:

     Write to me at the following address:

     James Herron
     Aciran Software Systems,
     29 duncryne Place,
     BishopBriggs,
     Glasgow G64 2DP
     Scotland



 2. INSTALLATION 
----------------

  You should read the rest of this README file to get further
  information about this release before you do the installation.

  From the DOS prompt select the drive containing the ACIRAN disk and
  type install <return>.

  Follow the instructions to complete the installation.
 

 3. IMPORTANT NOTES
-------------------

  o The executable and a number of other files are compressed. You cannot
    just copy the files to your hard drive, you must run the install program.

  o If at any time you wish to decompress a file manually, use the unpack.exe
    program supplied. Files that are compressed end in a $.

  o If you are running on a laptop or any other system that uses an LCD or
    mono display, you should set Aciran to black and white mode.
    You can do this from DOS with the following command line:

    Aciran /m <cr>

  o As mentioned in the installation section,if you are running from a single
    drive then you should only copy the essential files required to run Aciran.



 4. ADDITIONAL NOTES
--------------------
   
  o Actran can handle POT's from ORCAD files by converting them into two fixed
    resistors connected in series with the wiper coming from the common 
    connection. Both resistors are given values equal to one half of the POT
    value, in other words as if the POT was set to it's mid position.

  o Actran can handle tolerances so long as the Key field is set up correctly
    in draft.You must leave at least on space between the fields eg.

               V x

     where V is the value, the referance is included, and x is the field that
     contains the the tolerance value.

  o There is an additional version of Aciran supplied on the disk. This
    is TAC, (Tiny or Turbo Aciran). This version is fully
    compatable with the larger program but by limitting the data structures
    (node size) to within a single 64K boundrary the microprocessor does not
    have to alter it's data segment register as often as it does in the larger
    version and as a result the Turbo program runs four times faster. It is
    recommened that TAC be used whenever possible as it will save
    considerable time,especially when carrying out tolerance analysis.

 o  ACIRAN V3.6 was created using the Turbo Pascal Compiler (V5.5)
    and as such it supports co-processor floating point format in both
    Hardware and software Emulation. If your computer has a co-processor
    it will be detected by ACIRAN and used to perform all calculations.
    Should your machine not be fitted with a Maths chip then ACIRAN will
    emulated the chip in software. This means that the program is fully
    compatible with either hardware configuration. Obviously the program
    will run much faster if the co-processor chip is fitted.


 5a. FILES ON THE DISKS (Shareware Version Only).
-------------------------------------------------
  INSTALL  EXE    -  Install program
  INSTALL  INF    -  Install control script
  DUNPACK  EXE    -  Unpack utility
  README   DOC    -  This file
  ACIRAN   DO$    -  Aciran Manual on file
  ACIRAN   EX$    -  Full version 3.6 of Aciran AC circuit analysis program
         *.AMP    -  Opamp model parameters
         *.CIR    -  Circuit examples.
         *.FET    -  Fet model parameters
         *.TRN    -  Transistor model parameters.


 5b. FILES ON THE DISKS (Registered Version Only).
-------------------------------------------------

  INSTALL  EXE    -  Install program
  INSTALL  INF    -  Install control script
  DUNPACK  EXE    -  Unpack utility
  README   DOC    -  This file
  ACIRAN   EX$    -  Full version 3.6 of Aciran AC circuit analysis program
  ACIRAN   DO$    -  Aciran Manual on file
  ACTRAN   EX$    -  Utility to allow ORCAD netlist files to be converted
                     to Aciran circuit files.
  SPAC     EX$    -  Utility to allow PSpice circuit files to be converted
                     to Aciran circuit files.
  UPGRADE  EX$    -  Converts previous circuit files to new format
  ACIRAN   LI$    -  ORCAD Library for use with Actran

         *.AMP    -  Opamp model parameters
         *.CIR    -  Circuit examples.
         *.FET    -  Fet model parameters
         *.MAP    -  Orcad map file of each circuit example
         *.NET    -  Orcad netlist file (spice format) of each circuit
         *.SCH    -  Orcad schematic files of each circuit
         *.TRN    -  Transistor model parameters.

NOTE: files ending in $ are compressed and the install program should be
used to unpack them.