Don's Original Designs         
                          Oceanside, Ca
                     Don Rasmussen  WB8YQJ/6
 



              Don's Original Designs proudly introduces ProCat/HF
user  customized  software.  What you get  is  computer  keyboard 
control  of your transceiver, user defined command keys,  contest 
callsign duplicate checking, and transceiver memory loads for the 
Yaesu   FT747GX.  The  system  works  with  any  Icom  or   Yaesu 
transceiver that has provisions for computer control. You need an 
IBM compatible computer with hard drive, serial port, and EGA  or 
VGA  graphics  card.  An interface is  required  to  connect  the 
computer serial port to the transceiver, which is available  from 
the   transceiver   manufacturer.  Interfaces   can   be   easily 
constructed, and are generally compatible between  manufacturers. 
A  Yaesu FIF232 interface works great with Icom  transceivers  by 
connecting Yaesu DIN #1 to Icom remote connector center, and  DIN 
#3 to Icom remote connector ground. Once interfaced, the  program 
allows  instant  QSY  using the numeric keypad  on  the  computer 
keyboard.  The  control  keys  are grouped  to  make  tuning  the 
transceiver EASIER than it would be by using the transceiver  VFO 
knob.  You  can also add other commands to the  transceiver,  and 
assign  any key you wish to perform that command. The  programmed 
keys  are not available during contest duplicate  checking,  this 
makes  the duplicate checking easier. More on  contest  duplicate 
checking later. You can change the on screen colors to suit  your 
taste,  and  the on screen GMT clock is adjustable to  your  time 
zone. I hope you  find  ProCat/HF useful in  your shack, as  many
hours  were  spent  in  design, programming, and debugging.  

 
                                          Best 73's
                                             
                                            Don


Special Thanks To:

Edward J. Coan
Yaesu Musen Co. Ltd.
Tokyo,  Japan

Roy Kessler 
Janet Traylor
PC Globe Incorporated
Tempe, Arizona



                                                        
                      A Quick Demonstration
                             



All programs and files should be copied onto your hard disk.

To  run the program, key in PROCAT and then press the enter  key. 
Make sure your transceiver and interface are turned on and ready.

Make sure the NumLock light on the keyboard is on.

The  program  will  show  you  the  opening  screen,  with  the 
station  clock  in  the  upper  left    corner,  and  ten  VFO 
frequencys  listed along the right border of the screen.  One  of 
these VFO frequencys will have a highlighted background. You  can 
change the highlighted frequency by pressing the cursor up or the 
cursor down key, these keys are  located just to the left of  the 
numeric keypad.

NOTE: The transceiver that is currently configured is listed just 
below the time display. See configuration instructions to  change 
the current transceiver. 

You can set the transceiver display to the highlighted  frequency 
by  pressing the numeric keypad minus (-) key. You can raise  the 
highlighted frequency by pressing the keypad plus (+) key, the  6 
key, the 5 key, or the 4 key. When you press the plus key (+) the 
frequency will only be raised by 25 hertz, so you'll have to keep 
it depressed for a few seconds to hear a noticable change in  the 
received  signal.  You can lower the frequency  by  pressing  the 
keypad  (enter) key, the 3 key, the 2 key, or the 1  key.  Again, 
you'll have to hold down the (enter) key for a couple seconds  to 
notice  any  change.  Transceiver mode can  also  be  changed  by 
entering the first letter of the mode.  Notice how all tuning  of 
the transceiver can be easily done with one hand over the numeric 
keypad, and very little looking at the keys.

If  you  want to change the highlighted  frequency  to  something 
completely  different,  press  the "b" key to  enter  a  new  VFO 
frequency.


The TEN VFO's on the screen have a description in the lower right 
corner of the screen. You can change this description by pressing 
"e"  then pressing "l". Or, you can clear this group of VFO's  by 
pressing "e" then pressing "e" again.

There  are  up  to 20 groups of TEN VFO's, the  group  number  is 
listed just to the left of the description. A different group  of 
VFO's  can  be called by pressing "r" then entering a  new  group 
number (from 1 to 20).


                   Main Menu Key Definitions 


     F2 - adjusts on screen window color.
     F3 - adjusts on screen text color.
     
     F4 - adjusts the station clock.

     F5 - starts contest callsign checking.
     F6 - finishes contest callsign checking.

     F9 - clears the contest callsign file.  

     b - enter a new base frequency in highlighted VFO position.
     r - request a different page of VFO's.
     e - edit the label or erase a page of VFO's.
     o - call the configuration options program.

     u, l, c, a, f, n - used to set transceiver mode.

     KEYPAD KEYS

     4 - Up   100 KHZ
     1 - Down 100 KHZ
     

     5 - Up 10 KHZ
     2 - Down 10 KHZ

     6 - Up 1 KHZ
     3 - Down 1 KHZ

     (plus key) - up 25 HZ
     (enter key)  - down 25 HZ
     (minus key) - set displayed frequency, no change.
     (cursor keys) - select displayed VFO.


                     Duplicate QSO Checking


      Press F5 to start contest duplicate callsign checking.  All 
keys other than numeric keypad keys are disabled. Use the  keypad 
to tune in a contest station. Key in the station's  callsign  and 
press return. If the  call begins  with  the  number 1 through  6 
(this rarely happens) preceed the call with an asterisk. The call 
will  be added to the list, and displayed in large letters if  it 
is a good call. Then, try to work the station, use the  displayed 
QSO  number  in the exchange. If you can't work  him,  press  the 
backspace  key  to  drop  him from the list. If  the  call  is  a 
duplicate, it is not added to the list, and the WARNING LEMON  is 
displayed. Over 900 calls can be saved. Press F6 to save the  log 
and return to ragchew mode. Press F9 to clear the duplicate log.


                Configuration and Customization


     Configuration  can  be as simple as defining  your  graphics 
card  and transceiver brand. Or, you can  define custom  keys  by 
looking  up the computer command data in your  Yaesu  transceiver 
manual or the Icom C/IV communications manual. An example of this 
would  be to define the "S" key. First, specify a label  for  the 
key,  like "SPLIT ON". Then, look in your transceiver  manual  to 
find  the  command bytes that perform this function, and  key  in 
that data. When you finish, this will be displayed on the  screen 
  S - SPLIT ON    . You can also position this label anywhere  on 
the  screen you want. From then on, whenever you press the  upper 
case S, the split function on your transceiver will be turned on. 
You may want to define the lower case "s" as SPLIT OFF. There are 
20 keys available for definition.

         The options screen is available by pressing "o" from the 
main  menu. Then press return to select  configuration  from  the 
options  menu.  Here  is the list of options  and  the  responses 
required.

Change  Basic  Configuration? - enter Y to  specify  a  different 
brand of transceiver than that listed under the time on the  main 
menu.

Configure Icom Transceiver? - enter Y to select an Icom transceiver.

Did you modify your rig for 9600 BPS operation? - All Icoms  come 
from  the factory configured for 1200 BPS. There is a  jumper  in 
the  transceiver  that  can be moved to  enable  a  higher  speed 
transfer. Enter Y if you've enabled this option. (A Good Idea.) 

Command  Data  is 5 Bytes Long, is the command  byte  sent  last? 
(Yaesu Only) - All Yaesu commands are 5 bytes long. Depending  on 
your model the command byte may be the first byte, or more often, 
the last byte of the string.

Frequency set command byte? (Yaesu Only) - is usually 0a, look in 
your manual and remember to enter zero and not the letter "O"  in 
these hexadecimal responses.

Setup  Operating Modes? - enter y to define the keys used to  set 
transceiver mode.

Mode set command byte? - Icom users enter 00. Yaesu  transceivers 
that have one command byte and four dummy bytes for the mode  set 
command (this is rare) enter 00. For all other Yaesu's enter  the 
value that will be first or last in the 5 byte string (this  byte 
is also called the "instruction byte" by Yaesu.).




                    Configuration and Customization
                           (Continued)


AM  mode  set command byte? - Icom users enter  02,  Yaesu  users 
enter  the AM command byte, also called the mode  set  "parameter 
byte" by Yaesu.

CW  mode  set command byte? - Icom users enter  03,  Yaesu  users 
enter the CW narrow parameter byte.

FM  mode  set command byte? - Icom users enter  05,  Yaesu  users 
enter the FM narrow parameter byte.

LSB  mode  set command byte? - Icom users enter 00,  Yaesu  users 
enter the LSB parameter byte.

CWN  mode  set command byte? - Icom user enter 04  (RTTY),  Yaesu 
users enter the CWN parameter byte.

USB  mode  set command byte? - Icom users enter 01,  Yaesu  users 
enter the USB parameter byte.

Suggested values were listed for Icom because all Icom radios use 
the  same  values, Yaesu values should be taken from  the 
transceiver manual.

OTHER CONFIGURATION OPTIONS

Adjust memory loading delay?(Yaesu FT747GX only) - enter a  large 
enough value in this delay to ensure that memorys are not  loaded 
into  the  FT747GX too fast, when this happens memorys  are  lost 
after the transceiver is powered down.

Use auxillary serial port? - enter Y to use Comm Port 2.

Use  VGA graphics? - enter Y if you have VGA graphics.

Change  the  programmable keys? - enter Y to see a  list  of  the 
programmable  keys that have been defined, and to change them  if 
you wish.

Programmable keys available 20  - Press  an  alphabetic key. You
   Press Esc to finish            will redefine the key if  it is
                                  on  the  custom  key  list that
borders  the left side of the screen. You can  define a  new  key  
if  it does not appear on the list. Remember that upper case  and 
lower case are different keys. Press Esc to finish.

Enter  key label - Enter a short description of the key you  want 
to  define, such as SPLIT ON, SPLIT OFF, WWV, CLARIFIER ON,  etc. 
This  description will be seen on the main menu. The letters  are 
small, using upper case improves readability.

                    Configuration and Customization
                           (Continued)

Enter  Command  (10 digits) - this is where you  will  enter  the 
actual byte string from your transceiver manual that will perform 
the  function you described in the (Enter key  label)  procedure. 
For  example, in the Yaesu FT747GX manual the  SPLIT  ON  command
consists of these  5  bytes ( 00 00 00 01 01 ). In  this example,
these  are  the  exact  10 digits  to  enter  (there  are  always 
two  digits in one byte). Remember that although the  values  you 
are entering are in hexadecimal, there is no conversion  required 
by you!. Simply plug the ten digits in the way they are listed in 
the  manual.  All Yaesu commands are 10 digits (which is  also  5 
bytes)  long.  Whatever you put in this ten digit field  will  be 
sent directly to your transceiver, with no changes in byte  order 
etc.  Icom commands are not always ten digits long,  here is  the 
format  for Icom commands. In the Icom CI/V manual  (available  to 
anyone,  free  from Icom) on page 13 there is a  sample  FM  Mode 
command.  It  looks  like  this  ( FE FE 04 F1 01 05 FD ).  Every 
command  in Icoms manual starts with FE FE 04 F1 , and ends  with 
FD. Since that is true, the program will provide these characters 
to  the transceiver for you. In this example, if you  ignore  the 
characters  that the program adds for you, ( 01 05 ) is all  that 
is left. These are the digits for you to enter. When the  program 
asks for ten digits, key this in ( 01 05 FD FD FD ). Always use FD
to fill out the ten digit field. As an added example, the command
on page 12 looks like this ( FE FE 04 F1 00 10 32 54 21 FD ) for a
frequency set of 21.543.21 MHZ. You enter this ( 00 10 32 54 21 ).

Arrange  key  labels onscreen? - enter Y if you want  to  display 
your  key  labels  in another part of  the  screen.  

Move  which  key? - find a custom defined key  somewhere  on  the 
screen that you want to move. Press that key to select it. 

Use  the cursor keys to position the label - move the  key  label 
wherever it looks good, then press Esc to paste it in position.

FINAL NOTES

If  the  main file CATBASE.DAT is damaged, etc. Just  remove  the 
damaged file and execute ProEdit.exe A new file will be built.

ProCat.EXE - main program    ProEdit.EXE - options program
Catbase.dat - database       ProCatHF.DOC - documentation
EGAPCA.DAT - EGA SCREEN 1    EGAPCB.DAT - EGA SCREEN 2
VGAPCA.DAT - VGA SCREEN 1    VGAPCB.DAT - VGA SCREEN 2
TT747.EXE  - FT747 program   PT747.EXE - prints the database

I can accept no responsibility for damages caused either directly 
or  indirectly  from the use of this free program.  If  you  like 
ProCat/HF please pass it on to a friend, and remember your pal,

            Don Rasmussen, Oceanside Ca. January 1990