CD-SHARE DEMONSTRATION SOFTWARE PACKAGE

                     By - Digital Solutions Pty. Ltd.

                          Release 1.0 August 1991


     The programs  and documentation  packed with  this document  file
     form  the  CD-SHARE  peer  to  peer  CD-ROM  networking  software
     package.

     The demonstration package is a  generic version which will run on
     any NETBIOS  compatible network.  It is  restricted in  that a CD
     Server will  only accept a  log in  from one CD  Workstation at a
     time, and the CD Redirector will only log into one CD Server at a
     time.

     CD-SHARE sells for A$495.00  (i.e. Australian Dollars). For those
     of  you  in  the  USA  the  current  exchange  rate  between  the
     Australian and US dollar is about US$0.77 for A$1.00.

     If  you  have  any  questions  regarding  CD-SHARE  please  don't
     hesitate to contact us at :


     Digital Solutions Pty. Ltd.
     P.O. Box 178
     Margate
     QLD, Australia 4019

     Ph  (07) 8838151   Intl (617) 8838151
     Fax (07) 2831217   Intl (617) 2831217










































                CD SHARE - CD ROM NETWORK SHARING SOFTWARE

                                Version 1.0

                               User's Manual

































     Digital Solutions Pty. Ltd.
     P.O. Box 178
     Margate
     QLD, Australia. 4019
     Ph. 07 8831851 Intl. 617 8831852
     Fax 07 2831217 Intl. 617 2831217




































































                                  Page 1










                             TABLE OF CONTENTS

     CONTENTS                                                    PAGE

     1.0 BACKGROUND                                               1

         1.1 THE CD-ROM SOFTWARE INTERFACE                        1

         1.2 CD-SHARE - WHAT IT IS AND WHY WE NEED IT             2

     2.0 CONFIGURING A CD-SERVER                                  5

     3.0 CONFIGURING A CD-WORKSTATION                             5

     4.0 COMMAND LINE SWITCHES                                    9

         4.1 CD MANAGER COMMAND LINE SWITCHES                     9

         4.2 CD REDIRECTOR COMMAND LINE                          11

         4.3 CD-SERVER COMMAND LINE SWITCHES                     11

     5.0 CACHING YOUR CD-ROM DRIVES - CD-CACHE                   13

     6.0 ADVANCED TOPICS                                         15

         6.1 MEMORY USAGE                                        15

         6.2 OPTIMIZING CD-SERVE PARAMETERS                      16
             FOR A NON-DEDICATED SERVER

         6.3 OPTIMIZING CD-CACHE PARAMETERS                      17

         6.4 RUNNING CD-SERVE AND CD-CACHE IN DEDICATED MODE     19

     7.0 QUESTIONS AND ANSWERS                                   20



















                                  Page 2










     1.0 BACKGROUND

     1.1 THE CD-ROM SOFTWARE INTERFACE

     When you purchase a CD-ROM drive  and controller card for your PC
     you will usually also receive a disk containing a software device
     driver  for the  drive and  a program  written by  MicroSoft Corp
     called the "MS-DOS CD-ROM Extensions" (MSCDEX.EXE).

     Device drivers are programs that  are loaded by including them in
     a line  in the CONFIG.SYS  file on  your DOS boot  disk. A device
     driver is a software program  with a standard DOS interface which
     allows DOS  to talk  to hardware  devices which  it knows nothing
     about. Although you don't see it DOS actually talks to your disks
     via an internal device driver !

     The device driver  supplied with your  CD-ROM drive(s) allows DOS
     to interface  to the  CD-ROM drive  without actually  knowing the
     hardware specifics of the drive. This is how DOS can interface to
     various  different  brands  of  drives  with  different  hardware
     interfaces -  it simply  talks via  the device  driver which does
     know about the hardware.

     There are two different classes of device drivers - character and
     block device drivers. An example of a character device driver are
     the internal DOS  devices named CON (your  console) and PRN (your
     LPT1) since they work a character at a time. Your disk drives are
     block  devices since  they transfer  data to  and from  memory in
     blocks (e.g. a typical  cluster (block) size for  a disk might be
     2K bytes.  Character device drivers  and addressed  by name (e.g.
     CON,  PRN,  COM1,  etc) whereas  block  type  device  drivers are
     allocated a drive letter by DOS in the range A: to Z:.

     A single device driver can control a number of drives, in fact up
     to 255. Since DOS  only allows block device  drive names A: to Z:
     this limits the practical total number of drives to a total of 26
     minus  any  physical  hard  and   floppy  disk  drives  that  are
     installed.  If  you  had  two  floppy  disks  and  one  hard disk
     installed (A;, B: and C:) and a device driver named 'DEVICED' was
     installed  controlling 3  block devices  the  system would  be as
     follows :
                  ÚÄÄÄÄ A:
                  ³
                  ÃÄÄÄÄ B:
                  ³
                  ÃÄÄÄÄ C:
         DOSÄÄÄÄÄÄ´   ÚÄÄÄÄÄÄÄÄÄÄÄ¿    ÚÄÄÄÄ E:
                  ³   ³           ³    ³
                  ÀÄÄÄ´  DEVICED  ÃÄÄÄÄÅÄÄÄÄ F:
                      ³           ³    ³
                      ÀÄÄÄÄÄÄÄÄÄÄÄÙ    ÀÄÄÄÄ G:

                                  Fig. 1


                                  Page 3










     DOS automatically  gives block  devices the  next available drive
     letter(s) when the  device driver is  installed in the config.sys
     file.

     If CD-ROM's were normal block device that would be the end of the
     story, however a single  CD-ROM can hold a  massive 550 MBytes of
     information  - far  more than  DOS  was designed  to manage  on a
     single block device. To  overcome this limitation MicroSoft wrote
     some extensions  to DOS known  as the  "MS-DOS CD-ROM Extensions"
     (MSCDEX). MSCDEX  uses the networking  drive redirection features
     built into DOS versions  3.1 and later to  create a logical drive
     for each  drive attached to  each device driver  specified on the
     MSCDEX command  line when the  extensions are  started. MSCDEX is
     not a device driver, it is  a "Terminate and Stay Resident" (TSR)
     program which runs  and returns to  DOS but remains  in memory to
     it's work in the background.

     So that CD-ROM device drivers won't  be installed by DOS as block
     devices  the  device  driver  header  tells  DOS  that  they  are
     character  devices  (even  though  they  aren't).  CD-ROM  device
     drivers are block device drivers  that appear to DOS as character
     devices but  have a  special signature  so that  MSCDEX and other
     software wishing to talk to the  CD-ROM via the device driver can
     recognize them as  CD-ROM devices. If  our previous example (Fig.
     1)  of DOS  with a  three  drive device  driver were  replaced by
     MSCDEX and a  device driver (CDDRIVER)  driving three CD-ROMS the
     layout would now be as follows :
     
                  ÚÄÄÄÄ A:
                  ³
                  ÃÄÄÄÄ B:
                  ³
                  ÃÄÄÄÄ C:
         DOSÄÄÄÄÄÄ´   ÚÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄ E:
                  ³   ³          ³  ³          ³  ³
                  ÀÄÄÄ´  MSCDEX  ÃÄÄ´ CDDRIVER ÃÄÄÅÄÄÄÄ F:
                      ³          ³  ³          ³  ³
                      ÀÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄ G:

                                  Fig. 2
     
     When MSCDEX or any other software calls a CD-ROM device driver it
     specifies which drive (or unit) it wishes to access by specifying
     a number beginning with zero. It  figure 2 the logical drives E:,
     F: and G: would be drives 0,1 and 2 to CDDRIVER.

     1.2 CD-SHARE - WHAT IT IS AND WHY WE NEED IT

     As well as making CD-ROM's appear as normal (large capacity) disk
     drives,   MSCDEX  supplies   a  number   of  other   services  to
     applications  software  that   calls  MSCDEX  directly.  Although
     networks such as ArtiSoft's LANtastic can redirect a CD-ROM drive
     so that it  appears as an  extra drive on  a network workstation,


                                  Page 4









     CD-ROM software that  requires MSCDEX to run  won't work. To make
     matters  even   worse  some   CD-ROM  software   bypasses  MSCDEX
     completely and talks directly to the CD-ROM device driver.

     This is where  CD-SHARE comes in.  The CD-SHARE software contains
     CD-Server  and CDWORK/CD-Redirector.  CDServer  is a  TSR program
     which is run on the network  computer which has the CD-ROM drives
     fitted  and  the  appropriate  CD-ROM  device  drivers installed.
     CDWORK.SYS and CD-Redirector are run on workstations which wishes
     to access CD-ROM  devices on CD-Servers.  CDWORK.SYS appears as a
     local CD-ROM device driver, however it passes and device requests
     onto  CD-Redirector  which in  turn  passes the  requests  to the
     appropriate CD-Server for processing.  The results of the request
     are passed back to CD-Redirector/CDWORK.SYS  and then back to the
     application  which  called   CDWORK.SYS  .  CDWORK.SYS  therefore
     appears to  applications programs  (including MSCDEX)  as a local
     CD-ROM device driver.

     The CD-Manager program  allows you to alter  the number of drives
     that CDWORK.SYS appears to be controlling, and to connect each of
     those  logical drives  to  a CD-ROM  drive  on a  network machine
     running CD-SERVER.

     Because CD-ROM  seek times  and data  transfer rates  are so slow
     sharing a single CD-ROM amongst  a number of users usually causes
     applications on workstations to run unacceptably slow. Because of
     this the CD-SHARE software suite  also includes CD-CACHE which is
     a  CD-ROM  caching   program  written  specifically   to  run  in
     conjunction with CD-SHARE. When  CD-CACHE running, when a request
     to  read CD-ROM  data occurs  CD-CACHE  checks to  see if  it has
     already been read. If  not then the data  is read from the CD-ROM
     and  stored in  the cache  as well  as being  passed back  to the
     calling software. If a  request for data which  is already in the
     cache occurs  then the data  is returned directly  from the cache
     without any access  at all to the  CD-ROM. The CD-CACHE algorithm
     ensures that the most frequently read data (directories, etc) are
     always kept in the cache,  this improves response times even when
     only one users is running  programs from the CD-ROM. CD-CACHE can
     use conventional or extended memory up to 32 MBytes.

     The networking version of figure 2 using CD-SHARE would appear as
     follows :
         ÚÄÄÄÄ A:
         ³
         ÃÄÄÄÄ B:
         ³
         ÃÄÄÄÄ C:                                    ÚÄÄÄÄÄÄÄÄ¿
     DOSÄ´ ÚÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄ¿ ÚÄÄÄÄÄ¿     ÚÄÄÄÄÄ¿ ³        ÃÄÄÄ 0
         ÀÄ´ MSCDEX ÃÄ´ CDWORK ÃÄ´ CDR ³-----³ CDS ÃÄ´CDDRIVERÃÄÄÄ 1
           ÀÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÙ ÀÄÄÄÄÄÙ  ^  ÀÄÄÄÄÄÙ ³        ÃÄÄÄ 2
                                          ³          ÀÄÄÄÄÄÄÄÄÙ    ^
                     Network Connection ÄÄÙ           Drive Nos.ÄÄÄÙ

                                  Fig. 3


                                  Page 5









     Where :
                   1. CDWORK is the CD-Share CD-ROM device driver
                   2. CDR is the CD-Redirector
                   3. CDS is the CD-Server

     Note that figure three is  a very simple configuration. Each copy
     of  CDS which  is started  on a  CD-Server is  started up  with a
     unique name and can be attached to multiple device drivers on the
     server  computer. Using  CD-Manager (CDM)  each logical  drive on
     CDWORK may be connected to any CDServer\Device\Drive. For Example

                   SERVERS         DEVICE DRIVERS       DRIVES

                 ÚÄÄÄÄÄÄÄÄÄÄ¿      ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄ  0
         +-------³ CDSERV-1 ÃÄÄÄÂÄÄ´   DRIVER1  ÃÄÄ´
         |       ÀÄÄÄÄÄÄÄÄÄÄÙ   ³  ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄ  1
         |                      ³  ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄ  0
         |                      ÀÄÄ´   DRIVER2  ÃÄÄÅÄÄÄÄÄ  1
         |                         ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄ  2
         |
         |       ÚÄÄÄÄÄÄÄÄÄÄ¿      ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄ  0
         +-------³ CDSERV-2 ÃÄÄÄÄÄÄ´   DRIVER1  ÃÄÄÅÄÄÄÄÄ  1
         |       ÀÄÄÄÄÄÄÄÄÄÄÙ      ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄ  2
         |
         |       ÚÄÄÄÄÄÄÄÄÄÄ¿      ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄ  0
         +-------³ CDSERV-3 ÃÄÄÄÂÄÄ´   DRIVER1  ÃÄÄ´
         |       ÀÄÄÄÄÄÄÄÄÄÄÙ   ³  ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄ  1
         |                      ³  ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄ  0
         |                      ÃÄÄ´   DRIVER2  ÃÄÄÅÄÄÄÄÄ  1
         |                      ³  ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄ  2
         |                      ³  ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿
         |                      ÀÄÄ´   DRIVER3  ÃÄÄÄÄÄÄÄÄ  0
         |                         ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ
         |
         |
         |       WORKSTATION
         |
         |       DEVICE DRIVER       ATTACHED TO        DRIVES
         |
         |                         ÚÄCDSERV-1\DRIVER2\2 =  0
         |       ÚÄÄÄÄÄ¿ ÚÄÄÄÄÄÄÄÄ¿³
         +-------³ CDR ÃÄ´ CDWORK ÃÅÄCDSERV-3\DRIVER3\0 =  1
                 ÀÄÄÄÄÄÙ ÀÄÄÄÄÄÄÄÄÙ³
                                   ÀÄCDSERV-1\DRIVER1\1 =  2

                                  Fig. 4

     Note that since CDWORK simulates a CD-ROM device driver, there is
     no need to run MSCDEX on workstations running software that talks
     directly  to  the  CD-ROM  device  driver.  Also  CD-Server  is a
     non-dedicated server, this means that  CDR and CDWORK may also be
     run on the  server which may  then log into  and use devices made
     networkable  by  it's  own  copy of  CD-Serve  as  well  as other
     CD-Servers.


                                  Page 6










     2.0 CONFIGURING A CD-SERVER


     1.  Install  the  CD-ROM  drives,  controllers,  etc.  and device
         drivers  then test  run  the drives  and  programs as  if the
         system were  not to be  networked to make  sure everything is
         okay before adding the CD-Server.

     2.  If you have run  MSCDEX in step 1,  then re-boot the computer
         and DON'T  run MSCDEX. Copy  the CDServer  (CDS.EXE) from the
         CD-Share distribution disk onto your system boot disk.

     3.  Make  sure your  network  NETBIOS driver  has  been installed
         (with LANtastic this is  AILANBIO, LANBIOS, or LANBIOS2). You
         won't  need  any  other   networking  software  on  a  CD-ROM
         workstation  or  a CD-Server  in  order to  run  the CD-Share
         programs.   (You   can   still   run   network  re-directors,
         non-dedicated servers, etc. if need be).

     4.  Assuming you wish  to allow five logged  in users, have named
         your CD-ROM  device drivers  DRIVER1, DRIVER2,  etc (You will
         have specified the driver names on the "DEVICE=" line for the
         drivers in the  config.sys file. Typical  names take the form
         MSCD001,  MSCD002, etc)  and we  wish to  call our  CD server
         cdserver1 enter the following command line :

         CDS CDSERVER1 device=DRIVER1 device=DRIVER2 verbose users=5

         The "device=DeviceName" section  may be repeated  up to eight
         times. CD-Serve can handle up  to 32 drives (e.g. four device
         drivers  each driving  eight  drives, or  eight  drivers each
         driving four drives, one driver driving eight drives and four
         drivers driving six  drives, or any  mix). The verbose option
         is optional and causes CDS to indicate the names of connected
         device  drivers  as they  are  attached to  confirm  that the
         command line  was accepted  correctly. The  "device=" section
         may  be  abbreviated to  "d="  to  fit more  switches  on the
         command line.  CDS has more  command line  switches, they are
         covered in the "Advanced Topics" section.

         Note  that  after  CDS has  been  run,  all  connected device
         drivers are effectively  removed from the  DOS device list so
         they can't be accessed by any  other software. If you need to
         access  the device  drivers in  order to  gain access  to the
         CD-ROM(s)  from software  running locally  on the  server you
         will have to configure the server as a workstation as well.

     3.0 CONFIGURING A CD-WORKSTATION

     1.  Copy  the programs  CDWORK.SYS, CDR.EXE  (CD-Redirector), and
         CDM( CD-Manager) onto the workstation disk. CDWORK.SYS should
         be in the root directory, CDR.EXE  and CDM.EXE should be in a
         directory which is on the PATH.


                                  Page 7










     2.  Insert a  line similar  to that  following in  the config.sys
         file on the workstation boot disk :

         DEVICE=CDWORK.SYS [DEVICE_NAME]

         Where DEVICE_NAME is the name that MSCDEX or any other CD-ROM
         software  will  use  to  access  the  CD-ROM  driver. Typical
         examples might be :

         DEVICE=CDWORK.SYS MSCD001
         OR
         DEVICE=CDWORK.SYS CDWORK

         We  will  assume  that  the name  CDWORK  is  used  in future
         discussion. Whatever you use, make sure that the name doesn't
         conflict  with a  name  you have  given  to any  other device
         drivers (e.g. if you are setting up a non-dedicated CD-Server
         you will have both CDWORK.SYS  and real CD-ROM device drivers
         installed in the config.sys file).

     3.  You will now have to  re-boot the computer so that CDWORK.SYS
         is installed. CDWORK.SYS will sign on with a line similar to

         CDWORK Installed - Copyright Digital Solutions

         during the boot sequence.

     4.  Make  sure  that   your  network  NETBIOS   driver  has  been
         installed. Assuming you wish to call your CD Workstation CDW1
         and  you  wish  to  redirect  to  a  maximum  of  two CDROM's
         simultaneously enter the following command line :

         CDR CDW1 2

         The actual syntax for the CDR command line is :

         CDR [Station Name] {Maximum Drives}

         where []  indicates that  the parameter  is mandatory  and {}
         indicates that the switch is optional. If "Maximum Drives" is
         not specified  it defaults to  one. This is  all that usually
         required since CD-Manager (CDM) can be used to disconnect the
         redirected  CD-ROM  drive  from  any  CD  Server  device  and
         re-connect to another at will. Also MSCDEX uses an additional
         4K of memory for each logical drive on a device driver.

     5.  You can now use  CDM to connect to  devices and drives on any
         CD-Servers that are on  line. To log into  and connect to our
         CDSERVER1, DEVICE1,  DRIVE 0 that  we set up  in the previous
         section, enter the following command line :

         CDM V IN:ON +:0=\\CDSERVER1\DEVICE1\0



                                  Page 8









         After  CDM connects  output similar  to the  following should
         appear on the screen :


         C:\CDM V IN:ON +:0=\\CDSERVER1\DEVICE1\0

         DEVICE1            :           Units            =           2

         CD - REDIRECTOR STATUS....

         Connected                                           servers..

                 \\CDSERVER1

         Drives..

                 Drive 0: Connected to \\CDSERVER1\DEVICE1\0
                 Drive 1: NOT Connected

         Total Servers  Attached :  1
         Total Drives   Attached :  1
         Maximum Drives Attached :  2
         Activity  Indicator is  : ON at Row 1, Column 80

         C:\

                                    Fig. 5

         Let's analyze  the command line  to set what  we've done. The
         first switch  V{erbose} tells  CDW to  work in  verbose mode.
         This is why the line

                   DEVICE1 : Units = 2

         appeared,  and why  the CD  Redirector  status was  listed in
         full.

         The next switch

                   IN{dicator}:ON

         tells CDM  to turn on  the CD  Redirector activity indicator.
         This  causes  a  small activity  indicator  to  flash  on the
         workstation as CD-ROM activity is in progress. By default the
         position of this is  row one, column 80  on the screen (upper
         right corner), see "CDM Command Line Switches" for details on
         how to change this position.

         The next switch requires a little more description :


                   +:0=\\cdserver1\device1\0

         The + option tells CDM to  add a new connection to CDWORK, in


                                  Page 9









         this case to a  drive 0, on a device  named "device1" on a CD
         Server named "cdserver1". The actual syntax is as follows :

         +:[Local Drive Number]=\\[Server Name]\[Device Name]\Drive

         Where a device named "Device Name" be attached to a CD Server
         named "Server Name" and that  device must have a drive number
         "Drive".

         If you  now run the  Microsoft extensions  on the workstation
         specifying  the  name  that you  gave  CDWORK.SYS  (we'll use
         CDWORK as the name) you should get the following response :

         C:\mscdex /d:cdwork
         MSCDEX Version 2.10
         Copyright  (C) Microsoft  Corp. 1986,  1987, 1988,  1989. All
         rights reserved.
                Drive D: = Driver CDWORK unit 0
                Drive E: = Driver CDWORK unit 1

         C:\

                                    Fig. 6

         Note that your drive letters  may not necessarily begin at D:
         depending upon the drives installed  in your computer and any
         redirected network drives you may have.

         If you now type :

                   DIR D:

         You should now get a  directory listing of the root directory
         of the disk in your CD-ROM drive.

         Note that if you now type in

                   DIR E:

         You will  get an error  message from MSCDEX  stating that the
         drive  is  not  ready,  this is  because  drive  E:  which is
         attached to DRIVE  1 on CDWORK  is not connected  to a server
         device (see Fig. 5).

         Now that  MSCDEX has  been run  you may  refer to  the CDWORK
         drives by their drive number, or by their MSCDEX drive letter
         when using CDM.

         The - CDM command line switch allows a drive connection to be
         removed e.g.

         CDM -:0, or CDM -:D

         Would cause CDWORK drive 0 (Fig. 5) to be disconnected, or


                                  Page 10










         CDM LOGOUT:CDSERVER1

         Would cause all connections to CDSERVER1 to be removed.

     4.0 COMMAND LINE SWITCHES

     4.1 CD MANAGER COMMAND LINE SWITCHES

     The syntax of the CD Manager (CDM.EXE) command line is as follows

         CDM {switches}

     Where {switches} represents  any of the  following switches, each
     separated by a space. Note  that any characters between {} braces
     are optional, the {}  characters do NOT form  part of the switch.
     Square braces  [] indicate  that the words  between the  [] are a
     name  and should  not be  entered as  shown. i.e.  The name  of a
     Device, CD Server, or Drive  Number should be substituted for the
     [name]  entry  (the  []  characters  are  not  required.  e.g. To
     indicate  that a  device name  is required  we might  say [Device
     Name], when CDM is  actually run we might  use DEVICE1 instead of
     [Device Name]. In all cases a  = character may be substituted for
     the : character in the following list.

     Switch        Function
     
     V{erbose}     Causes verbose  operation of  CDM. CDM  will report
                   various activities  as they are  processed and will
                   cause CDM  to show  a CD  Redirector status listing
                   after all other switches have been processed.

     Sh{ow}        Causes CDM  to display  CD Redirector  status after
                   all other switches have been processed.

     Logo{ut}:     Syntax

                   Logout:Server_Name

                   Causes all  CDWORK drive  connections to  CD Server
                   "Server_Name" to  be deleted and  the connection to
                   "Server_Name" to be removed.

     +:            Syntax

                   +:[Local Drive]=\\[ServerName]\[DeviceName]\[Drive]

                   Attaches the CDWORK drive  [Local Drive] to [Drive]
                   on a device named [DeviceName] on a CD Server named
                   [ServerName].  For [Local  Drive] either  the local
                   CDWORK drive number or the drive letter may be used
                   if MSCDEX has been run.  [Drive] may be replaced by
                   ALL if you  want all of  the drives on [DeviceName]
                   to  be  attached to  CDWORK  beginning  with CDWORK


                                  Page 11









                   drive [Local Drive]. e.g.  to Connect local drive 1
                   to   [Drive]   2   on   [DeviceName]   MSCD001   on
                   [ServerName] CDSERVER1  the following  switch would
                   be used

                   +:1=\\CDSERVER1\MSCD001\2

                   If  MSCDEX  had  been run  and  Local  Drive number
                   corresponded to drive E:  then the following syntax
                   could also have been used

                   +:E=\\CDSERVER1\MSCD001\2

     -:            Syntax

                   -:[Local Drive]

                   Disconnects  [Local Drive]  from  the device  it is
                   currently attached to. [Local  Drive] may be either
                   the  CDWORK  logical  drive  (unit)  number  or the
                   MSCDEX drive name if MSCDEX has been run.

     Dr{ives}      Syntax

                   Drives:[New Number of Local Drives]

                   Alters the number of logical drives that CDWORK can
                   redirect.  This  switch  will  not  be  accepted if
                   MSCDEX has already been run.

     In{dicator}   Syntax

                   Indicator:[On|Off]{@Row,Column}

                   Turns the  CD Redirector  activity indicator  On or
                   Off depending upon whether  On, or Off is specified
                   after the : . If On is specified you may optionally
                   specify the screen coordinates by following On with
                   @Row,Column ; where valid ranges for row and column
                   are 1 to  25 and 1 to  80 respectively. The default
                   position for the indicator  is 1,80. For example to
                   turn  the indicator  on at  row  25, column  80 the
                   following switch would be used

                   in:on@25,80

                   or to turn it off

                   in:off

                   Note  that  if  in:on is  specified  without  a new
                   position,  then  the previous  position  setting is
                   retained.



                                  Page 12










     4.2 CD REDIRECTOR COMMAND LINE

     The CD  Redirector (CDR.EXE) command  line must  contain a unique
     name for  the CD Redirector  session and can  contain an optional
     number of Local Drives specifier for CDWORK.

     CDR [Unique Name] {Number of Local Drives}

     e.g.

     CDR STN1 1

     The  number of  local drives  defaults to  one if  not specified.
     Since MSCDEX uses an extra 4K of ram per local drive, a figure of
     1 is recommended  if MSCDEX is  to be used.  Since it is unlikely
     that  a  workstation  will  be  accessing  more  than  one CD-ROM
     simultaneously this  does not impose  a limitation as  CDM can be
     used to alter the actual CD-ROM drive that the single local drive
     is connected to at any time.

     Note that  providing MSCDEX hasn't  been run CDM.EXE  can also be
     used to alter the number of local drives.

     CDR can be  logged into a maximum  of five CD  Servers at any one
     time. Local Drives can range from one to twenty five.

     4.3 CD-SERVER COMMAND LINE SWITCHES
     
     The syntax of the CD Server (CDS.EXE) command line is as follows

         CDS [Server_Name] device=device_name {switches}

     [Server_Name] a  unique name  which is  used to  represent the CD
     Server on the network. At least one device must be specified.

     Where {switches} represents  any of the  following switches, each
     separated by a space. Note  that any characters between {} braces
     are optional, the {}  characters do NOT form  part of the switch.
     Square braces  [] indicate  that the words  between the  [] are a
     name  and should  not be  entered as  shown. i.e.  The name  of a
     Device, CD Server, or Drive  Number should be substituted for the
     [name]  entry  (the  []  characters  are  not  required.  e.g. To
     indicate  that a  device name  is required  we might  say [Device
     Name], when CDS is  actually run we might  use DEVICE1 instead of
     [Device Name]. In all cases a  = character may be substituted for
     the : character in the following list.

     Switch        Function

     D{evice}      Syntax

                   Device:[Device_Name]



                                  Page 13









                   where [Device_Name] is the named of a CD-ROM device
                   driver already installed on the server. This switch
                   may be used a maximum  of eight times connecting to
                   a  maximum of  32  drives per  server  (each device
                   driver can  handle multiple  drives -  the total of
                   these drives must not exceed 32). Device drivers to
                   which CDS attaches are  removed from the DOS device
                   list  so other  programs can  no longer  access the
                   device(s).

     Us{ers}       Syntax

                   Users:[Maximum Number of logged in CD users]

                   Note that  a NETBIOS  session is  required for each
                   logged  in  user.  CDS  DOES  NOT  check  that your
                   NETBIOS   can  support   the  number   of  sessions
                   corresponding  to your  Users specification,  it is
                   the  responsibility  of the  network  configurer to
                   ensure  that   enough  netbios   sessions  will  be
                   available. (Up to 254 with LANtastic)

     Bu{ffer}      Syntax

                   Buffer:[Buffer Size in sectors]

                   e.g. Buffer:4

                   Specifies the  size of the  network transfer buffer
                   used to  pass CD ROM  data to  CD workstations. The
                   actual  buffer  size  is  approximately  2K  by the
                   specified buffer  size. The default  Buffer Size is
                   three  sectors (about  6K). Larger  buffers improve
                   performance  but  use  more   memory  when  CDS  is
                   installed leaving  less room for  other programs to
                   run (This is not a  consideration when running a CD
                   Server in dedicated mode).  Note that one buffer is
                   allocated PER network task (see "Tasks")

     Ta{sks}       Syntax

                   Tasks:[Number of Network Tasks]

                   e.g. Tasks:3

                   The  network  tasks   figure  determines  how  many
                   network   CD   requests  the   server   can  handle
                   simultaneously.   The   default   is   one.   On  a
                   non-dedicated server the law of diminishing returns
                   is reached at  a figure of  about five tasks. Three
                   tasks  is usually  adequate, use  two if  memory is
                   tight.
     5.0 CACHING YOUR CD-ROM DRIVES - CD-CACHE



                                  Page 14









     CD-CACHE is  a caching program  specifically designed  to work in
     conjunction with CD-Serve on a CD-ROM server. Because of the slow
     access times of CD-ROM drives use of CD-CACHE is almost essential
     if three or  more than three  users will be  accessing the CD-ROM
     simultaneously.  In fact  using  CD-CACHE will  usually  speed up
     response times even when only one user is accessing the CD-ROM.

     CD-CACHE can use conventional,  extended, expanded, or XMS memory
     for caching purposes  CD-CACHE will  cache any accesses to any of
     the CD-ROM drives  (i.e. up to  32) that are  being managed by CD
     Serve (CDS.EXE).

     Like CDS.EXE CD-CACHE (CDC.EXE) is a TSR program. This means that
     when you run CDC from the command line it will install itself and
     return to the DOS prompt while  remaining in memory to perform CD
     caching as necessary. CDC will not install unless CDS has already
     been installed.

     CDC has a number of command line switches, the two that will most
     commonly be used are those that specify the type of memory CDC is
     to use for caching  purposes and the amount  of memory to use for
     caching.

     The syntax of the CD Cache (CDC.EXE) command line is as follows

         CDC {switches}

     Where {switches} represents  any of the  following switches, each
     separated by a space. Note  that any characters between {} braces
     are optional, the {}  characters do NOT form  part of the switch.
     Square braces  [] indicate  that the words  between the  [] are a
     name and should not be entered  as shown. i.e. A number of KBytes
     of memory to be used would  be substituted for the [Cache Size in
     Kbytes] entry  (the [] characters  are not required.  When CDC is
     actually run we might use 1000 instead of [Cache Size in KBytes].
     In all cases a = character may be substituted for the : character
     in  the  following  list.  Command  line  switches  are  not case
     sensitive, i.e. TYPE is the same as Type or typE.

     Switch        Function

     Type          Syntax

                   Type:{Conv|Ext|Ems|Xms}

                   e.g.

                   TYPE:CONV  means to  use conventional memory (below
                   the 640K boundary) for caching.

                   TYPE:EXT for Extended Memory
                   TYPE:EMS for Expanded memory
                   TYPE:XMS for XMS memory



                                  Page 15









                   The default  is Conventional  if no  TYPE switch is
                   used.

     Size          Syntax

                   Size:[Cache Size in KBytes]

                   e.g. type:1000 for  a 1MByte cache.  The default is
                   to use ALL of the specified type of cache memory if
                   no size switch  is found. Note that  if you use all
                   of conventional memory as cache it is preferable to
                   use the Dedicate CDC switch  to cause the CD Server
                   to  run  dedicated,  this will  always  use  all of
                   conventional   memory  for   caching  as   well  as
                   improving performance dramatically  and leaving you
                   the  option of  unloading CDC  at any  time without
                   re-booting the  CD Server.  See the  "Dedicate" CDC
                   switch  for more  detail. If  you run  CD-CACHE not
                   dedicated and use all available conventional memory
                   for caching  there will  be NO  MEMORY LEFT  TO RUN
                   OTHER PROGRAMS.

     Ded{icate}    Causes CD Cache  to run the  CD-Server in dedicated
                   mode.    This   improves    CD-Server   performance
                   dramatically  (5  to  10  fold)  and  will  add any
                   remaining  conventional memory  available  after CD
                   Cache has loaded  to the cache  memory. E.G. if you
                   have specified  1MByte of extended  memory as cache
                   and  use the  dedicate switch,  and CD  Cache finds
                   that 500K  of conventional  memory remain available
                   after it has  loaded - your  total cache size would
                   be  1.5MBytes. When  CD Cache  is run  in dedicated
                   mode pressing the Esc key on the CD-Server keyboard
                   will unload CD Cache and  return to the DOS command
                   line,  leaving the  CD  Server as  a non-dedicated,
                   non-cached  (as  far  as  CD  ROM's  are concerned)
                   server.

     Buff{er Sectors}
                   Syntax

                   Buffer:{Buffer Size in Sectors}

                   When CD-Cache  performs any CD-ROM  reads it ALWAYS
                   reads the same number  of sectors into cache memory
                   then returns the requests sectors from the cache to
                   CD Server. For optimum  performance the Buffer Size
                   set for CD-Cache  should be a  multiple of that set
                   for CD  Serve. The  default for  CD Serve  is three
                   sectors and the default for CD-CACHE is six. As you
                   can see the  default of six for  CD-Cache will be a
                   multiple of Buffer  settings for CD  Server of one,
                   two,  or  three sectors.  The  maximum  buffer size
                   setting is 25 sectors  (about 64KBytes). The buffer


                                  Page 16









                   size you choose will be determined by the amount of
                   conventional and  cache memory  you are  willing to
                   let CD-Cache  use and  the performance  you require
                   from the server. See  the "Advanced Topics" section
                   for  information on  how to  make decisions  on the
                   best  combinations  of  options  to  select  for CD
                   Server  and CD  Cache  to optimize  performance for
                   your application.

     An example  command line for  running CD Cache  in dedicated mode
     using 2 MBytes of extended memory would be as follows :

     CDC Type:Ext Size:2000

     6.0 ADVANCED TOPICS

     6.1 MEMORY USAGE

     The amount  of conventional memory  used by the  various CD Share
     programs and MSCDEX after being loaded is listed below.

     NOTE: 1K = 1024 Bytes

     PROGRAM       MEMORY USED

     CDWORK.SYS    < 650 Bytes
     CDR.EXE       8 KBytes

     CDS.EXE       12K + Users * 106 + Tasks * (BufferSecs*2532 + 225)

                   e.g. 10 Users, 2 tasks, 5 sectors per buffer =

                   12K + 10 * 106 + 2 * ( 5 * 2532 + 225)

                   = 39118 Bytes
                   = 38.2 K

     CDC.EXE       Conventional Cache :

                       12K + Size of Cache

                   Other               :

                       Buffer Size Bytes(BSB) = BufferSectors * 2532
                       Buffers in Cache (BIC) = CacheSize/BSB

                       Conventional Memory used = 12K + BIC*34 + BSB

                       e.g. Cache Size = 2MBytes of Extended Memory
                            BufferSectors = 6

                       BSB = 6 * 2532 = 15192 Bytes
                       BIC = (2000 * 1024)/15192 = 134(.8)



                                  Page 17









                       Conv Mem Used = 12K + 134*34 + 15192
                                     = 31012 Bytes
                                     = 30.3 K



     MSCDEX.EXE    22K + 4K per logical  drive (e.g. one device driver
                   controlling 2 drives  would use approximately 30K).
                   This will vary slightly according to the version of
                   MSCDEX.

     6.2 OPTIMIZING CD-SERVE PARAMETERS FOR A NON-DEDICATED SERVER

     For a non-dedicated CD  Server we are assuming  that you want the
     server to use as  little memory as possible.  As with most things
     in real life you rarely get  something for nothing - the more you
     prune back  the resources  available to  CD Serve  the poorer the
     performance will  be. The trick  is to strike  a compromise which
     gives both acceptable memory usage and acceptable performance.

     As  you can  see  from the  CDS.EXE  section in  section  6.1 CDS
     conventional memory usage is governed by three parameters

         1. Users
         2. Buffer Sectors
         3. Tasks

     Obviously you should only specify the number of CD users that you
     actually want the CD  Server to be able  to have connected at any
     one time.

     The "Buffer  Sectors" parameter  defines the  size of  the memory
     buffer that CDS  uses to return  CD ROM data  to a CD Redirector.
     The larger this parameter  is made (Max 25)  the larger the block
     of data that the server can send to the CD Redirector in one hit.
     However the maximum figure of 25 sectors amounts to a buffer size
     of about 64K and there is  one buffer allocated per network task,
     as  you can  see  allocating large  buffers  and tasks  can quite
     quickly gobble up huge amounts of memory.

     The number of tasks determines  how many CD network requests that
     the  CD Server  can  process at  any  one time.  Performance will
     improve  as  the  number  of  tasks  is  increased.  The  law  of
     diminishing returns  is reached for  a non-dedicated  server at a
     figure of about five tasks.

     The question then  arises as to  which combination is  best for a
     non-dedicated server. The  answer of course  lies in the question
     "how much memory do you want left over after CDS has been run and
     what  level  of   performance  are  you   going  to  consider  as
     satisfactory ?". For minimum memory usage both the Buffer Sectors
     and  Tasks should  be reduced  to a  minimum. The  default buffer
     sectors setting  is three,  a setting of  two is  probably a good
     starting  point if  you  a trying  to  minimize memory  usage and


                                  Page 18









     maintain reasonable performance. A Tasks setting of two will give
     a  fairly  substantial  improvement  over  the  default  of  one,
     improvements will be gradually decreasing  as the number of tasks
     is increased through three, four, and five.

     With  this  background  experimentation   is  probably  the  best
     indicator of what  will be acceptable  for your application. When
     evaluating   performance  it   should  be   noted  that   CD  ROM
     applications  usually  have  long   periods  of  disk  inactivity
     interspersed  with short  bursts  of activity  when  programs and
     images are  loaded from  the CD ROM.  A simple  method of gauging
     performance is to create a batch file on a number of workstations
     which  reads a  large  number of  files  from the  CD-ROM  into a
     temporary file  on a hard  disk, deletes the  temporary file then
     loops to the beginning - timing  the loop will give an indication
     of performance. If you have this  arrangement set up and you wish
     to re-boot  the server  in order  to alter  CDS parameters  it is
     quite acceptable to simply re-boot the server. Each CD Redirector
     will  eventually report  an error  and MSCDEX  will give  you the
     options Abort, Retry, or Ignore. After CDS has been re-run on the
     CD  Server  simply  select   Retry  and  the  CD-Redirector  will
     re-connect to the server and continue.

     6.3 OPTIMIZING CD-CACHE PARAMETERS

     We will assume here  that for a non-dedicated  CD Server CD Cache
     will always  be run  using cache  memory other  than conventional
     memory;  since you  would  have to  use  all of  the conventional
     memory in order to make  the cache of any use  and if you do this
     you might  as well run  the CD  Server in dedicated  mode and get
     some real performance improvements !

     As you  can see  from the  calculations for  CDC.EXE conventional
     memory usage  when using  extended memory,  the additional memory
     that CDC uses beyond it's fixed code  and data size is made up of
     two components

         1. A  single  buffer  the  size   of  which  is  set  by  the
            "BufferSectors" command  line switch.  The default setting
            for this is 6 sectors or about 15 KBytes.

         2. Cache Buffer management  memory which amounts  to 34 bytes
            for each time the buffer allocated at step 1 will fit into
            the cache memory size.

     From step 2  we can see that  for a given  amount of cache memory
     the amount of  cache management memory  required increases as the
     "Buffer Sectors" setting decreases. In the example calculation of
     section 6.1 for 2MByte  of cache memory and  6 sectors per buffer
     we used  134 *  34 Bytes  = 4556  bytes for  cache management and
     15192 bytes for the buffer  for a total extra conventional memory
     usage  of 19748  Bytes. If  we  halved the  buffer size  to three
     sectors we could used  269 * 34 =  9146 Bytes for management plus
     7596 bytes for buffering  for a total of  16742 bytes. As you can


                                  Page 19









     see we have  only reduced the  consumption of conventional memory
     by 3K  but we  have more  than doubled  the fragmentation  of the
     cache.

     As a general rule, the larger  the Buffers per Sector setting the
     better as  it allows  the CD-ROM  to read  more information  in a
     single disk read thus eliminating a seek from another position on
     the  disk  when  sequential sectors  are  read  from  the server.
     However a quick glance at some files on a CD-ROM will reveal that
     many of  the files  (and the directories  if you  could see their
     size) are actually less than 20K in length. This means that since
     there is  usually very  little file  fragmentation many  of these
     files could be  read with a  single access from  the CD ROM. Note
     that although CD-CACHE allocates 2532 bytes per sector so that it
     can cope with CD-ROM applications that request sector data in RAW
     mode (2532 bytes per sector) most applications read the CD-ROM in
     cooked mode which returns  2048 bytes per sector  (2K). Thus a 12
     sector buffer would  generally read 24K  bytes per read. Although
     CD-CACHE will accept buffer sizes  up to 25 sectors, using values
     above 12 decreases  the granularity of the  cache for very little
     improvement in performance.

     For  optimum  performance the  Buffer  size  should be  set  to a
     multiple of the BufferSectors setting  used with CDS. The default
     CD-CACHE  buffer size  is  set to  six  sectors, this  is  a good
     compromise between conventional memory usage and performance, and
     is also a  multiple of the  default CD-SERV buffer  size of three
     sectors (Also of 2, and 1 !).


     You should choose your buffer  sectors setting with the following
     things in mind:

         1. If  you  are  caching a  large  number  of  drives running
            different  applications,  then  for  a  given  cache  size
            smaller buffers  are going to  increase buffer granularity
            and therefore more  likely to keep  more of the frequently
            used sections of each CD-ROM in the cache.

         2. If  you don't  have  much memory  to  use as  cache memory
            smaller buffers  are better as  this will  help to improve
            the granularity.

         3. If you  have plenty of  cache memory in  comparison to the
            number  of CD-ROM's  that are  being  cached then  you can
            increase the buffer size to improve performance and reduce
            CD-ROM  drive wear  and  tear while  still  achieving good
            granularity.

         4. If you are running CD-CACHE in non-dedicated mode then you
            should choose a buffer size which results in an acceptable
            compromise   between   conventional    memory   used   and
            granularity



                                  Page 20









     6.4 RUNNING CD-SERVE AND CD-CACHE IN DEDICATED MODE

     If you  want the ultimate  in performance -  dedicate your CD-ROM
     Server !

     When using CD-CACHE you  can optionally tell it  to run CD Server
     in dedicated mode. This will  give an immediate speed improvement
     of  usually at  least five  hundred percent  as well  as allowing
     CD-CACHE to add  all remaining conventional  memory to it's cache
     buffers.

     As a bonus  you can unload  CD-CACHE and return  the CD-Server to
     non-dedicated/non-cached operation at the  touch of a key without
     disturbing  and other  network users  using  the CD-ROM's  on the
     server.

     To run in dedicated mode  simply include the "Dedicate" switch on
     the CD-Cache command line as follows :


     CDC Type:Extended Size:2000 Dedicated

     CD-Cache will respond with a  message saying that it is installed
     and running CD-Serve in dedicated mode.

     To  unload  CD-Cache  and   return  to  non-dedicated  CD  Server
     operation simply press  the Esc key. Network  users logged in and
     using the CD-ROM at this time will notice nothing excepting for a
     dramatic decrease in performance.

     If a computer is being used specifically as a dedicated CD Server
     in order to share multiple CD ROM's with maximum performance then
     the  memory  constraints  which  are  important  when  running in
     non-dedicated  mode lose  there importance.  The CD  Serve buffer
     size should be increased to about  six sectors and tasks to about
     five. The  CD-CACHE buffer  size should also  be set  to at least
     twelve sectors (you should install plenty of cache memory).

     Read sections 6.2 and 6.3 (if you haven't already done so) to get
     a good understanding of  the performance consequences of altering
     the CD-Serve and CD-Cache buffer sizes.















                                  Page 21










     7.0 QUESTIONS AND ANSWERS

     Question :    Does  a network  computer need  to be  set up  as a
                   network  server  or  have  a  redirector  or MSCDEX
                   installed in order to be used as a CD-Server.

     Answer   :    No - All  that is required of  the network in order
                   to run CD Serve on  a computer is a NETBIOS network
                   driver.

     Question  :   Do I need to run the network redirector on a CD ROM
                   workstation.

     Answer    :   No -  All that  is required  on the  workstation is
                   that CDWORK.SYS is included and given a device name
                   in the CONFIG.SYS file on the workstation boot disk
                   and   that  network   NETBIOS  network   driver  is
                   installed before running CDR.EXE.

     Question  :   Do I need to run MSCDEX on a CD-ROM workstation.

     Answer    :   Only  if your  CD-ROM application  requires MSCDEX.
                   Many CD-ROM applications  install themselves on the
                   workstation hard disk then  interface to the CD-ROM
                   directly via the device  driver (CDWORK.SYS in this
                   case)  -  these applications  usually  only require
                   MSCDEX for  the initial installation  (i.e. to copy
                   the  program  files  from the  CD-ROM  to  the hard
                   disk).

     Question  :   Can I  use a  CD-ROM workstation  to perform normal
                   network   activities   by   running   the   network
                   redirector.

     Answer    :   Yes - the CD Redirector and CDWORK appear simply as
                   another device  driver to  both the  network and to
                   DOS.

     Question  :   Can I  run CD  Serve in  dedicated or non-dedicated
                   mode on a normal non-dedicated network server (e.g.
                   LANtastic)

     Answer    :   Yes,  although the  activities  of the  two servers
                   will serve to  reduce the performance  of both when
                   running under heavy load conditions.

     Question  :   I cannot run my  normal network redirector up after
                   running CDR and MSCDEX

     Answer    :   MSCDEX  is  implemented as  a  network re-director.
                   Your network redirector sees MSCDEX as a previously
                   installed   network  redirector   and   refuses  to
                   install. The solution  is to run  MSCDEX after your


                                  Page 22









                   network  redirector  (and  before  your  server  if
                   running the  machine up as  a non-dedicated network
                   server e.g. LANtastic's SERVER.EXE).

     Question  :   After running MSCDEX I  don't have enough memory to
                   run my CD-ROM program.

     Answer    :   MSCDEX uses an  extra 4K of  memory for every drive
                   on every device driver it is attached to. Make sure
                   that when running CDR.EXE or CDM.EXE that you don't
                   set the number of drives supported by CD Redirector
                   to more than one. You can then use CDM.EXE to alter
                   this one  logical CD-ROM drive  to different CD-ROM
                   drives on any CD Servers on the network as and when
                   required.

     Question  :   After I run MSCDEX I get devices with names like

                             G.\A.
                             H.\B.
                             I.\C.

                   In   my  network   connection  manager's   list  of
                   redirected   drives   and   I   can't   remove  the
                   connection.

     Answer    :   MSCDEX functions  in exactly  the same  way as your
                   network redirector  - it  uses the  DOS redirection
                   functions and  therefore the  CD-ROM logical drives
                   appear in  the list  of redirected  drives. Because
                   your network redirector  doesn't recognize these as
                   it's own  re-directed drives  it won't  alter these
                   connections.























                                  Page 23