CARPENTER'S DREAM



        The construction program for contractors, carpenters, and home-
        owners. Measurements are expressed in feet, inches and fractions
        of an inch; and angles as pitch. Everything for residential
        construction as well as commercial and heavy industrial applica-
        tions.


                                  Version 2.11S
                                    Nov. 1991






                                 Workhorses Inc.
                                805 B 14th Street
                                Golden  CO 80401
                                 (303) 279-8551
                                 (800) 777-2477













                  Dan Heilman         Editor in Chief
                  Kata McCarville     Editor
                  Peggy Heilman       Assistant Editor
                  Joe Applegate       Principal Programmer
                  Layout and Design   IT'sNEWS! Publications
                  Orv Heilman         Construction Consultant


                        Copyright c 1990 WORKHORSES, INC.
                              All rights reserved.








                                        1






        Carpenter's Dream is not free software!  This program has been made
        available to you as shareware.  If you intend to use Carpenter's
        Dream you should register your copy by sending in the registration
        form with a payment of $25 to:

                                 WORKHORSES INC.
                                805 B 14th Street
                                Golden, CO 80401

        To charge your registration (MasterCard, Visa, or American Express)
        call 1-800-777-2477 (orders only), or fill in the appropriate blanks
        on the registration form.

        You will receive the latest version of the program, telephone
        support, Quick Reference Guide, and hard copy of the Educational
        Manual, and you will be notified of future updates.

        Registration will also allow you to purchase our latest program,
        Contractor's Dream for far less than the normal price, which is
        currently $275.  Contractor's Dream is a greatly enhanced version
        of Carpenter's Dream with a cursor controlled menu, full screen
        field entry of parameters, a material data base, prices for
        materials, printed estimates, Lotus (C) 123 and ASCII output,
        a Pop-Up carpenter's calculator, "what-if" modeling, and many
        more features of use to carpenters and contractors.

        That's why we are making Carpenter's Dream into a shareware product.
        Since 1989, Workhorses, Inc., has sold thousands of copies of
        Carpenter's Dream at $99.  We have received favorable reviews in
        numerous construction and computer magazines.  But Carpenter's Dream,
        while still a useful program, is surpassed by Contractor's Dream.
        We have included a demo of Contractor's Dream with this disk so that
        you can see for yourself how powerful Contractor's Dream is.
        REMEMBER:  As a registered owner of Carpenter's Dream you can buy
        Contractor's Dream for only $199!

        Please refer to the READ.ME file on the diskette for any last
        minute changes, any new files added to the disk, as well as other
        information that may not be included in the printed material.





        IBM is a trademark of International Business Machines, Inc.
        MS-DOS is a trademark of Microsoft Corporation.









                                        2






                                Limited Warranty

        Limited warranty. Workhorses, Inc. warrants that (a) the software
        will perform substantially in accordance with the accompanying
        written materials for a period of 90 days from the date of re-
        ceipt.  Any implied warranties on the software are limited to 90
        days.  Some states do not allow limitations on duration of an
        implied warranty, so the above limitation may not apply to you.
        Customer remedies. The liability of Workhorses, Inc., and your
        exclusive remedy, shall be, at the option of Workhorses, Inc.,
        either (a) return of the price paid or (b) repair or replacement
        of the software that does not meet the limited warranty of Work-
        horses, Inc., and which is returned to Workhorses, Inc. with a
        copy of your receipt.  This limited warranty is void if failure
        of the software has resulted from accident, abuse, or misapplica-
        tion.  Any replacement software will be warranted for the remain-
        der of the original warranty period or 30 days, whichever is
        longer.

        No other warranties. Workhorses, Inc. disclaims all other warran-
        ties, either express or implied, including but not limited to
        implied, including but not limited to implied warranties of
        merchantability and fitness for a particular purpose, with re-
        spect to the software and the accompanying written materials.
        This limited warranty gives you specific legal rights. You may
        have others, which may vary from state to state.

        No liability for consequential damages. In no event shall Work-
        horses, Inc. or its suppliers be liable for any damages whatsoev-
        er including, without limitation, damages for loss of business
        profits, business interruption, loss of business information, or
        other pecuniary loss arising out of the use of or inability to
        use this Workhorses, Inc. product, even if Workhorses, Inc. has
        been advised of the possibility of such damages. Because some
        states do not allow the exclusion or limitation of liability for
        consequential or incidental damages, the above limitation may not
        apply to you.

















                                        3






                                Table of Contents

        GENERAL USAGE                      6
        STARTING THE PROGRAM               6
        ENTERING FRACTIONS                 6
        ENTERING PITCHES                   6
        FUNCTION CONTROLS                  8
        ENTERING SHAPES                    8
        HELPFUL HINT WITH COMPLEX SHAPES   9
        PROGRAM 1
                CONCRETE                   10
                LIQUIDS                    10
                TRUCK LOADS                10
                        TANDEM LOADS       10
                        SEMI END DUMP      10
                BLOWN INSULATION
                        CEILINGS           11
                        WALLS              11
                CUBICS                     11
                  YARDS, FEET, AND METERS  11
        PROGRAM 2
                DECKS                      12
                SHEETS                     12
                AREA                       12
        PROGRAM 3
                TILES, BRICKS, CERAMICS    12
        PROGRAM 4
                ESTIMATE ROOFS             13
                        MAIN STYLE ROOF    13
                        DORMER STYLE       14
                        MULTI-SIDED        14
                        COMPLEX ROOFS      14
                ROLLS OF HALF LAP ROOFING  16
                REBAR                      16
                PRICE OR QUANTITY          16
                ON CENTERS                 16
        PROGRAM 5
                CUTTING LIST FOR RAFTERS & TRUSSES   18
                ABBREVIATIONS              18
                2x RIDGE OR TRUSS          18
                2x6 RIDGE ONLY             19
                2x RIDGE AND HIP ONLY      19
        PROGRAM 6
                STAIRS                     20
                        MAIN RUNNER        20
        PROGRAM 7
                CUTTING LIST FOR WINDOWS   21
        PROGRAM 8
                CROSS CORNER LENGTHS       22
        PROGRAM 9
                SPACING BETWEEN POSTS      23
        PROGRAM 10


                                        4





                ADD                        24
                SUBTRACT                   24
                MULTIPLY                   24
                DIVIDE                     24
                CONVERSIONS
                        FEET               24
                        INCHES             24
                        METERS             24
                        DECIMAL FEET       24
                        QUANTITY           24
                        PITCH TO DEGREES   25
        PROGRAM 11
                GENERAL INFORMATION        26
        PROGRAM 12
                REGISTRATION FORM          26
        TELEPHONE SUPPORT                  26
        GLOSSARY                           27
        Index                              29





































                                        5





        GENERAL USAGE

        STARTING THE PROGRAM
        To start the program, type in: DREAM and press the <ENTER> key.

        The program works in feet, inches, and fractions, but if you
        prefer, it will also work in decimal feet or decimal inches.

        EXAMPLE:
        7,6 = 7.5 = 7 feet 6 inches = 7 1/2 feet
        0,3,1/2 = 0,3.5 = 3 1/2 inches
        0,96 = 8 feet

        The program understands both forms with no other command neces-
        sary.

                            ALL MEASUREMENTS EXACT TO
                                 1/16 OF AN INCH

        ENTERING FRACTIONS:

        1/16, 1/8, 3/16, 1/4, 5/16, 3/8, 7/16, 1/2, 9/16, 5/8, 11/16,
        3/4, 13/16, 7/8, and 15/16.

        FOLLOW THESE EXAMPLES:

        For 10 feet 11 3/16 inches, TYPE IN:  10,11,3/16
        For 9 feet 5/8 inches, TYPE IN:  9,0,5/8
        For 3 1/2 inches, TYPE IN:  0,3,1/2
        For 38 feet 4 inches, TYPE IN: 38,4
        For 7 feet, TYPE IN:  7

             ALWAYS SEPARATE FEET, INCHES, AND FRACTIONS WITH COMMAS

        ENTERING PITCHES:

        1-12, 1.5-12, 2-12, 2.5-12, 3-12, 3.5-12, 4-12, 4.5-12, 5-12,
        5.5-12, 6-12, 6.5-12, 7-12, 7.5-12, 8-12, 8.5-12, 9-12, 9.5-12,
        10-12, 10.5-12, 11-12, 11.5-12, 12-12, 12.5-12, 13-12, 13.5-12,
        14-12, 14.5-12, 15-12, 15.5-12, 16-12, 16.5-12, 17-12, 17.5-12,
        18-12, 18.5-12, 19-12, 19.5-12, 20-12, 20.5-12, 21-12, 21.5-12,
        22-12, 22.5-12, 23-12, 23.5-12, and 24-12.

        Read "4.5-12" as "four and a half-twelve pitch," and so forth.

        When working with roof rafters, hips, and jacks, the program has
        already been adjusted for angular thickness of ridge, subfascia,
        and hip material using standard 2x material. There is no ridge in
        trusses only 2x subfascia. 2x means "2 by material" = 1 1/2
        inches.

                          NO OTHER DEDUCTIONS NECESSARY
                          WHAT YOU READ IS WHAT YOU CUT


                                        6






        If you have a printer attached to your PC, press the <PRINT
        SCREEN> key to get a copy of the screen.  All the programs are
        designed to accept input and produce output on a single screen.
        On some PCs, you must press both <SHIFT> and <PRINT SCREEN>
        together.


                               ESTIMATION PROGRAMS

        All programs figure exact amounts. You need to add in any waste
        you might expect for a job.











































                                        7





                                 FUNCTION  KEYS

        F1 = Help Screen
        You can press F1 at any time for help. Return to where you were
        working by pressing any key.

        F2 = Main Menu
        You can press F2 to go to the main menu at any time but, will not
        be able to return to where you were.

        F3 = Quick Graphic Reference Guide-STAIRS & POSTS
        This screen requires a CGA, MCGA, EGA, or VGA color monitor. It
        shows you what to enter for measurements and how to read the
        measurements that the program gives you. Return to where you were
        working by pressing any key.

        F4 = Quick Graphic Reference Guide-MULTI-SIDED &
                ROOF ESTIMATIONS
        This screen requires a CGA, MCGA, EGA, or VGA color  monitor. It
        shows you what to enter for measurements and how to read the
        measurements that the program gives you. Return to where you were
        working by pressing any key.

        F5 = Quick Graphic Reference-RAFTER CUT LIST
        This screen requires a CGA, MCGA, EGA, or VGA color monitor. It
        shows you what to enter for measurements and how to read the
        measurements that the program gives you. Return to where you were
        working by pressing any key.

        F10 = Exit Program
        Press F10 at any time to exit the program.

                                ENTERING SHAPES

        CIRCLE

        For the Diameter-give the distance across the circle.

        TRIANGLE


        This program works for any triangle.

        For the Base-give the distance across the bottom.

        For the Height-give the vertical distance from the base to the
        highest point above the base.


        Rectangle

        For the Length-give the distance on one side.
        For the Width-give the distance on the other side.


                                        8






        MULTI-SIDED

        For Length of One Side-Give the distance on one side.
        For Cross Corner Length-Give largest distance across the shape
        (labled "CC" on diagram).

        WORKS GREAT FOR GAZEBOS

        Examples: 3 sides = equilateral triangle
        Examples:
        Examples:
                  4 sides = square
                  5 sides = pentagon
                  6 sides = hexagon
                  7 sides = heptagon
                  8 sides = octagon

        HELPFUL HINT FOR COMPLEX SHAPES

        If you have a complex shape, break it up into circles, triangles,
        rectangles, and multi-sided shapes. Run the program for all of
        the pieces and save the figures for each by printing your re-
        sults. Then total all of your figures together.

        THICKNESS

        For the thickness-Give the average distance from top to bottom.
        Example-4 inches thick, type in: 0,4.




























                                        9





                     PROGRAM 1-CONCRETE, GALLONS,  AND MORE


        Make sure you have looked at the SHAPES AVAILABLE section before
        you try to use this program.

        All programs figure exact amounts. You need to add any waste that
        you might expect on that job.

                                    CONCRETE

        The program gives you the number of cubic yards of concrete to
        order.
                                     LIQUIDS

        U.S. GALLONS and LITERS

        These programs work identically. They give you the amount of
        liquid in U.S. Gallons or LITERS contained in the shape you
        choose. This is helpful for picking the size of pump that you
        will need to pump out a pond or basement. Check to see how many
        gallons (or liters) the pump puts out per hour or minute to
        decide which pump is right for you. You may just want to know the
        cost of filling the pool or how much water to haul to that dove
        pond. The program will also work for oil, gas, chemicals, or any
        other liquid.


                                   TRUCK LOADS

        All weights are based on the OPTIMUM MOISTURE level, just right
        for compaction. Be sure to check local load limits and your truck
        specifications.

        TANDEM LOADS: SAND, TOP SOIL, FILL
        (or anything with similar density)

        The program gives you the number of tandem loads you need to
        order. Specifications: 1.4 tons per cubic yard and 15 tons per
        load. If this doesn't meet your specifications, you must adjust
        accordingly.

        TANDEM LOADS: WHITE ROCK, ROAD GRAVEL,
        RIP RAP (or anything with similar density)
        RIP RAP
        RIP RAP

        The program gives you the number of tandem loads you need to
        order. Specifications: 1.6 tons per cubic yard and 15 tons per
        load. If this doesn't meet your specifications, you must adjust
        accordingly.

        SEMI END DUMP: SAND, TOP SOIL, FILL
        (or anything with similar density)



                                        10





        The program gives you the number of tandem loads you need to
        order. Specifications: 1.4 tons per cubic yard and 22 tons per
        load. If this doesn't meet your specifications you must adjust
        accordingly.

        SEMI END DUMP: WHITE ROCK, ROAD GRAVEL,
        SEMI END DUMP: WHITE ROCK, ROAD GRAVEL,
        SEMI END DUMP: WHITE ROCK, ROAD GRAVEL,
        RIP RAP (or anything with similar density)
        RIP RAP
        RIP RAP

        The program gives you the number of tandem loads you need to
        order. Specifications: 1.6 tons per cubic yard and 22 tons per
        load. If this doesn't meet your specifications you must adjust
        accordingly.


                                BLOWN INSULATION

        CEILINGS

        The program gives you the number of 30 pound bags to order.
        Specifications: 2.5 pounds per cubic feet. If this doesn't met
        your specifications, you must adjust accordingly.

        R VALUE FOR CEILINGS
         (Settled density depth in inches)

        R-50 = 13.9  R-32 = 8.9  R-24 = 6.7  R-18 = 5.0  R-10 = 2.8
        R-44 = 12.2  R-31 = 8.6  R-23 = 6.4  R-16 = 4.5  R-9  = 2.5
        R-40 = 11.1  R-30 = 8.3  R-22 = 6.1  R-14 = 3.9  R-8  = 2.2
        R-38 = 10.6  R-28 = 7.8  R-21 = 5.8  R-13 = 3.6  R-6  = 1.7
        R-36 = 10.0  R-27 = 7.5  R-20 = 5.6  R-12 = 3.3  R-4  = 1.1
        R-34 =  9.5  R-26 = 7.2  R-19 = 5.3  R-11 = 3.1  R-3.6= 1.0

        WALLS

        The program gives you the number of 30-pound bags to order.
        Specifications: 4 pounds per cubic foot. If this doesn't meet
        your specifications, you must adjust accordingly.

        R VALUE FOR WALLS

        For 2x4 studs: The cavity has an R value of 12.25
        For 2x6 studs: The cavity has an R value of 19.25

                                     CUBICS

        YARDS, FEET, AND METERS

        You can use these cubics for any material you choose, such as
        peat moss, sand, or fertilizer.  NOTE:  The cubic yards in con-
        crete can be used for cubic yards of anything.





                                        11






                            PROGRAM 2-DECKS, SHEETS,
                                    AND AREAS


        Make sure you have looked at the SHAPES AVAILABLE section before
        you try to use this program.

        All programs figure exact amounts. You need to add in any waste
        that you might expect.

        DECKS

        The program gives you the linear feet needed. To get the number
        of boards to order, take this length and divide by the length
        board you plan to use.

        Specifications:                 2x4 = 1 1/2 inches x 3 1/2 inches
        Specifications:
        Specifications:
                                        2x6 = 1 1/2 inches x 5 1/2 inches
                                        2x8 = 1 1/2 inches x 7 1/4 inches

        SHEETS

        The program gives you the number of sheets to order. It works for
        any thickness of sheet you choose on materials such as plywood,
        drywall, or paneling.

        Specification:                       4x8  = 4 feet by 8 feet
        Specification:
        Specification:
                                             4x9  = 4 feet by 9 feet
                                             4x10 = 4 feet by 10 feet
                                             4x12 = 4 feet by 12 feet

        AREA (YARDS, FEET, OR METERS)

        Use this for any material you wish, such as paint, linoleum, or
        carpet.


                      PROGRAM 3-TILES, BRICKS, AND CERAMICS

        Make sure you have looked at the SHAPES AVAILABLE section before
        you try to use this program.

        All programs figure exact amounts. You need to add any waste that
        you might expect on that job.

        The program will ask for the dimensions of a rectangular shape
        used to fill an area.  That fill material may be tiles, bricks,
        or any rectangular shape.  The fill shape will then be fitted to
        the selected shape and area and the program will report the
        calulated number of fill shapes required.

        Be sure and include mortor on two sides only.  Standard mortor on


                                        12





        bricks and blocks is 3/8 of an inch.  Standard mortor on ceramics
        is 1/8 of an inch.



                PROGRAM 4-ESTIMATE ROOFS, REBAR,  HALF-LAP, AND
                               16 INCH  ON-CENTERS


        All programs figure exact amounts. You need to add in any waste
        that you might expect.

                                      ROOFS

        Take measurements from Blue Print.

        NOTE:  For black paper use the squares of shingles for squares or
        black paper.

        MAIN STYLE AND DORMER STYLE ROOF

        For the Overall Length of Roof-Give the longest distance of that
        section of roof along the ridge.

        For the Overall Width of Roof-Give the full distance perpendicu-
        lar to the ridge.

        For the Pitch-Give the slope of the roof using one of the pitch
        choices on page 6.

        For Hip or Gable-Enter 1 for hip or 2 for gable.

        The program gives you the number of 4x8 sheets of plywood needed.

        The program gives you the number of squares of shingles needed.
        Most roofing material comes in squares. The program gives you the
        number of squares of shingles for caps. Add these two numbers to
        get the total number of squares of shingles you will need.

        The program gives you the length of rafters required and the
        length of hip material to order. Length is given to the nearest 2
        foot length just as you order them.

        The program gives you the number of rafters for both 16 inches
        and 2 feet on center. It does not matter if the roof is a hip or
        gable. The jacks are included for the hip style. This doesn't
        include subfascia or ridge material.  (Read these lengths off of
        blue prints.


        MAIN STYLE ROOF

        This is any section of the roof that can stand alone and is not


                                        13





        on another roof.






















































                                        14





        DORMER STYLE

        This is any section of the roof that lies on another section of
        the roof.

        The program gives you the roll valley material needed with the
        overlap already included.

        The program gives you the deductions for the plywood to take from
        the adjoining roof. Deductions are for only the triangular part.
        You may not want to take all of this deduction because generally
        you go ahead and lay most of the 4x8 sheets of plywood down.

        The program gives you the deductions for the shingles to take
        from the adjoining roof. You should take this deduction, which
        only includes the triangular part.

        MULTI-SIDED ROOFS

        This is any section of the roof where all of the sides are the
        same length and have the same angle between them. Works great for
        gazebos.

        For the Number of Sides-Give the number of outer edge sides.

        For the Pitch-Give the slope of the roof using one of the choices
        on page 2.

        As for main and dormer roofs, the program gives you the number of
        4x8 sheets of plywood, the number of squares of shingles, and the
        number of squares of shingles of cap you should order. The pro-
        gram also gives you the length of the common rafters required.
        The length is given to the 2 feet length just as you would order
        them.


                                  COMPLEX ROOFS

        For complex roofs, break the roof into sections. Then compute
        each section and total the results together.

        Dormer roof with different pitch than main roof: Run the dormer
        Dormer roof with different pitch than main roof:
        Dormer roof with different pitch than main roof:
        style program once for each pitch. Then add the results together
        and divide by 2. Don't forget to adjust for the overall length of
        the roof.
        Dormer roof that butts into two different main roofs: Cut the
        Dormer roof that butts into two different main roofs:
        Dormer roof that butts into two different main roofs:
        dormer in half and do it in two sections. Make each end a gable
        and deduct two rafters.

        Roof with an offset ridge: Treat the roof as though the ridge is
        Roof with an offset ridge:
        Roof with an offset ridge:
        in the center. To get singles, cap, and plywood run the program
        twice, once for each for each side of the offset. Make your
        overall width twice the distance of one side. This will give you


                                        15





        the length of the rafters for each side. Then divide the quantity
        of rafters by 2.

        Cone shaped roof: Use the multi-sided roof program. Figure how
        Cone shaped roof:
        Cone shaped roof:
        many common rafters the roof will take and use that number for
        the number of sides to enter. Measure the distance at the fascia
        on the center with the commons and use this measurement for the
        length of one side. This will give you the shingles, plywood, and
        rafter length. Ignore cap.














































                                        16





                            ROLLS OF HALF-LAP ROOFING

        Specifications: One roll of half lap covers 50 square feet. Five
        gallons of cold process are required for every 4 rolls of half
        lap. NOTE: This will be less in the summer and more in the win-
        ter. Each roll weighs 90 pounds. This program works for rectan-
        gles only.  See graphic on  p. 10

        When asked for the Length of Area to Cover-Give the distance on
        one side.

        When asked for the Width of Area to Cover-Give the length of the
        other side.

        The program gives you the number rolls of half lap needed.

        The program gives you the number gallons of cold process needed.


                                      REBAR

        Specification:
        Specification:
        Specification:
        #2 Rebar = 1/4 inch diameter = 0.167 lb. per linear foot
        #3 Rebar = 3/8 inch diameter = 0.367 lb. per linear foot
        #4 Rebar = 1/2 inch diameter = 0.668 lb. per linear foot
        #5 Rebar = 5/8 inch diameter = 1.043 lb. per linear foot
        #6 Rebar = 3/4 inch diameter = 1.502 lb. per linear foot
        #7 Rebar = 7/8 inch diameter = 2.044 lb. per linear foot
        #8 Rebar =   1 inch diameter = 2.670 lb. per linear foot

        For the Linear Footage-Give the total length needed.

        The program gives the number of pounds of rebar to order.


                                PRICE OR QUANTITY

        This program calculates the total price for an item, using the
        quantity of material multiplied times the unit price.

        For quantity-Give number of items, the amount, or the length
        needed.

        For Price-Give the price per unit.

        The program gives you the total price for the material or the
        quantity.


                                   ON CENTERS

        This program lets you find the studs, joists, rebar, roll insula-
        tion, and anything else that is on center, with ends included.


                                        17





        For things such as rebar and roll insulation, find out how many
        you need on center Then multiply that number times the length
        needed to get your linear footage. For rebar you can then go to
        rebar estimations and enter the linear footage to find how many
        pounds to order.

        For Length of Run-Give the overall distance.

        The program gives you quantity needed with the ends included.

        NOTE: In general, when estimating the number of studs for a house
        at 16 inches on center, total the length of all exterior and
        interior walls. The number of feet is the quantity of studs to
        order. This will include door doublers, partition posts, corner
        posts, and 2x4 headers. Next, take this total length and multiply
        by 3 for the bottom and double top plates. You still have to
        include backing, collar ties, braces, and garage studs to round
        out your 2x4 list.





































                                        18





                             PROGRAM 5-CUTTING LIST
                             FOR RAFTERS AND TRUSSES



        ABBREVIATIONS:
        LP = Long point
        SP = Short point
        BM = Bird's mouth
        2x = 1 1/2 inches

        The angular thickness of 2x ridge, 2x subfascia, and 2x hip
        material has already been adjusted for. There is no ridge in
        trusses, only 2x subfascia.

                          NO OTHER DEDUCTIONS NECESSARY
                          WHAT YOU READ IS WHAT YOU CUT

        When the program asks for the Width of the Building-Give the
        distance from outside to outside of building where the Bird's
        Mouth butts into. This is probably the celotex or something
        similar, not the top plates.  For trusses this is the top plates.

        For the Overhang
        When using rafters-Give the distance from the outside edge of the
        subfascia to the celotex or similar covering.
        When using trusses-Give the distance from the outside edge of the
        subfascia to the stud.

        For the Pitch-Give the slope of the roof. See ENTERING PITCHES.

        For either 2x Ridge or Truss: Give 2x if you are using 1 1/2 inch
        material or truss if there is no ridge.

        2x RIDGE OR TRUSS

        The program gives you the degree of the common, which is the
        slope of the roof.

                        See Quick Graphic Reference Guide
                   These measurements are exactly what you cut

        The program gives the long point to bird's mouth.

        The program gives the long point to short point.

        The program gives the  height of ridge from top plate minus
        bird's mouth. This is very helpful when setting up scaffolding.
        Just take this height and add to the wall height and ground-to-
        floor height.

        The program gives you level line of bottom of 2x6 subfascia to
        outside wall PLUS bird's mouth.


                                        19





                        This is an IMPORTANT measurement
        Check to see where this hits with respect to the window.

        EXAMPLE: If you are using:
                 PLUS                        MINUS
                 3 in. of top plate          1 in. reveal on brick mold
                 11 1/4 in. of 2x12 header   1/2 in. aluminum J mold
                 1/2 in. clearance above     1/4in. of play

        This totals 13 inches MINUS bird's mouth. Standard bird's mouth
        is 1 1/2 inches. If these measurements don't match PLUS & MINUS
        the bird's mouth then either adjust overhang, pitch, or bird's
        mouth. EXAMPLE: If the program gave you 10 inches for level line
        and you where using the materials above and 1 1/2 inch bird's
        mouth this would be a perfect fit for the soffit and brick mold
        with a 1/4 inch play. Both would equal 11 1/2 inches. 13 inches
        MINUS bird's mouth = 10 inches PLUS bird's mouth = 11 1/2 inches

        2x6 RIDGE ONLY

        The program gives you cripple height MINUS bird's mouth. This is
        a very helpful measurement. Now you can nail up your first two
        rafters to the ridge and then set it right on the cripple!

        2x RIDGE AND HIP ONLY

        The program gives you the degrees of the hip and the pitch. For
        the pitch change the 12 to 17. EXAMPLE: If roof is a 6-12 pitch
        then the hip pitch is 6-17.

        The program gives you long point to bird's mouth of the hip.
        Don't precut the hip from long point to short point. This should
        be done after it is up by snapping a line from common ends.

        The program gives you the difference to cut the jacks for both
        two feet and 16 inches on center.

        The program gives you what to cut the first jack rafter laid out
        at either two feet or 16 inches on center.
















                                        20





                                PROGRAM 6-STAIRS
                        CAN BE USED ON ANY SET OF STAIRS

        The program was designed to find the best rise and run using the
        first measurement equal to or over 7 inches. This program can be
        used for small stairs and for very large stairs, too.  For con-
        crete stairs, make the overlap equal to 0 and ignore the length
        of opening. For spiral stairs, use the rise measurement and the
        number of tread and ignore everything else.

        For Height of Opening-Give it from finished floor to finished
        floor.

        For Tread Width-Give the width of material you are using. EXAM-
        PLE: 2x12 tread would be 11 1/2 inches = 0,11,1/2. For the Over-
        lap: Give the distance the tread hangs over the run. EXAMPLE: 1
        inch overlap = 0,1.

        The program gives you rise, which is the distance from bottom of
        tread to bottom of next tread.

        The program gives you run, which is the distance of the width of
        the tread minus overlap.

        The program gives you the length of opening figured using 1/8-
        inch floor tile, 3/4-inch plywood flooring, and 2x10 floor joist
        on upper floor. If your flooring material is different adjust
        accordingly. This measurement is very helpful, as it allows for
        needed head height. This measurement is only given if the height
        of opening is big enough. You don't want to hit your head.

        The program gives you the floor space needed. This is helpful for
        finding out if there is enough room for a       3-foot landing at
        the bottom. You don't want to run into a wall.

        CUTTING YOUR MAIN RUNNER: Don't forget to cut the thickness of
        CUTTING YOUR MAIN RUNNER:
        CUTTING YOUR MAIN RUNNER:
        your tread of the horizontal bottom of the main runner.  When
        using kicker boards cut the thickness of your kicker off the
        vertical top of the main runner.
















                                        21





                       PROGRAM 7-CUTTING LIST FOR WINDOWS

        This program gives you the cutting list for the windows for
        framing in. Specifications:  Using standard 92 5/8 inch studs,
        single 2x bottom plate, double 2x top plate, and 2x12 header (11
        1/4 inch).  Some local codes require that the sill butt into the
        window doubler.  If this is the case for you, just subtract 3
        inches from sill and ignore window sides. NOTE: The 92 5/8 inch
        studs may be different for your area; adjust accordingly.

        For the Rough Opening Height:  Give the rough opening height of
        the specification of your window.

        For the Rough Opening Width:  Give the rough opening width of the
        specification of your window.

        The program gives header and sill length.

        The program gives window side length.

        The program gives the length for cripplers, the boards between
        the sill and the bottom plate.

































                                        22





                         PROGRAM 8-CROSS CORNER LENGTHS


        This program will square up your project for you.  When dealing
        with multi-sided shapes, all sides must be the same length and
        have the same angle between them.  In other words, it must be a
        regular polygon. See ENTERING SHAPES, MULTI-SIDED.

        For the Length of One Side-Give the length of one edge.

        The program gives you the cross corner length, (CC) on graphics.
        This is the distance from one corner to the farthest opposite
        corner.










































                                        23





                   PROGRAM 9-FENCING AND SPACING BETWEEN POSTS


        This program can be used for spacing support beam posts, deck
        railings, stair railings, Fencing, gardens (tomato plants etc.),
        Ornamental railings, and more!

        For Length of Run - Give the overall distance with end posts
        included.  When asked for Width of Posts:  Give the width of a
        post. EXAMPLE:  For a 4x4, give 3 1/2 inches = 0,3,1/2.

        For approximate spacing between posts-Give the longest distance
        desired between posts.

        The program gives you the exact spacing between the posts and the
        number of posts, ends included.







































                                        24





             PROGRAM 10-ADD, SUBTRACT, MULTIPLY, DIVIDE, AND CONVERT


        ADD

        For the Starting Length-Give a distance.

        For the Length to Add-Give a distance you want to add to the
        first distance.

        The program gives you the total of the two.

        SUBTRACT

        For the Starting Length-Give the longer of two distances.

        For the Length to Subtract-Give the other distance.

        The program gives you the difference between the longer and
        shorter length.

        MULTIPLY

        For the Starting Length-Give the first distance or quantity.

        For the Length to Multiply by-Give the length or quantity to
        multiply by.

        The program gives you the answer in square units of the same
        units you enter.


        DIVIDE

        This will be handy to find fencing, on centers, and placements.
        It is great for figuring blocks or bricks needed.

        For the Starting Length:  Give a distance or quantity.

        For the Length to Divide- Give  a length or quantity to divide
        by.

        The program gives you the answer in the same units you enter.

        CONVERSION OF FEET, INCHES, AND FRACTIONS OF AN INCH, METERS, AND
                            DECIMAL FEET OR QUANTITY

        For feet, inches, and fraction of an inch, decimal feet, or
        meters:  Enter your measurement.

        The program gives you the measurement in all three forms: feet,
        inches, and fraction of an inch, decimal feet, and meters.



                                        25





                         CONVERSIONS OF PITCH TO DEGREES

        For Pitch-Give one of the pitches listed in ENTERING PITCHES.
        Always put a dash (-) between numbers as in 4-12.

        The program gives you degrees. This is helpful for setting your
        saw.


        NOTE: This program only does one function (add, subtract, multi-
        ply, and divide) at a time.  To do multiples of a function (or
        multiple functions) you need to buy Workhorses' Pop-Up calcula-
        tor, "Pop an Inch".










































                                        26





                                   PROGRAM 11
                               GENERAL INFORMATION


        This program gives you many standard measurements that are easily
        forgotten.  Some of these measurements may be regulated by local
        code.  Be sure to check your local code.

                           PROGRAM 12REGISTRATION FORM

        This program gives you the registration form that you should send
        in. After you have registered, you will receive information on
        updates, as well as telephone support.  Press the print screen
        key on your computer to print the form on paper. Fill in all
        blanks appropriately.  Your comments are appreciated. Send the
        form (and $99 if you have not already paid for the program-Visa,
        MasterCard, or COD's accepted, COD's add $5) to:

        WORKHORSES, INC.
        805 B 14th Street
        Golden, CO  80401
        1-303-279-8551 for telephone support.

        Registration entitles you to a copy of the latest version of
        CARPENTER'S DREAM, a hardcopy of the Educational Manual, notifi-
        cation of future updates, and telephone support.  Prices subject
        to change without notification.


                                TELEPHONE SUPPORT

        After you have sent in your registration, you may call our tele-
        phone support line if you have questions or problems with CARPEN-
        TER'S DREAM.  The telephone support number is: (303) 279-8551.
        Hours:  Monday through Friday, 9:00 a.m.-5:00 p.m. Mountain time.




















                                        27






                                    Glossary

        angular        slope or pitch
        area           amount of surface
        bird's mouth   the cutout of the rafter that sits on the wall and
        butts into the outside wall
        bottom plate   the board that goes across the bottom of the studs
        braces         temporary supports
        brick mold     type of window trim
        butts          edge to edge joints
        cap            cut-up shingles that lie on the ridge and hip
        cellulose      treated, ground-up paper stock
        celotex        a thick insulating sheet
        cold process   a tar substance
        collar tie     the support between rafters on opposite sides of
                       the room
        common         identical rafters that extend from the subfascia
                       to the ridge
        conversion     changes from one unit of measure to another
        cripple        a support board
        cubic          three-dimensional volume
        decking        flooring
        degrees        measurement of the angle
        density        of similar weight per size
        dormer         a roof section that lies on another section of
                       roof
        doubler        the board under the header butted next to the stud
        gable          no pitch on the end of the roof
        gazebos        a multi-sided outdoor summer retreat
        half-lap       rolled roofing with half-granular and half smooth
        header         beam
        hip            pitch on the end of the roof
        j mold         the soffit enters this at the wall
        jack           the short rafters from the hip to the subfascia
        joist          main supports of a wall or a ceiling
        landing        area at the bottom of the stairs
        long point     longest point on an angular end cut board
        main runner    the board that extends from floor to floor on
                       stairs
        on center      spacing distance from center to center
        optimum
            moisture   just right for compaction
        overhang       distance from outside wall to the outside of the
                       subfascia
        parallel       running in the same direction
        perpendicular  at 90 degrees to each other
        pitch          the slope or angle
        placements     where something goes
        play           clearance
        r value        heat storage value
        rafters        main angular supports of the roof
        rebar          steel reinforcing rods


                                        28





        reveal         the exposed part
        ridge          upper most part of the roof
        rip rap        generally, broken-up concrete
        rise           distance form bottom of tread to bottom of next
                       tread
        rough opening  the opening the door or window sit in
        run            the distance of the tread minus the overlap
        short point    the shortest point on an angular end cut board
        sides          a form of doubler
        sill           bottom of the rough opening for a window or door
        slope          pitch or angle
        squares        one unit by one unit area
        standard       most widely used
        studs          main supports of a wall
        subfascia      the board going across the ends of the rafters
        top plate      the board that goes across the top of the studs
        tread          the board you walk on
        trusses        where the common rafters butt into each other
        waste          cut offs, bowed, and damaged material




































                                        29





                                      Index

                                         Ridge 6, 13, 14, 15, 16, 18, 19
        Add 24                           Rip Rap 10
        Area 11, 12                      Road gravel 10
        Bricks 12                        Roll insulation 16
        Blown insulation 11              Roll valley 14
        Cap 13, 14                       Sand 10
        Carpet 12                        Semi-end dump 10
        Ceramics 12                      Sheets 12
        Chemicals 10                     Shingles 12, 13, 14
        Circle 8                         Soil 10
        Cold process 16                  Spiral stairs 20
        Complex roofs 14                 Stairs 6, 20
        Concrete 10                      Studs 16
        Concrete stairs 20               Subfascia 6, 14, 18, 19
        Cone shaped roof 14              Subtract 24
        Conversion 24, 25                Tandem loads 10
        Cross corner lengths 22          Telephone support 26
        Decks 12                         Tiles 12
        Dormer roof 14                   Top 10
        Drywall 12                       Tread Width 20
        Fencing 23                       Truck Loads 10
        Fill 10                          Trusses 18
        Floor joist 20                   U.S. gallons 10
        Floor tile 12                    White rock 10
        Gable 13                         Windows 21
        Gas 10
        Gazebos 9, 14
        Half lap 16
        Hip 6, 13, 14, 18, 29
        hips 6
        Jack rafter 6, 13, 19
        Joists 16
        Landing 20
        Linoleum 12
        Liquids 10
        Liters 10
        Main & dormer style roof 13, 14
        Multi-sided 6, 16
        Offset ridge 16
        Oil 10
        On centers 16, 19, 24
        Paint 12
        Paneling 12
        Placements 24
        Plywood 12, 13, 14, 15, 20
        Posts 6, 16, 23
        Price or quantity 16
        R value 11
        Rafters 6, 13, 14, 15, 16, 19
        Rebar 12, 15, 16
        Registration form 26


                                        30





                                      NOTES






















































                                        31





                                      NOTES






















































                                        32





                                      NOTES






















































                                        33